UNITED STATES ENVIRONMENTAL PROTECTION AGENCY

REGION IX AIR DIVISION

Technical Support Document

for

EPA’s Notice of Proposed Rulemaking and Direct Final Rule

for the

California State Implementation Plan

South Coast Air Quality Management District

Rule 1122, Solvent Degreasers

Prepared by: Francisco Dóñez

October 2005

AGENCY NAME:		South Coast Air Quality Management District (SCAQMD)

SUBMITTED RULE:	Rule 1122, Solvent Degreasers

Adopted: October 1, 2004

Submitted: January 13, 2005

Complete: February 16, 2005

PREVIOUS RULE		No other versions of Rule 1122 have been submitted to

SUBMITTALS:		EPA as a revision to the State Implementation Plan (SIP).

SIP-APPROVED RULE:	Rule 1122, Solvent Degreasers

Adopted: July 11, 1997

Submitted: September 8, 1997

Approved: April 2, 1999 (64 FR 15922)

RULE SUMMARY

SCAQMD Rule 1122 applies to all persons who own or operate batch-loaded cold cleaners, open-top vapour degreasers, all types of conveyorized degreasers, and air-tight and airless cleaning systems that carry out solvent degreasing operations with a solvent containing Volatile Organic Compounds (VOCs) or with a NESHAP halogenated solvent.  The most recent rule amendments reflect the findings of a technology assessment to evaluate an exemption for certain small degreasers.

Revisions to Rule 1122

Submitted Rule 1122 makes the following changes to the SIP-approved rule.  Unless otherwise noted, section references apply to the version of the rule submitted on January 13, 2005.

- Section (k)(1)(C) extends the sunset date for the existing exemption for small-sized degreasers to June 1, 2005.

- Section (k)(1)(D) exempts from the rule small degreasers, used in specific cleaning applications, that are vented to an emission collection and control system.

- Section (k)(1)(E) contains a limited exemption for small degreasers used only for cleaning electronic components designed to travel over 100 miles above the earth’s surface.

- Section (k)(1)(F) provides a permanent exemption for small degreasers used for research and development/quality assurance programs.

- Section (k)(2)(H) extends the exemption for the cleaning of photocurable resins from stereolithography equipment and models to December 31. 2008.

- Section (h)(7) lists compliance test methods for determining the efficiency of a VOC emission collection and control system.

- Additional minor rule language clarifications.

RULE EVALUATION

Generally, SIP rules must be enforceable (see section 110(a) of the CAA), must require Reasonably Available Control Technology (RACT) for major sources in ozone nonattainment areas (see section 182(a)(2)(A)), and must not relax existing requirements (see sections 110(l) and 193). The SCAQMD regulates an extreme ozone nonattainment area (see 40 CFR part 81) and Rule 1122 must fulfill RACT.

Documents used to evaluate the rule include the following: EPA’s Issues Relating to VOC Regulation Cutpoints, Deficiencies, and Deviations (May 25, 1988, the “Bluebook”); and EPA Region IX’s Guidance Document for Correcting Common VOC and Other Rule Deficiencies (August 21, 2001, the “Little Bluebook”).

Submitted Rule 1122 is consistent with these documents and EPA SIP approval criteria.  The revised rule contains more stringent criteria for exempting small degreasers from the rule.  Except for some narrowly defined applications, small degreasers may only be exempted if they are vented to a VOC emission control system.  The rule fulfills RACT and all other requirements mentioned above.

Net Effect on Emissions

No emissions reductions are expected from this rule revision.  According to the SCAQMD, the VOC emissions associated with the small degreaser exemptions will continue to be 25 pounds per day.

RECOMMENDED ACTION

I recommend full approval of submitted Rule 1122 under Section 110(k) of the Clean Air Act to replace the SIP-approved version of Rule 1122.

ATTACHMENTS

- SCAQMD Rule 1122, Solvent Degreasers, adopted October 1, 2004.

- SCAQMD Rule 1122, Solvent Degreasers, adopted September 8, 1997.

- U.S. EPA. Issues Relating to VOC Regulation Cutpoints, Deficiencies, and Deviations. May 25, 1988 (the "Bluebook," cover only).

- U.S. EPA Region IX. Guidance Document for Correcting Common VOC & Other Rule Deficiencies. August 21, 2001 (the "Little Bluebook," cover only).