MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A04769 | In-Flight Anomaly Number -- | Contractor Report Number P-043 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title EXCESSIVE LEAKAGE LO2 FEEDLINE AT STA. 1129 (2.6 SCIM) |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1 |
| HCRIT -- | Sys_Lvl Y | Misc Codes A B C D E (X) F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE EXTERNAL TANK | PART# 82601000000 | SER/LOT# ET-4 | MANUFACTURER MMC |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE LO2 PROP FEEDLINE | PART# 82621011009 | SER/LOT# ET-4 | MANUFACTURER MMC |
| Test/Operation L - FLD | Prevailing Condtion -- | F / U F | Fail Mode -- | Cause -- |
| System PROPULSION | Defect -- | Material -- | Work Contact J. FINCHER | Fail Date 03/05/1982 |
| Received at MSFC 05/10/1982 | Date Isolated -- | FMEA Reference 2.1.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location KSC | Symptom MV - EXT LEAK | Time Cycle -- |
| Effectivity Text ET-4 AND SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 10/07/1987 | CN RSLV SBMT 05/10/1982 | Defer Date -- | Add Date -- | R/C Codes 2 - MFG -- -- |
| Assignee |
| Design R. ZAGRODSKY | Chief Engineer -- | S & MA D. NEWMAN | Project C. CRANE | Project MGR -- |
| Approval |
| Design R. ZAGRODSKY | Chief Engineer -- | S & MA D. NEWMAN | Project C. CRANE | Project MGR -- |
| PAC Assignee M. GLASS | PAC Review Complete MG | MSFC Closure Date 05/28/1982 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description REF: MARS T-53237 (PROB 'B' PV3-006911) 5/10/82 - DURING LEAK CHECK OF LO2 FEEDLINE FLANGE AT STA. 1129 A LEAK OF A 2.6 SCIM WAS DETECTED (MAX. ALLOWABLE BY PROCEDURE IS .5 SCIM GN(2). UPON DISASSY OF FEEDLINE FLANGES DISCOVERY OF PARTIALLY MASHED SEALS BETWEEN FLANGES. A REVIEW OF MAF TEST DATA REVEALED NO LEAK WAS DOCUMENTED ON THIS FLANGE |
| Contractor Investigation/Resolution 5/10/82 CAUSE - PRIMARY & SECONDARY FEEDLINE SEALS WERE DAMAGED DURING INSTALLATION AT MAF. IN- ADEQUATE CLEARANCE/MISALIGNMENT OF FLANGES EXTRUDED THE SEALS WITH A 'WIPING' & CLAMPING ACTION DURING BOLT INSTALLATION. ALSO THE LO2 FORWARD ELBOW STRUT (P/N 8263011036-031) WAS NOT ALIGNED PROPERLY. CORRECTIVE ACTION - ET-4 - SEALS WERE REPLACED AT KSC & SUCCESSFULLY RELEAKED TESTED. RECURRENCE CONTROL - ET-5 - PROPULSION LINES WERE INSTALLED IN 'F/A POSITION 3' WHERE BRIDGE CRANE IS USED & FLOWMETER MONITORED FOR LONGER PERIOD OF TIME. ET-6 - ALIGNMENT PINS WILL BE USED FOR FLANGE CLOSEOUT, TOOLING STRUTS WILL BE ATTACHED FORWARD OF ELBOW SECTION TO COMPRESS BELLOWS TO PROVIDE CLEARANCE FOR SEAL INSPECTION & ATTACHMENT. LWT-1 & SUBS - ALIGNMENT TOOL WILL BE PROVIDED TO GUIDE FLANGES TOGETHER PREVENTING ANY LATERAL MOVEMENT. ALSO LEAK TESTING WILL BE BY THE WATER DISPLACEMENT METHOD FOR INCREASED SENSI- TIVITY, HOWEVER LEAK QUAL WILL CONTINUE BY THE FLOWMETER METHOD. A BRIDGE CRANE INSTALLATION IN F/A POSITION 1 & 2 IS SCHEDULED ON FY83 FUNDING |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A04769 | IFA# -- | Contractor RPT# P-043 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# -- | Asmnt Part Name -- | Asmnt Serial/Lot# -- |
| HCRIT CD -- | FCRIT CD -- | CAUSE CD -- | FAIL MODE MV - EXT LEAK |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |