POLAR Spacecraft Status As of: Tues 05 Aug 03  12:00 EST

(Abbreviated edition:  changes from last week in bold border)

| Subsystem/ Component | NOAA-11H Standby PM STIP data only | NOAA-12D Standby AM STIP data only | NOAA-14J Standby AM STIP data only | NOAA-15K BACKUP AM GAC data only | NOAA-16L PRIMARY PM GAC&LAC data | NOAA-17M PRIMARY AM GAC&LAC data |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 09/23/88 | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 |
| CNTL OBP | OBP2 | OBP2 | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 |
| BUS | A-BUS XSU-1 | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS | DEGRADED (Y, Z- Gyros Failed) Reduced Gyro S/W | NOMINAL RGmode=Monitor | NOMINAL Rgmode=Disabled SS check Disabled when mode=YGC | OK Rgmode=Monitor Rgyro test planned for Fall 2003 Gyro-3 Off/Anom | NOMINAL Rgmode=Disabled Gyro channels swapped to AAA and Gyro#3 deselected on 29 July 14:30Z | NOMINAL Rgmode=Disabled |
| RXO | PRI BU random enables ETCUP +70 mSecs | PRI BU random enables | PRI BU random enables ETCUP –7.3 Msec | PRI ETCUP -8 mSec | PRI ETCUP –5.1 mSec | PRI ETCUP -1 msec |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | ON | ON | ON External Sync. Rephase Daily | ON External Sync, Rephase Daily. | ON External Sync, Rephase Enabled | ON Internal Synch Rephase Enabled |
| TIP SIDE | 1 | 1 | 1 | 2 Since 4/24/03 | 1 Analog telem drifting | 1 |
| DTRs | 1A, 2B, 3, 4A Safestate - 2B, | 1, 3, 4, 5B Safestate- 1B | 1, 2B, 3A, 5 Safestate- 1B | 1, 2, 3, 4 Safestate 1B EOT | 1,2,3,4A Safestate 3A 4B TOAR 418 (STIP only) | 1,2,3,4 Safestate=1B DTR2-SSR DTR5 TOAR 420 |
| VTX (APT data) | OFF | OFF since 7/12/03 Conflict with N15 back on 8/12/03 | OFF Since 8/14/02 (conflicts & poor AVHRR data) | 1 Conflict with N12 from 7/12 to 8/12 | INOP OFF since 11/15/00 | 2 |
| BTX | 2 | 1 | 2 | 1 | 1 | 2 |
| STX | 3 – TIP 1,2 - Playback | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 1, 2, 3 - degraded; 2 Omni–HRPT; 4- Playback | 1 – HRPT; 2– Playback; 4 – Playback 3 low power unused | 3 – HRPT TOAR424 low power 1&2 Playback 4 – TIP |
| POWER (Array offset, charge and eclipse states, sun angle) | Array Off -30 Since 6/19/02 Eclipse all year Sun angle 78 Steady Trend Batts 1-3= LRC VT1,2=6/8 VT3 = 8/11 Charge state safe trip disabled | ArrayOff -60 since 7/30/03 Eclipse Season Ends 8/25 Sun Angle at 32 trend down to 16 on 10/17 Batts 1&2=LRC V/T=4 | Array Off -45 Since 6/19/03 Eclipse Season Ends 8/15 Sun Angle at 30 trend down to 22 Batts 1-3= LRC Batt 1&3V/T=8/11 Batt2 VT=9/11 ) Shunt Degradation TOAR 425 | Array Off -45 Since 1/25/01 Eclipse Season Ended 4 Aug Sun Angle at 28 trend down to 14 on 10/8 Batts 1-3= LRC V/T=7/9 | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 65 Downtrend to 54 Batt2A TOAR403 Unregulated Temp Batts 1-3= LRC V/T=4/8 | Array Off. –35 Since 7/1/02 Eclipse all year Sun Angle at 68 Steady Trend Batts 1-3= LRC V/T=4/8 Batt2A TOAR 416 Unregulated Temp |
| AVHRR | OFF Failed Power Supply | ON Nominal | ON Scan Motor degraded 5/1/03 (but improving) STATUS=RED | ON Rare Scan motor surges. Last Incident 7/4/03 | ON Nominal (3B) 3A-B switch once per week over north pole. Last switch 1Aug 03 | ON Nominal (3A&B) 3A-B switch enabled |
| AMSU-A1 |  |  |  | ON Ch14 inoperative Ch11 inoperative | ON TOAR 415 on primary PLLO chans 9-14 bias shift. TOAR 417 on Backup PLLO Status=Yellow | ON TOAR 413 Chan-3 popcorn noise TOAR 414 on PLLO chans 9-14 bias shift. TOAR 421 on Channel-7 elevated NEDT’s noise |
| AMSU-A2 |  |  |  | ON | ON Space Position-2 | ON |
| AMSU-B |  |  |  | ON Bias in All Channels. Motor current surges most recent 7/12/03 | ON Space Position-3 | ON |
| HIRS | OFF Filter Wheel Anomaly | INOP Filter Wheel turned OFF 10/17/02. Electronics On | ON Operational | ON Operational FW in Hi power, FW Heaters OFF Filter Motor current surges. Last incident 7/12 New anomaly detected 7/29. Excess noise in space view channels 13-19 | ON Nominal | ON 1 Pixel cross track misalignment . |
| MSU | INOP OFF, Antenna Failed | INOP Scan Motor OFF since 3/12/03 Electronics ON. | ON Scan motor and antenna problems |  |  |  |
| SSU | ON |  | ON |  |  |  |
| DCS | ON | ON | ON | ON | ON Nominal | ON Nominal |
| SARR | ON Low signal |  | ON | ON-A All AGC Mode Intermittent failures for 243MHz A&B | ON-A All AGC Mode (B-side Receiver in FG mode) 243 MhZ INOPERATIVE. | ON-A Nominal All AGC Mode |
| SARP | ON Nominal |  | OFF Failed Power Supply | ON Nominal RCVR B/W = 2 | ON Nominal RCVR B/W = 2 | ON Nominal |
| SEM |  | ON Elec-CH-HVPS=4 Prot-CH-HVPS=0 | ON Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Telescopes inoperative | ON Nominal E-CDEM-HVPS=2 Since 1/14/03 P-CDEM-HVPS=0 | ON Nominal E-CDEM-HVPS=4 P-CDEM-HVPS=4 since 4/15/03 | ON Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 since 2/18/03 |
| SBUV | INOP Grating motor OFF since 5/29/03 Electronics and Heater remain ON |  | ON Occasional Reduced Grating Drive Motion Reduced operations profile started 6/5/03 |  | ON Backup Diffuser in use since 6/16/03.) Primary =TOAR 426 antenna deploy anomaly, AMSU EMI causing erratic Behavior from PMT cathod, in range 3 No corrective action possible | ON Nominal Anode Mode |
| SADPOS |  |  |  | N/A | ON ENABLED MFactor =50% | ON ENABLED |
|  | N11 | N12 | N14 | N15 | N16 | N17 |

COMMENTS/CHANGES:

NOAA-11	No changes since previous report.

NOAA-12.  	 To further alleviate a shunt degradation problem isolated by EMOSS POC Andy Miller, the N12 solar array offset was

again increased to –60 degrees (from –45) on 30 July.  Preliminary analysis has indicated that this had the desired affect of reducing charge current (and shunt workload).  This offset should remain in place until late September when the sun angle on the spacecraft will be such that the 60 degree offset solar array may begin to shade the sun sensor.  In that situation, either the array will have to be moved back to at least –30 degrees or a “software/configuration workaround” will have to be implemented that prevents this sun sensor shading situation from causing an operational problem.

NOAA-14:	N14 AVHRR scan motor current continued to improve during the past week as it has for the past 9 weeks.  Recently it

has begun to “gravitate” into a range  what could be considered nominal.  In addition, and imagery data has also continued to improve.  (Illustrations 1 & 2).  An upgrade in color status (currently RED) is not under consideration at this time because of the inconsistency of this component in maintaining nominal values over an extended period of time.

NOAA-15:	EMOSS has received a report from user Robert Levin that since JD210 July 29 the N15 HIRS channels 13-19 have

all shown increasing Space view noise and that currently 3 channels are exceeding their spec limits.  Users have been unable to determine the cause of this violation and EMOSS analysis of N15 HIRS telemetry has revealed very stable filter motor currents (no surges) and very stable voltages, temps, product monitor values and imagery on the SOCC PIDES system (illustration 3a, 3b, 4 and 5).  A preliminary analysis conducted outside of EMOSS has concluded that this anomaly indicates that the noise increase in the shortwave channels does not appear to be related to the typical NOAA-15/HIRS filter wheel problem.  However, the following possibilities can not be ruled out at this point:   1). The possibility of solar contamination in the fore optics.   2). Shortwave detector problem.    3). Problems in the electronics. 4). Other causes.  The possibility of solar contamination can be ruled out if this pattern does not change with solar geometry.   Will Kent is investigating for EMOSS.  An Incident Report has been generated in SITARS and an Event Report is being generated.  A TOAR is under consideration and will be discussed further at the TOAR Board to be held on 5 Aug.

Eclipse season (defined as a minimum solar array patch current in excess of 100 mAmp; enough to power the entire spacecraft without battery input) ended on 4 Aug at approximately 17:00Z.  Some “shading” of the solar array may continue for another day or two but all spacecraft power is now being provided exclusively by the solar array.  (Illustration 6)

NOAA-16: 	Preliminary analysis conducted by EMOSS ADACS engineer Jim Sheperd has indicted that the gyro channel swap that

was implemented on 29 July was successful in eliminating the “excessive” yaw update values that were periodically observed prior to the swap.  The final determination on the success or failure of this operation to alleviate that problem is primarily time dependant.

The macro developed by EMOSS engineer Jon Woodward to switch the AVHRR to Channel 3A over the northern

polar region was once again triggered nominally on 1 Aug.  No requests for additional triggerings of this macro have been received by EMOSS since that 1 Aug operation and it is currently unknown by EMOSS engineers whether any more will be required.

NOAA-17:	RF testing continues at Svaalbard. These tests dump GAC data over the Svaalbard site once or twice a day using a

variable combination of S-band transmitters and frequencies (often STX-4).  These tests are being conducted to validate the Svaalbard ground station capabilities ability to support METOP and will continue out of the schedule until August 23rd.  STX-4 appears to be performing in a nominal manner.

NOAA-N 	Level 2 Data base validation (Phase One) was completed by the EMOSS team and delivered to NASA as scheduled (25

July) for their review despite some difficulties experienced with performing the process on the Dev Rail.  A schedule for TTS time during the month of August when NASA and EMOSS engineers can review the data base to a Level 3 (Phase One) is being generated and will be distributed in the coming days.  Phase Two data base validation will require CWS and PACS upgrades to be complete before being implemented and whose completion status remains undetermined at the present time.

Misc:	EMOSS engineer Jim Walters supported the MHS pre flight model hand over review in Sunnyvale CA between 28

and 30 July and has generated a trip report detailing the highlights of that trip.

### Illustration 1:  N14 AVHRR Scan Motor Current 25 July through 3 Aug 03

1 Aug 03					2 Aug 03			5 Aug 03

### Illustration 2:  N14 representative AVHRR Imagery 1, 2 and 5 Aug 2003

Illustration 3a:  N15 HIRS Health #1, before, during and after channel 13-19 noise anomaly started (25 July through 3 Aug 03)

Illustration 3a:  N15 HIRS Health #2, before, during and after channel 13-19 noise anomaly started (25 July through 3 Aug 03)

N15 HIRS 29 Jul @ 01:30 PRE-noise	         N15 HIRS 29 Jul 23:00 POST-noise

N15 HIRS image 2 Aug 03				N15 HIRS Image 5 Aug 03

Illustration 4: N15 HIRS imagery analysis before during and after noise reported

Illustration 5: N15 HIRS Channel 14, 16 and 17 out of spec graphics

Illustration 6:  N15 Representative EPS telemetry depicting the end of eclipse season.

Illustration 7:  N16 Yaw update values before, during and after gyro channel swap

Illustration 7:  N16 Yaw update value Statisics before, during and after gyro channel swap

POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING July 25, 2003

| DAY/DATE | NOAA-11 | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 |
| --- | --- | --- | --- | --- | --- | --- |
| FRI. 07/18 | -1149 msec | -113 msec | -044 msec | +049 msec | -021 msec | -008 msec |
| SAT. 07/19 | -1149 msec | -120 msec | -044 msec | +049 msec | -022 msec | -007 msec |
| SUN. 07/20 | -1149 msec | -125 msec | -043 msec | +048 msec | -022 msec | -006 msec |
| MON. 07/21 | -1149 msec | -131 msec | -045 msec | +047 msec | -022 msec | -004 msec |
| TUE. 07/22 | -1149 msec | -141 msec | -045 msec | +050 msec | -022 msec | -003 msec |
| WED. 07/23 | -1149 msec | -145 msec | -040 msec | +049 msec | -022 msec | -003 msec |
| THU. 07/24 | -1149 msec | -151 msec | -039 msec | +050 msec | -022 msec | -001 msec |

EMOSS POC for this chart is JIM SHEPHERD

NOAA-12:  As of 09/03/02 the TIP clock is corrected daily by +70 msec to compensate for drift.

NOAA-14:  As of 04/23/03 the TIP clock is corrected daily by –-7.3 msec to compensate for drift.

NOAA-15:  As of 04/23/03 the TIP clock is corrected daily by –-8 msec to compensate for drift.

NOAA-16:  As of 04/23/03 the TIP clock is corrected daily by –5.1 msec to compensate for drift.

NOAA-17:  As of 04/23/03 the TIP clock is corrected daily by -1 msec to compensate for drift.

N12:  ADDED 1250 mSecs to spacecraft command clock on 6 June

N14:  SUBTRACTED 150 msec from spacecraft command on 10 June.

N15:  ADDED 100 msec to spacecraft command clock on 10 June.

N16:  SUBTRACTED 100 msec from spacecraft command clock on 10 June.

N17:  SUBTRACTED 100 msec from spacecraft command clock on 10 June.

Two weeks of N17 CPU Error Scrubs

### Red/Circle = CPU#1     Black/X = CPU#2

NOAA-17 Scrubber Hits from 21 Jul 2003 through 4 Aug 2003:

PACS DATA AVAILABILITY (%)

July 25, 2003 through July 31, 2003

JDAY 206-212

|  |  |  | NOAA15 | NOAA14 | NOAA11 | NOAA16 | NOAA17 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Friday | 07/25 | 206 | 100.0 | 100.0 | 100.0 | 100.0 | 100.0 |
| Saturday | 07/26 | 207 | 100.0 | 100.0 | 85.7(a) | 100.0 | 100.0 |
| Sunday | 07/27 | 208 | 100.0 | 100.0 | 84.8(b) | 100.0 | 100.0 |
| Monday | 07/28 | 209 | 99.9(c) | 100.0 | 100.0 | 100.0 | 100.0 |
| Tuesday | 07/29 | 210 | 99.9(d) | 100.0 | 100.0 | 100.0 | 100.0 |
| Wednesday | 07/30 | 211 | 99.9(e) | 100.0 | 100.0 | 100.0 | 100.0 |
| Thursday | 07/31 | 212 | 99.9(f) | 100.0 | 100.0 | 100.0 | 100.0 |

Comments:

- Rev 76511/F: S4A noisy; 98.1% recovered 12DL 59 PE.

- Rev 76519/F: S4A noisy; 98.0% recovered 5DL 11PE.

- Rev 27059/F: G1A noisy; 99.4% recovered 3DL 4PE.

- Rev 27066/F: G2B noisy; 98.3% recovered.

- Rev 27080/F: G3B noisy; 98.5% recovered 4DL 2PE.

- Rev 27106/W: G1A noisy; 99.1% recovered.

DTR Inf. (*):

NOAA-11        	DTR 1B -Inoperative.

DTR 2A/B -Frequently noisy

DTR 4B -Frequently noisy

DTR 5A/B -Inoperative

NOAA-12	DTR 5A -Inoperative.

DTR 2B -Occasionally noisy and short

NOAA-14	DTR 4A/B -Inoperative.

DTR 3B -Unreliable playbacks, Removed from operations.

DTR 2A -Inoperative, DOY/200

NOAA-15	DTR 5A/B - Inoperative

NOAA-16            DTR 5A/B -Inoperative

DTR 3A -safe state change 1B

DTR 4B –Inoperative 1/12/03

NOAA-17	DTR 5A/B-Inoperative 2/16/03 Anomaly

Acronyms:

DL – Drop lock(s)	PE - Parity Error(s)			DQR - Data Quality Report

BE - Bit Error(s)	DAR - Data Accountability Report	MFR - Multi-Function Receiver