POLAR Spacecraft Status As of: Tues 29 July 03  12:00 EST

(Abbreviated edition:  changes from last week in bold border)

| Subsystem/ Component | NOAA-11H Standby PM STIP data only | NOAA-12D Standby AM STIP data only | NOAA-14J Standby AM STIP data only | NOAA-15K BACKUP AM GAC data only | NOAA-16L PRIMARY PM GAC&LAC data | NOAA-17M PRIMARY AM GAC&LAC data |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 09/23/88 | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 |
| CNTL OBP | OBP2 | OBP2 | OBP2 OBP1 inoperative | OBP2 Non-encrypted command testing at Svaalbard 21-25 July | OBP2 | OBP2 |
| BUS | A-BUS XSU-1 | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS | DEGRADED (Y, Z- Gyros Failed) Reduced Gyro S/W | NOMINAL RGmode=Monitor | NOMINAL Rgmode=Disabled SS check Disabled when mode=YGC | OK Rgmode=Monitor Rgyro test planned for Fall 2003 Gyro-3 Off/Anom | NOMINAL Rgmode=Disabled Gyro channels swapped to AAA on 29 July 14:30Z | NOMINAL Rgmode=Disabled |
| RXO | PRI BU random enables ETCUP +70 mSecs | PRI BU random enables | PRI BU random enables ETCUP –7.3 Msec | PRI ETCUP -8 mSec | PRI ETCUP –5.1 mSec | PRI ETCUP -1 msec |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | ON | ON | ON External Sync. Rephase Daily | ON External Sync, Rephase Daily. | ON External Sync, Rephase Enabled | ON Internal Synch Rephase Enabled |
| TIP SIDE | 1 | 1 | 1 | 2 Since 4/24/03 | 1 Analog telem drifting | 1 |
| DTRs | 1A, 2B, 3, 4A Safestate - 2B, | 1, 3, 4, 5B Safestate- 1B | 1, 2B, 3A, 5 Safestate- 1B | 1, 2, 3, 4 Safestate 1B EOT | 1,2,3,4A Safestate 3A 4B TOAR 418 (STIP only) | 1,2,3,4 Safestate=1B DTR2-SSR DTR5 TOAR 420 |
| VTX (APT data) | OFF | OFF since 7/12/03 Conflict with N15 back on 8/12/03 | OFF Since 8/14/02 (conflicts & poor AVHRR data) | 1 Conflict with N12 from 7/12 to 8/12 | INOP OFF since 11/15/00 | 2 |
| BTX | 2 | 1 | 2 | 1 | 1 | 2 |
| STX | 3 – TIP 1,2 - Playback | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 1, 2, 3 - degraded; 2 Omni–HRPT; 4- Playback | 1 – HRPT; 2– Playback; 4 – Playback 3 low power unused | 3 – HRPT TOAR424 low power 1&2 Playback 4 – TIP |
| POWER (Array offset, charge and eclipse states, sun angle) | Array Off -30 Since 6/19/02 Eclipse all year Sun angle 78 Steady Trend Batts 1-3= LRC VT1,2=6/8 VT3 = 8/11 Charge state safe trip disabled | ArrayOff -45 since 7/10/03 move to –60 planned for 7/30 Eclipse Season Ends 8/25 Sun Angle at 34 trend down to 16 on 10/17 Batts 1&2=LRC V/T=4 | Array Off -45 Since 6/19/03 Eclipse Season Ends 8/15 Sun Angle at 31 trend down to 22 Batts 1-3= LRC Batt 1&3V/T=8/11 Batt2 VT=9/11 ) Shunt Degradation TOAR 425 | Array Off -45 Since 1/25/01 Eclipse Season Ends 8/4 Sun Angle at 291 trend down to 14 on 10/8 Batts 1-3= LRC V/T=7/9 | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 66 Start new trend down to 54 degs on 1 Nov Batt2A Temps TOAR 403 Batts 1-3= LRC V/T=4/8 | Array Off. –35 Since 7/1/02 Eclipse all year Sun Angle at 68 Steady Trend Batts 1-3= LRC V/T=4/8 Batt2A temp TOAR 416 |
| AVHRR | OFF Failed Power Supply | ON Nominal | ON Scan Motor degraded 5/1/03 (but improving) STATUS=RED | ON Rare Scan motor surges. Last Incident 7/4/03 | ON Nominal (3B) 3A-B switch once per week over north pole next 10 weeks. Last switch 21 July 23:46 | ON Nominal (3A&B) 3A-B switch enabled |
| AMSU-A1 |  |  |  | ON Ch14 inoperative Ch11 inoperative | ON TOAR 415 on primary PLLO chans 9-14 bias shift. TOAR 417 on Backup PLLO Status=Yellow | ON TOAR 413 Chan-3 popcorn noise TOAR 414 on PLLO chans 9-14 bias shift. TOAR 421 on Channel-7 elevated NEDT’s noise |
| AMSU-A2 |  |  |  | ON | ON Space Position-2 | ON |
| AMSU-B |  |  |  | ON Bias in All Channels. Motor current surges most recent 7/12/03 | ON Space Position-3 | ON |
| HIRS | OFF Filter Wheel Anomaly | INOP Filter Wheel turned OFF 10/17/02. Electronics On | ON Operational | ON Operational FW in Hi power, FW Heaters OFF Filter Motor current surges. Last incident 7/12 | ON Nominal | ON 1 Pixel cross track misalignment . |
| MSU | INOP OFF, Antenna Failed | INOP Scan Motor OFF since 3/12/03 Electronics ON. | ON Scan motor and antenna problems |  |  |  |
| SSU | ON |  | ON |  |  |  |
| DCS | ON | ON | ON | ON | ON Nominal | ON Nominal |
| SARR | ON Low signal |  | ON | ON-A All AGC Mode Intermittent failures for 243MHz A&B | ON-A All AGC Mode (B-side Receiver in FG mode) 243 MhZ INOPERATIVE. | ON-A Nominal All AGC Mode |
| SARP | ON Nominal |  | OFF Failed Power Supply | ON Nominal RCVR B/W = 2 | ON Nominal RCVR B/W = 2 | ON Nominal |
| SEM |  | ON Elec-CH-HVPS=4 Prot-CH-HVPS=0 | ON Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Telescopes inoperative | ON Nominal E-CDEM-HVPS=2 Since 1/14/03 P-CDEM-HVPS=0 | ON Nominal E-CDEM-HVPS=4 P-CDEM-HVPS=4 since 4/15/03 | ON Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 since 2/18/03 |
| SBUV | INOP Grating motor OFF since 5/29/03 Electronics and Heater remain ON |  | ON Occasional Reduced Grating Drive Motion Reduced operations profile started 6/5/03 |  | ON Backup Diffuser in use since 6/16/03. (Imagery has improved) Primary diffuser has antenna deploy anomaly, TOAR 426 AMSU EMI causing erratic Behavior from PMT cathod, in range 3 No corrective action possible | ON Nominal Anode Mode |
| SADPOS |  |  |  | N/A | ON ENABLED MFactor =50% | ON ENABLED |
|  | N11 | N12 | N14 | N15 | N16 | N17 |

COMMENTS/CHANGES:

NOAA-11	No changes since previous report.

NOAA-12.  	 In analyzing a larger than usual data set on N12, EMOSS power engineer Andy Miller has noticed a significant

number of small surges in bus voltage that is indicative of continued shunt stress which motivated the recent previous two array moves to –45 degree offset.  Therefore, Andy will oversee an additional move of the N12 offset to –60 degree offset scheduled for Weds, 30 July.  Furthermore, at the beginning of October the sun angle (relative to the array position) will begin to shade the sun sensor and the array will have to moved again to a position of –30 degree offset for the duration of that month.

NOAA-14:	N14 AVHRR scan motor current continued to improve during the past week as it has for the past 8 weeks.  Recently it

has begun to fluctuate in what could be considered nominal values.  Current images from N14 show good to poor image quality.

NOAA-15:	Svalbard unencrypted command tests using STX-4 were performed each day from 21 through 25 July.  In general these

tests were very successful with Svalbard proving their ability to command the POES spacecraft in clear mode using

NOOP commands from both antenna 1 and 2.  Some difficulties in the timing of commanding (between the Fairbanks CDA and Svalbard) were encountered but overall the concept objective was achieved.

NOAA-16: 	EMOSS ADACS engineer Jim Sheperd chaired a “Gyro Summit” between NOAA, NASA and Lockheed engineers on

24 July because of concerns about the performance of N16’s gyro characteristics. The primary topics discussed at this meeting were as follows:

1.     NOAA-16 IMU performance, and related issues, plans for  configuration changes

2.     Plans for RGYRO testing and requirements/preparations for conducting the test

- Other related concerns with this series IMU (NOAA-15, DMSP, etc.)

Primary action items originating from the meeting included the following:

1)  Swap N16 gyro channel assignments.  This was done Tuesday, 29 July at 14:30Z:  The previous N16 gyro

assignments were: Gyro-2: Z/Pitch on chan-B,   Gyro-3: X/Yaw and Y/Roll on chan-B,  Gyro-1:  not used

The new gyro assignments are now:  Gyro-1: Z/Pitch and Y/Roll on chan-A  Gyro 3, X/Yaw on chan-A,

Gyro-2 deselected.  Jim Sheperd oversaw this operation.

- Study the effects of the DMSP Rgyro software test and determine the implications on a proposed N15

Rgyro software test.  The analysis report on this DMSP operation is due to EMOSS engineer Jim

Sheperd by 8 August.  Nodal analysis review per POES will be undertaken.

- Generate a draft N16 Rgyro test plan for N15 by 18 August with a test implementation date sometime in

the Fall of 2003 after the NOAA-N end to end test..

The macro developed by EMOSS engineer Jon Woodward to switch the AVHRR to Channel 3A over the northern

polar region will be triggered 28 July.  The next triggering of this macro is expected to be 1 August.

NOAA-17:	RF testing continues at Svaalbard. These tests dump GAC data over the Svaalbard site once or twice a day using a

variable combination of S-band transmitters and frequencies (often STX-4).  These tests are being conducted to validate the Svaalbard ground station capabilities ability to support METOP and will continue out of the schedule until August 23rd.  STX-4 appears to be performing in a nominal manner.

NOAA-N 	Level 2 Data base validation (Phase One) was completed by the EMOSS team and delivered to NASA as scheduled (25

July) for their review despite some difficulties experienced with performing the process on the Dev Rail.  A schedule for TTS time during the month of August when NASA and EMOSS engineers can review the data base to a Level 3 (Phase One) is being generated and will be distributed in the coming days.  Phase Two data base validation will require CWS and PACS upgrades to be complete before being implemented.  On 24 July EMOSS POC’s Azi Dinat and Jeff Devine met with the NOAA software managers to discuss methods by which to improve the efficiency of data base generation and distribution using the Dev Rail a number of process improvements originated from this meeting including improving coordination among Dev Rail users with via a more robust “scheduling mechanism” and adding another disk to the Dev Rail to serve as a “work in progress” area from which finished products can be copied to the Base area which will serve as the area that provides configuration controlled copies of each product.

Misc:	EMOSS engineer Jim Walters is supporting the MHS pre flight model hand over review in Sunnyvale CA between 28

and 30 July.  A trip report will be generated by Jim regarding the highlights of this meeting and attached to a future weekly report.

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING July 25, 2003

| DAY/DATE | NOAA-11 | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 |
| --- | --- | --- | --- | --- | --- | --- |
| FRI. 07/18 | -1149 msec | -113 msec | -044 msec | +049 msec | -021 msec | -008 msec |
| SAT. 07/19 | -1149 msec | -120 msec | -044 msec | +049 msec | -022 msec | -007 msec |
| SUN. 07/20 | -1149 msec | -125 msec | -043 msec | +048 msec | -022 msec | -006 msec |
| MON. 07/21 | -1149 msec | -131 msec | -045 msec | +047 msec | -022 msec | -004 msec |
| TUE. 07/22 | -1149 msec | -141 msec | -045 msec | +050 msec | -022 msec | -003 msec |
| WED. 07/23 | -1149 msec | -145 msec | -040 msec | +049 msec | -022 msec | -003 msec |
| THU. 07/24 | -1149 msec | -151 msec | -039 msec | +050 msec | -022 msec | -001 msec |

EMOSS POC for this chart is JIM SHEPHERD

NOAA-12:  As of 09/03/02 the TIP clock is corrected daily by +70 msec to compensate for drift.

NOAA-14:  As of 04/23/03 the TIP clock is corrected daily by –-7.3 msec to compensate for drift.

NOAA-15:  As of 04/23/03 the TIP clock is corrected daily by –-8 msec to compensate for drift.

NOAA-16:  As of 04/23/03 the TIP clock is corrected daily by –5.1 msec to compensate for drift.

NOAA-17:  As of 04/23/03 the TIP clock is corrected daily by -1 msec to compensate for drift.

N12:  ADDED 1250 mSecs to spacecraft command clock on 6 June

N14:  SUBTRACTED 150 msec from spacecraft command on 10 June.

N15:  ADDED 100 msec to spacecraft command clock on 10 June.

N16:  SUBTRACTED 100 msec from spacecraft command clock on 10 June.

N17:  SUBTRACTED 100 msec from spacecraft command clock on 10 June.

PACS DATA AVAILABILITY (%)

July 18, 2003 through July 24, 2003

JDAY 199-205

|  |  |  | NOAA15 | NOAA14 | NOAA11 | NOAA16 | NOAA17 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Friday | 07/18 | 199 | 100.0 | 100.0 | 100.0 | 100.0 | 100.0 |
| Saturday | 07/19 | 200 | 100.0 | 100.0 | 100.0 | 100.0 | 100.0 |
| Sunday | 07/20 | 201 | 100.0 | 100.0 | 100.0 | 100.0 | 99.9(a) |
| Monday | 07/21 | 202 | 100.0 | 100.0 | 100.0 | 100.0 | 99.9(b) |
| Tuesday | 07/22 | 203 | 86.9(c) | 100.0 | 100.0 | 100.0 | 94.6(d) |
| Wednesday | 07/23 | 204 | 99.9(e) | 100.0 | 100.0 | 100.0 | 100.0 |
| Thursday | 07/24 | 205 | 100.0 | 100.0 | 100.0 | 100.0 | 100.0 |

Comments:

- Rev 05564/F: G4B noisy; 99.4% recovered.

- Rev 05575/W: G2B noisy; 99.9% recovered.

- Rev 26968/F: G1A noisy; 95.8% recovered 1PE.

- Rev 05585/F: L2A noisy; 91.5% recovered.

- Rev 26979/F: G2A noisy; 99.8% recovered 1PE.

DTR Inf. (*):

NOAA-11        	DTR 1B -Inoperative.

DTR 2A/B -Frequently noisy

DTR 4B -Frequently noisy

DTR 5A/B -Inoperative

NOAA-12	DTR 5A -Inoperative.

DTR 2B -Occasionally noisy and short

NOAA-14	DTR 4A/B -Inoperative.

DTR 3B -Unreliable playbacks, Removed from operations.

DTR 2A -Inoperative, DOY/200

NOAA-15	DTR 5A/B - Inoperative

NOAA-16            DTR 5A/B -Inoperative

DTR 3A -safe state change 1B

DTR 4B –Inoperative 1/12/03

NOAA-17	DTR 5A/B-Inoperative 2/16/03 Anomaly

Acronyms:

DL – Drop lock(s)	PE - Parity Error(s)			DQR - Data Quality Report

BE - Bit Error(s)	DAR - Data Accountability Report	MFR - Multi-Function Receiver

N17 Weekly CPU Scrub Report and other standard features of this weekly report will return next week.