CMS ENDCAP MUON

# POSITION MONITORING SYSTEM

QUALITY CONTROL MANUAL

Draft

May 11, 2001

EMPMS Group:

Fermilab, Northeastern University, Petersburg Nuclear

Physics Institute, University of Wisconsin-Madison

Abstract:

In this note, we designate the set of measurements, tests, logging, archiving

for the Quality Assurance of  Endcap Position monitoring system elements, for

Assembly, Installation, and system maintenace.

CONTENTS:

- Introduction

- Quality Control, Quality Assurance, Calibration Outline

- Recording and Archiving Information, Tracking

  - Barcode

3.1.2  Items

3.1.3  Details

4.  Quality Control of  System  Parts

  - Mechanical Parts

4.2  Electronics Parts, Printed circuit boards

4.3  Sensors, optical parts

5.  Quality Control of   System  Subassemblies

  - Mechanical sub assemblies

  - Mechanical assemblies

5.3   Commercial Electronic Units

5.4   Custom Electronics fabrications

5.5   DCOPs sensor assemblies

5.6   Cable assemblies/harnesses

5.7   Low voltage power supplies

6. Calibrations, Testing, Certification of   System  Subassemblies

6.1   Analog sensor calibrations

6.2   DCOPS sensor calibrations

6.3   Electronics performance and burn in tests

  - Cable assembly/harness testing

  - SLM string test-certification on test bench

  - Transfer Plate Measurements, calibration

6.7   Z tube measurements

6.8   MAB DCOPS sensor measurements, tests, calibrations

6.9   Tests, measurements, certifications of layer SLMs

CONTENTS:

7. Quality Control during System Installation-Commissioning

7.1    Tests, measurements, certifications of layer SLMs

7.2    Tests, measurements, certifications of each YE (n)

DAQ, electronics, laser gate, low voltage systems,

grounds, earth shield, mechanical installations

  - Tests, measurements, certifications of Transfer Line systems

7.4    Optical path, safety, mechanical protection, CSC

grounds, earth shield, mechanical installation –tests

and certification

8. Quality Assurance during System Operation and Maintenance

8.1    Tests, measurements, re-certifications of layer SLMs

in open maintenance and after re-closure

8.2    Tests, measurements, re-certifications of each YE (n)

DAQ,  lasers and laser gates, low voltage systems,

re-check grounds, shields, mechanical installations

in open maintenance and after re-closure

  - Tests, measurements, re-certifications of Transfer Line systems

after re-closure

8.4    Optical path protection, CSC  grounds, earth shield, –tests

and re-certification

1. Introduction

This document describes the elements of Quality Control and Assurance

during the procurement of parts, commercial production of  OEM, custom parts and

subassemblies; group calibrations, measurements, testing, and certification of sensors

and subassemblies; group quality assurance procedures in Installation and commissioning.

The Quality Control-Quality Assurance plan encompasses all of these

phases and is characterized differently in each phase. There are many detailed system elements with specific requirements. We divide the system into two main outlines:

- Electronics

  - Commercial electronic units (Agilent Data Acquisition, serial port hubs)

  - Electronic circuit parts  (ADCs, DSPs, CPLDs, Flash Memory)

  - Custom printed circuit boards

  - Custom circuit board assemblies (DCOPS Interface, Analog Interface, Low Voltage distribution, laser gating, Temperature sensor Interface)

  - Low Voltage supplies

  - Custom cable assemblies/harnesses

  - Analog Sensors and custom connectors

  - Temperature sensors and custom connectors

  - DCOPS Optical Sensors and Kapton cables

  - Laser module assemblies

  - Grounds, electronics protection, testing

- Mechanical

  - Alignment sensor mounting hardware for CSCs (ME1, ME2, ME3, ME4)

  - Alignment sensor mounting hardware for MABs

  - Transfer Line laser mount-articulation assemblies

  - Transfer plate mechanical parts

  - DCOPS sensor mechanical parts

  - DCOPS sensor mechanical assemblies

  - SLM Laser source articulation subassemblies

  - Transfer plate mechanical assemblies

  - Earth ground electronics enclosures, Transfer plate covers, Optical path tubes

  - Z tubes and mounts

2. Quality Control, Quality Assurance, Calibration Outline

Procedures, methods, and acceptance criteria are described in detail.

At present, the tests described are considered mandatory. Non-conformity

procedures are included which demonstrate tracking ability. All information

will  be in a common database used by all collaborators and sites. At present,

productions of given sub-assemblies, sensors, electronics, etc are likely to be

site specific, so all Quality control for a given production, calibration,

certification can be coordinated at one site.

The Quality control tests are divided into four principle parts:

- Tests/measurements  of  commercial parts and sub assemblies

- Tests/measurements  of  assemblies, sensors in calibration and certification

- Tests/measurements in subsystem certification (burn-in, performance, reliability)

- Tests/measurements/configuration checks in Installation/commissioning

Tests in each stage have pass/fail criteria specified. Testing will be by sampling for each production batch of parts and subassemblies. Some subassemblies are checked in great detail in assembly measurements and calibrations and in electronics burn-in/reliability tests. Any failures will be monitored and will trigger further extended testing to establish the integrity of the production and compliance of the vendor with QC specified in the contract.

In the other stages, tests/measurements apply to all sensors and assemblies.

3. Recording and Archiving Information, Tracking

All sub assemblies and assemblies in the system will have an ID number

corresponding  to a computer readable bar code. Minor parts used in sub assemblies

will  be  identified by a batch number and an associated sub assembly group.

The barcode marking sub assemblies and assemblies has the following

structure:

- 52       NN        LL P       QQQ            LMN              M

CMS   EMU     SITE    ITEM    DETAIL         S N          Check digit

3.1.1 Operational Sites

| Production Center | Code | Fabrications, Tasks, Coord |
| --- | --- | --- |
| Fermilab | 01 | Analog sensors, DAQ, Mechanical parts, LV, electronics, cables |
| Northeastern U | 02 | DCOPS sensors, electronic enclosures, calibrations |
| Petersburg Nuclear Phys Ins | 03 | DCOPS electronics |
| U Wisconsin- Madison | 04 | Mechanical parts, Integration, Project management |
| Mechanical Fabricator | 05 | CNC mechanical parts |
| Electrical Fabricator | 06 | PCB assembly-test |
| Cable Fabricator | 07 | Cable/harness assembly |

    - Alignment System Items

| Item | Code | Tag | Configure |
| --- | --- | --- | --- |
| ME1-3 Outer sensor mount | 01 | ID | P = Left P = Right |
| ME1-3 Inner sensor mount | 02 |  | P = Left P = Right |
| ME1-2 Outer sensor mount | 03 |  |  |
| ME1-2 Inner sensor mount | 04 |  |  |
| ME234-2 Outer sensor mount | 05 |  | P = Left P = Right |
| ME234-2 Inner sensor mount | 06 |  |  |
| ME234-2 Outer tower mount | 07 |  | P = Left P = Right |
| ME2-1 Outer sensor mount | 08 |  | P = Left P = Right |
| ME2-1 Inner sensor mount | 09 |  |  |
| ME3-1 Outer sensor mount | 10 |  | P = Left P = Right |
| ME3-1 Inner sensor mount | 11 |  |  |
| ME4-1 Outer sensor mount | 12 |  | P = Left P = Right |
| ME4-1 Inner sensor mount | 13 |  |  |
| MAB DCOPS sensor mount | 14 |  |  |
| Transfer plate support ME1 | 15 |  |  |
| Transfer plate support ME2, ME3, ME4 | 16 |  |  |
| Item | Code | Tag | Configure |
| Transfer laser support/actuator | 17 | ID | P= offset1 P= offset2 |
| Transfer Plate ME1 | 18 | ID | P= offset1 P=offset2 |
| Transfer Plate ME2 | 19 | ID | P=offset1 P=offset2 P=offset3 |
| Transfer Plate ME3 | 20 | ID | P=offset1 P=offset2 P=offset3 P=special |
| Transfer Plate ME4 | 21 | ID | P=offset1 P=offset2 P=offset3 P=special |
| Z tube assembly ME1-ME2 | 22 | ID |  |
| Z tube assembly ME2-ME3 | 23 | ID |  |
| Z tube assembly ME3-ME4 | 24 | ID |  |
| DCOPS sensor box | 25 | ID |  |
| DCOPS CCD-FEB assembly | 26 | ID |  |
| DCOPS sensor assembly | 27 | ID | P=Left P=Right |
| LPX50 R sensor assembly | 28 | ID | P= Outer P=Inner |
| Transfer-MEN2 outer cable extension | 29 | ID |  |
| MEN2-MEN1 inner cable extension | 30 | ID |  |
| LCP8-10 Z Potentiometer Assembly | 31 | ID | P= Input P=Output |
| Z4MW100 Laser distance sensor | 32 | ID |  |
| AD592 T sensor assembly | 33 | ID | P=Inner P=Outer P=Tertiary |
| AppGeo900 Inclinometer Assembly | 34 | ID |  |
| DCOPS readout board | 35 | ID |  |
| DCOPS LVDS cable (includes loop around Barrel) | 36 | ID | P=pathN |
| R sensor SLM cable | 37 | ID | P=pathN |
| T sensor SLM cable | 38 | ID | P=pathN |
| DCOPS JTAG,LVDS-RS485 Interface, Low voltage distribution Board | 39 | ID |  |
| Analog Interface, Low Voltage Distribution board | 40 | ID |  |
| DCOPS Interface-Serial Port, Interface-Interface cable | 41 | ID | P=pathN |
| AGILENT Input- Analog Inteface cable | 42 | ID | P=pathN |
| Laser Driver cable (3 SLM Station) | 43 | ID | P=pathN |
| SLMn T sensor – T Interface cable | 44 | ID | P=pathN |
| ITEM | Code | Tag | Configure |
| DCOPS power cable | 45 | ID | P=pathN |
| ANALOG power cable | 46 | ID | P=pathN |
| Transfer Z cable (SLM) | 47 | ID | SLM# |
| Transfer Inclinometer cable (SLM) | 48 | ID | SLM# |
| SLM Laser driver cable (SLM) | 49 | ID | P=pathN |
| 12v Low Voltage Regulator (DCOPS) | 50 |  | P=layer |
| 12v Low Voltage Regulator (filtered) (ANALOG) | 51 |  | P=layer |
| Transfer Laser driver cable | 52 |  | P=location |
| AGILENT- T sensor Interface cable | 53 |  | P=layer |
| AGILENT Data Acquisition Unit | 54 |  | P=layer |
| Ethernet-Serial Port HUB | 55 |  | P=layer |
| T sensor Interface Unit | 56 |  | P=layer |
| Laser driver Unit | 57 |  | P=layer |
| Inner MAB DCOPS sensor | 58 |  | P=pathN |
| Inner MAB DCOPS sensor mount | 59 |  | P=pathN |

    - DETAIL CODE

To describe special conditions, geometry reflections, mirror configurations on certain elements etc; we allow special  code positions.  This code may include

a pointer to alignment  or the pointer can be included in the serial number.

| Code | Special Conditions |
| --- | --- |
| 000 | None |
| -NM | Z minus Endcap assignment |
| mNM | Mirror configuration of MN (item) |
| NMx | Special geometry or position for standard NM (item) |

All of the Barcode data shall be entered into a database configuration which can

be merged with the general CMS Endcap database, other Muon alignment subsystems, and the general CMS database in development. One simple database

package will be used by all sites in a given alignment subsystem; for consistency and merging. An alignment pointer filter can be used to isolate the subsystem entries  and information in a larger database. Tracking can be performed by filtering on production center.

4. Quality  Control of  System  Parts

Qualification criteria about the technical requirements for system parts are

Included in the Requests for Quotation and the Purchase orders issued to vendors for

each item. Vendor Quality Control obligations on parts before shipping are given. In

many cases, these requirements will include ASTM, ANSI, ISO, and MIL standard specifications.

We describe the tests to be performed  at a specified Production center upon delivery.