PRELIMINARY SOIL-SLIP SUSCEPTIBILITY MAPS, SOUTHWESTERN CALIFORNIA

By D.M. Morton1, R.M. Alvarez1, and R.H. Campbell1

Digital preparation by K.R. Bovard1, D.T. Brown2, K.M. Corriea1, and J.N. Lesser3

Prepared in cooperation with

CALIFORNIA GEOLOGICAL SURVEY

Open-File Report OF 03-17

2003

Any use of trade, product, or firm names is for descriptive purposes only and does not imply endorsement by the U.S. Government.  This database, identified as “Preliminary Soil-Slip Susceptibility Maps, Southwestern California” has been approved for release and publication by the Director of the USGS.

U.S. DEPARTMENT OF INTERIOR

U.S. GEOLOGICAL SURVEY

1U.S. Geological Survey

Department of Earth Sciences

###### University of California

Riverside CA 92521

2Department of Earth Sciences

University of California

Riverside CA 92521

3U.S. Forest Service

Department of Earth Sciences

University of California

Riverside CA 92521

## TABLE OF CONTENTS

Introduction

General

How to obtain paper plots

Database contents

Data package

Plot package

Other files

Software utilities

How to obtain the digital files

How to extract the soil-slip susceptibility map database from the tar files

Digital database

Postscript plot files

Portable Document Format  (.pdf) files

Digital soil-slip susceptibility map specifications

Digital compilation

Spatial resolution

Map accuracy standards

Database specifics

General

References

## INTRODUCTION

### General

Open-file Report 03-17 contains a digital soil-slip susceptibility map database of southwestern California that includes:

ARC/INFO (Environmental Systems Research Institute, http://www.esri.com) version 8.1 grids of the soil-slip susceptibility maps.

Postscript files to plot the soil-slip susceptibility maps on a topographic base.

Ascii text files and Portable Document Format (.pdf) files of:

This Readme; includes in Appendix I, data contained in sus_met.txt

The same graphic as plotted in 2 above.  Test plots have not produced precise 1:100,000-scale map sheets.  Adobe Acrobat page size setting influences map scale.

Accompanying text that describes the map, the process used to produce the map, and its uses.

This Readme file describes the digital data, such as types and general contents of files making up the database, and includes information on how to extract and plot the maps and accompanying graphic files.  Metadata information can be accessed at http://geo-nsdi.er.usgs.gov/metadata/open-file/03-17and is included in Appendix I of this Readme.

## HOW TO OBTAIN PAPER PLOTS

For those having access to large-format plotters such as HP650C, HP755C, HP2500C, and HP5000, plots may be made directly from the included plot file.

## DATABASE CONTENTS

The files constituting the soil-slip susceptibility map database of this Open-file Report are listed below along with the interchange files from which they are extracted.

### Data Package

All files listed below are in compressed tar files (*.tar.gz, ranging in size from 0.6 Mb to 10.5 Mb); see section below titled, SOFTWARE UTILITES.

| Plate Number | Area covered | Compressed tar file | ARC/INFO Grid | Contains |
| --- | --- | --- | --- | --- |
| Plate 1 | Santa Barbara 100K sheet | sbarb_sus.tar | sbarb_sus | Cells with soil-slip susceptibility values |
| Plate 2 | Part of the Los Angeles 100K sheet | la_sus.tar | la_sus | Cells with soil-slip susceptibility values |
| Plate 3 | South half of the San Bernardino 100K sheet | sbern_sus.tar | sbern_sus | Cells with soil-slip susceptibility values |
| Plate 4 | Long Beach 100K sheet | lb_sus.tar | lb_sus | Cells with soil-slip susceptibility values |
| Plate 5 | Santa Ana 100K sheet | sa_sus.tar | sa_sus | Cells with soil-slip susceptibility values |
| Plate 6 | Oceanside 100K sheet | ocs_sus.tar | ocs_sus | Cells with soil-slip susceptibility values |
| Plate 7 | San Diego and eastern part of the El Cajon 100K sheet | sd_sus.tar | sd_sus | Cells with soil-slip susceptibility values |

The directory, info/, is produced in the process of importing interchange files to ARC grids in ARC/INFO.  For example the la_sus (Los Angeles 30’ X 60’ quadrangle) info/ directory contains:

| Feature Attribute Tables |  |
| --- | --- |
| Value attribute table | la_sus.vat |

### Plot Package

Postscript plot files of the susceptibility maps; please see section below titled, SOFTWARE UTILITIES for additional information.

| Compressed file | Resultant image | Contains |
| --- | --- | --- |
| plate*.ps.zip | plate*.ps | Postscript plot file of susceptibility map |

The Postscript files are compressed using winzip.

The uncompressed Postscript files will plot 1:100,000 scale, full color soil-slip susceptibility maps of the quadrangles included in the report on a topographic base.  The sheets range from 25 X 36 inches to 41X 36 inches in size.  The map sheet has been successfully plotted on Hewlett-Packard large-format plotters, models HP650C, HP2500C, and HP5000.

### Other files

README.pdf		This document

plate*.pdf		Portable Document Format file of the susceptibility map (the asterisk used here

and in the text that follows is a wildcard meant to represent each of the seven

soil-slip susceptibility maps included in this database)

text.pdf		Portable Document Format file of the accompanying text.

## SOFTWARE UTILITIES

Files which have a .gz file extension were compressed using gzip.  Gzip utilities are available free of charge via the Internet at the gzip home page, http://www.gzip.org.  Files with a .zip file extension were compressed using WinZip, available at http://www.winzip.com.

The data files are additionally bundled into tar (tape archive) files.  The individual files must be extracted using a tar utility, available free of charge via the Internet through links on the Common Internet File Formats page, http://www.matisse.net/files/format.html. One such utility is WinZip, available at http://www.winzip.com.

## HOW TO OBTAIN THE DIGITAL FILES

The data and plot files, constituting the susceptibility map database of this Open-file Report may be obtained over the Internet.

The files can be obtained via the Web from Western Region Geologic Information Server. Go to the web page at http://geopubs.wr.usgs.gov/open-file/of03-17 and follow the directions to download the files.

## HOW TO EXTRACT THE SOIL-SLIP SUSCEPTIBILITY MAP DATABASE FROM THE TAR FILE

### Digital database

After downloading the files, they must be uncompressed using a gzip utility such as gzip itself or WinZip. The data files must then be extracted using a tar utility or Winzip.

This process will create a directory such as la_sus/, that will contain the ARC/INFO grid and supporting files. When uncompressing the files, do not extract them to an existing workspace, as this will destroy the pre-existing info directories, coverages and grids.  The directory should contain the following files:

la_sus/

la_sus		ARC/INFO grid

sus.rmp		ARC/INFO remap table

/info		ARC/INFO info directory

The remap table (sus.rmp) is provided with each ARC/INFO grid, and is identical for each map.  The remap table values are used in conjunction with colornames.shd (this is a standard ARC/INFO shadeset).

The following are not included in the database tar file, but can be downloaded separately.

plate*.ps.zip

README.pdf

text.pdf

plate*.pdf

### Postscript plot files

Make an uncompressed file, plate*.ps (plot of complete map, ranging in size from 19 Mb to 75 Mb), by using gzip or winzip utility of choice.

### Portable Document Format  (.pdf) files

PDF files are not stored as gzip files. They are accessed using Adobe Acrobat Reader software, available free from the Adobe website http://www.adobe.com.  Follow instructions at the website to download and install the software. Acrobat Reader contains an on-line manual and tutorial.

## DIGITAL SUSCEPTIBILITY MAP SPECIFICATIONS

### Digital compilation

The susceptibility values were calculated by combining numerical values from ARC/INFO grids for geologic units, slope, and aspect.  The resulting 10 m grid files were assembled on 1:100,000-scale base maps which were derived from U.S. Geological Survey Digital Line Graph data.  About 20% of the mapped area was covered by 30 m grids, which were resampled to produce 10 m grid files (for information regarding the specific areas covered by resampled grids, see the open-file report text).  The digital files and the plot files are arranged on 30’ X 60’ quadrangles.  The San Diego 30’ X 60’ quadrangle includes the western part of the El Cajon 30’ X 60’ quadrangle.

### Spatial resolution

Use of this digital soil-slip susceptibility map database should not violate the spatial resolution of the data.  Although the digital form of the data removes the constraint imposed by the scale of a paper map, the detail and accuracy inherent in map scale are also present in the digital data.  Although the map plot files are released at 1:100,000-scale, the elevation and the geologic data were derived from 1:24,000-scale data, so plotting the data at this scale is permissible.  However, the fact that this database was compiled from 1:24,000-scale Digital Elevation Models means that higher resolution information is not generally present in the dataset.  Plotting at scales larger than 1:24,000 will not yield greater real detail, although it will reveal irregularities above the intended resolution of the database.

### Map accuracy standards

The digital elevation data meet U.S. Geologic National Digital Elevation Model standards and the geologic data meet national geologic map standards.

### Database specifics

General--The map database consists of ARC/INFO format grids, which are stored in universal transverse mercator (UTM) projection, zone 11 (Table 1), and a series of data tables.

| Table 1 --- | Map Projection |
| --- | --- |
| Projection | UTM |
| Datum | NAD27 |
| Zunits | No |
| Units | Meters |
| Spheroid | Clark 1866 |
| X shift | 0.000000000 |
| Y shift | 0.000000000 |

The database is composed of ARC/INFO grids, which are raster data files composed of cells.  Definitions of the database items are explained in Table 2.

Table 2 – Item Definition Terms

ITEM NAME		Name of the database field

WIDTH			Maximum number of digits or characters stored

OUTPUT		Output width

TYPE	B-binary integer, F-binary floating point number, I-ASCII integer, C-ASCII character string

N. DEC.	Number of decimal places maintained for floating point numbers

Table 3 – Items, Value Attribute Table (*_sus.vat)

ITEM NAME      WIDTH     OUTPUT     TYPE     N. DEC.

VALUE                     4                 10             B               -		Default item for cell values

COUNT                     4                10              B               -		Number of cells with specific value

SUSCODE                 8                 8              N               3		Item containing susceptibility

values

The grid cell values range from 0 to 5000, though not all of the grids use the full range of values.  A cell value of zero indicates the cell does not meet the criteria needed to fall into the low, moderate, or high susceptibility categories.  Cell values greater than zero are divided into 3 classes representing low, moderate, and high susceptibility.  Areas of low susceptibility include values ranging from 6 to 999, areas of moderate susceptibility include values ranging from 1000 to 3250, and areas of high susceptibility include values ranging from 3251 to 5000.

# REFERENCES

Environmental Systems Research Institute, Inc, 1991, ARC/INFO command references 6.0: Proprietary software manual.

Appendix I (metadata text)

Identification_Information:

Citation:

Citation_Information:

Originator: Douglas M. Morton

Originator: Rachel M.H. Alvarez

Originator: Russell H. Campbell

Publication_Date: 200301

Title: Preliminary Soil-Slip Susceptibility Maps, Southwestern California

Edition: Version 1.0

Geospatial_Data_Presentation_Form: raster digital data

Series_Information:

Series_Name: U.S. Geological Survey Open-File Report

Issue_Identification: USGS OF 03-17

Publication_Information:

Publication_Place: Menlo Park, California

Publisher: U.S. Geological Survey

Online_Linkage: http://geopubs.wr.usgs.gov/open-file/of03-17

Description:

Abstract:

This data set maps the soil-slip susceptibility for several areas in southwestern California.  Created using Environmental Systems Research Institute's ARC/INFO software, the data base consists of raster maps containing grid cells coded with soil-slip susceptibility values.  In addition, the data set includes the following graphic and text products: (1) postscript graphic plot files containing the soil-slip susceptibility map, topography, cultural data, and a key of the colored map units, and (2) PDF and text files of the Readme (including the metadata file as an appendix) and accompanying text, and a PDF file of the plot files.

Intense winter rains commonly generated debris flows in upland areas of southwestern California.  These debris flows initiate as small landslides referred to as soil slips.  Most of the soil slips mobilize into debris flows  that travel down slope at varying speeds and distances.  The debris flows can be a serious hazard to people and structures in their paths.  The soil-slip susceptibility maps identify those natural slopes most likely to be the sites of soil slips during periods of intense winter rainfall.  The maps were largely derived by extrapolation of debris-flow inventory data collected from selected areas of southwestern California.  Based on spatial analyses of soil slips, three factors in addition to rainfall, were found to be most important in the origin of soil slips.  These factors are geology, slope, and aspect.  Geology, by far the most important factor, was derived from existing geologic maps.  Slope and aspect data were obtained from 10-meter digital elevation models (DEM).  Soil-slip susceptibility maps at a scale of 1:24,000 were derived from combining numerical values for geology, slope, and aspect on a 10-meter cell size for 128 7.5’ quadrangles and assembled on 1:100,000-scale topographic maps.  The resultant maps of relative soil-slip susceptibility represent the best estimate generated from available debris-flow inventory maps and DEM data.

Purpose: These data sets were derived to describe the relative soil-slip susceptibility for upland areas of southwestern California.  Although released on a 1:100,000-scale topographic base, the data were derived at a scale of 1:24,000 and as such can be transferred from 1:100,000-scale to 1:24,000-scale without any loss of accuracy.  The maps are not intended to be used at any scale larger than 1:24,000.

Supplemental_Information: none

Time_Period_of_Content:

Time_Period_Information:

Single_Date/Time:

Calendar_Date: 2003/01

Currentness_Reference: Not for use after June, 2003

Status:

Progress: Complete

Maintenance_and_Update_Frequency: None planned

Spatial_Domain:

Bounding_Coordinates:

West_Bounding_Coordinate: -120.00446939

East_Bounding_Coordinate: -116.8742505

North_Bounding_Coordinate: 34.52044023

South_Bounding_Coordinate: 32.49939779

Keywords:

Theme:

Theme_Keyword_Thesaurus: none

Theme_Keyword: Soil slips

Theme_Keyword: Debris flows

Place:

Place_Keyword_Thesaurus: none

Place_Keyword: California

Place_Keyword: Southwestern California

Place_Keyword: Los Angeles County

Place_Keyword: Orange County

Place_Keyword: Riverside County

Place_Keyword: San Bernardino County

Place_Keyword: San Diego County

Place_Keyword: Santa Barbara County

Place_Keyword: Ventura County

Access_Constraints: none

Use_Constraints: This data base is not to be used at a scale larger than 1:24,000.

Point_of_Contact:

Contact_Information:

Contact_Person_Primary:

Contact_Person: Douglas M. Morton

Contact_Organization: U.S. Geological Survey, Western Region, Earth Surface Processes Team

Contact_Position: Project geologist

Contact_Address:

Address_Type: mailing address

Address: U.S. Geological Survey

Address: Department of Earth Sciences

Address: University of California, Riverside

City: Riverside

State_or_Province: California

Postal_Code: 92521

Country: United States of America

Contact_Voice_Telephone: (909) 276-6397

Contact_Facsimile_Telephone: (909) 276-6295

Contact_Electronic_Mail_Address: scamp@usgs.gov

Data_Set_Credit: Geologic mapping and digital preparation of this report were sponsored jointly by (1) the National Cooperative Geologic Mapping Program of the U.S. Geological Survey, (2) the California Geological Survey, and (3) the Southern California Areal Mapping Project (SCAMP).  The California Geological Survey graciously provided geologic map data and critical input.

Native_Data_Set_Environment:

Windows_NT, 5.0, Intel

ARC/INFO version 8.1

Data_Quality_Information:

Attribute_Accuracy:

Attribute_Accuracy_Report: The map meets national geologic map standards.  The digital elevation data meet U.S. Geological National Digital Elevation Model standards.

Logical_Consistency_Report: Not applicable for raster data.

Completeness_Report: The map reflects the most accurate geologic map data and DEM data currently available to the U.S. Geological Survey.

Positional_Accuracy:

Horizontal_Positional_Accuracy:

Horizontal_Positional_Accuracy_Report: For accuracy information for DEM data refer to the U.S. Geological Survey Digital Elevation Models, Data User's Guide 5.  Complete reference is in the explanatory text document.

Lineage:

Process_Step:

Process_Description: Process included mapping debris flows from several generations of aerial photographs in selected areas of southwestern California.  Debris flows were transferred by inspection to 7.5’ topographic quadrangle maps to produce debris flow inventory maps.  Debris flow inventory maps were digitized in a GIS system (Arc/Info).  Geologic data were obtained from digital geologic data bases from various sources.  Digital elevation data were obtained from U.S. Geological Survey digital elevation models (DEM).  Susceptibility values were the product of numerical values assigned to geologic map units, slope, and aspect.

Process_Date: 200209-200301

Process_Step:

Process_Description:

First draft of metadata created by Rachel Alvarez using

FGDCMETA.AML ver. 1.2 05/14/98 on ARC/INFO data set

Process_Date: 20030108

Process_Step:

Process_Description: Digital database review by Scott Graham.

Process_Date: 20030113

Spatial_Data_Organization_Information:

Direct_Spatial_Reference_Method: Raster

Raster_Object_Information:

Raster_Object_Type: Grid Cell

Row_Count: 22569

Column_Count: 29031

Spatial_Reference_Information:

Horizontal_Coordinate_System_Definition:

Planar:

Grid_Coordinate_System:

Grid_Coordinate_System_Name: Universal Transverse Mercator

Universal_Transverse_Mercator:

UTM_Zone_Number: 11

Transverse_Mercator:

Scale_Factor_at_Central_Meridian: 1

Longitude_of_Central_Meridian: -118 26 15

Latitude_of_Projection_Origin: 32 30

False_Easting: 0

False_Northing: 0

Planar_Coordinate_Information:

Planar_Coordinate_Encoding_Method: coordinate pair

Coordinate_Representation:

Abscissa_Resolution: 10.0

Ordinate_Resolution: 10.0

Planar_Distance_Units: Meters

Geodetic_Model:

Horizontal_Datum_Name: North American Datum of 1927

Ellipsoid_Name: Clarke 1866

Semi-major_Axis: 6378206.4

Denominator_of_Flattening_Ratio: 294.98

Entity_and_Attribute_Information:

Overview_Description:

Entity_and_Attribute_Overview:

Version 1.0 of the Preliminary Soil-Slip Susceptibility Maps, Southwestern California comprises seven ARC/INFO grids, la_sus, lb_sus, ocs_sus, sbern_sus, sd_sus, sa_sus, sbarb_sus, which contain soil-slip susceptibility values.  The item names and definitions are the same for each raster data set and are as follows:

*_sus.vat

COLUMN   ITEM NAME        WIDTH OUTPUT  TYPE N.DEC  ALTERNATE NAME

1  VALUE                  4    10     B      -

5  COUNT                  4    10     B      -

9  SUSCODE                8     8     N      3

*_sus.sta

COLUMN   ITEM NAME        WIDTH OUTPUT  TYPE N.DEC  ALTERNATE NAME

1  MIN                    8    15     F      3

9  MAX                    8    15     F      3

17  MEAN                   8    15     F      3

25  STDV                   8    15     F      3

The item suscode contains the susceptibility values.

Entity_and_Attribute_Detail_Citation: none

Detailed_Description:

Entity_Type:

Entity_Type_Label: *.vat

Entity_Type_Definition: Susceptibility values identified in each of the seven mapped areas (the Santa Barbara 100K sheet, the Los Angeles 100K sheet, the south half of the San Bernardino 100K sheet, the Long Beach 100K sheet, the Santa Ana 100K sheet, the Oceanside 100K sheet, and the San Diego and western El Cajon 100K sheets)

Attribute:

Attribute_Label: suscode

Attribute_Definition: number corresponding to a susceptibility value = not included in low, moderate or high

Attribute_Domain_Values:

Enumerated_Domain:

Enumerated_Domain_Value: 0

Enumerated_Domain_Value_Definition: A value of 0 indicates the cell does not meet the criteria needed to fall into the low, moderate or high susceptibility categories.

Susceptibility values identified in each of the seven mapped areas (the Santa Barbara 100K sheet, the Los Angeles 100K sheet, the south half of the San Bernardino 100K sheet, the Long Beach 100K sheet, the Santa Ana 100K sheet, the Oceanside 100K sheet, and the San Diego and western El Cajon 100K sheets).

Attribute:

Attribute_Label: suscode

Attribute_Definition: number corresponding to a susceptibility value = low

Attribute_Domain_Values:

Range_Domain:

Range_Domain_Minimum: 6

Range_Domain_Maximum: 999

Attribute:

Attribute_Label: suscode

Attribute_Definition: number corresponding to a susceptibility value = moderate

Attribute_Domain_Values:

Range_Domain:

Range_Domain_Minimum: 1000

Range_Domain_Maximum: 3250

Attribute:

Attribute_Label: suscode

Attribute_Definition: number corresponding to a susceptibility value = high

Attribute_Domain_Values:

Range_Domain:

Range_Domain_Minimum: 3251

Range_Domain_Maximum: 5000

Distribution_Information:

Distributor:

Contact_Information:

Contact_Organization_Primary:

Contact_Organization: U.S. Geological Survey Information Services

Contact_Address:

Address_Type: mailing address

Address: Box 25286 Denver Federal Center

City: Denver

State_or_Province: Colorado

Postal_Code: 80225

Country: USA

Contact_Voice_Telephone: (303) 202-4700

Contact_Facsimile_Telephone: (303) 202-4693

Distribution_Liability:

The U.S. Geological Survey (USGS) provides these geographic data "as is".  The USGS makes no guarantee or warranty concerning the accuracy of information contained in the geographic data.  The USGS further makes no warranties, either expressed or implied as to any other matter whatsoever, including, without limitation, the condition of the product, or its fitness for use lies entirely with the user.  Although these data have been processed successfully on computers at the USGS, no warranty, expressed or implied, is made by the USGS regarding the use of these data on any other system, nor does the fact of distribution constitute or imply any such warranty.

In no event shall the USGS have any liability whatsoever for payment of any consequential, incidental, indirect, special, or tort damages of any kind, including, but not limited to, any loss of profits arising out of use of or reliance on the geographic data or arising out of the delivery, installation, operation, or support by USGS.

These digital map databases, 1:100,000 scale, and any derivative maps thereof, is not meant to be used or displayed at any scale larger than 1:24,000 (e.g., 1:12,000).

Metadata_Reference_Information:

Metadata_Date: 20030108

Metadata_Review_Date: 20030113

Metadata_Contact:

Contact_Information:

Contact_Organization_Primary:

Contact_Organization: U.S. Geological Survey

Contact_Person: Rachel M.H. Alvarez

Contact_Position: Geologist

Contact_Address:

Address_Type: mailing address

Address: U.S. Geological Survey

Address: Department of Earth Sciences

Address: University of California, Riverside

City: Riverside

State_or_Province: California

Postal_Code: 92521

Country: USA

Contact_Voice_Telephone: (909) 276-6397

Contact_Facsimile_Telephone: (909) 276-6295

Contact_Electronic_Mail_Address: rhauser@usgs.gov

Metadata_Standard_Name: FGDC Content Standards for Digital Geospatial Metadata

Metadata_Standard_Version: FGDC-STD-001-1998

Metadata_Access_Constraints: none

Metadata_Use_Constraints: none