| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 22 to Document 41-E |
|  | 22 August 2007 |
|  | Original: English |
| Asia-Pacific Telecommunity Administrations |
| common proposals for the work of the conference |
| Agenda item 2 |

2	to examine the revised ITU-R Recommendations incorporated by reference in the Radio Regulations communicated by the Radiocommunication Assembly, in accordance with Resolution 28 (Rev.WRC-03), and to decide whether or not to update the corresponding references in the Radio Regulations, in accordance with principles contained in the Annex to Resolution 27 (Rev.WRC-03)

Introduction

Resolutions 27 (Rev.WRC-03) and 28 (Rev.WRC-03) provide clear guidance on the principles and application for incorporating by reference ITU-R Recommendations in the Radio Regulations. Therefore WRC-07 should follow the incorporation by reference process in Resolution 27 (Rev.WRC-03) and Resolution 28 (Rev.WRC-03).

Part 1	Incorporation by reference of ITU-R Recommendations mentioned in Volumes 1 and 2 of the Radio Regulations – Changes to provisions of a non-mandatory nature

APT countries concur with the conclusions reached at the CPM that references to ITU-R Recommendations of a non-mandatory character do not need to be updated by a WRC.

The conclusions of the CPM are supported with respect to updating the non-mandatory ITU-R Recommendations references, i.e. that Resolutions 27 (Rev.WRC-03) and 28 (Rev.WRC-03) do not contain a procedure for updating the references to ITU Recommendations of a non-mandatory character. Consequently, WRC-07 may wish to consider the need to establish such a procedure and to adopt the necessary texts as appropriate.

APT countries support the proposed modifications to the footnotes and provisions as shown in Section 7/2/1 of the CPM Report. With respect to No. 5.536A, Option 1 is supported.

ARTICLE  5

Frequency allocations

Section IV  –  Table of Frequency Allocations
(See No. 2.1)

MOD	ASP/41A22/342

5.208A	In making assignments to space stations in the mobile-satellite service in the bands 137-138 MHz, 387-390 MHz and 400.15-401 MHz, administrations shall take all practicable steps to protect the radio astronomy service in the bands 150.05-153 MHz, 322-328.6 MHz, 406.1-410 MHz and 608-614 MHz from harmful interference from unwanted emissions. The threshold levels of interference detrimental to the radio astronomy service are shown in Table 1 of Recommendation ITU-R RA.769.     (WRC-07)

Reasons:	To conform to Resolution 27 (Rev.WRC-03) (Annex 2, § 5), as the language indicates this Recommendation is not mandatory and is not in RR Volume 4.

MOD	ASP/41A22/343

5.536A	Administrations operating earth stations in the Earth exploration-satellite service or the space research service shall not claim protection from stations in the fixed and mobile services operated by other administrations. In addition, earth stations in the Earth exploration-satellite service or in the space research service should be operated taking into account the most recent versions of Recommendations ITU-R SA.1278 and ITU-R SA.1625, respectively.     (WRC-07)

Reasons:	To conform to Resolution 27 (Rev.WRC-03) (Annex 2, § 5), as the “should” language indicates this Recommendation is not mandatory and is not in RR Volume 4.

ARTICLE  47

Operator’s certificates

Section IV  –  Qualifying service1     (WRC-03)

MOD	ASP/41A22/344

47.26	§ 8	1)	The holder of a radiocommunication general operator’s certificate or a first- or second-class radiotelegraph operator’s certificate shall be authorized to embark as chief operator of a ship station of the fourth category (which is described in the most recent version of Recommendation ITU-R M.1169).     (WRC-07)

Reasons:	To conform to Resolution 27 (Rev.WRC-03) (Annex 2, § 5), as the Recommendation is for information only in this context.

MOD	ASP/41A22/345

47.27		2)	However, before becoming chief or sole operator of a ship station of the fourth category (in accordance with the most recent version of Recommendation ITU-R M.1169) which is required by international agreements to carry a radiotelegraph operator, the holder of a radiocommunication general operator’s certificate or a first- or second-class radiotelegraph operator’s certificate shall have had adequate experience as operator on board ship at sea.     (WRC-07)

Reasons:	To conform to Resolution 27 (Rev.WRC-03) (Annex 2, § 5), as the Recommendation is for information only in this context.

MOD	ASP/41A22/346

47.28		3)	Before becoming chief operator of a ship station of the second or third category (in accordance with the most recent version of Recommendation ITU-R M.1169), the holder of a radiocommunication general operator’s certificate or a first- or second-class radiotelegraph operator’s certificate shall have had, as operator on board ship or in a coast station, at least six months’ experience of which at least three months shall have been on board ship.     (WRC-07)

Reasons:	To conform to Resolution 27 (Rev.WRC-03) (Annex 2, § 5), as the Recommendation is for information only in this context.

MOD	ASP/41A22/347

47.29		4)	Before becoming chief operator of a ship station of the first category (in accordance with the most recent version of Recommendation ITU-R M.1169), the holder of a radiocommunication general operator’s certificate or a first-class radiotelegraph operator’s certificate shall have had, as operator on board ship or in a coast station, at least one year’s experience of which at least six months shall have been on board ship.     (WRC-07)

Reasons:	To conform to Resolution 27 (Rev.WRC-03) (Annex 2, § 5), as the Recommendation is for information only in this context.

Part 2	Incorporation by reference of ITU-R Recommendations mentioned in WRC Resolutions

APT countries support the outcome of the CPM in this regard, namely if a WRC Resolution includes a resolves referring to an ITU-R Recommendation or portion thereof in a specific manner (by number and version) using mandatory language (i.e. shall), the ITU-R Recommendation or parts thereof are considered to be incorporated by reference.

There are cases where these ITU-R Recommendations are not contained in RR Volume 4. Table 2-1 in Section 7/2/2 of the CPM Report is a non-exhaustive list of cases where an ITU-R Recommendation is referenced using mandatory language (i.e. shall) in a WRC Resolution, which have been analysed to determine whether the Recommendations are incorporated by reference.

APT countries propose modification to Resolution 27 (Rev.WRC-03) in order to clarify the scope of incorporation by reference and confirm the treatment of the above-mentioned ITU-R Recommendations is also supported.

MOD	ASP/41A22/348

RESOLUTION  27  (Rev.WRC-07)

Use of incorporation by reference in the Radio Regulations

The World Radiocommunication Conference (Geneva, 2007),

considering

a)	that the principles of incorporation by reference were adopted by WRC-95, revised by WRC-97 and further refined by WRC-2000 (see Annexes 1 and 2 to this Resolution);

b)	that there are provisions in the Radio Regulations containing references which fail to distinguish adequately whether the status of the referenced text is mandatory or non-mandatory,

noting

that references to Resolutions or Recommendations of a world radiocommunication conference (WRC) require no special procedures, and are acceptable for consideration, since such texts will have been agreed by a WRC,

resolves

1	that for the purposes of the Radio Regulations, the term “incorporation by reference” shall only apply to those references intended to be mandatory;

2	that when considering the introduction of new cases of incorporation by reference, such incorporation shall be kept to a minimum and made by applying the following criteria:

–	only texts which are relevant to a specific WRC agenda item may be considered;

–	the correct method of reference shall be determined on the basis of the principles set out in Annex 1 to this Resolution;

–	the guidance contained in Annex 2 to this Resolution shall be applied in order to ensure that the correct method of reference for the intended purpose is employed;

3	that the procedure described in Annex 3 to this Resolution shall be applied for approving the incorporation by reference of ITU-R Recommendations or parts thereof;

4	that existing references to ITU-R Recommendations shall be reviewed to clarify whether the reference is mandatory or non-mandatory in accordance with Annex 2 to this Resolution;

5	that ITU-R Recommendations, or parts thereof, incorporated by reference at the conclusion of each WRC shall be collated and published in a volume of the Radio Regulations (see Annex 3 to this Resolution),

instructs the Director of the Radiocommunication Bureau

1	to bring this Resolution to the attention of the Radiocommunication Assembly and the ITU-R Study Groups;

2	to identify the provisions and footnotes of the Radio Regulations containing references to ITU-R Recommendations and make suggestions on any further action to the second session of the Conference Preparatory Meeting (CPM) for inclusion in its Report to the next WRC;

3	to identify the provisions and footnotes of the Radio Regulations containing references to WRC Resolutions containing references to ITU-R Recommendations and make suggestions on any further action to the second session of the Conference Preparatory Meeting (CPM) for inclusion in its Report to the next WRC,

invites administrations

to submit proposals to future conferences, taking into account the CPM Report, in order to clarify the status of references, where ambiguities remain regarding the mandatory or non-mandatory status of the references in question, with a view to amending those references:

i)	that appear to be of a mandatory nature, identifying such references as being incorporated by reference by using clear linking language in accordance with Annex 2;

ii)	that are of a non-mandatory character, so as to refer to “the most recent version” of the Recommendations.

MOD	ASP/41A22/349

ANNEX  1  TO  RESOLUTION  27  (Rev.WRC-07)

Principles of incorporation by reference

1	For the purposes of the Radio Regulations, the term “incorporation by reference” shall apply only to those references intended to be mandatory.

2	Where the relevant texts are brief, the referenced material should be placed in the body of the Radio Regulations rather than using incorporation by reference.

2bis	Where a mandatory reference to an ITU-R Recommendation, or parts thereof, is included in the resolves of a WRC Resolution, which is itself cited in a footnote or provision of the Radio Regulations using mandatory language (i.e. shall), that ITU-R Recommendation or parts thereof, shall also be considered for incorporation by reference.

3	Texts which are of a non-mandatory nature or which refer to other texts of a non-mandatory nature shall not be considered for incorporation by reference.

4	If, on a case-by-case basis, it is decided to incorporate material by reference on a mandatory basis, then the following provisions shall apply:

4.1	the text incorporated by reference shall have the same treaty status as the Radio Regulations themselves;

4.2	the reference must be explicit, specifying the specific part of the text (if appropriate) and the version or issue number;

4.3	the text incorporated by reference must be submitted for adoption by a competent WRC in accordance with resolves 3;

4.4	all texts incorporated by reference shall be published following a WRC, in accordance with resolves 4.

5	If, between WRCs, a text incorporated by reference (e.g. an ITU-R Recommendation) is updated, the reference in the Radio Regulations shall continue to apply to the earlier version incorporated by reference until such time as a competent WRC agrees to incorporate the new version. The mechanism for considering such a step is given in Resolution 28 (Rev.WRC-03).

Reasons:	If a WRC Resolution having mandatory effects includes a resolves referring to an ITU-R Recommendation or portion thereof in a specific manner (by number and version) using mandatory language (i.e. shall), the ITU-R Recommendation or parts thereof are considered to be incorporated by reference.

VOLUME  4

ITU-R  Recommendations incorporated by reference

ADD	ASP/41A22/350

RECOMMENDATION  ITU-R  M.1652*

Dynamic frequency selection (DFS)1 in wireless access systems including radio
local area networks for the purpose of protecting the
radiodetermination service in the 5 GHz band

Reasons:	RR No. 5.446A states that mobile service operating in the band 5 150 -5 350 MHz and 5 470-5 725 MHz shall operate in accordance with the provisions of Resolution 229 (WRC-03). resolves 8 of this Resolution states that Recommendation ITU-R M.1652 shall be used. Therefore, the referenced Recommendation fulfils the criteria to be incorporated into the Radio Regulations.

ADD	ASP/41A22/351

RECOMMENDATION  ITU-R  M.1642-1

Methodology for assessing the maximum aggregate equivalent power
flux-density at an aeronautical radionavigation service station
from all radionavigation-satellite service systems
operating in the 1 164-1 215 MHz band

Reasons:	RR No. 5.328A states that radionavigation-satellite service operating in the band 1 164-1 215 MHz shall operate in accordance with the provisions of Resolution 609 (WRC-03). resolves 10 of this Resolution states that Recommendation ITU-R M.1642 shall be used. Therefore, the revised referenced Recommendation fulfils the criteria to be incorporated into the Radio Regulations.

ADD	ASP/41A22/352

RECOMMENDATION  ITU-R  M.1583*

Interference calculations between non-geostationary mobile-satellite
service or radionavigation-satellite service systems 
and radio astronomy telescope sites

Reasons:	RR No. 5.443B states that radionavigation-satellite service (space-to-Earth) operating in the band 5 010-5 030 MHz shall operate in accordance with the provisions of Resolution 741 (WRC-03). resolves 2 of this Resolution states that Recommendation ITU-R M.1583 shall be used. Therefore, the referenced Recommendation fulfils the criteria to be incorporated into the Radio Regulations.

Part 3	ITU-R Recommendations incorporated by reference in the RR which have been revised and approved since WRC-03

The list of those ITU-R Recommendations incorporated by reference in the RR (Resolution 27 (Rev.WRC-03)) which have been revised and approved during the elapsed study period since WRC-03 is shown in Section 7/2/3 of the CPM Report.

The CPM also noted that, in some cases, different texts of the RR make reference to different versions of ITU-R Recommendations (see, for instance, No. 22.5C.6 which makes reference to Recommendation ITU-R S.1428-1, which is included in RR Volume 4, and Annex 1 to Resolution 76 (WRC-2000) which makes reference to Recommendation ITU-R S.1428). The CPM considers that WRC-07, under Agenda item 2, should also review the references to the ITU-R Recommendations incorporated by reference which are referred to in other texts (such as Annex 1 to Resolution 76 (WRC-2000)) and amend them accordingly, as part of the consequential changes envisaged by Agenda item 3 of the Conference.

VOLUME  4

ITU-R  Recommendations incorporated by reference

MOD	ASP/41A22/353

RECOMMENDATION  ITU-R  M.541-9*

Operational procedures for the use of digital selective-calling
equipment in the maritime mobile service

Reasons:	This Recommendation was updated to Rev. 9 in May 2004. The updated revision was examined as requested by Resolution 28 (Rev.WRC-03). It is appropriate to update the corresponding reference in the Radio Regulations in accordance with the principles contained in the Annex to Resolution 27 (Rev.WRC-03).

MOD	ASP/41A22/354

RECOMMENDATION  ITU-R  P.838-3

Specific attenuation model for rain for use in prediction methods

Reasons:	This Recommendation was updated to Rev. 3 in May 2004. The updated revision was examined as requested by Resolution 28 (Rev.WRC-03). It is appropriate to update the corresponding reference in the Radio Regulations, in accordance with the principles contained in the Annex to Resolution 27 (Rev.WRC-03).

MOD	ASP/41A22/355

RECOMMENDATION  ITU-R  M.1174-2*

Technical characteristics of equipment used
for on-board vessel communications in
the bands between 450 and 470 MHz

Reasons:	This Recommendation was updated to Rev. 2 in May 2004. The updated revision was examined as requested by Resolution 28 (Rev.WRC-03). It is appropriate to update the corresponding reference in the Radio Regulations, in accordance with the principles contained in the Annex to Resolution 27 (Rev.WRC-03).

MOD	ASP/41A22/356

RECOMMENDATION  ITU-R  M.1187-1

A method for the calculation of the potentially affected region
for a mobile-satellite service network
in the 1-3 GHz range using circular orbits

Reasons:	This Recommendation was updated to Rev. 1 in March 2006. The updated revision was examined as requested by Resolution 28 (Rev.WRC-03). It is appropriate to update the corresponding reference in the Radio Regulations, in accordance with the principles contained in the Annex to Resolution 27 (Rev.WRC-03).

MOD	ASP/41A22/357

RECOMMENDATION  ITU-R  BO.1443-2

Reference BSS earth station antenna patterns for use in 
interference assessment involving non-GSO satellites 
in frequency bands covered by RR Appendix 30*

Reasons:	This Recommendation was updated to Rev. 2 in May 2006. The updated revision was examined as requested by Resolution 28 (Rev.WRC-03). It is appropriate to update the corresponding reference in the Radio Regulations, in accordance with the principles contained in the Annex to Resolution 27 (Rev.WRC-03).

MOD	ASP/41A22/358

RECOMMENDATION  ITU-R  S.1586-1

Calculation of unwanted emission levels produced by a non-geostationary 
fixed-satellite service system at radio astronomy sites

Reasons:	This Recommendation was updated to Rev.1 in January 2007. The updated revision was examined as requested by Resolution 28 (Rev.WRC-03). It is appropriate to update the corresponding reference in the Radio Regulations, in accordance with the principles contained in the Annex to Resolution 27 (Rev.WRC-03).

______________

# Footnotes

Resolution 27 (Rev.WRC-03) – Use of incorporation by reference in the Radio Regulations

Resolution 28 (Rev.WRC-03) – Revision of references to the text of ITU-R Recommendations incorporated by reference in the Radio Regulations