FINDING OF NO SIGNIFICANT IMPACT

County of Ventura, General Service Agency

Soule Park Bank Repairs

FEMA-1203-DR-CA; DSR #52055/73861

The County of Ventura (the County), through the California Office of Emergency Services, has applied to the Federal Emergency Management Agency (FEMA) Public Assistance Program for funding to repair and stabilize stream banks along Thacher and San Antonio Creeks.  Heavy rains from the winter storms of February 1998 caused severe slope failure and erosion along Thacher and upper San Antonio Creeks in Soule Park and Soule Golf Course.  Therefore, the County has identified the need to protect public health and safety, as the steep and unprotected slopes are vulnerable to continued erosion and possible failure.

Under the Proposed Action, the County would repair two areas along Thacher Creek and one area along San Antonio Creek.  The Thacher Creek project area is located on the south bank of the creek within Soule Park, approximately 1,500 feet upstream from its confluence with San Antonio Creek.  In total, the two damaged areas measure 784 linear feet and are separated by a 300 linear foot segment of stable vegetated bank.  The 445-foot upstream segment would be stabilized using interlocking, x-shaped, concrete blocks call “A-jacks” placed in 3 feet deep and 5 feet wide excavated trench. Established willows would be hand-cut and placed among the “A-jacks” with soil to help re-establish the vegetation.  Above the “A-jacks”, the banks would be graded to a 2:1 slope.  The banks along the 339-foot downstream segment would be cut to a 2:1 slope.  Filter material would be placed on the new slope and would be seeded with native grasses.  All work would be performed from the top of the bank.

The San Antonio creek bank repair would occur along 300 linear feet of the creek’s eastern bank in an area adjacent to the Soule Golf Course.  The top of the bank would be lowered approximately 3 to 5 feet and cut to a 2:1 slope.  “A-jacks” would be placed in a 5-foot wide by 4-foot deep trench.  Existing willows would be hand-cut, stripped of their leaves, placed among the “A-jacks” and covered with soil to help establish growth.  All construction would occur from the existing equestrian trail.

The Supplemental Environmental Assessment that was prepared for the County of Ventura Soule Park Bank Repairs Project tiers from the Final Programmatic Environmental Assessment for Typical Recurring Actions Resulting from Flood Disasters in California as Proposed by the Federal Emergency Management Agency, FEMA-1203-DR-CA (PEA; April 16, 1998).  The PEA resulted in a Finding of No Significant Impact (April 16, 1998).  Both the SEA for the Soule Park Bank Repairs Project and the PEA are available online at http://www.fema.gov/mit/ep/assess.htm and http://www.fema.gov/reg-ix/env/nhpapa.htm, respectively.

A public notice has been circulated explaining reasons for siting the project in the floodplain, pursuant to Executive Order 11988 (Floodplain Management).  This Finding of No Significant Impact serves as the final notice for Executive Order 11988 compliance.

Based upon the conditions and the information contained in the Programmatic Environmental Assessment and the Supplemental Environmental Assessment for the County of Ventura Soule Park Bank Repair Project  (April 22, 2002 make sure that this is the date of the final document), and in accordance with FEMA’s regulations in 44CFR Part 10 (Environmental Considerations) and Executive Orders 11988 (Floodplain Management), 11990 (Protection of Wetlands), and 12898 (Environmental Justice), the following is concluded:

A Finding of No Significant Impact.  Therefore, an environmental impact statement will not be prepared, based on the fact that there will be no long-term adverse impacts to the natural environment resulting from this project.

This Finding of No Significant Impact is based upon the conditions contained in the Programmatic Environmental Assessment and the Supplemental Environmental Assessment.

For more information, contact Sandro Amaglio, Region IX Environmental Officer, at (415) 923-7027.  No action will be allowed to occur until 15 days after publication of this Finding of No Significant Impact.