# CDF SVX Power Supply Connections	9/13/99

Remote sensor

## Connector at the CAEN Power Supply

0.050" Mini D Ribbon (MDR) Connector, IDC Wiremount Plug --- Shielded.

3M Part #:  10136-6000EC  	Pins as numbered in 3M drawing TS-0423-07 sheet 3 of 3

Metal Junction Shell Part #: 10336-1230-00

## Connector at the Junction Board

0.050" Mini D Ribbon (MDR) Connector, IDC Wiremount Plug --- Shielded.

3M Part #: 10126-6000EC  	Pins as numbered in 3M drawing TS-0423-07 sheet 2 of 3

Metal Junction Shell Part #: 10326-1230-00

## Cable

0.025" Pleated Foil Shielded Cable, 30 AWG Solid, TPE Primary, TPE Cover

Part #: 90201/26

| PIN @ CAEN | PIN @ JB1 | Conductor Number | Description | CAEN Designation | Comment |
| --- | --- | --- | --- | --- | --- |
| 1 | - | - | Enable | Enable | Connected to PIN 19 in the Connector at CAEN |
| 19 | - | - | Enable 1 | En 1 | See pin 19 |
| 2 | - | - | No Connection |  | not/connected |
| 20 | - | - | No Connection |  | n/c |
| 3 | - | - | No Connection |  | n/c |
| 21 | - | - | No Connection |  | n/c |
| 4 | - | - | DTERM POS. | DTERMSP | n/c |
| 22 | - | - | DTERM NEG. | DTERMSN | n/c |
| 5 | 1 | 1 | 5VDOIM POS. | 5VDOIMSP |  |
| 23 | 14 | 2 | 5VDOIM NEG. | 5VDOIMSN |  |
| 6 | 2 | 3 | 2VDOIM POS. | 2VDOIMSP |  |
| 24 | 15 | 4 | 2VDOIM NEG. | 2VDOIMSN |  |
| 7 | 3 | 5 | Digital layer 0 pos. | DSPLY0 |  |
| 25 | 16 | 6 | Digital layer 0 neg. | DSNLY0 |  |
| 8 | 4 | 7 | Analog layer 0 pos. | ASPLY0 |  |
| 26 | 17 | 8 | Analog layer 0 neg. | ASNLY0 |  |
| 9 | 5 | 9 | Digital layer 1 pos. | DSPLY1 |  |
| 27 | 18 | 10 | Digital layer 1 neg. | DSNLY1 |  |
| 10 | 6 | 11 | Analog layer 1 pos. | ASPLY1 |  |
| 28 | 19 | 12 | Analog layer 1 neg. | ASNLY1 |  |
| 11 | 7 | 13 | Digital layer 2 pos. | DSPLY2 |  |
| 29 | 20 | 14 | Digital layer 2 neg. | DSNLY2 |  |
| 12 | 8 | 15 | Analog layer 2 pos. | ASPLY2 |  |
| 30 | 21 | 16 | Analog layer 2 neg. | ASNLY2 |  |
| 13 | 9 | 17 | Digital layer 3 pos. | DSPLY3 |  |
| 31 | 22 | 18 | Digital layer 3 neg. | DSNLY3 |  |
| 14 | 10 | 19 | Analog layer 3 pos. | ASPLY3 |  |
| 32 | 23 | 20 | Analog layer 3 neg. | ASNLY3 |  |
| 15 | 11 | 21 | Digital layer 4 pos. | DSPLY4 |  |
| 33 | 24 | 22 | Digital layer 4 neg. | DSNLY4 |  |
| 16 | 12 | 23 | Analog layer 4 pos. | ASPLY4 |  |
| 34 | 25 | 24 | Analog layer 4 neg. | ASNLY4 |  |
| 17 | - | - | GROUND | EARTH | n/c |
| 35 | 13 | 25 | GROUND | EARTH |  |
| 18 | 26 | 26 | SHIELD | SHIELD |  |
| 36 | - | - | SHIELD | SHIELD | n/c |

1 Junction Board

Low Voltage Connection

## Connector at the CAEN Power Supply

Plug connector, Size 5, 78 position, Amplimite HDP-22

AMP Part #:  748368-1 	Pins as numbered in AMP drawing 748368 1 of 1.

Metalized Shell Part #:  748677-5

Spring Latches #:  745255-2

Latch Blocks #  745245-2

Male Contact #:  748333-2

## Connector at the Junction Board

Plug connector, Size 4, 62 position, Amplimite HDP-22

AMP Part #:  748367-1 	Pins as numbered in AMP drawing 748367 1 of 1.

Metalized Shell Part #:  748677-4

Spring Latches #:  745255-2

Latch Blocks #  745245-2

Male Contact #:  748333-2

## Cable

30 Conductor, 22 AWG Spectra-Bond parallel conductor ribbon cable.

Amphenol Spectra-Strip Part #: 843-111-2214-030.

NOTE:  Using two cables per assembly.

| PIN @ CAEN | PIN @ JB | Conductor Number | Description | CAEN Designation | Comment |
| --- | --- | --- | --- | --- | --- |
| 62 | - | - | Analog layer 3 neg. | AVNLY3 | n/c |
| 63 | - | - | Analog layer 3 pos. | AVPLY3 | n/c |
| 46 | - | - | Analog layer 0 neg. | AVNLY0 | n/c |
| 66 | - | - | Analog layer 0 pos. | AVPLY0 | n/c |
| 8 | - | - | Dterm negative | DTERM_N | n/c |
| 28 | - | - | Dterm positive | DTERM_P | n/c |
| 47 | - | - | Dterm negative | DTERM_N | n/c |
| 67 | - | - | Dterm positive | DTERM_P | n/c |
| 49 | - | - | Digital layer 3 neg. | DVNLY3 | n/c |
| 69 | - | - | Digital layer 3 pos. | DVPLY3 | n/c |
| 50 | - | - | Digital layer 2 neg. | DVNLY2 | n/c |
| 70 | - | - | Digital layer 2 pos. | DVPLY2 | n/c |
| 51 | - | - | Digital layer 1 neg. | DVNLY1 | n/c |
| 71 | - | - | Digital layer 1 pos. | DVPLY1 | n/c |
| 52 | - | - | Digital layer 0 neg. | DVNLY0 | n/c |
| 72 | - | - | Digital layer 0 pos. | DVPLY0 | n/c |
| 17 | - | - | 5VDOIM NEG. | 5VDOIMN | n/c |
| 76 | - | - | 5VDOIM POS. | 5VDOIMP | n/c |
| 19 | - | - | EARTH | EARTH | n/c |
| 78 | - | - | SHIELD | SHIELD_2 | n/c |
| 20 | - | - | ENABLE 1 | EN_1 | Connected to PIN 59 in Connector at CAEN |
| 59 | - | - | ENABLE 2 | EN_2 | See Pin 20 |
| - | 20 | - |  |  | n/c |
| - | 21 | - |  |  | n/c |
| - | 41 | - |  |  | n/c |
| - | 42 | - |  |  | n/c |
| - | 61 | - |  |  | n/c |
| - | 62 | - |  |  | n/c |
| 1 | 1 | A 1 | Analog layer 4 neg. | AVNLY4 |  |
| 2 | 22 | A 2 | Analog layer 4 pos. | AVPLY4 |  |
| 21 | 43 | A 3 | Analog layer 4 neg. | AVNLY4 |  |
| 22 | 44 | A 4 | Analog layer 4 pos. | AVPLY4 |  |
| 40 | 23 | A 5 | Analog layer 4 neg. | AVNLY4 |  |
| 41 | 2 | A 6 | Analog layer 4 pos. | AVPLY4 |  |
| 60 | 3 | A 7 | Analog layer 4 neg. | AVNLY4 |  |
| 61 | 24 | A 8 | Analog layer 4 pos. | AVPLY4 |  |
| 3 | 45 | A 9 | Analog layer 3 neg. | AVNLY3 |  |
| 4 | 46 | A 10 | Analog layer 3 pos. | AVPLY3 |  |
| 23 | 25 | A 11 | Analog layer 3 neg. | AVNLY3 |  |
| 24 | 4 | A 12 | Analog layer 3 pos. | AVPLY3 |  |
| 42 | 5 | A 13 | Analog layer 3 neg. | AVNLY3 |  |
| 43 | 26 | A 14 | Analog layer 3 pos. | AVPLY3 |  |
| 5 | 47 | A 15 | Analog layer 2 neg. | AVNLY2 |  |
| 25 | 48 | A 16 | Analog layer 2 pos. | AVPLY2 |  |
| 44 | 27 | A 17 | Analog layer 2 neg. | AVNLY2 |  |
| 64 | 6 | A 18 | Analog layer 2 pos. | AVPLY2 |  |
| 6 | 7 | A 19 | Analog layer 1 neg. | AVNLY1 |  |
| 26 | 28 | A 20 | Analog layer 1 pos. | AVPLY1 |  |
| 45 | 49 | A 21 | Analog layer 1 neg. | AVNLY1 |  |
| 65 | 50 | A 22 | Analog layer 1 pos. | AVPLY1 |  |
| 7 | 29 | A 23 | Analog layer 0 neg. | AVNLY0 |  |
| 27 | 8 | A 24 | Analog layer 0 pos. | AVPLY0 |  |
| 39 | 9 | A 25 | EARTH | EARTH |  |
| 58 | 30 | A 26 | SHIELD | SHIELD_2 |  |
| 9 | 51 | D 1 | Digital layer 4 neg. | DVNLY4 |  |
| 29 | 52 | D 2 | Digital layer 4 pos. | DVPLY4 |  |
| 48 | 31 | D 3 | Digital layer 4 neg. | DVNLY4 |  |
| 68 | 10 | D 4 | Digital layer 4 pos. | DVPLY4 |  |
| 10 | 11 | D 5 | Digital layer 3 neg. | DVNLY3 |  |
| 30 | 32 | D 6 | Digital layer 3 pos. | DVPLY3 |  |
| 11 | 53 | D 7 | Digital layer 2 neg. | DVNLY2 |  |
| 31 | 54 | D 8 | Digital layer 2 pos. | DVPLY2 |  |
| 12 | 33 | D 9 | Digital layer 1 neg. | DVNLY1 |  |
| 32 | 12 | D 10 | Digital layer 1 pos. | DVPLY1 |  |
| 13 | 13 | D 11 | Digital layer 0 neg. | DVNLY0 |  |
| 33 | 34 | D 12 | Digital layer 0 pos. | DVPLY0 |  |
| 14 | 55 | D 13 | 2VDOIM NEG. | 2VDOIMN |  |
| 15 | 56 | D 14 | 2VDOIM POS. | 2VDOIMP |  |
| 34 | 35 | D 15 | 2VDOIM NEG. | 2VDOIMN |  |
| 35 | 14 | D 16 | 2VDOIM POS. | 2VDOIMP |  |
| 53 | 15 | D 17 | 2VDOIM NEG. | 2VDOIMN |  |
| 54 | 36 | D 18 | 2VDOIM POS. | 2VDOIMP |  |
| 73 | 57 | D 19 | 2VDOIM NEG. | 2VDOIMN |  |
| 74 | 58 | D 20 | 2VDOIM POS. | 2VDOIMP |  |
| 16 | 37 | D 21 | 5VDOIM NEG. | 5VDOIMN |  |
| 18 | 16 | D 22 | 5VDOIM POS. | 5VDOIMP |  |
| 36 | 17 | D 23 | 5VDOIM NEG. | 5VDOIMN |  |
| 38 | 38 | D 24 | 5VDOIM POS. | 5VDOIMP |  |
| 56 | 59 | D 25 | 5VDOIM NEG. | 5VDOIMN |  |
| 37 | 60 | D 26 | 5VDOIM POS. | 5VDOIMP |  |
| 55 | 39 | D 27 | 5VDOIM NEG. | 5VDOIMN |  |
| 57 | 18 | D 28 | 5VDOIM POS. | 5VDOIMP |  |
| 75 | 19 | D 29 | 5VDOIM NEG. | 5VDOIMN |  |
| 77 | 40 | D 30 | 5VDOIM POS. | 5VDOIMP |  |

Bias, High Voltage Connection

## Connector at the CAEN Power Supply

Plug assembly, Low Profile, 25 position, Amplimite HDF-20 (Ribbon Cable)

AMP Part #:  747306-2 	Pins as numbered in AMP drawing 747306.

Strain Relief #: 747275-2

Thumb Screw #:  746881-1

## Connector at the Junction Board

Plug assembly, Low Profile, 15 position, Amplimite HDF-20 (Ribbon Cable)

AMP Part #:  747306-3 	Pins as numbered in AMP drawing 747306.

Strain Relief #: 747275-3

Thumb Screw #:  746881-1

## Cable

0.050" Shielded/Jacketed, Flat Cable, 28 AWG Stranded, PVC Primary, PVC Cover

3M Part #: 3517/25

| PIN @ CAEN | PIN @ JB | Conductor Number | Description | CAEN Designation | Comment |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | 1 | +VBIAS layer 0 pos. | VBPISL0 |  |
| 14 | 9 | 2 | +VBIAS layer 0 neg. | VBNISL0 |  |
| 2 | 2 | 3 | H.V.Ref layer 0 | VBFISL0 |  |
| 15 | 10 | 4 | +VBIAS layer 1 pos. | VBPISL0 |  |
| 3 | 3 | 5 | -VBIAS layer 1 neg. | VBNISL0 |  |
| 16 | 11 | 6 | H.V.Ref layer 1 | VBFISL1 |  |
| 4 | 4 | 7 | +VBIAS layer 2 pos. | VBPISL1 |  |
| 17 | 12 | 8 | -VBIAS layer 2 neg. | VBNISL1 |  |
| 5 | 5 | 9 | H.V.Ref layer 2 | VBFISL2 |  |
| 18 | 13 | 10 | +VBIAS layer 3 pos. | VBPISL3 |  |
| 6 | 6 | 11 | -VBIAS layer 3 neg. | VBNISL3 |  |
| 19 | 14 | 12 | H.V.Ref layer 3 | VBFISL3 |  |
| 7 | 7 | 13 | +VBIAS layer 4 pos. | VBPISL4 |  |
| 20 | 15 | 14 | -VBIAS layer 4 neg. | VBNISL4 |  |
| 8 | 8 | 15 | H.V.Ref layer 4 | VBFISL4 |  |
| 21 | - | - | ENABLE | EN_0 | Connected to PIN 9 in the Connector at CAEN |
| 9 | - | - | ENABLE | EN_1 | See Pin 21 |
| 22 | - | - | GROUND | EARTH | n/c |
| 10 | - | - | GROUND | EARTH | n/c |
| 23 | - | - | GROUND | EARTH | n/c |
| 11 | - | - | SHIELD | SHIELD | n/c |
| 24 | - | - | SHIELD | SHIELD | n/c |
| 12 | - | - | No Connection |  | n/c |
| 15 | - | - | No Connection |  | n/c |
| 13 | - | - | No Connection |  | n/c |