| Job Aid-DRVSM Appl.doc | 26 Jan 2008 |
| --- | --- |

Domestic U.S. RVSM: this Job Aid is focused on an initial operator application for RVSM authority for the domestic U.S. References are also provided on RVSM in Canada. Subsequent versions of the Job Aid may be expanded to include oceanic and international operations.

Policy References. FAA Order (FAAO) 8900.1 (Flight Standards Information Management System (FSIMS)) references have replaced previous FAA document references, where appropriate. Guidance 91-RVSM and the FAA RVSM Documentation Webpage are cited as sources of policy guidance in FAAO 8900.1 paragraph 4-108. Note: FAAO 8900.1 paragraph 4-108, E currently erroneously links to AC 91-70 instead of 91-RVSM. This is being corrected.

OPSS Generated Letters of Authorization (LOA). The Operations Safety System (OPSS) generated LOA’s that are applicable to RVSM are: A001 (Issuance and Applicability), A004 (Summary of Authorizations) and B046 (Operations in RVSM Airspace). Also, LOA D098 (Flight in Special Areas of Operations For Short-Term Operations) is intended to be used for short-term authorizations. There is no “Domestic U.S. RVSM (DRVSM) LOA”. See Guidance 91-RVSM, paragraph 11g(2).

Purposes of this Job Aid. The Job Aid: 1. Provides core RVSM reference documents for operators and inspectors. 2. In Part 2, provides a list of operator documents or exhibits that an operator should submit to support an application for RVSM authority. 3. In Part 3-5, provides a matrix that shows: Required RVSM program elements. Reference paragraphs related to those elements. Location in operator documents/exhibits where an RVSM element is addressed. Columns for inspector to comment on and track the status of various RVSM program elements.

Recommended Inspector and Operator Actions. The following are suggestions on how the Job Aid can be used: 1. In the pre-application meeting with the operator, the inspector first reviews the “RVSM Approval Checklist – US Operators” to provide an overview of approval process events. (See “Core FAA References on the next page). 2. Inspector next reviews this Job Aid to inform the operator of the form and content of the operator application for RVSM authority. 3. Operator uses Job Aid as guide to assemble documents/exhibits for RVSM application. See Part 2 below for suggested list of documents/exhibits. 4. Operator annotates Job Aid to show location of RVSM program elements in the operator documents/exhibits and submit to inspector. 5. Inspector annotates Job Aid to show task or document complete/satisfactory or open/further operator action required. 6. Inspector informs the operator as soon as possible when further operator action is required. 7. When requested, operator provides inspector with revised material. 8. Inspector issues LOA to operator when required tasks and documents are completed.

| Job Aid Organization | Page |
| --- | --- |
| Part 1 | General Operator Information 3 |
| Part 2 | List of Operator Exhibits/Document Submissions 4 |
| Part 3 | Basic Elements for Operator RVSM Authorization (Operator Application) 6 |
| Part 4A | Basic Pilot Procedures for RVSM Operations 8 |
| Part 4B | Domestic U.S. Operational Policy & Procedures 13 |
| Part 5 | RVSM Maintenance Programs 14 |

Primary Source of Core Documents, Information and Contacts. The “FAA RVSM Documentation Webpage” can be accessed from the FAA RVSM Homepage: www.faa.gov/ats/ato/rvsm1.htm or www.faa.gov/about/office_org/headquarters_offices/ato/service_units/enroute/rvsm/

| Core FAA References | Location on RVSM Documentation Webpage: |
| --- | --- |
| 1. | RVSM Approval Process Events – U.S. Operators Getting Started Section |
| 2. | FAA Guidance 91-RVSM (Change 2, 2/10/04).……………………………… Documents Applicable To All RVSM Approvals |
| 3. | Guidance On Letters of Authorization For Operation In Special Areas of Operations: Operator and Airframe Authorization For Flight In Special Areas of Operation (SAO) FAA Inspector Guidance |
| 4. | *FAA Order 8900.1, Vol. 4, Chapter 1, Section 5, paragraph 4-108 (RVSM Airspace) link to FSIMS under FAA Inspector Guidance |
| 5. | *FAA Order 8900.1, Vol. 4, Chapter 10 (Evaluate Operator’s Application To Conduct Flight In RVSM Airspace) link to FSIMS under FAA Inspector Guidance |
| 6. | FAA Notice GEN04009 (Sept 1, 2005): Operational Policy/Procedures for RVSM Domestic US, Alaska, Offshore Airspace and the San Juan FIR Area of Operations Specific Information & Operational Policy/Procedures |
| 7. | FAA Notice (10/27/04): Gulf of Mexico Airspace, RVSM Policy & Procedures and Strategic Lateral Offsets Area of Operations Specific Information & Operational Policy/Procedures |
| 8. | Global Change 59 (Minimum Equipment List provisions) Documents Applicable to All RVSM Approvals |
| 9. | Contacts Contacts |
| 10. | Domestic U.S. Minimum Monitoring Requirements Monitoring Requirements & Procedures |
| *FAA Order 8900.1 (Flight Standards Information Management System (FSIMS)). These two documents are “Key” RVSM documents that can be accessed at: http://fsims.faa.gov/PICResults.aspx?mode=Search&q=rvsm&kw=rvsm&status=a&syn=1&sort=0& |

PART 1:   GENERAL OPERATOR INFORMATION

OPERATOR NAME:

RESPONSIBLE PERSON: Information for automated LOA B046, Table 2:  information for person to sign the LOA.

| Name | E-mail Address | Telephone Number |
| --- | --- | --- |

*AIRCRAFT PROPOSED FOR RVSM AUTHORIZATION.   Provide aircraft information for inclusion in automated LOA B046, Table

| Serial Number | Registration Number | Airplane M/M/S |
| --- | --- | --- |

*NOTE:  airplane information may be provided in a separate document.

DATE OF PRE-APPLICATION MEETING ________

DATE APPLICATION RECEIVED: __________ DATE OPERATOR PLANS TO START RVSM OPERATIONS __________

NOTIFCATION TIME TO FSDO ADEQUATE?  	  ___YES  	 ___NO

AREA(S) OF OPERATION WHERE OPERATOR INITIALLY INTENDS TO START RVSM OPERATIONS:

__ *DOMESTIC U. S. ONLY (See Job Aid Part 4B)

__ CANADA

__ MEXICO

*For the purpose of this Job Aid, Domestic US RVSM is considered to include the lower 48 states, Alaska, Atlantic and Gulf of Mexico High Offshore Airspace and the airspace in the San Juan FIR where VHF or UHF voice direct controller-pilot communication (DCPC) is normally available.   RVSM policies and procedures for oceanic airspace (including the West Atlantic Route System, New York Oceanic and oceanic airspace in the San Juan FIR are posted in “Global Areas of RVSM Operations” in the “Area of Operations Specific Information” section of the RVSM Documentation Webpage.

PART 2:  OPERATOR EXHIBITS/DOCUMENT SUBMISSIONS

| Exhibit or Document | Exhibit / Document Title | Operator Indication of Inclusion | Inspector Comments |
| --- | --- | --- | --- |
| A | Operator Letter Requesting RVSM Authority |  |  |
| B | (Recommended) Draft Letter of Authorization With Operator Information Filled In. |  |  |
| C | Aircraft RVSM-compliance Documents (RVSM Airworthiness Documents) 1. For in-service aircraft: As applicable: Service Bulletin (SB), Supplemental Type Certificate (STC), Aircraft Service Change (ASC) or Service Letter (SL) (Documents normally accompanied by corresponding AFM Revision or AFM Supplement). 2. For aircraft manufactured RVSM-compliant: AFM, AFM Supplement and/or Type Certificate Data Sheet (TCDS) |  |  |
| D | For In-service Aircraft. Documentation of Aircraft Inspection and/or Modification: Maintenance records documenting completion of aircraft system modification and/or inspection (e.g., Major Repair and Alteration (FAA Form 337) |  |  |
| E | MEL (only for operators operating under an MEL): MEL or MMEL that complies with GC 059 – (MEL pages applicable to RVSM required systems) Note: Many MMELs have been revised to incorporate Global Change (GC) 059. |  |  |
| F | Maintenance Program. Stand-alone RVSM Maintenance Manual or list of RVSM maintenance elements incorporated into an existing approved program. Ref: FAA Order 8900.1, Vol. 4, Chapter 10 Note: see Notes 1 and 2 on the next page. |  |  |
| G | 1. Method of Pilot Training/Knowledge (e.g., Part 142 training center, course of instruction, in-house training; record of course completion). 2. Pilot Training/Knowledge Syllabus: if requested by the inspector. Ref: FAA Order 8900.1, Vol. 4, Section 5, paragraph 4-108G (RVSM Process and Policy); Guidance 91-RVSM paragraph 11d(3)(Operations Training Programs & Operating Practices & Procedures; 11d(3)(ii) (14 CFR Part 91 Operators) |  |  |

PART 2:  OPERATOR EXHIBITS/DOCUMENTS (Cont.)

| Exhibit or Document | Exhibit / Document Title | Operator Indication of Inclusion | Inspector Comments |
| --- | --- | --- | --- |
| H | Operational Policy & Procedures Documents or Manuals. Stand-alone RVSM Operations Manual or section of operator’s application documenting RVSM operational policy & procedures. Reference: Guidance 91-RVSM paragraph 11d(4)(Operations Manuals and Checklists) Note: See Note 1 below. |  |  |
| I | RVSM Monitoring: method and schedule to complete RVSM height monitoring References: FAA Order 8900.1, Vol. 4, Chapter 1, Section 5, paragraph 4-108, H (Monitoring Programs); Guidance 91-RVSM paragraph 11d(8) Note 1: monitoring is not required to be completed prior to the LOA being issued. Note 2: monitoring results can be accessed on the U.S. RVSM Approvals Database at: http://www.tc.faa.gov/act-500/niaab/rvsm/approvals.asp |  |  |

*SUBMITTED APPLICATION CONTAINS:  	____ AIRCRAFT RVSM COMPLIANCE DOCUMENTION

____ RVSM MAINTENANCE PROGRAM

____ OPERATIONAL POLICY/PROCEDURES

Note 1:  If stand-alone maintenance and operations manuals are submitted, they may be combined into one manual.

Note 2:  Exhibits/documents may be included in a binder or submitted as a stand-alone document(s).

PART 3:  BASIC ELEMENTS FOR OPERATOR RVSM AUTHORIZATION

(OPERATOR APPLICATION)

| # | Elements For RVSM Authorization | Reference Paragraphs: | Where Found in Operator Exhibits/Documents | FAA Inspector Recommendations and/or Comments | Inspector Tracking: Item Status / Date |
| --- | --- | --- | --- | --- | --- |
|  | Ref: RVSM Approval Checklist - U.S. Operators | Guidance 91-RVSM and Other FAA Documents, as noted | Note: operator should update this column to reflect the content of its application. |  |  |
| 1. | Operator Letter Requesting RVSM Authority |  | Exhibit A |  |  |
| 2. | Letter of Authorization (LOA) | Paragraph 11g(2); FAAO 8900.1, Chapter 10 | Exhibit B |  |  |
| 3. | Aircraft RVSM-compliance (RVSM Airworthiness) Documents: 1. For in-service aircraft: As applicable: Service Bulletin (SB); Supplemental Type Certificate (STC); Aircraft Service Change (ASC); or Service Letter (SL) 2. For aircraft manufactured RVSM-compliant: AFM and/or Type Certificate Data Sheet (TCDS) | Paragraph 11b(3) Paragraph 11d(1)(i) Paragraph 11d(1)(ii) | 1. Exhibit C (As applicable: SB, STC, SL or ASC and AFM Supplement) 2. Exhibit C: AFM and/or TCDS |  |  |
| 4. | For in-service aircraft: maintenance records documenting completion of required inspections and/or modifications (e.g. FAA Form 337, Manufacturer’s Compliance Letter, etc.) | Paragraph 11d(1)(i) | Exhibit D |  |  |
| 5. | Description of aircraft equipment (detailing all components and equipment relevant to RVSM operations) | Paragraph 11d(2) | Exhibits C Exhibit F, Section ___. |  |  |
| 6. | Only applicable to operators operating under a Minimum Equipment List (MEL): Revised MEL and/or Master Minimum Equipment List (MMEL) | Paragraph 11d(6) Global Change 59 | Exhibit E (MEL pages applicable to RVSM) Exhibit F, Section ____ |  |  |
| 7. | Maintenance Program | 91-RVSM paragraphs 10 and 11d(7); FAAO 8900.1, Vol. 4, Chapter 10. | Exhibit F |  |  |
| 8. | Participation in RVSM Monitoring Program Method and schedule or… Monitoring results Note: See “Monitoring Requirements & Procedures” section of FAA RVSM Documentation Webpage for monitoring method options, e.g., GMU, AGHME, HMU. | Paragraphs 11d(8), 11h; FAAO 8900.1, Vol 4, paragraph 4-108, H; Domestic US/North American Monitoring Requirements Chart; Monitoring Procedures for U.S. Operators | Exhibit J |  |  |
| 9. 9a. | Method of Pilot Training/Knowledge (e.g., part 142 training center, course of instruction, operator in-house training, record or certificates of completion) Pilot Knowledge/Training Syllabus (if requested by the inspector in accordance with Notice 8700.26, paragraph 9f(1) | Paragraph 11d(3) and 11d(3)(ii); 91-RVSM Appendix 4; DRVSM Operational Policy/Procedures Notice (as amended); FAAO 8900.1, Vol. 4 paragraph 4-108, G | Exhibit G |  |  |
| 10. | Operations Manuals or Documents: DRVSM Operational Policy & Procedures | Paragraph 11d(4); 91-RVSM Appendix 4; DRVSM Operational Policy & Procedures Notice (as amended) | Exhibit H. |  |  |
| 11. | Past Performance Statement | Paragraph 11d(5) | Exhibit A |  |  |
| 12. | Plan for reporting altitude-keeping errors | Paragraph 11i | Exhibit F and H |  |  |

PART 4A   BASIC PILOT PROCEDURES FOR RVSM OPERATIONS

| Elements For RVSM Authorization | Reference Paragraphs: | Where Found in Operator Exhibits/Documents | FAA Inspector Recommendations and/or Comments | Inspector Tracking: Item Status / Date |
| --- | --- | --- | --- | --- |
| Ref: RVSM Approval Checklist - U.S. Operators | Guidance 91-RVSM and Other FAA Documents, as noted | Note: operator should update this column to reflect the content of its application. |  |  |
| Flight Planning (Guidance 91-RVSM Appendix 4, paragraph 2) |
| Verify aircraft approved for RVSM operations | Appendix 4, para 2a. | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Minimum equipment requirements pertaining to height-keeping systems | Appendix 4, para 2 d. | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Reported and forecast weather conditions on the route of flight. Sources of observed and forecast information that can help the pilot ascertain the possibility of MWA or severe turbulence are: Forecast Winds and Temperatures Aloft (FD), Area Forecast (FA), SIGMETS and PIREPS. | Appendix 4, para 2c FAA DRVSM Operational Procedures Notice (as amended), para f.2. | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Annotating the flight plan to be filed with the ATS Provider to show that the aircraft and operator are approved for RVSM operations | 1. Appendix 4, para. 2b. 2. FAA DRVSM Operational Procedures Notice (as amended), para. d. | Exhibit G, Section _____. Exhibit H _____. |  |  |
| If required for the aircraft, accounting for any RVSM required aircraft operating restrictions | Appendix 4, para.2e. | Exhibit G, Section _____. Exhibit H _____. |  |  |

PART 4A   BASIC PILOT PROCEDURES FOR RVSM OPERATIONS

| Elements For RVSM Authorization | Reference Paragraphs: | Where Found in Operator Exhibits/Documents | FAA Inspector Recommendations and/or Comments | Inspector Tracking: Item Status / Date |
| --- | --- | --- | --- | --- |
| Ref: RVSM Approval Checklist - U.S. Operators | Guidance 91-RVSM and Other FAA Documents, as noted | Note: operator should update this column to reflect the content of its application. |  |  |
| Preflight Procedures at the Aircraft (91-RVSM Appendix 4, paragraph 3) |
| Review maintenance logs and forms. Ensure maintenance action has been taken to correct defects of required equipment | Appendix 4, para 3a. | Exhibit G _____ Exhibit H ___. |  |  |
| During the external inspection of the aircraft, particular attention should be paid to the condition of the static sources etc. | Appendix 4, para 3b. | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Before takeoff, the aircraft altimeters should be set to the local altimeter (QNH) setting and should display a known field elevation within the limits specified in the aircraft operating manuals. | Appendix 4, para. 3c. | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Before takeoff, equipment required for flight into RVSM airspace should be operational and malfunctions resolved. | Appendix 4, para 3d. | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Procedures Prior to RVSM Airspace Entry (91-RVSM Appendix 4, paragraph 4) |
| List RVSM equipment that must be operational prior to RVSM airspace entry | Appendix 4, para. 4a-4d | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Operating Transponder. The operator should ascertain the requirement for an operating transponder in the airspace where operating. | Appendix 4, para. 4, Note Also see Part 4B “Contingency Actions” | Exhibit G, Section _____. Exhibit H _____. |  |  |

PART 4A:   BASIC PILOT PROCEDURES FOR RVSM OPERATIONS

| Elements For RVSM Authorization | Reference Paragraphs: | Where Found in Operator Exhibits/Documents | FAA Inspector Recommendations and/or Comments | Inspector Tracking: Item Status / Date |
| --- | --- | --- | --- | --- |
| Ref: RVSM Approval Checklist - U.S. Operators | Guidance 91-RVSM and Other FAA Documents, as noted | Note: operator should update this column to reflect the content of its application. |  |  |
| In-flight Procedures (91-RVSM Appendix 4, paragraph 5) |
| Flightcrew should comply with aircraft operating restrictions related to RVSM airworthiness approval (if applicable) | Appendix 4, para. 5a. | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Emphasis should be placed on promptly setting the sub-scale on all primary and standby altimeters to 29.92 in. Hg/1013.2 hPa when passing through the Transition Altitude and rechecking the proper altimeter setting when reaching the initial cleared flight level (CFL) | Appendix 4, para. 5b. | Exhibit G, Section _____. Exhibit H _____. |  |  |
| In level cruise it is essential that the aircraft is flown at the CFL. Clearances must be fully understood and followed. | Appendix 4, para. 5c. | Exhibit G, Section _____. Exhibit H _____. |  |  |
| During cleared transition between levels, the aircraft should not be allowed to overshoot or undershoot the CFL by more than 150 ft. (45m) | Appendix 4, para 5d. | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Unless circumstances dictate otherwise, an automatic altitude control system should be operative and engaged during cruise, etc. | Appendix 4, para 5e. | Exhibit G, Section _____. Exhibit H _____. |  |  |
| An altitude alerting system should be operational | Appendix 4, para 5f. | Exhibit G, Section _____. Exhibit H _____. |  |  |

PART 4A:   BASIC PILOT PROCEDURES FOR RVSM OPERATIONS

| Elements For RVSM Authorization | Reference Paragraphs: | Where Found in Operator Exhibits/Documents | FAA Inspector Recommendations and/or Comments | Inspector Tracking: Item Status / Date |
| --- | --- | --- | --- | --- |
| Ref: RVSM Approval Checklist - U.S. Operators | Guidance 91-RVSM and Other FAA Documents, as noted | Note: operator should update this column to reflect the content of its application. |  |  |
| In-flight Procedures (91-RVSM Appendix 4, paragraph 5) |
| At intervals of approximately one hour, cross-checks between the primary altimeters and the standby altimeter should be made. A minimum of two primary altimeters must agree within 200 ft. or a lesser value if specified in the aircraft operating manual. | Para. 5g, 5g(1) | Exhibit G, Section _____. Exhibit H _____. |  |  |
| The difference between the primary and standby altimeters should be noted for use in contingency situations. At least the initial altimeter crosscheck should be recorded | Para 5g, 5g(2) | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Normally the altimeter system being used to control the aircraft should be selected to provide the input to the altitude reporting transponder that is transmitting the information to ATC. | Para. 5h. | Exhibit G, Section _____. Exhibit H _____. |  |  |
| If the pilot is notified by ATC of an assigned altitude deviation (AAD) error, which exceeds 300 ft., then the pilot should take action to return to the CFL as quickly as possible. | Para. 5i. | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Contingency Procedures after entering RVSM airspace. The pilot should notify ATC of contingencies, which affect the ability to maintain the CFL and coordinate a plan of action. | Para 5j. Also see “Contingency Actions” in Part 4B. | Exhibit G, Section _____. Exhibit H _____. |  |  |

PART 4A:   BASIC PILOT PROCEDURES FOR RVSM OPERATIONS

| Elements For RVSM Authorization | Reference Paragraphs: | Where Found in Operator Exhibits/Documents | FAA Inspector Recommendations and/or Comments | Inspector Tracking: Item Status / Date |
| --- | --- | --- | --- | --- |
| Ref: RVSM Approval Checklist - U.S. Operators | Guidance 91-RVSM and Other FAA Documents, as noted | Note: operator should update this column to reflect the content of its application. |  |  |
| In-flight Procedures, Special Emphasis Items (91-RVSM, Appendix 4, paragraph 7). Note: Appendix 4 paragraph 7 items that are generally part of normal operations are not listed here. |
| Area of Operations Specific Operational Policy & Procedures, Including Standard ATC Phraseology | Para 7a | This information is addressed in Part 4B, 4C and 4D (as applicable) of this Job Aid. |  |  |
| Use and limitations of standby altimeters in contingencies | Para 7c | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Problems of visual perception of other aircraft at 1,000 ft. vertical separation | Para 7d | Exhibit G, Section _____. Exhibit H _____. |  |  |
| TCAS operating characteristics in RVSM airspace | Para.7f | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Aircraft operating restrictions (only if applicable to the aircraft) | Para. 7h | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Post flight Procedures (91-RVSM Appendix 4 paragraph 6) |
| In making maintenance log book entries against malfunctions in height keeping systems, the pilot should provide sufficient detail to enable maintenance to effectively troubleshoot and repair the system. | Para. 6 | Exhibit G, Section _____. Exhibit H _____. |  |  |

PART 4B:   DOMESTIC U.S. OPERATIONAL POLICY & PROCEDURES

| Elements For RVSM Authorization | Reference Paragraphs: | Where Found in Operator Exhibits/Documents | FAA Inspector Recommendations and/or Comments | Inspector Tracking: Item Status / Date |
| --- | --- | --- | --- | --- |
| Ref: RVSM Approval Checklist - U.S. Operators | FAA Notice GEN 04009 See page 2 and note below. | Note: operator should update this column to reflect the content of its application. |  |  |
| Date/time and Area Where RVSM Mandated | Paragraph a Paragraph e.1 | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Flight Level Orientation Scheme | Paragraph b | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Aircraft and Operator Approval Policy & Procedures | Paragraph c | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Flight Planning Into DRVSM Airspace | Paragraph d | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Guidance on Severe Turbulence and Mountain Wave Activity (MWA) | Paragraph f | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Guidance on Wake Turbulence | Paragraph g | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Pilot/Controller Phraseology | Paragraph h | Exhibit G, Section _____. Exhibit H _____. |  |  |
| Contingency Actions: Weather Encounters and Aircraft Systems (Pilot & Controller Actions) | Paragraph i | Exhibit G, Section _____. Exhibit H _____. |  |  |
| (If applicable) Strategic Lateral Offset Procedure for Gulf of Mexico Oceanic Operations (outside of radar coverage). | Gulf of Mexico Airspace Notice (10/27/04) See RVSM Documentation Webpage | Exhibit G, Section _____. Exhibit H, Section _____. |  |  |

#Note:  the policy/procedures in the “Domestic U.S. Alaska, etc. Notice” apply in the lower 48 states, Alaska, Gulf of Mexico and Atlantic High Offshore airspace and in the San Juan FIR where VHF or UHF controller-pilot communication is available.   The Gulf of Mexico airspace notice provides the strategic lateral offset procedure for Gulf oceanic operations.  See the RVSM Documentation webpage for current editions.

PART 5:   RVSM MAINTENANCE PROGRAM

| Elements For RVSM Authorization | Reference Paragraphs: | Where Found in Operator Exhibits/Documents | FAA Inspector Recommendations and/or Comments | Inspector Tracking: Item Status / Date |
| --- | --- | --- | --- | --- |
| Ref: RVSM Approval Checklist - U.S. Operators | FAA Order 8900.1, Vol. 4, Chapter 10. (See page 2); also 91-RVSM. | Note: operator should update this column to reflect the content of its application. |  |  |
| General: 1. Operators without an approved aircraft maintenance program are required to develop and obtain approval of an RVSM maintenance program. 2. Operators who maintain their aircraft under a continuous airworthiness maintenance program (CAMP) may choose to incorporate the RVSM maintenance requirements into the program | Para 4-1235 A-C 91-RVSM para 10a |  |  |  |
| RVSM Maintenance Program Elements: (1) Identification of components considered to be RVSM critical, and identification of structural areas noted as RVSM critical areas | Para 4-1235 D 1) |  |  |  |
| (2) The name or title of the person who will ensure that the aircraft is maintained in accordance with the approved program. | Para 4-1235 D 2) |  |  |  |
| (3) The method the operator will use to ensure that all personnel performing maintenance on the RVSM system are properly trained, qualified, and knowledgeable of that specific system. | Para 4-1235 D 3) 91-RVSM para 10f |  |  |  |
| (4) The method the operator will use to notify the crew if the aircraft has been restricted from RVSM but is airworthy for an intended flight | Para 4-1235 D 4) |  |  |  |

PART 5:  RVSM MAINTENANCE PROGRAM (Cont.)

| Elements For RVSM Authorization | Reference Paragraphs: | Where Found in Operator Exhibits/Documents | FAA Inspector Recommendations and/or Comments | Inspector Tracking: Item Status / Date |
| --- | --- | --- | --- | --- |
| Ref: RVSM Approval Checklist - U.S. Operators | FAA Order 8900.1, Vol. 4, Chapter 10. (See page 2); also 91-RVSM | Note: operator should update this column to reflect the content of its application. |  |  |
| (5) The method the operator will use to ensure conformance to the RVSM maintenance standards, including the use of calibrated and appropriate test equipment and a quality assurance program for ensuring continuing accuracy and reliability of test equipment, especially when outsourced. | Para 4-1235 D 5) 91-RVSM para 10g |  |  |  |
| (6) The method the operator will use to verify that components and parts are eligible for installation in the RVSM system, as well as to prevent ineligible parts from being installed. | Para 4-1235 D 6) |  |  |  |
| (7) The method the operator will use to return an aircraft to service after maintenance has been performed on an RVSM component/system or after the aircraft was determined to be non-compliant. | Para 4-1235 D 7) 91-RVSM para 10e |  |  |  |
| (8) Periodic inspections, functional flight tests, and maintenance and inspection procedures with acceptable maintenance practices for ensuring continued compliance with the RVSM aircraft requirements. | Para 4-1235 D 8) 91-RVSM para 10d |  |  |  |

PART 5:  RVSM MAINTENANCE PROGRAM (Cont.)

| Elements For RVSM Authorization | Reference Paragraphs: | Where Found in Operator Exhibits/Documents | FAA Inspector Recommendations and/or Comments | Inspector Tracking: Item Status / Date |
| --- | --- | --- | --- | --- |
| Ref: RVSM Approval Checklist - U.S. Operators | FAA Order 8900.1, Vol. 4, Chapter 10. (See page 2); also 91-RVSM | Note: operator should update this column to reflect the content of its application. |  |  |
| (9) The maintenance requirements listed in Instructions for Continued Airworthiness (ICA) associated with any RVSM associated component or modification. | Para 4-1235 D 9) |  |  |  |
| (10) Any other maintenance requirement that needs to be incorporated to ensure continued compliance with RVSM requirements. | Para 4-1235 D 10) |  |  |  |
| Use of Part 145 Repair Stations: Operators using the services of FAA Part 145 Certified repair Stations must include provisions to ensure that the requirements of their RVSM programs are being met. | Para 4-1235 E |  |  |  |