WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A13553 | In-Flight Anomaly Number -- | Contractor Report Number E-139-1 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title TEMPERATURE TRANSDUCER FAILED THE 32 DEGREE F CALIBRATION TEST |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT -- | Sys_Lvl N | Misc Codes A (1) B C D (P) E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE TEMPERATURE TRNSDCR | PART# PD7400244-029 | SER/LOT# 171 | MANUFACTURER ROSEMOUNT |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode UC - UNSAT | Cause MAW - MFG-ASY-WORK |
| System ELECTRICAL | Defect MW - MISWIR | Material D - DIE | Work Contact J. ADAMS | Fail Date 09/28/1990 |
| Received at MSFC 10/10/1990 | Date Isolated 10/02/1990 | FMEA Reference 3.9.13.3 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location ROSEMOUNT | Symptom EN - OPEN | Time Cycle -- |
| Effectivity Text -- |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary CAUSE: VENDOR ERROR - THE TRANSDUCER SENSING ELEMENTS WERE INCORRECTLY MANUFACTURED DUE TO WORKER ERROR. RECURRENCE CONTROL: TEST WAS ADDED |
| Last MSFC Update 05/07/1992 | CN RSLV SBMT 03/12/1991 | Defer Date -- | Add Date 03/13/1991 | R/C Codes 4 - TEST -- -- |
| Assignee |
| Design R. MOYE | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. LADNER |
| Approval |
| Design R. MOYE | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. LADNER |
| PAC Assignee T. HESTER | PAC Review Complete TH | MSFC Closure Date 03/21/1991 | Status C - CLOSED | F/A Completion 01/24/1991 |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID MARS T-112806 |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary CONTRACTOR CLOSED CAPS ON 01/31/91 BY REV. A, ADDED ADDITIONAL CLOSURE INFORMATION ON 3/12/91 BY REV. B |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description THE TRANSDUCERS FAILED THE 32 DEGREES F. CALIBRATION TEST SEGMENT OF THE VENDOR ACCEPTANCE TEST PLAN CRITICALITY: THE TRANSDUCER TYPE IS BEING PROCURED TO REPLACE THE PD7400095-149 TRANSDUCER WHICH IS CRIT. 1R; FMEA ITEM CODES 3.9.11.3, 3.9.12.3, AND 3.9.13.3; "FAILS WITH AN UNDETECTED FALSE BIAS OUTPUT." NOTE: THE TRANSDUCERS ARE LIMITED LIFE CONTROLLED REVISION "B" PROVIDES ADDITIONAL BACKGROUND INFORMATION TO SUPPORT THE CLOSURE RATIONALE. SEE TASK I CLOSURE GENERAL: THE PD7400244-029 TRANSDUCERS ARE BEING PROCURED AS REPLACEMENTS FOR THE PD7400095-149 TRANSDUCERS. THE -029 TRANSDUCERS ARE FOR USE IN THE NOSE CONE AND INTERTANK AREAS OF THE ET TO MONITOR THE GAS TEMPERATURE. THE TRANSDUCERS ARE AUTHORIZED FOR USE ON ET-61/SUBSEQUENT SERIAL NUMBER 171 FAILED DURING VENDOR ACCEPTANCE TEST PER ROSEMOUNT PROCEDURE D8830178, PARAGRAPH 4.1, AND WAS DOCUMENTED ON MARS T-112806 THE UNIT HAD A RESISTANCE OF 1390.31 OHMS AT 32 DEGREES F. THE ACCEPTABLE RESISTANCE RANGE IS 1380 +/- 3.0 OHMS |
| Contractor Investigation/Resolution |
| MSFC Response/Concurrence TASK I. FAILURE INVESTIGATION FAILURE ANALYSES WILL BE PERFORMED ON THE DEFECTIVE UNITS. THE VENDOR WILL SUBMIT A FAILURE ANALYSIS PLAN. SCHEDULE IS DEPENDENT UPON RECEIPT AND APPROVAL OF THE PLAN COMPLETE: 1/24/91 CLOSURE STATEMENT THE FAILURE ANALYSES CONCLUDED THAT THE PROBABLE CAUSE OF FAILURES WAS WORKER ERROR DURING FABRICATION OF THE TRANSDUCER SENSING ELEMENTS. THE SENSING ELEMENTS ARE FABRICATED FROM SMALL DIAMETER PLATINUM WIRE. THE STRUCTURAL SUPPORT FOR THE ELEMENT IS A .1 INCH DIAMETER, THIN WALL, PLATINUM ALLOY TUBE. A .3 INCH LONG GLASS INSULATING LAYER IS FIRED ONTO THE OUTSIDE OF THE TUBE NEAR ONE END. TWO PLATINUM WIRES, SEVERAL THOUSANDTHS OF AN INCH IN DIAMETER, RUN THROUGH THE TUBE AND ARE INSULATED FROM THE TUBE BY MAGNESIUM OXIDE. AT THE LOCATION OF THE SENSING ELEMENT END OF THE TUBE, THE PLATINUM WIRES ARE CUT SHORT AND FORMED TO PLACE THEIR ENDS NEAR THE GLASS. THE SENSING ELEMENT IS FORMED BY WELDING VERY FINE PLATINUM WIRES, ONE TO EACH OF THE HEAVIER PLATINUM WIRES FROM THE CENTER OF THE TUBE, AND THEN WINDING THE FINE WIRES IN A BIFILAR, HELICAL MANNER OVER THE GLASS. THE WIRES ARE TEMPORARILY SECURED TO THE GLASS AND THE ENDS OF THE TWO SENSING ELEMENT WIRES ARE JOINED TOGETHER. THE RESISTANCE OF THE ELEMENT IS ADJUSTED TO THE PROPER VALUE BY INITIALLY MAKING THE ELEMENT SLIGHTLY HIGHER IN RESISTANCE THAN NEEDED AND THEN PROGRESSIVELY SHORTENING THE BIFILAR ELEMENT UNTIL THE RESISTANCE IS CORRECT. AT THIS POINT THE ELEMENT IS COVERED WITH ANOTHER LAYER OF GLASS BY APPLYING A GLASS POWDER AND THEN FIRING IT IN A FURNACE. THE ENTIRE SEQUENCE OF OPERATIONS IS MADE DIFFICULT BY THE SMALL SIZE OF THE PARTS INVOLVED. THE SENSING ELEMENT WIRE IS APPROXIMATELY .001 INCH IN DIAMETER. THE COMPLETED ELEMENT ASSEMBLY IS SMALLER THAN A WOOD MATCH DURING THE RESISTANCE TRIMMING PROCESS THE PRODUCTION WORKER CHECKS THE RESISTANCE OF THE ELEMENT WHILE IT IS IMMERSED IN AN ICE BATH. THE DELICACY OF THE PART PREVENTS THE PART FROM BEING REPEATEDLY HANDLED OR TESTED. DESPITE THE CARE AND ATTENTION OF THE WORKERS AND INSPECTORS, IF AN INCORRECT RESISTANCE READING IS MADE DURING TRIMMMING, IT WILL ESCAPE DETECTION IN THE PRODUCTION STEPS THAT IMMEDIATELY FOLLOW. THE NEXT STEPS IN PRODUCTION INVOLVE MOUNTING THE ELEMENT, ADDING LEAD WIRES, AND POTTING THE BASE. NO WATER CAN BE LEFT IN THE UNIT IF IT IS TO FUNCTION PROPERLY AT THE END OF THE FABRICATION CYCLE, THE UNIT IS WATERPROOF. AT THIS STAGE IT IS POSSIBLE TO CHECK THE RESISTANCE OF THE COMPLETED UNIT TESTING AT THIS STAGE WOULD CHECK THE ELEMENT AS WELL AS THE LEAD WIRES THE VENDOR HAD NO STEP FOR CHECKING THE ACCURACY BETWEEN THE TIME OF INITIAL ELEMENT TRIMMING AND THE ATP ON THE COMPLETED UNIT TASK CLOSED TASK II. CORRECTIVE ACTION THE VENDOR DOES NOT REPEATEDLY CHECK CHARACTERISTICS OF THE TRANSDUCERS DURING THE BUILD CYCLE. EACH CHARACTERISTIC IS CHECKED ONLY DURING THE STEP THAT ACCOMPLISHES THE APPROPRIATE WORK FUNCTION. THIS IS DONE FOR REASONS OF SIMPLICITY, SPEED, AND ECONOMY. SHOULD A CHARACTERISTIC BE MEASURED OR CHECKED INCORRECTLY DURING THE SINGLE BUILD CYCLE INSPECTION, IT MAY ESCAPE DETECTION UNTIL THE VENDOR ACCEPTANCE TEST IN ORDER TO PREVENT A RECURRENCE OF THE TYPE OF ATP FAILURE DOCUMENTED IN THIS CAPS, THE VENDOR ADDED A SECOND TEST OF THE TEMPERATURE VERSUS RESISTANCE CHARACTERISTIC OF THE TRANSDUCER TO THE BUILD CYCLE. THE TEST WAS PLACED IN THE SHOP TRAVELER AT A POINT IMMEDIATELY PRIOR TO THE ACCEPTANCE TEST. REFERENCE: ROSEMOUNT ROUTING - MFG. 172-95-01, STEP 438 TASK CLOSED TASK III. CLEARANCE OF EFFECTIVITIES ALL ETS CLEARED. THE TRANSDUCERS FAILED DURING VENDOR ACCEPTANCE TESTING AND ALL INSTALLED UNITS HAVE PASSED THE VENDOR TESTS. THERE ARE NO PD7400244 TRANSDUCERS ON DELIVERED ETS; THEY ARE AUTHORIZED FOR ET-61/SUBSEQUENT TASK CLOSED TASK IV. CLOSURE SUMMARY THE VENDOR ATP FAILURE OCCURRED DUE TO AN ERROR IN MEASURING THE ELEMENT RESISTANCE AT THE TIME OF FABRICATION. FOR REASONS OF ECONOMY THERE WERE NO OTHER CHECKS OF THE RESISTANCE OF THE ELEMENT OR THE COMPLETED TRANSDUCER BEFORE ATP. AN IN-PROCESS TEST OF THE RESISTANCE OF THE COMPLETED TRANSDUCER WAS ADDED TO THE BUILD CYCLE IMMEDIATELY PRIOR TO THE VENDOR ATP. THE ADDITIONAL IN-PROCESS TEST WILL PREVENT FUTURE ATP FAILURES OF THE TYPE REPORTED IN THIS CAPS TASK CLOSED PAC NOTE: PROBLEM REPORT WAS CLOSED BY PRB ON 3/21/91 |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A13553 | IFA# -- | Contractor RPT# E-139-1 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD7400244-029 | Asmnt Part Name TEMPERATURE TRNSDCR | Asmnt Serial/Lot# 171 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD MAW - MFG-ASY-WORK | FAIL MODE UC - UNSAT |
| Asmnt FMEA 3.9.13.3 | Asmnt FM 3 | FMEA CSE A | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |