SUPPORTING  STATEMENT FOR STANDARD FORM 83-1

REPORTING AND RECORDKEEPING REQUIREMENTS

FOR THE ENFORCEMENT POLICY REGARDING

THE SALE AND USE OF AFTERMARKET CATALYTIC CONVERTERS

PART A OF THE SUPPORTING STATEMENT

1.  IDENTIFICATION OF THE INFORMATION COLLECTION

1(a)  Title of the Information Collection

Enforcement Policy Regarding the Sale and Use of Aftermarket Catalytic Converters (Renewal).  51 FR 28114-28119, 28133 (Aug. 5, 1986); 52 FR 42144 (Nov. 3, 1987), 67 FR 319-320 (Jan. 3, 2002).

OMB No. 2060-0135; EPA ICR No. 1292.07.

1(b)  Short Characterization

The aftermarket catalytic converter policy (51 Fed. Reg. 28114-28119, 28113 (Aug. 5, 1986); 52 Fed. Reg. 42144 (Nov. 3, 1987)) allows aftermarket automobile catalytic converter manufacturers and reconditioners to compete with the automobile manufacturers for the aftermarket catalytic converter replacement market.  Without this policy, it would be illegal, under section 203 of the Clean Air Act, 42 U.S.C. § 7522, to sell or install aftermarket catalytic converters that do not conform exactly to the automobile manufacturers’ original equipment (OE) versions of these parts.  The policy also makes it possible for automobile repair shops, which are often small businesses, to take on a significant share of the aftermarket catalyst replacement market.  In doing so, consumers are able to purchase replacement catalytic converters (converters) at a much lower price than they would pay for an OE converter.  This helps to ensure that vehicles will not create excessive air pollution because motorists are more likely to replace damaged catalytic converters if they cost much less than OE converters (cost savings resulting from the policy are estimated to be about $680 million in 2005 dollars).

However, to ensure that air quality will not be compromised, it was necessary to set standards for aftermarket catalytic converters, both for performance and durability.  It was also necessary to ensure that appropriate applications are installed on vehicles (i.e., the converter has to be of a type and size appropriate for the vehicle application).  To these ends, the following recordkeeping and reporting  requirements exist for aftermarket converter manufacturers, reconditioners and installers:

Manufacturers:  On a one-time basis for each type or line of converter manufactured, the manufacturer must report information identifying the supplier, and information regarding the physical specifications of each catalytic converter line produced, and information regarding pre-production testing of the converters that show they meet standards for certain specified vehicle applications (a single converter line can be used on a large number of vehicle applications).  The original policy required that once production had begun the manufacturer would submit to EPA on a semi-annual basis the number of each type of catalyst manufactured and a summary of information contained on warranty cards or, at the option of the respondent, copies of warranty cards for all converters sold. This reporting regarding sales and warranty information was eliminated in March 1999, with the stipulation that records must be maintained and the information submitted to EPA upon request.

Reconditioners:  On a one-time basis, the catalyst reconditioner must report the identity of the company and a description of the test bench used for testing used catalytic converters and the intended vehicle application(s) for each converter type.  All used converters must be tested individually to ensure they are still functional.  On a semi-annual basis, the catalyst reconditioner must report the names and addresses of distributors along with the number of each type of converter sold to each distributor.  This reporting requirement was also eliminated in March 1999, with the stipulation that records must be maintained and the information submitted to EPA upon request.

Installers of aftermarket converters:  Installers have no reporting requirements.  They simply fill out the warranty card and hand it to the retail customer.  They must also include a brief statement with each invoice stating the need for replacing the original converter.  They also tag each removed converter with a reference to the invoice for repair.  The invoices are required to be kept for 6 months.  The tagged converters are required to be kept for 15 days.

2.  NEED FOR AND USE OF THE COLLECTION

2(a)  Need/Authority for the Collection

Section 203(a)(3) of the Clean Air Act (Act) prohibits removal or rendering inoperative of motor vehicle emission control equipment by commercial service establishments or any other person.  It also prohibits the causing of such acts.  In addition, it prohibits the manufacture, sale or installation of devices that defeat the emission control components or design elements.  The catalytic converter is the major emission control device used by motor vehicle manufacturers.  Oxidation (two-way) catalytic converters reduce hydrocarbons and carbon monoxide emissions, while oxidation-reduction (three-way) converters (widely used since 1981) additionally reduce oxides of nitrogen emissions.  If a vehicle is properly maintained, the catalytic converter frequently will not require replacement for the life of the vehicle.  However, catalytic converters sometimes need replacement subsequent to the automobile manufacturer emissions control warranty period, and therefore any replacement cost is paid for by the vehicle owner.

The U.S. Environmental Protection Agency (EPA) has promoted vehicle emissions inspection programs which require converter replacement where missing or non-functioning converters are discovered.  The EPA believes that the success of State and local government programs of this type depends, in part, on the availability and cost of replacement converters.  The average cost of a new original equipment manufacturer (OE) converter is approximately $540-$650 installed.  This high cost of replacement severely limited their installation after the warranty period expired.  This enforcement policy allows the sale of low-cost effective alternatives to the OE converters.  For the aftermarket converter industry, including the installers, this is a multimillion dollar industry.  Over 2,000,000 aftermarket converters are installed each year.

The popularity of these low-cost replacement converters and the need to ensure air quality benefits while promoting local tampering inspection programs have led the Agency to implement this policy for the manufacture, sale, and installation of new non-OE and used, reconditioned OE converters.  Prior to the implementation of the policy, aftermarket converter manufacturers and reconditioners were frequently selling catalysts that had little, if any, efficacy.  Manufacturers who were attempting to make a quality product were not able to compete on a level playing field because muffler shops could purchase poor quality converters for half the price of better aftermarket converters and undersell the competition.  The manufacturer reporting and recordkeeping requirements help ensure that proper equipment is manufactured and distributed to installers and helps ensure proper retail level installation of converters.

The installer requirements exist to enable EPA to monitor whether correct  applications are made at the retail level and whether OE converters are being replaced with aftermarket converters only in appropriate circumstances (e.g., the original equipment converter should not be replaced with an aftermarket converter while the vehicle is still under its emissions warranty).  A strong incentive exists for cheating; for example installing a used, untested converter would cost less than half the price of a properly tested converter.

These are important conditions to the installation of aftermarket or reconditioned catalytic converters.  An improper application (e.g., a 2-way converter on a vehicle that needs a 3-way converter) will result in much higher emissions of harmful pollutants than a proper application would.  Likewise, replacement of the original converter when the repair is not needed can result in an increase in emissions since working OE converters are more efficient than aftermarket converters.

2(b)  Practical Utility/Users of the Data

USE

The collection of information is necessary for the proper performance of the functions of the Agency, including that the information collected will have practical utility.  Without these requirements, enforcement would be nearly impossible.  Neither EPA nor a reconditioner can determine whether a used converter is effective by conducting a visual inspection of the converter.  The efficacy of new aftermarket converters for particular vehicle applications cannot be determined without prototype testing and information on specifications.

All testing is to be conducted by the manufacturer or reconditioners, and therefore the Agency believes that it is important that it have access to testing records.  A record of the names and addresses of dealers and distributors, as is required in the policy, allows for prompt notification of these parties in the event of such an enforcement action.

The primary use of the sales and warranty card information is for direct compliance action.  Warranty cards often reveal direct evidence of misapplication or defect warranty violations.  Sales information from reconditioners provides an indirect way to make sure that production is not exceeding the capacity of the test stand, and provides the Agency with a list of distributor or retail facilities  for enforcement audits and testing.

The installer requirements are needed to assure installation of appropriate applications and to assure that catalytic converters are only replaced when necessary.  Some repair shops could gain an unfair advantage if they were to install cheaper 2-way converters on vehicles requiring 3-way converters.  Repair shops could also improperly benefit, at cost to both the consumer and ambient air quality, if OE converters are replaced when they are still functional or when they are still within the warranty period.

The requirements also facilitate knowledge on the part of the installers of aftermarket converters and of the driving public that the converters they are using are appropriate and effective and that no potential liability should exist for the installer so long as the appropriate converter is installed on each vehicle.

USERS

Air Enforcement Division, Office of Civil Enforcement, Office of Enforcement and Compliance Assurance, U.S. Environmental Protection Agency.  As noted above, the requirements also assist industry by assuring a level playing field and by ensuring installers and their customers that the converter to be installed is effective and appropriate for the vehicle (e.g., 3-way converter of proper capacity on vehicle that needs 3-way).

3.  NONDUPLICATION, CONSULTATIONS, AND OTHER COLLECTION CRITERIA

3(a)  Nonduplication

The information collection is not unnecessarily duplicative of information otherwise reasonably accessible to the Agency.  The required warranty provisions and the manufacturer reports and test records are the only records of their kind available to document the information needed to determine compliance.  The information can be in a variety of formats and the manufacturers’ warranty card information reporting can be electronic or the manufacturer can submit the actual warranty cards.

3(b)  Public Notice Required Prior to ICR Submission to OMB

In compliance with the Paperwork Reduction Act, a public comment period of 60 days was announced in the Federal Register (70 Fed. Reg. 30941-43 (May 31, 2005)) regarding this proposed renewal ICR.  No comments were received.  However, we have continued to update burden and cost information and this ICR Supporting Statement, the associated Form 83-I and the second Federal Register notice reflect these changes.

The ICR estimated burdens and costs that are being submitted to OMB for this renewal have been revised and updated to reflect wage and inflation increases, as well as estimated current workloads and corresponding burden times for installers, reconditioners and manufacturers. An additional estimate has been continued in this ICR regarding amortized startup costs for new aftermarket converter installation businesses. A second Federal Register notice is being published announcing the submission of this Policy to OMB for approval.

3(c)  Consultations

For this ICR, EPA has contacted various affected industry respondents for information regarding burdens and costs.  Following is a list of non-EPA contacts, by name, phone number and affiliation:

1.  Peter Nitoglia, Car Sound Exhaust System, Inc. 865.458.4681.

2.  George Schafer, Eastern manufacturing, Inc.,800-533-7199.

3.  Pat Haynes, Tenneco automotive, 517.796.6744.

4.  Dave Miller, Miller Catalyzer, 510.732.0622.

5.  Paula Couch, Brown Recycling, 800.367.9271.

6.  Helamon Andre, KGC Warehouse, 417.276.3059.

7.  Harley Mayer, Jr., Kataco Creek Converters, 800.275.5116.

8.  Jim/Mark Zuckerman, Meineke Muffler, New Haven, CT. 203.397.2353

9.  Katie, Midas Muffler, Beaverton, OR., 503.643.5561

3(d)  Effects of Less Frequent Collection

The information requested from the manufacturers would normally by kept as part of their records, and should not constitute a significant burden to maintain.  Additionally, the information requested is the minimum considered necessary to adequately monitor the aftermarket converter market and properly enforce the policy.  Note that the manufacturers and reconditioners are voluntarily accepting recordkeeping burdens as a condition of EPA not bringing actions for violation of section 203 of the Clean Air Act.  EPA is willing to allow the sale of aftermarket converters not certified to meet OE standards only if it can insure that aftermarket converters meet the less strict standards of the policy and that they are properly installed.

The product development information requested is only collected when a new product line is introduced by an aftermarket converter manufacturer.  Less frequent collection of test results would allow some converters to reach the market without proof of sufficient emission testing to verify their effectiveness.  Semi-annual reports of production or sales information are no longer required.  Test data on used converters cannot be taken on less than every converter that is recycled, since the condition of  the used converters varies widely because of prior use history.

No reporting is required for installers.  The recordkeeping must accompany installation since there is no way to collect the information afterward.

3(e)  General Guidelines

The collection is in compliance with OMB guidelines except that new aftermarket converter manufacturers are required to keep warranty cards for 5 years.  Because the warranty period for the converters is 5 years, this length of time is necessary.  This requirement is also in line with the applicable statute of limitations.  EPA has not received negative comment regarding this maintenance period from the industry.

3(f)  Confidentiality

Confidentiality protections are provided pursuant to 40 C.F.R. § 2.201 et seq.

3(g)  Sensitive Questions

This section is inapplicable to this ICR.

4.  THE RESPONDENTS AND THE INFORMATION REQUESTED

4(a)  Respondents/SIC Codes

Respondents include the manufacturers of new aftermarket motor vehicle catalytic converters and reconditioners of used aftermarket converters.  The SIC code is 346 (NAICS 336399).  The other respondents are automobile exhaust repair facilities.  Their SIC code is 7533 (NAICS 811112).

4(b) Information Requested

(i) Data Items, Including Recordkeeping Requirements

This ICR indicates for each recordkeeping requirement the length of time persons are required to maintain the records specified.

One-time Reporting:

Parties required to submit converter testing information include all manufacturers of new non-OEM converters and reconditioners of used OEM converters.

Manufacturers of New Converters--Specifications Information:

1)  Converter supplier and address.

2)  General type of converter (e.g., oxidation, reduction, three-way, etc.).

3)  Number of each type of catalyst used per can (number of individual monoliths containing catalytic metals in each unit).

4)  Substrate (e.g., monolithic, pelleted) - give configuration construction technique (e.g., extruded, laid-up, formed, etc.), composition, supplier and address, composition of active constituents in substrate (grams or troy ounces); for monolithic substrates, give number of cells per square inch of frontal area, design tolerances, and nominal cell wall thickness (in mils); for pelleted substrates, specify pellet shape and dimensions, pellet bulk density, the use of more than one type of pellet (e.g., Rh, or Pt/Pd), any geometrical distribution of pellets, and (if this is controlled in production) the mean impregnation depth (in microns) of active materials with production tolerances.

5)  Washcoat - give composition of active constituents, and total active material loading (grams or troy ounces) in washcoat.

6)  Active material - give composition of active constituents, loading of each active material including design tolerances, and total active material loading including design tolerances (grams or troy-ounces).

7)  Container - specify dimensions, volume, materials used, technique of containment and restraint, method of constructing container, canner (if different from catalyst supplier), and insulation and shielding (converter and/or vehicle).

8)  Physical description - dimensions (e.g., length, width, height, etc.), weight (lbs.), volume including design tolerances, active surface area (BET), and total active surface area including design tolerances.

__New converter manufacturers Prototype Testing:

1)  Year, make, and model of vehicles tested.

2)  Method of mileage accumulation.

3)  Name and address of testing facility.

4)  Summary of conversion efficiency test results.

5)  Intended vehicle applications for each converter type tested.

__Reconditioners of Catalytic Converters--Information on Test Bench:

1)  Name and address of testing facility.

2)  Description of facilities used for testing.

3)  Intended vehicle applications for each converter type.

Periodic Reporting:

__Manufacturers:

Manufacturers are no longer required to submit the following information on a semi-annual basis; EPA reserves the right to require information upon request:

1)  The number of each type of converter manufactured.

2)  A summary of the information contained on the warranty cards received, or copies of the actual warranty cards.

_Reconditioners:

Reconditioners are no longer required to submit names and addresses of the persons or companies to whom the remanufacturer distributes, along with the number of each type of converter sold to each on a semi-annual basis.  EPA reserves the right to require this information upon request.

Recordkeeping by Manufacturers of New Aftermarket Converters:

The period of record retention for new aftermarket converter manufacturers for warranty cards is 5 years.

Recordkeeping by Installers:

There is no reporting.  Installers are required to fill out warranty card if new aftermarket converter are installed, or provide card to vehicle owner for completion of applicable sections and submittal to manufacturer.  Installers must state reason for replacement on invoice, maintain invoices for 6 months, and tag replaced converters for 15 days.

(ii)  Respondent Activities

The information collection is to be implemented in ways consistent and compatible, to the maximum extent practicable, with the existing reporting and recordkeeping practices of those who are to respond.

“*” indicates an item is a customary and usual business practice (CBP), or is partially CBP.

“N/A” indicates this was a one-time cost that has already been absorbed under start-up costs associated with the policy when it was promulgated or is otherwise not applicable.

NOTE:  There have been losses of new aftermarket catalytic converter manufacturers since the last ICR. The overall population has been reduced from 12 to 8.

A.  New Aftermarket Catalytic Converter Manufacturers:

A.1.  Provide Information Re Specifications and Applications

and Information re Test Results for New Product Lines

N/A(1) Reviewing instructions;

(2) Developing, acquiring, installing and utilizing (“DAIU”) technology and systems for the purpose of collecting, validating, and verifying information;

(3) DAIU technology and systems for the purpose of processing and maintaining information;

N/A(4) DAIU technology and systems for the purpose of disclosing and providing information;

N/A(5) Adjusting the existing ways to comply with any previously applicable instructions and requirements;

N/A(6) Training personnel to be able to respond to a collection of information;

(7) Searching data sources;

(8) Completing & reviewing the collection of information;

(9) Transmitting or otherwise disclosing the information.

This requirement is a one-time burden that only applies to new product lines.  It has already been accomplished for all existing product lines, many of which are likely to be usable for many years to come.  ICR assumes each manufacturer develops and tests one new line every year.

A.2.  Testing for Each New Product Line

N/A(1) Reviewing Instructions;

(2) DAIU technology and systems for collecting, validating and verifying information;

(3) DAIU technology and systems for processing and maintaining information;

N/A(4) DAIU technology and systems for disclosing and providing information;

N/A(5) Adjusting the existing ways to comply with any previously applicable instructions and requirements;

N/A(6) Training personnel to be able to respond to a collection of information;

(7) Searching data sources;

(8) Completing & reviewing collection of information;

(9) Transmitting or otherwise disclosing the information.

This requirement is a one-time burden that only applies to new product lines.  In many cases it is contracted out.

A.3.  Semi-Annual Reports re Manufacturing and Submittal of

Warranty Cards and Maintain Warranty Cards:

These reports are no longer required on a routine basis; EPA reserves the right to require submission of information upon request.

N/A(1) Reviewing instructions;

(2) DAIU technology and systems for collecting, validating and verifying information;

*(3) DAIU technology and systems for processing and maintaining information;

N/A(4) DAIU technology and systems for disclosing and providing information;

N/A(5) Adjusting the existing ways to comply with any previously applicable instructions and requirements;

N/A(6) Training personnel to be able to respond to a collection of information;

(7) Searching data sources;

(8) Completing & reviewing the collection of information;

(9) Transmitting or otherwise disclosing information.

B.  Used Catalytic Converter Reconditioners:

B.1.  Submit Test Facility Information

N/A(1) Reviewing instructions;

(2) DAIU technology and systems for collecting, validating and verifying information;

(3) DAIU technology and systems for processing and maintaining information;

(4) DAIU technology and systems for disclosing and providing information;

N/A(5) Adjusting the existing ways to comply with any previously applicable instructions and requirements;

N/A(6) Training personnel to be able to respond to a collection of information;

(7) Searching data sources;

(8) Completing & reviewing the collection of information;

(9) Transmitting or otherwise disclosing the information.

This is a one-time burden which has already been absorbed by on-going facilities and we know of no new facilities.

B.2.  Perform Efficiency Test on Each Used Converter

N/A(1) Reviewing instructions;

(2) DAIU technology and systems for collecting, validating and verifying information;

(3) DAIU technology and systems for processing and maintaining information;

N/A(4) DAIU technology and systems for disclosing and providing information;

N/A(5) Adjusting the existing ways to comply with any previously applicable instructions and requirements;

N/A(6) Training personnel to be able to respond to a collection of information;

(7) Searching data sources;

(8) Completing & reviewing the collection of information;

(9) Transmitting or otherwise disclosing the information.

B.3.  Semi-Annual Report Regarding Distribution of Products:

These reports are no longer required on a routine basis; EPA reserves the right to require submission of information upon request.

N/A(1) Reviewing instructions;

(2) DAIU technology and systems for collecting, validating and verifying information;

(3) DAIU technology and systems for processing and maintaining information;

N/A(4) DAIU technology and systems for disclosing and providing information;

N/A(5) Adjusting the existing ways to comply with any previously applicable instructions and requirements;

N/A(6) Training personnel to be able to respond to a collection of information;

(7) Searching data sources;

(8) Completing & reviewing the collection of information;

(9) Transmitting or otherwise disclosing the information.

C.  Catalytic Converter Installers

C.1.  Fill Out Warranty Card (For New Aftermarket Converters

Only), State Reason for Replacement on Invoice and Place Tag on

Removed Converter

N/A(1) Review instructions;

*(2) DAIU technology and systems for collecting, validating and verifying information;

*(3) DAIU technology and systems for processing and maintaining information;

N/A(4) DAIU technology and systems for disclosing and providing information;

N/A(5) Adjust the existing ways to comply with any previously applicable instructions and requirements;

N/A(6) Train personnel to be able to respond to a collection of information;

*(7) Search data sources;

*(8) Complete & review the collection of information;

(9) Transmit or otherwise disclose the information.

Most of the recordkeeping and maintenance is CBP.

This ICR also makes an estimate for startup burdens and costs for new businesses.

5.  THE INFORMATION COLLECTED--AGENCY ACTIVITIES, COLLECTION                  METHODOLOGY AND INFORMATION MANAGEMENT

5(a) Agency Activities

The information collection has been developed by an office within EPA (OECA) that has planned and allocated resources for the efficient and effective management and use of the information to be collected, including the processing of the information in a manner which shall enhance, where appropriate, the utility of the information to agencies and the public.

EPA engages in the following activities in regard to the information collection.

--          Review reports,

--          Conduct inspections or audits as appropriate,

--          Take enforcement actions where appropriate.

5(b) Collection Methodology and Management

New aftermarket catalytic converter manufacturers collect sales data and warranty cards submitted to them by retail customers who have had converters installed, or directly from the installers themselves.  This is a customary business practice for many businesses.  Until 1999, the new aftermarket converter manufacturers then reported semi-annually to EPA manufacturing information (types of converters and how many sold) and either a computerized list summarizing converter installations or copies of the actual warranty cards, at their option.  However, routine reporting is now only required regarding specifications for new product lines.  Cards must be kept 5 years because that is the length of the warranty period.

Since warranties are not required on reconditioned converters, the converter reconditioners were required, prior to 1999, to provide semi-annual information regarding to whom they sold reconditioned converters, how many were sold, and what types were sold.  However, routine reporting is no longer required.  .

No other recordkeeping or reporting is necessary for new aftermarket converter manufacturers unless they create a new line of converters, in which case data must be submitted regarding test results and appropriate applications of the converters.  For used converter reconditioners, testing of each converter is necessary to determine if it is still functional.  However, no specific record retention requirement exists regarding the results of individual tests, other than to include a certification with the converter that it passed testing.  This short statement can be pre-printed form.

If industry voices an interest in electronic reporting, EPA will facilitate such data interchange, if practical. In the meantime, we would be willing to accept computer discs or other electronic information containing warranty information instead of hard copies of the information.  Since routine reporting of sales and warranty information is no longer required this does not appear to be a significant issue.

Installers have no reporting requirement.  They merely fill out a warranty card for each converter installed, and include on the customary business practice invoice a pre-printed statement with a blank for why replacement was appropriate.  The invoice, including the “reason for replacement” statement, must be kept for 6 months.  In addition, the removed converter is tagged for a 15 day period, so it can be directly related to the vehicle and to the aftermarket converter that replaced it.

5(c) Small Entity Flexibility

The information collection reduces to the extent practicable and appropriate the burden on persons who shall provide information to or for the Agency, including with respect to small entities, as defined by the Regulatory Flexibility Act (5 U.S.C. § 601(6)), the use of such techniques as:  (1) establishing differing compliance or reporting requirements or timetables that take into account the resources available to those who are to respond; (2) the clarification, consolidation, or simplification of compliance and reporting requirements; or (3) an exemption from coverage of the collection of information, or any part thereof.

New aftermarket catalytic converter manufacturers are substantial businesses with gross revenues in the millions of dollars per year.  The catalytic converter reconditioners tend to be smaller businesses and the recordkeeping and reporting requirements are somewhat less; to wit: there are no warranty requirements and therefore no requirements to maintain warranty cards or report warranty information.  More importantly, the policy allows small businesses to compete with the original equipment manufacturers in a market which was previously inaccessible to them, and which would not be legal but for this policy.  Many installers are small businesses and have benefitted significantly from this multimillion dollar industry.  Their requirements are minimal (4-5 minutes per installation, at least some of which is not an EPA imposed burden since maintaining invoices is a customary business practice).

5(d)  Collection Schedule

Sales reports were previously required to be submitted to EPA by manufacturers and reconditioners semi-annually.  This routine reporting is no longer required.  No other regular reporting exists, but reports must be submitted by new aftermarket converter manufacturers for new product lines.  Installers do not report.  Their recordkeeping occurs at the time of each installation transaction.

6.  ESTIMATING THE BURDEN AND COST OF THE COLLECTION

Assumptions:

The estimated dollar cost for new aftermarket converter manufacturers will be different than for used OE converter reconditioners, since the policy is different for each group.  The cost estimates for manufacturers and reconditioners, and for installers, are outlined below.

New Converter Manufacturers

1.  The number of new aftermarket converter manufacturers is approximately 8 (down from 12 in the previous ICR).  The cost to new converter manufacturers consists of 1) the one-time cost of submitting new product line specifications and testing information to EPA; and 2)  the one-time cost to test two converters for each product line using the specifications outlined in the policy.  There is no longer a burden for submission of semi-annual reports regarding manufacturing and sales.

2.  Contractor cost:  Based on estimates supplied by companies that provide the testing services, the testing cost for a typical manufacturer is approximately $88,044 per product line.  This estimate includes the cost for personnel to conduct the testing, as well as the actual cost of the testing equipment and procedures.  If the typical manufacturer markets approximately one new product line every two years, the total testing cost for a typical new converter manufacturer would be $88,044 for two years. Under the assumption that the prevailing interest rate is 10%, the annualized cost of the development testing would be $88,044 amortized over 24 months at 10% compounded monthly, or $48,753 per manufacturer per year. We have estimated a 50% increase in the number of new product lines over the last ICR, in part because there are fewer manufacturers making the same number of converters.

3.  To estimate the labor cost of tabulating and reporting the information as required, it was assumed in the 2002 ICR that the cost for a technician was $33.68/hr. This cost figure was doubled to reflect the cost of benefits and overhead, and was adjusted for inflation from data on the BLS website.  For this ICR we have used the newest available data from the Bureau of Labor Statistics website, which is found at http://stats.bls.gov/news.release/ecec.t02.htm). While no job category necessarily perfectly fits the technical work performed by aftermarket catalytic converter manufacturers, we selected one of the highest paying job categories of those that are closely related: precision metal workers.  Their hourly wage as of 2003 was $19.62 per hour.  In reality, much of the burden can be performed by lower pay scale clerical staff.  To account for benefits and overhead we have doubled this hourly wage, which results in an hourly cost of $39.24.  To account for possible inflation since 2003, we have applied an inflation factor of 1.0571, which results in an inflation adjusted hourly cost burden of $41.48.

4.  The actual hour estimates per response (aside from the elimination of the semi-annual reports as noted above) have been remained the same since the last ICR.  For new converter manufacturers, putting together an EPA report on specifications of a new product line takes about 2 hours.  We have eliminated reporting on manufacturing and sales information, which  took about 0.5 hr.; and eliminated submission of warranty card information, which took about 1 hour to box and send to EPA.  The maintaining of records, including warranty records, requires about 1 hour per year.

Reconditioners of Used Converters

1.  The number of reconditioned converter businesses is six at this time, down from eight.

2.  The cost to a used converter reconditioner consists of the labor costs of testing each` individual converter according to the test procedures outlined in the policy, the cost of setting up the bench testing equipment, and the cost of tabulating and reporting the information required in the policy.  These cost elements are treated separately below.

3.  Two technicians are needed to test each converter.  The cost of a technician per hour is estimated to be somewhat less than for a new aftermarket converter manufacturer, and instead is estimated to be about the same as an automobile mechanic.  For the cost of an employee burden hour, we used the same costs as for new aftermarket converter manufacturers.  This gives an hourly cost per employee of $41.48, including the cost of benefits and overhead and adjusted for inflation to 2005 dollars.

4.  An average of 2.00 minutes are required for each test.

5.  Capital Costs for reconditioners equipment are based on test equipment cost of about $172,000, having a useful life of about 5 years.  If this is amortized over 5 years the yearly cost comes to about $43,854 per reconditioner per year, including interest charges (10% interest).

6.  Record-keeping costs for tabulating and reporting information to Agency are based on the same labor rate as above, even though some of this work may be done by lower pay scale clerical workers.

7.  Reconditioners no longer have the previous reporting burden of  preparation of a semi-annual report (such reports previously took about 4 hrs.; less than 8 hrs. per year). The maintenance of these records takes about 1 hour per year.

Installers of Aftermarket Converters

1.  There are approximately 30,000 automotive exhaust repair shops nationwide.  It is assumed that these entities install the vast majority of aftermarket converters and it is further assumed that all of these entities install converters, and generally excludes tire/brake shops, and other non-exhaust repair facilities such as electrical diagnostic and other such facilities.

2.  There are currently 2.3-2.7  million new aftermarket converters installed per year. A recent report from the Manufacturers of Emission controls Association reported a total of 3,079,249 new aftermarket converters produced in 2001 (including catalytic converters manufactured for use in Mexico).

3.  Typically, it takes an exhaust repair technician 4-5 minutes per installation to handle all recordkeeping requirements (fill out warranty card if applicable, fill in blank on invoice regarding reason for replacement, and tag the converter that was removed).  This estimate is based on information from shop owners as well as EPA experience with the paperwork. In many cases, blank warranty cards are simply provided to customers, further reducing burden times.

4.  The cost of an employee per hour is estimated to be about the same as an automobile mechanic.  For the cost of an employee burden hour, we used the most recent data from the Bureau of Labor Statistics for 2003 ($17.88) and doubled that figure to reflect benefits and overhead.  This gives an hourly cost of $35.76.  We adjusted for inflation to 2005 dollars, which results in an hourly cost estimate of $37.80.

5.  Using the above assumptions, each shop averages 83 installations per year.  On the average, the paperwork is assumed to take about 5 minutes per installation, or 7 hours per year.  At $37.80 per hour, this comes to $263 per year per shop.

6(a)  Estimates of Respondent Burden and Cost

A.  New Aftermarket Catalytic Converter Manufacturers

1.  PROVIDE SPECIFICATIONS FOR NEW PRODUCT LINES:

One-time burden for each new product line.  Assume each manufacturer develops one new product line every year.

HRS. PER RESPONDENT:             2.0

COST PER RESPONDENT:           $82.96

HRS. FOR 8 RESPONDENTS:        16

COST FOR 8 RESPONDENTS:      $664

2.  TESTING OF PROTOTYPES (Purchased Services):

One-time burden for new product lines.  Assume 1 new product line per manufacturer every two years.

HRS. PER RESPONDENT:    (contracted out)

ANNUALIZED COST PER RESPONDENT:       $48,753

HRS FOR 8 RESPONDENTS:  N/A

COST FOR 8 RESPONDENTS:  $390,024

3.  SEMI-ANNUAL SUBMISSIONS OF MANUFACTURING DATA AND

WARRANTY CARDS (reporting requirement discontinued; Recordkeeping                             exists):

HRS. PER RESPONDENT:             1

COST PER RESPONDENT:           $41.48

HRS. FOR 8 RESPONDENTS:       8

COST FOR 8 RESPONDENTS:     $331.84

4.  ANNUALIZED O & M COSTS (for postage): $5 * 8 parties = $40 for all respondents.

B.  USED CATALYTIC CONVERTER RECONDITIONERS

1.  SUBMIT TEST FACILITY INFORMATION:

This is a one-time burden which has already been absorbed by current reconditioners.  No new facilities are anticipated within the period.

2.  PERFORM EFFICIENCY TESTS ON EACH NEW CONVERTER:

HRS. PER RESPONDENT:          623 (Represents 9345 converters tested per year per Respondent)

COST PER RESPONDENT:       $25,842

HRS. FOR 6 RESPONDENTS:      3,738

COST FOR 6 RESPONDENTS:   $155,052

3.  SEMI-ANNUAL REPORTS REGARDING DISTRIBUTION OF PRODUCTS                        (No reporting, but must maintain records):

HRS. PER RESPONDENT:            1

COST PER RESPONDENT:           $41.48

HRS. FOR 6 RESPONDENTS:       6

COST FOR 6 RESPONDENTS:     $248.88

4.  AMORTIZED CAPITAL COSTS PER RESPONDENT:        $43,854.

AMORTIZED CAPITAL COSTS FOR 6 RESPONDENTS:  $263,124.

5.  ANNUALIZED O & M (for postage):  None.

C.  RECORDKEEPING BY EXHAUST SYSTEM REPAIR FACILITIES

1.  MAINTAIN INVOICES & REMOVAL JUSTIFICATION & TAG                             CONVERTERS

HRS. PER RESPONDENT:          7

COST PER RESPONDENT:         $263

HRS. FOR 30,000 RESPONDENTS: 209,000

COST FOR 30,000 RESPONDENTS:  $7,875,000

2.  STARTUP COSTS:  100 STARTUPS * 5 HRS. = 500 TOTAL hours x $37.80 =

$18,900

CAPITAL COSTS (to purchase converter storage space): $228 * 100 = $22,800 for all respondents.

6(b)  Summary of Respondent Costs

1.  Total Yearly Costs for New Aftermarket Converter Manufacturers:

$48,758 per respondent, including contractor testing costs & O

& M costs; $390,064 for all 8 respondents.

2.  Total Yearly Costs for Converter Reconditioners:

$25,884 for yearly converter tests to check

efficiency, capital costs of $43,854 = $69,737 per respondent, and $418,425 for all 6                          respondents.

3.  Total yearly costs for installers:

$263 for 1 respondent =  $7,875,000 for all 30,000 installer facilities.

Total Startup costs for new businesses:  5 hrs. plus $228 for 	     filing space or $417 per party * 100 new parties per year = $41,700 total.

TOTAL YEARLY BURDEN:  $8,725,189 (including salaries); 212,101 hrs. 	      for all respondents, including testing (plus 500 hrs. for 100    	      startups = 212,601 hrs.).  Annualized cost burden other than 	      salaries: $675,988.

SUMMARY OF RESPONDENTS’ BURDENS AND COSTS BY CATEGORY:

I.  New Aftermarket Catalytic Converter Manufacturers

A.  Annual Burden Hours per Party: 3. (24 for all 8 respondents)

B.  Annualized Capital Costs per Party:  $0.00.

C.  Annualized Operating Costs per party:  $5.00 ($40 for all 8)

D.  Annualized Startup Costs:  $0.00 (no new entities entering the market).

E.  Annual Purchased Services per Party (for Testing of Prototypes):  $48,753. ($390,024 for all 8).

II. Used Aftermarket Catalytic Converter Manufacturers

A.  Annual Burden Hours per Party:  624 (testing of catalytic converters to determine they are functional; the actual recordkeeping burden is minimal).  (3,744 for all 6)

B.  Annualized Capital Costs per Party:  $43,854. ($263,124 for all 6)

C.  Annualized Operating Costs per Party:   $0.

D.  Annualized Startup Costs:  None.  There have been no new parties and none are expected in the next 3 years.

E.  Annual Purchased Services per Party:  $0.00.

III. Installers of Aftermarket Converters

A.  Annual Burden Hours per Party: 7

B.  Annualized Capital Costs per Party:  $0.00.

C.  Annualized Operating Costs per party:  $0.00.

D.  Annual Purchased Services per Party:  $0.00.

E.  Annualized Startup Costs:  Assume 100 new installers per year; Assume reviewing instructions and setting up recordkeeping systems requires 5 hrs per party and the purchase of file space of $228.  Total startup cost would be $189 plus $228, for a total of $417 per party and $41,700 nationwide.

6(c)  Estimated EPA Burden and Cost

The direct cost of personnel to process and analyze the information collected is estimated to be $500 or about 20 hours at the cost of a grade 12 employee.  An estimated travel cost of $5,000 would be needed to monitor compliance with the policy, in addition to travel already used for retail level inspections for automobile emissions tampering generally.  The total annual cost to the government is thus estimated to be $5500.

6(d)  Reasons for Change in Burden

Burdens for new and used aftermarket converter manufacturers and  reconditioners have been decreased to reflect reduced reporting since reporting sales and warranty information is no longer required.  We also increased the amount of burden for testing new converters since the number of new converters made has remained the same while the number of manufacturers has decreased. We have adjusted cost figures for inflation.  The number of converter installation facilities, and converters being installed have stayed flat as have the burden hours per converter installation; however, total burden hours requested have increased due to the correction of an error in previous renewals (see below for explanation). Government cost has been decreased significantly as the result of the elimination of most respondent reporting requirements.

It is important to note that a combination of errors in calculations in the previous ICR (67FR 319-320, Jan. 3, 2002) led to the annual burden hours for installers being represented as 3.5 hours/year, rather than 7 hours/year. Spread over 30,000 installer respondents this led to a shortfall of 104, 000 burden hours. This figure has been correctly calculated in this ICR renewal.   There is, therefore,  no increase in burden hours to the industry, rather the correction of a previous error which accounts for the higher burden hour numbers.

6(e)  Burden Statement

The public recordkeeping burden for this collection of information is estimated to average:

3 hours per new aftermarket converter manufacturer, on average, with $5 annual operational costs per year and annualized purchased services costs per year of $48,753;

624 hours (including converter testing time) per used converter reconditioner, on average, with annualized capital costs per year of $43,854; and

7 hours per respondent for aftermarket converter installation facilities, with an additional 5 hours for the first year for startup facilities and an additional $228 for startup capital costs.

The overall average is 7 hours per response (212,101 total burden hours divided by 30,014 respondents).

Burden means the total time, effort, or financial resources expended by persons to generate, maintain, retain, or disclose or provide information to or for a Federal agency.  This includes the time needed to review instructions, develop, acquire, install, and utilize technology and systems for the purpose of collecting, validating, and verifying information, processing and maintaining information, and disclosing and providing information; adjust the existing ways to comply with any previously applicable instructions and requirements; train personnel to be able to respond to a collection of information; search data sources; complete and review the collection of information; and transmit or otherwise disclose the information.  An agency may not conduct or sponsor, and a person is not required to respond to, a collection of information unless it displays a currently valid OMB control number.  The OMB control numbers for EPA’s regulations are listed in 40 C.F.R. Part 9 and 48 C.F.R. Chapter 15.

To comment on the Agency’s need for this information, the accuracy of the provided burden estimates, and any suggested methods for minimizing respondent burden, including the use of automated collection techniques, EPA has established a public docket for this ICR under Docket ID No. OECA-2005-0052, which is available for public viewing at the Enforcement and Compliance Docket and Information Center in the EPA Docket Center (EPA/DC), EPA West, Room B102, 1301 Constitution Avenue, NW, Washington, DC. The EPA Docket Center Public Reading Room  is open from 8:30 a.m. to 4:30 p.m., Monday through Friday, excluding legal holidays.  The telephone number for the Reading Room is (202) 566-1744, and the telephone number for the Enforcement and Compliance Docket and Information Center is (202) 566-1752. An electronic version of the public docket is available through EPA Dockets (EDOCKET) at http://www.epa.gov/edocket.  Use EDOCKET to submit or view public comments, access the index listing of the contents of the public docket, and to access those documents in the public docket that are available electronically.  Once in the system, select “search,” then key in the docket ID number identified above.  Also, you can send comments to the Office of Information and Regulatory Affairs, Office of Management and Budget, 725 17th Street, NW, Washington, DC 20503, Attention: Desk Office for EPA.  Please include the EPA Docket ID No. OECA-2005-0052 and OMB control number 2060-0135 in any correspondence.

Part B of the Supporting Statement

This part is not applicable..

PART B.  COLLECTION OF INFORMATION EMPLOYING STATISTICAL METHODS

This section is not applicable because statistical methods are not used in the data collection associated with the aftermarket catalytic converter policy.

APPENDIX A.  Summary of Comments to First Federal Register Notice

No comments were received.

APPENDIX B.  Citation for Information Requirements of the ICR

The information requirements of this ICR are enumerated in the Agency’s proposed and interim enforcement policy published in the Federal Register on August 5, 1986 (51 Fed. Reg.  28114).  In this Federal Register notice the Agency proposed to amend 40 C.F.R. Part 85 by adding a new Appendix IX, which would consist of this enforcement policy.  There are no regulations applicable to this information collection.  The citations listed below for the information requirements refer to this Federal Register notice.

Information Requirement                                                                          Fed. Reg. Citation

New Converter Manufacturers

Collect and Transmit Converter specifications to EPA	51 FR 28119

Collect, file and maintain warranty information	51 FR 28117

Used Converter Reconditioners

Collect, file and maintain sales information and customer lists	51 FR 28118

Installers

Invoices, Warranties, Tag converters	51 FR 28816