MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A10102 | In-Flight Anomaly Number -- | Contractor Report Number E-100-1 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title LH2 LEVEL SENSOR FAILED INSULATION RESISTANCE TEST |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1 |
| HCRIT 1 | Sys_Lvl Y | Misc Codes A (4) B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE LH2 LEVEL SENSOR | PART# 74L4-2 | SER/LOT# 1293 | MANUFACTURER SIMMONDS |
| HARDWARE LRU | NOMENCLATURE LH2 TANK | PART# 80911000000 | SER/LOT# N/A | MANUFACTURER MMC |
| HARDWARE NCA | NOMENCLATURE LH2 LEVEL SENSOR | PART# 74L4-2 | SER/LOT# 1293 | MANUFACTURER SIMMONDS |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EE - RANDOM | Cause ETP - EI-TEST-INST |
| System ELECTRICAL | Defect EM - ELADJ | Material C - EEE | Work Contact J. ADAMS | Fail Date 05/20/1986 |
| Received at MSFC 06/23/1986 | Date Isolated -- | FMEA Reference 3.6.1.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location SIMMONDS | Symptom EVM - CON/MEG FAIL | Time Cycle -- |
| Effectivity Text LWTS 16, 20, 21, 22, 24 AND SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 02/10/1995 | CN RSLV SBMT 09/28/1987 | Defer Date -- | Add Date -- | R/C Codes 4 - TEST -- -- |
| Assignee |
| Design P. MULLER | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| Approval |
| Design P. MULLER | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete JE | MSFC Closure Date 12/17/1987 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description REF: PREVIOUS CAPS E-081, E-093, MARS T-53578, A11016. A LIQUID HYDROGEN LEVEL SENSOR FAILED TO MEET THE INSULATION RESISTANCE REQUIREMENT OF THE VENDOR ACCEPTANCE TEST PLAN. THE MINIMUM ALLOWABLE RESISTANCE AT 500 VOLTS DC IS 2 MEGHOMS. THE ACTUAL VALUE OBTAINED WAS A NEAR 0 OHMS INDICATION |
| Contractor Investigation/Resolution REMEDIAL ACTION - THE TEST REQUIREMENTS FOR THE SENSORS ARE NOT CONSISTENT AMONG THE VENDOR, MAF, AND THE LAUNCH SITE. TEST REQUIREMENTS HAVE BEEN REVISED TO BE CONSISTENT WITH THE VENDOR'S ALSO,THE REVISION TO INCLUDE CONTROLS ON THE RELATIVE HUMIDITY AND THE TEMPERATURE DURING THE TEST. LAUNCH CONSTRAINT - NONE. THE FAILURE OCCURRED DURING ACCEPTANCE TESTING AT THE VENDOR. ALL LEVEL SENSORS ARE TESTED AGAIN WHEN INSTALLED IN AN ET. 6/26/86 BACKGROUND INFORMATION - LIQUID LEVEL SENSORS UNDERGO A SERIES OF VENDOR LEVEL ACCEPTANCE TESTS TO ASSURE THAT THEY ARE IN COMPLIANCE WITH THE DRAWING REQUIREMENTS THE SEQUENCE OF TESTS, UP TO THE POINT AT WHICH FAILURE OCCURRED ON THIS SENSOR, ARE AS FOLLOWS: 1. VERIFICATION OF THE PHYSICAL DIMENSIONS OF THE SENSOR. 2. VISUAL EXAMINATION OF THE SURFACE FINISH OF THE CASE AND THE CONDITION OF THE WIRES. 3. WEIGHT OF THE SENSOR. 4. DIELECTRIC STRENGTH TEST OF 500 VOLTS AC FOR 1 MINUTE. 5. INSULATION RESISTANCE GREATER THAN 2 MEGOHMS AT 500 VOLTS DC, AT WHICH POINT THE SENSOR FAILED AND TESTING WAS HALTED. LATER TESTS IN THE SERIES INCLUDE THERMAL SHOCK, RESPONSE RATE, RESISTANCE OF THE ELEMENT, ETC. FAILURE INVESTIGATION - THE VENDOR, SIMMONDS PRECISION, WILL PERFORM THE INITIAL STEPS OF THE FAILURE ANALYSIS AT THEIR FACILITY. THE F/A PLAN HAS BEEN COORDINATED WITH MMC RELIABILITY ASSURANCE AND WILL BE WITNESSED BY THE MMC PROCUREMENT QUALITY REPRESENTATIVE. 7/15/86 PRB STATUS - FA PARTIALLY COMPLETE. EXPECT COMPLETION WITHIN 40 DAYS. MR G. P. BRIDWELL REQUESTED THE PROBLEM REPORTS SHOULD INDICATE THAT THIS SENSOR IS INTERCHANGEABLE WITH THE DEPLETION SENSOR AND THE DEPLETION SENSOR HAS A CRITICALITY 1 FUNCTION. MMC CONCURRED. 8/21/86 PRB STATUS - TWO ADDITIONAL NOISE FAILURES ON -039. FAILURE ANALYSIS TO BE CONDUCTED ON THE ADDITIONAL FAILURES. 9/18/86 PRB STATUS - FA CONTINUING AT VENDOR. FAILURE IS AN ARC-OVER. PIN HOLES IN COVER PAINT IS WHERE ARC-OVERS OCCUR. COVER TO GE FOR FA. FAILURE CONSIDERED NORMAL PRODUCTION FALLOUT. TEST IS AT 500V. ACTUAL USAGE IS APPROXIMATELY 20V NO CORRECTIVE ACTION PLANNED. ECD IS MID OCTOBER 86. 10/16/86 PRB STATUS - NO CHANGE. ECD FOR COMPLETION AT MMC IS 12-5-86. 2/19/87 PRB STATUS - ELECTRICAL ENGINEERING WILL GENERATE A PRCN TO REVISE OMRSD FILE 4 TO INCLUDE AN ISOLATION RESISTANCE CHECK OF THE LH2 ECO SENSORS AND TO TEST ALL VEHICLES THAT HAVE ALREADY COMPLETED FILE 4 TESTING ENGINEERING IS ALSO EVALUATING THE EFFECT OF THE ADDITIONAL SENSOR FAILURE UPON THE ACCEPTABILITY OF THE SENSORS IN COMPLETED ETS. 4/31/87 - ADDITIONAL CORRECTIVE ACTIONS REQUIRED. ECD 6/19/87 5/28/87 - UPDATE STATUS - NO CHANGE 9/29/87 CLOSURE UPDATE - REF MMC CAPS E-100B GENERAL A. BACKGROUND INFORMATION THE CRYOGENIC, POINT, LIQUID LEVEL SENSORS, PART NUMBERS 74L4-1 AND -2, LOX AND LH2 SENSORS RESPECTIVELY, ARE VIRTUALLY IDENTICAL IN CONSTRUCTION. THE SOLE DIFFERENCE BETWEEN THE SENSORS LIES IN THE TYPE OF TEFLON INSULATION ON THE OUTPUT WIRES. THE SENSORS ARE USED TO INDICATE THE PROPELLANT LEVELS IN THE ET AND, IN THE CASE OF THE LH2 SENSORS, FOUR ARE USED AS PROPELLANT DEPLETION SENSORS TO SHUTDOWN THE ORBITER MAIN ENGINES. VENDOR LEVEL ACCEPTANCE TESTING VERIFIES PHYSICAL DIMENSIONS, RESPONSE RATE, ELEMENT RESISTANCE, AND ISOLATION RESISTANCE OF EACH SENSOR. TESTS AT MAF AND THE LAUNCH SITES CHECK ELEMENT RESISTANCE AND ISOLATION RESISTANCE TASK I - THE RESULTS OF FAILURE ANALYSIS T-53578 PERFORMED BY SIMMONDS PRECISION ARE AS FOLLOWS: 1. THE CAUSE OF THE SENSOR FAILURE WAS ARCING BETWEEN THE CIRCUIT PATH ON THE SENSOR ELEMENT SUBSTRATE AND THE METAL CASE OF THE SENSOR. 2. THE SENSOR DESIGN IS SUCH THAT THE CIRCUIT PATH ON THE SUBSTRATE CAN CONTACT THE METAL CASE FROM WHICH IT IS SUPPOSED TO BE INSULATED. THE SOLE INSULATION AT THAT POINT IS THE SPRAYED ON, BAKED, TEFLON PAINT ON THE INTERNAL SURFACES OF THE CASE. 3. THE TEFLON PAINT ON THE CASE MET THE DESIGN REQUIREMENTS FOR THICKNESS. TASK II CORRECTIVE ACTION A. THE VENDOR DEVELOPED AN ASSEMBLY AID TO MORE ACCURATELY CENTER THE SUBSTRATE IN THE CASE. THIS SHOULD REDUCE THE OCCURRENCES OF THE CIRCUIT PATH TOUCHING THE INTERNAL SURFACE OF THE CASE (REFERENCE MARS T-53578). HOWEVER, THE DESIGN OF THE SENSOR PROVIDES NO POSITIVE MECHANICAL SEPARATION AND THE PARTS COULD SHIFT INTO CONTACT AT A LATER TIME. B. ELECTRICAL ENGINEERING HAS SUBMITTED PRCN-MMC-XL TO REVISE OMRSD FILE 4 TO INCLUDE AN ISO- LATION RESISTANCE TEST OF THE LH2 DEPLETION SENSORS AND TO TEST ALL VEHICLES THAT HAVE ALREADY COMPLETED FILE 4 TESTING. THE RCN HAS BEEN APPROVED AND ASSIGNED NUMBER MT-7484. CHANGE SUMMARY B01806 WAS APPROVED ON SEPTEMBER 16, 1987. THE VENDOR ATP REQUIREMENTS WERE REVISED TO INCLUDE HUMIDITY AND TEMPERATURE CONTROLS DURING THE ISOLATION RESISTANCE TESTS. THE MAF FLIGHT ACCEPTANCE REQUIREMENTS, MMC-ET-TM04K-B, WERE REVISED TO REQUIRE THE SAME ISOLATION RESISTANCE VALUE AS USED DURING THE VENDOR ATP. TASK III CLEARANCE OF EFFECTIVITIES THERE ARE NO CONSTRAINTS. ALL ETS ARE TO BE RETESTED FOR ISOLATION RESISTANCE OF THE LH2 DEPLETION CIRCUITS, PER RCN MT-7484. TASK IV CAPS CLOSURE SUMMARY THE SENSORS EXPERIENCED ISOLATION RESISTANCE FAILURES WHICH RESULTED FROM BOTH THE SENSITIVITY OF THE SENSORS TO HIGH HUMIDITY AND THE ISOLATION RESISTANCE REQUIREMENTS BEING MORE STRINGENT AT MAF THAN AT THE VENDOR. HISTORICALLY, THERE HAVE BEEN NO LEVEL MEASUREMENT CIRCUIT FAILURES AT KSC WHICH WERE ATTRIBUTED TO LOW ISOLATION RESISTANCE ON ANY OF THE APPROXIMATELY 20 SENSORS ON EACH ET.THE SENSOR DESIGN IS CONSIDERED TO BE ADEQUATE. THE ISOLATION RESISTANCE REQUIREMENTS WERE REVISED AT THE VENDOR, MAF, AND THE LAUNCH SITE. THE CHANGES WILL INCREASE THE LIKELIHOOD OF DETECTING SENSOR FAILURES DURING VENDOR ACCEPTANCE TESTING, RATHER THAN AFTER INSTALLATION ON AN ET. THE REQUIREMENTS AT THE LAUNCH SITE FOR THE SENSORS IN THE LH2 DEPLETION CIRCUITS WERE REVISED TO INCLUDE AN ISOLATION RESISTANCE TEST TO THE SAME VALUE AS A NEW SENSOR. LOW ISOLATION RESISTANCE WILL CAUSE AN ORBITER LEVEL SENSOR SIGNAL CONDITIONER TO GIVE A FALSE "WET" INDICATION. SINCE THIS FAILURE MODE IS CRITICAL ONLY FOR THE LH2 DEPLETION CIRCUITS, ADDITIONAL TESTS FOR THE REMAIN- ING SENSORS WERE NOT ADDED TO THE TESTING AT THE LAUNCH SITE. THE VENDOR ACCEPTANCE TEST REQUIREMENTS ARE NOW SUFFICIENTLY STRINGENT TO DETECT THE MAJORITY OF ALL SENSORS WHICH HAVE LOW ISOLATION RESISTANCE. A LIMITED NUMBER OF ISOLATION RESISTANCE TEST FAILURES CAN BE EXPECTED TO OCCUR DURING VENDOR TESTING AS A NATURAL RESULT OF THE SENSOR DESIGN. THIS PROBLEM IS SUBMITTED TO MSFC FOR CLOSURE REVIEW AND APPROVAL |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A10102 | IFA# -- | Contractor RPT# E-100-1 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 74L4-2 | Asmnt Part Name LH2 LEVEL SENSOR | Asmnt Serial/Lot# 1293 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD ETP - EI-TEST-INST | FAIL MODE EM - ELECT LEAK |
| Asmnt FMEA 3.6.1.1 | Asmnt FM 1 | FMEA CSE A | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |