LEDAPS Mid-Atlantic Disturbance Mosaics

LEDAPS is releasing aggregated maps at 500m and 1/20th degree resolution.  At present, these aggregates are only subsets along the Mid-Atlantic region of the US.  All products are in HDF-EOS format.  The product specifications are given here:

1.  500m Lambert Product

Projection:  Lambert Equal Azimuthal

Pixel size:  500 meters

Radius of Sphere:  6370997

Longitude of origin:  100 00 00 W

Latitude of origin:  50 00 00 N

False easting:  0.0

False northing: 0.0

XY corner coordinates (center of pixel) in projection units (meters):

Size xy=(1344,1762)

Lower left:  ( 1583250.0,-1468750.0 )

Upper left:  ( 1583250.0, -588250.0 )

Upper right: ( 2254750.0, -588250.0 )

Lower right: ( 2254750.0,-1468750.0 )

Data Layers

|  | Layer | Units | Bits | Scaling/format |
| --- | --- | --- | --- | --- |
| 1 | % cell area disturbed | percent | 8 | none (0-100) |
| 2 | % cell area regrown | percent | 8 | none (0-100) |
| 3 | % 2001 forest area disturbed | percent | 8 | none (0-100) |
| 4 | % 2001 forest area regrown | percent | 8 | none (0-100) |
| 5 | Interval between TM, ETM acquisitions | decimal years | 16 | Years * 1000 |
| 6 | TM acquisition date |  | 16 | [DOY][YY] |
| 7 | ETM acquisition date |  | 16 | [DOY][YY] |
| 8 | Not mapped | percent | 8 | none (0-100) |
| 9 | QA bits |  | 8 | See below |

2.  1/20th Degree Product

Projection:  None (geographic)

Pixel size:  0.05 degrees

Lat/lon corner coordinates (center of pixel):

Size xy= (173,128)

Lower left:  ( 82:09:00.0 W, 35:00:00.0 N )

Upper left:  ( 82:09:00.0 W, 41:21:00.0 N )

Upper right: ( 73:33:00.0 W, 41:21:00.0 N )

Lower right: ( 73:33:00.0 W, 35:00:00.0 N )

Data Layers

|  | Layer | Units | Bits | Scaling/format |
| --- | --- | --- | --- | --- |
| 1 | % cell area disturbed | percent | 8 | none (0-100) |
| 2 | % cell area regrown | percent | 8 | none (0-100) |
| 3 | % 2001 forest area disturbed | percent | 8 | none (0-100) |
| 4 | % 2001 forest area regrown | percent | 8 | none (0-100) |
| 5 | Interval between TM, ETM acquisitions | decimal years | 16 | Years * 1000 |
| 6 | TM acquisition date |  | 16 | [DOY][YY] |
| 7 | ETM acquisition date |  | 16 | [DOY][YY] |
| 8 | Not mapped | XXX | 8 | XXX |
| 9 | QA bits |  | 8 | See below |

QA Bits Key:

Bit 0 – regrowth somewhere

Bit 1 – disturb somewhere

Bit 2 – not changed somewhere

Bit 3 – cloud somewhere

Bit 4 – shadow somewhere

Big 5 – snow somewhere

Bit 6:  Landsat-4 data used (i.e. beware of a poor calibration)

Bit 7:  entire cell contaminated with cloud/snow or shadow

Note: fill value= 0.  When no bits are set, no valid data maps to the output cell.

3.  30-meter (scene pair based) disturbance map product.

UTM projection (not reprojected from GeoCover, 8-bit).
   - Layer 1:  disturbance map with separate values for:
        - disturbed forest (biomass loss)
        - regrown forest (biomass gain)
        - no change
        - not mapped (null, cloud, shadow)
   - Layer 2 :  DI_diff image  (rescaled to 8-bit)

Scaled as follows :

nearest_integer( 127.5 + (di_diff/4.679)*20.0 );

- Layer 3:   TM fuzzy forest probability (8-bit scaled 0 to 100%)

- Layer 4:   ETM fuzzy forest probability (8-bit scaled 0 to 100%)

- Layer 5    QA bits (8-bit)

bit 0 (lsb):	regrowth

bit 1: 		disturbance

bit 2:	 	filtered

bit 3 :		cloud

bit 4 :		shadow

bit 5 :		snow

bit 6:                  	sieve filtered

bit 7 (msb) :	fill

Also add TM, ETM+ acquisition dates to product  metadata

Total size ~ 225 MB