SF-33

PART I – THE SCHEDULE

SECTION B – SUPPLIES OR SERVICES AND PRICES/COSTS

B.1  SCHEDULE OF ITEMS

| Item No. | Description | Estimated Quantity | Unit | Unit Price | Amount |
| --- | --- | --- | --- | --- | --- |
| 1. | Mechanized thinning and removal of both sawlog and biomass material, stump treatment, hand pile roadside/view area and machine pile landing slash, road maintenance, dust abatement, erosion control and sub soiling (scarification) of landings. Prattville Forest Recovery DFPZ, Units: |  |  |  |  |
| A | 4 | 53 | acre |  |  |
| B | 5 | 15 | acre |  |  |
| C | 11 | 23 | acre |  |  |
| D | 22 | 16 | acre |  |  |
| E | 24 | 13 | acre |  |  |
| F | 27 | 4 | acre |  |  |
| G | 30 | 33 | acre |  |  |
| H | 31 A & B | 15 | acre |  |  |
| I | 32 A | 219 | acre |  |  |
| J | 32 B | 277 | acre |  |  |
| K | 32 C | 308 | acre |  |  |
| L | 32 D | 124 | acre |  |  |
| M | 34 | 6 | acre |  |  |
| N | 51 | 19 | acre |  |  |
| O | 56 | 18 | acre |  |  |
| P | 57 | 20 | acre |  |  |
| Q | 60 | 12 | acre |  |  |
| R | 64 A & B | 35 | acre |  |  |
| S | 68 | 21 | acre |  |  |
| T | 71 | 8 | acre |  |  |
| U | 78 | 33 | acre |  |  |
| V | 86 | 50 | acre |  |  |
| W | 91 | 6 | acre |  |  |
| X | 95 | 6 | acre |  |  |
| Y | 97 | 22 | acre |  |  |
|  | Total Item 1 | 1356 |  | $_____ | $_____ |

B.2  ALTERNATIVE PAYMENT METHODS

This contract provides for payments to the Contractor through several alternative methods. The contract awardee will select the specific method of payment and the designation of the payment office prior to contract award.  The alternative payment methods are;

- Payment made in accordance with the Prompt Payment clause processed by Financial Operations, Plumas National Forest, Quincy, California.  Payment will be by Electronic Funds Transfer (EFT); or

- Payment made in accordance with the Discount for Prompt Payment clause and Payment by Third Party clause processed by the Contracting Officer.  Payment will be by VISA credit card or check.  See Clause I.9, Payment by Third Party, FAR 52.232-36, page 36.

B.3  SITE VISIT

(a) The clauses at 52.236-2, Differing Site Conditions, and 52.236-3, Site Investigations and Conditions Affecting the Work, will be included in any contract awarded as a result of this solicitation. Accordingly, offerors or quoters are urged and expected to inspect the site where the work will be performed.

(b) An organized site visit has been scheduled for--

Wednesday, August 16, 2000, at 0900 hours.

(c) Participants will meet at--

Almanor Ranger Station, 900 Hwy. 36, Chester, CA

For additional information concerning the project requirements, contact Robin Bryant, Acting District Timber Management Officer, (530) 258-2141.

For additional information concerning the procurement process or contract terms and conditions, contact Miley Sutherland, Contracting Officer, (530) 252-6621.

SECTION C –DESCRIPTION/SPECIFICATIONS/WORK STATEMENT

C.1  GENERAL REQUIREMENTS

C.1.1 Background

This contract combines several processes that have historically been accomplished by numerous individual contracts.  In the past, contracts have been awarded for logging, fuel reduction, precommercial thinning, and subsoiling all in the same general area.  Each of these was designed to meet the management objectives for a narrow range of resources.  Fuel reduction was for fire management goals while logging and thinning were for forest health goals, and subsoiling was for soils and hydrology goals.  This contract combines all of these operations into one contract to take advantage of the efficiencies of having one larger operation to meet multiple objectives.

The project area contains 1,356 acres within treatment units.  The boundaries of the project area are shown on the attached Contract map, which is made part of this contract.  All Contract map detail indicating location is approximate, therefore, actual locations, as the Forest Service has designated on the ground take precedence over the Contract Map.

The environmental documentation (Prattville Forest Recovery Project Environmental Assessment) for this project is available for review at the Almanor Ranger District office in Chester, California.

C.1.2  Scope of Contract

The purpose of this contract is to secure a complete set of services to accomplish stand treatments identified in the Prattville Forest Recovery Project Environmental Assessment, specifically, the reduction of existing fuels through: tree thinning; retention of the largest trees; and removal of biomass and small sawlog material.  The needs in each unit may vary from a mixture of all the above tasks to only one single task.  The contractor shall, considering given sets of resource objectives for each unit, develop a plan of operations to accomplish these objectives, and organize and direct all of the equipment and personnel needed to fully accomplish the work.  The contractor shall furnish all technical expertise, labor, equipment, supervision, transportation, operating supplies, and incidentals necessary to complete the work required.

Utilizable material shall be purchased from the Government under the terms of a 2400-3 Timber Sale Contract attached as Exhibit B.  Within 30 days following award of the service contract the contractor shall sign and execute the 2400-3 Timber Sale Contract AND make a 10 percent downpayment based on the total estimate value.  Failure to execute the timber sale contract and provide the downpayment by the date due is cause for termination of the service contract.

C.1.3  Location and Description  The project is located approximately 6 miles southeast of Chester, CA. off State Highway 89.

C.1.3.1  Location  See Map Exhibit A-1.

C.1.3.2  Description  The project area consists of forested stands dominated by gentle slopes less than 30

percent.  It is expected that ground based equipment will be used on all units.

The project area is comprised of one (1) bid item.

Item 1 - Thinning (see also C.2.3.1), is comprised of thinning 1356 acres of forested stands on ground that is all workable with ground based machinery and removing utilizable products (see C.2.3.1.4). Volume estimates for products are stated in Exhibit B, FS-2400-3 Timber Sale Contract.  Item 1 also includes: Hand and Machine Piling of Contractor created slash within View Areas and roads (see C.2.3.1.6), Road Maintenance and Dust Abatement (see C.2.3.1.7) of roads used for contract operations, Erosion Control measures necessary for soil and water resource protection and Sub Soil Scarification of Landings (see C.2.3.1.9).

C.1.3.3  Boundaries  A  map is attached as Exhibit A-1, showing the location of the unit boundaries.

Exterior boundaries of all units are marked in the field with blue flagging and orange boundary paint facing into the unit and along the boundary.  Boundaries are not painted along existing roads.

C.1.3.4  Access  Access to all items exist and will require some road maintenance.  See C.1.3.6 and C.3.6

for restrictions.

C.1.3.5  Maps  The size, shape, and location of the contract units were mapped by utilizing the Global

Positioning Satellite (GPS) technology.  Positions of the features shown on the maps are approximate.

C.1.3.6  Restrictions on Work  Work may be performed at any time during the period of the contract,

except as outlined in this part.  Nothing in this part shall be construed to take away any of the Government's rights under the Suspension of Work Clause (52.242-14, Page 19, Item F.8).  Restrictions are as follows:

1.  In accordance with the fire plan, attached in Section J.

2.  When Contracting Officer Representative has determined that adverse weather has made access, haul, or skidding too dangerous, or that continued vehicular travel would cause unacceptable road, landing, or skid trail damage.  If damage to roads, landings, or skid trails occurs, it shall be mitigated according to Specifications C.2.3.1.7 and 2.3.1.9.

3.  Within a sub-item boundary, the Government may exclude no work areas such as:  rocky areas, wildlife areas, wet areas, streamside buffers, and other special areas.  No-work areas will be designated by the Contracting Officer's Representative.  Payment will not be made for no-work areas greater than one acre in size.

4.  Limited Operating Periods: Refer to Exhibit A-2 for a map of the Limited Operating Periods.  Individual Limited Operating Periods may be lifted at the discretion of the Contracting Officer when site specific conditions warranted a reduction in the time period.

Sub-items 1.a, 1.c, 1.p, q, 1.u, 1.x, and 1.y (Units 4 - east half, 11, 57, 60, 78, 95 and 97:) no operations shall be allowed between April 1 and August 31, due to wildlife restrictions (within ¼ mile of all active Osprey nest sites).

Sub-items 1.g, 1h, 1.k, and 1.n (Units 30, 31B - between road 27N03 and Highway 89, 32C, and 51): no operations shall be allowed between November 1 and August 31, due to wildlife restrictions (within designated Bald Eagle territory, and active nests).

If winter roosts are identified during the contract period, a limited operation period will be put in place at that time. (Sub-items/Units - none known at this time): no operations shall be allowed between November 1 and March 1, due to wildlife restrictions (Bald Eagle Winter Roosts).

Sub-items 1.r and 1.s (Units 64B and 68): no operations shall be allowed between March 1 and August 31, due to wildlife restrictions (within ¼ mile of a California spotted owl protected activity center boundary).

Sub-items 1.i and 1.w (Units 32A – southwest corner, and 91): no operations shall be allowed between March 1 and September 15, due to wildlife restrictions (within ¼ mile of Goshawk nest site).

Sub-items 1.r, 1.s, 1.t, and 1.w (Units 64A&B, 68, 71, and 91): no operations shall be allowed between March 1 and August 1, due to wildlife restrictions (within ½ mile of suitable marten or fisher den habitat).

Sub-items 1a, 1.b, and 1.c (Units 4, 5 and 11): no operations shall be allowed between December 26 and April 15 to maintain winter sports opportunities in the vicinity of County Road 307 and 308, and the portion of the Almanor Recreation Trail from the Almanor West Development to the Almanor North Campground.  Hauling shall not be allowed on County Roads 307 and 308 during this period.

5.  Location of areas needing special measures for protection of plants, animals and heritage resources are shown on individual unit maps and identified on the ground with red and white striped flagging.  If a Limited Operating Period is needed for such protection, the dates of restricted activity are shown on the project area map and listed above.

6.  If protection measures prove inadequate, if other such areas are discovered, or if new species are listed or found during the term of the contract, the Forest Service may modify under clause 52.243-01 Alternate 1 ( Page 38, Item I.12)this contract to provide additional protection regardless of when such facts become known.  Discovery of such areas by either party shall be promptly reported to the other party.

C.1.3.7  Definitions

Additional Timber - Any sawlog size tree that is designated and agreed to by the Contracting Officer after contract award.

Best Management Practice (BMP) - An alternative structural or nonstructural practice approved by the California Regional Water Quality Board for the effective manual erosion control and management of surface runoff.  BMP's are described in Chapter 30 of the Forest Service Manual (the BMP Handbook).

Biomass - Any portion of any tree, designated for cutting, which does not meet the utilization standards for Sawlog set forth in the contract, but has a small end diameter of one (1) inch, or greater, and is six (6) feet, or greater, in length. The anticipated product of this material is wood chip for fuel or mulch. This material includes non-sawlog quality products.  Biomass is sometimes referred to as Miscellaneous Convertible Products.

Bole - Stem portion of a tree.

Conifer - A cone-bearing tree with needles or leaf scales (e.g. pine, fir, cedar).

Cut-tree - A tree that is designated by the Forest Service for felling. Designated cut-trees are either marked for removal with blue paint, or not marked in area designated with leave trees marked in white paint, meeting the specifications listed under C.2.3.1.2 and C.2.3.1.3.  Leave trees marked with white paint shall not be cut.  Trees marked for boundaries (orange paint) shall not be cut.  Trees marked with a combination of paint colors that include white paint shall not be cut.

Damaged Trees - Any tree with one or more of the following injuries:

1. Any true fir that has any bark cut or removed to the cambium from more than 25% of the circumference of the bole.

2. Any tree that has had 25% or more of the live limbs or branches broken or removed by any operation.

DBH - Diameter at breast height; the diameter of a tree measured at a point 4.5 feet above the ground on the uphill side of the tree.

DFPZ - Defensible Fuels Profile Zone, also referred to as "shaded fuel break". A strategically located strip or block of land approximately one quarter to one half mile wide on which the vegetation has been changed by a variety of fuel treatments into a fuel profile with an acceptable fire spread rate and intensity.  DFPZ's shall not be constructed inside Riparian Habitat Conservation Areas (RHCA).

DSH - Diameter at stump height; the diameter measured at a point six (6) inches above the ground on the uphill side of the tree or stump.

Hardwood - A tree with broad leaves rather than needles (i.e. aspen, willow, etc.).

Incomplete Marking – Forest Service designation of Leave Trees or Individual Cut Trees is not complete in some units.  Forest Service will complete the marking of these units prior to contractor operations.  Boundaries of Incompletely Marked units have been designated in advance with Orange Paint.  Sample mark areas for both Individual Tree Marking (ITM) and Leave Tree marking (LTM) have been completed.  See contract map for the location of sample mark areas.

Improvement – All roads, trails, ditches, land survey corners, telephone lines, power lines, fences, buildings and structures, recreational development sites, research plots, septic systems, water guzzlers and similar items which the contractor must protect during operations.  Refer to C.3.3 Other Resource Protection.

Leave Tree - Conifers planned to become part of the forest canopy in the long term.  A leave tree is determined by both spacing and vigor of existing conifers.  Any tree marked with white paint in a Leave Tree Marked unit is a leave tree and shall not be cut.  Trees marked with orange paint, to determine units boundaries are leave trees, and shall not be cut.  Trees marked with a combination of paint colors that include white paint shall not be cut.  In Individual Tree Marked units, trees not designated for removal with blue paint are Leave Trees and shall be protected from damage during operations

Reserve Trees – Trees identified to be resistant to white pine blister rust and trees identified as candidates for blister rust resistance.  Rust Resistant Sugar pine trees and Candidate trees are marked with orange painted RRSP and or RT.  These trees are identified on the project map in Exhibit A-1, Section J.

Riparian Habitat Conservation Areas (RHCA) -  Generally an area which owes its biological and physical characteristics to the presence of surface or near surface ground water, including stream courses, riparian habitat, drainage ways, meadows, vernal pools, and other areas of water influence.  The RHCA buffer width requirements were identified by the Scientific Analysis Team (SAT) Report (Viability Assessment and Management Considerations for Species Associated wit Late-Successional and Old-Growth Forests of the Pacific Northwest, The Report of The Scientific Analysis Team, USDA Forest Service, March 1993).

Sawlog - Any log length, of any tree designated for cutting, which meet the utilization standards of 25% sound wood, ten feet minimum length and a small end minimum diameter of six (6)  inches. The anticipated product of the Sawlog material is lumber.

Slash -  Vegetative debris generated by Contractor's Operations that measures 1-2.9 inches in diameter on the large end and 3-5.9 feet in length. Within DFPZ's slash shall also include brush cut by Contractor's operations.

Snag - Any standing conifer tree without green needles.

Subsoiling (Scarification) - Tilling or breaking up the compacted layers of the soil without destroying soil structure or mixing soil layers.

Thinning - The cutting of trees in excess of those to be left for future stand needs.

Upper Limit Diameter Breast Height - The diameter breast height at which trees equal to or larger than may not be cut or removed.  Trees equal to or larger that the Upper Limit Diameter are needed for retention to meet the Interim Guidelines for Management of California Spotted Owls (CASPO).

Utilization - The removal of all felled and yarded material from National Forest land.  Forms of utilization include chips, logs, fuel wood, posts, etc.

C.2  TECHNICAL REQUIREMENTS

C.2.1  Desired End Result  The desired end result of this project is to achieve the following:

1.  Reduce ladder and surface fuels, thereby reducing the susceptibility of the forest to catastrophic losses caused by wildfire,

2.  Open gaps in the canopy and retain the largest trees, thereby restoring fire resiliency in stands located in high risk fire areas,

The method of accomplishing these objectives may consist of a combination of tasks where in the past, each task was intended to meet a single resource management objective.  Treatment on each item may vary from using only one type of task to using a combination of many of these tasks.  The desired result should minimize the need for any further mechanical treatment for the next ten years.

C.2.2  Detailed Requirements

A proposed treatment plan and schedule shall be prepared by the Contractor and be reviewed and approved by the Contracting Officer before starting work in each unit. The proposed treatment plan shall include information on what tasks will be used to meet the resource management objectives, what equipment will be used, a schedule of work, and what protection measures will be used to protect specific features.  The proposed treatment plan shall discuss any suggested changes to the resource objectives, boundaries or exclusions due to new information discovered during a field reconnaissance.

C.2.3  Work Standards

C.2.3.1  Item 1 – Thinning  This includes various activities to increase the health and vigor of residual trees and modify the quantity and/or arrangement of live and dead forest fuels to reduce fire size, severity, and level of resource damage.  The methods to accomplish thinning include mechanized harvesting with ground based skidding, hand piling, and removing utilizable material.

Thinning in this contract is defined by the diameter of trees that are to be cut by either Area Designation (Orange painted harvest unit boundaries) with white painted Leave Tree Marking (LTM) or are Individually Tree Marked for cutting with blue tree marking paint (ITM).  A detailed table for each unit is located in section C.2.3.1.1.  This project is Incompletely Marked, in some units marking of either leave trees or cut trees was not accomplished prior to solicitation.   Subitems identified as incompletely marked will be designated by the Forest Service in advance of harvesting operations.  Boundaries of incompletely marked units has been accomplished on the ground with orange paint.  Forest Service marking prescription is described in section C.2.3.1.2.

C.2.3.1.1  Unit Thinning Specifications

The table below sets the parameters for thinning in each unit:

Prattville Forest Recovery DFPZ

| Unit | Method of Designation | Status of Marking | Diameter Range of Trees to be removed (DBH) | Upper Limit DBH |
| --- | --- | --- | --- | --- |
| 4 | ITM | Incompletely Marked | 3.0 “ to 15.9”. | 16.0” |
| 5 | LTM | Incompletely Marked | 3.0 “ to 15.9”. | 16.0” |
| 11 | LTM | Incompletely Marked | 3.0 “ to 15.9”. | 16.0” |
| 22 | LTM | Incompletely Marked | 3.0 “ to 15.9”. | 16.0” |
| 24 | LTM | Incompletely Marked | 3.0 “ to 15.9”. | 16.0” |
| 27 | ITM | Complete | 3.0 “ to 15.9”. | 16.0” |
| 30 | ITM | Complete | 3.0 “ to 15.9”. | 16.0” |
| 31A & B | ITM | Complete | 3.0 “ to 15.9”. | 16.0” |
| 32A | LTM | Incompletely Marked | 3.0 “ to 15.9”. | 16.0” |
| 32B | LTM | Incompletely Marked | 3.0 “ to 15.9”. | 16.0” |
| 32C | LTM | Incompletely Marked | 3.0 “ to 15.9”. | 16.0” |
| 32D | LTM | Incompletely Marked | 3.0 “ to 29.9”. | 30.0” |
| 34 | LTM | Incompletely Marked | 3.0 “ to 15.9”. | 16.0” |
| 51 | LTM | Incompletely Marked | 3.0 “ to 15.9”. | 16.0” |
| 56 | ITM | Incompletely Marked | 3.0” to 17.9”. | 18.0” |
| 57 | ITM | Incompletely Marked | 3.0 “ to 15.9”. | 16.0” |
| 60 | ITM | Incompletely Marked | 3.0 “ to 15.9”. | 16.0” |
| 64 A & B | ITM | Complete | 3.0 “ to 15.9”. | 16.0” |
| 68 | ITM | Complete | 3.0 “ to 15.9”. | 16.0” |
| 71 | LTM | Incompletely Marked | 3.0 “ to 15.9”. | 16.0” |
| 78 | LTM | Incompletely Marked | 3.0 “ to 15.9”. | 16.0” |
| 86 | ITM | Complete | 3.0” to 15.9”. | 16.0” |
| 91 | LTM | Incompletely Marked | 3.0 “ to 15.9”. | 16.0” |
| 95 | ITM | Complete | 3.0” to 17.9”. | 18.0” |
| 97 | ITM | Complete | 3.0” to 17.9”. | 18.0” |

Tree designation will follow the above table.

C.2.3.1.2  Marking Prescription for Incompletely Marked Units  The column headed as Diameter Range of trees to be removed in the table under Section C.2.3.1.1 indicates the diameter range of trees within each unit shown that may be removed.  Trees in this diameter range that are not needed to meet stocking retention guidelines will be designated for removal by the Forest Service.  Trees larger than the Upper Limit DBH will not be marked for removal regardless of residual stocking levels.  All trees not designated for removal are considered to be leave trees and are subject to damage restrictions.

Forest Service shall designate trees for removal that are not necessary to meet the stocking guidelines listed in table C.2.3.1.2.1 below.

# C.2.3.1.2.1 Stocking Guidelines for Defensible Fuels Profile Zones

| Average Leave Tree DBH (inches) | Average Spacing (feet) | Average Leave (trees per acre) | Average Basal Area (sq. ft.) | Average Crown Radius (feet) | Average Leave Crown Closure (%) |
| --- | --- | --- | --- | --- | --- |
| 4 – 8 | 16 * 16 | 170 | 33 | 3.5 | 15 |
| 9 – 12 | 18 * 18 | 134 | 90 | 4.5 – 5.5 | 24 |
| 13 – 16 | 20 * 20 | 110 | 135 | 5.6 – 7.0 | 31 |
| 16 + | 22 * 22 | 90 | 195 | >7.7 | 40 |

1.  Leave all trees larger than the unit specific Upper Limit diameter.

2.  Meet snag retention guidelines for DFPZ.

3.  Thin from below whenever possible, removing smaller poorer formed trees, and reducing fuel ladders.

4.  Clump up to four codominant trees and vary the spacing up to 25 percent to leave the most desirable future crop tree.  However, the number of leave trees per acre shall not materially depart from the guidelines listed above.

5.  Less than acceptable crop trees will not be retained to meet the average desired stocking requirements.

6.  Species selection for leave trees varies between units, but in general an effort will be made to improve species diversity and to improve stand health.

7.  Unit 32 D has a unique prescription designed to control and reduce the spread of black stain root disease.  The Marking prescription for Unit 32 D is in Section J, Exhibit D.

C.2.3.1.3  Designation of Timber

1.  Units identified for ITM in table C.2.3.1.1 Unit Thinning Specifications under the column headed Method of Designation will be individually tree marked for cutting above and below stump height with BLUE paint.  The column headed  ‘Diameter Range of Trees to be Removed’  indicates the diameter size of trees that are, or will be designated for cutting.  Trees not designated for cutting are Leave Trees.

2.  Units identified for LTM in table C.2.3.1.1 under the column headed Method of Designation will be Area Designated with Leave Tree Marking.  Boundaries of Area Designations are marked in ORANGE paint with three horizontal bands facing towards the cutting unit.  Unit numbers are occasional painted in lieu of the three horizontal bands.  An additional ORANGE mark is painted on the sides of the trees in line with the unit boundary.  Within the boundaries of the treatment unit, Leave Trees are marked above and below stump height with WHITE paint for retention.  Within the unit boundary, live and dead trees not identified with white paint as leave trees are designated for removal.  Trees greater than the Upper Limit DBH, whether marked with white paint or not shall not be cut unless painted with a blue “H” by the Forest Service.

C.2.3.1.4  Utilization  Utilization shall consist of removing woody material from the project area.

All trees shall be removed to landings prior to being limbed and lopped.

Stump height shall not exceed eight (8) inches measured from the ground on the uphill side, or four (4) inches above natural obstacles (boulders, wildlife logs, etc.).  All limbs below the cutting point shall be severed flush with the stump.

Utilized material shall be purchased from the Government under the terms of the FS-2400-3 Timber Sale Contract.  Under the terms of the Timber Sale Contract, all material will be Weight Scaled and paid for at the rate per ton specified.

After award of the contract, the Contracting Officer may agree to the designation of additional trees that may need to be removed for landing or skid trail construction or that may be accidentally damaged during the operation.  Any additional trees that are agreed to and designated after award will be paid for at the rates shown in G.5 – Timber Subject to Agreement.

C.2.3.1.5  Removal.  Removal of thinned material in Item 1 shall be accomplished by mechanized felling and ground based skidding or other equipment that performs with comparable results.

The Contractor shall fell designated thinning material using a self-propelled mechanical harvester (feller-buncher) capable of operation on slopes up 35 percent, with an articulating boom having an operating radius of at least 20 feet for cutting trees, capable of lowering and placing trees up to 22.0 inches dbh, on the ground.  Trees exceeding the feller-buncher’s capability may be felled by conventional chainsaw methods.  Conventional felling by chainsaw may be necessary in some instances to provide for resource protection.  Included products must be skidded to landings approved by the Contracting Officer's Representative.

Skid trails and Landings will be approved by the Forest Service prior to felling.

The Contractor must not leave any Included Timber or biomass untreated on the ground for more than 20 days.

Trees shall be directionally felled away from pockets of residual trees, protected improvements, RHCA's, meadows, or private property using normal felling practices, wedging, jacking or lining as needed.  Such directional felling shall not be required when in the faller's judgment it is unsafe to do so, and the tree shall be left standing.

Cut stumps of all species, except cedar, which are greater than eight (8) inches diameter, shall be treated by Contractor. Treatment shall consist of removing sawdust and other loose debris from the cut surface and application of a thin layer of an EPA-registered borate compound for the prevention of annosus root disease. Application rates shall comply with those specified on the product label and application shall be completed within four hours after felling. Any surface irregularities on the stump, which would prevent uniform application of borate, shall be cut level prior to treatment. Contractor shall provide borate compound and apply it in compliance with California states laws and regulations pertaining to pesticides and pest control operations. Contractor shall provide Forest Service with a copy of the "Monthly Summary Pesticide Use Reports" submitted to the appropriate County Agricultural Commissioner.

C.2.3.1.6  Slash Treatment  Slash treatment includes:

1. Slash left within View areas and within 50 feet both sides of all roads accessing the area shall be piled by hand.  Any slash generated from landing operations shall be machine piled for burning.  In lieu of piling and burning, Contractor may chip slash.  Chips must be removed or spread to a depth not to exceed 6 inches. View Areas are shown in Exhibit A-1 Section J, under Contract Requirements.

2. Piles must be constructed in such a manner that results in 85% consumption of debris when burned.  Minimum spacing between piles shall be equivalent to one and one-half the diameter of the adjacent pile. Landing piles shall have a fire line constructed around them down to mineral soil at least one bulldozer blade width wide.

3. No hand piling shall be performed within Controlled Areas as shown in Exhibit A-1, Section J.

4. All burn piles shall be at least 50 feet horizontal distance from RHCA’s and shall be located so that burning will not damage standing trees, snags, or improvements.

5.  Slash accumulated at landings shall be piled.

6. All piles shall be covered with a durable waterproof covering of either water resistant paper or plastic (at least 3 mil. Thickness). The material shall be at least six feet in width. Piles shall not be less than 50 percent covered, with the covering extending not less than halfway down at least two sides. Piece of burnable material shall be placed on top of the durable waterproof covering to keep the covering from blowing off the pile.

C.2.3.1.7  Road Maintenance  The following specifications shall govern road maintenance made necessary by Contractor's road use and responsibilities for using, protecting and maintaining roads during contract operations, from seasonal weather damage and for safeguarding soil and water.  Roads shall be maintained is a satisfactory condition commensurate with the use requirements generated under this contract.  Performance by contractor of this road maintenance work may be required prior to, during, or after each period of use.

1. Blading - The Contractor shall maintain the existing road cross section by blading and shaping surface shoulders.  Surface material shall not be side-cast, but shall be returned onto the traveled way. Banks shall not be undercut.  Established berms shall be maintained.  Waterbars, dips, and overside drains shall be installed as directed by the Forest Service.

2. Surface Protection - While performing ordinary road maintenance work, Contractor shall avoid permanently fouling gravel or asphalt surfaces through covering them with earth or debris from side ditches, slides or other sources. Contractor shall avoid blading surface course off road, if present.

3. Slide Disposal - In removing material from slides or other sources, Contractor shall deposit the material which must be moved to locations chosen with the objective that such material will not erode into streams, lakes, or reservoirs. Material shall not be wasted over planted road fill.

4. Visibility - Contractor shall remove brush or tree growth or other obstructions to visibility as such obstructions develop during the permit period. All treated vegetation will be lopped and scattered within open areas adjacent to the road.

5. Drainage Maintenance - Contractor shall keep ditches, culverts, waterbars and other drainage facilities clear and functioning.  Overside drains will be installed and maintained to prevent damage to fill slope. Any erosion channels on fill slopes will be filled with rock or other material and revegetated.

6. Preventive Maintenance - Contractor shall perform preventive maintenance at end of Contractor's use each season to minimize weather damage during the non-use period.  Work will consist of blading to remove ruts or other surface irregularities, cleaning of ditches and culverts and any other work that would prevent excessive erosion or bank slough.  Damage resulting from Contractor's use or failure to perform required preventive maintenance shall be repaired by Contractor.

7. Dust Abatement - The following dust abatement requirements will apply to use of roads under this contract.

| Road | Material Type | Application Rate | Frequency of Application |
| --- | --- | --- | --- |
| All roads accessing project area | Water | N/A | As needed to abate dust. |

C.2.3.1.8  Cooperative Road Use

When two or more commercial users are simultaneously using the same road, they shall agree on a maintenance plan and arrangements for accomplishing the work.  This plan shall be approved by the Forest Service.

C.2.3.1.9  Erosion Control

1. To minimize potential of sediment transport from grading activities, the components of the drainage stabilization must be in place prior to grading.

2. All erosion control structures must be installed prior to November 15 of each year.  However in the event all structures have not been completed, temporary BMP's shall remain installed, and disturbed areas shall be stabilized.  (see Soil and Water Mitigations & Best Management Practices, Exhibit F, Section J)

3. All grading activities shall be halted and appropriate BMPs installed during periods of precipitation when it is determined by Contracting Officer Representative (C.O.R.) that grading would adversely affect the water quality of the area.

4.  Use of roads and landings shall be halted during wet periods (reference Exhibit C, Wet Haul Conditions). Contractor shall install temporary waterbars to maintain drainage on travel way if rutting results in unacceptable road damage (C.1.3.6).

5. After landings, log decking and sorting areas have served Contractor's purpose or prior to any seasonal period of precipitation, Contractor shall ditch or slope landings to permit water to drain or spread if determined necessary by Forest Service.  If landings are used for log decking, Contractor shall close all landings following completion of log hauling and fuels treatment.  Closure shall consist of subsoiling (see C.3.1 Soils).

6.  Sub-soiling of landings shall be accomplished by equipment that will lift and fracture the soil by vertical and lateral shattering, leaving the soil loosened through the full width and depth of the compacted layer with the top soil remaining substantially in place rather than being inverted.  Sub-soiling shall extend to a depth of 18 inches.  Agreement may be made to lesser depth if rocks or other limiting site conditions are encountered.  Sub-soiling shall be limited to periods when soil dryness will allow crumbled soil, avoiding the formation of large clods.  The Contractor and Forest Service shall agree on timing of completion of such work to coordinate with desirable soil moisture conditions.  (See Vegetative Soil Stabilization Specification and Subsoiling Specification, Exhibit D, Section J)

C.2.4  Product Identification Before removal from the Project Area; (a) all products ten(10) feet or more in length and one-third or more sound shall be hammer branded on each end that is six (6) inches or more in diameter: and (b) all domestic processing products ten (10) feet or more in length and one-third or more sound shall be painted with a spot of highway-yellow paint on each end that is  six (6) inches or more in diameter.   Each paint spot must be not less than three (3) square inches in size.

The Contracting Officer shall assign brands and, if the Project Area is within a State that maintains a log brand register, brands shall be registered with the State.  Contractor will furnish and apply highway-yellow paint of a lasting quality (oil-base or equivalent).

All hammer brands and/or highway-yellow paint must remain on logs until they are domestically processed.  If the identifying marks are lost, removed, or become unreadable, they shall be replaced.  Contractor may remanufacture products into different log lengths.  Except for logs remanufactured as part of the mill in-feed process immediately before processing, remanufactured products must be rebranded with the assigned sale brand and repainted with highway-yellow paint.  For such remanufactured products, Contracting Officer may approve use of a brand to be used exclusively as a catch brand, in lieu of the assigned sale brand.

C.2.5  Hauling.  Forest Service and Contractor shall agree upon the haul route(s) prior to use.  All products removed from project area shall be transported over the designated route of haul.

Contractor shall:

(a)  Require truck drivers to sign form R5-2400-242, Wood Receipt, that states the driver's responsibility when hauling Included Timber.

(b)  Assign a competent individual at the landing to record the following information for each load of logs on the Wood Receipt provided by Forest Service:

1.  Date and time load is physically punched out with a paper punch or equivalent.

2.  Truck ID or license number.

3.  Load destination.

Used books of Woods Receipts (stub portion) shall be returned to Forest Service at least weekly.

(c)  Require truck drivers to stop at agreed upon locations for accountability checks, if requested by the Forest Service, when products are in transit from Sale Area to contractor's processing facility(s).

(d)  Inform truck drivers of the designated route(s) of haul, the method of alerting drivers of an impending stop, and the fact that loads may be inspected at other locations where it is safe and possible to do so.

(e)  Insure that the Woods Receipt attached to each load of logs shall remain attached to its original log until manufactured into products, and then shall be either destroyed or otherwise rendered unusable.

C.3  RESOURCE PROTECTION STANDARDS

C.3.1  Soils  Refer to Exhibit F, Soil and Water Integrated Design Features and Best Management Practices.

Maintain soil productivity by providing adequate soil cover to prevent accelerated sheet and rill erosion from occurring.  The amount of material should not create an adverse effect to fuels and should be consistent with an Erosion Hazard rating of LOW.

Maintain soil productivity by leaving up to 5 existing down logs per acre throughout the project area.

Maintain soil productivity by ensuring soil porosity is not adversely affected by operating while soils are wet and by minimizing the extent of disturbance.  Forest Service shall review soil moisture prior to or during the contract as needed.

C.3.2  Water Quality  The following measures shall be observed to protect stream courses (RHCA’s):

1. Contractor's operations shall be conducted to prevent soil and vegetative debris from entering stream courses.  In event Contractor causes debris to enter stream courses in amounts which may adversely affect the natural flow of the stream, water quality or fishery resource, Contractor shall remove such debris as soon as practicable, but not to exceed 48 hours, and in an agreed manner that will cause the least disturbance to stream courses.

2. Wheeled or track-laying equipment shall not be operated within RHCA’s except at crossings designated by Forest Service.  If crossing a drainage is necessary, it shall be done at designated locations on existing roads with stream crossing structures in place.

Activities with the greatest potential impact are temporary road building, landing and skid trail construction, soil disturbance and vegetation removal.  Standard mitigation measures are listed in the project environmental analysis and include:

1. Establish Riparian Habitat Conservation Areas (RHCA’s), along all project streams and meadows in which equipment shall not operate.  Minimum width of RHCA's shall be 300 feet each side of permanently flowing streams, 100 feet horizontal distance on each side of seasonally flowing or intermittent streams; and 150 feet each side of wetlands greater than 1 acre.  Lake Almanor shall receive a 150-foot horizontal distance buffer from the high water mark.  RHCA buffer width will be determined in advance of operations and designated on the ground by the C.O.R, approximate locations of RHCA’s are displayed on the Contract map (Exhibit A, Section J).

C.3.3  Other Resource Protection  All of the activities associated with this project shall be conducted in such a manner that there shall not be any adverse impact as determined by Forest Service to the following resources listed.

1. All section corners, post markers, fences, bearing trees, RHCA’s, reserve trees, improvements, trails, non-treatment areas, recreational development sites, controlled areas and other improvements displayed on the Contract map (Exhibit A, Section J) shall not be disturbed in any way.

2. The location of known historic or prehistoric sites, buildings, objects, and properties related to American history, architecture, archaeology and culture, such as settler or Indian artifacts, protected by American Antiquities Act of 1906 (16 U.S.C. 431-433), National Historic Preservation Act of 1966 (16 U.S.C.470) and the Archaeological Resources Protection Act of 1979  (16 U.S.C. 470aa-ll) (36 CFR 296.4 and 36 CFR 261.9(e)), has been identified on-the-ground by the Forest Service prior to award of this contract.  The Government may unilaterally modify or cancel this contract  in whole or in part, to protect an area, object of antiquity, artifact, or similar object which is or may be entitled to protection under these Acts regardless of when the area, object or artifact is discovered or identified.  Discovery of such areas or objects by either party shall be promptly reported to the other party.

The Contractor shall protect all known and identified historic or prehistoric sites, buildings, objects, and properties related to American history, architecture, archaeology and culture against destruction, obliteration, removal or damage during the Contractor's operations.  Specific protection measures, if required, are listed in the Special Provisions below.  The Contractor shall bear costs of restoration in accordance with 36 CFR 296.14(c), provided that such payment shall not relieve the Contractor from civil or criminal remedies otherwise provided by law.

The Contractor shall not operate wheeled or track-laying equipment within such areas except on roads, landings, tractor roads or skid trails approved under Standard Provision 30.  Unless the Contracting Officer or designee agrees in writing otherwise, the Contractor will not fell trees into such areas.  The Contracting Officer or designee may require the Contractor to backblade skidtrails and other ground disturbed by the Contractor's Operations within such areas in lieu of cross ditching.

3.  Protection of Protected Species - The location of areas needing special measures for protection of plants or animals listed as threatened or endangered under the Endangered Species Act of 1973, 16 U.S.C. 1531, et seq., or a sensitive species identified by the Regional Forester have been  identified on-the-ground by the Forest Service prior to award of this contract and these locations are shown on the project area map.  If the Contracting Officer determines that protection measures are inadequate, if other such areas are discovered, or if new species are listed on the Endangered Species List, Contracting Officer may modify this contract under clause 52.243-01 Alternate 1 ( Page 38, Item I.12)to provide additional protection regardless of when such facts become known.  Discovery of such areas by either party shall be promptly reported to the other party.  This provision and any protections listed pursuant to this provision do not constitute a warranty of any kind, either express or implied, including, but not limited to, implied warranties of merchantability or fitness for a particular purpose.  Contractor is on notice that special protection measures not currently listed may be required at any time.

4.  Reserve Trees.  The contractor shall not cut live or dead  reserve trees or groups of reserve trees.  The Forest Service has identified reserve trees on-the-ground prior to award of this contract by the method indicated in the table below.  The Contactor shall protect reserve trees from damage or destruction by the Contactor 's operations.  Damage to reserve trees will cause serious and substantial silvicultural or other damage to the National Forest.  It will be difficult if not impossible to determine the amount of such damage.  Therefore, in the event that the Contracting Officer or designee determines that the Contactor's operations have unnecessarily cut or unnecessarily damaged reserve trees through Contactor's carelessness, the Contactor shall pay the amount indicated in the table below as fixed, agreed and liquidated damages for each reserve tree cut or damaged.

Damage includes any injury to the living crown, bole, or roots of reserve trees.  If areas are marked on the ground around such reserve trees, operation of heavy equipment or skidding of products within said area shall be considered to be damaging to the tree.

Units with reserve trees are shown on the Contract map.

| Description of Reserve Trees | Method Reserve Tree Has Been Identified On-The-Ground | Liquidated Damage Amount $ |
| --- | --- | --- |
| Rust Resistant Sugar Pine Trees and Candidate Trees | Orange Painted “RRSP” and “RT” | $ 5,000 |

5.  Protection of Improvements not owned by Forest Service.  When the Contactor 's operations are adjacent to

properties of railway, telegraph, telephone, power companies or other property, the Contactor's operations shall not begin until the Contactor makes all necessary arrangements to prevent damage.

The Contactor shall cooperate with the owners of any underground or overhead utility lines in their removal and/or rearrangement operations in order that these operations may progress in a reasonable manner; utility duplication or rearrangement work may be reduced to a minimum; and services shall not be unnecessarily interrupted.

If the Contactor's operations interrupt utility services because of the Contactor's accidental breakage or as a result of lines being exposed or unsupported, the Contactor shall promptly notify the proper authority and shall cooperate with that authority in the restoration of service.  If utility services are interrupted, cooperation shall be required until the service is restored.

When materials are to be hauled across the tracks of any railway, the Contracting Officer or designee will make arrangements with the railroad for the use of any existing crossing or for any new crossing required.  The Contactor shall make arrangements for use of alternate crossings.  The Contactor shall be liable to the railroad for damages to the railroad's property caused by the Contactor's operations.

C.3.4  Safety  When Contractor's operations are in progress adjacent to or on Forest Service controlled roads and trails open to public travel, Contractor shall furnish, install and maintain all temporary traffic controls which provide the user with adequate warning of hazardous or potentially hazardous conditions associated with Contractor's  operations.  This may require the use of flag persons in addition to signing or other methods of warning.  A specific traffic control plan for each individual project shall be prepared by the Contractor and approved by the Forest Service prior to commencing operations.  Devices shall be appropriate to current conditions and shall be covered or removed when not needed.  Flagmen and devices shall be as specified in the "Manual on Uniform Traffic Control Devices for Streets and Highways" (MUTCD).

C.3.5  Cleaning of Equipment  Contractor shall insure that all off-road equipment moved on to National Forest Land in this timber sale that last operated in areas known by Forest Service to be infected with noxious weeds is free of soil, seeds, vegetative matter or other debris that could contain or hold seeds.  For purposes of this provision, equipment shall be considered free of soil, seeds, and other such debris when a visual inspection does not disclose such material. Disassembly of equipment components or specialized inspection tools will not be required.   A current list of noxious weeds of concern to Forest Service is available at the District Ranger's Office for this sale.

Equipment will also be cleaned prior to moving between cutting units on this sale known to be infested with noxious weeds, and other units, if any, which are free of such weeds.  Sale Area Map shows such areas known by Forest Service prior to advertisement.

Contractor shall employ whatever cleaning methods are necessary to ensure compliance with the terms of this provision, and shall notify Forest Service at least 10 working days prior to moving each piece of equipment on to National Forest Land, unless otherwise agreed.  Notification will include identifying the location of the equipment's most recent operations.  If the prior location of the equipment cannot be identified, Forest Service may assume that it was infested with noxious weed seeds.   Upon request of Forest Service, arrangements will be made for Forest Service to inspect each piece of equipment prior to it being placed in service.

Contractor shall certify in writing compliance with the terms of this provision prior to each start-up of sale operations.  Measures taken to ensure compliance for equipment present at start-up, and planned for equipment to be moved in later, will be identified.  For the purposes of this provision, "off-road equipment" includes all logging machinery except for log trucks, chip vans, pickup trucks, and cars or other highway vehicles used for daily transport of personnel.

If Contractor desires to clean equipment on National Forest Land, such as at the end of a project prior to moving to a new project, Purchaser and Forest Service shall agree on methods of cleaning, locations for the cleaning, and control of off-site impacts, if any.

New infestations of noxious weeds of concern to Forest Service, identified by either Contractor or Forest Service, on National Forest land in the Sale Area or on the haul route shall be promptly reported to the other party.   Both parties shall agree on treatment methods to reduce or stop the spread of noxious weeds when new infestations are found.

C.3.6  Use of Roads by Contractor  The Contractor's use of existing roads identified on Contract map by the following codes is prohibited or subject to restrictive limitations, unless the Contracting Officer or designee agrees in writing otherwise:

| Code | Use Limitations |
| --- | --- |
| X | Hauling prohibited |
| R | Hauling restricted |
| P | Use prohibited |
| A | Public use restriction |
| W | Regulation waiver |

### Restricted Road List

| Road |  | Termini | Map | Description of |
| --- | --- | --- | --- | --- |
| Number | Road Name | From | To | Legend | Restrictions |
| 27N44 | N/A | 27N03 | 27N71 | P | Use of road prohibited for any harvesting operations |
| 27N35A | N/A | 27N03 | .25 | P | Use of road prohibited for any harvesting operations |

C.3.7  View Areas.  Shown on the Contract map are Travel and Water Influence Zones and Special Management Units which include roads, recreation trails, streamsides, lakeshores and other view areas with distance limitations for visible slash treatments.  Within such zones, the Contractor shall treat visible logging slash.  Primary treatment shall be by hand piling.  Logging slash not readily treated by hand piling shall be removed to designated areas or treated as agreed by the Contracting Officer.

C.4  REFERENCE DOCUMENTS

C.4.1. Herger-Feinstein Quincy Library Group Forest Recovery Act Final Environmental Impact Statement, August 1999 (HFQLG FEIS).

C.4.2.  Forest Service Handbook for Best Management Practices (BMP), Chapter 30, FSM.

C.4.3.  Prattville Forest Recovery Project Environmental Assessment, June 2000.

C.4.4.  The above referenced documents are available at the Almanor Ranger District Office.

SECTION E - INSPECTION AND ACCEPTANCE

E.1   INSPECTION OF SERVICES--FIXED-PRICE (FAR 52.246-4)(AUG 1996)

(a) Definition: "Services," as used in this clause, includes services performed, workmanship, and material furnished or utilized in the performance of services.

(b) The Contractor shall provide and maintain an inspection system acceptable to the Government covering the services under this contract. Complete records of all inspection work performed by the Contractor shall be maintained and made available to the Government during contract performance and for as long afterwards as the contract requires. [See Clause E.2, Progress Reporting]

(c) The Government has the right to inspect and test all services called for by the contract, to the extent practicable at all times and places during the term of the contract. The Government shall perform inspections and tests in a manner that will not unduly delay the work.

(d) If the Government performs inspections or tests on the premises of the Contractor or a subcontractor, the Contractor shall furnish, and shall require subcontractors to furnish, at no increase in contract price, all reasonable facilities and assistance for the safe and convenient performance of these duties.

(e) If any of the services do not conform with contract requirements, the Government may require the Contractor to perform the services again in conformity with contract requirements, at no increase in contract amount. When the defects in services cannot be corrected by reperformance, the Government may--

(1) Require the Contractor to take necessary action to ensure that future performance conforms to contract requirements; and

(2) Reduce the contract price to reflect the reduced value of the services performed.

(f) If the Contractor fails to promptly perform the services again or to take the necessary action to ensure future performance in conformity with contract requirements, the Government may--

(1) By contract or otherwise, perform the services and charge to the Contractor any cost incurred by the Government that is directly related to the performance of such service; or

(2) Terminate the contract for default.

E.2   PROGRESS REPORTING

For each day of operation, the Contractor shall complete and mail or fax, on a daily basis, copies of Contract Daily Diary form to the Contracting Officer Representative. Content of Contract Daily Diary form shall include, but not be limited to, current working location, progress of work, quantity of work accomplished, and quality of work accomplished (work inspection results).

E.3   INSPECTION AND ACCEPTANCE (AGAR 452.246-70)(FEB 1988)

(a) The Contracting Officer or the Contracting Officer's duly authorized representative will inspect and accept the supplies and/or services to be provided under this contract.

(b) Inspection and acceptance will be performed at the project site.

SECTION F - DELIVERIES OR PERFORMANCE

F.1   PERIOD OF PERFORMANCE (AGAR 452-211-74)(FEB 1988)

The performance period for this project is September 29, 2000, through November 30, 2002.

Service contract work shall be performed in accordance with the order of preference approved by the Contracting Officer Representative.  The Contractor shall maintain progress at a rate, which will assure quality and completion within the service contract time specified above.

F.2   WINTER SHUTDOWN

When winter weather sets in and the continuation of work is impractical, upon written request by the Contractor, the Contracting Officer may authorize a total suspension until such winter weather has passed and work can proceed.

F.3   TIMBER SALE CONTRACT TERM EXTENSION

The  Timber Sale Contract will only be extended if an extension of time is authorized under the terms and conditions of the Federal Acquisition Regulations for Service Contracts.  If such an extension of time is granted and such award of time is not due to any Government Delay or Stop Work order, the Contractor shall pay the Government for increased cost determined for:  (a) increased costs of regeneration, including nursery stock loss, carryover or replacement costs, and (b) cost of remarking timber on the Project Area or reestablishing project or block boundaries.

F.4  QUANTITY DETERMINATION

The Forest Service has determined the estimated quantities of Included Timber listed on Page 1 of Exhibit B, Timber Sale Contract (2400-3) prior to award of this contract.  The Contracting Officer or designee will determine any additional designated timber prior to felling during the term of the contract.  The estimated quantities are determined in accordance with the volume equations or tables approved for use in the area by the Forest Service with adjustment for defect as appropriate.  Copies of the volume equations and/or tables are on file in the office of the Contracting Officer.  The Forest Service makes no representation, warranty, or guarantee of the accuracy of the estimate..

F.5  VARIATION IN ESTIMATED QUANTITY (FAR 52.211-18)(APR 1984)

If the quantity of a unit-priced item in this contract is an estimated quantity and the actual quantity of the unit-priced item varies more than 15 percent above or below the estimated quantity, an equitable adjustment in the contract price shall be made upon demand of either party. The equitable adjustment shall be based upon any increase or decrease in costs due solely to the variation above 115 percent or below 85 percent of the estimated quantity. If the quantity variation is such as to cause an increase in the time necessary for completion, the Contractor may request, in writing, an extension of time, to be received by the Contracting Officer within 10 days from the beginning of the delay, or within such further period as may be granted by the Contracting Officer before the date of final settlement of the contract. Upon the receipt of a written request for an extension, the Contracting Officer shall ascertain the facts and make an adjustment for extending the completion date as, in the judgment of the Contracting Officer, is justified.

F.6   STOP-WORK ORDER (FAR 52.242-15)(AUG 1989)

(a) The Contracting Officer may, at any time, by written order to the Contractor, require the Contractor to stop all, or any part, of the work called for by this contract for a period of 90 days after the order is delivered to the Contractor, and for any further period to which the parties may agree. The order shall be specifically identified as a stop-work order issued under this clause. Upon receipt of the order, the Contractor shall immediately comply with its terms and take all reasonable steps to minimize the incurrence of costs allocable to the work covered by the order during the period of work stoppage. Within a period of 90 days after a stop-work is delivered to the Contractor, or within any extension of that period to which the parties shall have agreed, the Contracting Officer shall either--

(1) Cancel the stop-work order; or

(2) Terminate the work covered by the order as provided in the Default, or the Termination for Convenience of the Government, clause of this contract.

(b) If a stop-work order issued under this clause is canceled or the period of the order or any extension thereof expires, the Contractor shall resume work. The Contracting Officer shall make an equitable adjustment in the delivery schedule or contract price, or both, and the contract shall be modified, in writing, accordingly, if--

(1) The stop-work order results in an increase in the time required for, or in the Contractor's cost properly allocable to, the performance of any part of this contract; and

(2) The Contractor asserts its right to the adjustment within 30 days after the end of the period of work stoppage; provided, that, if the Contracting Officer decides the facts justify the action, the Contracting Officer may receive and act upon the claim submitted at any time before final payment under this contract.

(c) If a stop-work order is not canceled and the work covered by the order is terminated for the convenience of the Government, the Contracting Officer shall allow reasonable costs resulting from the stop-work order in arriving at the termination settlement.

(d) If a stop-work order is not canceled and the work covered by the order is terminated for default , the Contracting Officer shall allow, by equitable adjustment or otherwise , reasonable costs resulting from the stop-work order.

F.7   GOVERMENT  DELAY OF WORK  (FAR 52.242-17)(APR 1984)

(a) If the performance of all or any part of the work of this contract is delayed or interrupted (1) by an act of the Contracting Officer in the administration of this contract that is not expressly or impliedly authorized by this contract, or (2) by failure of the Contracting Officer to act within the time specified in this contract, or within a reasonable time if not specified, an adjustment (excluding profit) shall be made for any increase in the cost of performance of this contract caused by the delay or interruption and the contract shall be modified in writing accordingly. Adjustment shall also be made in the delivery or performance dates and any other contractual term or condition affected by the delay or interruption. However, no adjustment shall be made under this clause for any delay or interruption to the extent that performance would have been delayed or interrupted by any other cause, including the fault or negligence of the Contractor, or for which an adjustment is provided or excluded under any other term or condition of this contract.

(b)A claim under this contract shall not be allowed-

(1)For any costs incurred more than 20 days before the Contractor shall have notified the Contracting Officer ii writing of the act or failure to act involved; and

(2) Unless the claim in an amount stated, is asserted in writing as soon as practicable after the termination of the delay or interruption, but not later than the day of final payment under the contract.

F.8  SUSPENSION OF WORK (FAR 52.242-14)(APR 1984)

(a) The Contracting Officer may order the Contractor, in writing, to suspend, delay, or interrupt all or any part of the work of this contract for the period of time that the Contracting Officer determines appropriate for the convenience of the Government.

(b) If the performance of all or any part of the work is, for an unreasonable period of time, suspended, delayed, or interrupted (1) by an act of the Contracting Officer in the administration of this contract, or  (2) by the Contracting Officer's failure to act within the time specified in this contract (or within a reasonable time if not specified), an adjustment shall be made for any increase in the cost of performance of this contract (excluding profit) necessarily caused by the unreasonable suspension, delay, or interruption, and the contract modified in writing accordingly. However, no adjustment shall be made under this clause for any suspension, delay, or interruption to the extent that performance would have been so suspended,

delayed, or interrupted by any other cause, including the fault or negligence of the Contractor, or for which an equitable adjustment is provided for or excluded under any other term or condition of this contract.

(c) A claim under this clause shall not be allowed--

(1) For any costs incurred more than 20 days before the Contractor shall have notified the Contracting Officer in writing of the act or failure to act involved (but this requirement shall not apply as to a claim resulting from a suspension order); and

(2) Unless the claim, in an amount stated, is asserted in writing as soon as practicable after the termination of the suspension, delay, or interruption, but not later than the date of final payment under the contract.

SECTION G - CONTRACT ADMINISTRATION DATA

G.1  DESIGNATION OF CONTRACTING OFFICER'S REPRESENTATIVE

A Contracting Officer's Representative (COR) will be designated after contract award by the Contracting Officer.

The contractor will be notified by letter of the name and duties of the COR.

G.2  INVOICES

Contractor shall prepare and submit invoices for payment to the Contracting Officer’s Representative.

Each invoice is required to include the following information to be considered a proper invoice.  Failure to include all of the required information, may result in a delay of payment.

- Name of vendor;

- Invoice date;

- Contract number;

- Vendor’s invoice number;

- Description of goods or services provided, including; contract item; price; and quantity;

- Payment terms ( i.e., discounts for prompt payment);

- Vendor’s VXP number for Electronic Funds Deposit (EFT); and

- Contact name, title, and telephone number.

G.3   MEASUREMENT

G.3.1. Methods of Measurement.

Acreage was measured on a horizontal plane using a Global Positioning System.

G.3.2  Remeasurement

Unless otherwise indicated by this contract, the contractor may request remeasurement of any quantities in Part B, when the units are acres or any linear measurement. The request must be made in writing and must be made within 10 calendar days of completing work on the unit in question. If remeasurement indicates a variance of five percent or less from the stated quantity, the Contractor shall pay for the actual cost of remeasurement and no adjustment will be made in the quantity as stated in Part B. If remeasurement indicates a variance more than five percent from the stated quantity, payment will be based on the remeasured quantity, and the Contractor will not be liable for the costs of remeasurement. All remeasurements will be done by the Government. Remeasurement of acreage will be done with two people using a hand compass and ground measurement or by means of a Global Positioning System.  This clause is not applicable to quantities listed as estimated quantities.

G.4  PAYMENT

G.4.1.  Payments and deductions

Payment will be made for fully acceptable work at the prices in the schedule of items.  In the event of extended non-work periods because of adverse weather, the Contracting Officer may authorize progress payments for partially completed sub-items on a case-by-case basis.  In accordance with the appropriate inspection clause, payment may be made for less than fully acceptable work at a reduced price.

G.5   ADDITIONAL TIMBER PAY RATE.

ADDITIONAL PAYMENT FOR GREEN TREES CUT SUBJECT TO AGREEMENT

10.0 inch dbh and greater - Volume will be determined from the R5 Cubic Foot Volume Tables (9/97) and the rate of $49.75/ccf for PP or JP, $47.36/ccf for SP, $73.85/ccf for WF or RF, $55.21/ccf for DF, $59.21/ccf for IC and $14.71/ccf for  LP.

G.6   CUTTING UNDESIGNATED TREES

The Contractor shall pay for cut or damaged merchantable timber meeting Utilization Standards as follows:  (a) double the Payment Rate in Clause G.5, Additional Timber Pay Rate, for undesignated trees unnecessarily cut or unnecessarily damaged.  In view of the difficulty in determining the actual damage to the United States, the amounts specified above shall be considered liquidated damages; provided, that, if such damage involves small amounts of material, and in the judgment of the Contracting Officer or designee, is justified by existing conditions, the payments may not be required.

The Contracting Officer or designee shall determine rates per unit of measure for standing timber or other forest products if they are not Included Timber using the standard Forest Service appraisal methods and appraisal data in use at time of the damage calculation. In addition to liquidated damages, if designated for removal by the Contracting Officer or designee, the Contractor shall make payments at the rate determined above. The right, title, and interest to any product for which payment of liquidated damages has been made or which has been regularly paid for, cut, but not removed, shall remain in or revert to the United States if not removed from the project area at the expiration or termination of this contract.

### SECTION H - SPECIAL CONTRACT REQUIREMENTS

H.1  DIFFERING SITE CONDITIONS (FAR 52.236-2)(APR 1984)

- The Contractor shall promptly, and before the conditions are disturbed, give a written notice to the Contracting

Officer of--

(1) Subsurface or latent physical conditions at the site which differ materially from those indicated in this contract; or

(2) Unknown physical conditions at the site, of an unusual nature, which differ materially from those ordinarily encountered and generally recognized as inhering in work of the character provided for in the contract.

(b) The Contracting Officer shall investigate the site conditions promptly after receiving the notice. If the conditions do materially so differ and cause an increase or decrease in the Contractor's cost of, or the time required for, performing any part of the work under this contract, whether or not changed as a result of the conditions, an equitable adjustment shall

be made under this clause and the contract modified in writing accordingly.

(c) No request by the Contractor for an equitable adjustment to the contract under this clause shall be allowed, unless the Contractor has given the written notice required; provided, that the time prescribed in paragraph (a) of this clause for giving written notice may be extended by the Contracting Officer.

(d) No request by the Contractor for an equitable adjustment to the contract for differing site conditions shall be allowed if made after final payment under this contract.

H.2  SITE INVESTIGATION AND CONDITIONS AFFECTING THE WORK (FAR 52.236-3)(APR 1984)

(a) The Contractor acknowledges that it has taken steps reasonably necessary to ascertain the nature and location of the work, and that it has investigated and satisfied itself as to the general and local conditions which can affect the work or its cost, including but not limited to (1) conditions bearing upon transportation, disposal, handling, and storage of materials; (2) the availability of labor, water, electric power, and roads; (3) uncertainties of weather, river stages, tides, or similar physical

conditions at the site; (4) the conformation and conditions of the ground; and (5) the character of equipment and facilities needed preliminary to and during work performance. The Contractor also acknowledges that it has satisfied itself as to the character, quality, and quantity of surface and subsurface materials or obstacles to be encountered insofar as this information is reasonably ascertainable from an inspection of the site, including all exploratory work done by the Government, as well as from the drawings and specifications made a part of this contract. Any failure of the Contractor to take the actions described and acknowledged in this paragraph will not relieve the Contractor from responsibility for estimating properly the difficulty and cost of successfully performing the work, or for proceeding to successfully perform the work without additional expense to the Government.

(b) The Government assumes no responsibility for any conclusions or interpretations made by the Contractor based on the information made available by the Government. Nor does the Government assume responsibility for any understanding reached or representation made concerning conditions, which can affect the work by any of its officers or agents before the execution of this contract, unless that understanding or representation is expressly stated in this contract.

H.3  SUPERINTENDENCE BY THE CONTRACTOR (FAR 52.236-6)(APR 1984)

At all times during performance of this contract and until the work is completed and accepted, the Contractor shall directly superintend the work or assign and have on the worksite a competent superintendent who is satisfactory to the Contracting Officer and has authority to act for the Contractor.

H.4  PERMITS AND RESPONSIBILITIES (FAR 52.236-7)(NOV 1991)

The Contractor shall, without additional expense to the Government, be responsible for obtaining any necessary licenses and permits, and for complying with any Federal, State, and municipal laws, codes, and regulations applicable to the performance of the work. The Contractor shall also be responsible for all damages to persons or property that occur as a result of the Contractor's fault or negligence. The Contractor shall also be responsible for all materials delivered and work performed until completion and acceptance of the entire work, except for any completed unit of work, which may have been accepted under the contract.

H.5   PROTECTION OF EXISTING VEGETATION, STRUCTURES, EQUIPMENT, UTILITIES, AND

IMPROVEMENTS (FAR 52.236-9)(APR 1984)

(a) The Contractor shall preserve and protect all structures, equipment, and vegetation (such as trees, shrubs, and grass) on or adjacent to the work site, which are not to be removed and which do not unreasonably interfere with the work required under this contract. The Contractor shall only remove trees when specifically authorized to do so, and shall avoid damaging

vegetation that will remain in place. If any limbs or branches of trees are broken during contract performance, or by the careless operation of equipment, or by workmen, the Contractor shall trim those limbs or branches with a clean cut and paint the cut with a tree-pruning compound as directed by the Contracting Officer.

(b) The Contractor shall protect from damage all existing improvements and utilities (1) at or near the work site, and (2) on adjacent property of a third party, the locations of which are made known to or should be known by the Contractor. The Contractor shall repair any damage to those facilities, failure to comply with the requirements of this contract or failure to exercise reasonable care in performing the work. If the Contractor fails or refuses to repair the damage promptly, the Contracting Officer may have the necessary work performed and charge the cost to the Contractor.

H.6  INQUIRIES (AGAR 452.204-70)(FEB 1988)

Inquiries and all correspondence concerning this solicitation should be submitted in writing to the Contracting Officer.  Offerors should contact only the Contracting Officer issuing the solicitation about any aspect of this requirement prior to contract award.

H.7  POST AWARD CONFERENCE (AGAR 452.215-73)(NOV 1996)

A post award conference with the successful offeror is required. It will be scheduled within 15 days after the date of contract award. The conference will be held at a place and time determined by the Contracting Officer.

H.8  USE OF PREMISES (AGAR 452.236-72)(NOV 1996)

(a) Before any camp, quarry, borrow pit, storage, detour, or bypass site, other than shown on the drawings, is opened or operated on USDA lands or lands administered by the USDA, the Contractor shall obtain written permission through the Contracting Officer.  A camp is interpreted to include a campsite or trailer parking area of any employee working on the project for the Contractor.

(b) Unless excepted elsewhere in the contract, the Contractor shall:

(i) provide and maintain sanitation facilities for the workforce at the site, and

(ii) dispose of solid waste in accordance with applicable Federal, State, and local	 regulations.

H.9  ARCHEOLOGICAL OR HISTORIC SITES (AGAR 452.236-73)(FEB 1988)

If a previously unidentified archeological or historic site(s) is encountered, the Contractor shall discontinue work in the general area of the site(s) and notify the Contracting Officer immediately.

H.10  CONTROL OF EROSION, SEDIMENTATION AND POLLUTION  (AGAR 452.236-74)(NOV 1996)

(a) Operations shall be scheduled and conducted to minimize erosion of soils and to prevent silting and muddying of streams, rivers, irrigation systems, and impoundments (lakes, reservoirs, etc.).

(b) Pollutants such as fuels, lubricants, bitumen’s, raw sewage, and other harmful materials shall not be discharged on the ground; into or near rivers, streams, and impoundments; or into natural or man-made channels.  Wash water or waste from concrete or aggregate operations shall not be allowed to enter live streams prior to treatment by filtration, settling, or other means sufficient to reduce the sediment content to not more than that of the stream into which it is discharged.

(c) Mechanized equipment shall not be operated in flowing streams without written approval by the Contracting Officer.

H.11  EMERGENCY RESPONSE (AGAR 452.236-77)(NOV 1996)

(a) Contractor's Responsibility for Fire Fighting. (1)The Contractor, under the provisions of FAR clause 52.236-9, PROTECTION OF EXISTING VEGETATION, STRUCTURES, EQUIPMENT, UTILITIES, AND IMPROVEMENTS, shall immediately extinguish all fires on the work site other than those fires in use as a part of the work.  (2) The Contractor may be held liable for all damages and for all costs incurred by the Government for labor, subsistence, equipment, supplies, and transportation deemed necessary to control or suppress a fire set or caused by the Contractor or the Contractor's agents or employees.

(b) Contractor's Responsibility for Notification in Case of Fire. The Contractor shall immediately notify the Government of any fires sighted on or in the vicinity of the work site.

(c) Contractor's Responsibility for Responding to Emergencies. When directed by the Contracting Officer, the Contractor shall allow the Government to temporarily use employees and equipment from the work site for emergency work (anticipated to be restricted to fire fighting).  An equitable adjustment for the temporary use of employees and equipment will be made under the CHANGES clause FAR 52.243-01A1.

H.12  KEY PERSONNEL (AGAR 452-237-74)(FEB 1988)

(a) The Contractor shall assign to this contract the following key personnel: As provided in the technical proposal.

(b) During the first ninety (90) days of performance, the Contractor shall make no substitutions of key personnel unless the substitution is necessitated by illness, death, or termination of employment. The Contractor shall notify the Contracting Officer within 15 calendar days after the occurrence of any of these events and provide the information required by paragraph (c) below. After the initial 90-day period, the Contractor shall submit theinformation required by paragraph (c) to the Contracting Officer at least 15 days prior to making any permanent substitutions.

(c) The Contractor shall provide a detailed explanation of the circumstances necessitating the proposed substitutions, complete resumes for the proposed substitutes, and any additional information requested by the Contracting Officer. Proposed substitutes should have comparable qualifications to those of the persons being replaced. The Contracting Officer will notify the Contractor within 15 calendar days after receipt of all required information of the decision on substitutions. The contract will be modified to reflect any approved changes of key personnel.

H.13  RESTRICTIONS AGAINST DISCLOSURE (AGAR 452.237-75)(FEB 1988)

(a) The Contractor agrees, in the performance of this contract, to keep all information contained in source documents or other media furnished by the Government in the strictest confidence. The Contractor also agrees not to publish or otherwise divulge such information in whole or in part in any manner or form, or to authorize or permit others to do so, taking such reasonable measures as are necessary to restrict access to such information while in the Contractor's possession, to those employees needing such information to perform the work provided herein, i.e., on a "need to know" basis. The Contractor agrees to immediately notify in writing, the Contracting Officer, named herein, in the event that the Contractor

determines or has reason to suspect a breach of this requirement.

(b) The Contractor agrees not to disclose any information concerning the work under this contract to any persons or individual unless prior written approval is obtained from the Contracting Officer. The Contractor agrees to insert the substance of this clause in any consultant agreement or subcontract hereunder.

H.14  PROPERTY AND PERSONAL DAMAGE

- The Contractor shall use every precaution necessary to prevent damage to public and private property.

- The Contractor shall be responsible for all damage to private property and to persons, including third parties, that occur as a result of a fire, which is due to his or his agent’s or employee’s fault or negligence.  The term “third parties” is construed to include employees of the Government.

- The Contractor shall be responsible for the total costs for fire suppression that occur as a result of his or his agent’s or employee’s fault or negligence.

- The Contractor shall procure and maintain during the term of this contract, and any extension thereof, commercial general liability insurance providing minimum coverage of $1,000,000 and insurance covering damages from an operational fire, such as a ‘loggers broad form’, providing minimum coverage of $1,000,000.  General liability insurance shall contain a minimum coverage for personal bodily injury of $500,000 per occurrence.  The parties named insured under the policy or policies shall be the Contractor and the United States of America.

- The Contractor may be otherwise insured by a combination of primary and excess policies.  Such policies shall have a combined coverage equal to, or greater than, the minimums required.

- The Contractor, prior to the commencement of work, shall submit to the Contracting Officer one copy of the insurance policy, or confirmation from the insurance company, certifying that the coverage described in this clause has been obtained.

- Each policy or certificate evidencing the insurance shall contain an endorsement that provides that the insurance company will notify the Contracting Officer 30 days prior to the effective date of any cancellation or termination of any policy or certificate or any modification of a policy or certificate that adversely affects the interest of the Government in such insurance. The notice shall be sent by registered mail and shall identify this contract, the name and address of the Contracting Office, the policy, and the insured.

H.15  NOTIFICATION OF ABSENCE

The Contractor shall notify the COR when intending to leave the project area for 3 or more consecutive calendar days and also when planning to return to the project area.  Failure to give notice as required herein may be considered as abandonment and could place the Contractor in danger of default termination.

H.16  SUBCONTRACTING

The Contractor shall request permission, in advance and in writing, to subcontract any portion of the contract and shall furnish sufficient evidence that the subcontractor is experienced and equipped for such work.  The written request shall be specific in indicating which separable, identifiable, and measurable portion of the project is to be subcontracted.  Written consent to subcontract any portion of the contract shall not be construed to relieve the Contractor of any responsibility under the contract.  Neither shall such written consent be construed as approval of a subcontract but rather as approval to subcontract a specific portion of the project to a specific entity.  All subcontracts must incorporate the specifications, terms, and conditions of the prime contract and otherwise be in compliance with applicable laws and regulations.

H.17  CAMPING

Camping is not permitted in U.S. Forest Service campgrounds.  The Contractor (   ) will (   ) will not be permitted to camp elsewhere on U.S. Forest Service land.  Camping on Forest Service land is not a right; permission may be revoked for failure to comply with camping permit issued by the District Ranger.

H.18  EROSION CONTROL

When determined by Forest Service, Contractor shall (1) avoid operating equipment when soil conditions are such that excessive damage will result; (2) construct erosion control structures as needed to control erosion; (3) repair promptly any existing erosion control structures damaged by Contractor's operations; (4) complete seasonal erosion control work prior to suspending operations; and (5) perform other soil erosion control work as may be required under this contract.

Prior to suspension of operations or seasonal periods of precipitation or runoff; Contractor shall smooth landings, remove ruts from roads and construct cross ditches, water bars, water-spreading ditches on landings and roads where staked or otherwise marked on the ground by Forest Service.  If Contractor chooses to overwinter landings, Contractor shall mulch and line landings with temporary sediment barriers.

If Contractor fails to do seasonal erosion work prior to any seasonal period of precipitation or runoff, Forest Service may temporarily assume responsibility for the work and any unencumbered deposits hereunder may be used by Forest Service to do the work.  If needed for such work, Contractor shall make additional deposits on request by Forest Service.  Any money deposited or used for this purpose shall be on the basis of cooperation or assistance (16 U.S.C. 572).

H.19  PROTECTION, USE, AND MAINTENANCE OF IMPROVEMENTS

Contractor, in all phases of construction and logging operations, shall protect insofar as practicable all land survey corners, telephone lines, ditches, fences, and other improvements.  If such improvements are damaged by Contractor's operations under this contract, Contractor shall restore them immediately to condition existing immediately prior to logging.  When necessary, Forest Service may require Contractor to move any such telephone lines or fences from one location to another.  All roads and trails, designated by Forest Service as needed for fire protection or other purposes, shall at all times be kept free of logs, brush, and debris resulting from Contractor's operations.  Contractor shall perform or pay for road maintenance commensurate with his use.  Roads or trails damaged through such use shall promptly be restored by Contractor. Contractor's use of existing roads may be restricted as indicated on sale area map.

H.20  LANDSCAPE PRESERVATION

(a) The Contractor shall confine operations to within the clearing limits or other areas designated in contract documents, and prevent the depositing of rocks, excavated materials, stumps, or other debris outside of these limits.  Material which falls outside of these limits shall be retrieved, disposed of, or incorporated in the work as directed by the Contracting Officer.

(b) Operation shall be scheduled and conducted to minimize erosion of soils and to prevent silting and muddying of streams, rivers irrigation systems, lakes, reservoirs, and other surface waters.

Wash water or waste from concrete or aggregate operations shall not be allowed to enter live streams prior to treatment by filtration, settling, or other means sufficient to reduce the sediment content to not more than that of the stream into which it is discharged.  Mechanized equipment shall not be operated in live streams without written approval by the Contracting Officer.

(c) Pollutants such as fuels, lubricants, bitumen’s, raw sewage, and other harmful materials shall not be discharged into or near rivers, streams, and impoundments, or into or near rivers, streams, and impoundments, or into natural or man made channels leading thereto.

Fuel Storage

According to EPA requirements (40 CFR 112), if the total oil or oil products storage exceeds

1,320 gallons or if any single container exceeds a capacity of 660 gallons, the Contractor shall

prepare and implement a Spill Prevention and Countermeasures (SPCC )  Plan.  Such plan shall

be certified by a registered professional engineer.

Oils and Other Hazardous Substances Spills

Executive Order 11752 - Prevention, Control, and Abatement of Environmental Pollution a

Federal Facilities, 40 CFR 300 - National Oil and Hazardous Substances Contingency Plan, 40

CFR 110  - Discharge of Oil, 40 CFR 112 - Oil Prevention Pollution, and the Clean Water Act

of 1977 (P. l. 95 -217), Fixes liability for clean-up and abatement of spills of oil and hazardous

substances on the Contractor.

The Contractor under the direction of the Contracting Officer, or in the absence of said officer, acting independently, shall immediately take action to contain and clean up, without expense to the Government, all petroleum products spills on/or in the vicinity of the project which are caused by the Contractor's employees directly or indirectly as a result of construction operations.   The Contractor will be liable for all damages and costs of additional labor, subsistence, equipment, supplies, and transportation deemed necessary by the Government for the containment and clean up of petroleum products spills.

The Contractor shall immediately report all petroleum products spills to the Contracting Officer.

H.21  LANGUAGE REQUIREMENT

The Contractor's on-site Representative MUST be fully conversant in the English Language.  See Section H, Clause 52.236-06 - Superintendence by the Contractor.

# H.22  ALIEN LABOR

This contract involves the employment of unskilled labor working under arduous field conditions.  Such employment may be attractive to persons coming from foreign countries, sometimes illegally.  Offerors are reminded that it is a crime to (1) bring into the United States, (2) transport within the United States, or (3) harbor within the United States, aliens who do not have a proper visa for entry and work in this country (8 U.S.C. 1323-1325).  If violations are suspected during the performance of work under this contract, they will be reported to the U.S. Immigration and Naturalization Service (INS) for investigation and appropriate action.  Conviction under these statutes will be considered in determining responsibility of a Contractor in future awards.

If an employer suspect’s fraud, they should contact the nearest Office of Immigration and Naturalization.

H.23  LABOR STANDARDS FOR CONTRACTS INVOLVING MIGRANT AND SEASONAL AGRICULTURAL

WORKERS

Scope - The Migrant and Seasonal Agricultural Workers Protection Act (MSPA) was passed to eliminate activities that are detrimental to migrant and seasonal agricultural workers, to require registration of farm labor contractors, and to assure necessary protections for the workers.  In addition, to traditional farm labor activities, the Act applies to predominately manual forestry work including, but not limited to, tree planting, release, precommercial thinning, and site preparation.

Definitions - The following are summaries of certain terms contained in the Act.  Complete definitions can be found in 29 CFR 500.20.

"Migrant Agricultural Worker" and "Seasonal Agricultural Worker" means; individuals employed in agricultural (including forestry) work on a seasonal or temporary basis.   A worker who moves from one seasonal activity to another is employed on a seasonal basis even though he or she may continue to be employed during a major portion of the year.  Migrant workers are required to be absent overnight from their permanent place of residence. Seasonal workers are not required to be absent overnight from their permanent place of residence.  Members of the contractor's immediate family are not considered to be either migrant or seasonal workers.

"Farm Labor Contractor" means; an individual who, for pay, performs any recruiting, soliciting, hiring, employing, furnishing, or transporting of any migrant or seasonal agricultural worker.

"Immediate family" includes only 1) spouse; 2) children, stepchildren, or foster children; 3) parents, stepparents, or foster parents; and 4) brothers and sisters.

Registration Requirement - Any contractor who provides or hires migrant or seasonal workers to perform agricultural or manual forestry work is required to first obtain a Certificate of Registration from the Department of Labor or an authorized State agency.  The contractor must carry the Certificate at all times while engaged in labor contracting activities, and must display it upon request.  Any of the contractor's employees who also perform farm labor contractor duties must have their own Farm Labor Contractor Employee Certificate.

Worker Protections - The Act provides protections and standards related to wage disclosure, recordkeeping, vehicle safety, and housing.  The full text of the regulation can be found in 29 CFR 500.

1) Wage and Payroll Standards

a). The contractor must disclose to each worker the full terms of their employment at the time they

are recruited or hired.  The Department of Labor provides an optional form for contractor's use

in disclosure.

b). The contractor must display and maintain the MSPA poster provided by the Department of

Labor.  The poster shall be in the language common to the workers.

c). The contractor must keep the following payroll records for each employee:  name, address, social security number, basis for wages (i.e. per hour, per tree, per acre), number of units earned if paid on a per unit basis, hours worked, total pay, withholdings and purpose for each, and net pay.  Payroll records shall be retained for three years.  (If paid on a piece rate basis, the employee's wage must be at least equivalent to the required hourly wage for the hours worked, including overtime differential for time in excess of 40 hours per week.)

d). Payments must be made no less frequently than every two weeks.  At the time of each payment, the contractor shall provide to the employee a written itemization of the information listed above.

2.  Motor Vehicle Safety

a). The authorization to transport employees must appear on the contractor's certificate.  The con-

tractor must be registered to transport employees, unless employees provide their own transportation

or carpool by their own arrangement in one of their own vehicles.  If contractor directs or

requests employees to car-pool the registration requirement is still applicable.

b). Contractor-provided automobiles and station wagons shall comply with specified safety stan-

dards.  Vehicles larger than a station wagon must comply with additional standards described

in 29 CFR 500.105, and  must be operated by a certified driver.

c). An insurance policy or liability bond is required for each contractor-provided vehicle used to

transport workers.

3.  Housing

a). The authorization to furnish housing, other than commercial lodging, must appear on the

contractor’s certificate.

b). The act allows workers to be housed only in a commercial establishment or a facility that has

been certified by a health authority or other appropriate agency.  The certificate must be posted at the site.

H.24  USE OF UNDOCUMENTED WORKERS

The Immigration and Nationality Act as amended by the Immigration Reform and Control Act (8 USC 1324a; 8 CFR 274a) makes it unlawful for an employer to hire unauthorized aliens (undocumented workers) and established the I09 Form as the document to be used for employment eligibility verification.

The contractor is required to 1) have all employees completed and sign the I-9 Form to certify that they are eligible for employment; 2) examine documents presented by the employee and ensure the documents appear to be genuine and related to the individual; 3) record information about the documents on the form, and complete the certification portion of the form; 4) retain the form for three years, or one year past the end of employment of the individual, whichever is longer.

It is illegal to discriminate against any individual (other than a citizen of another country who is not authorized to work in

the U.S.) in hiring, discharging, or recruiting because of that individual's national origin or citizenship status. For further information on the requirements of the Act, contractors should contact the Employer and Labor Relations Officer of their local INS office.

H.25  PREWORK CONFERENCE

Prior to commencement of work, the Contractor will meet with the Contracting Officer to discuss contract terms, work performance requirements and work progress schedules.  Also at this meeting such things as sanitation, camping requirements, fire prevention and suppression plans will be developed.  The meeting will be held at a time and place determined by the Contracting Officer.

H.26  WORK PROGRESS SCHEDULE

The Contractor shall be required to present at the prework conference (or within 10 days thereafter) a written plan of work providing for the orderly and timely completion of the contract requirements.  This plan is subject to the approval of the Contracting Officer.  The schedule may be modified in writing during the course of the contract when conditions warrant it.

If the work progress falls behind schedule, the Contractor shall take such action as necessary to ensure that the timely completion of the contract is not jeopardized.  In addition, the Contracting Officer may require the Contractor to submit a revised plan of work showing how he intends to complete the project on time and in compliance with all contract requirements.

H.27  WORKERS COMPENSATION INSURANCE

The Contractor shall provide evidence of Worker's Compensation Insurance or a letter from the State Department of Industrial Relations exempting the Contractor from the requirement.  NOTE: A Contractor working alone is not required to carry the insurance.

SECTION I - CONTRACT CLAUSES

I.1  See FAR Clause 52.252-02 - CLAUSES INCORPORATED BY REFERENCE (FEB 1998) at the end of this

Section I.

Clauses Incorporated by Reference are designated in Lower Case Letter.

CLAUSES INCLUDED IN FULL TEXT ARE DESIGNATED IN UPPER CASE LETTERS.

52.202-01	Definitions (OCT 1995)

52.203-03	Gratuities (APR 1984)

52.203-05	Covenant Against Contingent Fees (APR 1984)

52.203-06	Restrictions on Subcontractor Sales to the Government (JUL 1995)

52.203-07	Anti-Kickback Procedures (JUL 1995)

52.203-08	Cancellation, Rescission, and Recovery of Funds for Illegal or Improper Activity

(JAN 1997)

52.203-10	Price or Fee Adjustment for Illegal or Improper Activity (JAN 1997)

52.203-12	Limitations on Payments to Influence Certain Federal Transactions (JUN 1997)

52.204-04	Printing/Copying Double- Sided on Recycled Paper (JUN 1996)

52.209-06	Protecting the Government's Interest When Subcontracting with Contractors

Debarred, Suspended, or Proposed for Debarment (JUL 1995)

52.215-02	Audit and Records--Negotiation (JUN 1999)

    - Order of Precedence--Uniform Contract Format (OCT 1997)

52.219-06	Notice of Total Small Business Set-Aside (JUL 1996)

    - Utilization of Small Business Concerns (OCT 1999)

52.222-03	Convict Labor (AUG 1996)

52.222-04	Contract Work Hours and Safety Standards Act--Overtime Compensation (JUL 1995)

52.222-21	Prohibition of Segregated Facilities (FEB 1999)

52.222-26	Equal Opportunity (FEB 1999)

52.222-35	Affirmative Action for Disabled Veterans and Veterans of the Vietnam Era  (APR 1998)

52.222-36	Affirmative Action for Workers with Disabilities (JUN 1998)

52.222-37	Employment Reports on Disabled Veterans and Veterans of the Vietnam Era (JAN 1999)

    - SEVICE CONTRACT ACT OF 1965, AS AMENDED (MAY 1989)

    - STATEMENT OF EQUIVALENT RATES FOR FEDERAL HIRES (MAY 1989)

    - Fair Labor Standards Act and Service Contract Act—Price Adjustment (Multiple Year and Option Contracts)(MAY 1989)

52.222-44	Fair Labor Standards Act and Service Contract Act--Price adjustment (MAY 1989)

52.223-06	Drug-Free Workplace (JAN 1997)

52.225-14	Inconsistency between English Version and Translation of Contract (FEB 2000)

52.227-01	Authorization and Consent (JUL 1995)

    - Notice of Assistance Regarding Patent and Copyright Infringement (AUG 1996)

52.228-05	INSURANCE—WORK ON A GOVERNMENT INSTALLATION (JAN 1997)

52.229-03	Federal, State, and Local Taxes (JAN 1991)

52.232-01	Payments (APR 1984)

52.232-08	DISCOUNTS FOR PROMT PAYMENT (MAY 1997)

52.232-11	Extras (APR 1984)

52.232-17	Interest (JUN 1996)

52.232-18	Availability of Funds (APR 1984)

52.232-23	ASSIGNMENT OF CLAIMS (JAN 1986)

52.232-25	Prompt Payment (JUN 1997)

    - PAYMENT BY ELECTRONIC FUNDS TRANSFER—OTHER THAN CENTRAL CONTRACTOR REGISTRATION (MAY 1999)

    - DESIGNATION OF OFFICE FOR GOVERNMENT RECEIPT OF ELECTRONIC FUNDS TRANSFER INFORMATION (MAY 1999)

    - PAYMENT BY THIRD PARTY (MAY 1999)

52.233-01	DISPUTES (DEC 1998)

52.233-03	Protest after Award (AUG 1996)

52.237-02	PROTECTION OF GOVERNMENT BUILDINGS, EQUIPMENT, AND VEGETATION 				(APR 1984)

52.242-13	Bankruptcy (JUL 1995)

52.243-01A1	CHANGES—FIXED PRICE (AUG 1987)

52.244-05	Competition in Subcontracting (DEC 1996)

52.244-06	SUBCONTRACTS FOR COMMERCIAL ITEMS AND COMMERCAL COMPONENTS

(OCT 1998)

52.245-04	Government-Furnished Property (Short Form) (APR 1984)

    - Limitation of Liability--Services (FEB 1997)

52.249-02	TERMINATION FOR CONVENICE OF THE GOVERNMENT (FIXED-PRICE)

(SEP 1996)

52.249-08	DEFAULT (FIXED-PRICE SUPPLY AND SERVICE)(APR 1984)

52.252-02	CLAUSES INCORPORATED BY REFERNCE (FEB 1998)

52.253-01	Computer Generated Forms (JAN 1991)

I.2  SERVICE CONTRACT ACT OF 1965, AS AMENDED (FAR 52.222-41)(MAY 1989)

(a) Definitions. "Act," as used in this clause, means the Service Contract Act of 1965, as amended (41 U.S.C. 351, et seq.).

"Contractor," as used in this clause or in any subcontract, shall be deemed to refer to the subcontractor, except in the term "Government Prime Contractor."

"Service employee," as used in this clause, means any person engaged in the performance of this contract other than any person employed in a bona fide executive, administrative, or professional capacity, as these terms are defined in Part 541 of Title 29, Code of Federal Regulations, as revised. It includes all such persons regardless of any contractual relationship that may be alleged to exist between a Contractor or subcontractor and such persons.

(b) Applicability. This contract is subject to the following provisions and to all other applicable provisions of the Act and regulations of the Secretary of Labor (29 CFR Part 4). This clause does not apply to contracts or subcontracts administratively exempted by the Secretary of Labor or exempted by 41 U.S.C. 356, as interpreted in Subpart C of 29 CFR Part 4.

(c) Compensation. (1) Each service employee employed in the performance of this contract by the Contractor or any subcontractor shall be paid not less than the minimum monetary wages and shall be furnished fringe benefits in accordance with the wages and fringe benefits determined by the Secretary of Labor, or authorized representative, as specified in any wage determination attached to this contract.

(2)(i) If a wage determination is attached to this contract, the Contractor shall classify any class of service employee which is not listed therein and which is to be employed under the contract (i.e., the work to be performed is not performed by any classification listed in the wage determination) so as to provide a reasonable relationship (i.e., appropriate level of skill comparison) between such unlisted classifications and the classifications listed in the wage determination. Such conformed class of employees shall be paid the monetary wages and furnished the fringe benefits as are determined pursuant to the procedures in this paragraph (c).

(ii) This conforming procedure shall be initiated by the Contractor prior to the performance of contract work by the unlisted class of employee. The Contractor shall submit Standard Form (SF) 1444, Request For Authorization of Additional Classification and Rate, to the Contracting Officer no later than 30 days after the unlisted class of employee performs any contract work. The Contracting Officer shall review the proposed classification and rate and promptly submit the completed SF 1444 (which must include information regarding the agreement or disagreement of the employees' authorized representatives or the employees themselves together with the agency recommendation), and all pertinent information to the Wage and Hour Division, Employment Standards Administration, U.S. Department of Labor. The Wage and Hour Division will approve, modify, or disapprove the action or render a final determination in the event of disagreement within 30 days of receipt or will notify the Contracting Officer within 30 days of receipt that additional time is necessary.

(iii) The final determination of the conformance action by the Wage and Hour Division shall be transmitted to the Contracting Officer who shall promptly notify the Contractor of the action taken. Each affected employee shall be furnished by the Contractor with a written copy of such determination or it shall be posted as a part of the wage determination.

(iv)(A) The process of establishing wage and fringe benefit rates that bear a reasonable relationship to those listed in a wage determination cannot be reduced to any single formula. The approach used may vary from wage determination to wage determination depending on the circumstances. Standard wage and salary administration practices which rank various job classifications by pay grade pursuant to point schemes or other job factors may, for example, be relied upon. Guidance may also be obtained from the way different jobs are rated under Federal pay systems (Federal Wage Board Pay System and the General Schedule) or from other wage determinations issued in the same locality.  Basic to the establishment of any conformable wage rate(s) is the concept that a pay relationship should be maintained between job classifications based on the skill required and the duties performed.

(B) In the case of a contract modification, an exercise of an option, or extension of an existing contract, or in any other case where a Contractor succeeds a contract under which the classification in question was previously conformed pursuant to paragraph (c) of this clause, a new conformed wage rate and fringe benefits may be assigned to the conformed classification by indexing (i.e., adjusting) the previous conformed rate and fringe benefits by an amount equal to the average (mean) percentage increase (or decrease, where appropriate) between the wages and fringe benefits specified for all classifications to be used on the contract which are listed in the current wage determination, and those specified for the corresponding classifications in the previously applicable wage determination. Where conforming actions are accomplished in accordance with this paragraph prior to the performance of contract work by the unlisted class of employees, the

Contractor shall advise the Contracting Officer of the action taken but the other procedures in subdivision (c)(2)(ii) of this clause need not be followed.

(C) No employee engaged in performing work on this contract shall in any event be paid less than the currently applicable minimum wage specified under section 6(a)(1) of the Fair Labor Standards Act of 1938, as amended.

(v) The wage rate and fringe benefits finally determined under this subparagraph (c)(2) of this clause shall be paid to all employees performing in the classification from the first day on which contract work is performed by them in the classification. Failure to pay the unlisted employees the compensation agreed upon by the interested parties and/or finally determined by the Wage and Hour Division retroactive to the date such class of employees commenced contract work shall be a violation of the Act and this contract.

(vi) Upon discovery of failure to comply with subparagraph (c)(2) of this clause, the Wage and Hour Division shall make a final determination of conformed classification, wage rate, and/or fringe benefits which shall be retroactive to the date such class or classes of employees commenced contract work.  (3) Adjustment of compensation. If the term of this contract is more than 1 year, the minimum monetary wages and fringe benefits required to be paid or furnished there under to service employees under this contract shall be subject to adjustment after 1 year and not less often than once every 2 years, under wage determinations issued by the Wage and Hour Division.

(d) Obligation to furnish fringe benefits. The Contractor or subcontractor may discharge the obligation to furnish fringe benefits specified in the attachment or determined under subparagraph (c)(2) of this clause by furnishing equivalent combinations of bona fide fringe benefits, or by making equivalent or differential cash payments, only in accordance with Subpart D of 29 CFR Part 4.

(e) Minimum wage. In the absence of a minimum wage attachment for this contract, neither the Contractor nor any subcontractor under this contract shall pay any person performing work under this contract (regardless of whether the person is a service employee) less than the minimum wage specified by section 6(a)(1) of the Fair Labor Standards Act of 1938. Nothing in this clause shall relieve the Contractor or any subcontractor of any other obligation under law or contract for payment of a higher wage to any employee.

(f) Successor contracts. If this contract succeeds a contract subject to the Act under which substantially the same services were furnished in the same locality and service employees were paid wages and fringe benefits provided for in a collective bargaining agreement, in the absence of the minimum wage attachment for this contract setting forth such collectively bargained wage rates and fringe benefits, neither the Contractor nor any subcontractor under this con-tract shall pay any service employee performing any of the contract work (regardless of whether or not such employee was employed under the predecessor contract), less than the wages and fringe benefits provided for in such collective bargaining agreement, to which such employee would have been entitled if employed under the predecessor contract, including accrued wages and fringe benefits and any prospective increases in wages and fringe benefits provided for under such agreement. No Contractor or subcontractor under this contract may be relieved of the foregoing obligation unless the limitations of 29 CFR 4.1b(b) apply or unless the Secretary of Labor or the Secretary's authorized representative finds, after a hearing as provided in 29 CFR 4.10 that the wages and/or fringe benefits provided for in such agreement are substantially at variance with those which prevail for services of a character similar in the locality, or determines, as provided in 29 CFR 4.11, that the collective bargaining agreement applicable to service employees employed under the predecessor contract was not entered into as a result of arm's length negotiations. Where it is found in accordance with the review procedures provided in 29 CFR 4.10 and/or 4.11 and Parts 6 and 8 that some or all of the wages and/or fringe benefits contained in a predecessor Contractor's collective bargaining agreement are substantially at variance with those which prevail for services of a character similar in the locality, and/or that the collective bargaining agreement applicable to service employees employed under the predecessor contract was not entered into as a result of arm's length negotiations, the Department will issue a new or revised wage determination setting forth the applicable wage rates and fringe benefits. Such determination shall be made part of the contract or subcontract, in accordance with the decision of the Administrator, the Administrative Law Judge, or the Board of Service Contract Appeals, as the case may be, irrespective of whether such issuance occurs prior to or after the award of a contract or subcontract (53 Comp. Gen. 401 (1973)). In the case of a wage determination issued solely as a result of a finding of substantial variance, such determination shall be effective as of the date of the final administrative decision.

(g) Notification to employees. The Contractor and any subcontractor under this contract shall notify each service employee commencing work on this contract of the minimum monetary wage and any fringe benefits required to be paid pursuant to this contract, or shall post the wage determination attached to this contract. The poster provided by the Department of Labor (Publication WH 1313) shall be posted in a prominent and accessible place at the worksite. Failure to comply with this requirement is a violation of section 2(a)(4) of the Act and of this contract.

(h) Safe and sanitary working conditions. The Contractor or subcontractor shall not permit any part of the services called for by this contract to be performed in buildings or surroundings or under working conditions provided by or under the control or supervision of the Contractor or subcontractor which are unsanitary, hazardous, or dangerous to the health or safety of the service employees. The Contractor or subcontractor shall comply with the safety and health standards applied under 29 CFR Part 1925.

(i) Records. (1) The Contractor and each subcontractor performing work subject to the Act shall make and maintain for 3 years from the completion of the work, and make them available for inspection and transcription by authorized representatives of the Wage and Hour Division, Employment Standards Administration, a record of the following:

(i) For each employee subject to the Act--

(A) Name and address and social security number;

(B) Correct work classification or classifications, rate or rates of monetary wages paid and fringe benefits provided, rate or rates of payments in lieu of fringe benefits, and total daily and weekly compensation;

(C) Daily and weekly hours worked by each employee; and

(D) Any deductions, rebates, or refunds from the total daily or weekly compensation of each employee.

(ii) For those classes of service employees not included in any wage determination attached to this contract, wage rates or fringe benefits determined by the interested parties or by the Administrator or authorized representative under the terms of paragraph (c) of this clause. A copy of the report required by subdivision (c)(2)(ii) of this clause will fulfill this requirement.

(iii) Any list of the predecessor Contractor's employees which had been furnished to the Contractor as prescribed by paragraph (n) of this clause.

(2) The Contractor shall also make available a copy of this contract for inspection or transcription by authorized representatives of the Wage and Hour Division.

(3) Failure to make and maintain or to make available these records for inspection and transcription shall be a violation of the regulations and this contract, and in the case of failure to produce these records, the Contracting Officer, upon direction of the Department of Labor and notification to the Contractor, shall take action to cause suspension of any further payment or advance of funds until the violation ceases.

(4) The Contractor shall permit authorized representatives of the Wage and Hour Division to conduct interviews with employees at the worksite during normal working hours.

(j) Pay periods. The Contractor shall unconditionally pay to each employee subject to the Act all wages due free and clear and without subsequent deduction (except as otherwise provided by law or regulations, 29 CFR Part 4), rebate, or kickback on any account. These payments shall be made no later than one pay period following the end of the regular pay period in which the wages were earned or accrued. A pay period under this Act may not be of any duration longer than semi-monthly.

(k) Withholding of payments and termination of contract. The Contracting Officer shall withhold or cause to be withheld from the Government Prime Contractor under this or any other Government contract with the Prime Contractor such sums as an appropriate official of the Department of Labor requests or such sums as the Contracting Officer decides may be necessary to pay underpaid employees employed by the Contractor or subcontractor. In the event of failure to pay any employees subject to the Act all or part of the wages or fringe benefits due under the Act, the Contracting Officer may, after authorization or by direction of the Department of Labor and written notification to the Contractor, take action to cause suspension of any further payment or advance of funds until such violations have ceased. Additionally, any failure to comply with the requirements of this clause may be grounds for termination of the right to proceed with the contract work. In such event, the Government may enter into other contracts or arrangements for completion of the work, charging the Contractor in default with any additional cost.

(l) Subcontracts. The Contractor agrees to insert this clause in all subcontracts subject to the Act.

(m) Collective bargaining agreements applicable to service employees. If wages to be paid or fringe benefits to be furnished any service employees employed by the Government Prime Contractor or any subcontractor under the contract are provided for in a collective bargaining agreement which is or will be effective during any period in which the contract is being performed, the Government Prime Contractor shall report such fact to the Contracting Officer, together with full information as to the application and accrual of such wages and fringe benefits, including any prospective increases, to service employees engaged in work on the contract, and a copy of the collective bargaining agreement. Such report shall be made upon commencing performance of the contract, in the case of collective bargaining agreements effective at such time, and in the case of such agreements or provisions or amendments thereof effective at a later time during the period of contract performance such agreements shall be reported promptly after negotiation thereof.

(n) Seniority list. Not less than 10 days prior to completion of any contract being performed at a Federal facility where service employees may be retained in the performance of the succeeding contract and subject to a wage determination which contains vacation or other benefit provisions based upon length of service with a Contractor (predecessor) or successor (29 CFR 4.173), the incumbent Prime Contractor shall furnish the Contracting Officer a certified list of the names of all service employees on the Contractor's or subcontractor's payroll during the last month of contract performance. Such list shall also contain anniversary dates of employment on the contract either with the current or predecessor Contractors of each such service employee. The Contracting Officer shall turn over such list to the successor Contractor at the commencement of the succeeding contract.

(o) Rulings and interpretations. Rulings and interpretations of the Act are contained in Regulations, 29 CFR Part 4.

(p) Contractor's certification.

(1) By entering into this contract, the Contractor (and officials thereof) certifies that neither it (nor he or she) nor any person or firm who has a substantial interest in the Contractor's firm is a person or firm ineligible to be awarded Government contracts by virtue of the sanctions imposed under section 5 of the Act.

(2) No part of this contract shall be subcontracted to any person or firm ineligible for award of a Government contract under section 5 of the Act.

(3) The penalty for making false statements is prescribed in the U.S. Criminal Code, 18 U.S.C. 1001.

(q) Variations, tolerances, and exemptions involving employment. Notwithstanding any of the provisions in paragraphs (b) through (o) of this clause, the following employees may be employed in accordance with the following variations, tolerances, and exemptions, which the Secretary of Labor, pursuant to section 4(b) of the Act prior to its amendment by Pub. L. 92-473, found to be necessary and proper in the public interest or to avoid serious impairment of the conduct of Government business:

(1) Apprentices, student-learners, and workers whose earning capacity is impaired by age, physical or mental deficiency, or injury may be employed at wages lower than the minimum wages otherwise required by section 2(a)(1) or 2(b)(1) of the Act without diminishing any fringe benefits or cash payments in lieu thereof required under section 2(a)(2) of the Act, in accordance with the conditions and procedures prescribed for the employment of apprentices, student-learners, handicapped persons, and handicapped clients of sheltered workshops under section 14 of the Fair Labor Standards Act of 1938, in the regulations issued by the Administrator (29 CFR Parts 520, 521, 524, and 525).

(2) The Administrator will issue certificates under the Act for the employment of apprentices, student-learners, handicapped persons, or handicapped clients of sheltered workshops not subject to the Fair Labor Standards Act of 1938, or subject to different minimum rates of pay under the two acts, authorizing appropriate rates of minimum wages (but without changing requirements concerning fringe benefits or supplementary cash payments in lieu thereof), applying procedures prescribed by the applicable regulations issued under the Fair Labor Standards Act of 1938 (29 CFR Parts 520, 521, 524, and 525).

(3) The Administrator will also withdraw, annul, or cancel such certificates in accordance with the regulations in 29 CFR Parts 525 and 528.

(r) Apprentices. Apprentices will be permitted to work at less than the predetermined rate for the work they perform when they are employed and individually registered in a bona fide apprenticeship program registered with a State Apprenticeship Agency which is recognized by the U.S. Department of Labor, or if no such recognized agency exists in a State, under a program registered with the Bureau of Apprenticeship and Training, Employment and Training Administration, U.S. Department of Labor. Any employee who is not registered as an apprentice in an approved program shall be paid the wage rate and fringe benefits contained in the applicable wage determination for the journeyman classification of work actually performed. The wage rates paid apprentices shall not be less than the wage rate for their level of progress set forth in the registered program, expressed as the appropriate percentage of the journeyman's rate contained in the applicable wage determination. The allowable ratio of apprentices to journeymen employed on the contract work in any craft classification shall not be greater than the ratio permitted to the Contractor as to his entire work force under the registered program.

(s) Tips. An employee engaged in an occupation in which the employee customarily and regularly receives more than $30 a month in tips may have the amount of these tips credited by the employer against the minimum wage required by section 2(a)(1) or section 2(b)(1) of the Act, in accordance with section 3(m) of the Fair Labor Standards Act and Regulations, 29 CFR Part 531. However, the amount of credit shall not exceed $1.34 per hour beginning January 1, 1981. To use this provision--

(1) The employer must inform tipped employees about this tip credit allowance before the credit is utilized;

(2) The employees must be allowed to retain all tips (individually or through a pooling arrangement and regardless of whether the employer elects to take a credit for tips received);

(3) The employer must be able to show by records that the employee receives at least the applicable Service Contract Act minimum wage through the combination of direct wages and tip credit; and

(4) The use of such tip credit must have been permitted under any predecessor collective bargaining agreement applicable by virtue of section 4(c) of the Act.

(t) Disputes concerning labor standards. The U.S. Department of Labor has set forth in 29 CFR Parts 4, 6, and 8 procedures for resolving disputes concerning labor standards requirements. Such disputes shall be resolved in accordance with those procedures and not the Disputes clause of this contract. Disputes within the meaning of this clause include disputes between the Contractor (or any of its subcontractors) and the contracting agency, the U.S. Department of Labor, or the employees or their representatives.

I.3  STATEMENT OF EQUIVALENT RATES FOR FEDERAL HIRES (FAR 52.222-42)(MAY 1989)

In compliance with the Service Contract Act of 1965, as amended, and the regulations of the Secretary of Labor (29 CFR Part 4), this clause identifies the classes of service employees expected to be employed under the contract and states the wages and fringe benefits payable to each if they were employed by the contracting agency subject to the provisions of 5 U.S.C. 5341 or 5332.

This Statement is for Information Only: It is not a Wage Determination

EMPLOYEE CLASS 		MONETARY WAGE-- FRINGE BENEFITS

Forestry Truck Driver		WG-6			$14.05

I.4   INSURANCE--WORK ON A GOVERNMENT INSTALLATION (FAR 52.228-5)(JAN 1997)

(a) The Contractor shall, at its own expense, provide and maintain during the entire performance of this contract, at least the kinds and minimum amounts of insurance required in the Schedule or elsewhere in the contract.

(b) Before commencing work under this contract, the Contractor shall notify the Contracting Officer in writing that the required insurance has been obtained. The policies evidencing required insurance shall contain an endorsement to the effect that any cancellation or any material change adversely affecting the Government's interest shall not be effective--

(1) For such period as the laws of the State in which this contract is to be performed prescribe; or

(2) Until 30 days after the insurer or the Contractor gives written notice to the Contracting Officer, whichever period is longer.

(c) The Contractor shall insert the substance of this clause, including this paragraph (c), in subcontracts under this contract that require work on a Government installation and shall require subcontractors to provide and maintain the insurance required in the Schedule or elsewhere in the contract. The Contractor shall maintain a copy of all subcontractors' proofs of required insurance, and shall make copies available to the Contracting Officer upon request. (See Section H.15).

I.5  DISCOUNTS FOR PROMPT PAYMENT (FAR 52.232-8)(MAY 1997)

(a) Discounts for prompt payment will not be considered in the evaluation of offers. However, any offered discount will form a part of the award, and will be taken if payment is made within the discount period indicated in the offer by the offeror. As an alternative to offering a prompt payment discount in conjunction with the offer, offerors awarded contracts may include prompt payment discounts on individual invoices. (b) In connection with any discount offered for prompt payment, time shall be computed from the date of the invoice. If the Contractor has not placed a date on the invoice, the due date shall be calculated from the date the designated billing office receives a proper invoice, provided the agency annotates such invoice with the date of receipt at the time of receipt. For the purpose of computing the discount earned, payment shall be considered to have been made on the date that appears on the payment check or, for an electronic funds transfer, the specified payment date. When the discount date falls on a Saturday, Sunday, or legal holiday when Federal Government offices are closed and Government business is not expected to be conducted, payment may be made on the following business day.

I.6  ASSIGNMENT OF CLAIMS (FAR 52.232-23)(JAN 1986)

(a) The Contractor, under the Assignment of Claims Act, as amended, 31 U.S.C. 3727, 41 U.S.C. 15 (hereafter referred to as "the Act"), may assign its rights to be paid amounts due or to become due as a result of the performance of this contract to a bank, trust company, or other financing institution, including any Federal lending agency. The assignee under such an assignment may thereafter further assign or reassign its right under the original assignment to any type of financing institution described in the preceding sentence.

(b) Any assignment or reassignment authorized under the Act and this clause shall cover all unpaid amounts payable under this contract, and shall not be made to more than one party, except that an assignment or reassignment may be made to one party as agent or trustee for two or more parties participating in the financing of this contract.

(c) The Contractor shall not furnish or disclose to any assignee under this contract any classified document (including this contract) or information related to work under this contract until the Contracting Officer authorizes such action in writing.

I.7   PAYMENT BY ELECTRONIC FUNDS TRANSFER--OTHER THAN CENTRAL CONTRACTOR

REGISTRATION (FAR 52.232-34)(MAY 1999)

(a) Method of payment. (1) All payments by the Government under this contract shall be made by electronic funds transfer (EFT) except as provided in paragraph (a)(2) of this clause. As used in this clause, the term "EFT" refers to the funds transfer and may also include the payment information transfer.

(2) In the event the Government is unable to release one or more payments by EFT, the Contractor agrees to either--

(i) Accept payment by check or some other mutually agreeable method of payment; or

(ii) Request the Government to extend payment due dates until such time as the Government makes payment by EFT (but see paragraph (d) of this clause).

(b) Mandatory submission of Contractor's EFT information.

(1) The Contractor is required to provide the Government with the information required to make payment by EFT (see paragraph (j) of this clause). The Contractor shall provide this information directly to the office designated in this contract to receive that information (hereafter: "designated office") by no later than 15 days prior to submission of the first request for payment.  If not otherwise specified in this contract, the payment office is the designated office for receipt of the Contractor's EFT information. If more than one designated office is named for the contract, the Contractor shall provide a separate notice to each office. In the event that the EFT information changes, the Contractor shall be responsible for providing the updated information to the designated office(s). (2) If the Contractor provides EFT information applicable to multiple contracts, the Contractor shall specifically state the applicability of this EFT information in terms acceptable to the designated office. However, EFT information supplied to a designated office shall be applicable only to contracts that identify that designated office as the office to receive EFT information for that contract.

(c) Mechanisms for EFT payment. The Government may make payment by EFT through either the Automated Clearing House (ACH) network, subject to the rules of the National Automated Clearing House Association, or the Fedwire

Transfer System. The rules governing Federal payments through the ACH are contained in 31 CFR part 210.  (d) Suspension of payment. (1) The Government is not required to make any payment under this contract until after receipt, by the designated office, of the correct EFT payment information from the Contractor. Until receipt of the correct EFT information, any invoice or contract financing request shall be deemed not to be a proper invoice for the purpose of prompt payment under

this contract. The prompt payment terms of the contract regarding notice of an improper invoice and delays in accrual of interest penalties apply.

(2) If the EFT information changes after submission of correct EFT information, the Government shall begin using the changed EFT information no later than 30 days after its receipt by the designated office to the extent payment is made by EFT. However, the Contractor may request that no further payments be made until the updated EFT information is implemented by the payment office. If such suspension would result in a late payment under the prompt payment terms of this contract, the Contractor's request for suspension shall extend the due date for payment by the number of days of

the suspension.

(e) Liability for uncompleted or erroneous transfers. (1) If an uncompleted or erroneous transfer occurs because the Government used the Contractor's EFT information incorrectly, the Government remains responsible for--

(i) Making a correct payment;

(ii) Paying any prompt payment penalty due; and

(iii) Recovering any erroneously directed funds.

(2) If an uncompleted or erroneous transfer occurs because the Contractor's EFT information was incorrect, or was revised within 30 days of Government release of the EFT payment transaction instruction to the Federal Reserve

System, and--

(i) If the funds are no longer under the control of the payment office, the Government is deemed to have made payment and the Contractor is responsible for recovery of any erroneously directed funds; or

(ii) If the funds remain under the control of the payment office, the Government shall not make payment and the provisions of paragraph (d) shall apply.

(f) EFT and prompt payment. A payment shall be deemed to have been made in a timely manner in accordance with the prompt payment terms of this contract if, in the EFT payment transaction instruction released to the Federal

Reserve System, the date specified for settlement of the payment is on or before the prompt payment due date, provided the specified payment date is a valid date under the rules of the Federal Reserve System.

(g) EFT and assignment of claims. If the Contractor assigns the proceeds of this contract as provided for in the assignment of claims terms of this contract, the Contractor shall require as a condition of any such assignment, that the assignee shall provide the EFT information required by paragraph (j) of this clause to the designated office, and shall be paid by EFT in accordance with the terms of this clause. In all respects, the requirements of this clause shall apply to the assignee as if it were the Contractor. EFT information that shows the ultimate recipient of the transfer to be other than the Contractor, in the absence of a proper assignment of claims acceptable to the Government, is incorrect EFT information within the meaning of paragraph (d) of this clause.

(h) Liability for change of EFT information by financial agent. The Government is not liable for errors resulting from changes to EFT information provided by the Contractor's financial agent.

(i) Payment information. The payment or disbursing office shall forward to the Contractor available payment information that is suitable for transmission as of the date of release of the EFT instruction to the Federal Reserve System. The Government may request the Contractor to designate a desired format and method(s) for delivery of payment information from a list of formats and methods the payment office is capable of executing. However, the Government does not guarantee that any particular format or method of delivery is available at any particular payment office and retains the latitude to use the format and delivery method most convenient to the Government. If the Government makes payment by check in accordance with paragraph (a) of this clause, the Government shall mail the payment information to the remittance address in the contract.

(j) EFT information. The Contractor shall provide the following information to the designated office. The Contractor may supply this data for this or multiple contracts (see paragraph (b) of this clause). The Contractor shall designate a single financial agent per contract capable of receiving and processing the EFT information using the EFT methods described in paragraph (c) of this clause.

(1) The contract number (or other procurement identification number).

(2) The Contractor's name and remittance address, as stated in the contract(s).

(3) The signature (manual or electronic, as appropriate), title, and telephone number of the Contractor official authorized to provide this information.

(4) The name, address, and 9-digit Routing Transit Number of the Contractor's financial agent.

(5) The Contractor's account number and the type of account (checking, saving, or lockbox).

(6) If applicable, the Fedwire Transfer System telegraphic abbreviation of the Contractor's financial agent.

(7) If applicable, the Contractor shall also provide the name, address, telegraphic abbreviation, and 9-digit

Routing Transit Number of the correspondent financial institution receiving the wire transfer payment if the Contractor's financial agent is not directly on-line to the Fedwire Transfer System; and, therefore, not the receiver of the wire transfer payment.

I.8  DESIGNATION OF OFFICE FOR GOVERNMENT RECEIPT OF ELECTRONIC FUNDS TRANSFER

INFORMATION (FAR 52.232-35)(MAY 1999)

(a) As provided in paragraph (b) of the clause at 52.232-34, Payment by Electronic Funds Transfer--Other than Central Contractor Registration, the Government has designated the office cited in paragraph (c) of this clause as the office to receive the Contractor's electronic funds transfer (EFT) information, in lieu of the payment office of this contract.

(b) The Contractor shall send all EFT information, and any changes to EFT information to the office designated in paragraph (c) of this clause. The Contractor shall not send EFT information to the payment office, or any other office than that designated in paragraph (c). The Government need not use any EFT information sent to any office other than that designated in paragraph (c).

(c) Designated Office:

To initiate EFT payment, contact the National Finance Center at (504) 255-4647.

I.9  PAYMENT BY THIRD PARTY (FAR 52.232-36)(MAY 1999)

(a) General. The Contractor agrees to accept payments due under this contract, through payment by a third party in lieu of payment directly from the Government, in accordance with the terms of this clause. The third party and, if applicable, the particular Government wide commercial purchase card to be used are identified elsewhere in this contract

(b) Contractor payment request. In accordance with those clauses of this contract that authorize the Contractor to submit invoices, contract financing requests, other payment requests, or as provided in other clauses providing for payment to the Contractor, the Contractor shall make such payment requests through a charge to the Government account with the third

party, at the time and for the amount due in accordance with the terms of this contract.

(c) Payment. The Contractor and the third party shall agree that payments due under this contract shall be made upon submittal of payment requests to the third party in accordance with the terms and conditions of an agreement

between the Contractor, the Contractor's financial agent (if any), and the third party and its agents (if any). No payment shall be due the Contractor until such agreement is made. Payments made or due by the third party under this clause are not payments made by the Government and are not subject to the Prompt Payment Act or any implementation thereof in this contract.

(d) Documentation. Documentation of each charge against the Government's account shall be provided to the Contracting Officer upon request.

(e) Assignment of claims. Notwithstanding any other provision of this contract, if any payment is made under this clause, then no payment under this contract shall be assigned under the provisions of the assignment of claims terms of this contract or the Assignment of Claims Act of 1940, as amended, 31 U.S.C. 3727, 41 U.S.C. 15.

(f) Other payment terms. The other payment terms of this contract shall govern the content and submission of payment requests. If any clause requires information or documents in or with the payment request, that is not provided in the third party agreement referenced in paragraph (c) of this clause, the Contractor shall obtain instructions from the Contracting

Officer before submitting such a payment request.

I.10  DISPUTES (FAR 52.233-1)(DEC 1998)

(a) This contract is subject to the Contract Disputes Act of 1978, as amended (41 U.S.C. 601-613).

(b) Except as provided in the Act, all disputes arising under or relating to this contract shall be resolved under this clause.

(c) "Claim," as used in this clause, means a written demand or written assertion by one of the contracting parties seeking, as a matter of right, the payment of money in a sum certain, the adjustment or interpretation of contract terms, or other relief arising under or relating to this contract.  A claim arising under a contract, unlike a claim relating to that contract, is a claim that can be resolved under a contract clause that provides for the relief sought by the claimant. However, a written demand or written assertion by the Contractor seeking the payment of money exceeding $100,000 is not a claim under the Act until certified as required by subparagraph (d)(2) of this clause. A voucher, invoice, or other routine request for payment that is not in dispute when submitted is not a claim under the Act.   The submission may be converted to a claim under the Act, by complying with the submission and certification requirements of this clause, if it is disputed either as to liability or amount or is not acted upon in a reasonable time.

(d)(1) A claim by the Contractor shall be made in writing and, unless otherwise stated in this contract, submitted within 6 years after accrual of the claim to the Contracting Officer for a written decision. A claim by the Government against the Contractor shall be subject to a written decision by the Contracting Officer.

(2)(i) The Contractor shall provide the certification specified in paragraph (d)(2)(iii) of this clause when submitting any claim exceeding $100,000.

(ii) The certification requirement does not apply to issues in controversy that have not been submitted as all or part of a claim.

(iii) The certification shall state as follows: "I certify that the claim is made in good faith; that the supporting data are accurate and complete to the best of my knowledge and belief; that the amount requested accurately reflects the contract adjustment for which the Contractor believes the Government is liable; and that I am duly authorized to certify the claim on behalf of the Contractor."

(3) The certification may be executed by any person duly authorized to bind the Contractor with respect to the claim.

(e) For Contractor claims of $100,000 or less, the Contracting Officer must, if requested in writing by the Contractor, render a decision within 60 days of the request. For Contractor-certified claims over $100,000, the Contracting Officer must, within 60 days, decide the claim or notify the Contractor of the date by which the decision will be made.

(f) The Contracting Officer's decision shall be final unless the Contractor appeals or files a suit as provided in the Act.

(g) If the claim by the Contractor is submitted to the Contracting Officer or a claim by the Government is presented to the Contractor, the parties, by mutual consent, may agree to use alternative dispute resolution (ADR). If the Contractor refuses an offer for ADR, the Contractor shall inform the Contracting Officer, in writing, of the Contractor's specific reasons for rejecting the offer.

(h) The Government shall pay interest on the amount found due and unpaid from (1) the date that the Contracting Officer receives the claim (certified, if required); or (2) the date that payment otherwise would be due, if that date is later, until the date of payment. With regard to claims having defective certifications, as defined in FAR 33.201, interest shall be paid from the date that the Contracting Officer initially receives the claim. Simple interest on claims shall be paid at the rate, fixed by the Secretary of the Treasury as provided in the Act, which is applicable to the period during which the Contracting Officer receives the claim and then at the rate applicable for each 6-month period as fixed by the Treasury Secretary during the pendency of the claim.

(i) The Contractor shall proceed diligently with performance of this contract, pending final resolution of any request for relief, claim, appeal, or action arising under the contract, and comply with any decision of the Contracting Officer.

I.11  PROTECTION OF GOVERNMENT BUILDINGS, EQUIPMENT, AND VEGETATION (FAR 52.237-2)

(APR 1984)

The Contractor shall use reasonable care to avoid damaging existing buildings, equipment, and vegetation on the Government installation. If the Contractor's failure to use reasonable care causes damage to any of this property, the Contractor shall replace or repair the damage at no expense to the Government as the Contracting Officer directs. If the Contractor fails or refuses to make such repair or replacement, the Contractor shall be liable for the cost, which may be deducted from the contract price.

I.12  CHANGES--FIXED PRICE (FAR 52.243-1)(APR 1984) ALTERNATE I

(a) The Contracting Officer may at any time, by written order, and without notice to the sureties, if any, make changes within the general scope of this contract in any one or more of the following:

(1) Description of services to be performed.

(2) Time of performance (i.e., hours of the day, days of the week, etc.).

(3) Place of performance of the services.

(b) If any such change causes an increase or decrease in the cost of, or the time required for, performance of any part of the work under this contract, whether or not changed by the order, the Contracting Officer shall make an equitable adjustment in the contract price, the delivery schedule, or both, and shall modify the contract.

(c) The Contractor must assert its right to an adjustment under this clause within 30 days from the date of receipt of the written order. However, if the Contracting Officer decides that the facts justify it, the Contracting Officer may receive and act upon a proposal submitted before final payment of the contract.

(d) If the Contractor's proposal includes the cost of property made obsolete or excess by the change, the Contracting Officer shall have the right to prescribe the manner of the disposition of the property.

(e) Failure to agree to any adjustment shall be a dispute under the Disputes clause. However, nothing in this clause shall excuse the Contractor from proceeding with the contract as changed.

I.13   SUBCONTRACTS FOR COMMERCIAL ITEMS AND COMMERCIAL COMPONENTS (FAR 52.244-06)

(OCT 1998)

(a) Definitions.

"Commercial item," as used in this clause, has the meaning contained in the clause at 52.202-1, Definitions.

"Subcontract," as used in this clause, includes a transfer of commercial items between divisions, subsidiaries, or affiliates of the Contractor or subcontractor at any tier.

(b) To the maximum extent practicable, the Contractor shall incorporate, and require its subcontractors at all tiers to incorporate, commercial items or nondevelopmental items as components of items to be supplied under this contract.

(c) Notwithstanding any other clause of this contract, the Contractor is not required to include any FAR provision or clause, other than those listed below to the extent they are applicable and as may be required to establish the reasonableness of prices under Part 15, in a subcontract at any tier for commercial items or commercial components:

(1) 52.222-26, Equal Opportunity (E.O. 11246);

(2) 52.222-35, Affirmative Action for Disabled Veterans and Veterans of the Vietnam Era (38 U.S.C. 4212(a));

(3) 52.222-36, Affirmative Action for Workers With Disabilities (29 U.S.C. 793); and

(4) 52.247-64, Preference for Privately Owned U.S.-Flagged Commercial Vessels (46 U.S.C. 1241) (flow down not required for subcontracts awarded beginning May 1, 1996).

(d) The Contractor shall include the terms of this clause, including this paragraph (d), in subcontracts awarded under this contract.

I.14  TERMINATION FOR CONVENIENCE OF THE GOVERNMENT (FIXED-PRICE)(FAR 52.249-02)

(SEP 1996)

(a) The Government may terminate performance of work under this contract in whole or, from time to time, in part if the Contracting Officer determines that a termination is in the Government's interest. The Contracting Officer shall terminate by delivering to the Contractor a Notice of Termination specifying the extent of termination and the effective date.

(b) After receipt of a Notice of Termination, and except as directed by the Contracting Officer, the Contractor shall immediately proceed with the following obligations, regardless of any delay in determining or adjusting any amounts due under this clause:

(1) Stop work as specified in the notice.

(2) Place no further subcontracts or orders (referred to as subcontracts in this clause) for materials, services, or facilities, except as necessary to complete the continued portion of the contract.

(3) Terminate all subcontracts to the extent they relate to the work terminated.

(4) Assign to the Government, as directed by the Contracting Officer, all right, title, and interest of the Contractor under the subcontracts terminated, in which case the Government shall have the right to settle or to pay any termination settlement proposal arising out of those terminations.

(5) With approval or ratification to the extent required by the Contracting Officer, settle all outstanding liabilities and termination settlement proposals arising from the termination of subcontracts; the approval or ratification will be final for purposes of this clause.

(6) As directed by the Contracting Officer, transfer title and deliver to the Government--

(i) The fabricated or unfabricated parts, work in process, completed work, supplies, and other material produced or acquired for the work terminated; and

(ii) The completed or partially completed plans, drawings, information, and other property that, if the contract had been completed, would be required to be furnished to the Government.

(7) Complete performance of the work not terminated.

(8) Take any action that may be necessary, or that the Contracting Officer may direct, for the protection and preservation of the property related to this contract that is in the possession of the Contractor and in which the Government has or may acquire an interest.

(9) Use its best efforts to sell, as directed or authorized by the Contracting Officer, any property of the types referred to in subparagraph (b)(6) of this clause; provided, however, that the Contractor (i) is not required to extend credit to any purchaser and (ii) may acquire the property under the conditions prescribed by, and at prices approved by, the Contracting Officer. The proceeds of any transfer or disposition will be applied to reduce any payments to be made by the Government under this contract, credited to the price or cost of the work, or paid in any other manner directed by the Contracting Officer.

(c) The Contractor shall submit complete termination inventory schedules no later than 120 days from the effective date of termination, unless extended in writing by the Contracting Officer upon written request of the Contractor within this 120-day period.

(d) After expiration of the plant clearance period as defined in Subpart 45.6 of the Federal Acquisition Regulation, the Contractor may submit to the Contracting Officer a list, certified as to quantity and quality, of termination inventory not previously disposed of, excluding items authorized for disposition by the Contracting Officer. The Contractor may request the Government to remove those items or enter into an agreement for their storage. Within 15 days, the Government will accept title to those items and remove them or enter into a storage agreement. The Contracting Officer may verify the list upon removal of the items, or if stored, within 45 days from submission of the list, and shall correct the list, as necessary, before final settlement.

(e) After termination, the Contractor shall submit a final termination settlement proposal to the Contracting Officer in the form and with the certification prescribed by the Contracting Officer. The Contractor shall submit the proposal promptly, but no later than 1 year from the effective date of termination, unless extended in writing by the Contracting Officer upon written request of the Contractor within this 1-year period. However, if the Contracting Officer determines that the facts justify it, a termination settlement proposal may be received and acted on after 1 year or any extension. If the Contractor fails to submit the proposal within the time allowed, the Contracting Officer may determine, on the basis of information available, the amount, if any, due the Contractor because of the termination and shall pay the amount determined.

(f) Subject to paragraph (e) of this clause, the Contractor and the Contracting Officer may agree upon the whole or any part of the amount to be paid or remaining to be paid because of the termination. The amount may include a reasonable allowance for profit on work done. However, the agreed amount, whether under this paragraph (f) or paragraph (g) of this clause, exclusive of costs shown in subparagraph (g)(3) of this clause, may not exceed the total contract price as reduced by (1) the amount of payments previously made and (2) the contract price of work not terminated. The contract shall be modified, and the Contractor paid the agreed amount. Paragraph (g) of this clause shall not limit, restrict, or affect the amount that may be agreed upon to be paid under this paragraph.

(g) If the Contractor and the Contracting Officer fail to agree on the whole amount to be paid because of the termination of work, the Contracting Officer shall pay the Contractor the amounts determined by the Contracting Officer as follows, but without duplication of any amounts agreed on under paragraph (f) of this clause:

(1) The contract price for completed supplies or services accepted by the Government (or sold or acquired under subparagraph (b)(9) of this clause) not previously paid for, adjusted for any saving of freight and other charges.

(2) The total of--

(i) The costs incurred in the performance of the work terminated, including initial costs and preparatory expense allocable thereto, but excluding any costs attributable to supplies or services paid or to be paid under subparagraph (g)(1) of this clause;

(ii) The cost of settling and paying termination settlement proposals under terminated subcontracts that are properly chargeable to the terminated portion of the contract if not included in subdivision (g)(2)(i) of this clause; and

(iii) A sum, as profit on subdivision (g)(2)(i) of this clause, determined by the Contracting Officer under 49.202 of the Federal Acquisition Regulation, in effect on the date of this contract, to be fair and reasonable; however, if it appears that the Contractor would have sustained a loss on the entire contract had it been completed, the Contracting Officer shall allow no profit under this subdivision (g)(2)(iii) and shall reduce the settlement to reflect the indicated rate of loss.

(3) The reasonable costs of settlement of the work terminated, including--

(i) Accounting, legal, clerical, and other expenses reasonably necessary for the preparation of termination settlement proposals and supporting data;

(ii) The termination and settlement of subcontracts (excluding the amounts of such settlements); and

(iii) Storage, transportation, and other costs incurred, reasonably necessary for the preservation, protection, or disposition of the termination inventory.

(h) Except for normal spoilage, and except to the extent that the Government expressly assumed the risk of loss, the Contracting Officer shall exclude from the amounts payable to the Contractor under paragraph (g) of this clause, the fair value, as determined by the Contracting Officer, of property that is destroyed, lost, stolen, or damaged so as to become undeliverable to the Government or to a buyer.

(i) The cost principles and procedures of Part 31 of the Federal Acquisition Regulation, in effect on the date of this contract, shall govern all costs claimed, agreed to, or determined under this clause.

(j) The Contractor shall have the right of appeal, under the Disputes clause, from any determination made by the Contracting Officer under paragraph (e), (g), or (l) of this clause, except that if the Contractor failed to submit the termination settlement proposal or request for equitable adjustment within the time provided in paragraph (e) or (l), respectively, and failed to request a time extension, there is no right of appeal.

(k) In arriving at the amount due the Contractor under this clause, there shall be deducted--

(1) All unliquidated advance or other payments to the Contractor under the terminated portion of this contract;

(2) Any claim which the Government has against the Contractor under this contract; and

(3) The agreed price for, or the proceeds of sale of, materials, supplies, or other things acquired by the Contractor or sold under the provisions of this clause and not recovered by or credited to the Government.

(l) If the termination is partial, the Contractor may file a proposal with the Contracting Officer for an equitable adjustment of the price(s) of the continued portion of the contract. The Contracting Officer shall make any equitable adjustment agreed upon. Any proposal by the Contractor for an equitable adjustment under this clause shall be requested within 90 days from the effective date of termination unless extended in writing by the Contracting Officer.

(m)(1) The Government may, under the terms and conditions it prescribes, make partial payments and payments against costs incurred by the Contractor for the terminated portion of the contract, if the Contracting Officer believes the total of these payments will not exceed the amount to which the Contractor will be entitled.

(2) If the total payments exceed the amount finally determined to be due, the Contractor shall repay the excess to the Government upon demand, together with interest computed at the rate established by the Secretary of the Treasury under 50 U.S.C. App. 1215(b)(2). Interest shall be computed for the period from the date the excess payment is received by the Contractor to the date the excess is repaid. Interest shall not be charged on any excess payment due to a reduction in the Contractor's termination settlement proposal because of retention or other disposition of termination inventory until 10 days after the date of the retention or disposition, or a later date determined by the Contracting Officer because of the circumstances.

(n) Unless otherwise provided in this contract or by statute, the Contractor shall maintain all records and documents relating to the terminated portion of this contract for 3 years after final settlement. This includes all books and other evidence bearing on the Contractor's costs and expenses under this contract. The Contractor shall make these records and documents available to the Government, at the Contractor's office, at all reasonable times, without any direct charge. If approved by the Contracting Officer, photographs, microphotographs, or other authentic reproductions may be maintained instead of original records and documents.

I.15  DEFAULT (FIXED-PRICE SUPPLY AND SERVICE)(FAR 52.249-8)(APR 1984)

(a)(1) The Government may, subject to paragraphs (c) and (d) of this clause, by written notice of default to the Contractor, terminate this contract in whole or in part if the Contractor fails to--

(i) Deliver the supplies or to perform the services within the time specified in this contract or any extension;

(ii) Make progress, so as to endanger performance of this contract (but see subparagraph (a)(2) of this clause); or

(iii) Perform any of the other provisions of this contract (but see subparagraph (a)(2) of this clause).

(2) The Government's right to terminate this contract under subdivisions (a)(1)(ii) and (1)(iii) of this clause, may be exercised if the Contractor does not cure such failure within 10 days (or more if authorized in writing by the Contracting Officer) after receipt of the notice from the Contracting Officer specifying the failure.

(b) If the Government terminates this contract in whole or in part, it may acquire, under the terms and in the manner the Contracting Officer considers appropriate, supplies or services similar to those terminated, and the Contractor will be liable to the Government for any excess costs for those supplies or services. However, the Contractor shall continue the work not terminated.

(c) Except for defaults of subcontractors at any tier, the Contractor shall not be liable for any excess costs if the failure to perform the contract arises from causes beyond the control and without the fault or negligence of the Contractor. Examples of such causes include (1) acts of God or of the public enemy, (2) acts of the Government in either its sovereign or contractual capacity, (3) fires, (4) floods, (5) epidemics, (6) quarantine restrictions, (7) strikes, (8) freight embargoes, and (9) unusually severe weather. In each instance the failure to perform must be beyond the control and without the fault or negligence of the Contractor.

(d) If the failure to perform is caused by the default of a subcontractor at any tier, and if the cause of the default is beyond the control of both the Contractor and subcontractor, and without the fault or negligence of either, the Contractor shall not be liable for any excess costs for failure to perform, unless the subcontracted supplies or services were obtainable from other sources in sufficient time for the Contractor to meet the required delivery schedule.

(e) If this contract is terminated for default, the Government may require the Contractor to transfer title and deliver to the Government, as directed by the Contracting Officer, any (1) completed supplies, and (2) partially completed supplies and materials, parts, tools, dies, jigs, fixtures, plans, drawings, information, and contract rights (collectively referred to as

"manufacturing materials" in this clause) that the Contractor has specifically produced or acquired for the terminated portion of this contract. Upon direction of the Contracting Officer, the Contractor shall also protect and preserve property in its possession in which the Government has an interest.

(f) The Government shall pay contract price for completed supplies delivered and accepted. The Contractor and Contracting Officer shall agree on the materials delivered and accepted and for the protection and preservation of the property. Failure to agree will be a dispute under the Disputes clause. The Government may withhold from these amounts any sum the Contracting Officer determines to be necessary to protect the Government against loss because of outstanding liens or claims of former lien holders.

(g) If, after termination, it is determined that the Contractor was not in default, or that the default was excusable, the rights and obligations of the parties shall be the same as if the termination had been issued for the convenience of the Government.

(h) The rights and remedies of the Government in this clause are in addition to any other rights and remedies provided by law or under this contract.

I.16  CLAUSES INCORPORATED BY REFERENCE (FAR 52.252-2)(FEB 1998)

This contract incorporates one or more clauses by reference, with the same force and effect as if they were given in full text. Upon request, the Contracting Officer will make their full text available. Also, the full text of a clause may be accessed electronically at this/these address (es):

http://www.arnet.gov.

LIST OF DOCUMENTS, EXHIBITS, AND OTHER ATTACHMENTS

SECTION J - LIST OF ATTACHMENTS

The following hereto form a part of this solicitation and any resultant service contract:

EXHIBITS

Exhibit A-1		Project Map

Exhibit A-2		Spot Map of Limited Operating Periods

Exhibit A-3		Prattville DFPZ sample Mark Areas

Exhibit B		FS-2400-3 Timber Sale Contract

Exhibit C		Wet Haul Conditions

Exhibit D		Subsoiling Specifications

Exhibit D-1		Marking Prescription for Control of Black Stain Root Disease in Unit 32D

Exhibit E 		Fire Plan

Exhibit F		Soil and Water Integrated Design Features & Best  Management Practices

Exhibit G		Wage Determination

Exhibit A		Vicinity Map

Exhibit A-1	Project Map

Exhibit A-2	Spot Map of Limited Operating Periods

EXHIBIT B

| Region: Pacific Southwest (R-5) | U.S. DEPARTMENT OF AGRICULTURE - FOREST SERVICE |  |
| --- | --- | --- |
| National Forest: Lassen | TIMBER SALE CONTRACT | FS-2400-3S (8/99) |
| Ranger District: Almanor | (Ref. FSM 2430, FSH 2409.18) | Page 1 |
| Sale Name: Prattville Forest Recovery DFPZ | Contract No. | Award Date | Termination Date |
| Purchaser's Name and Complete Address: |  |  |  |
|  | Total Sale Acres | Acres to be Cut | Type of Sale |
|  | 1,356 | 1,356 | Scaled |
|  | Legal Description of Sale Area (1): Sections 3, 4, 9,10,12 -16, 23 & 24, T.27N., R.7E.; and Sections 17-19, T.27N., R.8E., MDM. |
| The Parties to this contract are the United States of America, acting through the Forest Service, United States Department of Agriculture, hereinafter called Forest Service, and , hereinafter called Purchaser. Standard Provisions of this contract begin on page 2. Specific conditions are given below. Numbers in parentheses refer to Standard Provisions. Forest Service address to receive payments (9,11,12): Bank of America, File No. 71652, P.O. Box 60000, San Francisco, CA 94160-1652. Measurement will be done after felling. Products will be scaled, counted or otherwise measured according to the National Forest Cubic Scaling Handbook (FSH 2409.11a) Edition (5/91), as Supplemented. Logs will be measured in cubic feet. |

INCLUDED TIMBER (4,7)

|  | Minimum Specifications | Payment Rates Per |
| --- | --- | --- |
|  | Tree | Piece Required to be Removed | Unit of Measure |
| Species | Product | Estimated Quantity | Unit of Measure | DBH (Inches) | No. of Minimum Pieces Per tree | Length (Feet) | D.I.B. at small end (Inches) | Net Volume in % of Gross Volume | Bid Rates $ | Required Slash Disposal $ |
| PP, JP | Sawtimber | 14,238 | GT | 10.0 | 1 | 10 | 6 | NA | 1.37 | X |
| SP, WWP | Sawtimber | 664 | GT | 10.0 | 1 | 10 | 6 | NA | 1.37 | X |
| WF, RF | Sawtimber | 704 | GT | 10.0 | 1 | 10 | 6 | NA | 1.37 | X |
| DF | Sawtimber | 32 | GT | 10.0 | 1 | 10 | 6 | NA | 1.37 | X |
| IC | Sawtimber | 106 | GT | 10.0 | 1 | 10 | 6 | NA | 1.37 | X |
| LP | Sawtimber | Unest. | GT | 10.0 | 1 | 10 | 6 | NA | 1.37 | X |
| All species | MCP | 17,885 | GT | 3.0 | 1 | 6 | NA | NA | 1.37 | X |
| Timber Subject to Agreement Under Special Provision 07.1# |
| Total Quantity | 33,629 |  |  | Total Sale Value $ | 46,071.73 |  |
| GT – Green Ton MCP – Miscellaneous Convertible Product |
| Designation for cutting (7): Refer to table in Section C – Description/Work Statement, C.2 Technical Requirements |
| Slash Disposal (33): Refer to table in Section C – Description/Work Statement, C.2.3 Work Standards |
|  | UNITED STATES OF AMERICA |
| Maximum stump height (29): in Section C.2.3.1.4 Utilization |  |
|  | By (Signature) |
| Normal Operating Season (3,21): From June 1 to November 15 |  |
| Listing of Special Provisions attached to this contract: 7.2#, 7.21#, 7.3, 7.4#, 7.5, |  |
| 7.6, 7.7, 7.8, |  |
| *(1)- Contractor’s Fire Liability is stated in Section H – Special Contract | CONTRACTING OFFICER |
| Requirements, H.15 Emergency Response (AGAR 452,236-77)(Nov 1996), | PURCHASER |
| Subsection (a) Contractor’s Responsibility for Fighting Fire. |  |
| In witness hereof, the parties hereto have executed this contract as of the award date. |  |
|  | By (Signature) |
| (Witness Signature) |  |
| (Witness Signature) | (Title) |

CERTIFICATION

I,                                                                          , certify that I am the                                                       , Secretary of the corporation named as Purchaser herein; that                                                           who signed this contract on behalf of the Purchaser, was then

of said corporation; that said contract was duly signed for and on behalf of said corporation by authority of its governing body, and is within the scope of its corporate powers.

|  |  | CORPORATE |
| --- | --- | --- |
|  |  | SEAL |

1.  Included Timber - The Forest Service agrees to sell and the Contractor agrees to purchase, cut and remove all Included Timber as located and described in Section C of the attached Service Contract, including all pieces that meet minimum piece specifications, and as shown on the Project Area map.  Designation(s) for cutting is(are) shown and described in Section C - DESCRIPTION/SPECIFICATIONS/WORK STATEMENT.

Title to all timber included in this contract shall remain with the United States until its estimated quantities have been determined by the Contracting Officer or designee and, paid for and removed from the Project Area by the Contractor.  The Contractor shall not cut any timber until its quantities have been estimated by the Contracting Officer or designee, and paid for by the Contractor.

The Contractor shall cut and remove Included Timber in strict accordance with the requirements on Page 1, the following Standard Provisions, and with all conditions and requirements in the attached Service Contract, and with the regulations governing timber sales prescribed by the Secretary of Agriculture.

The Contracting Officer or designee may designate additional timber not included in the original volume estimate for cutting within the Project Area as needed to utilize damaged trees, trees to be removed in authorized clearings, or trees the Contracting Officer or designee determines have been unnecessarily damaged or cut by the Contractor.  The Contractor shall pay for additional timber at Bid Rates and Required Deposits, in addition to any payments for liquidated damages as shown in Section G - CONTRACT ADMINISTRATION DATA, G.2 MEASUREMENT AND PAYMENT.*   The additional trees will become Included Timber when designated by the Contracting Officer or designee.

2.  Deposits.   The Contractor agrees to make cash deposits in advance of cutting.  Advance deposits shall be in such amount as to cover the applicable charges for Blocks released for cutting as shown on the Project Area map and in the attached Block/Item Schedule, and for estimated additional specified timber  as described in SECTION C - DESCRIPTION/WORK of the attached Service Contract, to be cut in the next 30 to 60 days.  Except for amounts required for the downpayment, the Contractor shall not be required to make additional deposits when the credit balance in the timber sale account exceeds the charges for Blocks released and for estimated additional specified timber as described in SECTION C - DESCRIPTION/WORK of the attached Service Contract to be cut in the next 60 days.

To the extent payment guarantee is provided, the Contracting Officer or designee shall waive requirements for advance cash deposits for the value of timber on the Project Area which has been released for cutting but not removed, and for the estimated value of species and products removed from the Project Area.  Advance cash deposits shall not be required for more than a monthly billing period.

If at any time the credit balance of the timber sale account exceeds the charges for timber within Blocks released for cutting and for additional Included Timber as described in SECTION C - DESCRIPTION/WORK of the attached Service Contract  that is expected to be cut within the next 60 calendar days, the Contracting Officer or designee shall refund any portion of such unobligated cash balance in the timber sale account, if requested in writing by the Contractor.  The Contracting Officer or designee shall not refund cash in the Contractor's account if the cash is deposited to meet downpayment, extension deposits, or a periodic payment.

If the Contractor plans no cutting within the next 60 calendar days, the Contracting Officer or designee may refund the entire unobligated cash balance, if requested in writing by the Contractor, unless the cash is used for the downpayment, extension deposits, or a periodic payment.  However, the Contracting Officer or designee shall not reduce the account balance below the total value of Blocks released for cutting and for an estimated 10 day cut of additional material  designated as Included Timber as described in SECTION C - DESCRIPTION/WORK of the attached Service Contract.  The Contractor shall make deposits to meet the requirements of advance deposits, before cutting may resume.

Payments are due and payable on the date indicated on the bill for collection.  When a payment for timber cut, other charges, and other payments is not received at the location designated by the Contracting Officer or designee within the 15 calendar days allowed for receipt of payment as indicated on the bill for collection, or when the credit balance in the timber sale account is exceeded by the charges for timber within Blocks released for cutting and additional Included Timber designated as described in SECTION C - DESCRIPTION/WORK of the attached Service Contract, the Contracting Officer or designee shall suspend all or any part of the Contractor's operations until payment or acceptable payment guarantee is received.

Except for advance deposits, the Contractor's failure to pay amounts due by the date allowed for receipt of payment as indicated on the bill for collection shall be considered for Termination for Convenience of the Government as stated in SECTION I.

If the performance or payment is guaranteed by surety bond, the Contracting Officer shall send a copy of the written notification of the Termination to the surety.  Ten calendar days after the Contracting Officer issues written notification to the Contractor of the termination, the Contracting Officer shall make written demand for immediate payment on the surety or other institution providing the guarantee or bond instrument.

Pursuant to the Debt Collection Act, as amended (31 U.S.C. 3701, et seq.), if payment is not received by the Forest Service within 30 days after the bill for collection's date of issue the Contracting Officer shall:

(a) Assess simple interest at the higher of the U.S. Treasury current value of funds rate, as published by the Secretary of Treasury in the Federal Register, or the rate established by the Secretary of Treasury under section 12 of the Contract Disputes Act of 1978 (41 U.S.C. 611).  Interest will begin to accrue as of the initial bill for collection's date of issue;  (b) Assess debtors' administrative charges in addition to the delinquent amount due.  Administrative charges are those additional costs incurred by the Government in processing, handling and collecting delinquent debts;  (c) Assess a penalty charge of 6 percent per annum on any portion of a debt delinquent more than 90 days.  This penalty charge will be in addition to the interest and administrative charges under paragraphs (a) and (b).  Such penalty charge shall accrue from the bill for collection's date of issue and shall be assessed on all outstanding amounts including interest and administrative costs assessed under paragraphs (a) and (b).

Payments will be credited on the date received at the location designated on the bill for collection.

10.  Payment Guarantee - The Contractor may furnish and maintain an acceptable payment guarantee on forms provided by the Contracting Officer or designee, to guarantee payments for stumpage and stumpage related deposits under this contract, in lieu of an advanced cash deposit.  Such guarantee may be a surety bond, negotiable securities, irrevocable letter of credit, assigned savings account, certificates of deposit, or corporate guarantee, and may apply only to the named timber sale contract.  The Contracting Officer shall return the payment guarantee within 60 days of contract closure.

In lieu of an individual payment guarantee, the Contractor may furnish an acceptable blanket payment guarantee for all timber sale contracts the Contractor holds within the same National Forest.  The Contractor shall specify in writing how to distribute the amount of such guarantee to any and all sales.  When the Contractor gives written notice to the Contracting Officer that the Contractor will not cut any trees for 30 calendar days or more, has made payment of current charges, and removed all cut timber, the Contractor may request that the amount allocated to this contract be reallocated to other sales or left unallocated.  The Contractor may not resume cutting on this sale until the Contractor returns the blanket payment guarantee to this contract in an amount sufficient to meet the Contractor's obligations on this contract. The Contractor may combine the blanket payment guarantee with cash to meet these obligations.

At the Contractor's request, the Contracting Officer shall reduce or return the Contractor's blanket payment guarantee when the Contracting Officer suspends the Contractor's operations for 60 or more consecutive calendar days through no fault of the Contractor, and there are no outstanding obligations.  The Contracting Officer shall return the ContractorContractor's blanket payment guarantee within 60 calendar days of contract closure.

3.  Downpayment - The Contractor agrees to make a downpayment in cash in the amount shown on Page 1.  This payment must be made by the time the contract is required to be executed and returned by the Contractor.  The downpayment may not be used for any other purpose, transferred to other sales, or refunded until stumpage value representing 25 percent of the total sale value of the sale has been shown as paid for, cut and removed on the statement of account, except that total deposits for downpayment and Included Timber will not be required in excess of total sale value.  The Contractor's failure to make the downpayment within the required time constitutes repudiation of this contract.  The Contracting Officer may terminate the contract and assess damages pursuant to SECTION 1 of the attached Service Contract..

When, pursuant to SECTION F or SECTION C of the attached Serice Contract, the Contracting Officer requests the Contractor to interrupt or delay all or any portion of the Contractor's operations under this contract for more than 60 consecutive days, the Contracting Officer may temporarily reduce the downpayment amount being held on deposit upon the written request of the Contractor or at the Contracting Officer's discretion.  For the period of the interruption or delay, the Contracting Officer may reduce the downpayment on deposit to $1,000 or 2 percent of the downpayment amount listed on Page 1, whichever is larger.  Upon the Contractor's receipt of the bill for collection and written notice from the Contracting Officer that the basis for the interruption or delay no longer exists, the Contractor shall restore the downpayment to the full amount shown on Page 1 within 30 days after the bill for collection's date of issue.  The Contractor shall not resume contract operations until the downpayment amount is fully restored.  The Contractor's failure to restore the downpayment is a breach of the contract under SECTION F of the attached Service Contract and if the Contractor fails to remedy the breach the Contracting Officer may terminate this contract and shall assess damages pursuant to SECTION I of the attached Service Contract.

4.  Periodic Payments - The Contractor shall make periodic payments as listed on

Page 1.  If the Contractor's total stumpage payments do not equal or exceed the amount required on the date due, the Contractor shall make a periodic payment for the amount of the difference.  A periodic payment is not required if the Contractor's total stumpage payments exceed the amount required on the date due.  Periodic payments may be used as a deposit in the Contractor's timber sale account to pay charges for timber released for cutting.  The Contractor may use only cash to meet this obligation.

The Contracting Officer shall adjust the periodic payment schedule dates, if they have not been reached, when a contract term adjustment pursuant to SECTION F or a Market-related Contract Term Addition pursuant to SECTION F of the attached Service contract has been granted.  The Contracting Officer shall adjust the dates for a period of time equal to the period of time granted for the contract term adjustment or Market-related Contract Term Addition.  The Contracting Officer may not adjust the periodic payment schedule dates when a contract term extension is granted pursuant to SECTION F - TIMBER SALE CONTRACT EXTENSION of the attached Service Contract.

The Contractor's failure to make a periodic payment within the required time is a breach of the contract under SECTION F of the attached Service Contract and if the Contractor fails to remedy the breach, the Contracting Officer may terminate this contract and shall assess damages pursuant to SECTION I of the attached Service Contract.

5.5# - USE OF TIMBER.  (8/98)  This contract is subject to the Forest Resources Conservation and Shortage Relief Act of 1990, as amended (16 U.S.C. 620, et seq.).

Except for NONE determined pursuant to public hearing to be surplus, unprocessed Included Timber shall not be exported from the United States nor used in direct or indirect substitution for unprocessed timber exported from private lands by the Contractor or any person as defined in the Act (16 U.S.C. 620e).

Timber in the following form will be considered unprocessed:  (a) trees or portions of trees or other roundwood not processed to standards and specifications suitable for end product use; (b) lumber, construction timbers or cants intended for remanufacturing not meeting standards defined in the Act

(16 U.S.C. 620e); and (c) Aspen or other pulpwood bolts exceeding 100 inches in length.

Unless the Contracting Officer and the Contractor otherwise agree in writing, unprocessed Included Timber shall be delivered to a domestic processing facility and shall not be mixed with logs intended for export.

Prior to award, during the life of this contract, and for a period of 3 years from Termination Date, the  Contractor shall furnish to the Contracting Officer, upon request, records showing the volume and geographic origin of unprocessed timber from private lands exported or sold for export by the Contractor or the Contractor's affiliates.

Prior to delivering unprocessed Included Timber to another party, the Contractor shall require each buyer, exchangee, or recipient to execute an acceptable agreement, which shall:  (a) identify the Federal origin of the timber, (b) specify domestic processing for the timber involved, (c) require the execution of such agreements between the parties to any subsequent transactions involving said timber, (d) require that all hammer brands and/or yellow paint must remain on logs until they are either legally exported or domestically processed, whichever is applicable, and (e) otherwise comply with the requirements of the Act (16 U.S.C. 620d).

No later than 10 days following the execution of any such agreement between the Contractor and another party, the Contractor shall furnish to the Contracting Officer a copy of each such agreement.  The Contractor shall retain, for 3 years from the Termination Date, the records of all sales, exchanges, or dispositions of all Included Timber.

The Regional Forester may terminate this contract pursuant to Standard Provision 18 for the Contractor's breach under this provision and take such other action as may be provided by statute or regulation, including the imposition of penalties.  When the Regional Forester terminates this contract under this provision the Forest Service will not be liable for any claim submitted by the Contractor relating to the termination.

7.1#  - TIMBER SUBJECT TO AGREEMENT.  (8/98)  In addition, there is within Sale Area an unestimated quantity of material meeting Sawlog and Miscellaneaous Convertible Products specifications which shall be Included Timber upon the written agreement of the Contracting Officer and the Purchaser.

7.2# - SCALING SERVICES.  (8/98)  Scaling services shall be provided and performed by Forest Service personnel or parties under contract to the Forest Service in accordance with the instructions and specifications listed below.  The Contracting Officer shall exclusively select the Scaling services provided.

Contract Scaling Deposits.  In the event the Forest Service enters into contracts with another party to provide Scaling services, the Purchaser shall make Required Deposits in cash to the Contracting Officer for such contract Scaling services at rates stated in 7.21# - Scaling Services Deposit Schedule. The Purchaser shall make such deposits in advance of Scaling.  By written notice, the Contracting Officer may adjust such rates to reflect redetermined costs, provided that such rates may not increase by more than ten percent during the original term of this contract.

Purchaser's Required Deposits for contract Scaling services shall include all costs sufficient to pay for Scaling services, including but not limited to:  contract preparation and supervision, Scaling, check Scaling, data processing, facility maintenance and other Forest Service overhead expenses.  By written agreement of the Contracting Officer, and pursuant to the Purchaser's operating plan and annual operating schedule, the Purchaser may pay deposits for Scaling services in total or deposits may be based on the estimated quantities of timber to be scaled in not less than 30 calendar days and not more than 60 calendar days, unless the Purchaser's production exceeds haul estimates.  The Purchaser's failure to make advanced deposits when due shall be a material breach of contract under Standard Provision 10.  The Contracting Officer shall make refunds to the Purchaser after Scaling is completed pursuant to Standard Provision 9.

Scaling Location.  Forest Service shall provide Scaling services at the following Scaling

site(s): Bar J Scales, 1.5 miles off Lassen County Road A3 on Lassen County Road 311.  The Scaling site(s), normally will be a non-exclusive site where more than one National Forest timber sale Purchaser may be served.

The Purchaser may request, in writing, to the Contracting Officer an alternate Scaling site, such as at a private mill yard, private truck ramp, or a privately operated log transfer facility.  The Contracting Officer may approve an alternate Scaling site when the Contracting Officer determines that existing conditions ensure that Scaling at an alternate site is acceptable.  Such conditions shall include at a minimum:  (a) scaler safety and comfort; (b) product accountability and security; (c) conditions conducive to accurate and independent Scaling; and (d) remote check Scaling.  Upon the Contracting Officer's written approval of an alternate Scaling site, the Contracting Officer and the Purchaser shall enter into a written memorandum of agreement governing Scaling at that alternate location.  The Purchaser agrees that Scaling services at an alternative Scaling site shall be performed by Forest Service personnel or persons under contract with the Forest Service.  In no instance shall Scaling services be performed by the Purchaser or employees of the Purchaser.

Definitions.  Scaling services may be Continuous, Intermittent, or Extended.  "Continuous Scaling Services" is Scaling at one site five eight-hour shifts a week, exclusive of Sundays and Federal holidays designated by statute.  "Intermittent Scaling Services" are non-continuous Scaling services.  "Extended Scaling Services" are Scaling services exceeding Continuous Scaling Services, and may include Sundays and designated Federal holidays.

Other Services.  Upon written request of Purchaser, the Contracting Officer may approve the Forest Service providing other services, such as but not limited to grading, tagging or marking of scaled logs.

Interrupted or Delayed Services.  In the event Scaling services are interrupted or delayed, the Contracting Officer shall provide written notification to the Purchaser and the Purchaser shall suspend the Purchaser's operations.  The Purchaser agrees that in the event such an interruption or delay occurs for reasons not caused by the Purchaser, its sole and exclusive remedy shall be (a) contract term adjustment pursuant to Standard Provision 3, or (b) when such an interruption or delay exceeds 30 days during Normal Operating Season, contract term adjustment pursuant to Standard Provision 3, plus out-of-pocket expenses involved in acquiring and holding the contract such as maintaining performance bonds and cash deposits incurred as a direct result of the interruption or delay of Scaling services under this provision.  Out-of-pocket expenses apply only when the Forest Service provides Scaling services and do not include lost profits, attorney's fees, replacement cost of timber, or any other anticipatory losses suffered by the Purchaser.  The Purchaser agrees to provide receipts or other documentation to the Contracting Officer which clearly identifies and verifies actual expenditures.  The Purchaser further agrees that no log hauling shall be conducted outside agreed upon Scaling services scheduled.

SCALING SPECIFICATIONS

|  | Trim Allowance |
| --- | --- |
| Species | Product | Unit of Measure | Maximum Scaling Length (feet) | Diameter Range (inches) | Length Range (feet) | Trim Allowance (inches) |

7.21# - SCALING SERVICES DEPOSIT SCHEDULE (11/99)  Purchaser shall make deposits for Scaling Services to the Forest Service under Standard Provision 9 at the following rate(s):

Standard Rate 	Premium Rate

Scaling Services:	$_N/A__ per load.	$_N/A_ per load

Weighing Services:	$_27.56 per load.

When Purchaser requests scaling services outside normal working hours, Saturdays, Sundays or the listed holidays and the Forest Service agrees, scaling deposits will be paid at the premium rate of 1.5 X the contract scaling rate plus overhead:

Normal working hours are Monday - Friday between 6:00 a.m. and 8:00 p.m.

Holidays:

New Years Day 	Labor Day

Martin Luther King's Birthday 	Columbus Day

Washington's Birthday	Veteran's Day

Memorial Day 	Thanksgiving Day

Independence Day 	Christmas Day

Attachment A

WORKSHEET TO DETERMINE SCALING COSTS

SALE NAME:  PRATTVILLE FOREST RECOVERY DFPZ

Original Worksheet: [ X ]        Revised Worksheet: [   ]

Instructions:  Use for estimating scaling costs to be included in 7.21# - Scaling Services Deposit Schedule and for adjusting scaling costs, if applicable, to reflect actual scaling costs and indirect cost assessment.

SALE INFORMATION:

1.  Estimated scaled volume  100%                                                       	33,629 GT

2.  Average volume/load			                                             	       25 GT

3. Estimated number of loads for the timber sale	                                           	  1,345 loads

4.  Check scale:  Frequency = 1 check scale per month, per scale

to equal 2% of total volume scaled for sale                                                       	$  0.00/load

5.  Facility maintenance:  Upgrading existing truck ramp or establishing temporary ramp at A-14 	$  0.00/load

| Item | $/Month | No of Months | Total |
| --- | --- | --- | --- |
| Office Trailer |  |  |  |
| Generator |  |  |  |
| Portable Toilet |  |  |  |
| Set-Up / Breakdown |  |  |  |
| TOTAL |  |  |  |

6.  Indirect cost assessment (%)      	  (check with your forest)	$          .20

CALCULATION FOR THE SALE:

7.  Estimated or actual bid rates for scaling (based on which (HIGHEST BID)

contractor will likely accept or has accepted delivery order):                                                         $ 15.45/load

8. Check Scaling Costs (Line 4)		                                           $  0.00/load

9.  Weight Scaling Cost:  Cost of weighing load (if applicable)

at A-14 location or an alternate location requiring payment for

weigh services.  (Use only when weight scaling is required and

Forest Service is paying with funds collected through C6.811).                                                   	   7.00 /load

10.  Facility Maintenance (Line 5)			$   0.00/load

11.  Bid rate PLUS indirect cost assessment (Line 7 / (1.0-16%)     	 $ 18.39/load

a. Estimated or actual cost per load for indirect cost assessment

collection (Line 11 - 7).                                                            	$  5.11/load

12.  Total estimated cost (included in C6.811) or actual cost per

load charged to purchaser (Lines 8 + 9 + 10 + 11a)	    	$ 27.56/load

13.  Estimated total cost for scaling for timber sale

(Line 12 X Line 3 =)				$ 37,068.20

INITIAL ADVANCE SCALING DEPOSITS REQUIRED FROM PURCHASER:1

14. Estimated advance deposit required for 60 days production prior to hauling.  Based on Purchaser's Plan of

Operations, calculate the following:

00  loads/day X 22 days/month X 2 months = total # loads 60 days  	          000

Estimated total value of deposit = Line 12 X Line 14 =	   $   N/A

7.3 - WEIGHING SERVICES.  (8/98)  Weighing services for stumpage payment purposes may be provided by either public or privately owned and operated weighing facilities.  A Weighing Services Agreement, approved by the Forest Supervisor, must be executed at each weighing facility providing weighing services.

Scales used to weigh National Forest products for stumpage payment purposes must be a currently certified scale in accordance with State law and be capable of weighing the entire load of products in a single operation.  The weighing of less than the entire load is prohibited.  Unless the Contracting Officer agrees in writing otherwise, the minimum sized weighing facility shall be a 60-ton capacity scale with a 10' x 70' platform or larger.  The weightmaster must work in a position where it is possible to verify that the truck wheels are on or off the scales.

Weighbeam facilities shall meet the following minimum requirements:

(a) be an electronic design;

(b) use electronic load cells or have a fully enclosed and sealed weighbeam;

(c) have digital weight meters sealed with  a seal approved by the State;

(d) have a zero interlocking device on the printer;

(e) have an automatic zeroing setting mechanism;

(f) have an automatic motion detecting device;

(g) be shielded against radio or electromagnetic interference; and

(h) have a date and time stamp which prints with each weighing.

The Purchaser shall bear all charges or fees for weighing services.

7.4# - THIRD PARTY SCALING SERVICES.  (8/98)  Notwithstanding the requirement for Forest Service or parties under contract to Forest Service to provide scaling services under Special Provision 7.2, scaling designated in the table below shall be conducted by a Third Party Scaling Organization (TPSO) approved by the Contracting Officer.  Scaling shall be done in accordance with Special Provision 7.2# and the Purchaser shall bear costs for the scaling service.

In the event the Third Party Scaling Service is suspended for causes such as strike(s), the Forest Service's termination of the third party's approval to scale National Forest System logs, or the Purchaser's failure to pay third party scaling costs, Purchaser's hauling operations shall be suspended until the Contracting Officer agrees, in writing, to alternate scaling services or service by a third party is resumed.

When an approved alternate scaling location, pursuant to Special Provision 7.2, does not have an approved third party scaling organization as a commonly used scaling services provider, the Forest Service or parties under contract to the Forest Service shall provide scaling services at the approved alternate location.  In such an event the cost of waived the third party scaling listed in table below shall be charged to the timber sale account.

If the Contracting Officer and the Purchaser agree in writing that scaling will be performed by another party under contract to the Forest Service, the Purchaser's Timber Sale Account will be charged for such scaling pursuant to Special Provision 7.2.

| Species | Product | Unit of Measure | Site and Geographic Location | Standard Method | Estimated Cost Per Unit $ |
| --- | --- | --- | --- | --- | --- |

7.5 (OPTION 1) - PRODUCT IDENTIFICATION.  (8/98)  Before removal from the Sale Area, unless the Contracting Officer determines that circumstances warrant a written waiver or adjustment, (a) all products 8 feet or more in length and one-third or more sound shall be hammer branded on each end that is 7 inches or more in diameter and (b) all domestic processing products 8 feet or more in length and one-third or more sound shall be painted with a spot of highway-yellow paint on each end that is 7 inches or more in diameter.   Each paint spot must be not less than 3 square inches in size.

Brands shall be assigned by the Contracting Officer and, if the Sale Area is within a State that maintains a log brand register, brands shall be registered with the State.  The Purchaser will furnish and apply highway-yellow paint of a lasting quality (oil-base or equivalent).

All hammer brands and/or highway-yellow paint must remain on logs until they are domestically processed.  If the identifying marks are lost, removed, or become unreadable, they shall be replaced.  The Purchaser may remanufacture products into different log lengths.  Except for logs remanufactured as part of the mill in-feed process immediately before processing, remanufactured products must be rebranded with the assigned sale brand and repainted with highway-yellow paint, unless otherwise agreed to in writing by the Contracting Officer.  For such remanufactured products, the Contracting Officer may approve use of a brand to be used exclusively as a catch brand, in lieu of the assigned sale brand.?

7.6 - LOG ACCOUNTABILITY.  (11/99)  Forest Service and Purchaser shall agree upon the haul route(s) prior to use.  All products removed from Sale Area shall be transported over the designated route of haul.  If products are removed in log form using conventional logging trucks, follow instructions on the inside cover of product removal permit for attaching permit to the load.  If purchaser elects to use chip vans, dump trucks or vehicles other than conventional logging trucks, the following additional requirements shall apply:

Product removal permits shall be stapled to a piece of wood or similar material attached to the lower front corner of the van or other non-conventional trailer or dump, on the drivers side.

Purchaser shall:

(a)  Assign a competent individual to insure form R5-2400-41, product removal permit, is completely and accurately filled out.  Require truck drivers to sign the stub of a completed product removal permit, assure permit is attached to the load as indicated on the inside cover of the product removal permit book, prior to removal from the Sale Area and while in transit to the scaling location.

(b)  Inform all drivers of their responsibilities and assure that drivers have access to form R5-2400-219, Off-loaded or Lost Log(s) Report, at all times during the haul.

(c)  Require truck drivers to complete form R5-2400-219 at the time and location logs are lost or off-loaded.  Upon arrival at scaling location, the truck driver shall staple the form to the scaler's copy of the product removal permit or otherwise deliver to the scaler.

(d)  Require truck drivers to stop for transportation inspections, if requested by Forest Service, for the following reasons:

(1)  For accountability checks when products are in transit from Sale Area to the designated scaling location.

(2)  For a remote check scale when products are in transit after being truck scaled at the designated scaling location.

(e)  Inform truck drivers of the designated route(s) of haul, the agreed upon location(s) for transportation inspections, the method of alerting drivers of an impending stop, and the fact that loads may be inspected at other locations where it is safe and possible to do so.

(f)  Require truck drivers to report to Purchaser instances when the load will be delayed in transit for more than 24 hours.  Purchaser in turn shall promptly notify Forest Service of delayed loads by product removal permit number and reason for the delay.  Routine delays may be approved by Forest Service in writing in advance, provided the location of the delayed truck load is specified.

Purchaser shall arrange for notice of off-loaded or lost logs by the scaling organization.  Purchaser shall notify Forest Service of off-loaded or lost log(s) and their location within 24 hours of such loss.  The scaler shall attach form R5-2400-219 to the Ranger District's copy of the scale ticket along with the scaler's copy of the Product removal permits.

In the event Purchaser's branded and unreported logs are found by Purchaser, Purchaser will notify the Forest Service and/or cooperate and participate in an investigation to determine the reason the log was not reported as required.

Locations for accountability checks shall be established by agreement between Purchaser and Forest Service in advance of haul.  Such locations shall be only in areas where trucks can be safely stopped and parked.

Remote check Scale locations shall be established by agreement between Forest Service and Purchaser in areas where it is safe to stop trucks and scale logs.

7.7 - SCALING LOST PRODUCTS.  (8/98)  The Contracting Officer or designee shall determine the volume of lost products by the best methods currently available, using data from the records for the period in which the loss occurred or the most applicable period if loss should occur substantially after cutting.  In the absence of specific information indicating size or species of lost truck loads, lost loads will be deemed to have a scale volume and species composition equal to that of the highest value load scaled during the report period.  Individual products shall be assumed to be the same as that of the average volume of the highest priced species scaled during the report period.  No payment for lost products may be required if the Contracting Officer or designee determines that the volume involved is small and justified by existing conditions.

7.8 - SCALING LOST SAMPLE LOADS.  (8/98)  If loads of logs selected to be sample scaled are placed in the decks before they are scaled, they will be considered lost sample loads.  It will be difficult if not impossible, to determine the volume and species contained in such loads for payment purposes.  Therefore, lost sample loads will be deemed to have a scale volume and species composition equal to that of the highest value load scaled during the sampling period as determined by the Contracting Officer or designee.  If no sample loads were scaled during the period, the scale data for the high valued load will be taken from the most current preceding sampling period with scale.  Sample loads lost as a result of Forest Service actions shall be treated as non-scaled loads.

EXHIBIT C

### Wet Haul Conditions

The following is a supplement to the Road Maintenance and Erosion Control item (C.2.3.1).  It is intended as a set of operating conditions for the use of roads during wet periods within the normal operating season (June 1 through November 15).  Roads are a forest improvement and are protected under C.3  "Resource Protection Standards."

A.  Haul may be allowed when:

1.  The haul route from the unit to the paved road is stabilized with sufficient aggregate to support haul under evaluated conditions.

2.  Earth surfaced roads must be dry enough to be bladed and shaped to maintain proper drainage.  This may be necessary quite frequently, depending on road conditions and pending storms.

3.  If the road is in a condition acceptable for drainage and it is frozen.

B.  Haul shall not be allowed when:

1.  The road is stabilized with aggregate, but the subgrade becomes saturated and the stability of the road prism cannot support the haul.

2.  When native surface roads turn to mud and cannot be immediately shaped for drainage.

3.  If sections of roads lose structural strength and will not support haul.

4.  When sediment is draining from the roadway and entering a streamcourse.

C.  Other than haul traffic:

1.  In some instances, crew traffic may alter the designed road drainage through minor rutting.  Minor rutting is defined as the travelway being rutted to a depth less than or equal to two (2) inches over less than 10% of the length of the road (measured on a mile by mile basis).  When this occurs, the purchaser will be required to install temporary waterbars to maintain drainage on the road.  This will be done on a daily basis if melting and run-off is occurring.   If this traffic is causing road resource damage or sediment to enter a streamcourse, crews shall find alternate ways of reaching the area.

D.  General

1.  If Contractor removes snow from roads, such work shall be done in a manner that will protect roads and adjacent resources.

2.  Snow berms shall be removed or placed to avoid accumulation of melt water on the road and prevent water concentration on erosive slopes or soils.  If the road surface is damaged, Contractor shall replace lost surface material and repair structures damaged in blading operations prior to hauling, unless climatic conditions prevent necessary work from being accomplished.

3.  Single lane roads shall be plowed full width including turnouts.  In event double lane roads are not plowed to full width, warning signs shall be required and plowing shall be no less than single lane (12 feet) with intervisible turnouts.

4. Snow removals to two (2) to four (4) inches above road surface may be permitted.  Road surface shall not be removed by plowing.  Any damage or loss of road surface shall be replaced or repaired.  Drainouts shall be provided at 100 to 200 foot intervals or as designated on the ground.

5.  Trucks shall track over the entire road surface to disperse water run-off.

6.  Temporary cross drains may be required in advance of predicted storms or warm fronts.

7.  Large puddles shall be drained.

8.  Ditches and culverts shall be maintained so they will be functional at all times.

EXHIBIT D

Subsoiling Specifications

Contractor shall subsoil landings unless otherwise agreed to by the Contracting Officer and the Contractor.  Subsoiling shall be accomplished by a winged subsoiler or other equipment that will lift and fracture the subsoil by vertical and lateral shattering, leaving the soil loosened through the full width and depth of the compacted layer with the topsoil remaining substantially in place rather than being inverted.  Subsoiling shall extend to a depth of 18 inches.  Forest Service may agree to lesser depths when excessive rock or other limiting site conditions are encountered.  Use of rock rippers shall not be permitted to accomplish subsoiling requirements.

EXHIBIT D-1

Marking Prescription for Control of Black Stain Root Disease in Unit 32D

General - Leave trees will be selected by the Forest Service from the dominant, codominant and intermediate crown classes.  Selected trees should be the best formed, disease/damage/defect free tress available.  Slightly damaged or disease trees may be left (not excessively damaged) when these are the healthiest trees available to meet stocking and spacing requirements.  Suppressed trees should not be marked for retention.  Spacing may be adjusted by up to 25%, in order to keep as many healthy trees as possible and to facilitate an irregular spacing pattern for visual quality objectives.

Markers should strive to maintain species diversity within the stand.  While leaving healthy trees should be a primary consideration, those species which are poorly represented will be generally be marked for leave, when all other things are considered equal.  These tree species include sugar pine, Douglas-fir, incense cedar, and white fir.  These trees may be found more commonly in the codominant crown classes, and they should be retained, when healthy, over ponderosa pine.  Douglas-fir in the intermediate crown classes should not be retained if it has low branching that would render DFPZ objectives less effective.

# Unacceptable trees

-  A live crown ratio of less than 30%

-  Fading, thinning, off-color foliage

-  Suppressed trees

-  Excessive damage, defect or disease infection

Blister Rust Infected – Sugar pine trees should be considered excessively diseased if they are bearing any visible blister rust cankers on the trunk or there are in excess of five branches with cankers.  Branch cankers can appear as ”flags” in which all the needles turn brown.

Black Stain Infected – Black stain is host-specific and is infecting only Ponderosa pine/Jeffrey pine trees in this stand.   Black stain centers typically start in a tree or stump and work outwards, spreading slowly in all directions.

Trees adjacent to these centers will show symptoms including chlorosis, fading crowns, and reduced needle length.  Trees continue to be infected through root contact, as well as through insect vectors, therefore, to minimize the spread in this manner, all ponderosa/Jeffrey pine trees within 60 feet (roots may extend the width of tree height) of a suspected center (dead and infected trees) will need to be removed.  There are numerous centers in this stand (at least 14 and up to 20).  These centers will likely overlap onto each other.  All other tree species may be retained in these centers, provided they do not hinder operations.

Immediately adjacent to the areas of complete removal, thinning will be initiated.  Spacing will be wider than normal, to 32’X 32’ spacing, to lessen root contact between infected trees.  This wide spacing “buffer” will extend for 200 feet surrounding the cut infection centers.  Thereafter, spacing will resume to a range of 18 to 32 ‘spacing, with an average of 25’ spacing.  Current spacing varies widely from 8X8’ to 16X16’.  Clumping is allowed only in the outermost thinning area.  Clumping up to 3 codominants and varying the spacing is acceptable when done in an effort to retain the best trees and to retain species diversity.  Be careful not to clump continuously as this defeats the purpose of thinning and may complicate timber-harvesting operations.

Elytroderma Infected – Ponderosa pine/Jeffrey pine – trees should be considered excessively infected if more than 60% of the crown is heavily infected.  Heavy infection appears as the current years needles are red or brown, and older infections create brooming similar to those seen in dwarf mistletoe infections, however they tend to be more compact and globulose.

Excessive damage – all species – broken tops in the lower two-thirds of the tree are characterized as excessively damaged and should not be considered as leave trees.

Defect – Forks and crook in the upper third of the tree are not classified as excessive.  These trees should only be left if no better formed trees exist within the specified distance.

### Snags and down logs guidelines:

### Snag retention

0-3 per acre in the primary corridor (1 to 2 tree heights in width)

Up to 8 of the largest snags per acre in the secondary zone

Down log retention

2 of the largest down logs per acre in the primary corridor

Up to 10-15 tons per acre of the largest logs

EXHIBIT E

FIRE PLAN FOR CONSTRUCTION AND SERVICE CONTRACTS

Sierra Cascade Province (07-20-00)

(Ref:  FSH 6309.32 and 6309.11)

- SCOPE:

The provisions set forth below outline the responsibility for fire prevention and suppression activities and establish an attack procedure for fires within the contract area.  The contract area is delineated by map in the contract.  The provisions set forth below also specify conditions under which contract activities will be curtailed or shut down.  See Section 5, Emergency Measures below.

2.	RESPONSIBILITIES:

# A.  Contractor

- Shall abide by the requirements of this Fire Plan.

(2) Shall take all steps necessary to prevent his/her employees, subcontractors and their employees from setting fires not required in completion of the contract, shall be responsible for preventing the escape of fires set directly or indirectly as a result of contract operations, and shall extinguish all such fires which may escape.

(3) Shall complete the Contractor's Plan Regarding Personnel, Equipment and organization (6.B) and shall furnish the Contracting Officer (CO) with a copy prior to commencing work at the site.  Shall currently advise the CO of any changes in personnel, equipment and organization as the changes occur.  Shall revise Section 6.B to reflect current activities upon request of the CO.

# B.  Forest Service

The Forest Service may conduct one or more inspections for compliance with the fire plan.  The number, timing, and scope of such inspections will be committed at the discretion of agency employees responsible for contract administration.  Such inspections do not relieve the Contractor of responsibility for correcting violations of the fire plan or for fire safety in general, as outlined in paragraph 2.A above.

3. 	 TOOLS AND EQUIPMENT:

- The Contractor shall comply with the following requirements:

  - Shall equip all diesel and/or gasoline-operated engines, both stationary and mobile, and all flues used in any contract and camp operations with spark arresters that meet Forest Service standards set forth in the National Coordinating Group publication for Multiposition Small Engines, #430-4, or General Purpose and Locomotive, #430-2.  Spark arresters are not required on equipment powered by exhaust-driven turbo-charged engines or motor vehicles equipped with a maintained muffler as defined in California Public Resources Code (CPRC), Section 4442 and 4443.

  - Shall furnish and have available for emergency use on each piece of equipment used in conjunction with performance of the work as listed below, hand tools and/or equipment as follows (CPRC 4427, 4428 and 4431):

(a) One shovel, one axe (or pulaski) and a fully charged fire extinguisher U.L. rated at 4 B:C or more on each truck, personnel vehicle, tractor, grader and other heavy equipment.

Contractor shall equip each mechanized harvesting machine with hydraulic systems, powered by an internal combustion engine (chipper, feller/buncher, harvester, forwarder, stroke delimber, etc), except tractors and skidders, with at least two 10 lb 4A/60B:C fire extinguishers or equivalent.  In addition, concentrations of wood dust and debris shall be removed from such equipment daily.

(b) One shovel and one back-pack 5 gallon water-filled tank with pump with each welder.

(c) One shovel and one chemical pressurized fire extinguisher (fully charged) for each gasoline-powered tool, including but not restricted to chain saws, soil augers, rock drills, etc.  Fire extinguishers shall be of the type and size set forth in the California Public Resources Code Section 4431.  Shovel must be kept within 100 feet from each chain saw when used off cleared landing areas.

  - All tools and equipment required in (1) and (2) above shall be in good workable condition and shall meet the following principle Forest Service specifications for fire tools:

    - Shovels shall be size "O" or larger and be not less than 46 inches in overall length.

    - Axes (or pulaskis) shall have 2-1/2 pound or larger heads and be not less than 28 inches in overall length.

  - Shall furnish a water tank truck or trailer, if so designated in Section 5.F.  Tank truck or trailer shall be located on or immediately adjacent to the contract area and meet the following minimum specifications:  Contain at least 300 gallons of water; a combination straight stream-fog nozzle with 300 feet of one inch fire hose with no segment longer than 50 feet; fire hose with nozzle closed shall be capable of withstanding 200 psi pump pressure without leaking, slipping of couplings, distortions, or other failures; nozzle discharge rating of six to 20 gallons per minute; a pump capable of delivering 23 gallons per minute at 175 pounds psi at sea level; power unit for pump shall have fuel for at least two hours operation, with ample transport available for immediate and safe movement of tank over roads serving the contract area; and shall be in good working order;  pump outlet shall be equipped with 1-1/2 inch National Standard Fire Hose thread.

  - Shall furnish two tractor headlights for each tractor dozer, if so designated in Section 5.G.  Tractor headlights shall be attachable to each tractor and served by an adequate power source.

B.  Forest Service  (1) Contracting Officer's Representative (COR) will deliver Government-furnished fire tool box to contract site and remove after completion and acceptance of the contract, if so designated in Section 5.C below.

4. 	GENERAL

A.  State Law.  The Contractor shall comply with all applicable laws of the State of California.  In particular, see California Public Resource Codes.

B.  Permits Required.  The Contractor must secure a special written permit from the District Ranger or designated representative before engaging in any of the activities listed below.  The terms and conditions of any of the permits required for this contract are as shown on copies attached to the Fire Plan.

(1) Blasting and Storage of Explosives and Detonators.  (Explosives Permit required by California Health & Safety Code, Section 12101.)

(2) Burning.

(3) Air Pollution.   (Issued by local State or County Air Pollution Control Districts, as applicable.)

(4) Camp, Lunch and Warming Fires.

(5) Welding and Cutting.

C.  Regulations for Burning.  Before setting any fires whatsoever, the Contractor shall notify the CO of his/her intentions.  Special care shall be taken to prevent scorching or causing any damage to adjacent structures, trees, and shrubbery.  Piles of material to be burned shall be of such size and so placed that during burning no damage shall result to adjacent objects.

D.  Smoking and Fire Rules.  Smoking shall not be permitted during fire season, except in a barren area or in an area cleared to mineral soil at least three feet in diameter (CPRC 4423.4).  In areas closed to smoking, the CO may approve special areas to be used for smoking.  These areas shall be signed by the Contractor. Contractor shall post signs regarding smoking and fire rules in conspicuous places for all employees to see.  Contractor's supervisory personnel shall require compliance with these rules. Under no circumstances shall smoking be permitted during fire season while employees are operating light or heavy equipment, or walking or working in grass and woodlands.

E.  Storage and Parking Areas.  Equipment service areas, parking areas, and gas and oil storage areas shall be cleared of all inflammable material for a radius of at least 50 feet.  Small mobile or stationary engine sites shall be cleared of inflammable material for a radius of at least 15 feet from such engine.  Areas of the type described above must be approved in writing by the CO.

F.  Welding.  Contractor shall confine welding activity to cleared areas having a minimum radius of ten feet measured from place of welding.

G.  Blasting.  Contractor shall use electric caps only.  When blasting is necessary in slash areas, a watchperson equipped with shovel and a water-filled backpack can (5 gallon) with hand pump shall remain in the immediate area for an hour after blasting has been completed.

H.  Oil Filter and Glass Jugs.  Contractor shall remove from National Forest land all oily rags and used oil filters.  Contractor shall prohibit use of glass bottles and jugs on contract operations.

I.  Reporting Fires.  As soon as feasible after initial control action is taken, Contractor shall notify Forest Service of any fires along roads used by Contractor.

J.   Communications.  If required in Section 5.I of these Fire Plan Requirements, Contractor shall furnish a serviceable telephone, radio-telephone, or radio system connecting each operation with the designated Forest Service Dispatch Center.  A radio-equipped fire patrolperson vehicle will satisfy this requirement if in operation during the time required.  The communication system shall provide prompt and reliable communications between the Contractor's operations and the Forest Service Dispatch Center.  The communications system shall be operable during Contractor's operation in the fire precautionary period and at the time fire patrolperson service is required.  The communications system shall be capable of contacting the designated Forest Service Dispatch Center within five (5) minutes of discovery of a fire in the Contractor’s operating area.

5.  EMERGENCY MEASURES

The table set forth below establishes work restrictions and fire precautions that the Contractor must observe at each activity level.

If so designated in paragraph 5.H. below, the Contractor shall install a weather station representative of conditions within the contract area for the purpose of determining the activity level.  If the Contractor installs a weather station, the Contractor shall determine and implement the appropriate activity level immediately after taking weather observations.

If the Contractor does not install a weather station, it shall obtain the activity level from the Forest Service before starting work each day.  If practicable, the Forest Service will determine the activity level for the following day by 4:00 each afternoon.  The activity level may be changed at any time if, in the judgment of the Forest Service, fire danger is higher or lower than predicted and the change is consistent with forest management objectives.  Whether to change the activity level and whether, when and how to take weather observations for that purpose are within the discretion of the Forest Service.

Activity  	Limitations or Requirements for Next Day Based on Predicted Activity Level

Level				or When Actual Activity Level is Measured

- Minimum required by state law.

- When the Activity Level shown under (1) of this Fire Plan is met or exceeded:

In addition to complying with the limitations and requirements for the preceding level, the Contractor shall:  Furnish fire patrolperson (if required under 5.E below).  Furnish tank truck or trailer (if required under 5.F below).

(3)	When the Activity Level shown under (2) of this Fire Plan is met or exceeded:

In addition to complying with the limitations and requirements shown for the preceding levels, the Contractor shall:  Stop all dead tree felling except when the 10-hour fuel stick measures 4 or less, and the relative humidity is 20 percent or less, equipment with a rotary cutting head shall only be operated with appropriate additional precautions approved by the District Fire Management Officer (FMO) and Contracting Officer (C.O.).

(4)	When the Activity Level shown under (3) of this Fire Plan is met or exceeded:

In addition to complying with the limitations and requirements shown for the preceding levels, the Contractor shall:  Stop all falling, limbing, bucking, skidding and other clearing and grubbing operations at 1:00 p.m. (local time).  Welding only by special permit.  No blasting after 10:00 a.m.  Open burning of any kind shall not be permitted at any time during the day.

(5)	When the Activity Level shown under (4) of this Fire Plan is met or exceeded:

In addition to complying with the limitations and requirements shown for the preceding levels, the Contractor shall:  Shut down all operations except as specifically permitted by written order of CO.  No welding, burning or blasting of any kind shall be permitted.  Roads may be watered, or dust oiled (does not include pit development).  Equipment at landings may be serviced.  Work in non-hazardous areas may continue if specifically permitted by written order of CO.

- The Contractor can obtain the Predicted Activity level for the following day at telephone number: (530) 573-2600.

B.    The Contractor (X) will (  ) will not be required to furnish a sealed box of fire fighting tools, to be located in the operating area, at a point accessible in the event of fire.  This box shall contain: one 5-gallon, backpack pump-type fire extinguisher filled with water; two axes; two Mcleod fire tools; one serviceable chain saw of three and one-half or more horsepower with a cutting bar 20 inches in length or longer; and enough shovels so that each employee at the operation can be equipped to fight fire.  The box shall remain unlocked, but be sealed with a Forest Service seal to be broken for emergency use only.

C.  The Forest Service (  ) will (X) will not furnish box of fire fighting tools, the contents of which is within the discretion of agency employees at the district level.  The Contractor shall ensure that the box remains unlocked but sealed with a Forest Service seal to be broken for emergency use only.  The Contractor will be responsible for keeping the box in the operating area, at a point accessible in the event of fire, and will return it to the government upon completion of the work.  The cost of replacing any shortage of tool inventory or loss or damage to the box will be withheld from the final contract payment due the Contractor.

D.  The Contractor (X) will (   ) will not be required to furnish a filled five gallon backpack pump at each work site at activity level 3 or above.

E.  The Contractor (X) will (  ) will not be required to furnish a fire patrolperson with a filled 5-gallon backpack pump to prevent, detect, and suppress any fires in the contract area.  The patrolperson shall remain on duty at least two hours after the close of work, at Activity Level 3 or above.  SUPPLEMENT:  The fire patrolperson (X) may (  ) may not perform other duties on the contract.

F.  The Contractor (X) will (  ) will not be required to furnish a water tank truck or trailer.  Water tank truck or trailer (  ) may (  ) may not be used for other work on the contract.

G.  The Contractor (X) will (  ) will not be required to furnish tractor headlights.

H.  The Contractor (X) shall (  ) may not install a fire weather station for obtaining Activity level.  The Forest Service shall designate the fire weather station location.  Instruments needed to obtain Activity level shall meet specifications and standards in Weather Station Handbook (Inter-agency Guide For Wildland Managers, March 1990 PMS 426-2 NFES 2140), which is available for inspection in the District Ranger's Office.  Observations shall be taken hourly, starting at 10:00 am.  When Activity Level 3 or above is predicted, additional observations shall be taken beginning at the time work starts.  Observations shall measure; relative humidity; 10-hour fuel stick; and wind speed.  Emergency precautions for the measured Activity level shall be implemented.  Records of weather measurements shall be maintained and shall be available to the Forest Service on request.

I.  The Contractor (X) will (  ) will not be required to furnish communications equipment.

- The appropriate fuel model(s) for this project is G at the Almanor weather station.

  - REPORTING ALL WILD FIRES

A.  Contractor's employees shall report all fires to any of the following Forest Service facilities and/or personnel listed below, but not necessarily in the order shown:

|  | Name | Office Address and/or telephone | Home address and/or telephone |
| --- | --- | --- | --- |
| Dispatch Center | SIFC ECC | (530) 252-1588 |  |
| Nearest FS Station | Almanor R.S. | (530) 258-2141 |  |
| Inspector |  |  |  |
| COR |  |  |  |
| District Ranger |  |  |  |
| D.R. Designated Rep |  |  |  |

When reporting a fire, provide the following information;

Your Name;

Call back telephone number;

Project name;

Location;

Legal description (Township, Range, Section); and

Descriptive location (Reference point);

Fire Information;

Acres;

Rate of Spread; and

Wind Conditions.

B.  Contractor's Plan Regarding Personnel, Equipment and Organization.   The Contractor shall, prior to commencing work, furnish the following information relating to key personnel, tools and equipment available for the purpose of fighting wild fires within and adjacent to the Contract Area:

(1)  Key Personnel:  (In order of call preferences)

| Title | Name | Address and/or telephone |
| --- | --- | --- |
| Fire Supervisor |  |  |
| Fire Patrolperson |  |  |

# (2)  Personnel and Equipment

|  | Number | Classification or Type, Make & Model |
| --- | --- | --- |
| Fire Fighters: |  |  |
| Fallers: |  |  |
| Power Saws: |  |  |
| Other Equipment: |  |  |

(3) Fire Suppression Plan:

Contractor's Signature                                                                           Date

Contracting Officer                                                                               Date

EXHIBIT F

Soil and Water Integrated Design Features and Best Management Practices

BMP 1.3 Use of Erosion Hazard Ratings for Timber Harvest Unit Design. The EHR for this project is LOW. Erosion control structures on skid trails should be based on this rating.

BMP 1.4 Use of Sale Area Maps for Designating Water Quality Protection Needs. Protection of Riparian Habitat Conservation Areas (RHCAs) has been identified by Project Foresters and the Forest Soil Scientist.

BMP 1.8 Streamside management zone designation. Buffers should be consistent with the SAT guidelines.

BMP 1.12 Log Landing Location:  Locate landings in such a way as to avoid creation of hazardous watershed conditions and resulting water quality degradation. Where possible re-use existing landings that do not adversely affect water quality. Scarify the surface of landings and spread any existing soil piles to restore soil infiltration and productivity.

BMP 1.13 Erosion Prevention and Control Measures During Timber Sale Operations. Ensure that Purchaser’s operations shall be conducted reasonably to minimize soil erosion.

BMP 1.17 Erosion Control on Skid Trails: To protect water quality by minimizing erosion and sedimentation derived from skid trails. Refer to Erosion Hazard Rating of LOW for distance between water bars.

BMP 1.19 Stream course Protection: This is to protect the natural flow of streams, to provide unobstructed passage of stormflows, to reduce sediment and other pollutants from entering streams, and to restore the natural course of any stream as soon as practicable if the stream is diverted as a result of timber management activities. RHCA buffer width requirement identified by the Scientific Analysis Team (SAT) Report (Viability Assessment and Management Considerations for Species Associated with Late-Successional and Old-Growth Forests of the Pacific Northwest, The Report of The Scientific Analysis Team, USDA Forest Service, March 1993).  Buffer strip distances were not modified during the watershed analysis.  The following interim guideline distances will be used:

  - Ponds, Reservoirs, and Wetlands Greater Than One Acre: The Riparian Habitat Conservation Area consists of the body of water (the maximum pool elevation of Lake Almanor) for 150 feet horizontal distance.

  - Seasonally Flowing or Intermittent Streams: Wetlands less than One Acre: This Riparian Habitat Conservation Area consists of the stream channel or wetland to 100 feet horizontal distance (200 feet, including both sides of the channel).

  - Permanently Flowing Non-fish-bearing Streams: The RHCA consists of the stream and the area on either side of the stream extending from the edges of the active stream channel for 150 feet horizontal distance.

BMP 2.26 Obliteration of Temporary Roads: To reduce sediment generated from temporary roads by obliterating them at the completion of their intended use. Temporary roads are constructed for a specific short-term purpose. In order to prevent continued low level casual use, such roads are obliterated at the completion of their intended use. Obliteration is achieved by the following:

  - Road is effectively drained and blocked.

  - Temporary culvert and natural drainage configuration is reestablished.

  - The road prism is returned to resource production through tillage, reshaping, and stabilization of side slopes as needed to prevent erosion and foster recovery.

  - Each temporary road should be treated in the manner described above at the end of its intended use and prior to the beginning of seasonal precipitation.

BMP 6.1 Fire and Fuel Management Activities:  One of the objectives of fire management is to reduce public and private losses which result from wildfires and or subsequent flooding and erosion, by reducing the frequency, intensity and destructiveness of wildfire.  Surface fuels that are treated through a combination of understory burning or jackpot burning will be performed in conjunction with applicable BMPs, which include BMP 1.22 Slash Treatment in Sensitive Areas. This protects meadows, wetlands, streamside zones and other sensitive areas.

BMP 7.1 Watershed restoration: To improve water quality and soil stability watershed restoration is a corrective measure to repair degraded watershed conditions and restore hydrologic balance with a vegetative cover. This will maintain or improve soil stability, reduce surface runoff, increase infiltration, and reduce flood occurrence and flood damage.

Maintain soil productivity by providing adequate soil cover to prevent accelerated sheet and rill erosion from occurring. The amount of material should not create adverse effects to fuels. (Should be consistent with Erosion Hazard documentation for soils.)

Maintain soil productivity by providing up to 5 downed logs per acre is maintained throughout the activity area.  Special emphasis should be placed on unit 32 since this area has minimal LWD and limited potential recruitment.

Maintain soil productivity by ensuring soils porosity is not adversely affected by operating while soils are wet and by minimizing the extent of disturbance. Forest Soil Scientist is available to review soil moisture prior to or during the contract as needed.

Require that all roads on lands managed by the Forest Service, including those operated by others, be maintained and operated in a manner consistent with the planned uses and with meeting Riparian Management Objectives. (SAT Guidelines)

Roads have been inventoried and evaluated in RHCAs. Through this interdisciplinary team review process, the influence of each road in an RHCA was identified and a prescription for closure, modification of road level or obliteration was identified. This is consistent with SAT guidelines RF-3 (pg 449).

Wage Determination 5 Pages

SECTION K - REPRESENTATIONS, CERTIFICATIONS, AND OTHER STATEMENTS

### OF OFFERORS OR RESPONDENTS

K.1  CERTIFICATE OF INDEPENDENT PRICE DETERMINATION (FAR 52.203-2)(APR 1985)

(a) The offeror certifies that--

(1) The prices in this offer have been arrived at independently, without, for the purpose of restricting competition, any consultation, communication, or agreement with any other offeror or competitor relating to--

(i) Those prices;

(ii) The intention to submit an offer; or

(iii) The methods or factors used to calculate the prices offered.

(2) The prices in this offer have not been and will not be knowingly disclosed by the offeror, directly or indirectly, to any other offeror or competitor before bid opening (in the case of a sealed bid solicitation) or contract award (in the case of a negotiated solicitation) unless otherwise required by law; and

(3) No attempt has been made or will be made by the offeror to induce any other concern to submit or not to submit an offer for the purpose of restricting competition.

(b) Each signature on the offer is considered to be a certification by the signatory that the signatory--

(1) Is the person in the offeror's organization responsible for determining the prices being offered in this bid or proposal, and that the signatory has not participated and will not participate in any action contrary to subparagraphs (a)(1) through (a)(3) of this provision; or

(2)(i) Has been authorized, in writing, to act as agent for the following principals in certifying that those principals have not participated, and will not participate in any action contrary to subparagraphs (a)(1) through (a)(3) of this provision ____________________ [insert full name of person(s) in the offeror's organization responsible for determining the prices offered in this bid or proposal, and the title of his or her position in the offeror's organization];

(ii) As an authorized agent, does certify that the principals named in subdivision (b)(2)(i) of this provision have not participated, and will not participate, in any action contrary to subparagraphs (a)(1) through (a)(3) of this provision; and

(iii) As an agent, has not personally participated, and will not participate, in any action contrary to subparagraphs (a)(1) through (a)(3) of this provision. (c) If the offeror deletes or modifies subparagraph (a)(2) of this provision, the offeror must furnish with its offer a signed statement setting forth in detail the circumstances of the disclosure.

K.2  CERTIFICATION AND DISCLOSURE REGARDING PAYMENTS TO INFLUENCE CERTAIN

FEDERAL TRANSACTIONS (FAR 52.203-11)(APR 1991)

(a) The definitions and prohibitions contained in the clause, at FAR 52.203-12, Limitation on Payments to Influence Certain Federal Transactions, included in this solicitation, are hereby incorporated by reference in paragraph (b) of this certification.

(b) The offeror, by signing its offer, hereby certifies to the best of his or her knowledge and belief that on or after December 23, 1989--

(1) No Federal appropriated funds have been paid or will be paid to any person for influencing or attempting to influence an officer or employee of any agency, a Member of Congress, an officer or employee of Congress, or an employee of a Member of Congress on his or her behalf in connection with the awarding of any Federal contract, the making of any Federal grant, the making of any Federal loan, the entering into of any cooperative agreement, and the extension, continuation, renewal, amendment or modification of any Federal contract, grant, loan, or cooperative agreement;

(2) If any funds other than Federal appropriated funds (including profit or fee received under a covered Federal transaction) have been paid, or will be paid, to any person for influencing or attempting to influence an officer or employee of any agency, a Member of Congress, an officer or employee of Congress, or an employee of a Member of Congress on his or her behalf in connection with this solicitation, the offeror shall complete and submit, with its offer, OMB standard form LLL, Disclosure of Lobbying Activities, to the Contracting Officer; and

(3) He or she will include the language of this certification in all subcontract awards at any tier and require that all recipients of subcontract awards in excess of $100,000 shall certify and disclose accordingly.

(c) Submission of this certification and disclosure is a prerequisite for making or entering into this contract imposed by section 1352, title 31, United States Code. Any person who makes expenditure prohibited under this provision or who fails to file or amend the disclosure form to be filed or amended by this provision shall be subject to a civil penalty of not less than $10,000, and not more than $100,000, for each such failure.

K.3  TAXPAYER IDENTIFICATION (FAR 52.204-3)(OCT 1998)

(a) Definitions.  Common parent, as used in this provision, means that corporate entity that owns or controls an affiliated group of corporations that files its Federal income tax returns on a consolidated basis, and of which the offeror is a member. Taxpayer Identification Number (TIN), as used in this provision, means the number required by the Internal Revenue Service (IRS) to be used by the offeror in reporting income tax and other returns.  The TIN may be either a Social Security Number or an Employer Identification Number.

(b) All offerors must submit the information required in paragraphs (d) through (f) of this provision to comply with debt collection requirements of 31 U.S.C. 7701(c) and 3325(d), reporting requirements of 26 U.S.C. 6041, 6041A, and 6050M, and implementing regulations issued by the IRS. If the resulting contract is subject to the payment reporting requirements described in Federal Acquisition Regulation (FAR) 4.904, the failure or refusal by the offeror to furnish the information may result in a 31 percent reduction of payments otherwise due under the contract.

(c) The TIN may be used by the Government to collect and report on any delinquent amounts arising out of the offeror's relationship with the Government (31 U.S.C. 7701(c)(3)). If the resulting contract is subject to the payment reporting requirements described in FAR 4.904, the TIN provided hereunder may be matched with IRS records to verify the accuracy of the offeror's TIN.

(d) Taxpayer Identification Number (TIN).

[ ] TIN:.

[ ]TIN has been applied for.

[ ] TIN is not required because:

[ ]Offeror is a nonresident alien, foreign corporation, or foreign partnership that does not have income effectively connected with the conduct of a trade or business in the United States and does not have an office or place of business or a fiscal paying agent in the United States;

[ ] Offeror is an agency or instrumentality of a foreign government;

[ ] Offeror is an agency or instrumentality of the Federal Government.

(e) Type of organization.

[ ] Sole proprietorship;

[ ] Partnership;

[ ] Corporate entity (not tax-exempt);

[ ] Corporate entity (tax-exempt);

[ ] Government entity (Federal, State, or local);

[ ] Foreign government;

[ ] International organization per 26 CFR 1.6049-4;

[ ] Other

(f) Common parent.

[ ] Offeror is not owned or controlled by a common parent as defined in paragraph (a) of this provision.

[ ] Name and TIN of common parent:

Name

TIN

K.4  CERTIFICATION REGARDING DEBARMENT, SUSPENSION, PROPOSED DEBARMENT, AND

OTHER RESPONSIBILITY MATTERS (FAR 52.209-5)(MAR 1996)

(a)(1) The Offeror certifies, to the best of its knowledge and belief, that--

(i) The Offeror and/or any of its Principals--

(A) Are ___ are not ___ presently debarred, suspended, proposed for debarment, or declared ineligible for the award of contracts by any Federal agency;

(B) Have ___ have not ___, within a three-year period preceding this offer, been convicted of or had a civil judgment rendered against them for: commission of fraud or a criminal offense in connection with obtaining, attempting to obtain, or performing a public (Federal, state, or local) contract or subcontract; violation of Federal or state antitrust statutes relating to the submission of offers; or commission of embezzlement, theft, forgery, bribery, falsification or destruction of records, making false statements, tax evasion, or receiving stolen property; and

(C) Are ___ are not ___ presently indicted for, or otherwise criminally or civilly charged by a governmental entity with, commission of any of the offenses enumerated in subdivision (a)(1)(i)(B) of this provision.

(ii) The Offeror has ___ has not ___, within a three-year period preceding this offer, had one or more contracts terminated for default by any Federal agency.

(2) "Principals," for the purposes of this certification, means officers; directors; owners; partners; and, persons having primary management or supervisory responsibilities within a business entity (e.g., general manager; plant manager; head of a subsidiary, division, or business segment, and similar positions).

This Certification Concerns a Matter Within the Jurisdiction of an Agency of the United States and the Making of a False, Fictitious, or Fraudulent Certification May Render the Maker Subject to Prosecution Under Section 1001, Title 18, United States Code.

(b) The Offeror shall provide immediate written notice to the Contracting Officer if, at any time prior to contract award, the Offeror learns that its certification was erroneous when submitted or has become erroneous by reason of changed circumstances.

(c) A certification that any of the items in paragraph (a) of this provision exists will not necessarily result in withholding of an award under this solicitation. However, the certification will be considered in connection with a determination of the Offeror's responsibility. Failure of the Offeror to furnish a certification or provide such additional information as requested by the Contracting Officer may render the Offer or nonresponsible.

(d) Nothing contained in the foregoing shall be construed to require establishment of a system of records in order to render, in good faith, the certification required by paragraph (a) of this provision. The knowledge and information of an Offeror is not required to exceed that which is normally possessed by a prudent person in the ordinary course of business dealings.

(e) The certification in paragraph (a) of this provision is a material representation of fact upon which reliance was placed when making award. If it is later determined that the Offeror knowingly rendered an erroneous certification, in addition to other remedies available to the Government, the Contracting Officer may terminate the contract resulting from this solicitation for default.

K.5  SMALL BUSINESS PROGRAM REPRESENTATIONS (FAR 52.219-1)(MAY 1999)

(a)(1) The standard industrial classification (SIC) code for this acquisition is 2411- Logging.

(2) The small business size standard is 500 employees.

(3) The small business size standard for a concern which submits an offer in its own name, other than on a construction or service contract, but which proposes to furnish a product which it did not itself manufacture, is 500 employees.

(b) Representations. (1) The offeror represents as part of its offer that it __ is, __is not a small business concern.

(2) [Complete only if the offeror represented itself as a small business concern in paragraph (b)(1) of this provision.] The offeror represents, for general statistical purposes, that it __is, __ is not, a small disadvantaged business concern as defined in 13 CFR 124.1002.

(3) [Complete only if the offeror represented itself as a small business concern in paragraph (b)(1) of this provision.] The offeror represents as part of its offer that it __is, __is not a women-owned small business concern.

(c) Definitions.

"Small business concern," as used in this provision, means a concern, including its affiliates, that is independently owned and operated, not dominant in the field of operation in which it is bidding on Government contracts, and qualified as a small business under the criteria in 13 CFR Part 121 and the size standard in paragraph (a) of this provision.

"Women-owned small business concern," as used in this provision, means a small business concern--

(1) Which is at least 51 percent owned by one or more women or, in the case of any publicly owned business, at least 51 percent of the stock of which is owned by one or more women; and

(2) Whose management and daily business operations are controlled by one or more women.

(d) Notice. (1) If this solicitation is for supplies and has been set aside, in whole or in part, for small business concerns, then the clause in this solicitation providing notice of the set-aside contains restrictions on the source of the end items to be furnished.

(2) Under 15 U.S.C. 645(d), any person who misrepresents a firm's status as a small, small disadvantaged, or women-owned small business concern in order to obtain a contract to be awarded under the preference programs established pursuant to section 8(a), 8(d), 9, or 15 of the Small Business Act or any other provision of Federal law that specifically references section 8(d) for a definition of program eligibility, shall--

(i) Be punished by imposition of fine, imprisonment, or both;

(ii) Be subject to administrative remedies, including suspension and debarment; and

(iii) Be ineligible for participation in programs conducted under the authority of the Act.

K.6  PREVIOUS CONTRACTS AND COMPLIANCE REPORTS (FAR 52.222-22)(FEB 1999)

The offeror represents that--

(a) It __ has, __ has not participated in a previous contract or subcontract subject the Equal Opportunity clause of this solicitation;

(b) It __ has,__ has not filed all required compliance reports; and

(c) Representations indicating submission of required compliance reports, signed by proposed subcontractors, will be obtained before subcontract awards.

K.7  AFFIRMATIVE ACTION COMPLIANCE (FAR 52.222-25)(APR 1984)

The offeror represents that--

(a) It __has developed and has on file, __has not developed and does not have on file, at each establishment, affirmative action programs required by the rules and regulations of the Secretary of Labor (41 CFR 60-1 and 60-2); or

(b) It __has not previously had contracts subject to the written affirmative action programs requirement of the rules and regulations of the Secretary of Labor.

K.8  MIGRANT AND SEASONAL AGRICULTURAL WORKER PROTECTION ACT REGISTRATION

In compliance with the Migrant and Seasonal and Agricultural Worker Protection Act (MSPA) (29 USC 1801-1872; 5 CFR 500), the offeror certifies that he/she:

___

|___|    Has been issued MSPA Registration Number

|___|    Has applied for a MSPA Registration Number.

|___|    Has not applied for a number.

|___|    Is not required to register because the offeror does not employ other than immediate family members.  (Parents, children, brothers and sisters.

Any employer who hires or anticipates hiring employees subject to MSPA and who anticipates bidding on a federal contract nor or in the future must submit an application to obtain a registration number.

Applications for a registration number should be made on Form WH-510 which is available at your State Employment Service Offices.  Questions concerning the application should be directed to the State Employment Office or the Department of Labor office, shown below.

California

U.S. Department of Labor (ESA)

Wage and Hour Division

71 Stevenson Street, Room 905

San Francisco, California 94105   (415) 975-4520

Completed forms should be mailed to the appropriate U.S. Department of Labor Office above.

A valid U.S. Department of Labor Registration Number must be supplied to the Contracting Officer prior to issuance of a "Notice to Proceed" with the work. Failure to provide such number within   10   days of award is grounds for termination of your contract.

#### K.9  EXPEREINCE & PAST PERFORMANCE QUESTIONNAIRE

The Offeror shall complete and submit the attached experience and past performance questionnaire.

Experience & Past Performance Questionnaire

1.  Firm Name/ Business Address:

2.  Year Present Firm Established:

3.  Name of Parent Company, if any:

4.  Principal Contact at Firm:  Name/ Title/ Telephone

- Work Experience, during the past 3 years, which best illustrates current qualifications relevant to this project.  For each project provide the following information;

  - Client’s name, address, & telephone number;

  - Description & location of work;

  - Dates of contract performance period;

  - Contract dollar amount; and

  - Client, Project Manager, or Contracting Officer who can verify your experience and provide a reference on the quality of your work.  Provide name and telephone number.

6.  All work currently under contract, or being performed, for Federal agencies, as a prime or subcontractor:

| Project Name & Location | Agency Name & Address and Project Manager's Name & Telephone Number | Percent Complete | Estimated Cost (In Thousands) |
| --- | --- | --- | --- |

7.  Use this space to provide any additional information supporting your firm's qualifications for the proposed project, including resources (e.g. equipment and personnel) available to accomplish the proposed tasks under this contract.

8.  The foregoing is a statement of fact.

Signature                                                                                             	Date:___________________

Typed Name & Title

SECTION L

### INSTRUCTIONS, CONDITIONS, AND NOTICES TO OFFERORS OR RESPONDENTS

L.1  DATA UNIVERSAL NUMBERING SYSTEM (DUNS) NUMBER (FAR 52.204-6)(JUNE 1999)

(a) The offeror shall enter, in the block with its name and address on the cover page of its offer, the annotation "DUNS" followed by the DUNS number that identifies the offeror's name and address exactly as stated in the offer. The DUNS number is a nine-digit number assigned by Dun and Bradstreet Information Services.

(b) If the offeror does not have a DUNS number, it should contact Dun and Bradstreet directly to obtain one. A DUNS number will be provided immediately by telephone at no charge to the offeror. For information on obtaining a DUNS number, the offeror, if located within the United States, should call Dun and Bradstreet at 1-800-333-0505. The offeror should be prepared to provide the following information:

(1) Company name.

(2) Company address.

(3) Company telephone number.

(4) Line of business.

(5) Chief executive officer/key manager.

(6) Date the company was started.

(7) Number of people employed by the company.

(8) Company affiliation.

(c) Offerors located outside the United States may obtain the location and phone number of the local Dun and Bradstreet Information Services office from the Internet home page at http://www.customerservice@dnb.com. If an offeror is unable to locate a local service center, it may send an e-mail to Dun and Bradstreet at globalinfo@mail.dnb.com.

L.2  SUBMISSION OF OFFERS IN THE ENGLISH LANGUAGE (FAR 52.214-34)(APR 1991)

Offers submitted in response to this solicitation shall be in the English language. Offers received in other than English shall be rejected.

L.3  SUBMISSION OF OFFERS IN U.S. CURRENCY (FAR 52.214-35)(APR 1991)

Offers submitted in response to this solicitation shall be in terms of U.S. dollars. Offers received in other than U.S. dollars shall be rejected.

L.4  INSTRUCTIONS TO OFFERORS--COMPETITIVE ACQUISITION (FAR 52.215-1)(FEB 2000)

(a) Definitions. As used in this provision--

"Discussions" are negotiations that occur after establishment of the competitive range that may, at the Contracting Officer's discretion, result in the offeror being allowed to revise its proposal.

"In writing" or "written" means any worded or numbered expression which can be read, reproduced, and later communicated, and includes electronically transmitted and stored information.

"Proposal modification" is a change made to a proposal before the solicitation's closing date and time, or made in response to an amendment, or made to correct a mistake at any time before award.

"Proposal revision" is a change to a proposal made after the solicitation closing date, at the request of or as allowed by a Contracting Officer as the result of negotiations.

"Time," if stated as a number of days, is calculated using calendar days, unless otherwise specified, and will include Saturdays, Sundays, and legal holidays. However, if the last day falls on a Saturday, Sunday, or legal holiday, then the period shall include the next working day.

(b) Amendments to solicitations. If this solicitation is amended, all terms and conditions that are not amended remain unchanged. Offerors shall acknowledge receipt of any amendment to this solicitation by the date and time specified in the amendment(s).

(c) Submission, modification, revision, and withdrawal of proposals. (1) Unless other methods (e.g., electronic commerce or facsimile) are permitted in the solicitation, proposals and modifications to proposals shall be submitted in paper media in sealed envelopes or packages (i) addressed to the office specified in the solicitation, and (ii) showing the time and date

specified for receipt, the solicitation number, and the name and address of the offeror. Offerors using commercial carriers should ensure that the proposal is marked on the outermost wrapper with the information in paragraphs (c)(1)(i) and (c)(1)(ii) of this provision.

(2) The first page of the proposal must show--

(i) The solicitation number;

(ii) The name, address, and telephone and facsimile numbers of the offeror (and electronic address if available);

(iii) A statement specifying the extent of agreement with all terms, conditions, and provisions included in the solicitation and agreement to furnish any or all items upon which prices are offered at the price set opposite each item;

(iv) Names, titles, and telephone and facsimile numbers (and electronic addresses if available) of persons authorized to negotiate on the offeror's behalf with the Government in connection with this solicitation; and

(v) Name, title, and signature of person authorized to sign the proposal.  Proposals signed by an agent shall be accompanied by evidence of that agent's authority, unless that evidence has been previously furnished to the issuing office.

(3)  Submission, modification, revision, and withdrawal of proposals.  (i) Offerors are responsible for submitting proposals, and any modifications, or revisions, so as to reach the Government office designated in the solicitation by the time specified in the solicitation.  If no time is specified in the solicitation, the time for receipt is 4:30 p.m., local time, for the designated Government office on the date the proposal or revision is due.

(ii)(A) Any proposal, modification, or revision, or received at the Government office designated in the solicitation after the exact time specified for receipt of offers is "late" and will not be considered unless it is received before award is made, the Contracting Officer determines that accepting the late offer would not unduly delay the acquisition; and

(1) If it was transmitted through an electronic commerce method authorized by the solicitation, it was received at the initial point of entry to the Government infrastructure not later than 5:00 p.m. one working day prior to the date specified for receipt of proposals; or

(2) There is acceptable evidence to establish that it was received at the Government installation designated for receipt of offers and was under the Government's control prior to the time set for receipt of offers; or

(3) It is the only proposal received.

(B) However, a late modification of an otherwise successful proposal that makes its terms more favorable to the Government will be considered at any time it is received and may be accepted.

(iii) Acceptable evidence to establish the time of receipt at the Government installation includes the time/date stamp of that installation on the proposal wrapper, other documentary evidence of receipt maintained by the installation, or oral testimony or statements of Government personnel.

(iv) If an emergency or unanticipated event interrupts normal Government processes so that proposals cannot be received at the office designated for receipt of proposals by the exact time specified in the solicitation, and urgent Government requirements preclude amendment of the solicitation, the time specified for receipt of proposals will be deemed to be extended to the same time of day specified in the solicitation on the first work day on which normal Government processes resume.

(v) Proposals may be withdrawn by written notice received at any time before award.  Oral proposals in response to oral solicitations may be withdrawn orally.  If the solicitation authorizes facsimile proposals, proposals may be withdrawn via facsimile received at any time before award, subject to the conditions specified in the provision at 52.215-5, Facsimile Proposals.  Proposals may be withdrawn in person by an offeror or an authorized representative, if the identity of the person requesting withdrawal is established and the person signs receipt for the proposals before award.

(4) Unless otherwise specified in the solicitation, the offeror may propose to provide any item or combination of items.

(5)  Offerors shall submit proposals in response to this solicitation in English, unless otherwise permitted by the solicitation, and in U.S. dollars, unless the provision at FAR 52.225-17, Evaluation of Foreign Currency Offers, is included in the solicitation.

(6) Offerors may submit modifications to their proposals at any time before the solicitation closing date and time, and may submit modifications in response to an amendment, or to correct a mistake at any time before award.

(7) Offerors may submit revised proposals only if requested or allowed by the Contracting Officer.

(8) Proposals may be withdrawn at any time before award. Withdrawals are effective upon receipt of notice by the Contracting Officer.

(d) Offer expiration date. Proposals in response to this solicitation will be valid for the number of days specified on the solicitation cover sheet  (unless a different period is proposed by the offeror).

(e) Restriction on disclosure and use of data. Offerors that include in their proposals data that they do not want disclosed to the public for any purpose, or used by the Government except for evaluation purposes, shall--

(1) Mark the title page with the following legend:

This proposal includes data that shall not be disclosed outside the Government and shall not be duplicated, used, or disclosed--in whole or in part--for any purpose other than to evaluate this proposal. If, however, a contract is awarded to this offeror as a result of--or in connection with--the submission of this data, the Government shall have the right to duplicate, use, or disclose the data to the extent provided in the resulting contract. This restriction does not limit the Government's right to use

information contained in this data if it is obtained from another source without restriction. The data subject to this restriction are contained in sheets [insert numbers or other identification of sheets]; and

(2) Mark each sheet of data it wishes to restrict with the following legend:

Use or disclosure of data contained on this sheet is subject to the restriction on the title page of this proposal.

(f) Contract award. (1) The Government intends to award a contract or contracts resulting from this solicitation to the responsible offeror(s) whose proposal(s) represents the best value after evaluation in accordance with the factors and subfactors in the solicitation.

(2) The Government may reject any or all proposals if such action is in the Government's interest.

(3) The Government may waive informalities and minor irregularities in proposals received.

(4) The Government intends to evaluate proposals and award a contract without discussions with offerors (except clarifications as described in FAR 15.306(a)). Therefore, the offeror's initial proposal should contain the offeror's best terms from a cost or price and technical standpoint. The Government reserves the right to conduct discussions if the Contracting Officer later determines them to be necessary. If the Contracting Officer determines that the number of proposals that would otherwise be in the competitive range exceeds the number at which an efficient competition can be conducted, the Contracting Officer may limit the number of proposals in the competitive range to the greatest number that will permit an efficient competition among the most highly rated proposals.

(5) The Government reserves the right to make an award on any item for a quantity less than the quantity offered, at the unit cost or prices offered, unless the offeror specifies otherwise in the proposal.

(6) The Government reserves the right to make multiple awards if, after considering the additional administrative costs, it is in the Government's best interest to do so.

(7) Exchanges with offerors after receipt of a proposal do not constitute a rejection or counteroffer by the Government.

(8) The Government may determine that a proposal is unacceptable if the prices proposed are materially unbalanced between line items or subline items. Unbalanced pricing exists when, despite an acceptable total evaluated price, the price of one or more contract line items is significantly overstated or understated as indicated by the application of cost or price analysis techniques. A proposal may be rejected if the Contracting Officer determines that the lack of balance poses an unacceptable risk to the Government.

(9) If a cost realism analysis is performed, cost realism may be considered by the source selection authority in evaluating performance or schedule risk.

(10) A written award or acceptance of proposal mailed or otherwise furnished to the successful offeror within the time specified in the proposal shall result in a binding contract without further action by either party.

(11) The Government may disclose the following information in postaward debriefings to other offerors:

(i) The overall evaluated cost or price and technical rating of the successful offeror;

(ii) The overall ranking of all offerors, when any ranking was developed by the agency during source selection;

(iii) A summary of the rationale for award; and

(iv) For acquisitions of commercial items, the make and model of the item to be delivered by the successful offeror.

L.5  FACSIMILE PROPOSALS (FAR 52.215-5)(OCT 1997)

(a) Definition. "Facsimile proposal," as used in this provision, means a proposal, revision or modification of a proposal, or withdrawal of a proposal that is transmitted to and received by the Government via facsimile machine.

(b) Offerors may submit facsimile proposals as responses to this solicitation. Facsimile proposals are subject to the same rules as paper proposals.

(c) The telephone number of receiving facsimile equipment is: 530-252-6408

(d) If any portion of a facsimile proposal received by the Contracting Officer is unreadable to the degree that conformance to the essential requirements of the solicitation cannot be ascertained from the document--

(1) The Contracting Officer immediately shall notify the offeror and permit the offeror to resubmit the proposal;

(2) The method and time for resubmission shall be prescribed by the Contracting Officer after consultation with the offeror; and

(3) The resubmission shall be considered as if it were received at the date and time of the original unreadable submission for the purpose of determining timeliness, provided the offeror complies with the time and format requirements for resubmission prescribed by the Contracting Officer.

(e) The Government reserves the right to make award solely on the facsimile proposal. However, if requested to do so by the Contracting Officer, the apparently successful offeror promptly shall submit the complete original signed proposal.

L.6  INSTRUCTIONS FOR THE SUBMISSION OF OFFERS AND OTHER INFORMATION

Each offeror must; (1) submit an offer; (2) submit written information that pertains to its capability; and (3) submit a reasonable price proposal demonstrating its understanding of the Government's requirements.  When evaluating an offeror's capability to perform the prospective contract, the Government will consider how well the offeror complied with these instructions.  The Government will consider an offeror's noncompliance with these instructions to be indicative of the type of conduct that it may expect from the offeror during contract performance.

(a)  Offers  (Proposals).  Offers must include the following:

1.  Standard Form 33, "Solicitation, Offer, and Award", with blocks 12 through 18 completed by the offeror.

2.  RFP Section B.  "Supplies or Services and Prices/Costs", with the offeror's proposed contract line item prices inserted in the appropriate spaces.

3.  RFP Section K, "Representations, Certifications, and Other Statements of Offerors", completed by the offeror.

The completion and submission to the Government of the above items will constitute an offer (proposal) and will indicate the offeror's unconditional assent to the terms and conditions in this RFP and any attachments hereto.  Unless this RFP expressly authorizes alternate proposals with respect to specific terms or conditions of this RFP, any objection to any of the terms and conditions of this RFP will constitute a deficiency, which will make the offer unacceptable.  An offeror may correct a deficiency only through discussions.  The Government intends to award a contract without discussions.  Therefore, offerors are warned to consult with the contracting officer before submitting an offer that takes exception to any term or condition of this RFP.  However, the Government reserves the right to conduct discussions and to permit offerors to revise their proposals.

(b)  Other Information.

1.  Price Information.  Insert your proposed prices (unit prices and total amounts) in the blank spaces adjacent to the contract line items in RFP Section B.

2.  Written Capability Information.  Each offeror must prepare an Experience & Past Performance Questionnaire in the format which is attached to this RFP.  It is especially important that offerors disclose instances in which their past performance may be considered by previous customers or their representatives to have been less than fully satisfactory, and that they tell their side of the story and/or describe corrective actions they have taken.

L.7  CLARIFICATIONS AND AWARD WITHOUT DISCUSSIONS

Clarifications are limited exchanges, between the Government and offerors, that may occur when award without discussions is contemplated.  Offerors may be given the opportunity to clarify certain aspects of their proposal (e.g., the relevance of an offeror's past performance information and adverse past performance information to which the offeror has not previously had an opportunity to respond) or to resolve minor or clerical mistakes.

Clarifications are not used to cure proposal deficiencies or material omissions, materially alter the technical or cost elements of the proposal, and/or otherwise revise the proposal.

L.8  AMENDMENTS TO PROPOSALS  (AGAR 452.215-72) (FEB 1988)

Any changes to a proposal made by the offeror after its initial submittal shall be accomplished by replacement pages.  Changes from the original page shall be indicated on the outside margin by vertical lines adjacent to the change.  The offeror shall include the date of the amendment on the lower right corner of the changed pages.

L.9  TYPE OF CONTRACT (FAR 52.216-1)(APR 1984)

The Government contemplates award of a Fixed-Price contract resulting from this solicitation.

L.10  SERVICE OF PROTEST (FAR 52.233-2)(AUG 1996)

(a) Protests, as defined in section 33.101 of the Federal Acquisition Regulation, that are filed directly with an agency, and copies of any protests that are filed with the General Accounting Office (GAO), shall be served on the Contracting Officer (addressed as follows) by obtaining written and dated acknowledgment of receipt from

MILEY SUTHERLAND

SIERRA CASCADE PROVINCE

LASSEN NATIONAL FOREST

2550 RIVERSIDE DRIVE

SUSANVILLE, CA 96130

- The copy of any protest shall be received in the office designated above within one day of filing a protest

with the GAO.

L.11  SITE VISIT (FAR 52.237-1)(APR 1984)

Offerors or quoters are urged and expected to inspect the site where services are to be performed and to satisfy themselves regarding all general and local conditions that may affect the cost of contract performance, to the extent that the information is reasonably obtainable. In no event shall failure to inspect the site constitute grounds for a claim after contract award.

(b) An organized site visit has been scheduled for--

Wednesday, August 16, 2000, at 0900 hours.

(c) Participants will meet at--

Almanor Ranger Station, 900 Hwy. 36, Chester, CA

SECTION M - EVALUATION FACTORS FOR AWARD

M.1  GENERAL. The Government will award the contract to the offeror whose offer represents the best value to the Government on the basis of; (1) the merits of the offer; and (2) the offeror's capability, as explained below.

M.2  MERITS OF THE OFFER.  The Government will determine the merits of each offer on the basis of; (1) its acceptability; and (2) its price reasonableness.

a.  Acceptability.  The Government will determine the acceptability of each offer on a pass/fail basis.  An offer is acceptable when it manifests the offeror's assent, without exception, to the terms and conditions of this solicitation, and attachments.  If an offeror takes exception to any of the terms and conditions of the solicitation, then the Government will consider its offer to be unacceptable.  The Government reserves the right to change the terms and conditions of the solicitation by amendment at any time prior to the source selection decision.

b.  Price.  The Government will evaluate the reasonableness of the price of each acceptable offer in relation to the offeror's relative capability.  (See Source Selection Decision below.)

c.   Biomass Removal Factor.   For the purposes of evaluation and determination of the low acceptable bidder, the amount of $125 per acre will be calculated as an addition to the alternative other than Biomass removal.  This is to compensate government for additional treatment of material piled vs removal.   This amount is only a calculation to determine the lowest cost to the Government and does not infer in any way that this amount will be paid to the successful bidder.

M.3  CAPABILITY OF THE OFFEROR.  The Government will assess the capability of each offeror on the basis of; (1) its organizational experience; (2) its organizational past performance; (3) its understanding of the Government's requirements, as reflected in the reasonableness of the offered price; (4)  the economic area from which most of the offeror’s workforce is drawn; and (5) its demonstrated ability to comply with instructions.  The Government will not assess capability on a pass/fail basis, but will use its assessments of capability as a basis for comparing offerors to determine best value.

a.  Organizational Experience   (What have you done.)  Experience is the opportunity to learn by doing.  The Government will evaluate each offeror's organizational experience on the basis of its breadth, its depth, and its relevance to the work that will be required under the prospective contract.  The Government will not evaluate an offeror's experience on the basis of the personal experience of the offeror's key personnel.  However, the Government will consider the extent to which the offeror's key personnel have worked together in the past.  The Government will evaluate the organizational experience of the offeror's proposed key subcontractors.

b.  Organizational Past Performance   (How well did you do it.)  Past performance is a measure of the degree to which an offeror satisfied its customers in the past and complied with Federal, state, and local laws and regulations.  The Government will contact some of each offeror's customers to ask whether or not they believe; (1)  that the offeror was capable, efficient, and effective; (2) that the offeror's performance conformed to the terms and conditions of the contract; (3) that the offeror was reasonable and cooperative during contract performance; and (4) that the offeror was committed to customer satisfaction.  In evaluating past performance the Government will contact some of the references provided by the offeror and other sources of information, including, but not limited to; Federal, state, and local government agencies, better business bureaus, published media, and electronic databases.  The Government will not evaluate an offeror's organizational past performance on the basis of the personal past performance of the offeror's key personnel.  The Government may evaluate the organizational past performance of the offeror's proposed key subcontractors.

c.  Understanding of the Government's Requirements.  The Government will evaluate each offeror's relative understanding of the Government's requirements on the basis of its price proposal.

d.  Economic area from which most of the offeror’s workforce is drawn.  Preference will be given to offerors whose workforce is predominantly from the business zone around the Lassen, Plumas, and Tahoe National Forests.

e.  Compliance with Instructions.  In evaluating an offeror's capability, the Government will consider how well the offeror complied with the instructions in this solicitation.  The Government will consider any noncompliance to be indicative of what can be expected from the offeror during contract performance.

M.4  RELATIVE IMPORTANCE OF THE EVALUATION FACTORS.  Non-price evaluation factors, when combined, are as important as price.  An offer must be acceptable in order for the offeror to be eligible for award.  The Government will not award a contract on the basis of an unacceptable offer.  Thus, acceptability of the offer is the most important evaluation factor.  The Government considers an offeror's capability to be as important as price.  However, the Government will not select an offeror for award on the basis of a superior capability without consideration of the amount of its price.  The relative influence that capability and price will have on the award decision will depend on the marginal differences among the competing offerors.

M.5  SOURCE SELECTION DECISION.  In order to select the winning offeror, the Government will rank the offerors from best to worst by making a series of paired comparisons among them, trading off the marginal differences in capability and price between the members of each pair.  If one offeror has both the better capability and the lower price, then that offeror will be the better value.  If one offeror has the better capability and the higher price, then the source selection decision will be based on whether the marginal difference in capability is worth the marginal difference in price.  If the contracting officer considers the better capability to be worth the higher price, then the more capable, higher-priced offeror will be the better value.  If not, then the less capable, lower-priced offeror will be the better value.  The contracting officer will continue to make paired comparisons until the contracting officer has decided which offeror represents the best value.

The contract, resulting from this solicitation, will be awarded to the offeror which represents the best value to the Forest Service.