WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A12185 | In-Flight Anomaly Number -- | Contractor Report Number P-064 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title A PIECE OF FOREIGN MATERIAL WAS FOUND IN THE 2 INCH Q.D. OF ET-38 |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1 |
| HCRIT 1 | Sys_Lvl Y | Misc Codes A B C D E F (X) G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE ET-38 | PART# 80901000000 | SER/LOT# 31 | MANUFACTURER MMC |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE QUICK DISCONNECT | PART# V527-415273-028 | SER/LOT# DCN-03953- | MANUFACTURER ROCKEWELL DY |
| Test/Operation L - FLD | Prevailing Condtion P - PRESSURE | F / U UC | Fail Mode MS - STRUCT | Cause MAE - MFG-ASY-ENVR |
| System PROPULSION | Defect CE - EXTRA | Material S - STRUCT | Work Contact J. FINCHER | Fail Date 04/17/1989 |
| Received at MSFC 04/20/1989 | Date Isolated -- | FMEA Reference 03-1-0513-2 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location KSC | Symptom UC - UNSAT | Time Cycle N/A |
| Effectivity Text -- |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 02/10/1995 | CN RSLV SBMT 06/05/1989 | Defer Date -- | Add Date 04/21/1989 | R/C Codes 4 - TEST -- -- |
| Assignee |
| Design P. MULLER | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project G. LADNER | Project MGR G. BRIDWELL |
| Approval |
| Design P. MULLER | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project G. LADNER | Project MGR G. BRIDWELL |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete JE | MSFC Closure Date 07/14/1989 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary CAUSE: MOST PROBABLE - THE PIECE OF TEFLON WAS LEFT IN A TOOLING HOSE BY THE SUPPLIER. THIS HOSE IS USED TO PRESSURIZE THE EXTERNAL TANK FOR DELIVERY R/C: A BLOWDOWN TEST OF THE HOSES AT OPERATING PRESSURE PRIOR TO CONNECTING TO THE ET HAS BEEN IMPLEMENTED INTO THE APPLICABLE TEST PROCEDURE |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description AFTER REMOVAL OF THE TOOLING PLATE (GO 78-400010) FROM THE ET-38 2" ORBITER TO ET PRESSURIZATION QUICK DISCONNECT, A PIECE OF MATERIAL RESEMBLING TEFLON (APPROX. 3.37" LONG X 1.4 WIDE X .033 THICK) WAS CAPTURED IN THE Q.D. POPPET. (REF. MARS T99906) AND A NONCOMPLIANCE REPORT (GNC-ET-38-26) WAS WRITTEN TO TRAVEL THIS CONDITION TO KSC WHERE IT WOULD BE CORRECTED. THIS CAPS IS ISSUED TO INVESTIGATE THIS ANOMALY AND INITIATE CORRECTIVE ACTION AS DEEMED NECESSARY CRITICALITY: THIS PROBLEM IS CRITICALITY 1 IN FMEA NUMBER 03-1-0513-2 OF THE MAIN PROPULSION SECTION OF THE SHUTTLE CRITICAL ITEMS LIST |
| Contractor Investigation/Resolution 4/24/89 - THIS PROBLEM REPORT HAS BEEN DEFERRED FOR STS-30 (ET-29) BASED ON THE FOLLOWING RATIONALE: THE MOST PROBABLE SOURCE OF THE PIECE OF TEFLON FOUND ON ET-38, IS THAT IT WAS LOOSE INSIDE A HOSE USED TO PRESSURIZE THE LOX TANK IN THE MODIFICATION CENTER AT MAF. A BLOW DOWN TEST WAS PERFORMED AND THE RESULT CONFIRMED THE FINDING. AS FOR ET-29, (1) IT WAS NOT PROCESSED THROUGH THE MODIFICATION CENTER, (2) THE QUICK DISCONNECT VALVE DID NOT LEAK DURING TESTING AT MAF AND (3) THE QUICK DISCONNECT WAS INSPECTED AT KSC VISUALLY AND FOUND TO BE ACCEPTABLE THE ABOVE DEFERRAL RATIONALE MEETS DEFERRAL REQUIREMENTS OF NSTS 07700 VOLUME XI ITEM C, WHICH STATES "THE PROBLEM CONDITION DOES NOT EXIST IN THE FLIGHT HARDWARE AND IS CLEARLY SCREENED BY ACCEPTANCE TEST, PREFLIGHT CHECKOUT, OR SPECIAL TEST." THE ABOVE DEFERRAL RATIONALE HAS BEEN APPROVED BY THE ET PROJECT MANAGER MR. J. SMELSER _____________JERRY SMELSER (SIGNED 4/24/89)___________ GENERAL: DURING PERFORMANCE OF PR ET-38-FP-0004 DISPOSITION ON THE GO2 TWO INCH DISCONNECT (REF. COFR EXCEPTION SHEET NUMBER GNC-ET-38-26) A PIECE OF MATERIAL SIMILAR TO TEFLON WAS FOUND IN THE Q. D. IT APPEARS THAT THE PIECE OF FOREIGN MATERIAL WAS CAPTIVE BETWEEN THE Q. D. POPPET AND THE VALVE SEAT WHICH RESULTED IN LEAKAGE OF THE Q. D. DURING MODIFICATION ACTIVITIES AT MAF. THIS ABNORMAL ACTIVITY WAS DOCUMENTED ON THE AFOREMENTIONED EXCEPTION SHEET WITH A DISPOSITION TO CORRECT THE CONDITION AT KSC THE MATERIAL IN THE QUICK DISCONNECT WAS REMOVED AND SENT TO THE MALFUNCTION LABORATORY AT KSC TASK I - FAILURE/PROBLEM INVESTIGATION THE FOLLOWING ACTIONS SHALL BE ACCOMPLISHED TO DETERMINE THE ORIGIN OF THE MATERIAL AND TO EFFECT CORRECTIVE ACTIONS AS REQUIRED 1. RECEIVE THE MATERIAL AT MAF AND PERFORM DIMENSIONAL ANALYSIS AND MATERIAL COMPOSITION ANALYSIS. COMPLETE FTIR AND XRT ANALYSIS INDICATES THAT THE KSC MATERIAL IS THE SAME MATERIAL (PTFE) TEFLON USED IN MAF MOD CENTER PRESSURIZATION HOSES (TOOLING). BY SEM/EDX BOTH SAMPLES INDICATE THEY ARE EXTRUDED TEFLON MATERIALS. THE ONLY NOTABLE DIFFERENCES IN SAMPLES IS THE BRAID IMPRINTS ON THE MAF SAMPLE, WHERE AS THE KSC SAMPLES IS SMOOTH ON THE OUTSIDE WHICH WOULD INDICATE NO STAINLESS STEEL BRAID HAS BEEN WOVEN ONTO THE MATERIAL. REF. LAB ANALYSIS 89A155 2. RESEARCH ALL BUILD PAPER AND TEST DOCUMENTATION TO DETERMINE IF ANY ABNORMAL CHARACTERISTICS DEVELOPED OR ACTIVITIES OCCURRED WHICH WOULD PRODUCE A CLUE AS TO THE ORIGIN OF THE MATERIAL COMPLETE CLOSURE STATEMENT: NO ANOMALIES WERE IDENTIFIED IN THE BUILD PAPER/TEST PROCEDURES THAT WOULD CONTRIBUTE TO THE PROBLEM. REF. MEMO 3741-89-046 3. LEAK TEST TEFLON LINED HOSES USED DURING THE ET-38 MODIFICATION ACTIVITIES TO DETERMINE IF A PIECE OF THE EXTRUDED LINER IS MISSING REMOVE END FITTING AND INSPECT FOR ANY EVIDENCE OF SHEDDING OF THE TEFLON LINES COMPLETE CLOSURE STATEMENT: THE HOSE USED TO PRESSURIZE THE L02 TANK (F78-1359-6-102) WAS SCRAPPED AND REPLACED WITH A NEW HOSE PRIOR TO THE OPENING OF THE CAPS THE HOSES USED ON THE PREVIOUS ET (ET-23) WERE LEAK TESTED AT 10 PSIG SUBMERGED IN WATER AND NO LEAKAGE OCCURRED. THE END FITTINGS WERE REMOVED AND NO SHEDDING OR DEGRADATION OF THE LINER WAS NOTED 4. REMOVE A SECTION OF THE PRESSURIZATION HOSES AND PERFORM I.R. SCAN FOR MATERIAL COMPOSITION COMPARISON. MEASURE TEFLON LINER THICKNESS AND OTHER DIMENSIONS FOR PHYSICAL COMPARISON OF MATERIAL EXTRACTED FROM ET-38 Q.D COMPLETE CLOSURE STATEMENT: KSC SAMPLE WAS REPORTED TO BE .0327" (MEAN) THICK. SAMPLES TAKEN FROM THE PRESSURIZATION HOSE AT MAF WAS .0329" (MEAN) THICK. BY LAB ANALYSIS (SEE ITEM 1) THE WALL THICKNESSES AND MATERIAL COMPOSITIONS COMPARE FAVORABLY IN ALL RESPECTS. SEE SAMPLE "A" ON LAB REPORT 89A144 WHICH IS THE "1" HOSE ON LAB ANALYSIS REFERENCED IN ITEM 1 5. REVIEW TEST CONSOLES FOR POTENTIAL OF DISCHARGING TEFLON MATERIAL INTO THE SYSTEM COMPLETE CLOSURE STATEMENT: NO MATERIAL OF THIS TYPE IS USED IN THE PRESSURIZATION CONSOLE (REF MEMO" 3611-89-053WC) TASK II - CORRECTIVE ACTION 1. IMPLEMENTED A BLOW DOWN TEST OF HOSES AT OPERATING PRESSURING (250-300 PSI) PRIOR TO CONNECTING THEM TO THE EXTERNAL TANK, FOR BLDGS 420 AND THE MOD CENTER COMPLETE CLOSURE STATEMENT: THE FOLLOWING TEST PROCEDURES WILL BE REVISED TO INCORPORATE A BLOWDOWN TEST PER TCN 47 OF TOOL DRAWING F78-1359 IN THE MOD CENTER TP-5A150-MC TP-8C211-MC TP-5G250-MC TP-5A151-MC TP-8C212-MC TP-5G251-MC THIS REVISION WILL BE INCORPORATED FOR THE NEXT VEHICLES TO ENTER THE MOD CENTER. PRESENT VEHICLES IN THE MOD CENTER ET-33 AND 34 WILL BE ACCOMPLISHED VIA WORK AUTHORIZATION A39-083 FOR THE F78-1359-6-101 HOSE (FIRST TIME USAGE OF HOSE). THE F78-1359-6-102 HOSE HAS BEEN USED SIX TIMES AND WILL NOT REQUIRE A BLOWDOWN TEST FOR THESE TWO VEHICLES TEST PROCEDURE TP-5C101-AT FOR BOTH CELL 1 AND 2 IN BLDG. 420 HAS BEEN REVISED TO INCLUDE A BLOWDOWN TEST. (REF PCN 8 OF TP-5C101-AT) 2. RESEARCH ALL BUILD PAPER AND TEST DOCUMENTATION TO DETERMINE IF A NEW HOSE WAS USED TO PRESSURIZE ANY UNFLOWN VEHICLES IN THE MOD CENTER AFTER ET-38 COMPLETE CLOSURE STATEMENT: ET-32 WAS THE NEXT VEHICLE TO ENTER THE MOD CENTER. A NEW HOSE WAS USED TO PRESSURIZE THE L02 TANK. THE HOSE HAS NOT BEEN REPLACED SINCE THEN (REF. MEMO 3741-89-065) 3. INITIATE A MARS TO INSPECT THE L02 DIFFUSER AND THE L02 QD POPPET ON ET-32 COMPLETE CLOSURE STATEMENT: MARS T-107080 HAS BEEN ISSUED AND DISPOSITIONED BY ENGINEERING TO INSPECT THE L02 DIFFUSER AND THE L02 QD POPPET. (NOTE: INSPECTION REVEALED NO PARTICULATE) 4. ISSUE A GOVERNMENT-INDUSTRY ALERT ADDRESSING THIS PROBLEM COMPLETE TASK III - CLEARANCE OF EFFECTIVITIES ALL UNFLOWN ET TANKS WITH THE EXCEPTION OF ET-32 L02 UTILIZED PREVIOUSLY USED HOSES. ET-32 RESOLVED BY MARS T-107080 TASK IV - CAPS CLOSURE SUMMARY A SINGLE PIECE OF TEFLON (PTFE) WAS FOUND TRAPPED BETWEEN THE POPPET AND GUIDE OF ET-38 L02 ET PRESSURIZATION QUICK DISCONNECT. A THOROUGH INVESTIGATION WAS PERFORMED AND CONCLUDED THAT THE TEFLON WAS ORIGINALLY TRAPPED IN THE INNER LINER OF A TOOLING HOSE USED TO PRESSURIZE THE ET FOR DELIVERY. WHEN THE L02 TANK WAS PRESSURIZED FOR SHIPMENT, THE PIECE OF TEFLON WAS EJECTED FROM THE HOSE BY THE GAS FLOW. THIS WAS THE FIRST USAGE OF THE TOOLING HOSE. A BLOWDOWN TEST OF THE HOSES AT OPERATING PRESSURE PRIOR TO CONNECTING TO THE ET HAS BEEN IMPLEMENTED INTO THE APPLICABLE TEST PROCEDURES THIS PROBLEM REPORT IS CONSIDERED CLOSED |
| MSFC Response/Concurrence |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A12185 | IFA# -- | Contractor RPT# P-064 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# V527-415273-028 | Asmnt Part Name QUICK DISCONNECT | Asmnt Serial/Lot# DCN-03953 |
| HCRIT CD -- | FCRIT CD 1 | CAUSE CD MAP - MFG-ASY-INST | FAIL MODE UC - UNSAT |
| Asmnt FMEA N/A | Asmnt FM N/A | FMEA CSE N/A | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |