SPECIAL SPECIFICATION

SECTION 05810

EXPANSION JOINT COVER ASSEMBLIES

Page

PART 1 - GENERAL

1.01	Related Documents ..............................................................................	2

1.02	References ........................................................................................	2

1.03	Summary .........................................................................................	3

1.04	Submittals ........................................................................................	3

1.05	Quality Assurance ...............................................................................	4

PART 2 - PRODUCTS

2.01	Manufacturers ...................................................................................	4

2.02	Materials .........................................................................................	4

2.03	Expansion Joint Cover Assemblies............................................................	5

2.04	Metal Finishes ...................................................................................	6

PART 3 - EXECUTION

3.01	Preparation .......................................................................................	7

3.02	Installation  ......................................................................................	7

3.03	Cleaning and Protection ........................................................................	8

3.04	Interior Expansion Joint Cover Schedule ....................................................	8

3.05	Exterior Expansion Joint Cover Schedule ....................................................	8

SPECIAL SPECIFICATION

SECTION 05810

EXPANSION JOINT COVER ASSEMBLIES

PART 1 - GENERAL

1.01	RELATED DOCUMENTS

A.	Drawing and general provisions of the Contract, including General and Supplementary Conditions and Division 1 Specification Sections, apply to this Section.

1.02	REFERENCES

A.	Aluminum Association (AA)

AA-M10

B.	American Society of Testing and Materials (ASTM)

B 209	Specification for Aluminum and Aluminum-Alloy Sheet and Plate

B 221	Specification for Aluminum and Aluminum-Allow Extruded Bars, Rods, Wire, Shapes and Tubes

D 2000	Classification System for Rubber Products in Automotive Applications

E 119	Test Methods for Fire Tests of Building Construction and Materials

E 1399	Test Method for Cyclic Movement and Measuring the Minimum and Maximum Joint Widths of Architectural Joint Systems

C.	National Association of Architectural Metal Manufacturers (NAAMM)

NAAMM	"Metal Finishes Manual"

D.	National Fire Protection Association (NFPA)

NFPA 251

E.	Uniform Building Code (U.B.C.)

U.B.C. 43-1

F.	Underwriter Laboratory (UL)

UL263

1.03	SUMMARY

A.	This Section includes the following:

1.	Floor expansion joint cover assemblies.

2.	Wall expansion joint cover assemblies.

3.	Ceiling expansion joint cover assemblies.

4.	Fire-rated expansion joint cover assemblies.

5.	Compression seals.

B.	Related Sections:  The following Sections contain requirements that relate to this Section:

1.	Division 3 Section "Cast-In-Place Concrete" for cast-in anchorage and frames for expansion joints cover assemblies in concrete floors.

2.	Division 9 Sections for walls, partitions, ceilings, and floor finishes with expansion joints.

1.04	SUBMITTALS

A.	General:  Submit the following according to Conditions of the Contract and Division 1 Specification Sections.

B.	Product data for each type of expansion joint cover assembly specified, including manufacturer's product specifications, installation instructions, details of construction relative to materials, dimensions of individual components, profiles, and finishes.

C.	Shop drawings showing fabrication and installation of expansion joint cover assembly including plans, elevations, sections, details of components, joints, splices, and attachments to other units of Work.  Include details of drainage components and routing scheme to building exterior for exterior covers.

D.	Samples for verification purposes in full-size units of each type of expansion joint cover assembly indicated; in sets for each finish, color, texture, and pattern specified, showing full range of variations expected in these characteristics.

1.	Install elastomeric material for joints samples to verify color selected.

1.05	QUALITY ASSURANCE

A.	Single-Source Responsibility:  Obtain expansion joint cover assemblies specified in this Section from one source from a single manufacturer.  Coordinate compatibility with expansion joint cover assemblies specified in other sections.  Interior and exterior joint covers may be from separate manufacturers.

B.	Fire-Test-Response Characteristics:  Where indicated, provide expansion joint cover assemblies identical to those assemblies whose fire resistance has been determined per ANSI/UL 263, NFPA 251, U.B.C. 43-1, or ASTM E 119 , including hose stream test of vertical wall assemblies, by a testing and inspecting agency acceptable to authorities having jurisdiction.

1.	Fire-Resistance Ratings:  Not less than the rating of adjacent construction.

C.	All materials used shall not contain asbestos fibers or lead paint.

PART 2 - PRODUCTS

2.01	MANUFACTURERS

A.	Available Products:  Subject to compliance with requirements, products that may be incorporated in the Work include, but are not limited to, the products specified in the Expansion Joint Cover schedule at end of this Section.

2.02	MATERIALS

A.	Aluminum:  ASTM B 221, alloy 6063-T5 for extrusions; ASTM B 209 alloy 6061-T6, sheet and plate.

1.	Protect aluminum surfaces to be placed in contact with cementitious materials with a protective coating.

B.	Extruded Preformed Seals:  Single or multicellular elastomeric profiles as classified under ASTM D 2000, designed with or without continuous, longitudinal, internal baffles.  Formed to fit compatible frames, in color indicated or, if not indicated, as selected by Sandia Delegated Representative (SDR) from manufacturer's standard colors.

C.	Fire Barriers:  Designed for indicated or required dynamic structural movement without material degradation or fatigue when tested according to ASTM E 1399.  Tested in maximum joint width condition with a field splice as a component of an expansion joint cover per ANSI/UL 263, NFPA 251, U.B.C. 43-1, or ASTM E 119, including hose stream test of vertical wall assemblies by a nationally recognized testing and inspecting agency acceptable to authorities having jurisdiction.

D.	Accessories:  Manufacturer's standard anchors, fasteners, set screws, spacers, flexible moisture barrier and filler materials, drain tubes, lubricants, adhesive, and other accessories compatible with material in contact, as indicated or required for complete installations.

2.03	EXPANSION JOINT COVER ASSEMBLIES

A.	General:  Provide expansion joint cover assemblies of design, basic profile, materials, and operation indicated.  Provide units comparable to those indicated or required to accommodate joint size, variations in adjacent surfaces, and dynamic structural movement without material degradation or fatigue when tested according to ASTM E 1399.  Furnish units in longest practicable lengths to minimize number of end joints.  Provide hairline mitered corners where joint changes directions or abuts other materials.  Include closer materials and transition pieces, tee-joints, corners, curbs, cross-connections, and other accessories as required to provide continuous joint cover assemblies.

B.	Moisture Barrier:  Provide manufacturer's continuous, standard, flexible vinyl moisture barrier under exterior covers at locations indicated.  Provide additional accessories as required for complete system drainage to building exterior for exterior covers.

C.	Fire-Rated Joint Covers:  Provide expansion joint cover assemblies with manufacturer's continuous, standard, flexible fire barrier seals under covers at locations indicated to provide fire-resistive rating not less than the rating of adjacent construction.

D.	Coverless Fire Barrier:  Provide manufacturer's continuous standard flexible fire barrier seals at locations indicated to provide fire-resistive rating not less than the rating of adjacent construction.

E.	Metal Floor-to-Floor Joint Cover Assemblies:  Provide continuous extruded metal frames of profile indicated with seating surface and concealed bolt and anchors embedded in concrete.  Provide assemblies formed to receive cover plates of design indicated.  Furnish depth and configuration to suit type of construction and to produce a continuous flush wearing surface with adjoining finish floor surface.

1.	Self-Centering Cover Plates:  Concealed centering device with the cover plate secured in or on top of frames as to have free movement on both sides.

2.	Floor Cover Plate Wearing Surfaces:  Provide cover plates with the following type of wearing surfaces.

a.	Fluted.

F.	Floor-to-Wall Joints:  Provide one frame on floor side of joint only.  Provide wall side frame where required by manufacturer's design.

G.	Wall, Ceiling, and Soffit Joint Cover Assemblies:  Provide interior wall and ceiling expansion joint cover assemblies of same design and appearance.

H.	Joint Cover Assemblies with Preformed Seals:  Provide joint cover assemblies consisting of continuously anchored aluminum extrusions and continuous extruded preformed seals of profile indicated or required to suit types of installation conditions shown.  Furnish extrusions designed to be embedded in or attached to concrete with lugs.  Vulcanize or heat-weld splices (if any) to ensure hermetic joint condition.

1.	Cover Plate:  Include extruded aluminum cover plate fastened to one side of joint and extend plate to lap each side of joint to permit free movement with cover in close contact with adjacent contact surfaces.

I.	Compression Seals:  Preformed, elastomeric extrusions having internal baffle system in sizes and profiles shown or as recommended by the manufacturer.  Provide lubricant and adhesive for installation recommended by the manufacturer.

2.04	METAL FINISHES

A.	General:  Comply with NAAMM "Metal Finishes Manual" for finish designations and application recommendations, except as otherwise indicated.  Apply finishes to products in factory after fabrication.  Protect finishes on exposed surfaces before shipment.

B.	Aluminum Finishes:  Finish designations prefixed by AA conform to the system established by the Aluminum Association for designating aluminum finishes.

1.	Mill Finish:  AA-M10 (unspecified mill finish).

PART 3 - EXECUTION

3.01	PREPARATION

A.	Manufacturer's Instructions:  In addition to requirements of these specifications, comply with manufacturer's instructions and recommendations for phases of Work, including preparing substrate, applying materials, and protecting installed units.

B.	Coordinate and furnish anchorages, setting drawings, templates, and instructions for installation of expansion joint cover assemblies to be embedded in or anchored to concrete or to have recesses formed into edges of concrete slab for later placement and grouting-in of frames.

C.	Fastening to In-Place Construction:  Provide anchorage devices and fasteners where necessary to secure expansion joint cover assemblies to in-place construction, including threaded fasteners with drilled-in expansion shields for masonry and concrete where anchoring members are not embedded in concrete.  Provide fasteners of metal, type, and size to suit type of construction indicated and provide for secure attachment of expansion joint cover assemblies.

3.02	INSTALLATION

A.	Cutting, Fitting, and Placement:  Perform cutting, drilling, and fitting required to install expansion joint covers.  Install joint cover assemblies in true alignment and proper relationship to expansion joints and adjoining finished surfaces measured from established lines and levels.  Allow adequate free movement for thermal expansion and contraction of metal to avoid buckling.  Set floor covers at elevations to be flush with adjacent finished floor materials.  Locate wall, ceiling, roof, and soffit covers in continuous contact with adjacent surfaces.  Securely attach in place with required accessories.  Locate anchors at interval recommended by manufacturer, but not less than 3 inches from each end and not more than 24 inches on center.

B.	Continuity:  Maintain continuity of expansion joints cover assemblies with a minimum number of end joints and align metal members mechanically using splice joints.  Cut and fit ends to produce joints that will accommodate thermal expansion and contraction of metal to avoid buckling of frames.  Adhere flexible filler materials (if any) to frames with adhesive or pressure-sensitive tape as recommended by manufacturer.

C.	Extruded Preformed Seals:  Install seals complying with manufacturer's instructions and with minimum number of end joints.  For straight sections provide preformed seals in continuous lengths.  Vulcanize or heat-weld field splice joints in preformed seal material to provide watertight joints using procedures recommended by manufacturer.  Apply adhesive, epoxy, or lubricant-adhesive approved by manufacturer to both frame interfaces before installing preformed seal.  Seal transitions to manufacturer's instructions.

D.	Fire Barriers:  Install fire barriers, including transitions and end joints, according to manufacturer's instructions so that fire-rated construction is continuous.

3.03	CLEANING AND PROTECTION

A.	Do not remove protective covering until finish work in adjacent areas is complete.  When protective covering is removed, clean exposed metal surfaces to comply with manufacturer's instructions.

3.04	INTERIOR EXPANSION JOINT COVER SCHEDULE (for 1-1/2 inch joints)

A.	FEJ1 (Floor):

1.	Balco 6FS or 6FVS (where applicable) or approved substitute.

B.	CEJ1 (Ceiling):

1.	Acoustical panel:  Balco SC or CSC (where applicable) or approved substitute.

2.	Gypsum Board:  Balco FWG or CFWG (where applicable) or approved substitute.

C.	WEJ1 (Wall):  Non fire-rated and fire-rated.

1.	Balco FWG or CFWG (where applicable) or approved substitute.  Add UL fire-rated component where required to maintain fire resistance of adjacent construction.

3.05	EXTERIOR EXPANSION JOINT COVER SCHEDULE (for 1-1/2 inch joints)

A.	EFEJ1 (Floor):

1.	Construction Specialties Group FSS-300 or approved substitute.

END OF SECTION