SVX II Silicon Strip Detector Upgrade Project

###### SVX Module Production Testing Software

--PRELIMINARY--

21 Sept. 1998

Vince Pavlicek

Document # ESE-SVX-980916

# 1	Introduction to SVX Module Production Testing Software

This document describes the software diagnostic tests that will be applied to the production versions of seven VME modules that are being designed for the SVX II detector system for the CDF Upgrade.  The modules to be tested are

- The three members of the VRB (VME Readout Buffer) family

- The VRB

- The VFO (VRB Fan-out)

- The VTM (VRB Transition Module)

- The three members of the FIB (Fiber Interface Board) family

- The FIB

- The FFO (FIB Fan-out)

- The FTM (FIB Transition Module)

- In addition, two modules that are used to test the above boards:

- The GSTM that emulates the boards that connect to the board under test.

- The DEM that generates simulated front-end data and can insert it at several places.

Most of the basis for this test list came from the draft document, SVX Data Acquisition System Test Flow by J. Anderson and K. Woodbury, 2/19/97.  Many of the details needed to implement these tests are included in that document so it is recommended reading.  This document uses many acronyms that are in common use with =in the SVX project.  If you find an unfamiliar acronym, refer to http://www-ese.fnal.gov/eseproj/svx/svx_acronyms.htm.

# 2	Simple Tests applied to all Modules

## 2.1	Power Test.  No Software.  ESE/ESD Technician or assembly house.

Apply 5 volts with a current-limited power supply and measure current.  This test is done at a workbench and probably as part of the quality control after the assembly process.  Some boards also have on-board oscillators that can be checked for activity.

## 2.2	VRB simple tests

A VRB power-up self-test requires VRB, subrack, RS232 terminal.  It tests on-board processor function, shared memory, and FPGA download.  When the test is complete, the Processor LED will be ON and the VME access and SRC access LEDs will flash.  The terminal may be used to display specific errors.  The terminal will display digitized light levels from the VTM.  Other power-up self-tests will be added such as a simple program to blink the from panel processor LED.

# GSTM Test Stand – Board Level Tests

## 2.3	Testing untested or failing GSTM boards.

### 2.3.1	Loop-back test.  Java software.  ESE/ESD tester.

There are three general tests.  1) Test transfers through 27 bit ports.  This will be one direction and should exercise different data patterns.  There should be no errors.  2) Test bi-directional transfers through nine bit ports again with different data patterns.  3) Test control and status bits.  These tests should be able to run in two modes.  One is a quick tester that runs many data quickly and stops on errors.  The second needs to continue running when there are errors to allow hardware diagnostics to locate the error.

The following diagnostic descriptions are from the Loopback adapter specifications, ESE-SVX-960422.  They often refer to GSTM Motherboard logic that will be tested.  That reference is the GSTM Motherboard Specification, document number ESE-SVX-960126.  References made here to GSTM hardware can be seen in the GSTM Motherboard Specification, Figure 2: “Functional Blocks for the GSTM Motherboard”.

Insert Loop-back adapter on two ports.  Program the GSTM board for loop-back adapter.

A test program will be needed which generally adheres to the content and sequence detailed here.

- Issue a /Master-Reset and check for an ID value of 0x01 in both T-Port and R-Port fields of the GSTM Test Register.  This test verifies the receipt of /Master-Reset at each port.

- Test that all six ID bits of both ports are functional.  Generate a global GSTM CR-Cbit0 signal after putting bit-toggle test patterns in the T-FIFO.  The low-order six bits of T-FIFO data should appear on the ID bits.  A multiplexer failure might indicate a problem with the CR-Cbit0 signal at the erring port connector.

- Write test pattern data into the T-Port FIFO until full.  Clock the T-Port T11 (or T21) FIFO data into the R-Port R11 (or R21) FIFO.  Read the R-Port FIFO and compare for errors.

- Repeat FIFO tests while controlling the T-Port’s and R-Port’s nine bits of bi-directional data (called DATA-IO on both ports) as well as the GSTM Mode Register’s direction control bits.  Perform this to test both the bi-directional capabilities of the GSTM buffers and the data integrity of the FIFOs.  This FIFO test should be performed twice, once in each direction (T-Port to R-Port and vice versa).  The P-Cntrl <2> bits from both ports define direction control for the GSTM Loop-Back Daughter Card.

(Programmer’s note: The upper four bits of the GSTM Mode Register should be set to insure that no signal driver collisions occur between the Loop-Back Daughter Card and the GSTM.  The Loop-Back Daughter Card provides internal self-protection against on-board signal collision should both ports drive their DATA-IO lines.  It is possible to create a situation where the Loop-Back Daughter Card could drive against a GSTM port that is also driving.  Care must be exercised in the sequence used to enable signal drivers to prevent GSTM-to-daughter signal collisions when test software is constructed.)

- Using the T-Port’s and R-Port’s P-Cntrl <2> bits to control data flow direction, write test pattern data into the T12 (or T22) FIFO-1 and read the data out through the R12 (or R22) FIFO-2.  Perform the same test using the T12 (or T22) FIFO-2 and the R12 (or (R22) FIFO-1

- Test the functionality of the P-Control bits, the /CR-Control bits and the MR-Mode bits for both ports under test.  Generate a global GSTM CR-Cbit1 signal and the ID bits will be multiplexed in such a way as to monitor the status of the bits.  Test software must command the GSTM to generate these signals and use the ID bits to verify their operability at each port connector.  The control bits monitored through any given port ID bit field are the control bits for that port.  A multiplexer failure might indicate a problem with the CR-Cbit1 signal at the erring port connector.

- Test the functionality of daughter card status return bits P-Status<2:0> and SR-Status<1:0> for both ports under test.  Generate both the global GSTM CR-Cbit0 and CR-Cbit1 signals after loading test pattern data in the T-FIFO.  The low-order five T-FIFO bits will be echoed across the port-specific status return bits.

(Programmer’s note: Remember that the Loop-Back card tests are always being implemented on both Transmit and Receive ports, hence the diagnostic software must verify bit operations on both the T-Port and the R-Port for a complete test.)

### 2.3.2	GLink adapter tests.  Java software.  ESE/ESD tester.

Insert GLink receiver adapter on receiver port.  Insert GLink transmitter adapter on transmitter port.  Program board for GLink adapters.  Test transfers through 27 bit ports.  This will be one direction and should exercise different data patterns.  There should be no errors.  Monitor status bits for correctness.  This test expands the GSTM testing by exercising a different set of firmware in the GSTM programmable logic.

## 2.4	Testing DEMs

Data Emulator Modules are transition modules that can emulate a port card.  They operate in response to commands from a FIB and produce data in the format produced by SVX3 chips.  A DEM can plug in behind a FIB in a subrack and take commands through J3.  Alternatively, it can be connected to a FIB through the DEM “front panel” control port.  A DEM produces ten channels of data at the J3 connector or it can mount an optional DOIM transmitter to produce one fiber optic channel of data for a FTM.  The data part of the data stream is either an incrementing or a pseudo-random pattern.

Testing a DEM requires a FIB for creating control signals and accepting data.  The best procedure would be to have the DEM tests be the FIB tests that use the DEM as a data source.  The part-under-test would shift to the DEM rather than the FIB.  Two specific tests are numbers 2 and 3 in 0 below.

The DEM is programmed according to the Detector Emulator Module Specifications on the ESE document page at  http://www-ese.fnal.gov/eseproj/index/svxii/svxii.htm.  Note that the DEM is set-up by sending “commands” out one of the port card ports and clocked (operated) through the other port.  For future reference, also notice that the DEM can monitor the commands it receives on the operating port and return, in the status words, what the state of the DDR would be if there were a DDR connected.  This might help debug software if the diagnostics were aware of this feature.

## 2.5	Testing VRBs

### 2.5.1	Simple VME tests.  Java software.  ESE/ESD tester.

These tests do not require a GSTM.  They check VRB internal operation and the VME interface, but do not test the FIB or SRC input ports.

- A VRB basic access test will start with single word writes and reads to dual-port memory in the range 0-3FFF (plus the module base address).  A simple memory test is adequate.

- The VRB emulation mode loop test requires a VME processor, VRB, and subrack.  The VRB simulates the FIB and VTM by generating its own "event" data.  Simulated SRC control messages are written by the processor over VME.  Simulated events are read out through VME and checked.

- Write a “readout” message to VRB from VME (three single-word writes).  The VRB should display the message “processing READOUT message”.

- Write a “scan” message to VRB from VME (two single word writes), VRB should display message “processing SCAN message”, poll byte count register for non-zero value.

- Program Receive Logic to generate incremental data and write to data buffers on receipt of “readout” message (assumes VTM not yet available)

- VME block transfers from VRB data output FIFO (A24/D32, A32/D32 and A32/D64), check block transfer for incremental data.

- Check VRB/VME interrupt assertion.  Requires only that the VME CPU be able to display some kind of message when it receives a VME interrupt (IRQ3).

### 2.5.2	GSTM based tests.

The GSTM loop test requires a VME processor, VRB, VFO, VTM, GSTM with SRC emulator adapter, GSTM with G-Link Transmitter adapters, optical splitters, and subrack.

The GSTM/SRC emulator sends SRC control messages through the VFO to the VRB.  The GSTM / G-Link Transmitter sends FIB data through splitters and VTM to the VRB.  The event data is read out through VME and checked by the controlling processor.

This test exercises most of the VFO, VTM and VRB hardware.  It will not test the CDF Calorimeter application unless a TAXI data source is available.

A first level test could repeat the above VME control logic tests, this time using the GSTM/SRC to send “readout” and “scan” messages via VRB Fanout and J3 backplane.  GSTM monitors “readout busy” and “scan busy” status signals from Fanout module.

Next, use the GSTM to drive VTM G-link input(s) and check Receive Logic event recognition.

Example VRB test loop pseudo-code:

(GSTM setup)

copy "expected VRB output pattern data" file into memory

write to VRB channel enable register

write to VRB reset register

wait ~20 milliseconds

start loop

write to GSTM (SRC emulator) to send readout command

write to GSTM (FIB emulator) to send data

read VRB output data FIFO until non-zero value (N) is returned

read N bytes from VRB output data FIFO

compare to pattern data in memory

stop if error

end loop

## 2.6	Testing VFOs

The VFO can not be tested independently beyond the initial power test.  The VFO is a part of the VRB tests and VFO problems can be identified best by replacing the suspect VFO with a “golden” VFO.

## 2.7	Testing VTMs

The VTM can not be tested independently beyond the initial power test.  The VTM is a part of the VRB tests and VTM problems can be identified best by replacing the suspect VTM with a “golden” VTM. Simple testing of the light monitoring circuitry on the VTM is included in the VRB power up diagnostics.  Extensive testing of this light monitoring circuitry will require additions to the VRB tests.

## 2.8	Testing FIBs

### 2.8.1	Simple VME tests.

VMEbus access and control simple tests that are basic read/write activities.  SVX hardware required: FIB and FFO.

- Exercise secondary local bus access by writing and reading to ……….

- Exercise primary local bus access by writing and reading to ……….

- Exercise Pedestal and Calculation RAM accesses by writing and reading to ……….

- Exercise NVRAM access, save and restore operations by writing and reading to ……….

- Exercise Control Registers and Command and Status Registers over VME by writing and reading specific bits.

### 2.8.2	More complicated VME tests.

These tests only require the FIB and FFO with the subrack controller but the tests are more complicated in that known data is moved through the FIB and checked for correct processing.

- FIB/FFO - Pipeline / Data Processing Tests

- Pipeline Test A - Data Pattern Check (see Test Flow Document, figure 3)

- Pipeline Test B - Pedestal Subtraction (see Test Flow Document, figure 4)

- Pipeline Test C - Calculation RAM Test (see Test Flow Document, figure 5)

- FIB/FFO - Control Path

- Control Path A - Command FIFO Test (see Test Flow Document, figure 6)

- Control Path B - Log FIFO Test (see Test Flow Document, figure 7)

- Control Path C - Address Controller, Command Receipt Test (see Test Flow Document, figure 8)

- Control Path D - Command Output Test (see Test Flow Document, figure 9)

- Control Path F (1) - Upload FIFO Test (refer to Test Flow Document, figure 10 - Data manually transferred into Upload FIFO from VME)

- Control Path G (2) - Upload and Download FIFO Test (refer to Test Flow Document, figure 10 - Data manually transferred from Download to Upload FIFO).

- Control Path E  - SVX Initialization Internal Loop-back (see Test Flow Document, figure 10)

- FIB/FFO - J3 Command Transfers

- Subrack Control Path Test A - Command Transfer Test (see Test Flow Document, figure 13)

- Subrack Control Path Test C - Command Output and Interrupt Test (refer to  Test Flow Document, figure 13, FFO providing continuous commands)

- FIB/FFO/FTM - FTM Control Output

- Subrack Control Path Test B - Control Output Test (see Test Flow Document, figure 15)

- Subrack Control Path Test B.1 - Control Output Test (refer to Test Flow Document, figure 15, FFO providing SRC command input (labeled lookup))

### 2.8.3	Tests utilizing the GSTM adapters.

These tests require the FIB, FFO and GSTM with the subrack controller.  The tests are more complicated in that known data is moved through the FIB input output connectors rather than accessed through the VME bus.  The Data Emulator Module is used to create data.

- G-Link Data Transfers

- *Software Currently NOT Available*   Subrack Pipeline Path Test A - Data Transfer Test (see Test Flow Document, figure 14) (Note: this test is NOT at speed)

- FIB/FFO/DEM - Pipeline / Data Processing Tests using DEM (Hardware required: FIB/FFO/DEM)

- Pipeline Test D(2) - Data Pattern Check (refer to Test Flow Document, figure 3 - DEM is providing SVX data)

- FIB/FFO/FTM/DEM - Pipeline / Data Processing Tests using DEM  (Hardware required:  FIBx2/FFO/FTM/DEM)

- *Software Currently NOT Available* Subrack Pipeline Path Test B - Data Transfer Test (refer to Test Flow Document, figure 3 - DEM providing SVX data, transferring to secondary FTM and corresponding FIB)

- FIB/FFO/DEM/GSTM - Pipeline / Data Processing Tests using DEM with G-Link Data Transfers (Hardware required:  FIB/FFO/DEM/GSTMx2)

- *Software Currently NOT Available* Subrack Pipeline Path Test C - Data Transfer Test (refer to Test Flow Document, figure 14 - DEM providing SVX data) (Note: this test is NOT at speed)

- *Software Currently NOT Available* Subrack Pipeline Path Test D - Data Transfer Test with GSTM providing SRC commands (refer to Test Flow Document, figure 14 - DEM providing SVX data) (Note: this test is NOT at speed)

- Additional tests required for production FIB

- *Software Currently NOT Available* - FINISAR light output monitoring (if required)

- *Software Currently NOT Available* - FIB to FFO status

## 2.9	Testing FFOs

FIB Fan-Outs are an integral part of the FIB tests.  Most of the FFO functionality is tested with these tests.  However, there are FFO specific tests that can assist with debugging the FFO.

## 2.10	Testing FTMs

All FTM tests require the use of a FIB and DEM.

All tests require the use of a FIB because the FTM has no VME accessible registers and is only a level translator for signals into and out of the FIB.  The only adjustable parts on board are the delay lines used to extract the Odd-Byte-Data-Valid signal.  The values of the delay lines will be determined in the prototype testing and individual variations from these values will be detected during data quality tests.  The DEM can generate Fiber Optic Port Card data to feed the FTM and FIB.

# 3	Integration Tests

## 3.1	Testing FIBs

- FIB/FFO/VRB - Pipeline / Data Processing Tests using DEM with G-Link Data Transfers.  (Hardware required:  FIB/FFO/VRB)

- Subsystem Pipeline Path Test A - Data Transfer Test (refer to Test Flow Document, figure 14 - DEM providing SVX data, VRB in checksum mode) (Note: test A is at speed)

- *Software Currently NOT Available* Subsystem Pipeline Path Test B - Data Transfer Test (refer to Test Flow Document, figure 14 - DEM providing SVX data, VRB SVX mode) (Note: this test is NOT at speed)

- FIB/FFO/VTM/PORT-CARD - Port Card Testing.  (Hardware required:  FIB/FFO/VTM/PORT-CARD)

- Subsystem Control Path Test A - Port Card Control Cable Tests (see Test Flow Document, figure 16)

- Subsystem Control Path Test B - Initialization Loop-back (see Test Flow Document, figure 17)

- Subsystem Control and Pipeline Path Test A - Calibration Inject and Readout (refer to Test Flow Document, figure 17, and run full DAQ cycle with Calibration Inject).