| X MEETING OF PERMANENT CONSULTATIVE COMMITTEE II: RADIOCOMMUNICATIONS INCLUDING BROADCASTING July 31 to August 3, 2007 Orlando, Florida, United States of America | OEA/Ser.L/XVII.4.2 CCP.II-RADIO/doc. 1441/07 18 June 2007 Original: English |
| --- | --- |
|  | WRC-07 AGENDA ITEM 1.12: No. 22.2 OF THE RADIO REGULATIONS |  |
|  | (Item on the Agenda: 4.1) |  |
|  | (Document submitted by the delegation of United States of America) |  |

Introduction:

In this contribution, the United States introduces a new proposal under Agenda item 1.12 for WRC-07.  This proposal responds to suggestions included in Section 6/1.12/5 of the CPM Report on changes in wording of No. 22.2 of the Radio Regulations.  These changes have been included in a Draft Inter-American Proposal (DIAP/1.12/9) in Document CCP.II-RADIO/doc. 1403/07 rev.2 as the result of a contribution to the IX Meeting of PCC.II in San Salvador.  After careful consideration of this very important regulation, which has been the subject of much deliberation and debate at several recent WRCs, the United States strongly believes that No. 22.2 of the Radio Regulations should NOT be modified in the manner sugggested in Section 6/1.12/5 of the CPM Report and in DIAP/1.12/9.  Instead, the United States opposes the changes suggested in Section 6/1.12/5 of the CPM Report and in the DIAP to the same effect in Document CCP.II-RADIO/doc. 1403/07 rev.2, and proposes to the contrary that No. 22.2 not be changed in any way by WRC-07.

A proposal to this effect is attached.

Attachment (NOC proposal from USA for No. 22.2)

ATTACHMENT

Agenda item 1.12

1.12	To consider possible changes in response to Resolution 86 (Rev. Marrakesh, 2002) of the Plenipotentiary Conference: “Advance publication, coordination, notification and recording procedures for frequency assignments pertaining to satellite networks” in accordance with Resolution 86 (WRC-03)

## Proposal for Agenda item 12:  Provisions of RR No. 22.2

Background information

RR No. 22.2 is the provision that governs the sharing between non-geostationary satellite (non-GSO) systems vis-à-vis geostationary satellite (GSO) networks in the fixed-satellite service (FSS) and the broadcasting-satellite service (BSS), except when it is explicitly disabled through a footnote in RR Article 5 or through a Resolution adopted by a World Radiocommunication Conference (WRC).

Section 6/1.12/5 of the CPM Report specifies that there are two and only two situations in the RRs with regard to No. 22.2.  In the first case, No. 22.2 has been removed from a particular FSS or BSS band, putting non-GSO systems on an equal footing with BSS or FSS GSO networks (as the case may be).  In the second case, No. 22.2 is quantified (e.g., No. 22.5I by meeting the epfd limits) and the provisions of Article 5 contain footnotes that preclude a non-GSO system from claiming protection from a GSO FSS/BSS network that is operating in accordance with the Radio Regulations (e.g., No. 5.484A).

In a frequency band where No. 22.2 has been disabled, the language of No. 22.2, current or modified, is irrelevant.  In the second case above, copying Article 5 text that obligates non-GSO systems not to claim protection from a GSO into No. 22.2 appears not to do anything that the RRs do not already do.  In both of these cases, then, there is no reason to change No. 22.2 in the manner suggested in the CPM Report.

The CPM Report fails to mention that there are additional cases of how No. 22.2 is applied that are not covered by Section 6/1.12/5.  One omitted case involves the numerous FSS and unplanned BSS bands where No. 22.2 remains applicable, but where no EPFD limits have been adopted and No. 9.11A is not applied.  An example of these bands is the pair of FSS bands at 37.5-42.5 GHz and 47.2-50.2 GHz.  In these bands, WRC-03 has held open the possibility that greater flexibility and sharing between non-GSO and GSO FSS systems may emerge.  It specified, in considerings g) and h) of Resolution 136 (Rev.WRC-03):

g)	that in the frequency range 37.5-50.2 GHz where there has been little or no deployment of satellite systems to date, administrations concerned with both GSO FSS and non-GSO FSS systems should be expected to exhibit flexibility in achieving the appropriate balance in the sharing environment;

h)	that this Conference, having considered the outcome of the ITU-R studies on this subject, as summarized in the CPM Report to this Conference, has decided that further studies are needed before the conditions for non-GSO FSS systems to share these bands with GSO FSS networks can reliably be determined,

Changing No. 22.2, which applies in the Resolution 136 bands, in the manner suggested in the CPM Report example, would prejudge these important studies, and possibly remove flexibility that WRC-03 wanted to preserve.

No. 22.2 of the Radio Regulations was modified at WRC-97, and appears to have worked very well since then.  The current regulation was the basis of EPFD limitations adopted at WRC-2000 and WRC-03 in a number of FSS and BSS frequency bands.

The only justification given in the CPM Report for changing the provsion is that the new words would duplicate material already in Article 5 footnotes.  This is not universally so in bands where No. 22.2 applies, as noted above.  Even if it were so, it is questionable at best whether adding language to No. 22.2 that is already in the RRs is a suitable justification for changing No. 22.2.  The regulations are not inconsistent today.

Finally, it simply does not make sense to revisit one of the most controversial and heavily debated regulations of recent WRCs without having very good cause to do so.  No. 22.2 is the basis for a number of limits on non-GSO satellite systems.  There are associated provisions in some bands that apply to GSO networks to provide some protection to non-GSO systems.  Changing the language of No. 22.2 in the manner suggested in the CPM Report may unintentionally disturb this delicate balance, and necessitate revisiting matters that are now successfully resolved.

For all of these reasons, the proposal below is that the text of No. 22.2 of the Radio Regulations NOT be changed in any way by WRC-07.

Proposal

NOC 		USA/1.12/X

No. 22.2

Reasons:  The reasons provided in the CPM Report are incomplete; other cases exist where changing No. 22.2 as shown in the CPM Report would prejudice the sharing situation.  Modifying such an important and historically controversial regulation as No. 22.2 could disturb a delicate balance that is reflected in many RRs, and could have unintended negative consequences.