GOLDSTONE SOLAR SYSTEM RADAR

VME DATA ACQUISITION SYSTEM

OPERATION MANUAL

Revision 1.0

June 26, 1998

Jet Propulsion Laboratory

California Institute of Technology

GSSR VME DATA ACQUISITION SYSTEM

OPERATION MANUAL

APPROVAL SHEET

APPROVAL

Robert E. Frye

System Designer

Dr. Raymond F. Jurgens

Group Leader

Dr. Martin A. Slade

Group Supervisor

Jet Propulsion Laboratory

California Institute of Technology

TABLE of CONTENTS

1 INTRODUCTION

1.1 Identification

1.2 Overview

1.3 Document Scope

1.4 Controlling Documents

1.5 Applicable Documents

2 INSTALLATION

2.1 Rack Mounting

2.2 Rear Panel

2.3 Front Panel

2.4 System Interrconnects

2.4.1 Peripheral Devices

2.4.2 Ethernet Interface

2.4.3 Timing Inputs

2.4.4 Signal Inputs

2.5 Firmware Configuration

3 OPERATION

3.1 System Configuration

3.1.1 Sample Rate

3.1.2 FFT Size

3.1.3 PSD Setup

3.1.3.1 Average Count

3.1.3.2 Accumulate Mode

3.1.3.3 Moving Average Filter

3.1.3.4 LOG/Linear Mode

3.1.4 Frequency Hopping Setup

3.1.4.1 States

3.1.4.2 Duration

3.1.4.3 Bandwidth

3.1.4.4 Composite Mode

3.1.4.5 Composite Average

3.1.4.5 Ephemeris File

3.1.5 Voltage Data Format

3.1.6 Target Object

3.2 Station Parameters

3.2.1 Transmit Station

3.2.2 Receive Station

3.2.3 Noise Temperatures

3.2.4 Sky Frequency

3.2.5 Transmit Power

3.2.6 Transmit Polarization

3.2.7 Receive Polarization

3.3 Record Enables

3.3.1 Voltage Samples

3.3.2 FFT Data

3.3.3 PSD Data

3.3.4 Cross Power Data

3.4 Data Products

3.4.1 Local Data Storage

3.4.2 Host File

3.4.3 Tape Archive

3.4.4 Screen Dump and GIF File

APPENDIX A Pre-Calibration Checklist

APPENDIX B DSS14 Boot Parameters

1	INTRODUCTION

1.1	Identification

The Goldstone Solar System Radar VME Data Acquisition System (VDAS) is the processing system described herein.  It is a component of the Goldstone Solar System Radar.

1.2	Overview

The Goldstone Solar System Radar (GSSR) is a telecommunication facility that uses the Deep Space Network (DSN) antennas and receivers to generate images of planets and asteroids.  Data products are generated from low resolution delay-Doppler radar imaging of over-spread targets by coherent processing of random hop frequency sequences.  The VME Data Acquisition System (VDAS) is a high-speed data acquisition, storage, processing and display computer.  Baseband radar return signals from DSN receivers are digitized at up to 10 MHz.  A high capacity disk drive stores data during real-time acquisition.  An 8 mm tape drive stores archived data.  Parallel processing elements receive acquired data and execute display algorithms.  A high resolution color console displays algorithm results.  The storage device stores data as bandwidth permits.  On-line mass data storage is provided.  Data archival and retrieval operates concurrently with real-time computation and display activity.  Hardware and software interfaces are provided for data acquisition, mass storage and information display.

1.3	Document Scope

This document defines the setup and operation of the Goldstone Solar System Radar VME Data Acquisition System.  Section 2 describes the VDAS functional requirements.  Section 3 defines the software and hardware design standards.

1.4	Controlling Documents

[1]	Goldstone Solar System Radar Data Acquisition System Design Requirements, Daryl Strobert, May 4, 1993.

[2]	Preliminary CW Radar System Specifications and Rational, Dr. Raymond F. Jurgens, January 25, 1994.

[3]	Goldstone Solar System Radar CW Imaging System Functional Requirements, Robert E. Frye, January 26, 1994.

1.5	Applicable Documents

[3]	Versatile Backplane Bus: VMEbus, IEEE Standard 1014-1987.

[4]	Small Computer System Interface - 2 (SCSI-2), ANSI X3T9.2/86, May 20, 1991.

[5]	EXB-8500 8 mm Cartridge Tape Subsystem User’s Manual, Exabyte Corporation, 510201-002, Revision 002, December 1991.

2	INSTALLATION

The VDAS components are a system unit with one Exabyte 8505 tape drive, a 17 inch, 1192 x 1024 pixel color monitor, a keyboard, a mouse and a Trak Systems model 8397-37 time code translator (TCT).  The system unit, keyboard and monitor are rack mounted.

2.1	Rack Mounting

The VDAS system unit and touch screen monitor are installed in a standard 19 inch rack with supplied slide mounts.  The system unit is 6 rack units high and 23 inches deep.  One rack unit (U) equals 1 3/4 inches.  The touch screen unit is 11U high and 23 inches deep.  The keyboard and TCT are each 1U high.

2.2	Rear Panel

The VDAS rear panel is shown in Appendix A.  Table 1 describes the connectors and functions.

Table 1  VDAS Rear Panel Connectors and Interfaces

| GROUP | DESIGNATOR | CONNECTOR | INTERFACE | DIRECTION | FUNCTION |
| --- | --- | --- | --- | --- | --- |
| CHANNEL x | I | TNC | Analog (2.5V | INPUT | Inphase Signal |
|  | Q | TNC | Analog (2.5V | INPUT | Quadrature Signal |
|  | CLK IN | TNC | ----- | ----- | spare |
|  | CLK OUT | TNC | TTL | OUTPUT | Sample Clock |
|  | TRIG IN | TNC |  |  | spare |
| TIMECODE IN | 5 MHz | TNC | Analog/TTL (1.0V | INPUT | Station Reference Clock |
|  | 1 PPS | TNC | TTL | INPUT | TCT 1PPS Reference |
|  | TIME | DB25S | RS-232, 9600,8,N,1 | INPUT | ASCII Time |
|  | VT-100 CONTROL | DB25S | RS-232, 19200,8,N,1 | I/O | VT-100 Control Console |
|  | MOUSE | DB25P | RS-232 | INPUT | Serial Mouse Input |
| DAS PARALLEL COMM | PORT A | ----- | ----- | ----- | spare |
|  | KEYBOARD | DB25S | special | INPUT | Keyboard Input |
| STATION CONTROL | VIDEO MONITOR | DB37S | special | OUTPUT | SVGA Video Output |
|  | RF MATRIX 1 | ----- | ----- | ----- | spare |
|  | RF MATRIX 2 | ----- | ----- | ----- | spare |
|  | IEEE-488 | IEEE-488 | GPIB | I/O | GPIB Control |
| SCSI | ----- | ----- | SCSI | I/O | spare |
| LAN | ----- | AUI | Ethernet | I/O | Network I/O |
| DEBUG | ----- | DB25S | RS-232, 9600,8,N,1 | I/O | VxWorks debug |
| SPARE x | 1 | TNC | TTL | INPUT | External RESET* Input |
|  | 2 | TNC | ----- | ----- | spare |
|  | 3 | TNC | ----- | ----- | spare |
|  | 4 | TNC | ----- | ----- | spare |

2.3	Front Panel

The VDAS front panel is shown in Appendix A. Table 2 describes the connectors and functions.

Table 2  VDAS Front Panel Connectors and Interfaces

| DESIGNATOR | CONNECTOR | INTERFACE | DIRECTION | FUNCTION MT/FT |
| --- | --- | --- | --- | --- |
| POWER | ----- | ----- | ----- | AC power ON/OFF |
| RESET | ----- | ----- | ----- | System RESET |

2.4	System Interconnects

2.4.1	Peripheral Devices

2.4.2	Ethernet Interface

2.4.3	Timing Inputs

2.4.4	Signal Inputs

2.5	Firmware Configuration

3	OPERATION

3.1	System Configuration

The VDAS has parameters settings that adjust the system operation to match a target object.  The operating parameters are set during the pre-calibration phase of the radar track.

3.1.1	Sample Rate

Set the A/D sample rate to the value required for the target object.  The VDAS will calculate the closest available sample rate and set the A/D clock dividers accordingly.

3.1.2	FFT Size

Set the FFT size to the value required for the target object.  The available FFT sizes are: 128, 256, 512, 1024, 2048, 4096, 8192 and 16384.

3.1.3	PSD Setup

The VDAS displays and stores real power spectral density (PSD) data derived from the complex FFT data.  Adjustment parameters are provided for data generation and display functions.

3.1.3.1	Average Count

Sequential PSDs may be averaged before display and storage.  A count field is provided to specify how many averages are added before results are available.  This field is used when the sampling system is faster than the display system and the display cannot keep up with incoming data.  The plot and storage rate may be reduced without losing sampled data.  The average is restarted after every result.  The result is not divided by the total count.  The accumulated data is provided as a sum of previous results.  An average count of zero disables PSD averaging.

3.1.3.2	Accumulate Mode

The PSD Accumulate Mode operates with the PSD Average Count to produce averaged PSDs for storage and display.  Accumulate Mode retains the accumulated PSD over successive results, providing a running PSD average. The result is not divided by the total count.  The accumulated data is provided as a running sum of previous results.

3.1.3.3	Moving Average Filter

The VDAS provides a one-dimensional moving average (sliding) filter for real-time smoothing of displayed data.  The filter width is specified as an odd number of data points to average.  The filter replaces the center point with the average of the surrounding points, on a point-by-point basis.  The result is a smoothed PSD plot.  The filter data is for display only and is not stored to disk.

3.1.3.4	LOG/Linear Mode

The PSD plots may be set to display data on a LOG or linear scale.  The scale mode has no effect on stored data.

3.1.4	Frequency Hopping Setup

The VDAS produces real-time composite, baseline removed, frequency de-hopped data for display.  The VDAS tracks a frequency hopped signal source in real-time and produces a composite SNR plot of the target object.  Set the PSD Average Count to zero and Accumulate Mode OFF to run in hop tracking mode.  The VDAS compensates for the round-trip light time using the object ephemeris data.

3.1.4.1	States

The number of hop states pecifies the number of frequency hops used to illuminate the object.  The options are 2, 4 and 8 frequencies or “colors”.

3.1.4.2	Duration

The frequency hop duration specifies the dwell time in seconds for a given frequency in a hop sequence.  The minimum value is one second per hop.  A typical value is 30 seconds per hop.

3.1.4.3	Bandwidth

The frequency hop bandwidth specifies the total hopping bandwidth in Hz, including guard bands at the edges.  The hopping bandwidth is usually the same as the sample rate and the front end passband filter width.  The system calculates the hop spacing from the hop bandwidth and number of hops in the sequence.

3.1.4.4	Composite Mode

The de-hopped composite data may be generated using either of two methods, SIGNAL or SNR.  The SIGNAL mode calculates (S + N) - N.  The SNR mode calculates (S + N) / N - 1.  The default setting is SNR mode.

3.1.4.5	Composite Average

The composite PSD data may be averaged over multiple, bi-static transmit/receive cycles using the Composite Average feature.  The SNR composites are accumulated and saved in system memory until the average is restarted.  The composite provides automatic summing of object data over the entire track.  Composite Average feature is enabled for typical GSSR objects.  The SNR data is for display only and is not stored.

3.1.4.5	Ephemeris File

The ephemeris file name and path is set before enabling the frequency hopping mode.  The ephemeris file is read from the specified path to allow real-time calculation of object round-trip-time and header parameters.  The ephemeris for a target object is given in the PUNCH.OUT file for that object.  Only the receive records are used (lines ending in “R”), so the file may be edited to discard transmit records (lines ending in “T”) and moved to the local disk, GSSR0_DR1, for faster loading.  If the file fails to load, frequency hopping will remain disabled.  The ephemeris will not load if the date and time span do not fall within the current VDAS date and time.  The ephemeris will not load if the target object field does not match the object specified in the VDAS setup.

3.1.5	Voltage Data Format

Voltage data samples may be stored to disk as 16 bit signed shorts or 8 bit signed chars.  The A/D subsystem is 12 bits.   8 bit storage is specified only when the dynamic range is within the range of - 128 to +127.

3.1.6	Target Object

The target object is specified from the list of possible objects.  The selected object specifies an object number contained in the ephemeris file, that must match for the ephemeris to be loaded.

3.2	Station Parameters

The VDAS has station and radio system parameters that are included in the header for target object data.  The station parameters are set during the pre-calibration phase of the radar track.

3.2.1	Transmit Station

The transmit station is specified by selecting the station number from a list of Goldstone antenna sites.  The default transmit station is DSS14.

3.2.2	Receive Station

The receive station is specified by selecting the station number from a list of Goldstone antenna sites.  The default receive station is DSS14.

3.2.3	Noise Temperatures

The system noise temperatures, in degrees K, for up to eight complex channels are entered for inclusion in the header of all recorded data.  The values come from pre-calibration data provided by station operators.

3.2.4	Sky Frequency

The sky frequency carrier, in MHz, is specified for inclusion in the header of all recorded data.  The default value is 8510 MHz.

3.2.5	Transmit Power

The transmit power level in kW is specified for inclusion in the header of all recorded data.  The value is typically 460 to 480 kW.  The value comes from pre-calibration data provided by station operators.

3.2.6	Transmit Polarization

The transmit polarization is specified for inclusion in the header of all recorded data.  The value is normally LCP.  The value comes from pre-calibration data provided by station operators.

3.2.7	Receive Polarization

The receive polarization is specified for inclusion in the header of all recorded data.  The value is specified on a per-channel basis and is normally RCP for channel one and LCP for channel two.  The value comes from pre-calibration data provided by station operators.

3.3	Record Enables

The disk recording of individual data types is selectable using record enable selectors.

3.3.1	Voltage Samples

The recording of voltage samples is controlled with the VOLT Recording selector.  The A/D subsystem always produces voltage samples,  even if volt recording is disabled.

3.3.2	FFT Data

The recording of FFT data is controlled with the FFT Recording selector.  The FFT subsystem produces spectra if FFTs or PSDs are enabled,  even if FFT recording is disabled.

3.3.3	PSD Data

The recording of PSD data is controlled with the PSD Recording selector.  The PSD subsystem produces spectra for display,  even if PSD recording is disabled.

3.3.4	Cross Power Data

The recording of Cross Power (XPWR) data is controlled with the XPWR Recording selector.  The Cross Power subsystem produces spectra for display,  even if XPWR recording is disabled.

3.4	Data Products

The VDAS creates local, binary data files on the local 10 GB disk drive.  The drive content is supported by a directory structure located in system memory.  Tracks are identified by disk sector range after a track and data product files are generated from the stored binary data.

3.4.1	Local Data Storage

Three disk pointers are used to access data on the 10 GB data drive.  The EOD pointer indicates end-of-data, the first unused sector after used sectors.  The START pointer and END pointers indicate the inclusive range of sectors to use when generating host or tape data files.

3.4.2	Host File

Binary or ASCII data may be transferred to a network host computer for further analysis.  The host must be NFS mounted under VxWorks.  The Goldstone VDAS is set at installation time to automatically NFS mount the INTRUDER workstation.  A valid path for host files is “/h3/robert”.

The workstation name “intruder:” must NOT be specified in the path or the transfer will not use NFS and will fail.  VxWorks knows that “/h3” refers to INTRUDER.

3.4.3	Tape Archive

A binary tape archive may be generated from stored disk data.  The data output range is specified by the START and END disk sector pointers.  The tape is a binary copy of the data disk, and is not in TAR format.  The tape is workstation compatible, and is read using the C language “read()” command.

3.4.4	Screen Dump and GIF File

The data screens shown on the VDAS system console may be output directly to a printer.  The printer output is grayscale, for conventional laser printers.  The grayscale output is reverse video for best hardcoopy viewing and faxing.  A color “GSSRIMAGEx.gif” file is generated at the same time for later viewing or printing.  The print utility is located at Goldstone and id located on intruder:/h3/robert/dss14pr.  The utility is run on the workstation, and asks the user to mouse select a VDAS screen for printing.  The print job is sent to the “lpr” printer and a sequential .gif file is generated for future use.

APPENDIX A  GSSR VME DAS PRE-CALIBRATION CHECKLIST

GSSR VME DAS

CW Radar Track Configuration Parameters

Robert Frye

16 Nov 95

Revision C

1.	OBJECT NAME			__________________________

Ephemeris file code #		_________

2.	TRACK DATE (local)		____ ______ ____  Day ______________

3.	TRACK Tx WINDOW	(local)		____:____  to  ____:____

4.	SAMPLE RATE			___________ Hz

or	________ u sec

5.	RECORD PARAMETERS

VOLTAGE samples

16 bit (short)	____

8 bit (char)	____

FFTs	____

PSDs	____

6.	FFT SIZE

128	____

256	____

512	____

1024	____

2048	____

4096	____

8192	____

16384	____

7.	HOP STATES			____

8.	TOTAL HOP BANDWIDTH		___________ Hz	(Note 1)

9.	HOP DWELL TIME			_____ integer sec

10.	PSD AVERAGE COUNT		_____

11.	EPHEMERIS FILE NAME		____________________.pch

12.	TRANSMIT STATION

DSS 12	____

DSS 13	____

DSS 14	____

DSS 15	____

DSS 24	____

13.	RECEIVE STATION

DSS 12	____

DSS 13	____

DSS 14	____

DSS 15	____

DSS 24	____

14.	SKY FREQUENCY			_______ MHz

15.	TRANSMITTER OUTPUT POWER	_______ kW

16.	NOISE TEMPERATURE

CH 1	______ deg K

CH 2	______ deg K

CH 3	______ deg K

CH 4	______ deg K

CH 5	______ deg K

CH 6	______ deg K

CH 7	______ deg K

CH 8	______ deg K

17.	ANTENNA AZIMUTH			______ deg

18.	ANTENNA ELEVATION		______ deg

Note 1:	Sample HOP BANDWIDTH

HOP STATES	4

HOP BANDWIDTH	20 kHz

HOP SPAN	15 kHz

PLO BANDWIDTH	5 kHz

|<------- Total Hop Bandwidth = 20 kHz -------->|

|                                               |

|<- 5 kHz ->|<- 5 kHz ->|<- 5 kHz ->|<- 5 kHz ->|

|-----------------------------------------------|

|     |     |     |     |     |     |     |     |

|    hop    |    hop    |    hop    |    hop    |

|     |     |     |     |     |     |     |     |

|-----------------------------------------------|

|     |<------- Hop Span = 15 kHz ------->|     |

APPENDIX B  GSSR VME DAS DSS14 BOOT PARAMETERS

[VxWorks Boot]: p

boot device          : scsi;1,0

processor number     : 0

host name            : intruder

file name            : /GSSR0_DR1/vxWorks

inet on ethernet (e) : 158.154.2.20:ffffff00

host inet (h)        : 158.154.2.15

gateway inet (g)     : 158.154.2.1

user (u)             : robert

flags (f)            : 0x0

target name (tn)     : gssrvme0

startup script (s)   : /GSSR0_DR1/dss14136.scr

other (o)            : ei