MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A09197 | In-Flight Anomaly Number -- | Contractor Report Number E-087 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title TRANSDUCER ELECTRICAL OUTPUT EXCEEDED LIMITS |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT -- | Sys_Lvl N | Misc Codes A (5) B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE LH2 ULL PRES TRNSDCR | PART# PD7400098-039 | SER/LOT# 1409 | MANUFACTURER GULTON |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE LH2 ULL PRES TRNSDCR | PART# PD7400098-039 | SER/LOT# 1409 | MANUFACTURER GULTON |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EG - SIG HI OR LO | Cause MMW - MFG-MOV-WORK |
| System ELECTRICAL | Defect -- | Material B - CIRCBD | Work Contact J. ADAMS | Fail Date 05/01/1985 |
| Received at MSFC 05/24/1985 | Date Isolated -- | FMEA Reference 3.1.2.9 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location GULTON | Symptom EG - SIG HI OR LO | Time Cycle -- |
| Effectivity Text LWT-12 AND SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 02/09/1995 | CN RSLV SBMT 01/16/1986 | Defer Date -- | Add Date -- | R/C Codes 0 - EXPL -- -- |
| Assignee |
| Design W. COBB | Chief Engineer -- | S & MA R. JACKSON | Project J. BREWER | Project MGR -- |
| Approval |
| Design W. COBB | Chief Engineer -- | S & MA R. JACKSON | Project J. BREWER | Project MGR -- |
| PAC Assignee G. MILLER | PAC Review Complete GM | MSFC Closure Date 02/21/1986 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description REF: TRANSDUCER EXCEEDED MAX ALLOWABLE ELECTRICAL OUTPUT ERROR DURING ACCEPTANCE TESTING AT VENDOR |
| Contractor Investigation/Resolution 5/24/85 - NO CONSTRAINT TO FUTURE LAUNCHES. EACH TRANSDUCER MUST PASS ACCEPTANCE TESTING BEFORE IT IS SHIPPED TO MMC FOR INSTALLATION ONTO ET. 7/2/85 UPDATED FROM PRB MTG 6-20-85 AS FOLLOWS - CONCLUSION OF INVESTIGATION WAS THAT THE TRANS- DUCER HAD BEEN DROPPED, CAUSING INTERNAL DAMAGE THAT RESULTED IN FAILURE DURING ATP AT THE VENDOR'S PLANT. 7/3/85 STATUSED FROM UPDATED CAPS (E-087A) AS FOLLOWS - FAILURE ANALYSIS IS IN PROGRESS AT THE VENDOR ON THE HYDROGEN ULLAGE PRESSURE TRANSDUCER. THE UNIT EXCEEDED THE MAXIMUM ALLOWABLE ERROR IN THE OUTPUT VOLTAGE VS. INPUT PRESSURE BY ONE TO TWO PERCENT DURING VENDOR ACCEPTANCE TESTING. THE TRANSDUCER HAD PASSED THE SAME TEST REQMNTS DURING THE VENDOR PREACCEPTANCE TESTING. PRE- LIMINARY RESULTS INDICATE THAT THE PROBABLE CAUSE OF FAILURE WAS THAT THE TRANSDUCER WAS DROPPED OR STRUCK DURING HANDLING. 8/15/85 PRB STATUS - MARGINAL ERROR. FA COULD NOT POSITIVELY CONFIRM CAUSE; HOWEVER, IT IS BELIEVED THAT THE MOST PROBABLE CAUSE WAS THAT THE UNIT WAS DROPPED DURING HANDLING. ECD IS 8-31-85. 10/17/85 PRB STATUS - FURTHER INVESTIGATION REVEALED NO MECHANICAL PROBLEM. FA DOCUMENTATION TO BE COMPLETED BY VENDOR. CAPS TO BE CLOSED AS WORKER ERROR. 11/21/85 PRB STATUS - FA FOUND NOTHING. CAPS TO BE CLOSED AS WORKER ERROR. ECD IS 12-13-85. 1/16/86 RESOLUTION - FAILURE ANALYSIS OF THE DEFECTIVE TRANSDUCER FOUND THAT THE TRANSDUCER OUTPUT VOLTAGE WAS HIGHER AT ALL PRESSURES IN THE OPERATING RANGE THAN THE VOLTAGES RECORDED DURING IN-PROCESS TESTING OF THE UNIT. NO DEFECTS, OTHER THAN THE HIGH OUTPUT VOLTAGE, WERE FOUND IDENTICAL FAILURES HAVE OCCURRED ON TRANSDUCERS WHICH WERE KNOWN TO HAVE BEEN DROPPED BY THE MANUFACTURER'S PERSONNEL. THEREFORE, THE PROBABLE CAUSE OF THIS FAILURE WAS DETERMINED TO BE INADVERTENT MISHANDLING/DROPPING OF THE UNIT. RECURRENCE CONTROL - NO ACTION IS REQUIRED. THE DEFECT WAS DISCOVERED IN ACCEPTANCE TESTING. THE MANUFACTURER'S TRAINING OF THE WORKERS ALREADY EMPHASIZES THE DELICATE NATURE OF THE TRANSDUCERS AND THE FREQUENCY OF OCCURRENCE IS LOW RECOMMEND THIS PROBLEM REPORT BE CLOSED |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A09197 | IFA# -- | Contractor RPT# E-087 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD7400098-039 | Asmnt Part Name GH2 ULL PRES TRNSDCR | Asmnt Serial/Lot# 1409 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD MMW - MFG-MOV-WORK | FAIL MODE EG - SIG HI OR LO |
| Asmnt FMEA 3.4.1.1 | Asmnt FM 1 | FMEA CSE AA | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |