FPIX3 chip tests

Feb. 9, 2007

Tom Zimmerman

Fermilab - Particle Physics Division

Tests were performed on the FPIX3 chip in order to better understand sources of instability, and to arrive at an optimal configuration.  A simplified diagram of the relevant circuits is shown below.

The pixel sensor feeds a charge integrator, followed by a X4 gain stage.  One master DC bias current of approximately 1 uA drives multiple current DACs that can be programmed to set the required internal bias voltages and bias currents.

General biasing issues

Programmable bias currents are derived from internal current mirrors that are driven by current DACs (which are all referenced to the master bias current set by an external resistor).  Programmable bias voltages are generated from current DACs that drive internal 80K resistors.  One very important programmable voltage reference is Vref, which sets the output operating voltage of the second stage.  The output of this stage directly drives a PMOS transistor (MCOMP in the diagram) that serves as the input stage of an 8-stage comparator.  All of the 8 comparator thresholds are independently set by DACs.  The effective threshold of any comparator is then determined by the difference between its threshold setting and the Vref setting.

The comparator bias current Icomp is a critically important parameter.  It affects both the comparator delay and, unintentionally and unfortunately, the stability of the chip (which will be addressed in a later section).  Icomp is determined by (Vgs-Vt)^2 of the MCOMP PMOS transistor, and should nominally sit at about 0.8uA.  Vt is dependent on process variations, temperature, and radiation dose.  Vgs is simply (Vref – Vdda), so it depends on both Vref and Vdda.

Two options are available for setting the master bias current for the chip, with different implications for the comparator bias.  These are discussed below.

Biasing options:

The master bias can be set in one of two ways:  with a resistor from RefRes to ground, or with a resistor from Vmaster to ground, with different implications for the chip sensitivity to variations in parameters like process variables, threshold shifts, temperature, analog supply voltage, etc.

1.  When using a resistor from RefRes to ground, the master current is very stable and is determined only by a diode drop voltage that is duplicated across the external resistor.  Internal bias currents and voltages (like Vref) are thus very insensitive to parameter and Vdda variations, except for the comparator bias current Icomp, which is quite sensitive since it depends not only on the Vref setting but also on Vdda.  For example, lowering Vdda by 4% (100 mV) has almost no effect on the value of Vref or on the internal threshold (Vref – Vth0), but causes an 18% reduction in Icomp.

2.  When using a resistor from Vmaster to ground, the master current is somewhat affected by parameter variations and Vdda, meaning that the internal bias currents and voltages are also somewhat affected.  However, the Icomp sensitivity is considerably lower than with the RefRes method, since both Vdda and Vref tend to move together.  For example, lowering Vdda by 4% (100 mV) decreases both the threshold level and Icomp by about 5%.

Run-to-run (or even wafer-to-wafer) variations could thus have a noticeable impact on comparator current draw and power dissipation when using method 1.  Method 2 results in some variation in internal bias levels (not a big problem), but offers a more consistent comparator bias level (desirable).  Since the comparator bias level is critical to stability, method 2 is highly recommended.

The following tests were performed with the two different biasing methods, and show the sensitivity of Vref and Vth0 to the value of the bias resistor and changes in Vdda. For these tests, the Vref DAC was set to 202 (the default FFR value), and the Vth0 DAC to 182.  Notice that with method 1, the digital to analog conversion factor (∆ Vth/count) remains very stable with varying Vdda, but the supply current draw varies substantially (due to variation in comparator bias).  With method 2, the conversion factor varies somewhat with Vdda, as does comparator bias, but the comparator bias variation is much smaller than observed with method 1.

REFRES bias (method #1)

| Rbias1 | Vdd - Vref | Iavdd (total) | Vref - Vth0 | (∆ Vth)/(DAC count) |
| --- | --- | --- | --- | --- |
| 561K | 0.654 V | 65 mA | 172 mV | 9.2 mV |
| 585K | 0.734 V | 75 | 165 | 8.7 |
| 618K | 0.832 V | 90 | 156 | 8.2 |

Use Rbias = 585K, and vary Vdd:

| Vdda | Vdd - Vref | Iavdd (total) | Vref - Vth0 | (∆ Vth)/(DAC count) |
| --- | --- | --- | --- | --- |
| 2.4 | 0.639 V | 60 mA | 165 mV | 8.7 mV |
| 2.5 | 0.734 V | 75 | 165 | 8.7 |
| 2.6 | 0.834 V | 90 | 165 | 8.7 |

Vmaster bias (method #2)

| Rbias1 | Vdd - Vref | Iavdd (total) | Vref - Vth0 | (∆ Vth)/(DAC count) |
| --- | --- | --- | --- | --- |
| 1.382 Meg | 0.71 V | 75 mA | 170 mV | 8.5 mV |
| 1.440 Meg | 0.78 V | 80 | 161 | 8.5 |
| 1.500 Meg | 0.84 V | 90 | 154 | 8.2 |

Use Rbias = 1.440 Meg, and vary Vdd:

| Vdda | Vdd - Vref | Iavdd (total) | Vref - Vth0 | (∆ Vth)/(DAC count) |
| --- | --- | --- | --- | --- |
| 2.4 | 0.771 V | 75 mA | 152 mV | 8.1 mV |
| 2.5 | 0.776 V | 80 | 161 | 8.5 |
| 2.6 | 0.781 V | 85 | 170 | 9.0 |

Biasing for FFR stability

The resistor values chosen in the previous section were based on achieving the nominal DC bias conditions with the FFR (Fire Fighter Reset) register settings.  Unfortunately, the FFR default conditions usually result in oscillation, obviously not a desired result of any master reset.  (The major reason for the oscillation is that FFR turns on all 8 comparators – more on this later).  Therefore, a revised Vmaster bias resistor of 910K is suggested, which essentially kills the bias of the second stage and comparators, inhibiting oscillation and allowing a “clean” FFR.  This changes the granularity of all the DACs.  For example, the reference voltage granularity changes from approximately 7.5 mV/count to 12 mV/count, which is still acceptable.

The FFR default register settings are:

Ibp1=100

Ibp2=74

Ibb=29

Iff=13

Vref=202

Vfb2=172 (always 30 counts less than Vref)

Voltage reference DACs are approximately 7.5 mV/count (varies chip to chip) with a 1.44Meg resistor on Vmaster

With a bias resistor of 910K on Vmaster, the registers should be programmed as follows:

Ibp1=0

Ibp2=0

Ibb=18

Iff=8

Vref=122 (this depends on the desired comparator bias and speed)

Vfb2=103 (always 19 counts less than Vref)

Voltage reference DACs are approximately 12 mV/count (varies chip to chip)

Comparator bias issues

The comparator bias is probably the most important parameter that can be controlled by the user (through the Vref setting), since it affects the chip stability.  The total comparator bias current is affected by Vref, which sets the current per comparator stage, and the threshold settings Vth0-7, which determine how many of the eight comparator stages are enabled.   Comparator bias levels were measured on an 8-chip module with a sensor.  The revised master bias resistor value of 910K was used, and Vdda was set at 2.3.  The following table shows the measured comparator bias level (per comparator) on one chip as a function of Vref.

| Vref DAC | Vdda - Vref | Ibias per comparator |
| --- | --- | --- |
| 138 | 0.65 V | 0.13 uA |
| 135 | 0.69 V | 0.17 uA |
| 130 | 0.75 V | 0.35 uA |
| 125 | 0.81 V | 0.58 uA |
| 120 | 0.87 V | 0.87 uA |
| 115 | 0.93 V | 1.22 uA |
| 110 | 0.99 V | 1.62 uA |

Over all 8 chips, there is a chip to chip spread in comparator bias current for a given Vref setting.  In the module tested, this spread was a substantial 50% from the lowest to the highest.  The results shown in the table are for the chip that has the lowest comparator bias for a given Vref setting, so probably represent the “low case” more than the “nominal case”.  If consistent chip to chip comparator delay is desired, then the Vref setting may need to be “tweaked” for each chip based on measurements.

The comparator speed is directly affected by the bias level.  Measurements are shown below for a chip that has a charge gain of 340 mV/fC and a DAC granularity of 12 mV/count.  The threshold is always set to 10 counts below Vref, but there is a threshold offset of several counts, which results in an effective threshold setting of about 1400 e.  These measurements were performed by applying a “triangular” input pulse to the FPIX test injection input, with a 60 ns leading edge and a 2 us trailing edge.  The delay is measured from the time that the comparator input crosses the set threshold.  The time walk effect from different pulse amplitudes is not taken into account here, so would need to be added to the measured delay.

Input = 1600 e

| Vref DAC | Vth0 DAC | Delay from threshold crossing |
| --- | --- | --- |
| 125 | 115 | --- |
| 120 | 110 | --- |
| 115 | 105 | 99 ns |
| 110 | 100 | 78 ns |

Input = 1800 e

| Vref DAC | Vth0 DAC | Delay from threshold crossing |
| --- | --- | --- |
| 127 | 117 | --- |
| 125 | 115 | 176 ns |
| 120 | 110 | 111 ns |
| 115 | 105 | 89 ns |

Input = 2000 e

| Vref DAC | Vth0 DAC | Delay from threshold crossing |
| --- | --- | --- |
| 133 | 123 | --- |
| 130 | 120 | 186 ns |
| 125 | 115 | 119 ns |
| 120 | 110 | 83 ns |
| 115 | 105 | 61 ns |

Input = 2400 e

| Vref DAC | Vth0 DAC | Delay from threshold crossing |
| --- | --- | --- |
| >141 |  | --- |
| 141 | 131 | 275 ns |
| 135 | 125 | 169 ns |
| 130 | 120 | 119 ns |
| 125 | 115 | 85 ns |
| 120 | 110 | 68 ns |
| 115 | 105 | 54 ns |

Input = 3600 e

| Vref DAC | Vth0 DAC | Delay from threshold crossing |
| --- | --- | --- |
| 135 | 125 | 93 ns |
| 125 | 115 | 57 ns |
| 115 | 105 | 42 ns |

Input = 7200 e

| Vref DAC | Vth0 DAC | Delay from threshold crossing |
| --- | --- | --- |
| 135 | 125 | 60 ns |
| 125 | 115 | 43 ns |
| 115 | 105 | 33 ns |

Gain and calibration issues

The sensor capacitance from a standard pixel input to the sensor backside is 10 fF.  This is found by measuring the total backside capacitance of a sensor and dividing by 23*128*(# of chips).  (There are 20 columns of 128 standard size pixels and 2 columns of 128 pixels that are 50% larger, giving effectively “23 columns of standard size pixels”).  This measurement is quite consistent and varies very little over different sensors.  By applying a known voltage step to the sensor backside, a known charge can be injected into each pixel, thereby allowing an absolute calibration of the FPIX chip.  When this is done over a number of FPIX chips, the gain is found to vary substantially.  This is not too surprising, since this gain is set mostly by the integrator feedback capacitance, which is formed using field oxide that is not well controlled.  The gain observed over a limited number of chips was in the range of 290 - 500 mV/fC, which is quite a large variation chip to chip.  It may therefore be desirable to calibrate each chip in a system by using this method.

Stability problems

FPIX chips are observed to have serious stability problems, especially when they are coupled with sensors.  Oscillation can result from any or all of several on-chip unintended positive feedback paths.  These paths are enabled by the presence of parasitic resistance in the analog ground and supply lines, as shown in the FPIX block diagram.  Each of these positive feedback paths will be discussed.

In one potential feedback path, a change in comparator current couples through the Vdda parasitic resistance back to the DAC reference circuits and causes a reduction in DAC currents, which in turn causes a reduction in Vref, propagating through the second stage and causing a further change in comparator current that reinforces the original change.  The gain of this positive feedback path can easily be killed by bypassing Vref externally with 0.1 uF or more.  (Any bypass capacitor on Vmaster must be at least 10 times smaller than the Vref bypass to insure that this positive feedback path is suppressed).

A DC stability problem exists in the same area of the circuit that can be caused by internal transistor leakage current.  There is an unintentional leakage current (labeled Ileak in the block diagram) from the DAC programming switches that can divert a significant portion of the master Ibias under certain circumstances.  There are 14 DACs, each with 256 sections, so even a small leakage current per switch transistor can have a big effect.  The leakage is very dependent on the Vgs of the switch (and on other parameters like temperature), and can vary substantially from run to run.  The Vgs seen by the switch is (Vddd – Vdda), since the logic driving the switches is powered by the digital supply.  (Vgs here is normally negative, since the transistor is PMOS).  On the particular chip tested, the leakage current becomes noticeable for Vgs < 0, so if the value of Vdda is raised above Vddd, the leakage begins robbing significant current from the master reference.  The portion of the master Ibias current seen by its PMOS mirror transistor thus begins decreasing significantly.  This means that all programmed bias currents and voltages on the chip begin decreasing, including Vref.  Lowering Vref increases the comparator bias current significantly, raising the Vdda current.  The end result is that when Vdda is raised above Vddd, the internal biases are corrupted and the Vdda supply current increases rapidly with voltage.  This unintended behavior leads to the following constraint:  Vdda should always be set to a value that is approximately 0.2 volts lower than Vddd.  This insures that the unintentional leakage current always remains insignificant, even with elevated temperatures and/or process variations over different wafers.

Two other more problematic positive feedback paths exist, both of them from the comparator section back to the integrator.  These paths are enabled by the parasitic ground and supply resistance.  A changing comparator current causes voltage changes on both supply and ground, which each couple charge to the integrator input through a capacitance (parasitic capacitance from Vdda to input, and sensor capacitance from ground to input).  In both cases, the parasitic charge coupled to the integrator causes a voltage change at the output of the second stage that reinforces the original change in comparator current, resulting in positive feedback.  (This behavior could have been avoided by using separate supply nets for the comparators).

Multiple factors affect the strength of this feedback, some of which are under user control and others which are not:

- Comparator gm (depends on comparator bias and # of sections used)

- Parasitic R in ground supply bus (shunted somewhat by the substrate)

- Parasitic R in Vdda supply bus

- Parasitic C from Vdda to integrator input (several fF)

- Sensor C from external ground to integrator input

- Integrator feedback C (sets the FPIX charge gain)

Unfortunately, there can be a substantial chip to chip variation in most of these factors.  This results in an unavoidable chip to chip variation in sensitivity to oscillation, given identical master bias and DAC settings.

Stability tests with an 8-chip module

A module with 8 chips bump bonded to a sensor was used to investigate stability as a function of

- How many of the 8 comparator sections on each chip are enabled (a comparator is disabled by setting its threshold to 255)

- Vref setting

- How many of the 8 chips on the module are enabled

The module has one common Vdda supply and one common Vddd supply.  In the following tables, “Min. Vref” is the minimum Vref register value found to result in stability.  However, since a Vref value any lower would result in oscillation, practical values of Vref for operation should be well above the minimum Vref for safety margin.

3 comparator sections enabled per chip

| Chips enabled | Min. Vref |
| --- | --- |
| 1 | 118 |
| 2 | 118 |
| 3 | 116 |
| 4 | 114 |
| 5 | 115 |
| 6 | 112 |
| 7 | 114 |
| 8 | 122 |
| 1-8 (all) | 135 |
| 1-7 | 122 |
| 4,5,6,7 | 118 |
| 4,6,7,8 | 126 |
| 6,7,8 | 126 |
| 4,6,7 | 117 |

8 comparator sections enabled per chip

| Chips enabled | Min. Vref |
| --- | --- |
| 1-8 (all) | 147 |
| 1-7 | 137 |
| 8 | 138 |
| 4 | 130 |

4 comparator sections enabled per chip

| Chips enabled | Min. Vref |
| --- | --- |
| 1-8 (all) | 139 |
| 1-7 | 127 |
| 8 | 126 |
| 4 | 120 |
| 4,5,6,7 | 124 |
| 4,5,6,8 | 135 |

2 comparator sections enabled per chip

| Chips enabled | Min. Vref |
| --- | --- |
| 1-8 (all) | 130 |
| 1-7 | 113 |
| 8 | 122 |
| 4 | 104 |

1 comparator section enabled per chip

| Chips enabled | Min. Vref |
| --- | --- |
| 1-8 (all) | 100 (not consistent) |
| 8 | 100 |
| 4 | 84 |

The test results show that if any one chip oscillates, all chips begin to oscillate.  In addition, when more than chip is enabled, the oscillation begins earlier than with any of the individual chips.  Presumably, this is due to interaction between chips on a common (non-zero impedance) supply.  Unfortunately, the sensitivity of multiple chips to oscillation is determined by the one most sensitive chip.

The “best” configuration

Following is a summary of all important recommendations for biasing and operating FPIX chips:

- Vdda = 2.3V, Vddd = 2.5V

- Bias with 910K resistor from Vmaster to ground (no REFRES resistor)

- 0.1 uF or bigger bypass from Vref to ground

- 0.1 uF or bigger bypass from Vbp1 to ground

- 0.1 uF or bigger bypass from Vth0 to ground (for threshold stability)

- Minimize Vdda and ground resistance on PCB

- 0.01 uF bypass from Vmaster to Vdda (for ESD protection only).  Note this cap must be at least a factor of 10 smaller than the Vref bypass to avoid oscillation.

- Suggested DAC settings with 910K bias resistor:  Vref=122, Vfb2=103 (always Vref-19), Ibp1=0, Ibp2=0, Ibb=18, and Iff=8.

Summary

Attention to biasing, bypassing, etc., can help the immunity to oscillation, but by far the two most important factors are:

- The comparator bias current level

- The number of comparator sections used

At present, only one 8-chip module with a sensor has been tested.  There is significant chip to chip variation in the sensitivity to oscillation.  The sensitivity of the module as a whole is unfortunately determined by the most sensitive chip.  With a reasonable comparator bias current (giving reasonable comparator delay), operating all chips with one comparator seems safe.  Using more than one comparator per chip is risky unless the comparator bias is reduced.  Separating the integrator and comparator supply nets would resolve the stability problem, allowing any number of comparator sections to be used.  However, this would require a new fabrication run.