Phenix LDRD Pixel Plane Specifications

Version 1

Jeff Andresen, Guilherme Cardoso

April 19, 2007

Introduction

This document describes the specifications for the pixel plane utilized by the Phenix LDRD project. The pixel plane described here is the prototype for the LDRD. The goal of this pixel plane is the test of:

a group of 10 8-chip pixel modules working together in a system.

different power supply schemes.

different grounding schemes.

preliminary cooling using carbon-TPG substrate.

different interfaces to the DAQ.

Electrical Specifications

Charge Injection

A triangular-shaped analog voltage waveform can be used to inject charge on the preamplifier of the FPIX2.1 chips. Since the FPIX2.1 chips don’t have an internal pulser, an external voltage pulse must be supplied to calibrate the system once in operation. The pulser must comply to the following specifications

1- Triangular waveform

The issues to be considered in the design of the pulser are:

Each 8 chip module will have its own charge inject signal and ground coming into the pixel plane. A 24 pin Hirose DF11-24DP-2DS right angle through hole connector is used on the pixel plane for these signals. Once on the pixel plane, the ground is the common analog ground plane. Table 1 has the connector pinout for the charge injection.

| PIN # | SIGNAL | PIN # | SIGNAL |
| --- | --- | --- | --- |
| 1 | INJECTIN_1 | 2 | ANALOG GND |
| 3 | INJECTIN_2 | 4 | ANALOG GND |
| 5 | INJECTIN_3 | 6 | ANALOG GND |
| 7 | INJECTIN_4 | 8 | ANALOG GND |
| 9 | INJECTIN_5 | 10 | ANALOG GND |
| 11 | INJECTIN_6 | 12 | ANALOG GND |
| 13 | INJECTIN_7 | 14 | ANALOG GND |
| 15 | INJECTIN_8 | 16 | ANALOG GND |
| 17 | INJECTIN_9 | 18 | ANALOG GND |
| 19 | INJECTIN_10 | 20 | ANALOG GND |
| 21 | NO CONNECT | 22 | NO CONNECT |
| 23 | SHIELD GND | 24 | SHIELD GND |

Table 1: Charge Inject Connector Pinout

2- Charge in the chip’s preamplifier is collected in the falling edge of the triangular waveform.

Power Supplies

Hv and Lv power supplies

Each 8 chip module will have its own low voltage digital power, low voltage analog power, and high voltage power. Three 24 pin Hirose DF11-24DP-2DS connectors are used on the pixel plane for these powers. The low voltage digital powers have separate grounds at the connector where it becomes a common digital ground on the pixel plane. The low voltage analog powers and high voltage powers have separate grounds at the connector where it becomes a common analog ground on the pixel plane. Table 2, table 3, and table 4 have the power supply connector pinouts.

| PIN # | SIGNAL | PIN # | SIGNAL |
| --- | --- | --- | --- |
| 1 | VDDD_10 | 2 | DGND |
| 3 | VDDD_9 | 4 | DGND |
| 5 | VDDD_8 | 6 | DGND |
| 7 | VDDD_7 | 8 | DGND |
| 9 | VDDD_6 | 10 | DGND |
| 11 | VDDD_5 | 12 | DGND |
| 13 | VDDD_4 | 14 | DGND |
| 15 | VDDD_3 | 16 | DGND |
| 17 | VDDD_2 | 18 | DGND |
| 19 | VDDD_1 | 20 | DGND |
| 21 | +3.3V | 22 | DGND |
| 23 | SHIELD GND | 24 | SHIELD GND |

Table 2: Low Voltage Digital Power Supply Connector

| PIN # | SIGNAL | PIN # | SIGNAL |
| --- | --- | --- | --- |
| 1 | VDDA_1 | 2 | AGND |
| 3 | VDDA_2 | 4 | AGND |
| 5 | VDDA_3 | 6 | AGND |
| 7 | VDDA_4 | 8 | AGND |
| 9 | VDDA_5 | 10 | AGND |
| 11 | VDDA_6 | 12 | AGND |
| 13 | VDDA_7 | 14 | AGND |
| 15 | VDDA_8 | 16 | AGND |
| 17 | VDDA_9 | 18 | AGND |
| 19 | VDDA_10 | 20 | AGND |
| 21 | +3.3V | 22 | DGND |
| 23 | SHIELD GND | 24 | SHIELD GND |

Table 3: Low Voltage Analog Power Supply Connector

| PIN # | SIGNAL | PIN # | SIGNAL |
| --- | --- | --- | --- |
| 1 | VDET_1_IN | 2 | AGND |
| 3 | VDET_2_IN | 4 | AGND |
| 5 | VDET_3_IN | 6 | AGND |
| 7 | VDET_4_IN | 8 | AGND |
| 9 | VDET_5_IN | 10 | AGND |
| 11 | VDET_6_IN | 12 | AGND |
| 13 | VDET_7_IN | 14 | AGND |
| 15 | VDET_8_IN | 16 | AGND |
| 17 | VDET_9_IN | 18 | AGND |
| 19 | VDET_10_IN | 20 | AGND |
| 21 | NO CONNECT | 22 | NO CONNECT |
| 23 | SHIELD GND | 24 | SHIELD GND |

Table 4: High Voltage Connector

The digital powers have National Semiconductor LP3874EPM-2.5 fixed 2.5V output regulators located under the HDIs near the VDDD wire bond pad. The analog powers have Maxim MAX1793EUE25+ variable output regulators located under the HDIs near the VDDA wire bond pad. There are two resistors that set the desired output voltage. The Pixel Plane PCB can operate without regulators if the regulators are not left off of the PCB and the input is shorted to the output. As this PCB is inside the detector, voltage protection will be done before this PCB.

Interface to DAQ

The DAQ signals will interface with the PTA through 10 3M P50LE-050P1-SML-TGF connectors. All signals are differential pairs. There are 6 control signals for each HDI module. There is 1 data signal for each chip for a total of 8 data signals for each module. As the 8 chip module has data signals at both ends, there are 5 connectors on each side of the 10 modules. Table 5 through table 10 have the connector pinouts for the data and control signals of the 8 chip HDI modules.

| PIN # | SIGNAL | PIN # | SIGNAL |
| --- | --- | --- | --- |
| 1 | OUT5_1_10 | 2 | OUT5_1_10* |
| 3 | OUT6_1_10 | 4 | OUT6_1_10* |
| 5 | SCK_+A | 6 | SCK_*A |
| 7 | FFR1 | 8 | FFR1* |
| 9 | FFR2 | 10 | FFR2* |
| 11 | PTAGND | 12 | PTAGND |
| 13 | FFR3 | 14 | FFR3* |
| 15 | SHIFTOUT1 | 16 | SHIFTOUT1* |
| 17 | SHIFTOUT2 | 18 | SHIFTOUT2* |
| 19 | SHIFTOUT3 | 20 | SHIFTOUT3* |
| 21 | PTAGND | 22 | PTAGND |
| 23 | OUT8_1_1 | 24 | OUT8_*1_1 |
| 25 | OUT7_1_1 | 26 | OUT7_*1_1 |
| 27 | OUT6_1_1 | 28 | OUT6_*1_1 |
| 29 | OUT5_1_1 | 30 | OUT5_*1_1 |
| 31 | PTAGND | 32 | PTAGND |
| 33 | OUT8_1_2 | 34 | OUT8_*1_2 |
| 35 | OUT7_1_2 | 36 | OUT7_*1_2 |
| 37 | OUT6_1_2 | 38 | OUT6_*1_2 |
| 39 | OUT5_1_2 | 40 | OUT5_*1_2 |
| 41 | PTAGND | 42 | PTAGND |
| 43 | OUT8_1_3 | 44 | OUT8*_1_3 |
| 45 | OUT7_1_3 | 46 | OUT7*_1_3 |
| 47 | OUT6_1_3 | 48 | OUT6*_1_3 |
| 49 | OUT5_1_3 | 50 | OUT5*_1_3 |

Table 5: Left Side PTA Connector J1

| PIN # | SIGNAL | PIN # | SIGNAL |
| --- | --- | --- | --- |
| 1 | SHIFTOUT10 | 2 | SHIFTOUT*10 |
| 3 | FFR10 | 4 | FFR*10 |
| 5 | SCK_+B | 6 | SCK_*B |
| 7 | FFR4 | 8 | FFR*4 |
| 9 | FFR5 | 10 | FFR*5 |
| 11 | PTAGND | 12 | PTAGND |
| 13 | FFR6 | 14 | FFR*6 |
| 15 | SHIFTOUT4 | 16 | SHIFTOUT*4 |
| 17 | SHIFTOUT5 | 18 | SHIFTOUT*5 |
| 19 | SHIFTOUT6 | 20 | SHIFTOUT*6 |
| 21 | PTAGND | 22 | PTAGND |
| 23 | OUT8_1_4 | 24 | OUT8_*1_4 |
| 25 | OUT7_1_4 | 26 | OUT7_*1_4 |
| 27 | OUT6_1_4 | 28 | OUT6_*1_4 |
| 29 | OUT5_1_4 | 30 | OUT5_*1_4 |
| 31 | PTAGND | 32 | PTAGND |
| 33 | OUT8_1_5 | 34 | OUT8_*1_5 |
| 35 | OUT7_1_5 | 36 | OUT7_*1_5 |
| 37 | OUT6_1_5 | 38 | OUT6_*1_5 |
| 39 | OUT5_1_5 | 40 | OUT5_*1_5 |
| 41 | PTAGND | 42 | PTAGND |
| 43 | OUT8_1_6 | 44 | OUT8_*1_6 |
| 45 | OUT7_1_6 | 46 | OUT7_*1_6 |
| 47 | OUT6_1_6 | 48 | OUT6_*1_6 |
| 49 | OUT5_1_6 | 50 | OUT5_*1_6 |

Table 6: Left Side PTA Connector J2

| PIN # | SIGNAL | PIN # | SIGNAL |
| --- | --- | --- | --- |
| 1 | OUT7_1_10 | 2 | OUT7_*1_10 |
| 3 | OUT8_1_10 | 4 | OUT8_*1_10 |
| 5 | SCK_CNTRL | 6 | SCK_CNTRL* |
| 7 | FFR7 | 8 | FFR*7 |
| 9 | FFR8 | 10 | FFR*8 |
| 11 | PTAGND | 12 | PTAGND |
| 13 | FFR9 | 14 | FFR*9 |
| 15 | SHIFTOUT7 | 16 | SHIFTOUT*7 |
| 17 | SHIFTOUT8 | 18 | SHIFTOUT*8 |
| 19 | SHIFTOUT9 | 20 | SHIFTOUT*9 |
| 21 | PTAGND | 22 | PTAGND |
| 23 | OUT8_1_7 | 24 | OUT8_*1_7 |
| 25 | OUT7_1_7 | 26 | OUT7_*1_7 |
| 27 | OUT6_1_7 | 28 | OUT6_*1_7 |
| 29 | OUT5_1_4 | 30 | OUT5_*1_4 |
| 31 | PTAGND | 32 | PTAGND |
| 33 | OUT8_1_8 | 34 | OUT8_*1_8 |
| 35 | OUT7_1_8 | 36 | OUT7_*1_8 |
| 37 | OUT6_1_8 | 38 | OUT6_*1_8 |
| 39 | OUT5_1_8 | 40 | OUT5_*1_8 |
| 41 | PTAGND | 42 | PTAGND |
| 43 | OUT8_1_9 | 44 | OUT8_*1_9 |
| 45 | OUT7_1_9 | 46 | OUT7_*1_9 |
| 47 | OUT6_1_9 | 48 | OUT6_*1_9 |
| 49 | OUT5_1_9 | 50 | OUT5_*1_9 |

Table 7: Left Side PTA Connector J5

| PIN # | SIGNAL | PIN # | SIGNAL |
| --- | --- | --- | --- |
| 1 | OUT1_1_10 | 2 | OUT1_*1_10 |
| 3 | OUT2_1_10 | 4 | OUT2_*1_10 |
| 5 | BCO+A | 6 | BCO+A |
| 7 | SHIFTCTRL1 | 8 | SHIFTCTRL*1 |
| 9 | SHIFTCTRL2 | 10 | SHIFTCTRL*2 |
| 11 | PTAGND | 12 | PTAGND |
| 13 | SHIFTCTRL3 | 14 | SHIFTCTRL*3 |
| 15 | SHIFTIN1 | 16 | SHIFTIN*1 |
| 17 | SHIFTIN2 | 18 | SHIFTIN*2 |
| 19 | SHIFTIN3 | 20 | SHIFTIN*3 |
| 21 | PTAGND | 22 | PTAGND |
| 23 | OUT4_1_1 | 24 | OUT4_*1_1 |
| 25 | OUT3_1_1 | 26 | OUT3_*1_1 |
| 27 | OUT2_1_1 | 28 | OUT2_*1_1 |
| 29 | OUT1_1_1 | 30 | OUT1_*1_1 |
| 31 | PTAGND | 32 | PTAGND |
| 33 | OUT4_1_2 | 34 | OUT4_*1_2 |
| 35 | OUT3_1_2 | 36 | OUT3_*1_2 |
| 37 | OUT2_1_2 | 38 | OUT2_*1_2 |
| 39 | OUT1_1_2 | 40 | OUT1_*1_2 |
| 41 | PTAGND | 42 | PTAGND |
| 43 | OUT4_1_3 | 44 | OUT4_*1_3 |
| 45 | OUT3_1_3 | 46 | OUT3_*1_3 |
| 47 | OUT2_1_3 | 48 | OUT2_*1_3 |
| 49 | OUT1_1_3 | 50 | OUT1_*1_3 |

Table 8: Right Side PTA Connector J3

| PIN # | SIGNAL | PIN # | SIGNAL |
| --- | --- | --- | --- |
| 1 | OUT4_1_10 | 2 | OUT4_*1_10 |
| 3 | SHIFTIN10 | 4 | SHIFTIN*10 |
| 5 | BCO+B | 6 | BCO*B |
| 7 | SHIFTCTRL4 | 8 | SHIFTCTRL*4 |
| 9 | SHIFTCTRL5 | 10 | SHIFTCTRL*5 |
| 11 | PTAGND | 12 | PTAGND |
| 13 | SHIFTCTRL6 | 14 | SHIFTCTRL*6 |
| 15 | SHIFTIN4 | 16 | SHIFTIN*4 |
| 17 | SHIFTIN5 | 18 | SHIFTIN*5 |
| 19 | SHIFTIN6 | 20 | SHIFTIN*6 |
| 21 | PTAGND | 22 | PTAGND |
| 23 | OUT4_1_4 | 24 | OUT4_*1_4 |
| 25 | OUT3_1_4 | 26 | OUT3_*1_4 |
| 27 | OUT2_1_4 | 28 | OUT2_*1_4 |
| 29 | OUT1_1_4 | 30 | OUT1_*1_4 |
| 31 | PTAGND | 32 | PTAGND |
| 33 | OUT4_1_5 | 34 | OUT4_*1_5 |
| 35 | OUT3_1_5 | 36 | OUT3_*1_5 |
| 37 | OUT2_1_5 | 38 | OUT2_*1_5 |
| 39 | OUT1_1_5 | 40 | OUT1_*1_5 |
| 41 | PTAGND | 42 | PTAGND |
| 43 | OUT4_1_6 | 44 | OUT4_*1_6 |
| 45 | OUT3_1_6 | 46 | OUT3_*1_6 |
| 47 | OUT2_1_6 | 48 | OUT2_*1_6 |
| 49 | OUT1_1_6 | 50 | OUT1_*1_6 |

Table 9: Right Side PTA Connector J4

| PIN # | SIGNAL | PIN # | SIGNAL |
| --- | --- | --- | --- |
| 1 | OUT3_1_10 | 2 | OUT3_1_10 |
| 3 | SHIFTCTRL10 | 4 | SHIFTCTRL*10 |
| 5 | BCO_CNTRL | 6 | BCO_CNTRL* |
| 7 | SHIFTCTRL7 | 8 | SHIFTCTRL*7 |
| 9 | SHIFTCTRL8 | 10 | SHIFTCTRL*8 |
| 11 | PTAGND | 12 | PTAGND |
| 13 | SHIFTCTRL9 | 14 | SHIFTCTRL*9 |
| 15 | SHIFTIN7 | 16 | SHIFTIN*7 |
| 17 | SHIFTIN8 | 18 | SHIFTIN*8 |
| 19 | SHIFTIN9 | 20 | SHIFTIN*9 |
| 21 | PTAGND | 22 | PTAGND |
| 23 | OUT4_1_7 | 24 | OUT4_*1_7 |
| 25 | OUT3_1_7 | 26 | OUT3_*1_7 |
| 27 | OUT2_1_7 | 28 | OUT2_*1_7 |
| 29 | OUT1_1_7 | 30 | OUT1_*1_7 |
| 31 | PTAGND | 32 | PTAGND |
| 33 | OUT4_1_8 | 34 | OUT4_*1_8 |
| 35 | OUT3_1_8 | 36 | OUT3_*1_8 |
| 37 | OUT2_1_8 | 38 | OUT2_*1_8 |
| 39 | OUT1_1_8 | 40 | OUT1_*1_8 |
| 41 | PTAGND | 42 | PTAGND |
| 43 | OUT4_1_9 | 44 | OUT4_*1_9 |
| 45 | OUT3_1_9 | 46 | OUT3_*1_9 |
| 47 | OUT2_1_9 | 48 | OUT2_*1_9 |
| 49 | OUT1_1_9 | 50 | OUT1_*1_9 |

Table 10: Right Side PTA Connector J7

Clock Fanouts

Figure 1 shows the Micrel SY89828L clock fanout I.C.

Figure 1: Micrel SY8928L Clock Fanout I.C.

This I.C. will be used for the fanout of SCLK 1:10 and BCOCLK 1:10. Using this I.C. lessens the number of clock pins required on the PTA connectors, provides signal redundancy, and increases signal quality with less skew. There is an A and B LVDS input clock for redundancy. The CLK_SEL inputs are pulled low which always uses the LVDS inputs. The SEL inputs selects which LVDS input is used. The OE pins selects whether outputs Q0-Q9 are used or Q10-19 are used for further redundancy. A pair of Maxim MAX9130 I.C.s control the SEL and OE inputs.

Chip Hit

The OUT 6 data pair for each FPIX2 chip on the HDI can be wire bonded on the HDI so that those pads are the CHIPHIT pair instead. On the PIXEL Plane PCB, these pads will be used for CHIPHIT. The CHIPHIT signals for HDI modules 1 through 10 will be on 4 PTA connectors. Table 11 through table 14 have the pinouts for the CHIPHIT connectors.

| PIN # | SIGNAL | PIN # | SIGNAL |
| --- | --- | --- | --- |
| 1 | NO CONNECT | 2 | NO CONNECT |
| 3 | CHIPHIT8_1 | 4 | CHIPHIT*8_1 |
| 5 | CHIPHIT7_1 | 6 | CHIPHIT*7_1 |
| 7 | CHIPHIT6_1 | 8 | CHIPHIT*6_1 |
| 9 | CHIPHIT5_1 | 10 | CHIPHIT*5_1 |
| 11 | PTAGND | 12 | PTAGND |
| 13 | CHIPHIT8_2 | 14 | CHIPHIT*8_2 |
| 15 | CHIPHIT7_2 | 16 | CHIPHIT*7_2 |
| 17 | CHIPHIT6_2 | 18 | CHIPHIT*6_2 |
| 19 | CHIPHIT5_2 | 20 | CHIPHIT*5_2 |
| 21 | PTAGND | 22 | PTAGND |
| 23 | CHIPHIT8_3 | 24 | CHIPHIT*8_3 |
| 25 | CHIPHIT7_3 | 26 | CHIPHIT*7_3 |
| 27 | CHIPHIT6_3 | 28 | CHIPHIT*6_3 |
| 29 | CHIPHIT5_3 | 30 | CHIPHIT*5_3 |
| 31 | PTAGND | 32 | PTAGND |
| 33 | CHIPHIT8_4 | 34 | CHIPHIT*8_4 |
| 35 | CHIPHIT7_4 | 36 | CHIPHIT*7_4 |
| 37 | CHIPHIT6_4 | 38 | CHIPHIT*6_4 |
| 39 | CHIPHIT5_4 | 40 | CHIPHIT*5_4 |
| 41 | PTAGND | 42 | PTAGND |
| 43 | CHIPHIT8_5 | 44 | CHIPHIT*8_5 |
| 45 | CHIPHIT7_5 | 46 | CHIPHIT*7_5 |
| 47 | CHIPHIT6_5 | 48 | CHIPHIT*6_5 |
| 49 | CHIPHIT5_5 | 50 | CHIPHIT*5_5 |

Table 11: Left Side PTA Connector J6

| PIN # | SIGNAL | PIN # | SIGNAL |
| --- | --- | --- | --- |
| 1 | NO CONNECT | 2 | NO CONNECT |
| 3 | CHIPHIT8_6 | 4 | CHIPHIT*8_6 |
| 5 | CHIPHIT7_6 | 6 | CHIPHIT*7_6 |
| 7 | CHIPHIT6_6 | 8 | CHIPHIT*6_6 |
| 9 | CHIPHIT5_6 | 10 | CHIPHIT*5_6 |
| 11 | PTAGND | 12 | PTAGND |
| 13 | CHIPHIT8_7 | 14 | CHIPHIT*8_7 |
| 15 | CHIPHIT7_7 | 16 | CHIPHIT*7_7 |
| 17 | CHIPHIT6_7 | 18 | CHIPHIT*6_7 |
| 19 | CHIPHIT5_7 | 20 | CHIPHIT*5_7 |
| 21 | PTAGND | 22 | PTAGND |
| 23 | CHIPHIT8_8 | 24 | CHIPHIT*8_8 |
| 25 | CHIPHIT7_8 | 26 | CHIPHIT*7_8 |
| 27 | CHIPHIT6_8 | 28 | CHIPHIT*6_8 |
| 29 | CHIPHIT5_8 | 30 | CHIPHIT*5_8 |
| 31 | PTAGND | 32 | PTAGND |
| 33 | CHIPHIT8_9 | 34 | CHIPHIT*8_9 |
| 35 | CHIPHIT7_9 | 36 | CHIPHIT*7_9 |
| 37 | CHIPHIT6_9 | 38 | CHIPHIT*6_9 |
| 39 | CHIPHIT5_9 | 40 | CHIPHIT*5_9 |
| 41 | PTAGND | 42 | PTAGND |
| 43 | CHIPHIT8_10 | 44 | CHIPHIT*8_10 |
| 45 | CHIPHIT7_10 | 46 | CHIPHIT*7_10 |
| 47 | CHIPHIT6_10 | 48 | CHIPHIT*6_10 |
| 49 | CHIPHIT5_10 | 50 | CHIPHIT*5_10 |

Table 12: Left Side PTA Connector J13

| PIN # | SIGNAL | PIN # | SIGNAL |
| --- | --- | --- | --- |
| 1 | NO CONNECT | 2 | NO CONNECT |
| 3 | CHIPHIT4_1 | 4 | CHIPHIT*4_1 |
| 5 | CHIPHIT3_1 | 6 | CHIPHIT*3_1 |
| 7 | CHIPHIT2_1 | 8 | CHIPHIT*2_1 |
| 9 | CHIPHIT1_1 | 10 | CHIPHIT*1_1 |
| 11 | PTAGND | 12 | PTAGND |
| 13 | CHIPHIT4_2 | 14 | CHIPHIT*4_2 |
| 15 | CHIPHIT3_2 | 16 | CHIPHIT*3_2 |
| 17 | CHIPHIT2_2 | 18 | CHIPHIT*2_2 |
| 19 | CHIPHIT1_2 | 20 | CHIPHIT*1_2 |
| 21 | PTAGND | 22 | PTAGND |
| 23 | CHIPHIT4_3 | 24 | CHIPHIT*4_3 |
| 25 | CHIPHIT3_3 | 26 | CHIPHIT*3_3 |
| 27 | CHIPHIT2_3 | 28 | CHIPHIT*2_3 |
| 29 | CHIPHIT1_3 | 30 | CHIPHIT*1_3 |
| 31 | PTAGND | 32 | PTAGND |
| 33 | CHIPHIT4_4 | 34 | CHIPHIT*4_4 |
| 35 | CHIPHIT3_4 | 36 | CHIPHIT*3_4 |
| 37 | CHIPHIT2_4 | 38 | CHIPHIT*2_4 |
| 39 | CHIPHIT1_4 | 40 | CHIPHIT*1_4 |
| 41 | PTAGND | 42 | PTAGND |
| 43 | CHIPHIT4_5 | 44 | CHIPHIT*4_5 |
| 45 | CHIPHIT3_5 | 46 | CHIPHIT*3_5 |
| 47 | CHIPHIT2_5 | 48 | CHIPHIT*2_5 |
| 49 | CHIPHIT1_5 | 50 | CHIPHIT*1_5 |

Table 13: Right Side PTA Connector J8

| PIN # | SIGNAL | PIN # | SIGNAL |
| --- | --- | --- | --- |
| 1 | NO CONNECT | 2 | NO CONNECT |
| 3 | CHIPHIT4_6 | 4 | CHIPHIT*4_6 |
| 5 | CHIPHIT3_6 | 6 | CHIPHIT*3_6 |
| 7 | CHIPHIT2_6 | 8 | CHIPHIT*2_6 |
| 9 | CHIPHIT1_6 | 10 | CHIPHIT*1_6 |
| 11 | PTAGND | 12 | PTAGND |
| 13 | CHIPHIT4_7 | 14 | CHIPHIT*4_7 |
| 15 | CHIPHIT3_7 | 16 | CHIPHIT*3_7 |
| 17 | CHIPHIT2_7 | 18 | CHIPHIT*2_7 |
| 19 | CHIPHIT1_7 | 20 | CHIPHIT*1_7 |
| 21 | PTAGND | 22 | PTAGND |
| 23 | CHIPHIT4_8 | 24 | CHIPHIT*4_8 |
| 25 | CHIPHIT3_8 | 26 | CHIPHIT*3_8 |
| 27 | CHIPHIT2_8 | 28 | CHIPHIT*2_8 |
| 29 | CHIPHIT1_8 | 30 | CHIPHIT*1_8 |
| 31 | PTAGND | 32 | PTAGND |
| 33 | CHIPHIT4_9 | 34 | CHIPHIT*4_9 |
| 35 | CHIPHIT3_9 | 36 | CHIPHIT*3_9 |
| 37 | CHIPHIT2_9 | 38 | CHIPHIT*2_9 |
| 39 | CHIPHIT1_9 | 40 | CHIPHIT*1_9 |
| 41 | PTAGND | 42 | PTAGND |
| 43 | CHIPHIT4_10 | 44 | CHIPHIT*4_10 |
| 45 | CHIPHIT3_10 | 46 | CHIPHIT*3_10 |
| 47 | CHIPHIT2_10 | 48 | CHIPHIT*2_10 |
| 49 | CHIPHIT1_10 | 50 | CHIPHIT*1_10 |

Table 14: Right Side PTA Connector J15

Layout considerations

The Pixel Plane PCB has 8 layers. The digital data, chiphit, and control signals are differential pairs that will have 100 ohm edge coupled controlled impedance. The PCB layer stackup is as follows.

Layer 1: Top, trace layer 1.

Layer 2: IN3, trace layer 2

Layer 3: GND, digital ground plane, impedance reference for layer 1 and layer 2

Layer 4: PWR, +3V and VDDAs power plane

Layer 5: IN1, VDDDs and AGND power plane

Layer 6: IN2, digital ground plane, impedance reference for layer 7 and layer 8

Layer 7: IN4, trace layer 3

Layer 8: BOT, trace layer 4

There will be a large cutout in the Pixel Plane PCB under the active area of the 8 chip modules. This area will be filled with TPG with a .018” thickness. A cooling pipe will be on the back of the TPG. The Pixel Plane PCB will have a thickness of .093”. The Pixel Plane PCB must be rigid enough to support the 10  8 chip modules. The Pixel Plane PCB will be mounted face to face to a second Pixel Plane PCB with a 6.2 mm offset. The connectors will be on the back of the Pixel Plane PCB. High voltage minimum clearances will be required. The Pixel Plane PCB is under a size restriction which makes the layout and the cable routing a challenge.

Grounding

The low voltage digital powers have separate grounds at the connector where it becomes a common digital ground on the Pixel Plane PCB. The low voltage analog powers and high voltage powers have separate grounds at the connector where it becomes a common analog ground on the pixel plane. The connectors for are 24 pin for the 10 HDI modules. This provides an unused bottom pair of pins that can be used for SHIELD GROUND as an option. There is a large digital ground pad near each power connector to allow for the connection of a cable ground shield to digital ground if it is needed. There are pads for a zero ohm resistor in several spots on the Pixel Plane PCB to allow the connecting of analog ground to digital ground if it is needed.

Dimensions of the board

Figure 2 is the Pixel Plane PCB layout. The outer circle is the detector barrel which has a radius of 180mm. The lower circle of the Pixel Plane PCB is the beam pipe area with a diameter of 31.2mm. The Pixel Plane PCB has a maximum width of 353.16mm and a maximum height of 173.8mm. The PCB has a cutout under the HDI detectors that is 74mm wide and 133.0mm in height. This cutout area will be filled with a carbon-TPG substrate and contain a cooling pipe.

Figure 2: Pixel Plane PCB

The two Pixel Plane PCBs will be mounted face to face with the connectors mounted on the back side of the PCBs.

3.3	Pixel Plane PCB Design Schematic.