| U.S. Department of Transportation Federal Aviation Administration | Advisory Circular |
| --- | --- |

AC 121-1A

DATE: 7/7/1978

AC No:  121-1A

Change:  4

Date:  7/7/78

Initiated

by:  AFS-320

Subject:  STANDARD OPERATIONS SPECIFICATIONS - AIRCRAFT

MAINTENANCE HANDBOOK

1.   PURPOSE.  This handbook provides procedures acceptable to

the Federal Aviation Administration which may be used by

operators when establishing inspection intervals and

overhaul times.  A list of sample Operations Specifications

- Aircraft Maintenance, General, for aircraft currently

being used in air transportation, is incorporated in this

document to further aid the operator in preparing his

program.

2.   CANCELLATION.  This advisory circular cancels:

a.   Advisory Circular 120-21, Aircraft Maintenance Time

Limitations, dated 6/24/66.

b.   Advisory Circular 120-24A, Establishment and Revision

of Aircraft Engine Overhaul and Inspection Periods,

dated 2/25/69.

c.   Advisory Circular 121-1, Standard Maintenance

Specifications, dated 12/15/62.

3.   HOW TO ORDER THIS HANDBOOK.  This publication is furnished

free of charge.  Additional copies may be ordered from:

Department of Transportation

Distribution Operations Unit, TAD 484.3

Washington, D.C. 20591

Identify the publication in your order as:

FAA AC No. 121-1A,

Standard Operations Specifications - Aircraft

Maintenance Handbook

Dated:  June 26, 1973

4.   CHANGES TO THIS HANDBOOK.  Revised pages to this Advisory

Circular will be transmitted by Advisory Circular Changes.

If you order the basic handbook, we will put your name on

the mailing list to receive changes.

/s/ C. R. Melugin, Jr.

Acting Director, Flight Standards Service

TABLE OF CONTENTS

Page No.

CHAPTER 1.  INTRODUCTION.                                    1

1.  Purpose.                                         1

2.  Eligibility.                                     1

3.  Cancellation.                                    1

4.  Definitions.                                     1

5.  General.                                         2

6.  Revision of Time Limitations - General.          5

7.  Airframe - Revision of Time Limitations.         6

8.  Powerplant and Associated Appliances - Revision  6

of Time Limitations.

9.  Appliances - Revision of Time Limitations.       7

10.  Reliability vs. Hardtime  Conversion.            7

11.  Emergency Equipment.                             7

12.  Avionics and Instruments.                        7

13.-15.  Reserved.

CHAPTER 2.  PRORATION.                                       9

16.  Purpose.                                         9

17.  Application.                                     9

18.  Scope and Limitations.                           9

19.  Data Required.                                  11

20.  Proration Formula.                              13

21.-25.  Reserved.

APPENDIX 1.  ADDITIONAL PRORATION SAMPLE DATA.   (30 pages)

FIGURE 1.  TRANSFER OF AIRCRAFT FROM A BLOCK/PATTERN

SYSTEM TO A ONE-TIME OVERHAUL.             1

FIGURE 2.  TRANSFER OF AIRCRAFT FROM A BLOCK/PATTERN

SYSTEM TO A BLOCK/PATTERN SYSTEM.          5

FIGURE 3.  TRANSFER OF AIRCRAFT FROM A ONE-TIME

OVERHAUL TO A BLOCK/PATTERN SYSTEM

(BUYERS APPROVED OH TIME LIMIT HIGHER

THAN PREVIOUS OPERATORS).                  9

FIGURE 4.  TRANSFER OF AIRCRAFT FROM A ONE-TIME

OVERHAUL TO A BLOCK/PATTERN SYSTEM

(BUYERS APPROVED OH TIME LIMIT LOWER

THAN PREVIOUS OPERATORS).                 13

FIGURE 5.  FORMAT FOR PRESENTATION OF PRORATION DATA

ON AIRCRAFT BEING TRANSFERRED.            17

FIGURE 6.  TRANSFER OF PREVIOUSLY PRORATED AIRCRAFT. 19

FIGURE 7.  PROCEDURE FOR CONVERTING CALENDAR

OVERHAUL (MONTHS) TO HOURS SINCE OVERHAUL

FOR PRORATION PURPOSES.                   21

FIGURE 8.  METHOD OF DEPICTING AREAS, SECTIONS,

COMPONENTS ETC., THAT ARE TIED TO A

SPECIFIC BLOCK.                           23

FIGURE 9.  OPERATIONS SPECIFICATIONS -- PREFACE PAGE

FOR AIRCRAFT ON PRORATED TIME.            25

FIGURE 10. OPERATIONS SPECIFICATION, AIRCRAFT

MAINTENANCE -- GENERAL.                   27

FIGURE 11. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- PREFACE PAGE FOR AIRCRAFT

ON PRORATED TIME.                         29

*      FIGURE 12. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- PREFACE PAGE FOR AIRCRAFT

UTILIZING A PREVIOUS OPERATORS PRORATED

TIME.                                     30  *

APPENDIX 2.  STANDARD SPECIFICATIONS

FIGURE 1.  OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- AVIONICS (ALL AIRCRAFT).    1

FIGURE 2.  OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- DART 510 AND DART 525.      3

FIGURE 3.  WITHDRAWN -- CHG 1.

FIGURE 4.  OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- PRATT AND WHITNEY R2000

SERIES.                                    7

FIGURE 5.  OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- PRATT AND WHITNEY R2800

AND R-2800C-CA-CB SERIES.                  9

FIGURE 6.  WITHDRAWN -- CHG 1.

FIGURE 7.  OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- WRIGHT 1820 AND PRATT AND

WHITNEY R-1830 SERIES.                    13

FIGURE 8.  WITHDRAWN -- CHG 1.

FIGURE 9.  OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- WRIGHT AERO C18 SERIES.    17

FIGURE 10. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- WRIGHT AERO TC18 SERIES.   19

FIGURE 11. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- CONVAIR CV-240/340/440.    21

FIGURE 12. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- CURTISS WRIGHT C46 SERIES. 25

FIGURE 13. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - DOUGLAS DC-3 SERIES.        29

FIGURE 14. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - DOUGLAS DC-4 SERIES.        33

FIGURE 15. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - DOUGLAS DC-6, DC-7.         35

FIGURE 16. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - LOCKHEED

L-049/749/1049/1649.                      39

FIGURE 17. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - MARTIN M-202/404.           43

FIGURE 18. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - VISCOUNT 745D/810.          47

FIGURE 19. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - LOCKHEED L-188 A & C.       51

FIGURE 20. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - ALLISON 501-D13 ENGINE

AEROPRODUCTS PROPELLER.                   57

FIGURE 21. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - BOEING 707/720.             59

FIGURE 22. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - DOUGLAS DC-8/F AND

DC-8-61/61F.                              75

FIGURE 23. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - LOCKHEED MODEL 382.        109

FIGURE 24. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - CONVAIR CV-880.            123

FIGURE 25. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - FAIRCHILD F-27.            135

FIGURE 26. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - CONVAIR CV-990.            145

FIGURE 27. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - JET COMMANDER 1121.        159

FIGURE 28. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - DOUGLAS DC-8-62/62F.       173

FIGURE 29. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - DOUGLAS DC-8-63/63F.       185

FIGURE 30. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- LOCKHEED MODEL 300

(C-141A).                                197

FIGURE 31. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- LOCKHEED JETSTAR - MODEL

1329.                                    211

FIGURE 32. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- SHORT TURBO-SKYVAN        225

(SC-7).

FIGURE 33. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- SIKORSKY S-61L/N

HELICOPTER.                              233

FIGURE 34. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- LEAR MODEL 24/24B/25.     251

FIGURE 35. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- FAN JET FALCON - 20.      263

FIGURE 36. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- HAWKER-SIDDELEY DH-125

SERIES.                                  273

FIGURE 37. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- HFB 320 HANSA JET.        283

FIGURE 38. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- BOEING 727.               301

FIGURE 39. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- DOUGLAS DC-9.             319

FIGURE 40. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- HAWKER-SIDDELEY 748

SERIES 2A.                               331

FIGURE 41. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- FAN JET FALCON - 10.      343

FIGURE 42. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- GATES LEARJET MODELS

35/36.                                   355

*      FIGURE 43. OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE -- SOCIETE NATIONALE

INDUSTRIELLE AEROSPATIALE (SNIAS)

NORD-262A AND 262A/M-298.                369  *

STANDARD OPERATIONS SPECIFICATIONS - AIRCRAFT MAINTENANCE

CHAPTER 1.  INTRODUCTION

1.   PURPOSE.  This document prescribes, for air carrier aircraft

of 12,500 pounds or over certificated takeoff weight,

reasonable methods of determining initial overhaul time

limits and period inspection intervals for both new and used

airframes, powerplants, propellers, and appliances.  Under

the provisions of Federal Aviation Regulations 121 and 127,

the FAA approves for each aircraft, "Operations

Specifications - Aircraft Maintenance," which contain

maintenance intervals for airframes, powerplants,

propellers, and appliances.  Such approved overhaul time

limits and maintenance intervals apply only to the aircraft

used by each individual air carrier and are not transferable

from one air carrier to another.

2.   ELIGIBILITY.  Standard Operations Specifications - Aircraft

Maintenance, or Maintenance Review Board time limits, may be

applied to aircraft being placed in FAR 121, 127, and 135.2

operations.

3.   DEFINITIONS.  Terms as used in this document are defined as

follows:

a.   Aircraft.  An aircraft is any contrivance now known or

hereafter invented, used, or designed for navigation of

or flight in the air, including airframes, powerplants,

propellers, and appliances.

b.   Previous Operator.  Previous Operator is the last

operator who utilized the aircraft prior to its sale or

lease.

c.   Seller.  Seller is the same as Previous Operator.

d.   New Operator.  A new operator is a person who acquires

an aircraft, through purchase or lease, for operation

in accordance with his operating certificate, and who

HAS NOT had a previously approved maintenance program

for such type aircraft.

e.   Buyer.  A "Buyer" is a person who acquires an aircraft,

through purchase or lease, for operation in accordance

with his operating certificate, and who HAS an approved

maintenance program for such type aircraft.

f.   Approved Time Limits.  Approved time limits are those

which appear on the carrier's approved "Operations

Specifications - Aircraft Maintenance," FAA Form 1014.

(OMB 04-R0075)

g.   Maintenance Review Board.  A Maintenance Review Board

is a body of FAA maintenance specialists organized to

evaluate and establish inspection and overhaul time

limits for transport aircraft intended for use in U.S.

air carrier operations.

h.   Maintenance Review Board Reports.  That document

formulated by the Maintenance Review Board that

provides an acceptable initial maintenance program for

a specific aircraft or powerplant.

i.   Proration.  A process by which an operator calculates

the time since overhaul on a newly acquired airframe

and its installed powerplants, propellers, and

appliances when his approved overhaul time differs from

that of the previous operator.

j.   On Condition.  Items and appliances listed as "On

Condition" must be restricted to components on which a

determination of continued airworthiness may be made by

inspections, measurements, or tests.  These "On

Condition" functions are to be performed within the

time limitations prescribed for the inspection or

check.  Performance tolerances and wear or

deterioration limits shall be contained in the air

carrier's maintenance manual.  If an item or appliance

cannot be maintained in a condition of continued

airworthiness by use of "On Condition" procedures, it

must be placed on specific time limitation control or

be controlled by an acceptable standard for determining

time limitations (e.g., hard time or condition

monitoring).

Additional criteria to be used in determining the

eligibility of an item or appliance for "On Condition"

are:

(1)  Perceptibility of wear or other deterioration of

moving parts.

(2)  Adaptability to inspection for detection of

corrosion and internal structural integrity when

such parts or areas have an appreciable effect on

continued airworthiness.

k.   Direct Inclusion.  A process by which the buyer places

a newly acquired aircraft into his approved maintenance

program for that type aircraft utilizing the existing

times of the airframe, powerplants, and appliances.

4.   GENERAL.

a.   Three acceptable means currently in use for

establishing initial maintenance programs are as

follows:

(1)  Advisory Circular 121-1A, Standard Operations

Specifications -- Aircraft Maintenance.

(2)  Maintenance Review Board Reports.

*         (3)  Advisory Circular 120-17A, Maintenance Control by

Reliability Methods.                             *

b.   Maintenance Review Board reports, which are formulated

at the time of equipment manufacture, are valid only

until such time as the limits are published in AC

121-1A.  This transfer of limits from the MRB report to

AC 121-1A is accomplished only after sufficient

satisfactory service experience has been accumulated

that warrants an updating or revision of the original

MRB limits.

c.   When a non-air carrier aircraft is acquired (e.g., one

operating under FAR Part 91, the military, or foreign),

the initial time limits for the new operator will be

those set forth in the Standard Operations

Specifications - Aircraft Maintenance or the MRB

report, whichever is applicable.  The time remaining to

overhaul for the new operator will be the difference

between the actual TSO and the newly approved time

limit providing the actual TSO is the lower of the two

figures.

d.   When a non-air carrier aircraft is acquired (e.g., one

operating under FAR Part 91, the military or foreign),

the initial time limits for the buyer may be

established by using either direct inclusion or

proration in accordance with the provisions of Chapter

2.  In this type of situation, if proration is to be

used, the times shown in the Standard Operations

Specifications - Aircraft Maintenance or the MRB report

(whichever is applicable to the aircraft in question)

are to be used as the seller's approved overhaul time

and this figure will serve as the basis for the

proration computation.

e.   In the event an air carrier aircraft is acquired by a

new operator or buyer, up to 30 hours of time may be

accumulated under FAR Part 91 without the provisions of

the above paragraph  c  being invoked.

f.   The times listed in AC 121-1A (as in the case of MRB

reports) are recommended starting times.  They may be

reduced if an investigation of the proposed operation

indicates that lower time limits are advisable in the

interest of safety.

g.   Higher starting times may be approved providing

sufficient justification is provided to the assigned

maintenance inspector by the operator.  In making this

determination, consideration shall be given to the

following:

(1)  Type of intended operations (geographical areas of

operation).

(2)  The operator's experience in handling aircraft

equal in complexity to the new equipment.

(3)  The scope and depth of training provided for

maintenance personnel on the new aircraft.

(4)  The competency and capability of the carrier's

maintenance and quality control organizations.

(5)  The adequacy of the maintenance and inspection

programs.

(6)  The adequacy of all facilities and equipment

required for the maintenance of the equipment

involved.

(7)  Calendar time vs. utilization on the aircraft to

be transferred.  Long periods of idle storage time

or extremely low utilization over a period of time

can and often does have an appreciable ill effect

on the integrity of an aircraft.  Careful

consideration must be given to this time element

by the assigned inspector prior to putting the

aircraft on a new certificate.  Acceptance checks,

which are a necessary part of the certification

procedure must take into account the effects of

calendar time and assure that the product is

airworthy.

(8)  Industry-wide service history.

(9)  Previous operator's use of a reliability program.

h.   Appliances of the same make and basic models as those

currently in use by an operator and which are installed

in a newly acquired aircraft of a different type are

eligible for approval at the operator's approved

overhaul time providing it can be determined that

environmental factors will not have an adverse effect

on them.

i.   For those aircraft not listed in AC 121-1A or an MRB

document, the basic principle followed by the

Administrator will be that the inspections, checks,

maintenance, or overhaul be performed at times well

within the expected or proven service life of each

component of the aircraft.

In determining what the expected or proven time

limitations of an aircraft or any of its components

might be, the Administrator will consider the following

factors:

(1)  Geographical area or areas of operation.

(2)  Engine operating power, procedures, etc.

(3)  Number of landings, long haul vs. short haul.

(4)  Maintenance organization and inspection

procedures.

(5)  Other operators' service experience.

(6)  Manufacturer's recommendations.

(7)  Service history.

Special reliance will be placed on service experience,

including the information obtained from tests,

inspections, or measurements that were performed while

accumulating service experience.  The maintenance

program should specify the maintenance checks,

inspections, and overhauls to be performed and the

times at which they will be accomplished.

j.   An aircraft maintained in accordance with the

provisions of a reliability program may be incorporated

into another operator's maintenance system by direct

inclusion under the terms of the previous or present

operator's reliability program, if the PMI/PAI

determines that the maintenance controls established

relate realistically and responsively to operating

experience.

NOTE:  It is intended that the specific needs of the

operator, in terms of operating philosophy,

recordkeeping practices, statistical and data

processing, be thoroughly evaluated prior to program

approval.  Areas of program compatibility to be

considered are:  (1)  Adequacy of organizational

structure; (2)  Suitability of data collection and

analysis system; and (3)  Timeliness of corrective

action program.  Additional information that may prove

useful can be found in AC 120-17A.

*    k.   In the event an operator and the assigned PMI/PAI

cannot reach an agreement in the application of either

program, the assigned inspector should contact the

regional office for guidance.  If further guidance is

needed the Chief, Air Carrier Airworthiness Branch,

AFS-230, Washington, D.C., should be contacted by the

regional office.                                      *

5.   REVISION OF TIME LIMITATIONS - GENERAL.

a.   The inspection and overhaul time limitations applicable

to airframes, powerplants, propellers, and appliances

are normally revised on the basis of service experience

unless controlled by a reliability program in

accordance with AC 120-17A.

b.   Increases in such time limitations may be made as often

as the operator can submit proper justification and

substantiation to warrant a time increase.  The

justification should indicate that such increases will

not adversely affect airworthiness of the aircraft.

When the service records indicate that any component or

subcomponent consistently requires repair, adjustment,

or other maintenance because of damage, wear, or

deterioration, within the current time limitations, the

operator will be responsible for initiating corrective

action.

c.   Time limitations may be established in terms of hours

of operation, cycles, multiples of engine overhaul

periods, or multiples of inspection periods.

d.   Time limitations for components on which deterioration

is not necessarily a function of operation hours, such

as electronic units, emergency flotation equipment,

etc., may be established in terms of calendar months.

6.   AIRFRAME - REVISION OF TIME LIMITATIONS.

a.   The increases of time limitations for overhaul or major

inspections of airframes are normally based on

evaluation of all pertinent service records and/or

examination of at least one aircraft, of the model

involved, that has been operated within five percent of

the currently approved time limitation; or

b.   Any other method acceptable to the assigned principal

maintenance inspector such as industry experience,

etc., may also be used when sufficient justification

can be furnished by the operator.

c.   When a pattern or block overhaul type of maintenance

system is used, it will be permissible to reschedule

individual items in another block or pattern, if

performance and condition of the specific item warrants

such an increase.

7.   POWERPLANT AND ASSOCIATED APPLIANCES - REVISION OF TIME

LIMITATIONS.

a.   Increases in engine overhaul periods may be approved in

increments mutually agreed upon by the operator and the

assigned principal maintenance inspector.  Increase in

time limitations are normally considered on the basis

of satisfactory service experience and a teardown

examination of one exhibit engine.  The engine chosen

for exhibit should have operated to within five percent

of the currently approved time limitation; or

b.   Any other method acceptable to the assigned principal

maintenance inspector such as industry experience,

etc., may also be used to increase engine overhaul

periods when sufficient justification can be furnished

by the operator.

c.   Engine accessories may be operated to multiples of the

approved engine overhaul limit if it can be shown that

satisfactory service and overhaul experience justifies

the increase and will not adversely affect the

airworthiness of the component involved.

8.   APPLIANCES - REVISION OF TIME LIMITATIONS.  Increases in

established times for inspection, bench test, or overhaul

periods are normally based on consideration of the following

factors:  (1) geographical area or areas of operation; (2)

number of landings, long haul vs. short haul; (3)

maintenance organization and inspection procedures; (4)

manufacturers' recommendations; and (5) service history.

When electrical/electronics appliances are maintained on an

"on condition" basis, special consideration should be given

to the continued airworthiness of mechanical components of

such equipment.

9.   RELIABILITY VS. HARDTIME CONVERSION.  The following

procedures apply to aircraft transferred from a nonoverhaul

program (maintenance control by reliability methods) to a

program utilizing hard times.

a.   The record of last overhaul which is required by

section 121.380 will be used to determine time on units

which have been overhauled.

b.   When a record of last overhaul is not available for

units not subject to overhaul (for example, units under

reliability control), the carrier will determine TSO or

TSN on each unit by subtracting total time on aircraft

at the time of unit installation from the total time on

the aircraft at the time of change to an overhaul

program.  The time on each unit so determined will be

used to determine time remaining to overhaul on the new

program.

c.   If adequate records are not available to determine TSO

or TSN, the unit involved will have to be overhauled

before further use.

10.  EMERGENCY EQUIPMENT.  The inspection periods for first aid

kits, flotation equipment, evacuation slides, and other

emergency equipment should assure the continued

serviceability and immediate readiness of such equipment for

its intended emergency purposes.  Major inspection periods

are established for the purpose of determining that all

components of the emergency equipment are complete and

serviceable and may be expected to remain in this condition

until the next major inspection or actual use under

emergency conditions.

11.  AVIONICS AND INSTRUMENTS.  All Operations Specifications,

Aircraft Maintenance, must identify the manufacturer and

model number of the major components in ATA systems 22, 23,

24, 31, 33, 34, and 77.  If the operator chooses, the major

components and required data can be listed in any other

approved manual or document provided that the manual or

document is identified in the approved Maintenance

Specifications, preferably in the General section.

12.-15.  RESERVED.

CHAPTER 2.  PRORATION

16.  PURPOSE.  Proration is a mathematical procedure used to

determine the percent of overhaul time expended by one

operator and to establish the time remaining to overhaul for

the new operator.  As new type equipment becomes available,

many air carriers acquire this new equipment and sell or

lease their older equipment to other air carriers.  Since

the older equipment has accumulated a certain amount of time

in service, it is desirable to transfer this time as it

applies to an airframe and its installed powerplants,

propellers, and appliances to the buyer.  This "time in

service" may be phased in or prorated to the approved

overhaul time of the buyer to permit further utilization of

the affected items without the need for immediate overhaul.

17.  APPLICATION.

a.   When a buyer's approved overhaul time limits are lower

than those of the seller, the buyer has two options:

(1)  He (the buyer) may elect to use the proration

process.

(2)  The buyer may elect to use direct inclusion

providing the previous operator's actual time

since overhaul is less than the buyer's approved

overhaul time limit.

b.   When the direct inclusion option is used, the

difference between the buyer's approved overhaul time

limit and the previous operator's actual time since

overhaul will determine the time remaining to overhaul

for the buyer.

c.   When the buyer's approved overhaul time limit is higher

than that of the seller, proration procedures should be

used to adjust the time since overhaul.  However, based

upon the buyer's assigned PMI's comparison of the

buyer's and seller's maintenance program for

similarity, direct inclusion may be used if both

programs are found comparable.

18.  SCOPE AND LIMITATIONS.

a.   An operator's responsibility for maintaining his

aircraft in an airworthy condition is in no way

lessened by proration of the aircraft's time since

overhaul.

b.   All times obtained by use of the proration formula may

be rounded out to the nearest 10-hour figure.

c.   The percentage of aircraft overhaul time expended is

computed on the basis of the previous operator's actual

time since overhaul.

d.   When block/pattern overhaul time is to be prorated,

each block/pattern shall be treated separately, as

though a complete aircraft were being prorated.  (See

Appendix 1, Figures 1 and 2.)

e.   The operator will not be permitted to change aircraft

records to reflect only the adjusted time since

overhaul.  The operator will be required to maintain

adequate records showing the adjusted time since

overhaul and the actual time since overhaul.

f.   No partial proration will be acceptable.  If a carrier

elects to prorate, then the airframe and all its

installed powerplants, propellers, and appliances will

also be prorated.  Spare engines and propellers

acquired by the buyer at the time of sale or at a later

date with "time in service" may also be prorated.

g.   Aircraft components that are life-limited and

airworthiness directives may not be prorated.

h.   Amendments to "Operations Specifications - Aircraft

Maintenance," which increase overhaul time limits, are

applicable to all aircraft of the same type and model

operated by a carrier.  Such time increases would apply

equally to aircraft operating on a prorated time basis

as well as to the others in the fleet.  Aircraft

operating on prorated times will not have the time

increase prorated, but will be credited with the entire

increase.

i.   "Operations Specifications - Aircraft Maintenance," and

the applicable preface page which established prorated

time limits, will be cancelled when the aircraft,

powerplants, propellers, and appliances to which they

relate are first overhauled.  Thereafter, overhaul will

be accomplished in accordance with the operator's

approved overhaul time.

j.   For proration purposes, aircraft obtained from military

or non-air carrier civilian sources will be assigned

the Standard Operations Specifications - Aircraft

Maintenance or Maintenance Review Board Report times as

applicable to the particular aircraft.

k.   Any foreign air carrier aircraft listed in the Standard

Operations Specifications - Aircraft Maintenance or an

applicable Maintenance Review Board Report may be

phased into a U.S. air carrier's program, through the

proration formula, provided the U.S. operator presents

satisfactory evidence which indicates that the program

under which the aircraft was maintained is at least

equivalent to a program approved by the FAA for a

similar type of aircraft.

l.   Aircraft acquired by either a "new operator" or "buyer"

(see definitions, Chapter 1, paragraph 4) may enter

service via proration or direct inclusion.  The reason

for the difference in terminology lies in the fact that

a new operator will be limited by the maximum times set

forth in the Standard Operations Specifications

- Aircraft Maintenance (Appendix 2) or the applicable

MRB report.  On the other hand, a "buyer" will have

previously established time limits for the particular

aircraft in question.  For ease in presenting proration

sample exercises shown in Appendix 1, the terms "new

operator" and "buyer" are used interchangeably.

19.  DATA REQUIRED.  The following data will be submitted to the

assigned air carrier maintenance inspector by the operator,

when he desires to apply for approval of prorated overhaul

times:

a.   All "Operations Specifications - Aircraft Maintenance"

containing the overhaul time limits utilized for the

particular aircraft by the previous operator.  If the

Operations Specifications do not show hours, the buyer

shall submit such other specifications or documents

which will, in fact, establish the overhaul time limits

in hours.  If a conversion to hours is necessary, the

computations used for the conversion will be included

(see Appendix 1, Figure 7).

b.   All "Operations Specifications, Preface Pages"

pertinent to the particular aircraft.  This is

essential because the previous operator may have

operated the subject aircraft in accordance with a

preface page showing utilization of adjusted time since

overhaul calculated in accordance with the proration

formula.

c.   A document itemizing (for airframe, powerplants,

propellers, and appliances):

(1)  The previous operator's:

(a)  Approved overhaul time.

(b)  Time since overhaul.

(c)  Percent of overhaul time used.

(2)  The buyer's:

(a)  Approved overhaul time.

(b)  Prorated time since overhaul.

(c)  Prorated time remaining to overhaul.

(See Appendix 1, Figure 5.)

d.   When a block/pattern or similar overhaul system was

used by the previous operator, a document will be

submitted showing:

(1)  The time since overhaul for each block or pattern

together with a list of items which are part of

the block or pattern (see Appendix 1, Figure 8).

(2)  The time since overhaul for each individual item

on the aircraft.

e.   "Operations Specifications - Aircraft Maintenance" or a

"Proration Document" containing prorated times for each

aircraft operating on prorated times.  In either of

these cases, a pertinent preface page must be prepared

and submitted.

(1)  In the first case where the approved prorated

times are listed on "Operations Specifications

- Aircraft Maintenance" pages, a preface page such

as that shown in Appendix 1, Figure 9, will be

executed.

(2)  Where a proration document is used to list

prorated times in lieu of showing them on the

"Operations Specifications - Aircraft Maintenance"

pages, a document shall be prepared for each

aircraft operating on prorated times.  Each

document shall be clearly identified and each

shall be made a part of the Operations

Specifications by means of a preface page such as

the example shown in Appendix 1, Figure 11.

(3)  The information required by item 15c will provide

the supporting data for these specification pages

or documents.

The aforementioned documents are essential to the

application of the formula in establishing the adjusted

time since overhaul on each component, area, section,

etc., of the aircraft because if the proration formula

has been used by the previous operator of the aircraft

involved, the time since overhaul figures presented in

the document will not be the same as the actual hours

of time in service since the last overhaul of the

component, area, etc.  The proration formula for the

buyer should be calculated, using the actual time since

overhaul figures maintained by the previous operator.

20.  PRORATION FORMULA.  The simple mathematical procedure

explained below will result in a figure that will be the

"time remaining to overhaul" for the buyer.

KNOWN

8,000 hours --- Previous operator's approved overhaul time

limit.

2,000 hours --- Previous operator's time since overhaul.

12,000 hours --- Buyer's approved overhaul time limit.

STEP I

Divide the previous operator's TSO figure by the previous

operator's approved overhaul time limit (carry out to three

places).  This division will result in a decimal which can

be used to represent the percentage of approved overhaul

time already used.

_____.250 --- Percent of O.H. time used by

8,000/2,000.000       previous operator.

STEP II

Multiply the buyer's approved overhaul time limit figure by

the decimal arrived at in STEP I.  This multiplication will

result in the prorated TSO to be used by the buyer.

12,000 --- Buyer's approved O.H. time limit.

x .250

------

600.000

2400.0

--------

3000.000 --- Buyer's prorated TSO.

STEP III

Subtract the prorated TSO arrived at in STEP II from the

buyer's approved overhaul time limit.  The resultant figure

will be number of hours remaining to overhaul for the buyer.

12,000 --- Buyer's approved O.H. time limit.

-3,000

------

9,000 --- Buyer's prorated time remaining to

overhaul.

21.-25.  RESERVED.

----------------------------------------------------------------

FIGURE 1.  TRANSFER OF AIRCRAFT FROM A BLOCK/PATTERN SYSTEM

TO A ONE-TIME OVERHAUL

In this type of situation, each block/pattern is prorated as

though it was the overhaul time for the entire aircraft.

KNOWN

16,000 hours --- Previous operator's approved overhaul time limit

which is divided into four blocks/patterns of

4,000 hours each.

3,000 hours --- Previous operator's TSO for block/pattern A.

7,000 hours --- Previous operator's TSO for block/pattern D.

11,000 hours --- Previous operator's TSO for block/pattern C.

15,000 hours --- Previous operator's TSO for block/pattern B.

12,000 hours --- Buyer's approved overhaul time limit.

COMPUTATION  BLOCK/PATTERN A

STEP I

_____.187 --- Percent of O.H. time used by previous

16,000/3,000.000       operator.

STEP II

12,000 --- Buyer's approved O.H. time limit.

x .187

------

84.000

960.00

1200.0

--------

2244.000 --- Prorated TSO for buyer's block/pattern A.

STEP III

12,000 --- Buyer's approved O.H. time limit.

-2,244

------

9,756 --- Prorated time remaining to overhaul for buyer's

block/pattern A.

COMPUTATION  BLOCK/PATTERN B

STEP I

______.937 --- Percent of O.H. time used by previous

16,000/15,000.000       operator.

STEP II

12,000 --- Buyer's approved O.H. time limit.

x .937

------

84.000

360.00

10,800.0

----------

11,244.000 --- Prorated TSO for buyer's block/pattern B.

STEP III

12,000 --- Buyer's approved O.H. time limit.

11,244

------

756 --- Prorated time remaining to overhaul for buyer's

block/pattern B.

COMPUTATION  BLOCK/PATTERN C

STEP I

______.687 --- Percent of O.H. time used by previous

16,000/11,000.000       operator.

STEP II

12,000 --- Buyer's approved overhaul time limit.

x .687

------

84.000

960.00

7200.0

--------

8244.000 --- Prorated TSO for buyer's block/pattern C.

STEP III

12,000 --- Buyer's approved O.H. time limit.

- 8,244

-------

3,756 --- Prorated time remaining to overhaul for buyer's

block/pattern C.

COMPUTATION  BLOCK/PATTERN D

STEP I

_____.437 --- Percent of O.H. time used by previous

16,000/7,000.000       operator.

STEP II

12,000 --- Buyer's approved O.H. time limit.

x .437

------

84.000

360.00

4800.0

--------

5244.000 --- Prorated TSO for buyer's block/pattern D

STEP III

12,000 --- Buyer's approved O.H. time limit.

- 5,244

-------

6,756 --- Prorated time remaining to overhaul for buyer's

block/pattern D.

It should be recognized that when an operator elects to transfer

an aircraft from a block/pattern system to a one-time overhaul, a

substantial amount of "time remaining to overhaul" must be

sacrificed.

In the example given here, the buyer's "time remaining to

overhaul" for each block/pattern is as follows:

A - 9756                   C - 3756

B -  756                   D - 6756

Since the buyer's approved overhaul time is 12,000 hours, it

follows that all the items in block/pattern "B" will be due for

overhaul within 756 hours.  To phase the aircraft into a one-

time overhaul, all blocks would have to be overhauled at this

time.

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 2.  TRANSFER OF AIRCRAFT FROM A BLOCK/PATTERN SYSTEM TO A

BLOCK/PATTERN SYSTEM

In this type of situation, each block/pattern is prorated as

though it was the overhaul time for the entire aircraft.

KNOWN

(Based on the figures established in Figure 1.)

16,000 hours --- Previous operator's approved time limit which is

divided into four blocks/patterns of 4,000 hours

each.

.187       --- Percent of block/pattern A overhaul time used by

previous operator.

.937       --- Percent of block/pattern B overhaul time used by

previous operator.

.687       --- Percent of block/pattern C overhaul time used by

previous operator.

.437       --- Percent of block/pattern D overhaul time used by

previous operator.

12,000 hours --- Buyer's approved overhaul time limit which is to

be divided into four blocks/patterns of 3,000

hours each.  (Blocks/patterns I, II, III, and

IV)

COMPUTATION  BLOCK/PATTERN NO. I

STEP I

12,000 --- Buyer's approved overhaul time limit.

x .187 --- Percent of overhaul time used by previous

------       operator.

84.000

960.00

1200.0

--------

2244.000 --- Prorated TSO for buyer's block/pattern No. I.

STEP II

12,000 --- Buyer's approved overhaul time limit.

-2,244

------

9,756 --- Prorated time remaining to overhaul for buyer's

block/pattern No. I.

COMPUTATION  BLOCK/PATTERN NO. II

STEP I

12,000

X .937

------

84.000

360.00

10,800.0

----------

11,244.000 --- Prorated TSO for buyer's block/pattern No. II.

STEP II

12,000

-11,244

-------

756 --- Prorated time remaining to overhaul for

buyer's block/pattern No. II.

COMPUTATION  BLOCK/PATTERN NO. III

STEP I

12,000

x .687

------

84.000

960.00

7,200.0

---------

8,244.000 --- Prorated TSO for buyer's block/pattern No. III.

STEP II

12,000

-8,244

------

3,756 --- Prorated time remaining to overhaul for

buyer's block/pattern No. III.

COMPUTATION  BLOCK/PATTERN NO. IV

STEP I

12,000

x .437

------

84.000

360.00

4,800.0

---------

5,244.000 --- Prorated TSO for buyer's block/pattern No. IV.

STEP II

12,000

-5,244

------

6,756 --- Prorated time remaining to overhaul for

buyer's block/pattern No. IV.

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 3.  TRANSFER OF AIRCRAFT FROM A ONE-TIME OVERHAUL TO A

BLOCK/PATTERN SYSTEM (BUYER'S APPROVED OVERHAUL TIME

LIMIT IS HIGHER THAN THAT OF THE PREVIOUS OPERATOR)

In this process it is first necessary to find the buyer's

"prorated time since overhaul" and his prorated "time remaining

to overhaul" for the entire aircraft.  This is accomplished by

first applying the routine proration formula as shown below.

KNOWN

12,000 hours --- Previous operator's approved overhaul time

limit.

3,000 hours --- Previous operator's time since overhaul.

16,000 hours --- Buyer's approved overhaul time limit which is to

be divided into four blocks/patterns of 4,000

hours each.  (Blocks/patterns A, B, C, and D)

STEP I

_____.250 --- Percent of overhaul time used by

12,000/3,000.000       previous operator.

STEP II

16,000 --- Buyer's approved overhaul time limit.

x .250

------

800.000

3,200.0

---------

4,000.000 --- Buyer's prorated TSO.

STEP III

16,000 --- Buyer's approved overhaul time limit.

-4,000 --- Buyer's prorated TSO.

------

12,000 --- Buyer's prorated time remaining to overhaul.

In this particular example, since the buyer has elected to

transfer an aircraft from a one-time overhaul to a four

block/pattern system, he should recognize that a substantial

amount of his time remaining to overhaul will have to be

sacrificed.  This is brought about by the need to overhaul the

entire aircraft prior to 12,000 hours and at the same time, phase

selected portions of it into various blocks/patterns.

EXAMPLE

The buyer, desiring to establish a four block/pattern system,

separates his maintenance program into four equal parts and

places the items so separated into either block/pattern A, B, C,

or D.  Assuming the selection has been made, the blocks/patterns

would look like this:

Block/pattern A = 4,000 hours (cumulative time = 4,000 hours)

Block/pattern B = 4,000 hours (cumulative time = 8,000 hours)

Block/pattern C = 4,000 hours (cumulative time = 12,000 hours)

Block/pattern D = 4,000 hours (cumulative time = 16,000 hours)

The effect on items in each block/pattern as the result of

phasing them into a four block/pattern system would be as

follows:

BLOCK/PATTERN A

These items would have to be overhauled at 4,000 hours TSO for

the buyer.

This would result in a loss of 8,000 hours "time remaining to

overhaul."

BLOCK/PATTERN B

These items would have to be overhauled at 8,000 hours TSO for

the buyer.

This would result in a loss of 4,000 hours "time remaining to

overhaul."

BLOCK/PATTERN C

These items will be overhauled at 12,000 hours TSO for the buyer.

Since it was previously established through proration that this

was the buyer's "time remaining to overhaul," no time will be

sacrificed on the items scheduled in this block/pattern.

BLOCK/PATTERN D

The items in this block/pattern will have to be overhauled at a

point at, or prior to 12,000 hours and again at 16,000 hours in

order to properly phase them into the system.  The initial time

of overhaul of these particular items should be at the option of

the buyer, providing they do not exceed 12,000 hours.  There are

several methods he may choose from to accomplish this initial

overhaul.  Among these are:

1.  Initially O.H. all block/pattern D items in block/pattern   A

2.  Initially O.H. all block/pattern D items in block/pattern   B

3.  Initially O.H. all block/pattern D items in block/pattern   C

4.  Initially O.H. 1/2 of all block/pattern D items in

block/pattern                                               A

and O.H. 1/2 of all block/pattern D items in block/pattern  B

5.  Initially O.H. 1/2 of all block/pattern D items in

block/pattern                                               B

and O.H. 1/2 of all block/pattern D items in block/pattern  C

6.  Initially O.H. 1/2 of all block/pattern D items in

block/pattern                                               A

and O.H. 1/2 of all block/pattern D items in block/pattern  C

7.  Initially O.H. 1/3 of all block/pattern D items in

block/pattern                                               A

and O.H. 1/3 of all block/pattern D items in block/pattern  B

and O.H. 1/3 of all block/pattern D items in block/pattern  C

Because of the previously established prorated figure of 12,000

hours remaining to overhaul, the buyer stands to lose the same

total amount of time regardless of which method he chooses.

Method #7 appears to be the most practical approach, since it

would tend to spread the workload over a 12,000 hour period.  The

entire block/pattern D would, of necessity, have to be overhauled

again at 16,000 hours at which time all items would be correctly

phased into their proper block/pattern.  Consideration should be

given by the assigned inspectors to the extent of inspection

(overhaul) required in the case of initial overhauls that are

accomplished early solely for the purpose of phasing an aircraft

into a block/pattern system.

In the foregoing example, it can readily be seen that block A

items at the time of initial overhaul by the buyer will actually

have accumulated only 7,000 hours since previously overhauled

while block/pattern C items will have accumulated 15,000 hours.

In either case, it must be remembered that another 16,000 hours

will pass before they are overhauled again.

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 4.  TRANSFER OF AIRCRAFT FROM A ONE-TIME OVERHAUL TO A

BLOCK/PATTERN SYSTEM  (BUYER'S APPROVED OVERHAUL TIME

LIMIT IS LOWER THAN THAT OF THE PREVIOUS OPERATOR.)

In this process it is first necessary to find the buyer's

prorated "time since overhaul" and prorated "time remaining to

overhaul" for the entire aircraft.  This is accomplished by first

applying the routine proration formula as shown below:

KNOWN

12,000 hours --- Previous operator's approved overhaul time

limit.

3,000 hours --- Previous operator's time since overhaul.

8,000 hours --- Buyer's approved overhaul time limit which is to

be divided into four blocks/patterns of 2,000

hours each (A, B, C, and D).

STEP I

_____.250 --- Percent overhaul time used by

12,000/3,000.000       previous operator.

STEP II

8,000 --- Buyer's approved overhaul time limit.

x.250

-----

400.000

1,600.0

---------

2,000.000 --- Buyer's prorated TSO.

STEP III

8,000 --- Buyer's approved overhaul time limit.

-2,000 --- Buyer's prorated TSO.

------

6,000 --- Buyer's prorated time remaining to

overhaul.

In this particular example, since the buyer has elected to

transfer an aircraft from a one-time overhaul to a four

block/pattern system, he should recognize that a substantial

amount of his time remaining to overhaul will have to be

sacrificed.  This is brought about by the need to overhaul the

entire aircraft prior to the accumulation of 6,000 additional

hours and at the same time, phase selected portions of it into

various blocks/patterns.

EXAMPLE

The buyer, desiring to establish a four block/pattern system,

separates his maintenance program into four equal parts and

places the item so separated into either block/pattern A, B, C,

or D.  Assuming the selection has been made, the block/pattern

would look like this:

Block/pattern A = 2,000 hours (cumulative time = 2,000 hours)

Block/pattern B = 2,000 hours (cumulative time = 4,000 hours)

Block/pattern C = 2,000 hours (cumulative time = 6,000 hours)

Block/pattern D = 2,000 hours (cumulative time = 8,000 hours)

The effect of items in each block/pattern as the result of

phasing them into a four block/pattern system would be as

follows:

BLOCK/PATTERN A

These items would have to be overhauled at 2,000 hours TSO for

the buyer.

This would result in a loss of 4,000 hours "time remaining to

overhaul."

BLOCK/PATTERN B

These items would have to be overhauled at 4,000 hours TSO for

the buyer.

This would result in a loss of 2,000 hours "time remaining to

overhaul."

BLOCK/PATTERN C

These items will be overhauled at 6,000 hours TSO for the buyer.

Since it was previously established through proration that this

was the buyer's "time remaining to overhaul," no time will be

sacrificed on the items scheduled in this block/pattern.

BLOCK/PATTERN D

The items in this block/pattern will have to be overhauled at a

point at, or prior to 6,000 hours and again at 8,000 hours in

order to properly phase them into the system.  The initial time

of overhaul of these particular items should be at the option of

the buyer, providing they do not exceed 6,000 hours.  There are

several methods he may choose from to accomplish this initial

overhaul.  Among these are:

1.  Initially O.H. all block/pattern D items in block/pattern   A

2.  Initially O.H. all block/pattern D items in block/pattern   B

3.  Initially O.H. all block/pattern D items in block/pattern   C

4.  Initially O.H. 1/2 of all block/pattern D items in

block/pattern and O.H. 1/2 of all block/pattern D items     A

in block/pattern                                            B

5.  Initially O.H. 1/2 of all block/pattern D items in

block/pattern and O.H. 1/2 of all block/pattern D items     B

in block/pattern                                            C

6.  Initially O.H. 1/2 of all block/pattern D items in

block/pattern and O.H. 1/2 of all block/pattern D items     A

in block/pattern                                            C

7.  Initially O.H. 1/3 of all block/pattern D items in

block/pattern and O.H. 1/3 of all block/pattern D items     A

in block/pattern  and O.H. 1/3 of all block/pattern D items B

in block/pattern                                            C

Because of the previously established prorated figure of 6,000

hours remaining to overhaul, the buyer stands to lose the same

total amount of time regardless of which method he chooses.

Method #7 appears to be the most practical approach, since it

would tend to spread the workload over a 6,000 hour period.  The

entire block/pattern D would, of necessity, have to be overhauled

again at 8,000 hours at which time all items would be correctly

phased into their proper block/pattern.  Consideration should be

given by the assigned inspectors to the extent of inspection

(overhaul) required in the case of initial overhauls that are

accomplished early solely for the purpose of phasing an aircraft

into a block/pattern system.

In the foregoing example, it can readily be seen that block A

items at the time of initial overhaul by the buyer will actually

have accumulated only 5,000 hours since previously overhauled

while block/pattern C items will have accumulated 9,000 hours.

In either case it must be remembered that another 8,000 hours

will pass before they are overhauled again.

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 5.  FORMAT FOR PRESENTATION OF PRORATION

DATA ON AIRCRAFT BEING TRANSFERRED

Previous Operator (__________)  Buyer (_________)

Identify            Identify

Block/Pattern   Approved  Time   Percent of  Approved Pro-  Pro-

or Component    Overhaul  Since  Overhaul    Overhaul rated rated

& Serial No.    Time      Over-  Time Used   Time     T.S.O. Time

haul                              To

Over-

haul

(16000)   Respective         (12000)  Respective

Block/                      Block/

Pattern                     Pattern

Block/Pattern A 4000       3000    .187      12000     2244  9756

Block/Pattern B 4000      15000    .937      12000    11244   756

Block/Pattern C 4000      11000    .687      12000     8244  3756

Block/Pattern D 4000       7000    .437      12000     5244  6756

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 6.  TRANSFER OF PREVIOUSLY PRORATED AIRCRAFT

An aircraft was acquired by operator "X" and placed on his

maintenance program through the proration process.  After

acquisition, "X" operated the aircraft for an additional 1,000

hours.

1.  12,000 hours = approved overhaul time for "X".

2.  3,000 hours = prorated TSO for "X" at time of acquisition.

3.  2,000 hours = actual TSO at time of acquisition by "X".

4.  1,000 hours = additional flight time added to aircraft by

"X".

5.  3,000 + 1,000 = 4,000 hours - "X's" prorated TSO.

6.  2,000 + 1,000 = 3,000 hours - actual TSO on aircraft.

Operator "X" now desires to transfer the aircraft to operator

"Y".  The overhaul time is to be prorated for operator "Y" and

his approved overhaul time is 14,000 hours.

7.  3,000 divided by 12,000 = .250 of overhaul time used by "X".

8.  14,000 hours = approved O.H. time for "Y".

9.  14,000 x .250 = 3,500 hours prorated TSO for "Y".

10.  14,000 - 3,500 = 10,500 hours remaining to overhaul for

operator "Y" at time of transfer.

NOTE:  Actual TSO (Step 7) was used for purpose of proration to

operator "Y", not the prorated TSO.

* The buyer of a previously prorated aircraft whose approved

overhaul time limits are identical to the previous operators may

utilize the remaining prorated time of the previous operator.

When a buyer uses the remaining prorated time, a document shall

be prepared listing the previous operator or operators' approved

overhaul times on which the proration was based and shall be made

part of the operations specifications by means of a preface page

such as the example shown in Appendix 1, Figure 12.             *

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 7.  PROCEDURES FOR CONVERTING CALENDAR OVERHAUL

(MONTHS) TO HOURS SINCE OVERHAUL FOR PRORATION

PURPOSES

METHOD A

Previous operator's overhaul time limit is 18 months:  (360 +

180 = 540.

Previous operator's time since overhaul is 180 days.

Buyer's approved overhaul time limit is 2,000 hours.

COMPUTATIONS

180

--- = .333 time since overhaul.

540

.33 of 2,000 hours = 666 hours prorated time since overhaul for

buyer.

2,000 hours - 666 = 1,334 hours.  Buyer's prorated time remaining

to overhaul.

METHOD B

Previous operator's overhaul time limit:  18 months or 540 days.

Previous operator's utilization time:  8 hours per day.

Previous operator's overhaul time limit in hours:  (540 days x 8

hrs.) = 4,320.

Previous operator's time since overhaul (180 x 8 hours) = 1,440

hours.

Buyer's overhaul time limit is 2,000 hours.

COMPUTATIONS

1400

Time since overhaul in percent:  ---- = .333

4320

.333 of 2,000 hours = 666 hours prorated time since overhaul.

2,000 hours - 666 = 1,334 hours.  Buyer's prorated time remaining

to overhaul.

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 8.  METHOD OF DEPICTING AREAS, SECTIONS, COMPONENTS, ETC.,

THAT ARE TIED TO A SPECIFIC BLOCK

The following presentation is an example of how items such

as areas, sections, and appliances are included in a block.

An operator should submit such items and relate the items to

the block, or submit actual time for each item.

Block/Pattern    Block/Pattern    Block/Pattern    Block/Pattern

A                B                C                D

Nose gear        Center Section   Right wing fuel  Empennage

assembly &                        cells

components

Steering         Left wing fuel   Lights           Rudder-

mechanism &      cells                             vertical fin

controls

Accumulators     Pylons, Nos.     Electrical       Stabilizer

1 & 2            units,

components,

connections,

Nose gear doors  Lines            etc.

Brackets,        Electrical       Hydraulics       Tail

hinges, etc.     connections                       Compartment

Lights, wires,   Flaps                             Lights

etc.

Air inlets &     Spoilers                          Booster

anti-icing                                         control

Hydraulic

fittings

Main landing

gear assembly

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 9.  OPERATIONS SPECIFICATIONS - PREFACE PAGE

FOR AIRCRAFT ON PRORATED TIME

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

Page  of Page

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

PREFACE PAGE FOR AIRCRAFT ON PRORATED TIME

The aircraft listed herein, including powerplants, propellers,

and appliances which have prorated times, shall be overhauled in

accordance with their respective limitations as set forth in:

Operations Specifications

Aircraft Maintenance

Amendment No. _____, Dated _____

These specifications are applicable to:  Aircraft N_____ - Serial

No. ____, its powerplants, propellers, and appliances until they

are first overhauled.  Thereafter, these specifications are

cancelled and the aircraft will be inspected and overhauled in

accordance with the _____ airlines maintenance program and the

approved time limits.

Records maintained on the above aircraft shall show the actual

and adjusted time since overhaul and, thereafter, such time in

service shall be added thereto.

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 10.  OPERATIONS SPECIFICATIONS AIRCRAFT

MAINTENANCE - GENERAL

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

Page  of Page

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

(Part 121)

Irrespective of the type of operation to be conducted by (name of

operator), the continuous airworthiness and inspection program

limitations which are described and specified in these Operations

Specifications shall be applicable to all (name of operator)

aircraft listed and authorized for use under Federal Aviation

Regulations 121.

The operator shall provide in its currently effective Maintenance

Manual a comprehensive maintenance program necessary to fulfill

its responsibility to maintain the aircraft in an airworthy

condition in accordance with applicable Federal Aviation

Regulations and Standards prescribed and approved by the

Administrator.

The aircraft and its component parts, accessories, and appliances

shall be maintained in an airworthy condition in accordance with

the maximum time limits hereinafter set forth for the

accomplishment of the overhaul, periodic inspections, and routine

checks of the aircraft and its component parts, accessories, and

appliances.

"On Condition" items will be maintained in a continuous airworthy

condition by periodic and progressive inspections, checks,

services, repair, and/or preventive maintenance and shall be

appropriately described in the operator's Maintenance Manual.

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 11.  OPERATIONS SPECIFICATIONS - PREFACE PAGE

FOR AIRCRAFT ON PRORATED TIME

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

Page  of Page

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

PREFACE PAGE FOR AIRCRAFT ON PRORATED TIME

The aircraft listed hereon, including powerplants, propellers,

and appliances which have prorated times, shall be overhauled in

accordance with the respective limits as set forth in:

Proration Document

No. __________

Dated ________

This document is applicable to:  Aircraft N ____ - Serial No.

_____, its powerplants, propellers, and appliances until they are

first overhauled.  Thereafter, this document is cancelled and the

aircraft will be inspected and overhauled in accordance with the

_____ airlines maintenance program and the approved time limits.

Records maintained on the above aircraft shall show the actual

and adjusted time since overhaul and, thereafter, such time in

service shall be added thereto.

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

* FIGURE 12.  OPERATIONS SPECIFICATIONS - PREFACE PAGE FOR

AIRCRAFT USING PREVIOUS OPERATORS REMAINING

PRORATED TIMES.

Form Approved.

UNITED STATES OF AMERICA     OMB No. 04-R0075

DEPARTMENT OF TRANSPORTATION

FEDERAL AVIATION ADMINISTRATION

WASHINGTON

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

PREFACE PAGE FOR AIRCRAFT ON PRORATED TIME

The aircraft listed hereon had the airframe overhaul times

prorated when it was transferred from _____ Airlines with an FAA

approved overhaul time of 16,000 for the airframe to

_____ Airlines with an approved time of 12,000 hours.  The

aircraft is now operated by _____ Aviation who also has 12,000

hours airframe overhaul time.  Therefore this aircraft is

approved to use the remaining prorated time of _____ Airlines and

shall be overhauled in accordance with the respective limits set

forth in:

Proration Document

No. _______________________________

Dated _____________________________

This document is applicable to:  Aircraft N __________ - Serial

No. _____, until its first overhaul.  Thereafter, this document

is cancelled and the aircraft will be inspected and overhauled in

accordance with the __________ airlines maintenance program and

the approved time limits.

Records maintained on the above aircraft shall show the actual

and adjusted time since overhaul and, thereafter, such time in

service shall be added thereto.

Effective date _________________________

----------------------------------------------------------------

Appendix 2

----------------------------------------------------------------

FIGURE 1.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- AVIONICS

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          PAGE 1 of 2 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

AVIONICS

Overhaul      Inspection &

Period **    Check Period **

Communications*.  Chapter 23

Fixed Equipment - Wiring, plugs,

filters, junction boxes, relays,

resistors, capacitors, fuses,

circuit breakers, transformers,

antennas, transmission lines,

switches, controls, mounts, etc.

H. F. Communication System

V. H. F. Communication System

Sel-Cal Decoder

P. A. System

Amplifier

Interphone System

Amplifier

May be determined by assigned inspector **

Navigation*.  Chapter 34 (Radio-Radar)

Fixed Equipment - Wiring, plugs,

filters, junction boxes, relays,

resistors, capacitors, fuses,

circuit breakers, transformers,

antennas, transmission lines,

switches, controls, mounts, etc.

L. F. Navigation System

Receiver

Loop Antenna

V. H. F. Navigation System

Receiver (VOR/LOC)

Instrumentation Unit

I. L. S.  System

G. S. Receiver

Localizer Receiver

Marker Receiver

Loran System

Weather Radar System

Radar Altimeter System

ATC Transponder

Flight Director

Computer/Amplifier

Gyro

May be determined by assigned inspector **

Effective date _____________________

PAGE 2 of 2 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

AVIONICS

NOTE * The term "System" means all those interdependent

subassemblies, components, parts, etc., necessary for the

proper functioning of the system as a whole.  All the

individual components of the system should be listed.

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 2.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- DART 510/525

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          PAGE 1 of 2 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ENGINE MAKE - ROLLS ROYCE      PROPELLER MAKE - DOWTY ROTOL

ENGINE MODEL - DART 510        PROPELLER MODEL - R130/4-20-3/12E

ENGINE MODEL - DART 525        PROPELLER MODEL - R170/4-20-4/33

Overhaul      Inspection &

Period       Check Period

Propellers, Chapter 61

Alternator - Sync. Propeller         2000

Controller Propeller                 3500

Motor - Propeller Feathering         3500

Propeller Assembly                   3500

Pump - Propeller Feathering          3500

Powerplant General, Chapter 71

Cowling                              OC

Mount - Engine                       EO

Engine, Chapter 72

Accessory Gearbox                    3400

ACC Gearbox drive                    1400

Engine - Basic                       3000 *

Engine Fuel & Control, Chapter 73

Control Unit, Fuel Flow              4200

Indicator - Fuel Flow                7000

Pump - Engine Drive                  3000

Transmitter - Fuel Flow              2800

Ignition System - Chapter 74

Box, Ignition                        EO

Engine Indicating, Chapter 77

Generator DC                         1400

Indicator - Tachometer               2400

Indicator - Torque Pressure          6000

Transmitter - Torque Pressure        EO

Exhaust System - Chapter 78

Exhaust Unit                         EO

Oil System, Chapter 79

Transmitter - Oil Pressure           4000

Indicator - Oil Pressure             4000

* Sample one hot section inspection at 2000 hours, one engine

overhaul at 2400 hours, and one engine overhaul at 2700 hours.

Effective date _____________________

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ENGINE MAKE - ROLLS ROYCE      PROPELLER MAKE - DOWTY ROTOL

ENGINE MODEL - DART 510        PROPELLER MODEL - R179/4-20-4/33

Overhaul      Inspection &

Period       Check Period

Water Injection - Chapter 82

Actuator ADI                         2500

Pump ADI                             1400

Switch, Pressure Warning             EO

Valve, Pressure Relief               3000

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 3.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- DART 525

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ENGINE MAKE - ROLLS ROYCE      PROPELLER MAKE - DOWTY ROTOL

ENGINE MODEL - DART 525        PROPELLER MODEL - R130/4-20-4/12E

Overhaul      Inspection &

Period       Check Period

Propellers, Chapter 61

Alternator - Sync. Propeller        2000

Controller Propeller                3500

Motor, Propeller Feathering         3500

Propeller Assembly                  3500

Pump - Propeller Feathering         3500

Power Plant General, Chapter 71

Cowling                             OC

Mount, Engine                       EO

Engine, Chapter 72

Engine, Basic                       3000 *

Engine Fuel & Control, Chapter 73

Control Unit, Fuel Flow             4200

Indicator, Fuel Flow                7000

Pump, Engine Driven                 3000

Transmitter, Fuel Flow              2800

Ignition System, Chapter 74

Box, Ignition                       EO

Engine Indicating, Chapter 77

Generator DC                        1400

Indicator, Tachometer               2400

Indicator, Torque Pressure          6000

Transmitter, Torque Pressure        EO

Exhaust System, Chapter 78

Exhaust Unit                        EO

Oil System, Chapter 79

Transmitter, Oil Pressure           4000

Indicator, Oil Pressure             4000

Starting, Chapter 80

Starter                             EO

Water Injection, Chapter 82

Actuator ADI                        2500

Pump ADI                            1400

Valve, Pressure Relief              EO

* Sample one hot section inspection at 2000 hours, one engine

overhaul at 2400 hours, and one engine overhaul at 2700 hours.

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 4.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- PRATT & WHITNEY - R2000 SERIES

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          PAGE 1 of 2 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

R2000 SERIES

Overhaul      Inspection &

Period       Check Period

Propellers, Chapter 61

Motor, Propeller Feathering          3000

Propeller Assembly                   3000

Propeller Governors                  1500

Pump, Propeller Feathering           3000

Power Plant - General, Chapter 71

Actuator, Cowl Flap                  3000

Cowling                              1500

Mount, Engine                        1500

Engine, Chapter 72

Engine, Basic                        1500

Engine Fuel & Control, Chapter 73

Carburetor Assembly                  3000

Indicator, Fuel Flow                 4500

Indicator, Fuel Pressure             4500

Pump, Engine Driven                  1500

Transmitter, Fuel Flow               4500

Transmitter, Fuel Pressure           4500

Warning Unit, Fuel Pressure          4500

Ignition, Chapter 74

Ignition Harness                     1500

Spark Plugs                          OC

Engine Indicating, Chapter 77

Indicator, BMEP                      4500

Indicator, Carburetor Air

Temperature                       4500

Indicator, Cylinder Head Temperature 4500

Indication, Manifold Pressure        4500

Indicator, Tachometer                4500

Tachometer, Generator                3000

Exhaust, Chapter 78

Exhaust Manifold Assembly            1500

Effective date _____________________

PAGE 2 of 2 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

R2000 SERIES

Overhaul      Inspection &

Period       Check Period

Oil, Chapter 79

Indicator, Oil Pressure             3900

Indicator, Oil Quantity             3900

Indicator, Oil Temperature          3900

Oil Tank                   (3 E/C)

Regulator, Oil Cooler               1300

Transmitter, Oil Pressure           3900

Transmitter, Oil Quantity           3900

Transmitter, Torque Pressure        3900

Valve, Emergency Shutoff            3900

Warning Unit, Oil Pressure          3900

Starters, Chapter 80

Relay, Starter                      3900

Starter                             2600

NOTE:  Components or subcomponents of power plants that have

overhaul time limitations in multiples of the basic engine

overhaul time limitation shall receive an appropriate

inspection, check or test at the basic engine overhaul

period.

Effective date   December 15, 1962

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 5.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- PRATT & WHITNEY - R2800 SERIES

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          PAGE 1 of 2 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

R2800 SERIES

Overhaul      Inspection &

Period       Check Period

Propellers, Chapter 61

Motor, Propeller Feathering         3000

Propeller Assembly                  2500

Propeller Governors                 1500

Pump, Propeller Feathering          3000

Power Plant - General, Chapter 71

Actuator, Cowl Flap                 3000

Cowling                             1500

Mount, Engine                       1500

Engine, Chapter 72

Engine, Basic                       1500

Engine Fuel & Control, Chapter 73

Carburetor Assembly                 3000

Indicator, Fuel Pressure            4500

Pump, Engine Driven                 1500

Transmitter, Fuel Pressure          4500

Warning Unit, Fuel Pressure         4500

Ignition, Chapter 74

Ignition Harness                    1500

Spark Plugs                          330

Engine Indicating, Chapter 77

Indicators, BMEP                    4500

Indicators, Carburetor Air

Temperature                      4500

Indicators, Cylinder Head

Temperature                      4500

Indicators, Manifold Pressure       4500

Tachometer, Generator               3000

Exhaust, Chapter 78

Exhaust Manifold Assembly           1500

Effective date   December 15, 1962

Page 2 of 2 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

R-2800 and R-2800 C-CA-CB SERIES

Overhaul      Inspection &

Period       Check Period

Oil, Chapter 79

Indicator, Oil Pressure              4500

Indicator, Oil Quantity              4500

Indicator, Oil Temperature           4500

Oil Tank                    (3 E/C)

Regulator, Oil Cooler                1700

Transmitter, Oil Pressure            4500

Transmitter, Oil Quantity            4500

Transmitter, Torque Pressure         4500

Valve, Emergency Shutoff             4500

Warning Unit, Oil Pressure           4500

Starters, Chapter 80

Relay, Starter                       4500

Starter                              1700

Water Injection, Chapter 82

Indicator, Water Pressure            4200

Indicator, Water Quantity            4200

Pump, Water Injection       (ADI)    4200

Solenoid                    (4 E/C)

Transmitter, Water Quantity          4200

Valve, Oil Pressure                  4200

NOTE:  Components or subcomponents of power plants that have

overhaul time limitations in multiples of the basic engine

overhaul time limitation shall receive an appropriate

inspection, check or test at the basic engine overhaul

period.

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 7.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- WRIGHT AERO - R1820 SERIES

PRATT & WHITNEY R-1830 SERIES

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          PAGE 1 of 2 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

R-1820 and R-1830 SERIES

Overhaul      Inspection &

Period       Check Period

Propellers, Chapter 61

Motor, Propeller Feathering          2600

Propeller Assembly                   2600

Propeller Governors                  EO

Pump Propeller Feathering            2600

Power Plant - General, Chapter 71

Actuator, Cowl Flap                  EO

Cowling                              EO

Mount, Engine                        EO

Engine, Chapter 72

Engine, Basic                        1300

Engine Fuel & Control, Chapter 73

Carburetor Assembly                  (2 EO)

Indicators, Fuel Pressure            3600

Pump, Engine Driven                  EO

Transmitter, Fuel Pressure           3600

Warning Unit, Fuel Pressure          3600

Ignition, Chapter 74

Ignition Harness                     EO

Spark Plugs                          OC

Vibrator                             EO

Engine Indicating, Chapter 77

Indicators, Carburetor Air

Temperature                       4800

Indicators, Cylinder Head

Temperature                       4800

Indicators, Manifold Pressure        4800

Tachometer, Generator                2600

Indicator, Tachometer Generator      4800

Exhaust, Chapter 78

Exhaust Manifold Assembly            EO

Oil, Chapter 79

Indicator, Oil Pressure              4800

Indicator, Oil Quantity              4800

Indicator, Oil Temperature           4800

Regulator, Oil Cooler                EO

Valve, Emergency Shutoff             3600

Effective date _____________________

PAGE 2 of 2 PAGES

OPERATIONS SPECIFICATIONS

R-1820 and R-1830 SERIES ENGINE

Overhaul      Inspection &

Period       Check Period

Starters, Chapter 80

Relay, Starter                       3600

Starter                              EO

NOTE:  Components or subcomponents of power plants that have

overhaul time limitations in multiples of the basic engine

overhaul time limitations shall receive an appropriate

inspection, check or test at the basic engine overhaul

period.

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 9.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- WRIGHT AERO - C18 SERIES

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          PAGE 1 of 2 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

C18 SERIES

Overhaul      Inspection &

Period       Check Period

Propellers, Chapter 61

Motor, Propeller Feathering         2800

Propeller Assembly           43E60  2500

Propeller Assembly     C634-S/C400  2500

Propeller Governors                 1400

Pump, Propeller Feathering          2800

Power Plant - General, Chapter 71

Actuator, Cowl Flap                 2800

Cowling                             1400

Mount, Engine                       1400

Engine, Chapter 72

Engine, Basic                       1400

Engine Fuel & Control, Chapter 73

Indicator, Fuel Flow                4200

Indicator, Fuel Pressure            4200

Master Control Unit                 2800

Pump, Engine Driven                 1400

Pump, Fuel Injection                1400

Transmitter, Fuel Flow              4200

Transmitter, Fuel Pressure          4200

Warning, Fuel Pressure              4200

Ignition, Chapter 74

Ignition Harness                    4200

Spark Plugs                          330

Engine Indicating, Chapter 77

Indicator, BMEP                     4200

Indicator, Carburetor Air

Temperature                      4200

Indicator, Cylinder Head

Temperature                      4200

Indicator, Manifold Pressure        4200

Indicator, Tachometer               4200

Tachometer, Generator               2800

Exhaust, Chapter 78

Exhaust Manifold Assembly           1400

Effective date   December 15, 1962

PAGE 2 of 2 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

C18 SERIES

Overhaul      Inspection &

Period       Check Period

Oil, Chapter 79

Indicator, Oil Pressure             4200

Indicator, Oil Quantity             4200

Indicator, Oil Temperature          4200

Oil Tank                    (3 E/C)

Regulator, Oil Cooler               1400

Transmitter, Oil Pressure           4200

Transmitter, Oil Quantity           4200

Transmitter, Torque Pressure        4200

Valve, Emergency Shutoff            4200

Warning Unit, Oil Pressure          4200

Starter, Chapter 80

Relay, Starter                      4200

Starter                             1400

NOTE:  Components or subcomponents of power plants that have

overhaul time limitations in multiples of the basic engine

overhaul time limitation shall receive an appropriate

inspection, check or test at the basic overhaul period.

Effective date   December 15, 1962

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 10.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- WRIGHT AERO - TC18 SERIES

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          PAGE 1 of 2 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

TC-18 SERIES

Overhaul      Inspection &

Period       Check Period

Propellers, Chapter 61

Motor, Propeller Feathering         2400

Propeller Assembly           34E60  2500

Propeller Assembly           34H60  2000

Propeller Governors                 1200

Pump, Propeller Feathering          2400

Power Plant - General, Chapter 71

Actuator, Cowl Flap                 2400

Cowling                             1200

Mount, Engine                       1200

Engine, Chapter 72

Engine, Basic                       1200

Engine Fuel & Control, Chapter 73

Indicators, Fuel Flow               4800

Indicators, Fuel Pressure           4800

Master Control Unit                 2400

Pump, Engine Driven                 1200

Pump, Fuel Injection                1200

Transmitter, Fuel Flow              4800

Transmitter, Fuel Pressure          4800

Warning Unit, Fuel Pressure         4800

Ignition, Chapter 74

Ignition Harness                    1200

Spark Plugs                          330

Engine Indicating, Chapter 77

Indicators, BMEP                    4800

Indicators, Cylinder Head           4800

Indicators, Manifold Pressure       4800

Indicators, Tachometers             4800

Tachometer, Generator               2400

Exhaust, Chapter 78

Exhaust Manifold Assembly           1200

Effective date   December 15, 1962

PAGE 2 of 2 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

TC-18 SERIES

Overhaul      Inspection &

Period       Check Period

Oil, Chapter 79

Indicator, Oil Pressure             4800

Indicator, Oil Quantity             4800

Indicator, Oil Temperature          4800

Oil Tank                    (3 E/C)

Regulator, Oil Cooler               1200

Transmitter, Oil Pressure           4800

Transmitter, Oil Quantity           4800

Transmitter, Torque Pressure        4800

Valve, Emergency Shutoff            3600

Warning Unit, Oil Pressure          4800

Starter, Chapter 80

Relay, Starter                      3600

Starter                             1200

Turbine, Chapter 81

Cooling Cap, Flight Hood            1200

Power Recovery Turbine              1200

NOTE:  Components or subcomponents of power plants that have

overhaul time limitations in multiples of the basic engine

overhaul time limitation shall receive an appropriate

inspection, check or test at the basic engine overhaul

period.

Effective date   December 15, 1962

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 11.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- CONVAIR - CV-240/340/440

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          PAGE 1 of 3 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

CONVAIR CV-240/340/440

Overhaul      Inspection &

Period       Check Period

Air Conditioning, Chapter 21         12,000

Actuators & Valves                    6,000

Expansion Turbine                     4,000

Indicator, Cabin Altitude             6,000

Indicator, Cabin Rate of Change       6,000

Regulators, Pressure                  4,000

Selector, Cabin Altitude              6,000

Selector, Cabin Rate of Change        6,000

Turbo-Compressor                      2,000

Valve-Auto Emergency                  4,000

Auto Pilot, Chapter 22               12,000

Electrical, Chapter 24               12,000

Ammeter & Voltmeter                   6,000

Control Panel, Generator              2,000

Generator                            Engine Change

Inverter, Emergency                   5,000

Inverter, Main                        2,000

Relay, Battery                        6,000

Equipment & Furnishings, Chapter 25  12,000

Chute, Evacuation                      OC

First-Aid Kit                        6 months

Bottle-Slide Inflation               3 years     *

Fire Protection, Chapter 26          12,000

Cylinders                            *

Panel, Fire Detector                  6,000

Selector & Tank (CV-340,440)          8,000

* Inspections, hydrostatic test, and life limits will be

accomplished as set forth in Part 173, Chapter 1, Subtitle B of

CFR 49 currently in effect.

Flight Controls, Chapter 27          12,000

Indicator, Wing Flap Position         6,000

Motor, Wing Flap Actuating            6,000

Transmitter, Wing Flap Position       6,000

Valve, Wing Flap Selector             5,000

Fuel, Chapter 28                     12,000

Indicator, Fuel Quantity              5,000

Pump, Fuel Boost                      5,000

Transmitter, Fuel Quantity            5,000

Valve & Motor Cross-Feed              8,000

Valve & Motor Fuel Supply Shutoff     4,000

Valve, Vapor Vent Check               4,000

Effective date _____________________

PAGE 2 of 3 PAGES

OPERATIONS SPECIFICATIONS

@                     AIRCRAFT MAINTENANCE

CONVAIR CV-240/340/440

Overhaul      Inspection &

Period       Check Period

Hydraulic, Chapter 29                12,000

Accumulator                           8,000

Indicator, Hydraulic Pressure         6,000

Pump, Auxiliary Hydraulic             6,000

Regulator, Pressure                   6,000

Transmitter, Hydraulic Pressure       6,000

Valve, Unloading                      6,000

Ice & Rain, Chapter 30               12,000

Indicator, Augmentor Vane             6,000

Relay, Propeller Deice                6,000

Timer, Propeller Deicer               6,000

Transmitter, Anti-ice Temperature     6,000

Transmitter, Augmentor Vane           6,000

Valve, Heat Source                    4,000

Valve, Tail anti-ice                  8,000

Instruments, Chapter 31              12,000

Clock                                  OC

Landing Gears, Chapter 32            12,000

Bottle, Emergency Air                  *

Cylinders, Main and Nose Actuating    4,000

Indicator, Brake Hydraulic Pressure   6,000

Transmitter, Brake Hydraulic Pressure 6,000

Valve, Power Brake                    8,000

Wheels, Tires & Brakes                 OC

* Inspections, hydrostatic test, and life limits will be

accomplished as set forth in Part 173, Chapter 1, Subtitle B of

CFR 49 currently in effect.

Lights, Chapter 33                   12,000

Flasher                               4,000

Navigation, Chapter 34               12,000

Altimeter                             3,000 **

Compass, Magnetic                     6,000

Indicator, Air Speed                  4,000

Indicator, Gyro Horizon               3,000

Indicator, Outside Air Temperature    6,000

Indicator, Rate of Climb              5,000

Indicator, Turn & Bank                3,000

** Calibrate every 24 months

Effective date _____________________

PAGE 3 of 3 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

CONVAIR CV-240/340/440

Overhaul      Inspection &

Period       Check Period

Oxygen, Chapter 35                   12,000

Bottle, Oxygen                         *

Fuselage, Chapter 53                 12,000

Nacelles, Chapter 54                 12,000

Stabilizer, Chapter 55               12,000

Wings, Chapter 57                    12,000

Propellers, Chapter 61

Box, Propeller Reverse Relay          4,000

Relay, Propeller Feather              6,000

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 12.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- CURTISS WRIGHT C-46 SERIES

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          PAGE 1 of 2 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

CURTISS C-46

Overhaul      Inspection &

Period       Check Period

Air Conditioning, Chapter 21         10,000

Heaters & Blower                      2,500

Auto-Pilot, Chapter 22               10,000

Bank & Climb                          1,500

Control, Directional Gyro             1,500

Servo                                 6,000

Valve, Balance Oil                    6,000

Electrical, Chapter 24               10,000

Ammeter & Voltmeter                   6,000

Generator                              EC

Inverter, Emergency                   5,000

Inverter, Main                        2,000

Regulator, Voltage                    2,000

Relay, Reverse Current                2,000

Equipment & Furnishings, Chapter 25  10,000

First-Aid Kit                        6 months

Transmitter, Emergency               6 months

Fire Protection, Chapter 26          10,000

Cylinders, CO2                       *

Cylinder (wt. check)                 6 months

* Inspections, hydrostatic test, and life limits will be

accomplished as set forth in Part 173, Chapter 1, Subtitle B of

CFR 49 currently in effect

Flight Controls, Chapter 27          10,000

Cylinder, Flap Actuating              6,000

Indicator, Wing Flap Position         6,000

Transmitter, Wing Flap Position       6,000

Fuel, Chapter 28                     10,000

Indicator, Fuel Quantity              6,000

Pump, Fuel Boost                      4,500

Transmitter, Fuel Quantity            6,000

Hydraulic, Chapter 29                10,000

Accumulator                           8,000

Filter, Main                          5,000 Note 1

Indicator, Hydraulic Quantity         6,000

Pump, Auxiliary Hydraulic             6,000

Transmitter, Hydraulic Quantity       6,000

Note 1 - Sample filters at 2000 and 4000 to substantiate the 5000

hours.

Effective date _____________________

PAGE 2 of 2 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

CURTISS C-46

Overhaul      Inspection &

Period       Check Period

Ice & Rain, Chapter 30               10,000

Indicator, Deice Pressure             6,000

Motor, Wing Deice                    1 year

Pump, Alcohol Anti-ice               1 year

Instruments, Chapter 31              10,000

Clock                                 OC

Landing Gear, Chapter 32             10,000

Bottle, Emergency Air                  *

Wheels, Tires & Brakes                OC

Lights, Chapter 33                   10,000

Flasher                               4,000

Navigation, Chapter 34

Altimeter                             3,000 (calibrate every 24

Compass, Magnetic                     6,000  months)

Indicator, Air Speed                  4,000

Indicator, Gyro Horizon               3,000

Indicator, Outside Air Temperature    6,000

Indicator, Turn & Bank                6,000

Indicator, Rate of Climb              4,000

Oxygen, Chapter 35                   10,000

Bottle Oxygen                          *

Indicator, Oxygen Pressure            6,000

* Inspections, hydrostatic test, and life limits will be

accomplished as set forth in Part 173, Chapter 1, Subtitle B of

CFR 49 currently in effect.

Vacuum, Chapter 36                   10000

Indicator, Vacuum Pressure            6000

Valve, Relief                         6000

Fuselage, Chapter 53                 10000

Nacelles, Chapter 54                 10000

Stabilizers, Chapter 55              10000

Wings, Chapter 57                    10000

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 13.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- DOUGLAS - DC-3 SERIES

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          PAGE 1 of 2 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-3 SERIES

Overhaul      Inspection &

Period       Check Period

Air Conditioning, Chapter 21         12,000

Heater                                2,500

Auto-Pilot, Chapter 22               12,000

Bank & Climb                          1,500

Control, Directional Gyro             1,500

Servo                                 6,000

Valve, Balance Oil                    6,000

Electrical, Chapter 24               12,000

Ammeter & Voltmeter                   6,000

Generator                              EC

Inverter, Emergency                   5,000

Inverter, Main                        2,000

Regulator, Voltage                    2,000

Relay, Reverse Current                2,000

Equipment & Furnishings, Chapter 25  12,000

First-Aid Kit                        6 months

Transmitter, Emergency               6 months

Life Vests and Rafts                 1 year

Fire Protection, Chapter 26          12,000

Cylinders, CO2                         *

Panel, Fire Detector                  6,000

Bottle Weight Check                  6 months

* Inspections, hydrostatic test, and life limits will be

accomplished as set forth in Part 173, Chapter 1, Subtitle B of

CFR 49 currently in effect.

Flight Controls, Chapter 27          12,000

Cylinder, Flap Actuating              6,000

Fuel, Chapter 28                     12,000

Indicator, Fuel Quantity              6,000

Pump, Fuel Boost                      4,500

Transmitter, Fuel Quantity            6,000

Hydraulic, Chapter 29                12,000

Accumulator                           8,000

Indicator Hydraulic Pressure          6,000

Pump, Engine Driven                    EC

Effective date _____________________

PAGE 2 of 2 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-3 SERIES

Overhaul      Inspection &

Period       Check Period

Ice & Rain, Chapter 30               12,000

Indicator, Deice Pressure             6,000

Motor, Wing Deice                    1 year

Pump, Alcohol Anti-ice               1 year

Instruments, Chapter 31              12,000

Clock                                OC

Landing Gear, Chapter 32             12,000

Bottle, Emergency Air                  *

Indicator, Landing Gear Pressure      6,000

Wheels, Tires & Brakes               OC

Lights, Chapter 33                   12,000

Flasher                               4,000

Navigation, Chapter 34               12,000

Altimeter                             3,000**

Indicator, Air Speed                  4,000

Compass, Magnetic                     6,000

Indicator, Gyro Horizon               3,000

Indicator, Outside Air Temperature    6,000

Indicator, Rate of Climb              4,000

Indicator, Turn & Bank                3,000

** Calibrate every 24 months per FAR

Oxygen, Chapter 35                   12,000

Bottle, Oxygen                         *

Indicator, Oxygen Pressure            6,000

* Inspections, hydrostatic test, and life limits will be

accomplished as set forth in Part 173, Chapter 1, Subtitle B of

CFR 49 currently in effect.

Vacuum, Chapter 37                   12,000

Indicator, Vacuum                     6,000

Valve, Relief                         6,000

Pump, Engine Driven                  EC

Fuselage, Chapter 53                 12,000

Nacelles, Chapter 54                 12,000

Stabilizers, Chapter 55              12,000

Wings, Chapter 57                    12,000

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 14.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- DOUGLAS - DC-4 SERIES

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          PAGE 1 of 2 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-4

Overhaul      Inspection &

Period       Check Period

Air Conditioning, Chapter 21         12,000

Blower, Nose Heater                   6,000

Heater, Cabin                         2,500

Heater, Nose                          2,500

Auto-Pilot, Chapter 22               12,000

Electrical, Chapter 24               12,000

Ammeter & Voltmeter                   6,000

Generator                            EC

Inverter, Emergency                   5,000

Inverter, Main                        2,000

Regulator, Voltage                    2,000

Relay, Battery                        6,000

Equipment & Furnishings, Chapter 25  12,000

Chute, Evacuation                    1 year

First-Aid Kit                        6 months

Life Vest & Raft                     1 year

Transmitter, Emergency               6 months

Fire Protection, Chapter 26          12,000

Cylinders                              *

Panel, Fire Detector                  6,000

Cylinder Weight Check                 6 months

* Inspections, hydrostatic test, and life limits will be

accomplished as set forth in Part 173, Chapter 1, Subtitle B of

CFR 49 currently in effect.

Flight Controls, Chapter 27           12,000

Indicator, Flap Position               6,000

Transmitter, Flap Position             6,000

Fuel, Chapter 28                      12,000

Indicator, Fuel Quantity               5,000

Pump, Fuel Boost                       4,500

Transmitter, Fuel Quantity             4,000

Hydraulic, Chapter 29                 12,000

Accumulator                            8,000

Indicator, Hydraulic Pressure          6,000

Pump, Auxiliary Hydraulic              6,000

Regulator, Pressure                    6,000

Transmitter, Hydraulic Pressure        6,000

Firewall shutoff                       5,000

Effective date _____________________

PAGE 2 of 2 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-4

Overhaul      Inspection &

Period       Check Period

Ice & Rain, Chapter 30               12,000

Indicator, Anti-ice Quantity          6,000

Indicator, Deice Pressure             6,000

Pump, Alcohol                         8,000

Solenoids, Anti-ice                   6,000

Transmitter, Anti-ice Quantity        6,000

Instruments, Chapter 31              12,000

Clock                                OC

Landing Gear, Chapter 32             12,000

Bottle, Emergency Air                  *

Wheels, Tires & Brakes               OC

Lights, Chapter 33                   12,000

Flasher                               4,000

Rotating Beacon                      OC

Navigation, Chapter 34               12,000

Altimeter                             3,000 **

Compass, Magnetic                     6,000

Indicator, Air Speed                  4,000

Indicator, Gyro Horizon               3,000

Indicator, Outside Air Temperature    6,000

Indicator, Rate of Climb              4,000

Indicator, Turn & Bank                3,000

** Calibrate every 24 months

Oxygen, Chapter 35                   12,000

Bottle, Oxygen                         *

* Inspections, hydrostatic test, and life limits will be

accomplished as set forth in Part 173, Chapter 1, Subtitle B of

CFR 49 currently in effect.

Fuselage, Chapter 53                 12,000

Nacelles, Chapter 54                 12,000

Stabilizers, Chapter 55              12,000

Wings, Chapter 57                    12,000

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 15.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- DOUGLAS - DC-6, DC-7

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          PAGE 1 of 3 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-6, DC-7

Overhaul      Inspection &

Period       Check Period

Air Conditioning, Chapter 21         12,000

Accessory Containers                  4,000

Expansion Turbine                     4,000

Actuators & Valves                    6,000

Heater Unit                           2,500

Turbo-Compressor                      2,000

Unit, Ignition                        2,500

Auto-Pilot, Chapter 22               12,000

Amplifier (A-12)                      4,000

Engaging Control                      8,000

Gyro-Compass Control                  4,000

Gyro-Compass, Repeater                4,000

Pedestal Controller                   6,000

Servo, Controller                     2,500

Servo, Unit                           6,000

Vertical Gyro Control                 4,000

Electrical, Chapter 24               12,000

Ammeter & Voltmeter                   6,000

Generator                              EC

Inverter, Emergency                   5,000

Inverter, Main                        2,000

Regulator, Voltage                    2,000

Relay, Battery                        6,000

Equipment & Furnishings, Chapter 25  12,000

Chute, Evacuation                    1 year

First-Aid Kit                        6 months

Life Vest & Raft                     1 year

Transmitter, Emergency               6 months

Fire Protection, Chapter 26          12,000

Cylinders                              *

Panel, Fire Detector                  6,000

Cylinders, Weight Check              6 months

* Inspections, hydrostatic test, and life limits will be

accomplished as set forth in Part 173, Chapter 1, Subtitle B of

CFR 49 currently in effect.

Effective date _____________________

PAGE 2 of 3 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-6, DC-7

Overhaul      Inspection &

Period       Check Period

Flight Controls, Chapter 27          12,000

Indicator, Wing Flap Position         6,000

Transmitter, Wing Flap Position       6,000

Fuel, Chapter 28                     12,000

Indicator, Fuel Quantity              4,500

Pump, Fuel Boost                      4,500

Transmitter, Fuel Quantity            4,000

Hydraulic, Chapter 29                12,000

Accumulator                           8,000

Indicator, Hydraulic Pressure         6,000

Pump, Auxiliary Hydraulic             6,000

Regulator, Pressure                   6,000

Transmitter, Hydraulic Pressure       6,000

Ice & Rain Protection, Chapter 30    12,000

Accessory, Containers                 4,000

Blowers, Wing & Empennage Heater      8,000

Heater, Wing & Empennage              8,000

Unit, Ignition                        2,500

Instruments, Chapter 31              12,000

Clock                                  OC

Landing Gear, Chapter 32             12,000

Bottle, Emergency Air                  *

Wheels, Tires & Brakes                 OC

* Inspections, hydraulic test, and life limits will be

accomplished as set forth in Part 173, Chapter 1, Subtitle B of

CFR 49 currently in effect.

Lights, Chapter 33                   12,000

Flasher                               4,000

Navigation, Chapter 34               12,000

Altimeter                             3,000 **

Compass, Magnetic                     6,000

Indicator, Air Speed                  4,000

Indicator, Gyro Horizon               3,000

Indicator, Outside Air Temperature    6,000

Indicator, Rate of Climb              4,000

Indicator, Turn & Bank                3,000

** Calibrate every 24 months

Effective date _____________________

PAGE 3 of 3 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-6, DC-7

Overhaul      Inspection &

Period       Check Period

Oxygen, Chapter 35                   12,000

Cylinder                               *

* Inspections, hydrostatic test, and life limits will be

accomplished as set forth in Part 173, Chapter 1, Subtitle B of

CFR 49 currently in effect.

Fuselage, Chapter 53                 12000

Nacelles, Chapter 54                 12000

Stabilizers, Chapter 55              12000

Wings, Chapter 57                    12000

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 16.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- LOCKHEED - L-049/749/1049/1649

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          PAGE 1 of 3 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED L-049/749/1049/1649

Overhaul      Inspection &

Period        Check Period

Air Conditioning, Chapter 21        12,000

Actuators & Valves                   6,000

Blower, Flight Station               2,000

Expansion Turbine                    4,000

Fan, Heat Exchanger Cooling          4,000

Heat Cycling & Overheat Assembly     9,000

Heater Unit                          2,500

Ignition Unit                        2,500

Indicator, Cabin Altitude            6,000

Indicator, Cabin Rate of Change      6,000

Pump, Cabin Supercharger Reactor     2,000

Pump, Heater Fuel                    6,000

Selector, Cabin Altitude             6,000

Selector, Cabin Rate of Change       6,000

Separator, Water                     6,000

Turbo-Compressor                     2,000

Auto-Pilot, Chapter 22              12,000

Electrical, Chapter 24              12,000

Ammeter & Voltmeter                  6,000

Generator                             EC

Inverter, Emergency                  5,000

Inverter, Main                       2,000

Regulator, Voltage                   2,000

Relay, Battery                       6,000

Equipment & Furnishings, Chapter 25 12,000

Evacuation Chute                      OC

First-Aid Kit                       6 months

Life Vests & Raft                   6 months

Transmitter, Emergency              4 months

Fire Protection, Chapter 26         12,000

Cylinders                             *

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Flight Controls, Chapter 27         12,000

Indicator, Wing Flap Position        6,000

Transmitter, Wing Flap Position      6,000

Effective date _____________________

PAGE 2 of 3 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED L-049/749/1049/1649

Overhaul      Inspection &

Period        Check Period

Fuel, Chapter 28                    12,000

Indicator, Fuel Quantity             4,000

Pump, Fuel Boost                     4,000

Transmitter, Fuel Quantity           4,000

Hydraulic, Chapter 29               12,000

Accumulator                          8,000

Dampener                             8,000

Indicator, Hydraulic Pressure        6,000

Pump, Auxiliary Hydraulic            6,000

Regulator, Pressure                  6,000

Ice & Rain, Chapter 30              12,000

Box, Windshield Anti-ice Control     4,000

Motor, Cowl Flap                     4,000

Pump, Anti-ice                       8,000

Pump, Deicer                         4,000

Windshield Wiper Assembly            4,000

Instruments, Chapter 31             12,000

Clock                                 OC

Landing Gear, Chapter 32            12,000

Bottle, Emergency Air                 *

Wheels, Tires & Brakes                OC

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Lights, Chapter 33                  12,000

Flasher                              4,000

Navigation, Chapter 34              12,000

Altimeter                            3,000 **

Compass, Magnetic                    6,000

Indicator, Air Speed                 4,000

Indicator, Gyro Horizon              3,000

Indicator, Outside Air Temperature   6,000

Indicator, Rate of Climb             4,000

Indicator, Turn & Bank               3,000

** Bench check every 12 months.

Effective date _____________________

PAGE 3 of 3 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED L-049/749/1049/1649

Overhaul      Inspection &

Period        Check Period

Oxygen, Chapter 35                  12,000

Bottle, Oxygen                        *

Regulator, Oxygen Flow               8,000

Fuselage, Chapter 53                12,000

Nacelles, Chapter 54                12,000

Stabilizers, Chapter 55             12,000

Wings, Chapter 57                   12,000

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 17.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- MARTIN M-202/404

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          PAGE 1 of 3 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

MARTIN M-202/404

Overhaul      Inspection &

Period        Check Period

Air Conditioning, Chapter 21        12,000

Actuators & Valves                   6,000

Blower, Cabin                        2,000

Blower, Combustion Air               3,000

Box, Cabin Temperature Control       4,000

Control, Fuel Assembly               4,000

Heater Unit                          2,500

Ignition Units                       2,500

Solenoid Valves & Filters            4,000

Switches, Ram Air                    6,000

Turbo Compressor                     2,000

Auto-Pilot, Chapter 22              12,000

Electrical, Chapter 24              12,000

Ammeter & Voltmeter                  6,000

Contactor, Generator                 2,000

Control Panel, Generator             2,000

Generator                             EC

Inverter, Emergency                  5,000

Inverter, Main                       2,000

Regulator, Voltage                   2,000

Relay, Battery                       6,000

Equipment & Furnishings, Chapter 25 12,000

Chute, Evacuation                     OC

First-Aid Kit                       6 months

Fire Protection, Chapter 26         12,000

Cylinders                             *

Panel, Fire Detector                 6,000

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Flight Controls, Chapter 27         12,000

Actuator, Stabilizer Jack            8,000

Indicator, Wing Flap Position        6,000

Transmitter, Wing Flap Position      6,000

Fuel, Chapter 28                    12,000

Indicator, Fuel Quantity             4,000

Pump, Fuel Boost                     4,000

Transmitter, Fuel Quantity           4,000

Effective date _____________________

PAGE 2 of 3 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

MARTIN M-202/404

Overhaul      Inspection &

Period        Check Period

Hydraulic, Chapter 29               12,000

Accumulator                          8,000

Indicator, Hydraulic Pressure        6,000

Pump, Auxiliary Hydraulic            6,000

Regulator, Pressure                  6,000

Transmitter, Hydraulic Pressure      6,000

Ice & Rain, Chapter 30              12,000

Heater, Wing & Empennage             3,000

Unit, Windshield Wiper               8,000

Units, Ignition                      3,000

Instruments, Chapter 31             12,000

Clock                                 OC

Landing Gear, Chapter 32            12,000

Bottle, Emergency Air                 *

Motor, Nose Dampener                 4,000

Wheels, Tires & Brakes                OC

Lights, Chapter 33                  12,000

Flasher                              4,000

Navigation, Chapter 34              12,000

Altimeter                            3,000 **

Compass, Magnetic                    6,000

Gyro, Directional                    1,500

Indicator, Air Speed                 4,000

Indicator, Gyro Horizon              3,000

Indicator, Outside Air Temperature   6,000

Indicator, Rate of Climb             4,000

Indicator, Turn & Bank               3,000

** Bench Check every 12 months.

Oxygen, Chapter 35                  12,000

Bottle, Oxygen                        *

Regulator, Pressure                  8,000

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date _____________________

PAGE 3 of 3 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

MARTIN M-202/404

Overhaul      Inspection &

Period       Check Period

Fuselage, Chapter 53                 12000

Nacelles, Chapter 54                 12000

Stabilizers, Chapter 55              12000

Wings, Chapter 57                    12000

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 18.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- VISCOUNT - 745D/810

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          Page 1 of 3 pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

VISCOUNT 745D/810

Overhaul      Inspection &

Period       Check Period

Air-Conditioning System, Chapter 21 12000

Actuator, Cabin Hot Air Supply       3500

Actuator, Cabin Temperature Control  3500

Actuator, Intercooler Flap           3500

Actuator, Spill Valve Actuator       2500

Actuator, Unpressurized Flight Valve 3500

Altimeter, Cabin                     6000

Blower, Cabin Vent                   2500

Blower, Centrifugal Combustor        1500

Compressor, Cabin Air                2000

Controller, Cabin Pressure           4000

Controller, Mass Flow                4000

Heater Assembly                      2500

Ignition Assembly                    2500

Indicator, Cabin Differential

Pressure                          4000

Pump, Heater Fuel                    2500

Switch, Cycling                      2500

Switch, Thermal                      2500

Turbine, Cabin Air Cooling           4000

Valve, Cabin Outflow                 4000

Valve, Duct Relief                   6000

Valve, Safety                        6000

Auto-Pilot, Chapter 22              12000

Amplifier, Flux-Gate                 4000

Amplifier & Signal Generator         3500

Computer, Flight Path                1500

Controller, Pedestal                 6000

Indicator, Master Direction          4000

Indicator, Three Axis Trim           4000

Switch, Gaging                        o/c

Servo, Main                          3500

Transmitter, Flux-Gate               4000

Vertical Dynamic Sensor               o/c

Electrical System, Chapter 24       12000

Circuit Breaker, Differential

Overload                          3500

Generator                             o/c

Inverter, Emergency                  5000

Inverter, Main                       2000

Regulator, Voltage                   2000

Switch, Inverter Warning Failure     4000

Effective date   December 15, 1962

PAGE 2 of 3 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

VISCOUNT 745D/810

Overhaul      Inspection &

Period        Check Period

Equipment & Furnishings, Chapter 25 12,000

Evacuation Chute                      OC

Fire Protection, Chapter 26         12,000

Cylinders                             *

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Flight Controls, Chapter 27         12,000

Actuator, Aileron Trim Tab           4,500

Drum Assembly - Microswitch Control  7,000

Flap Brake Assembly                  4,500

Flap Clutch & Disconnect Assembly    4,500

Flap Gear Box                        7,000

Flap Gear Box Drive Motor            2,500

Indicator, Aileron Trim Position     4,000

Transmitter, Aileron Trim Tab

Position                          4,000

Indicator, Flap Position             6,000

Transmitter, Flap Position           6,000

Fuel System, Chapter 28             12,000

Actuator, Low Pressure Fuel          2,500

Actuator, Plessey Interengine        2,500

Amplifier, Fuel Quantity             2,500

Indicator, Fuel Datum Trim           6,000

Indicator, Fuel Quantity             4,000

Pump, Fuel Boost                     4,000

Hydraulic System, Chapter 29        12,000

Actuator, Foot Brake                 6,000

Motor, Undercarriage Control Valve   2,500

Unit, Maxaret                        3,500

Ice & Rain Protection, Chapter 30   12,000

Actuator, Jet Pipe Flap              2,500

Actuator, Thermal Deice Bypass Valve 2,500

Alternator, Prop Deice               2,500

Indicator, Jet Pipe Temperature      6,000

Inverter, Windshield Deice           2,000

Instruments, Chapter 31             12,000

Clock                                 OC

Effective date _____________________

PAGE 3 of 3 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

VISCOUNT 745D/810

Overhaul      Inspection &

Period        Check Period

Landing Gear, Chapter 32            12,000

Emergency Air Bottle                  *

Indicator, Brake Pressure            6,000

Switches, Gear                       4,000

Switches, Oleo                       4,000

Wheels, Tires & Brakes                OC

Lights, Chapter 33                  12,000

Flasher                              4,000

Lights, Landing                      2,500

Navigation Instruments, Chapter 34  12,000

Altimeter                            3,000 **

Compass, Magnetic                    6,000

Horizon, Gyro                        3,000

Indicator, Air Speed                 4,000

Indicator, Outside Air Temperature   6,000

Indicator, Rate of Climb             4,000

Indicator, Turn & Bank               3,000

** Bench Check every 12 months.

Oxygen System, Chapter 35           12,000

Oxygen Bottle                         *

Fuselage, Chapter 53                12,000

Nacelles, Chapter 54                12,000

Stabilizers, Chapter 55             12,000

Wings, Chapter 57                   12,000

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 19.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- LOCKHEED L-188 A & C

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

OPERATIONS SPECIFICATIONS

PART D                                          Page 1 of 5 pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED L-188 A & C

Overhaul      Inspection &

Period        Check Period

Air Conditioning System, Chapter 21 12,000

Air Cycle By-Pass Valve              4,000

Air Cycle Cooling Air Exit Door

Actuator                          4,000

Air Cycle Heat Exchange             O.C.

Air Cycle Cooling Turbine            4,000

Altimeter, Cabin                     7,000

Cabin Air Compressor                 2,000

Cabin Air Flow Control Valve         2,000

Cabin Pressure Reg. Outflow Valve    5,000         BC 2500

Cabin Pressure Safety Valve         12,000         BC 4000

Cabin Air Duct Shut-Off Valve       O.C.

Cabin Air Duct Check Valve          O.C.

Cabin Air Pressure Outflow Valve

Control                           3,500

Cabin Air Pressure Outflow Valve

Control Filter                    1,500

Cabin Freon Evaporator              O.C.

Cabin Aux. Vent Inlet Valve &

System                           O.C.

Cabin Air Warmup Valve Actuator     O.C.

Cabin Air Filter                    O.C.

Cabin Duct Heater                   O.C.

Cabin Recirculating Fan              4,000

Cooling Air Exit Door Actuator

(tunnel)                          4,000

Cooling Air Inlet Door Actuator

(tunnel)                          4,000

Flight Station Recirculating Fan     4,000

Flight Station Freon Evaporator     O.C.

Flight Station Duct Heater          O.C.

Flight Station Aux. Vent Inlet

Valve                            O.C.

Flight Station Air Filter           O.C.

Freon Suction Pressure Throttling

Valve                             4,000

Freon Condenser Fan                  4,000

Freon Condenser                     O.C.

Freon Compressor                     3,000

Lavatory Exhaust Fan                O.C.

Manual Control Valve                 5,000

Negative Pressure Relief Valve      O.C.

Radio Rack Exhaust Fan               1,400

Rate of Climb                        7,000

Radiant Heating Panel (floor and

wall)                            O.C.

Radiant Heating Panel (cargo

compt.)                          O.C.

Surge Control Valve                  2,000

Temperature Control Box              2,500

Effective date   April 1, 1964

PAGE 2 of 5 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED L-188 A & C

Overhaul      Inspection &

Period        Check Period

Auto-Pilot System, Chapter 22

May be determined by the assigned

inspector.

Communications System, Chapter 23

May be determined by the assigned

inspector.

Electrical Power, Chapter 24          OC

Battery                               OC

Flight Station Electrical &

Instrument Panels                  OC

Generator, AC                        2,000

Generator Control and Protection

Components                        2,000

Inverter                             2,000

Main & Flight Station Distribution

Centers, including Wiring,

Terminals, Relays, Circuit

Breakers, Etc.                     OC

Power Contactors and Reverse

Current Relays                    2,000

Secondary Electrical Centers,

including Wiring, Terminals,

Relays, Circuit Breakers, Etc.     OC

Transformer Rectifiers               2,000

Voltage Regulators                   2,000

Equipment & Furnishings, Chapter 25

May be determined by the assigned

inspector.

Fire Protection, Chapter 26           OC

Cylinder                              *

Discharge Valve Cartridges          3 years

Transfer Valve                       8,000

Valve, Drain                         3,500

Flight Controls, Chapter 27           OC

Aileron Trim Tab Control Unit       12,000

Aileron Trim Tab Actuator Unit      12,000

Aileron Push-Pull Tubes, Bellcranks

Fittings, etc.                    8,000

Asymmetry Detector Shut-Off Valve    6,000

Asymmetry Detector Actuated Flap

Actuator Brake                   12,000

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date _____________________

Page 3 of 5 pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED L-188 A & C

Overhaul      Inspection &

Period        Check Period

Flight Controls, Chapter 27,

continued

Booster Actuators                    8,000

Booster Valve Cluster                8,000

Booster Frame Disconnect Mechanism   8,000

Control Column                      12,000

Control Cables, Pulleys, Fairleads,

etc.                             O.C.

Elevator Trim Tab Control Unit      12,000

Elevator Trim Tab Actuator Unit     12,000

Elevator Push-Pull and Torque Tube   8,000

Flap Control System                  5,000

Hydraulic Load Sensors               8,000

Rudder Pedals                       12,000

Rudder Trim Tab Control Unit        12,000

Rudder Trim Tab Actuator & Linkage  12,000

Rudder Push-Pull and Torque Tube

Installation                      8,000

Wing Flap Main Drive Hydraulic

Motor                            12,000

Wing Flap Main Drive Gear Box       12,000

Wing Flap Actuators, Linkages,

Tracks and Carriages          @   4,000

Fuel System, Chapter 28

Boost Pump, Main                     5,000

Boost Pump, Scavange                 5,000

Fuel Valves (Crossfeed-Elect.; Shut-

Off-Manual)                       8,000

Fuel Dump Valves                     8,000

Fueling Valve                        8,000

Fuel Quantity Tank Units            O.C.

Fuel Quantity Indicators             5,000

Fuel Pressure Warning System        O.C.

Misc. Valves, Pilot & Vent.         10,000

Overflow Valve                       8,000

Transmitter, Fuel Crossfeed          8,000

Hydraulic System, Chapter 29        O.C.

Aux. Pump (DC)                       4,000

Hydraulic Motor Pump (AC)            2,000

Heat Exchanger                      O.C.

Relief Valve, Main System           12,000

Reservoir                           12,000

Pressure Switches                   O.C.

Effective date   April 1, 1964

PAGE 4 of 5 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED L-188 A & C

Overhaul      Inspection &

Period        Check Period

Ice & Rain Protection, Chapter 30     OC

Airfoil Temperature Sensor Amplifier 4,000

Bleed Air Shut-Off Valve             3,000

Control Unit, Temperature            8,000

Fuselage Isolation Valve             8,000

Indicator, Airfoil Temperature       8,000

Indicator, Bleed Air Manifold        8,000

Leakage Detector Valve               3,000

Modulating Control Valves            8,000

Switch Temperature Selector          8,000

Transmitter, Bleed Air Manifold      8,000

Thermostats                           OC

Universals                            OC

Firewall Bleed Air Shut-Off Valve    3,500

Timer, Prop De-Ice                   5,000

Windshield De-Fog                    8,000

Windshield Wiper Accumulator        12,000

Windshield Wiper Control Unit        4,000

Window Units                        12,000

Landing Gear, Chapter 32

Brake Accumulators                  12,000

Brake System                        12,000

Gear Up-and-Down Locks              10,000

Lockout Cylinder                    12,000

Main and Nose Wheels                  OC

Main Gear                           12,000

Main Gear Door Actuating Cylinder   10,000

Nose Gear                           12,000

Nose Gear Door Actuating Cylinder   10,000

Nose Wheel Steering                 12,000

Valve, Shuttle                      12,000

Valve, Priority                     12,000

Lighting, Chapter 33

May be determined by assigned

inspector.

Navigation, Chapter 34

May be determined by assigned

inspector.

Oxygen System, Chapter 35

Oxygen Bottle                           *

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date _____________________

Page 5 of 5 pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED L-188 A & C

Overhaul      Inspection &

Period        Check Period

Doors, Chapter 52

Actuators                            4,000

Cylinder, Stair Actuating            4,000

Doors and Emergency Exits           12,000

Valve, Stair Selector                8,000

Fuselage, Chapter 53

Crew Seats and Attachments           8,000

Exterior Covering                   12,000

Floor Support Members               12,000

Interior                            O.C.

Nose Gear Well Area                 12,000

Passenger Seats and Attachments     12,000

Structure Around Windows            12,000

Nacelles, Chapter 54

Attachments                         12,000         4,000

Main Gear Support Structure         12,000

Skin and Structure Beneath

Tail Pipe Shroud                 12,000         4,000

Tail Pipe and Shroud                12,000         2,000

Stabilizers, Chapter 55

Attachments and Joints               6,000

Exterior Covering                    6,000

Elevator and Tabs                   12,000      *    500

Interior Structure                   6,000      ** 2,000

Rudder and Tabs                     12,000

Vertical, Horizontal and

Installation                      6,000

Windows, Chapter 56

Cabin                               12,000

Windshield Structure                12,000

Wings, Chapter 57

Ailerons and Tabs                   12,000

Attach Joints                       12,000

Center Wing Section                  8,000

Flaps, Structure                    12,000

Interior Structure                  12,000

Wing to Fuselage Fillets             8,000

* Counter weight

bracket

Effective date   April 1, 1964             ** Inspection Rear

Spar Web

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 20.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- ALLISON 501-D13 ENGINE AEROPRODUCTS PROPELLER

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ENGINE MAKE - ALLISON              PROPELLER MAKE - AEROPRODUCTS

ENGINE MODEL - 501-D13             PROPELLER MODEL - A6441FN606

Overhaul      Inspection &

Period       Check Period

Propellers, Chapter 61

Alternator                           2000

Regulator                            2000

Hub                                  2500

Blades                               2500

Reservoir                            2500

Spinner                              OC

Power Plant General, Chapter 71

Engine Mounting System               OC

Vibration Isolators                  OC

Engine Cowling                       OC

Engine Fire Seal                     OC

Engine, Chapter 72

Compressor/Gearbox                   4000

Turbine Section                      4000

Engine Fuel and Control, Chapter 73

Temperature Datum Control System     3000

Fuel Control                         3000

Engine Fuel Pump                     3000

Fuel Flow Meter                      3000

Ignition System, Chapter 74

Exciter and Relay                    EO

Ignitor                              EO

Engine Air, Chapter 75

Ducts and Scoops                     OC

Anti-ice System                      3000

Speed-sensitive Control              3000

Engine Controls, Chapter 76

Power Lever System and Engine

Coordinator Controls and Linkages OC

Effective date _____________________

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ENGINE MAKE - ALLISON

ENGINE MODEL - 501-D13

Overhaul      Inspection &

Period        Check Period

Engine Indicating, Chapter 77

Tachometer Generator                 3,000

Tachometer Indicator                 5,000

T. I. T. Indicator                   5,000

Torquemeter Indicator                5,000

Torquemeter Phase Detector           5,000

Indicator Oil Temperature            5,000

Indicator Oil Quantity                OC

Indicator Oil Pressure Gearbox       5,000

Indicator Oil Pressure Engine        5,000

Engine Exhaust System, Chapter 78

Engine Exhaust System                 OC

Engine Oil System, Chapter 79

Engine Oil System                     OC

Actuator Oil Cooler Flap             3,000

Oil Quantity Transmitter              OC

Oil Pressure Warning Switch           OC

Oil Pressure Transmitters            5,000

Oil Cooler Flap Position Indicator    OC

Fuel Oil Heat Exchanger              3,000

Oil Cooler                            EO

Starting, Chapter 80

Engine Starter                        EO

Bleed Air Shutoff Valves             5,000

Isolation and Firewell Valves        5,000

Combustor Assembly                   1,800

Air Storage Bottles                   *

Corrosion Inspection                1 year

Air Bottle Cooling Valve             5,000

Air Compressor                        OC

Low Pressure Regulator Valve         EO

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 21.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- BOEING 707/720

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                        Page 1 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 707/720

Overhaul      Inspection &

Period       Check Period

Air Conditioning, Chapter 21        O.C.

Ducting, Plumbing, Electrical

Conduits                         O.C.

Turbo Compressor                     3,000

Outflow Valves                       2,500

Cabin Pressure Controller            5,000

Differential Pressure Indicator      8,000

Vapor Cycle Pack                     5,000

Tachometer, Turbo Compressor         3,500

Actuator - Ram Air Damper            7,500

Controller, Cockpit Airflow          7,500

Valve - Pack Shutoff                 5,000

Valve - Cabin Temp. Control          7,500

Valve - Cockpit Temp. Control (Hot) 10,000

Valve - Cockpit Temp. Control

(Cold)                           10,000

Valve - Ram Air Shutoff             12,500

Valve - Wing Shutoff                12,500

Blower - Recirculating               3,500

Controller - Cabin Pressure Manual   5,000

Fan Assembly - Condenser             4,000

Heat Exchanger                      O.C.

Heaters - Electric                  O.C.

Indicator - Cabin Temperature       O.C.

Indicator - Cabin Rate of Climb     10,000

Pump - Jet                          O.C.

Relay - Compressor Discharge

Overheat                         10,000

Relay - Cabin Pressure Warning      10,000

Elements - Temperature Sensing      O.C.

Switch - Duct Overheat              O.C.

Switch - Pressure Altitude          O.C.

Valve - Blower Shutoff              10,000

Valve - Cabin Air Check             O.C.

Valve - Cockpit Air Check           O.C.

Valve - Turbo Compressor Check      O.C.

Electronic Equipment Blower          6,000

Valve - Cabin Pressure Bleed Air

Shutoff                          O.C.

Air Cycle Machine                    5,000

Condenser                           O.C.

Evaporator                          O.C.

Compressor                          10,000

Auto Pilot - Chapter 22             O.C.

Auto Pilot Adapter                  O.C.

Box - Power Junction                 5,000

Control Panel                       O.C.

Indicator - 3 Axis Trim (Eclipse

Pioneer)                          7,500

Sero - Stabilizer Trim               5,000

Effective date   July 1, 1964

PAGE 2 of 12 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 707/720

Overhaul      Inspection &

Period        Check Period

Auto Pilot, Chapter 22 (continued)

Annunciator - Glide Scope             OC

Three Axis Rate Transmitter          5,000

Air Data Sensor                      3,000

Amplifier and Computer               3,000

Servo - Aileron, Rudder, & Elevator  2,500

Unit - Comparison                    2,500

Communications, Chapter 23

May be determined by assigned

inspector.                         OC

Electrical Power, Chapter 24          OC

Constant Speed Drive Oil Temp.

Indicator                        10,000

Resistance Bulb c/o Drive Oil Temp.   OC

Wattmeters                          10,000

DC Voltmeters                       10,000

DC Ammeters                         10,000

Generator Control Unit                OC

Relay - Essential Power Failure      5,000

Relay - External Power               6,000

Relay External Power Control         5,000

Relay - External Power Interlock     7,500

Relay - Negative Sequence Aux #1     7,500

Relay - Negative Sequence Aux #2     7,500

Relay - Negative Sequence            6,000

Transformer Rectifier                 OC

A/C Generator                        3,000

Voltage Regulator                    5,000

Load Controller                      5,000

Reverse Current Relay                5,000

Battery                               OC

A/C Voltmeter and Ammeter           10,000

Frequency Meter                     10,000

C/S Drive & Disconnect               3,000

Equipment and Furnishings,

Chapter 25                         OC

May be determined by assigned

inspector.

Fire Protection, Chapter 26           OC

Control Unit - Wheel Well Area Fire

Detector                          5,000

Valve - Double Tee                  10,000

Bottle - Fire Extinguisher            *

Control - Fire Warning Bell           OC

Stop Valve & Solenoid                6,000

Portable CO2 Bottles                  *

Wheel Well Fire Detector Sensing

Elements                           OC

Engine Fire Detector Thermo Switches  OC

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date _____________________

Page 3 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 707/720

Overhaul      Inspection &

Period       Check Period

Flight Controls - Chapter 27        O.C.

Flasher - Speed Brake and Flap

Warning                            5,000

Gear Box - Angle Flap Drive         10,000

Gear Box - Double Angle Fillet Flap

Drive                            10,000

Indicator - Flap Position           10,000

Motor - Emery Flap Drive            10,000

Motor - Hydraulic Flap Drive        10,000

Motor - Stabilizer Trim Drive        5,000

Power Unit - Flap Drive Gearbox     10,000

Relay - Emergency Flap Drive        10,000

Relay - Stabilizer Trim Control     10,000

Relay - Stabilizer Trim Safety      10,000

Screw Assembly - Fillet Flap Drive  10,000

Screw Assembly - Main Flap Drive    10,000

Transmitter - Flap Position         10,000

Valve - Flap By Pass                10,000

Valve - Flap Metering               10,000

Flap Cables - Tension Check and

Pressure Seal Inspection         O.C.

Valve - Spoiler Metering            10,000

Control Column                      O.C.

Snubber - Aileron Gust              O.C.

Snubber - Elevator Gust             O.C.

Snubber - Rudder Gust               10,000

Damper - Rudder Control Tab         10,000

Actuator - Leading Edge Flap        12,000

Valve - Leading Edge Flap Actuator  12,000

Actuator - Stabilizer Trim           5,000

Aileron Control Surface Assembly    10,000

Aileron Tab Cockpit Control Mech.   10,000

Spoiler Control Surface             O.C.

Spoiler Actuators                   10,000

Flap Assembly                       10,000

Rudder Control Jackshaft

Installation                     10,000

Rudder Pedal Assembly                5,000

Control Unit - Power - Rudder       10,000

Compensator - Rudder Power Control  10,000

Valve - Rudder Power Control        10,000

Valve - Rudder System Pressure

Control                          10,000

Valve - Rudder System Pressure

Reducing                         10,000

Elevator Control Surface Assembly   10,000        5,000

Horizontal Stabilizer Assembly       6,000        3,000

Stabilizer Trim Actuator

Installation                      5,000

Functional Check Entire Flight

Control System                                 3,000

Effective date   July 1, 1964

Page 4 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 707/720

Overhaul      Inspection &

Period       Check Period

Fuel System, Chapter 28             O.C.

Indicator - Fuel Flow                5,000

Indicator - Fuel Quantity            5,000

Power Unit Fuel Flow                 2,000

Snubber - Fuel Dump                 10,000

Solenoid - Fuel Dump Release         7,500

Compensator - Tank Unit             O.C.

Gauge - Fueling Quantity             5,000

Indicator - Fuel Temperature        10,000

Bulb - Fuel Temperature #1 Main

Tank                             O.C.

Valve - Defueling Check             O.C.

Valve - Pump Removal Check          O.C.

Valve - Defueling Manual            O.C.

Valve - Manual Fueling Shutoff      O.C.

Valve - Fueling Level Control

Shutoff                          O.C.

Valve - Fueling Test                O/C

Valve Thermal Relief                O.C.

Fuel Flow Transmitter                5,000

Booster Pumps                       10,000         7,500

Engine Fuel Feed Shutoff Valve       8,000

Engine Fuel Manifold Shutoff Valve   8,000

Engine Fuel Emergency Shutoff Valve  8,000

Reserve Tank Shutoff Valve          10,000

Dual Check Valve                    O.C.

Dump Chute Shutoff Valve            10,000

Fuel Dump Actuator and Motor         5,000

Fuel Dump Uplatch Actuator           5,000

Hydraulic Power, Chapter 29         O.C.

Indicator - Reservoir Level          7,500

Pump - Aux. Hydraulic Motor          2,500

Regulator - Reservoir Air Pressure  10,000

Switch - Pressure                   O.C.

Transmitter - Reservoir Level        7,500

Valve - Main and Auxiliary

Interconnect                     10,000

Valve - Utility System Relief       12,000

Valve Suction Shutoff               10,000

Relay - Auxiliary Pump               7,500

Gauge - Accumulator Pressure        O.C.

Transmitter - Temperature Sensing   O.C.

Valve - Manual Bypass               12,000

Hydraulic Pump - Engine Driven       2,000

Hydraulic Accumulator               O.C.

Hydraulic Reservoir                 O.C.

Pressure Transmitter                 7,500

Effective date   July 1, 1964

Page 5 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 707/720

Overhaul      Inspection &

Period       Check Period

Hydraulic Power, Chapter 29

(continued)

Pressure Indicator                  10,000

Pump Rudder Hydraulic Motor          4,000

Ice and Rain Protection, Chapter 30 O.C.

Ammeter - Pitot Heater              10,000

Ammeter - Empennage Anti Ice        10,000

Controller - Empennage Shedding Area 7,500

Controller - Automatic Empennage

Shedding Area                     7,500

Controller - Empennage Parting Strip 7,500

Relay - Nesa Control                10,000

Relay - Wing Anti Ice               10,000

Converter - Windshield Wiper        10,000

Drive - Windshield Wiper Flex.      O.C.

Duct - Temperature Indicator        10,000

Duct - Temperature Sensor           O.C.

Anti Ice Check Valve                12,000

Anti Ice Shutoff Valve              10,000

Anti Ice Ducting                    O.C.

Empennage De Icer Overheat Switch   O.C.

Empennage Temp. Control Switch      O.C.

Windshield Anti Ice Controller       5,000

Windshield Wiper Motor              10,000

Ice Detector                        O.C.

Ice Interpreter                     O.C.

Instruments, Chapter 31             O.C.

Ram Air Temperature Indicator

(Lewis)                          10,000

Static Air Temperature Indicator

(Kollsman)                        5,000

Air Speed - Angle of Attack

Indicator (Kollsman)              5,000

Machmeter (Kollsman)                 7,500

Altimeter and Scale Error Corrector  5,000

Altimeter (Kollsman 671-CPX-10-051)  5,000

Indicator - True Air Speed

(Kollsman)                        5,000

Pitot Tubes                         O/C

Static System                       O.C.

Flight Recorder                      2,000

Heading Amplifier                   O.C.

Angle of Attack Sensor              O.C.

Control Unit - Air Data             O.C.

Landing Gear, Chapter 32            O.C.

Actuator - Main Gear                10,000

Actuator - Main Gear Door           10,000

Actuator - Main Gear Side Strut     10,000

Actuator - Nose Gear                10,000

Actuator - Nose Gear Door           10,000

Effective date   July 1, 1964

PAGE 6 of 12 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 707/720

Overhaul      Inspection &

Period        Check Period

Landing Gear, Chapter 32 (continued)

Control Shield - Anti Skid          10,000

Cylinder - Nose Steering            10,000

Detector - Brake Anti Skid           2,500

Gauge Emergency Air Brake Pressure  10,000

Relay - Main Gear Position Warning  10,000

Relay - Nose Gear Position Warning  10,000

Relay - Safety Switch               12,500

Restrictor - Nose Gear Variable     12,500

Snubber Assembly - Main Gear        12,500

Solenoid - Landing Gear Latch Lever   OC

Transmitter - Brake Accumulator

Pressure                          7,500

Valve - Brake Anti Skid             10,000

Valve - Brake Deboost               10,000

Valve - Brake Shuttle               10,000

Valve - Landing Gear Selector       10,000

Valve - Main Gear Actuator Sequence 10,000

Valve - Nose Gear Door Control      10,000

Valve - Air Brake Control             OC

Valve - Steering Disconnect         10,000

Bottle - Air Brake                    *

Switch - Leveling Cyl.                OC

Centering and Snubber Assembly        OC

Valve - Landing Gear Door Safety      OC

Valve - Nose Gear Door Safety         OC

Nose Gear Assembly                  10,000

Nose Gear Shock Strut               10,000

Nose Gear Drag Strut and Lock

Assembly                         12,500

Nose Gear Torsion Link              12,500

Nose Gear Steering Collar           12,500

Nose Gear Axles                     12,500

Nose Gear Emergency Lockshaft,

Actuator Support Shaft, Lock

Arm Shaft and Drag Brace Shaft   12,500

Nose Gear Wheel Assembly              OC

Nose Gear Lock Mechanism            10,000

Nose Gear Emergency Release System    OC

Nose Gear Signal System               OC

Valve - Nose Gear Steering          10,000

Main Gear Assembly                  10,000

Main Gear Trunnion                  12,500

Main Gear Truck Assembly            12,500

Main Gear Drag Strut                12,500

Main Gear Side Strut                12,500

Main Gear Torsion Links             12,500

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date _____________________

PAGE 7 of 12 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 707/720

Overhaul      Inspection &

Period        Check Period

Landing Gear, Chapter 32 (continued)

Main Gear Walking Beam and Support

Link                             12,500

Main Gear Wheel Assembly              OC

Main Gear Brake Assembly              OC

Emergency Release System              OC

Power Brake Valve                   10,000

Centering Cylinder                  10,000

Lights, Chapter 33

May be determined by assigned

inspector.

Navigation, Chapter 34

May be determined by assigned

inspector.

Oxygen, Chapter 35                    OC

Automatic Altitude Sensing Valve     7,500

Manifold Pressure Switch            10,000

Disconnect - Crew Oxygen              OC

Bottle Oxygen Portable                *

Regulator - Constant Flow            7,500

Latch - Automatic                     OC

Valve - Mask Shutoff                  OC

Valve - Oxygen by Pass               7,500

Oxygen Cylinder                       *

Crew Demand Regulator                7,500

Pressure Reducing Valve               OC

Passenger Oxygen Mask Assembly        OC

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Powerplant General, Chapter 71

Engine Mount Links and Fittings       EO

Engine Mount Bolts                    EO

Engine Nose Cowl                      EO

Engine Nose Cone                      EO

Cowling                               EO

Engine, Chapter 72

Compressor Section                    3,000 **

Turbine Section                       2,000 **

** Sample one turbine overhaul at 1800 hours, one compressor

section overhaul at 2400 hours and one compressor section

overhaul at 2800 hours.

Effective date _____________________

Page 7A of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 707/720

Overhaul      Inspection &

Period       Check Period

Engine Fuel and Control, Chapter 73

Fuel and Oil Heat Exchanger         EO

Fuel Control Unit                   EO

Fuel Pump, Engine Driven            EO

Indicator, Fuel Pressure            10,000

Indicator, Fuel Flow                 5,000

Switch, Fuel Pressure Warning       EO

Transmitter, Fuel Pressure           5,000

Transmitter, Fuel Flow              EO

Ignition System, Chapter 74

Ignition Exciter                    EO

Ignition                            EO

Ignition Transformer                EO

High Tension Heads                  EO

Air System, Chapter 75

Anti-icing Control Valve and

System                           EO

Valve, Oil Cooler Ejector Control   OC

Compressor Bleed Valve and Actuator EO

Anti-icing Bleed Shutoff Valve      EO

Valve, Fuel Deice Shutoff           OC

Anti-icing Regulator                EO

Ejector, AC Generator Cooling        2,500

Valve, Nacelle Thermal Anti-ice     EO

Valve, Nose Cowl Anti-ice           EO

Engine Controls, Chapter 76

Cockpit Pedestal Area               OC

Cockpit to Engine Struts            OC

Engine Struts                       OC

Engine                              OC

Engine Indicating, Chapter 77

Bulb, Ram Air Temperature           EO

Generator, Tachometer               EO

Indicator, Pressure Ratio           EO

Transmitter, Pressure Ratio          3,500

Indicator, Tachometer                5,000

Indicator, Ram Air Temperature      OC

Indicator, Exhaust Gas Temperature   5,000

Indicator, Engine Vibration          5,000

Effective date _____________________

PAGE 7B of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 707/720

Overhaul      Inspection &

Engine Indicating, Chapter 77       Period        Check Period

(continued)

Detector, Engine Vibration            EO

Amplifier, Engine Vibration           EO

Exhaust System, Chapter 78

Exhaust Nozzle and Plug               EO

Aft Fairing Assembly                  EO

Thrust Reverser Assembly and Control  EO

Valve, Reverser Directional           EO

Thrust Reverser Actuating Cylinder    EO

Oil System, Chapter 79

Actuator, Oil Cooler Door             EO

Cooler Assembly                       EO

Indicator, Oil Pressure               EO

Indicator, Oil Quantity              7,500

Indicator, Oil Temperature          10,000

Oil Tank                              EO

Switch, Oil Pressure Warning          OC

Thermostat, Oil Temperature Control   EO

Transmitter, Oil Pressure             EO

Transmitter, Oil Quantity             OC

Valve, Oil Shutoff                    OC

Valve, Oil Temperature Control        OC

Starting, Chapter 80

Air Compressor                       2,500

Bottle, Air Start                     *

Corrosion Inspection                1 year

Starter, Pneumatic                    EO

Starter Low Pressure Shutoff Valve    EO

Gauge, Air Pressure                  7,500

Valve, Air Bottle Ground Charge       OC

Valve, Starter Air Relief           10,000

Regulator, Pressure Shutoff          7,500

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Water Injection, Chapter 82

Pump, Water Injection Electric       3,000

Pump, Water Injection Engine Driven   EO

Switch, Water Pressure              10,000

Valve, W/I Check                    10,000

Valve, Water Shutoff                 5,000

Valve, Water Drain                   5,000

Indicator, Water Quantity             OC

Sensor, Water Quantity                OC

Valve, Water Injection Relief         OC

Effective date _____________________

Page 8 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 707/720

Overhaul      Inspection &

Period       Check Period

The Following Systems are Structural

and Systems Items that are not

removed from the Aircraft.  Sample

items are identified by a Suffix

"S" and will be accomplished on 1/4

of the Fleet

Doors, Chapter 52

Electronic, forward Cargo, Rear

Cargo, L. Entry Door, Rt. Forward

Service Door, Rt. Entry Door,

Interior, Frames, Scuff Plates

Emergency Exits, Cutouts, Interior

and Exterior                         4,000 S

Fuselage, Chapter 53

Framing and Skin around Windshields

and Windows Zone 21-22-26            5,000 S

Framing and Skin around Galley,

Cargo Entrance Doors, Emergency

Exits, Hatches, Electronic Access

Doors, Battery Access Doors.

Zone 11-12-13-15-25-26-27

Above Floor   4,000 S

Below Floor   4,000 S

Galley, Cargo and Entrance Doors

Emergency Exit Hatches, and Lower

Nose Compartment Access Doors

Zone 11-12-25-26-42-43-44-45-46-

47-48                                4,000 S

Fuselage Skin Panels and

Circumferential and

Longitudinal Skin

Joints - Zone 14-15-16-21-22-23-

24-25-26-27-28-29-32-33-37           4,000 S

Fuselage Skin Panels under

Horizontal Stabilizer Fairing

Zone 37                             10,000

Tension Bolts between Body Section

at Stations 360 to 960 Zone 16-

24-26-29 and Station 1440 Zone 37    4,000 S

Pressure Bulkheads and Pressure

Panels at the Following Locations:

BS 178 Zone 41                       7,000

Nose Wheel Well Zone 31              3,000

BS 620 Zone 33-34                    4,000 S

BS 960 Zone 35-36                    4,000 S

BS 1440 Zone 37                      4,000 S

Horizontal Pressure Web Between

BS 820 and 960 - Zone 35-36          4,000 S

Wing and Empennage Attachment

Bulkhead at Following Body Stations:

BS 620-820 - Zone 14-26-35-36        7,000

BS 1440 Zone 29                      4,000 S

BS 1505.87 Zone 37                   5,000

BS 1592 Zone 38                      8,000

Effective date   July 1, 1964

Page 9 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 707/720

Overhaul      Inspection &

Period       Check Period

Body Frames at BS 740-758.95,

781.95, and 800 - Zone 26            5,000

Floor Beams at BS 360, 830, 920,

and 1,260 Zone 11-12-14-15-26        4,000 S

Fuselage Delta Beam BS 620-820

and Keel Beam BS 820-960 Zone 32     5,000

Main Gear Side Brace Support

Fittings Zone 35-36                  4,000

Nose Landing Gear Supporting

Structure Zone 31                    3,500

Skin and Stringer Splices in Crown

Area (510 and above) at BS 360-

481-620-820-960-1241 and 1440

Zones 24-25-26-29                    4,000 S

Intermediate Stringer Splices in

Crown Area's S-10 and above

BS 600-620-820-960-1440 Zone 26      4,000 S

Fuselage Skin in Lower Lobe under

Galley and Lavatory Areas - Zone

11-12-13-15-16                       4,000 S

Nacelles, Chapter 54

Forward Engine Mount Fittings        1,400

Forward Engine Mount Thrust Link     1,400

Thrust Link Terminal Bolts           4,000 S

Forward Engine Mount Thrust

Connection Fitting                1,400

Rear Engine Mount Fitting            1,400

Rear Engine Support Brackets         1,400

Nacelle Strut Front Spar Fittings    1,400

Nacelle Strut Midspar Fittings       4,000 S

Nacelle Strut Lower Spar Fittings    4,000 S

Nacelle Strut Diagonal Brace         4,000 S

Nacelle Front Spar Bolts             5,000

Diagonal Strut Bolts                10,000

Bolts - Mid Spar                    10,000

Wing Upper Surface Strut Support     5,000

Nacelle Strut Internal Structure     8,000

Forward and AFT Drag Support

Fittings                          8,000

Stabilizers, Chapter 55

Horizontal Stabilizer Upper and

Lower Spar Terminal Fittings and

Ends of Spars Zone 37                5,000

Horizontal Stabilizer Upper Rear

Spar Terminal Fishmouth Splices

Zone 91-92-37                        5,000

Horizontal Stabilizer Attach Pins

Zone 37                             10,000

Horizontal Stabilizer Structure

Internal Zone 91-92                  5,000

Horizontal Stabilizer Center Section

Zone 37                              5,000

Effective date   July 1, 1964

Page 10 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 707/720

Overhaul      Inspection &

Period       Check Period

Horizontal Stabilizer Center Section

Hinge Fittings BS 1592               2,500

Horizontal Stabilizer Jackscrew

Fittings on Front Spar and on Floor

of Body Section 48 BS 1505 Zone 37   3,500

Horizontal Stabilizer Leading Edge

Attachment Zone 91-92                3,500

Elevator Internal Structure Zone

93-94                               10,000

Elevator Balance Panels, Panel

Support Link Assemblies Balance By

Access and Top Panels Zone 93-94     3,500

Elevator Adjustable Weights (Bolted

to Balance Panels) Zone 93-94        3,500

Elevator Trim and Control Tabs

Zone 93-94                           1,200

Elevator Hinge Fittings Zone 93-94   1,200

Fuselage Fin Attach Fittings BS

1440 Zone 95                         4,000 S

Fuselage Fin Attach Fittings BS

1507 Zone 95                         4,000

Vertical Fin Front Spar Terminal

Fittings and End of Spars - Zone 95  4,000 S

Fin Rear Spar Terminal Fittings and

Fishmouth Splices - Zone 95         10,000

Fin Attach Pins - Zone 95            5,000 S

Vertical Fin Internal Structure      4,000 S

Vertical Fin Leading Edge Attachment

Zone 95                              3,500

Vertical Fin Splice Station 111.65   3,500

Rudder Hinge Fittings Zone 96        1,200

Rudder Balance Panels, Panel Support

Link Assemblies Skin and Covers in

Balance Bay Area's Zone 96           3,500

Control and Balance Tabs Zone 96     1,400

Rudder Internal Structure Zone 96    4,000 S

Wings, Chapter 57

Upper & Lower Interspar Skin Zone

71-72-73-74-75-79                    4,000

Lower Interspar Skin Underwing

Body Fairing and Wing Center Section

Zone 76-77-78                        4,000

Rear Spar Wing Terminal Forging

Zone 77                              5,000

Wing Production Joint Zone 71-74-

75-79                                4,000 S

Wing to Body Shear Attachment Wing

Upper Surface Zone 76-78             4,000 S

Wing Lower Surface at WBL 129.62

Zone 72-74-76-78                     4,000 S

Beaver Tail Attachment and Holes

Zone 72-73-76-78                     4,000 S

Wing Lower Surface Interspar Area

Zone 71-72-73-74-75-76-77-78-79      4,000 S

Effective date   July 1, 1964

Page 11 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 707/720

Overhaul      Inspection &

Period       Check Period

Wings, Chapter 57 (continued)

Wing Center Section Lower Surface

Stringers Adjacent to Manufacturing

Access Holes - Zone 77              12,000

Wing Lower and Upper Surface Splice

at WBL 64.38                         4,000 S

Wing Lower and Upper Surface

Stringer Splices at WBL 129.62

Zone 72-73-76-78                     4,000 S

Wing Lower and Upper Surface Splice

at WS 360 Zone 71-72-73-74           4,000 S

Wing Lower and Upper Surface Splice

at Wing Production Joint Zone 71-

74-75-79                             4,000

Stringer Connections at Boost Pump

Housing WBL 75 113,145,WS 340 and

WS 368 Zone 71-72-73-74-76-78        4,000 S

Lower Surface Stringers at WS

643.50 Zone 71-74                    4,000 S

Front Spar Zone 62-63-64-65-66-67-

14                                   4,000 S

Rear Spar Zone 33-34-35-36-81-82-

83-84-85-86-87-88                    4,000 S

Zone 84-85                 6,000

Zone 33-34 BBL 38.05                10,000

Front and Rear Spars (Internal)

Zone 71-72-73-74-75-79               4,000 S

Zone 76-77-78                        5,500

Wing Ribs and (Center Section)

Spanwise Beams Zone 71-72-73-74-75-

76-77-78-79                          4,000 S

Wing Body Breather Web and BL 12.78

Beams Zone 33-34                     5,000

Wing Terminal Forgings (BS 620-820)

Zone 64-65-35-36                     5,000

Zones 76-77-78                       5,000

Wing Body Bottle Pin Retaining Bolts

Zone 64-65-35-36                     3,500

Wing Body Bottle Pins and Pin Holes

Zone 64-65-35-36                    10,000

Wing Terminal Forgings Zone 76-78    5,000

Zone 76-78-33-34                     7,000

Leading Edge Internal Structure

Zone 81-82-83-84-85-86-87-88         4,000 S

Main Landing Gear AFT Support Rib

External Chord (Beaver Tail) Torque

Box Zone 35-36-84-85                 3,000

Trunnion Support Fitting Bolts and

Pin (Torque AFT Trunnion Cap

Internal Wrenching Bolts on all

Aircraft at 1000 +- 100 hours)      10,000

Wing Trailing Edge Skin and Support

Structure Zone 81-82-83-84-85-86-

87-88                                3,500

Effective date   July 1, 1964

Page 12 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 707/720

Overhaul      Inspection &

Period       Check Period

Wings, Chapter 57 (continued)

Fillet Flap Support Beam Attachment

to Uplock Support BS 900 - Zone

35-36                                5,000

Walking Beam Supports BS 850 and

860 Zone 35-36                       5,000

Spoilers Zone 82-84-85-86            4,000 S

Main Wing Flap Zones 82-84-85-87     4,000

Flap Tracks and Track Supports

Zone 82-84-85-87                     4,000

Fillet Flap Zone 84-85              10,000

Inboard and Outboard Ailerons Zone

81-83-86-88                          3,500

Inboard and Outboard Ailerons

Balance Panels Zone 81-83-86-88      3,500

Inboard and Outboard Aileron

Adjustable Weights (Bolted to

Balance Panels) Zone 81-83-86-88     3,500

Wing Glove Zone 64-65                4,000 S

Beaver Tail Bolts Zone 82-83         4,000 S

Structure under Cover Fillet Splice

Plate and Skin Zone 86-88            2,500

Beaver Tail (X-Ray Skin Beneath)

Zone 86-88                           4,000 S

Effective date   July 1, 1964

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 22.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- DOUGLAS DC-8/F

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

OPERATIONS SPECIFICATIONS

PART D                                        Page 1 of 20 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8/F

Overhaul      Inspection &

Period        Check Period

Air Conditioning, Chapter 21        O.C.

Actuator, Cabin Air Heat Exchanger

Door                              8,000

Actuator, Freon Condenser Selector

Valve                            12,500

Actuator, Freon Condenser Exhaust

Door                              7,500

Actuator, Mixing Valve              10,500

Actuator, Recirculating &

Ventilating Air Selector          7,000

Amplifier, Mixing Valve Control

Unit                             O.C.

Amplifier, Cabin Air Heat Exchanger

Control                          O.C.

Amplifier, Freon Temperature

Control                          O.C.

Amplifier, Cabin Pressure Control   O.C.

Bulb, Freon Condenser Thermistor    O.C.

Bulb, Outside Temperature Sensing   O.C.

Bulb, Cabin Duct Temperature        O.C.

Bulb, Freon Evaporator Differential

Temperature                      O.C.

Blower, Radio Rack Ventilating       5,000

Condenser, Freon                    O.C.

Controller, Cabin Pressure Rate      8,000

Door Assembly, Freon Condenser

Forward and Aft Exhaust          O.C.

Drive & Actuator, Cabin Outflow

Butterfly & Nozzle               12,500

Exhaust Assembly, Cabin Air Heat

Exchanger                        O.C.

Evaporator, Freon                   O.C.

Fan, Freon Condenser                 7,000

Fan, Cabin Air Recirculating         4,000

Heat Exchanger, Cabin Air           O.C.

Horn, Cabin Low Pressure Takeoff

Warning                          O.C.

Heater, Cockpit Floor Panel         O.C.

Indicator, Cabin Air Temperature    O.C.

Indicator, Freon Superheat &

Saturation Temperature           O.C.

Indicator, Cabin Rate of Climb      10,500

Indicator, Cabin Altitude &

Differential Pressure            10,500

Indicator, Cabin Compressor RPM     10,500

Limiter, Pressure Ratio             10,500

Effective date   November 6, 1964

Page 2 of 20 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8/F

Overhaul      Inspection &

Period        Check Period

Air Conditioning, Chapter 21

continued

Potentiometer, Manual Temperature

Control                          O.C.

Receiver, Freon                     O.C.

Switch, Air Manifold Under Pressure

Freon Control                    14,000

Switch, Cabin Turbo Compressor Oil

Overtemperature                  Comp. OH

Switches, Miscellaneous             O.C.

Switch, Freon Condenser Pressure

Cutout                           O.C.

Switch, Radio Rack Blower

Differential Pressure            14,000

Switch, Freon Compressor Overheat   Comp. OH

Switch, Cabin Low Pressure          12,500

Transmitter, Turbo Compressor       Comp. OH

Turbo Compressor, Cabin Air          3,500

Turbo Compressor, Freon              2,500

Thermistor, Freon Evaporator        O.C.

Transmitter, Freon Turbine RPM       3,500

Timer, Cabin Low Pressure & Takeoff

Warning                          14,000

Valve, Assembly, Cabin Turbo

Compressor                       O.C.

Valve, Turbo Compressor Shutoff     10,500

Valve Assembly, Recirculation       12,000

Valve, Thermostat Recirculation     10,500

Valve, Freon Condenser Air Selector O.C.

Valve, Condenser Fan Shutoff         8,000

Valve, Three Port Mixing            10,500

Valve, Cockpit Air Diverter         14,000

Valve, Radio Rack Cooling           14,000

Valve, Recirculating & Ventilating

Air Selector                      7,000

Valve, Freon Turbine Regulating      2,500

Valve, Freon Expansion              O.C.

Valve, Freon Turbine Shutoff         8,000

Valve, Radio Rack Venturi By-Pass    7,000

Valve, Cold Air Pressure Regulator  10,500

Valve, Cabin Pressure Relief        10,500

Valve, Cabin Outflow Butterfly      14,000

Valve, Outflow Nozzle               17,500

Effective date   November 6, 1964

Page 3 of 20 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8/F

Overhaul      Inspection &

Period        Check Period

Auto Pilot, Chapter 22

Automatic Cutoff                     7,500

Auto Pilot Indicator                10,500

Auto Pilot Controller                5,000

Auto Pilot Release Switch           O.C.

Computer, Flight Control             3,000

Computer, Yaw Command                5,000

Computer, Pitch Command              5,000

Computer, Roll Command               5,000

Computer, Pressure                   5,000

Gain Calibrator                      7,500

Interlock Rack                       7,000

Linear Accelerometer                O.C.

Pitot System Cutoff Switch          O.C.

Radio Coupler                        5,000

Stabilization Computer               7,500

Stabilization Computer Rack         O.C.

Servo Amplifier                      7,500

Servo Drive                          6,000

Servo Bracket                       O.C.

Trim Coupler                         5,000

Vertical Gyro                        2,500

Communications, Chapter 23

May be determined by assigned

inspector.

Electrical Power, Chapter 24

Box, Current Differential

Transformer                      O.C.

Box-Generator Current Transformer

& Fuse                           O.C.

Battery                             O.C.

Constant Speed Drive, 20 KVA        E.O.

Circuit Breakers                    O.C.

Control, CSD Frequency & Load

Controller                        3,500

Disconnect Assembly                 E.O.

External Power Receptacle           O.C.

External Power Relay                 7,000

Generator, 20 KVA                    1,500

Generator and Bus Tie Relays         3,500

Indicator, AC & DC Loadmeter        O.C.

Indicator, AC Frequency             O.C.

Panel, Frequency Reference           3,500

Effective date   November 6, 1964

PAGE 4 of 20 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8/F

Overhaul      Inspection &

Period        Check Period

Electrical Power, Chapter 24

(continued)

Panel, Bus Protection                 OC

Panel, Generator Control             2,000

Rectifier, Blocking                   OC

Relay, AC & DC Monitor               7,000

Shaft Assembly, Constant Speed Drive  EO

Switches                              OC

Transformer, Rectifier External

Power Control                      OC

Transformer Rectifier                 OC

Voltmeter AC, Voltmeter DC            OC

Voltage Regulator                    3,500

Equipment/Furnishings, Chapter 25

May be determined by assigned

inspector.

Fire Protection, Chapter 26

Amplifier, Engine Fire Detection      OC

Bell, Fire Warning                    OC

Cable Assembly, Engine Sector

Detector Element                   OC

Container and Valve Assembly, Fire

Extinguisher                       *

Detector, Cargo Compartment Overheat  OC

Lamp Assembly, Fire Warning           OC

Switch, Test                          OC

Valve Assembly, Double Check Tee    12,500

Valve, Two Way Direction            12,500

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Flight Controls, Chapter 27

Actuator, Pitch Trim Compensator     4,000

Accumulator, Flight Spoiler

Hydraulic                        15,000

Bus, Installation Aileron             OC

Cylinder Assembly, Aileron Tab

Lockout                          14,000

Control Assembly, Pilot and Copilot

Rudder Pedal                       OC

Cylinder & Control Valve Assembly

Rudder Power                      7,000

Column Assembly, Pilots Control

Wheel                              OC

Computer, Pitch Trim Compensator     4,000

Cylinder & Link Assembly, Flap

Actuating                         14,000

Effective date _____________________

Page 5 of 20 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8/F

Overhaul      Inspection &

Period        Check Period

Flight Controls, Chapter 27

continued

Cylinders, Flap Lockout             17,000

Cylinder Assembly, Spoiler Actuator 14,000

Cylinder, Valve & Gland Assembly,

Flight Spoiler                   12,500

Cylinder, Ground Spoiler Actuating  12,500

Cylinders, Slot Door Actuating      14,000

Damper Assembly, Aileron             7,000

Damper Assembly, Elevator & Rudder  O.C.

Drive Assembly, Horizontal

Stabilizer                       O.C.

Filter Assembly, Aileron Power

System                           O.C.

Filter Assembly, Rudder Power

System                           O.C.

Filter Assembly, Flight Spoiler

Hydraulic System                 O.C.

Heater, Stall Warning               O.C.

Hose Assembly, Fire Actuating       12,500

Indicator, Flight Spoiler Hydraulic

Pressure                         O.C.

Jack Screw Assembly                 14,000

Lift Transducer                      3,500

Lift Computer                        7,000

Motor & Brake Assembly, Hydraulic

Power                            10,500

Motor & Brake Assembly, Horizontal

Stabilizer Electric Drive         7,000

Mechanical Assembly, Flight Spoiler

Lateral Control                  O.C.

Mechanism, Slot Door Actuating      O.C.

Override Assembly, Outboard

Ailerons                         O.C.

Pump & Motor Assembly, Flight

Spoiler Hydraulic                 5,000

Reservoir Assembly, Flight Spoiler

Hydraulic                        12,500

Switch, Rudder & Aileron Hydraulic

Power                            O.C.

Spring Assembly, Elevator Load

Feel & Centering                 14,000

Shutoff Control Valves, Horizontal

Stabilizer Hydraulic System      14,000

Shaker, Control Column               3,500

Spring Assembly, Rudder Load &

Feel Trim                        17,000

Switch, Spoiler Limit               O.C.

Effective date   November 6, 1964

Page 6 of 20 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8/F

Overhaul      Inspection &

Period        Check Period

Flight Controls, Chapter 27

continued

Switch, Slot Door Actuating Light   O.C.

Tube Assembly, Aileron Bus Torque   16,000

Transmitter, Flap Position          10,500

Valve and Cylinder Assembly,

Aileron Hydraulic Power           6,000

Valve Assembly, Aileron & Rudder

Shutoff                          14,000

Valve Assembly, Rudder Pressure

Reducer                          14,000

Valves, Flap Balance Relief         17,000

Valve, Wing Flap Control            12,500

Valve, Flap Thermal Relief          14,000

Valve, Ground Spoiler Control       12,500

Valve, Wing Slot Control            14,000

Fuel System, Chapter 28

Adapter, Pressure Refueling         O.C.

Actuator, Fuel Dump Chute            7,500

Adapter Assembly, Filler Cap        O.C.

Bulb, Fuel Temperature              O.C.

Control Unit, Float                  7,000

Chute, Fuel Dump                    O.C.

Cap, Pressure Fuel Servicing        O.C.

Check Valve                          7,000

Compensator, Fuel Gauge             O.C.

Drain Valve, Refueling Manifold     O.C.

Drain Valve, Vent System             7,000

Filler Cap, Fuel                    O.C.

Housing Assembly, Drip Stick        O.C.

Indicator, Fuel Quantity            14,000

Indicator, Fuel Quantity Totalizer  14,000

Indicator, Fuel Temperature         O.C.

Pump, Fuel Boost Feed and Transfer   7,000

Switch, Fuel Dump Control           O.C.

Switch, Alternate Tank Fill Valve   O.C.

Switch, Main Tank Fill Valve        O.C.

Switch, Main Fuel Tank Boost Pump   O.C.

Switch, Fuel Tank Transfer Pump     O.C.

Switch, Reservoir Feed Pump

Pressure Warning                  7,000

Slip Tube Assembly, Drip Stick      O.C.

Screen Assembly, Filler Adapter     O.C.

Scroll, Fuel Boost Pump Feed &

Transfer                         O.C.

Effective date   November 6, 1964

Page 7 of 20 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8/F

Overhaul      Inspection &

Period        Check Period

Fuel System, Chapter 28 continued

Swivel, Fuel Dump                   O.C.

Transmitter, Densitometer           O.C.

Transmitter, Fuel Quantity          O.C.

Valve, Fire Wall Shutoff            14,000

Valve, Fuel Tank Selector            7,000

Valve, Auxiliary Tank Selector      15,000

Valve, Crossfeed                    15,000

Valve, Refueling Manifold Shutoff   17,500

Valve, Tank Fill Control            10,500

Valve, Fuel Dump                    15,000

Valve, Fuel Tank Sump Drain         O.C.

Valve, Single Float Level Pilot      7,000

Valve, Check with Screen Inlet      O.C.

Valve, Feed Pump Shuttle             7,000

Valve, Swing Check                  O.C.

Hydraulic Power, Chapter 29

Accumulator, Hydraulic System       17,500

Manifold Assembly, Right-Hand

Hydraulic Power                  O.C.

Manifold Assembly, Left-Hand

Hydraulic Power                  O.C.

Pump, Engine Driven Hydraulic        4,000

Pump Assembly, Auxiliary Hydraulic   7,000

Reservoir Assembly, Hydraulic

System                           O.C.

Relief Valve, Hydraulic Reservoir   14,000

Selector Valve, By Pass & Auxiliary

Pump                             14,000

Valve Assembly, Reservoir Pressure

Aspirator                         7,000

Valve, Auxiliary Pump Selector      14,000

Valve, Auxiliary Hydraulic System

Relief                           14,000

Valve Assembly, System Filter &

Relief                           14,000

Valve, Hydraulic Fire Shutoff       14,000

Ice & Rain Protection, Chapter 30

Amplifier, Windshield Temperature

Control                          O.C.

Ammeter, Pitot Heater               O.C.

Heater, PT2 Probe                   O.C.

Nacelle Anti Ice & Outer Wing

Shutoff Valve                    10,500

Effective date   November 6, 1964

PAGE 8 of 20 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8/F

Overhaul      Inspection &

Period        Check Period

Ice & Rain Protection, Chapter 30

(continued)

Probe Ice Detector                    OC

Switch, Tail Duct Differential

Pressure                         17,500

Switch, Nacelle Lip Pressure        10,000

Timer, Airfoil Deicing               7,000

Transformer, Windshield Heat          OC

Valve, Outer Wing & Empennage

Deicing                            OC

Valve, Wing Vent Scoop Anti-Ice

Shutoff                          12,500

Valve, Inner Wing De-Ice              OC

Valve, Empennage Ice Protection

Shutoff                          10,500

Valve, Fuselage Air Scoop Anti-Ice

Shutoff                          10,500

Valve, Windshield Rain Removal      15,000

Instruments, Chapter 31

May be determined by assigned

inspector.

Landing Gear, Chapter 32

Axle Nose Gear                      12,500

Accumulator, Nose Wheel Steering    15,000

Bogie Beam Assembly Including Axles

& Pivot Pins                     12,500

Bleeder Valve, Nose Wheel Steering    OC

Box, Anti-Skid Control               3,500

Cylinder Assembly, Main Gear

Actuating                        12,500

Cylinder Assembly, Brake Lockout    12,500

Cylinder Assembly, Bogie Trim       12,500

Cylinder Assembly, Main Gear Swivel

Lock                             12,500

Check Valves, Restrictor & Orifice    OC

Cylinder Assembly, Main Gear Door

Latch                            12,500

Cylinder Assembly, Main Gear

Inboard Door Operating           12,500

Cylinder Assembly, Main Gear

Uplatch                          12,500

Cylinder Assembly, Nose Gear

Retract                          12,500

Cylinder Assembly, Nose Gear

Uplatch                          12,500

Cylinder Assembly, Nose Gear Bungee 12,500

Cylinder Assembly, Nose Wheel

Steering                         12,500

Detector, Skid                       3,500

Emergency Air Brake Bottle            *

Emergency Air Brake Control           OC

Gland Assembly, Main Gear Retract

Cylinder                         12,500

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date _____________________

Page 9 of 20 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8/F

Overhaul      Inspection &

Period        Check Period

Landing Gear, Chapter 32 continued

Gland Assembly, Main Gear Pivot     12,500

Gauge, Emergency Air Brake Bottle   O.C.

Gland Assembly, Nose Gear Upper     12,500

Gland Assembly, Nose Wheel Steering

Swivel                           12,500

Gauge, Nose Wheel Steering

Accumulator                      15,000

Gear Lever, Down Limit Switch        7,000

High Pressure Hose Assemblies       O.C.

Horn, Landing Gear Warning          17,500

Indicator, System Brake Pressure    O.C.

Main Landing Gear Structural

Components Including Attachment

to Aircraft                      12,500

Manifold, Forward Hydraulic

Pressure                         12,500

Manifold, Aft Hydraulic Pressure    12,500

Manifold Assembly, Aft Brake        12,500

Main Gear Air Valve                 O.C.

Main Gear Swivel Lock Assembly      12,500

Main Gear Brake Links & Attachments 12,500

Main Gear Wheel Assembly            O.C.

Main Gear Brake Assembly            O.C.

Main Gear Side Brake Assembly       12,500

Main Gear Uplatch Assembly          12,500

Main Gear Doors                     O.C.

Main Gear Door Latching Mechanism   12,500

Main Gear Downlock Visual Indicator O.C.

Nose Gear Shock Strut Assembly      12,500

Nose Gear Drag & Side Brake

Assemblies                       12,500

Nose Gear Wheel Assembly            O.C.

Nose Gear Torque Arm Assembly       12,500

Nose Gear Anti-Retract Mechanism    12,500

Nose Gear Doors                     O.C.

Nose Gear Door Operating Linkage    14,000

Relays Landing Gear System           7,000

Switch, Nose Oleo Ground Control     7,000

Tires, Nose and Main                O.C.

Transmitter, Emergency Air Brake

Pressure                          7,000

Valve Assembly, Trim Cylinder

Relief                           12,500

Valve Assembly, Main Gear Door

Control                          12,500

Valve Assembly, Main Gear Door

Manual Operation                 12,500

Valve Assembly, Main Gear Bungee

Shuttle                          12,500

Effective date   November 6, 1964

PAGE 10 of 20 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8/F

Overhaul      Inspection &

Period        Check Period

Landing Gear, Chapter 32 (continued)

Valve Assembly, Bogie Lock          12,500

Valve Assembly, Nose Gear Control   12,500

Valve Assembly, Nose Wheel Steering

Control                          12,500

Valve Assembly, Nose Wheel Steering

Relief                           12,500

Valve, Anti-Skid Control             3,500

Warning Switches, Gear & Doors       7,000

Warning Horn Cut-Off Switch           OC

Lights, Chapter 33

May be determined by assigned

inspector.

Navigation, Chapter 34

May be determined by assigned

inspector.

Oxygen System, Chapter 35

Cylinder, Oxygen, Crew & Passenger

System                             *

Door Actuator Check Valve             OC

Outlet, Passenger Oxygen Valve        OC

Outlet, First Aid Valve, Passenger

Oxygen                             OC

Regulator Assembly, Crew Cylinder

Oxygen Pressure                   5,000

Regulator, Crew Oxygen               7,500

Regulator and Automatic Opening

Valve, Passenger Oxygen           5,000

Regulator, First Aid Oxygen

Cylinder                          5,000

Relay, Oxygen Time Delay             5,000

Switch Oxygen Altitude               7,500

Valve, First Aid Supply Passenger

Oxygen                             OC

Valve, Oxygen Surge                  5,000

Pneumatic System, Chapter 36

Amplifier, Pneumatic Temperature

Control                          12,500

Actuator, Bleed Air Heat Exchanger    EO

Bulb, Manifold Air Temperature        OC

Connector, Pneumatic Duct             OC

Door Assembly, Bleed Air Heat

Exchanger Exit                     OC

Heat Exchanger, Bleed Air             OC

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date _____________________

Page 11 of 20

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8/F

Overhaul      Inspection &

Period        Check Period

Pneumatic System, Chapter 36

continued

Indicator, Air Supply Temperature   OC

Relay, Low Pressure Pneumatic       OC

Switch, Manifold Under Pressure     14,000

Switch, Manifold Rupture Warning    OC

Temperature Thermistor              OC

Thermo Switches, Over and Under

Temperature                      OC

Valve, Pneumatic Pressure

Regulator                        EO

Valve, Bleed Air Pressure Relief    EO

Valve Assembly, First Spool Bleed

Air Shutoff and Check            7,000

Valve, Pneumatic Fire Shutoff       14,000

Valve, Pneumatic Crossfeed          7,500

Valve, Ground Pneumatic Supply      OC

Doors, Chapter 52

Cylinder Assembly, Door Snubber     14,000

Door Assembly, Turbo Compressor

Access                           OC

Main Cabin Cargo Door Hydraulic

System                           OC

Cylinder Assembly, Main Cabin Door

Actuating                        OC

Powerplant General, Chapter 71

Links, Engine Mount                 3EO

Engine, Chapter 72

Compressor Section                  3,000*

Turbine Section                     2,000*

Engine Fuel and Control, Chapter 73

Engine Fuel Filter Element          100

Fuel & Oil Heat Exchanger           2EO

Fuel Pump Pressure Warning Switch   OC

Fuel Boost Pump, Engine Driven      2EO

Fuel Flow Indicator                 3,500

Fuel Flow Transmitter               EO

Fuel Pressure Indicator             10,500

Fuel Pressure Transmitter           7,000

* Sample one turbine section overhaul at 1800 hours, one

compressor section overhaul at 2400 hours, and one compressor

section overhaul at 2800 hours.

Effective date _____________________

Page 12 of 20 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8/F

Overhaul      Inspection &

Period       Check Period

Engine Ignition, Chapter 74

Switch, Ignition Arming             OC

Switch, Ignition Override           OC

Switch, Fuel Lever Control          OC

Timer                                7,000

Engine Air, Chapter 75

Valve, Assembly, Jet Pump            6,000

Valve, Accessory Compartment

Cooling Shutoff                  OC

Engine Controls, Chapter 76

Lever, Power Control                OC

Lever, Fuel Shutoff                 OC

Sector, Engine Power Control        OC

Engine Indicating, Chapter 77

Generator, Tachometer                3,500

Indicator, Engine RPM                7,000

Indicator, Engine Pressure Ratio    OC

Indicator, Engine Exhaust Gas

Temperature                       7,000

Pickup, PT2 Pressure                OC

Transmitter, Pressure Ratio          3,500

Exhaust, Reverser & Thrust Brake,

Chapter 78

Aft Nozzle Cowl                     EO

Ejector & Reverser                   3,500

Ejector Operating Mechanism          5,000

Exhaust Nozzle                      EO

Pneumatic Components Attached to &

Related to the Ejector Reverser   3,500

Retractable Ejector Alternate Air

System                           OC

Oil System, Chapter 79

Actuator, Oil Cooler Exit Door      EO

Bulb, Oil Temperature               OC

Cooler, Engine Oil                  EO

Indicator, Constant Speed Drive

Oil Temperature                  10,000

Indicator, Engine Oil Pressure      EO

Indicator, Engine Oil Quantity       7,500

Indicator, Oil Temperature          10,000

Oil Tank                            2EO

Effective date _____________________

Page 13 of 20 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8/F

Overhaul      Inspection &

Period       Check Period

Oil System, Chapter 79 continued

Switch, Constant Speed Drive Oil

Level                             7,000

Switch, Oil Cooler Door             OC

Switch, Oil Pressure Warning        OC

Thermostat, Oil Temperature Control EO

Transmitter, Engine Oil Pressure    EO

Transmitter, Engine Oil Quantity    OC

Valve, Engine Oil Shutoff

Valve, Constant Speed Drive Oil

Shutoff                          OC

Valve, Oil Temperature Control      OC

Engine Starting, Chapter 80

Starter, Engine Air Turbine         EO

Valve, Starter Air Shutoff          2EO

Water Injection, Chapter 82

Adapter, Auxiliary Water Fill       OC

Cap, Auxiliary Water Fill           OC

Cell Assembly, Water                OC

Pump, Water Injection               2EO

Relay, Water Injection & Fill

Control                          OC

Switch, Water Injection Fill &

Drain                            OC

Switch, Water Level                 OC

Switch, Water Injection Arming      OC

Switch, Water Pressure Warning      OC

Valve, Water Shutoff                12,500

Valve, Engine Water Line Filling    14,000

Valve, Compressor Water Injection   14,000

Valve, Water Drain & Purge          14,000

Valve, Water Injection Relief        7,000

Valve, Tank Pressurization & Drain   7,000

Valve, Pressure Fill                OC

Valve, Tank Drain                    7,000

Effective date _____________________

Page 14 of 20

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8/F

Structure Inspection Program

The aircraft structure is divided into zones and a detailed

inspection time limitation is listed for each zone.  The

inspection of the zone shall include all areas of structure,

installation of components and appliances unless a specific time

limitation is listed otherwise for a particular item.

E Check -    4,000 Hours            Overhaul      Inspection &

D Check -      500 Hours            Period        Check Period

Demountable Powerplant

Aft Surface of Nose Cowl, Firewall,

Engine Control and Accessory

Brackets.  Zone 1, 2, 3, & 4                        D

Wings

Wing Tip Zone 5 L/R                 5E                D

Wing Outboard of Sta. Xrs 727

Zone 6 L/R                       5E

Wing Leading Edge Sta. Xfs 710

to Xw 761 Zone 7 L/R             E

Wing Leading Edge Sta. Xw 485 to

Xfs 710 Zone 8 L/R               E

No. 1 & 4 Alternate Fuel Tanks

Zone 9 L/R                       5E

Wing Trailing Edge Sta. Xw 408 to

Xw 761                               Aileron

Hinge

Aft of Rear Spar Zone 10 L/R        E   Brackets      4D

& Bolts

Aileron and Tab Zone 11 L/R         E   Hinges &      4D

Attachments

Aileron Leading Edge Balance

Weights                          2E

Wing Leading Edge at Outboard

Pylon Sta. Xw 454 to Xw 485

Zone 12 L/R                      E

Outboard Pylon, Apron and Nacelle

Access Doors Zone 13 L/R         4D

Top Side of Upper Spar Zone 13 L/R  2E

Inboard Pylon, Apron and Nacelle

Access Doors Zone 14 L/R         4D

Top Side of Upper Spar Zone 14 L/R  2E

Wing Leading Edge Sta. Xw 408 to

Xw 454 Zone 15 L/R               E

Wing Leading Edge Sta. Xw 257 to

Xw 408 Zone 16 L/R               E

No. 1 & 4 Main Fuel Tanks Zone

17 L/R                           5E

Wing Trailing Edge from Outboard

Auxiliary Spar to Sta. Xw 408

Zone 18 L/R                      E

Main Landing Gear Support Fittings

and Auxiliary Spars Zone 19 L/R  2E

Wing Leading Edge at Inboard Pylon

Sta. Xw 223 to Xw 257 Zone 20

L/R                              E

Effective date _____________________

Page 15 of 20

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8/F

Overhaul      Inspection &

Period        Check Period

Wing Leading Edge Sta. Xfs 107 to

Xw 223 Zone 21 L/R               E

Wing Leading Edge Sta. Xwo to Xfs

107 External Inspection Zone

22 L/R                           E

Internal Inspection Zone 22 L/R     5E

No. 2 & 3 Alternate Fuel Tanks

Zone 23 L/R                      5E

No. 2 & 3 Main Fuel Tanks Zone

24 L/R                           5E

Outboard Wing Flap Interior

Structure Zone 25 L/R            E

Flap Hinge Support Fittings Zone

25 L/R                           2E

Aft Side of Flap Spar Zone 25 L/R   4E

Inboard Wing Flap & Links at the

Outboard End of the Flap Which

Connect to the Inboard End of

the Outboard Flap Zone 26 L/R    E

Flap Hinge Support Fittings and

Aft Side of Flap Spar Zone 26

L/R                              4D

Interior of Center Wing Sta. Xcw

0 to Xcw 69.5 (Front to Rear

Spar) Zone 27 L/R                5E

Fuselage

Radome Zone 51                      E

Fuselage Turbo Compressor Compt.

Zone 52                          4E

Navigation Antenna Compt. Zone 53   E

Nose Gear Wheel Well Zone 54        4E

Nose Wheel Well Tunnel Zone 55 L/R  4E

Air Conditioning Accessory Compt.

Sta. 248 to 310 Zone 56          E

Forward Cargo Compartment Sta. 310

to 640 Zone 57                   4E

Forward Cargo Compartment Tunnel

Sta. 310 to 640 Zone 57 L/R      4E

Fuselage Accessory Compartment

Sta. 640 to 680 Zone 58          E

Upper and Lower Front Spar Cap,

Forward Face of Front Spar Web,

Upper and Lower Front Spar Caps

and Splice Plates at Sta. Xcw 0

Zone 58                          4E

Aft Cargo Compartment Sta. 980 to

1340 Zone 59                     4E

Aft Cargo Compartment Tunnel Sta.

980 to 1340 Zone 59 L/R             4E

Fuselage Belly Compartment Sta.

1337 to Pressure Dome at Sta.

1490 Zone 60 DC-8-50             E

Effective date _____________________

Page 16 of 20

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8/F

Overhaul      Inspection &

Period        Check Period

Fuselage

Fuselage Belly Compartment Sta.

1337 to Pressure Panel at

Sta. 1566 Zone 60 DC-8-F only    E

Aft Fuselage Sta. 1490 to 1690

Zone 61 DC-8-50                  E

Aft Fuselage Sta. 1566 to 1690

Zone 61 DC-8-F only              E

Aft Face and Periphery of Pressure

Panel at Fuselage Sta. 1566

Zone 61 DC-8-F only              E

Fuselage Tail Cone Zone 62          E

Fuselage Sta. 109 to 123 above

Cockpit Floor Zone 63            4E

Fuselage Cockpit Sta. 123 to 188

Zone 64                          4E

Fuselage Cockpit Sta. 188 to 265

Above Floor Zone 65 L/R          E

Fuselage Sta. 248 to 109 Between

Cockpit Floor and Horizontal

Pressure Panel Zone 66           E

Forward and Aft Galley Areas Sta.

360 to 460 and Sta. 1300 to

1420 R. Side Zone 67             E

Scuff Plates at Forward and Aft

Service Door Jambs.  Internal

Inspection of Door Jambs,

Intercostals and Frames at

Fuselage Sta. 395.430, 1338 &

1375.  Inspection of Door Hinge

Attachments and Door Snubber

Attachments to Jambs Zone 67     4E

Forward and Aft Lavatory Areas

Zone 68                          4E

Vertical Stabilizer Front and

Center Spar Attachments to

Fuselage Longerons, Between

Fuselage Sta.'s 1500 & 1566

DC-8-F only                      4E

Upper and Lower Attachments of Aft

Pressure Panel Vertical Beam

(Center Line-Forward Face of

Pressure Panel) Fuselage Sta.

1566 Zone 68 DC-8-F only         4E

Fuselage Entrance Doors Zone 69     4E

Fuselage Sta. 680 to 980 Between

Bottom of Floor and Top of Wing

and Wheel Well Zone 70

Upper Wing to Fuselage Fillet

Zone L/R                         4E

Effective date _____________________

Page 17 of 20

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8/F

Overhaul      Inspection &

Period        Check Period

Fuselage

Lower Wing to Fuselage Fillet Sta.

680 to 980 Zone 72 L/R           4E

Fuselage Less Zones 67 & 68 From

Sta. 265 to 1445 Above Cusp

Zone 73                          4E

Internal Inspection of Main Cabin

Cargo Door Jamb Intercostals

and Frames at Fuselage Sta. 370

and 510 Zone 73 DC-8-F only      4E

Left and Right Main Landing Gear

and Wheel Well Zone 74 L/R       4E

Wheel Well Keel Zone 74 L/R         E

Left & Right Horizontal Stabilizer

Leading Edge Zone 75 L/R         2E

Forward Face of Stabilizer Front

Spar Zone 75 L/R                 E

Left & Right Horizontal Stabilizer

Outer Panel Zone 76 L/R          4E

Horizontal Stabilizer Center

Section Zone 77                  2E

Left & Right Elevator & Tabs Zone

78 L/R                           E

Vertical Stabilizer Leading Edge

Zone 79                          2E

Vertical Stabilizer Front Spar to

Rear Spar Zone 80                2E

Vertical Stabilizer Tip Zone 81     3E

Rudder and Tab Zone 82              2E

Rudder Hinge Fittings and Damper    E

Horizontal Stabilizer Tip Zone 83

L/R                              2E

Left and Right Aft Fillet Zone 84

L/R                              2E

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 22.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- DOUGLAS DC-8-61/61F

PART D                                          PAGE 1 of 9 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-61/61F

Following are additional items and/or changes to the original

Douglas DC-8/F aircraft specification listing which apply to the

Douglas DC-8-61/61F aircraft.

Zone diagrams for the Douglas DC-8/F are also applicable to

Douglas DC-8-61/61/F aircraft, however, fuselage stations listed

will apply to the Douglas DC-8/F.

Overhaul      Inspection &

Period        Check Period

Air Conditioning, Chapter 21

Valve, Fan Unloader                   OC             D,E

Filter, Recirculating Fan             OC             D

Valve, Cold Air Bypass                OC             D,E

Electrical Power, Chapter 24

Constant Speed Drive, 30 KVA         3,000        D-oil Change

Fire Protection, Chapter 26

(61F) Pyrotector (Smoke Detector)     OC             D,E

Container - Fire Extinguisher         *              D,E

Cartridge - Dual Squib              4 years          D,E

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Landing Gear, Chapter 32

Energy Absorber, Tailskid             OC             D

Ice and Rain Protection, Chapter 30

Rain Repellent System                 OC             D

Tail De-icing Timer                   OC             D,E

Pneumatics, Chapter 36

Amplifier, Pneumatic Manifold

Rupture Warning System                OC             D,E

Sensing Element - Pneumatic

Manifold Rupture Warning              OC               E

Effective date _____________________

Page 2 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-61/61F

Overhaul      Inspection &

Period        Check Period

Doors, Chapter 52

(61F) Main Cabin Cargo Door

Hydraulic System (Same as 55F)   O.C.          See Note *

(61F) Cylinder Assembly, Main

Cabin Cargo Door Actuating       O.C.          See Note *

NOTE:

*    The design of the main cabin cargo door installation is such

that in the normally latched and locked position, it can be

structurally compared to any fixed portion of the fuselage.

It is only when the door is actuated open on the ground

during cargo loading operations that the heaviest loads are

incurred.  These loads would be greatest at the upper door

hinge and hydraulic actuating cylinder attach points.  The

door seal would also be subject to damage at this time.

Thus, door utilization establishes inspection frequency.

Under these conditions, Douglas suggests the following

procedure for purposes of inspection.

(1)  Conduct a general visual area inspection of the upper

cargo door hinge attachments, door jamb, door actuating

cylinder attachments, door seal and latching mechanism

at the scheduled "D" service following use of the

aircraft in cargo configuration.

(2)  If the aircraft is operated solely in the passenger

configuration, conduct a general visual area inspection

(as above) no later than "E" frequency.

Effective date _____________________

Page 3 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-61/61F

STRUCTURE INSPECTION PROGRAM

E Check -     4000 Hours            Overhaul      Inspection &

D Check -      500 Hours            Period        Check Period

Demountable Powerplant

Aft Surface of Nose Cowl, Firewall,

Engine Control and Accessory

Brackets, Zone 1, 2, 3 and 4                           D

Wings

Wing Tip, Zone 5 L/R                5E                 D

Wing Outboard of Sta. Xrs 727,

Zone 6 L/R & Zone 9 L/R          5E

Wing Leading Edge Sta. Xfs 710 to

Xw 761, Zone 7 L/R               E

Wing Leading Edge Sta. Xw 485 to

Xfs 710, Zone 8 L/R              E

No. 1 & 4 Alternate Fuel Tanks,

Zone 9 L/R                       5E

Wing Trailing Edge Sta. Xw 408 to

Xw 761 Aft of Rear Spar, Zone

10 L/R                           E            Aileron Hinge

Brackets and

Bolts 4D

Aileron and Tab, Zone 11 L/R        E            Hinges &

Attachments 4D

Aileron Leading Edge Balance

Weights                          2E

Wing Leading Edge at Outboard

Pylon Sta. Xw 454 to Xw 485,

Zone 12 L/R                      E

Outboard Pylon, Apron and Nacelle

Access Doors, Zone 13 L/R        4D

Top Side of Upper Spar, Zone 13

L/R                              2E

Effective date _____________________

Page 4 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-61/61F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Wings (continued)

Inboard Pylon, Apron and Nacelle

Access Doors, Zone 14 L/R        4D

Top Side of Upper Spar, Zone 14

L/R                              2E

Wing Leading Edge Sta. Xw 408 to

Xw 454, Zone 15 L/R              E

Wing Leading Edge Sta. Xw 257 to

Xw 408, Zone 16 L/R              E

No. 1 & 4 Main Fuel Tanks, Zone

17 L/R                           5E

Wing Trailing Edge from Outboard

Auxiliary Spar to Sta. Xw 408,

Zone 18 L/R                      E

Main Leading Gear Support Fittings

and Auxiliary Spars, Zone 19

L/R                              2E

Wing Leading Edge at Inboard Pylon

Sta. Xw 223 to Xw 257, Zone 20

L/R                              E

Wing Leading Edge Sta. Xfs 107 to

Xw 223, Zone 21 L/R              E

Wing Leading Edge Sta. Xwo to Xfs

107 External Inspection, Zone

22 L/R                           E

Internal Inspection, Zone 22 L/R    5E

No. 2 & 3 Alternate Fuel Tanks,

Zone 23 L/R                      5E

No. 2 & 3 Main Fuel Tanks, Zone

24 L/R                           5E

Outboard Wing Flap Interior

Structure, Zone 25 L/R           E

Flap Hinge Support Fittings, Zone

25 L/R                           2E

Effective date _____________________

Page 5 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-61/61F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Wings (Continued)

Aft Side of Flap Spar, Zone 25 L/R  4E

Inboard Wing Flap & Links at the

Outboard End of the Flap, which

Connect to the Inboard End of

the Outboard Flap, Zone 26 L/R   E

Flap Hinge Support Fittings and

Aft Side of Flap Spar, Zone 26

L/R                              4E

Interior or Center Wing Sta. Xcw 0

to Xcw 69.5 (Front to Rear

Spar), Zone 27 L/R               5E

Fuselage (All Stations are

DC-8-61/61F)

Radome, Zone 51                     E

Fuselage Turbo Compressor Compt.,

Zone 52                          4E

Navigation Antenna Compt., Zone

53                               E

Nose Gear Wheel Well, Zone 54       4E

Nose Wheel Well Tunnel, Zone 55

L/R                              4E

Air Conditioning Accessory Compt.

Sta. 8 to 70, Zone 56            E

Forward Cargo Compartment Sta. 70

to 640, Zone 57                  4E

Forward Cargo Compartment Tunnel

Sta. 70 to 640, Zone 57 L/R      4E

Fuselage Accessory Compartment

Sta. 640 to 680, Zone 58         E

Effective date _____________________

Page 6 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-61/61F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Fuselage (Continued)

Upper and Lower Front Spar Cap,

Forward Face of Front Spar

Web Upper and Lower Front

Spar Caps and Splice Plates at

Sta. Xcw 0, Zone 58              4E

Aft Cargo Compartment Sta. 980 to

1540, Zone 59                    4E

Aft Cargo Compartment Tunnel, Sta.

980 to 1540, Zone 59 L/R         4E

Fuselage Belly Compartment Sta.

1540 to Pressure Panel at Sta.

1766, Zone 60                    E

Aft Fuselage Sta. 1766 to 1890,

Zone 61                          E

Aft Face and Periphery of Pressure

Panel at Fuselage Sta. 1766,

Zone 61                          E

Fuselage Tail Cone, Zone 62         E

Fuselage Sta. -131 to -117 above

Cockpit Floor, Zone 63           4E

Fuselage Cockpit Sta. -117 to -52,

Zone 64                          4E

Fuselage Cockpit Sta. -52 to 25

above Floor, Zone 65 L/R         E

Fuselage Sta. 8 to -131 between

Cockpit Floor and Horizontal

Pressure Panel, Zone 66          E

Forward and Aft Galley Areas Sta.

360 to 460 and Sta. 1500 to

1620 R. Side, Zone 67            E

Effective date _____________________

Page 7 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-61/61F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Fuselage (Continued)

Scuff Plates at Forward and Aft

Service Door Jambs, Internal

Inspection of Door Jambs.

Intercostals and Frames at

Fuselage Sta. 395, 430, 1538

and 1575.  Inspection of Door

Hinge Attachments and Door

Snubber Attachments to Jambs,

Zone 67                          4E

Forward and Aft Lavatory Area,

Zone 68                          4E

Vertical Stabilizer Front and

Center Spar Attachments to

Fuselage Longerons, between

Fuselage Sta's. 1700 and 1766,

Zone 68                          4E

Upper and Lower Attachments of Aft

Pressure Panel Vertical Beam

(Center Line-Forward Face of

Pressure Panel) Fuselage Sta.

1766, Zone 68                    4E

Fuselage Entrance Doors, Zone 69    4E

Cargo Doors, Zone 69                4E

Exit Doors, All Types, Zone 69      4E

Fuselage Sta. 680 to 980 between

Bottom of Floor and Top of Wing

and Wheel Well, Zone 70          4E

Upper Wing to Fuselage Fillet,

Zone 71 L/R                      4E

Lower Wing to Fuselage Fillet Sta.

680 to 980, Zone 72 L/R          4E

Fuselage Less Zones 67 & 68, from

Sta. 25 to 1645 above Cusp.,

Zone 73                          4E

Effective date _____________________

Page 8 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-61/61F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Fuselage (Continued)

(61F) Internal Inspection of Main

Cabin Cargo Door Jamb

Intercostals and Frames at

Fuselage Sta. 130 and 270, Zone

73                               4E

Internal Inspection of Type I

Emergency Exit Door Jambs,

Intercostals and Frames at

Approx. Fuselage Sta. 392, 416,

1312 & 1336, Zone 73             4E

Left and Right Main Landing Gear

and Wheel Well, Zone 74 L/R      4E

Wheel Well Keel, Zone 74 L/R        E

Left and Right Horizontal

Stabilizer Leading Edge, Zone

75 L/R                           2E

Forward Face of Stabilizer Front

Spar, Zone 75 L/R                E

Left and Right Horizontal

Stabilizer Outer Panel, Zone 76

L/R                              4E

Horizontal Stabilizer Center

Section, Zone 77                 2E

Left and Right Elevator and Tabs,

Zone 78 L/R                      E

Vertical Stabilizer Leading Edge,

Zone 79                          2E

Vertical Stabilizer Front Spar to

Rear Spar, Zone 80               2E

Effective date _____________________

Page 9 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-61/61F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Fuselage (Continued)

Vertical Stabilizer Tip, Zone 81    3E

Rudder and Tab, Zone 82             2E

Rudder Hinge Fittings and Damper    E

Horizontal Stabilizer Tip, Zone 83

L/R                              2E

Left and Right Aft Fillet, Zone 84

L/R                              2E

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 22.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- DOUGLAS DC-8/F

DC-8 INSPECTION AND MAINTENANCE PROGRAM

[FIGURE NOT INCLUDED]

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 23.  OPERATIONS SPECIFICATIONS AIRCRAFT

MAINTENANCE - LOCKHEED MODEL 382

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                        Page 1 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL SERIES 382, 382B, D, E, F & G

INSPECTION/CHECK REQUIREMENTS

The basic requirements for performing these inspections and

checks are as specified in PART I of Lockheed Service Manual

Publication SMP 515, revised June 1, 1970, and subsequent

revisions thereto.

"A" INSPECTION/CHECK

To be accomplished each service calendar day.

"B" INSPECTION/CHECK

To be accomplished at intervals not exceeding 200 hours time in

service after the preceding "B" or "C" inspection/check period.

"C" INSPECTION/CHECK

To be accomplished at intervals not exceeding 600 hours time in

service after the preceding "C" inspection/check period.

AIRFRAME STRUCTURAL INSPECTIONS

The frequency and procedure for performing these inspections will

be accomplished as specified in PART I and PART III of Lockheed

Service Manual Publication SMP 515, revised June 1, 1970, and

subsequent thereto.

"SP" SPECIAL INSPECTIONS

The frequency and procedure for performing these inspections will

be accomplished as specified in PART IV of Lockheed Service

Publication SMP 515, revised June 1, 1970, and subsequent

revisions thereto.

Effective date _____________________

Page 2 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL SERIES 382, 382B, D, E, F & G

Overhaul      Inspection &

Period        Check Period

Air Conditioning, Chapter 21          OC          A  B  C   SP

Condenser, Water Separator (Cargo

Compt.)                            OC                C

Condenser, Water Separator (Flt.

Sta.)                              OC                C

Control Box, Temp. (Cargo Compt.)     OC                C

Control Box, Temp. (Flt. Sta.)        OC                C

Controller, Cabin Air Pressure       3,400              C

Fan, Recirculation                   6,300              C

Heat Exchanger (Cargo Compt.)         OC                C

Heat Exchanger (Flt. Sta.)            OC                C

Indicator, Cabin Altitude           12,600              C

Indicator, Cabin Rate of Climb      12,600              C

Indicator, Differential Press.      12,600              C

Separator, Water (Cargo Compt.)       OC                C

Separator, Water (Flt. Sta.)          OC                C

Switch, Differential Pressure        1,800              C

Switch, Emergency Depressurization    OC                C

Thermostat, Cabin Air Temp.          6,300              C

Thermostat, Duct Anticipator

(Cargo Compt.)                     OC                C

Thermostat, Duct Anticipator

(Flt. Sta.)                        OC                C

Turbine, Cooling (Cargo Compt.)      1,800              C

Turbine, Cooling (Flt. Sta.)         1,800              C

Valve, Aux. Vent (Cargo Compt.)     12,600              C

Valve, Aux. Vent (Flt. Sta.)        12,600              C

Valve, Cargo Floor Heat             12,600              C

Valve, Cargo Floor Heat Diverter    12,600              C

Valve, Flow Cont. & Shut-Off

(Cargo Compt.)                   12,600              C

Valve, Flow Cont. & Shut-Off

(Flt. Sta.)                      12,600              C

Valve, Outflow                       6,300              C

Valve, Safety                         OC                C

Valve, Temp. Cont. (Cargo Compt.

Dual Butterfly)                  12,600              C

Valve, Temp. Cont. (Flt. Sta. Dual

Butterfly)                       12,600              C

Auto Flight, Chapter 22               OC          A  B  C   2C

Amplifier, Electronic Control,

Approach and Nav.                 3,400              C

Amplifier, Electronic Control,

Auto Pilot (Main)                 3,400              C

Control, Engage & Approach           6,300              C

Control, Gyro, Roll & Pitch          3,400              C

Control, Servo                       3,400              C   2C

Control, Trim Tab Adapter            6,300              C

Controller, Flight                   6,300              C

Drum and Bracket Assembly             OC                C

Motor and Drive Assembly             6,300              C

Relay, Servo Engage                  6,300              C

Effective date _____________________

Page 3 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL SERIES 382, 382B, D, E, F & G

Overhaul      Inspection &

Period        Check Period

Communications, Chapter 23            OC          A  B  C   SP

May be determined by assigned

inspector.

Electrical Power, Chapter 24          OC          A  B  C

Battery                               OC          A  B  C

Control Panel, AC                    3,400              C

Frequency Meter                       OC                C

Generator, 20 KVA, ATM Driven       12,600              C

Generator, 40 KVA, Engine Driven      EO             B  C

Indicator, Loadmeter (AC)             OC                C

Indicator, Loadmeter (DC)             OC                C

Inverter, 250 VA                     6,300              C

Inverter, 2500 VA                    6,300              C

Regulator, Voltage, 20 KVA

Generator                        12,600              C

Regulator, Voltage, 40 KVA

Generator                         3,400              C

Relay, Battery                        OC                C

Relay, Bus                           6,300              C

Relay, Bus Off (AC)                   OC                C

Relay, Bus Off (DC)                   OC                C

Relay, External Power, AC             OC                C

Relay, External Power, DC             OC                C

Relay, Frequency Sensitive            OC                C

Relay, Generator & Bus Tie (AC)     12,600              C

Relay, Reverse Current               9,450              C

Transformer, Instrument               OC                C

Transformer, Instrument (Engine)      OC                C

Transformer, Rectifier                OC                C

Voltmeter, AC                         OC                C

Voltmeter, DC                         OC                C

Equipment & Furnishings, Chapter 25   OC          A  B  C

Kit, First Aid                        OC          A  B  C

Seat Belts and Harnesses              OC          A  B  C

Seat, Flight Station, FAA Observer    OC          A  B  C

Seats, Flight Station                 OC          A  B  C

Effective date _____________________

PAGE 4 of 12 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL SERIES 382B, D, E, & F

Overhaul      Inspection &

Period        Check Period

Fire Protection, Chapter 26           OC          A B C EC SP

Amplifier, Control Unit               OC              C

Amplifier, Control, Smoke Detection   OC              C

Control Panel, Assembly               OC              C

Control Relay (Unit)                  OC              C

Extinguisher, Portable                *             B C

Flasher, Overheat                     OC              C

Inert Element, Fire Detection         OC              C

Smoke Detector                        OC              C

Sensing Element, Fire Detection       OC              C EC

Sphere Assy., (Agent Container)       *             B C

Squib, Fire Extinguisher              OC              C    SP

(Note 1)

Valve, Directional                    OC              C

Note 1:  Replace at 5 years from date of manufacture.

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Flight Controls, Chapter 27           OC          A B C SP

Actuator, Rudder Trim Tab            6,300            C

Actuator, Aileron Trim Tab           6,300            C

Actuator, Elevator Trim Tab          3,400            C

Aileron & Trim Tab Assembly           OC          A B C

Booster Assy. Rudder                 8,000          B C

Booster Assy. Elevator               8,000          B C

Booster Assy. Aileron                8,000          B C

Brake, Flap Asymmetry               12,600            C

Control Column Assembly             12,600          B C

Elevator & Trim Tab Assy.             OC          A B C

Gear Box Assy., Flap Drive          12,600            C

Gear Box, Wing Flap Jackscrew        6,300          B C

Indicator, Flap Position            12,600            C

Indicator, Aileron Trim Tab

Position                         12,600            C

Indicator, Elevator Trim Tab

Position                         12,600            C

Indicator, Rudder Trim Tab

Position                         12,600            C

Motor, Wing Flap Drive               6,300          B C

Relay, Trim Tab Control             12,600            C

Effective date _____________________

Page 5 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL SERIES 382, 382B, D, E, F & G

Overhaul      Inspection &

Period        Check Period

Flight Controls, Chapter 27

continued

Rudder Pedal Assembly               12,600           B  C

Rudder & Trim Tab Assy.               OC             B  C

Screw and Yoke Assy., Flap

Jackscrew                          OC             B  C   SP

Screwjack, Elevator Trim Tab         6,300              C

Shaft, Flexible, Elevator Trim Tab   6,300              C

Shaft, Flexible, Elevator Trim Tab

Actuator                          6,300              C

Switch, Flap Asymmetry              12,600              C

Switch, Flap Cable Failure

Detection                          OC                C (Note

1)

Tension Regulator, Cable              OC                C

Transmitter, Flap Position          12,600              C

Valve, Flap Brake Control           12,600              C

Valve, Flap Selector                12,600              C

Valve, Pressure Reducer               OC                C

Valve, Rudder System Relief           OC                C

Wing Flap Assembly                    OC          A  B  C

Note 1:  Perform operational check at 6300 hours.

Fuel System, Chapter 28               OC          A  B  C   SP

Indicator, Fuel Quantity            12,600              C

Indicator, Manifold Fuel Pressure   12,600              C

Power Supply                          OC                C

Pump, Drain (SPR Manifold)          12,600              C

Pump, Fuel Boost                     6,300              C

Pump, Fuel Jettison                 12,600              C

Relay, Fuel Quantity                  OC                C

Switch, Fuel Press. Warning           OC                C

Tank Unit, Fuel Quantity              OC                C

Transmitter, Manifold Fuel

Pressure                         12,600              C

Valve, 1-inch Motor Operated Fuel

Shut Off                         12,600              C

Valve, Dual Level Control           12,600              C

Valve, Fuel Dump and Shut-Off       12,600              C

Valve, Fuel Shut-Off                12,600              C

Valve, Fuel Tank Vent               12,600              C

Effective date _____________________

Page 6 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL SERIES 382, 382B, D, E, F & G

Overhaul      Inspection &

Period        Check Period

Hydraulic Power, Chapter 29           OC          A  B  C   SP

Accumulator                         12,600           B  C

Filter Assy., High Pressure           OC                C

Filter Assy., Low Pressure            OC                C

Filter, Reservoir Vent Line           OC                C

Heat Exchanger                        OC                C

Indicator, Remote Pressure          12,600              C

Pump, Auxiliary Elec. Driven         6,300           B  C

Pump, Engine Driven                   EO             B  C

Pump, Hand                            OC                C

Pump, Suction Boost                  3,400           B  C

Reservoir                             OC          A  B  C

Switch, Low Pressure                  OC                C

Transmitter, Pressure               12,600              C

Valve, Check                          OC                C

Valve, Firewall Shut-Off             6,300              C

Valve, Pressure Shut-Off            12,600              C

Valve, Relief                       12,600              C

Valve, Relief, In-Line                OC                C

Valve, 9 Ported Manual               6,300              C

Ice & Rain Protection, Chapter 30     OC          A  B  C   SP

Ammeter, Propeller Anti-Icing         OC                C

Boot, Propeller Blade Anti-Icing      OC             B  C

Control Box, NESA                   12,600              C

Converter, Windshield Wiper         12,600           B  C

Detector, Ice                         OC                C

Duct, Bleed Air                       OC                C

Duct, Wing & Empennage                OC                C

Ejector, Wing & Empennage

Anti-Icing                         OC                C

Indicator, Temperature, Anti-Icing    OC                C

Interpreter, Ice Detector             OC                C

Light Assy., Ice Warning              OC                C

Motor, Windshield Wiper             12,600           B  C

Relay, Windshield, Anti-Icing       12,600              C

Switch, Thermal Inlet Duct

Anti-Ice                           OC                C

Temperature Bulb                      OC                C

Thermostat, Overheat Warning          OC                C

Timer, Propeller De-Icing           12,600              C

Effective date _____________________

Page 7 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL SERIES 382, 382B, D, E, F & G

Overhaul      Inspection &

Period        Check Period

Ice & Rain Protection, Chapter 30

continued

Transformer, NESA                     OC                C

Valve, Pressure Regulator           12,600              C

Valve, Pressure Relief (Radome)       OC                C

Valve, Wing & Empennage Anti-Icing    OC                C

Window, NESA                          OC             B  C

Instruments, Chapter 31               OC          A  B  C

Accelerometer                         OC                C

Accelerometer, Vertical (Flight

Recorder)                         3,400              C

Amplifier, Servo, Flight Recorder    3,400              C

Clock                                 OC                C

Control, Flight Recorder              OC                C

Flight Recorder                      3,400              C

Landing Gear, Chapter 32              OC          A  B  C   SP

Accumulator, Brake                  12,600           B  C   SP

Ball Screw Assy., MLG                3,400           B  C

Brake Assembly                        OC             B  C

Control Box, Anti-Skid               6,300              C

Cylinder, NLG Steering              12,600        A  B  C

Cylinder, NLG Up-Lock               12,600        A  B  C

Cylinder, NLG Drag Strut Actuating  12,600        A  B  C

Detector, Anti-Skid                  6,300        A  B  C (Note

1)

Fuse, Brake, Hydraulic                OC                C

Gear Box Assy., Manual Extension

& Retraction MLG                  6,300              C

Gear Box Assy., Extension &

Retraction, MLG (90 degrees)     12,600              C

Indicator, Position                   OC                C

Limit Switch                          OC                C

Linkages, Landing Gear Door

Actuating                          OC          A  B  C

Motor, Hydraulic, MLG Actuating      6,300              C

Relay, Touchdown                      OC                C

Strut, MLG, Oleo-pneumatic          12,600        A  B  C

Strut, NLG, Oleo-pneumatic          12,600        A  B  C

Tires, MLG                            OC          A  B  C

Tires, NLG                            OC          A  B  C

Torque Strut, MLG                   12,600        A  B  C

Valve, Brake Anti-Skid               6,300              C

Valve, Control By-Pass, LG          12,600              C

Effective date _____________________

PAGE 8 of 12 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL SERIES 382, 382B, D, E, F & G

Overhaul      Inspection &

Period        Check Period

Landing Gear, Chapter 32

(continued)

Valve, Dual Brake Control            6,300              C

Valve, NLG Emerg. Extension         12,600        A  B  C

Valve, NLG Steering Control          6,300              C

Valve, Selector Emer. Brake        12,600               C

Valve, Selector, Landing Gear       12,600              C

Valve, Shuttle                        OC                C

Valve, Shuttle, NLG                   OC                C

Wheel, Main Landing Gear              OC          A  B  C (Note

2)

Wheel, Nose Landing Gear              OC          A  B  C (Note

2)

Note 1:  Inspect at each wheel removal.

Note 2:  Visually inspect at each tire change; perform

non-destructive inspection each 5th tire change.

Lights, Chapter 33                    OC          A  B  C

Light Assy., Anti-Collision           OC             B  C

Light Assy., Dome                     OC             B  C

Light Assy., Instrument Edge          OC             B  C

Light Assy., Instrument Panel Floor   OC             B  C

Light Assy., Leading Edge Scanning    OC             B  C

Light Assy., Navigation               OC             B  C

Light Assy., Ramp Flood               OC             B  C

Light Assy., Retractable, Landing     OC             B  C

Light Assy., Thunderstorm             OC             B  C

Rheostat                              OC             B  C

Transformer, Instr. Lights            OC                C

Navigation, Chapter 34                OC          A  B  C

May be determined by assigned

inspector.

Oxygen, Chapter 35                    OC          A  B  C  SP

Cylinder Assy., Oxygen                *           A  B  C

Cylinder, Portable Oxygen             *           A  B  C

Mask, Crew                            OC          A  B  C

Regulator Assy., (Fixed System)      6,300        A  B  C

Regulator Assy., Portable System     6,300              C

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date _____________________

Page 9 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL SERIES 382, 382B, D, E, F & G

Overhaul      Inspection &

Period        Check Period

Pneumatic, Chapter 36                 OC          A  B  C   SP

Indicator, Bleed Air Pressure         OC                C

(Note 1)

Valve, Bleed Air Check                OC                C

Valve, Bleed Air Divider            12,600              C

Valve, Bleed Air Shut-Off           12,600              C

Valve, Wing Isolation               12,600              C

Note 1:  Bench Service to insure proper operation and calibration

at 12,600 flight hours.

Auxiliary Power, Chapter 49           OC          A  B  C   SP

Actuator, G.T.C. Door               12,600              C

Air Turbine Motor                   ETI 800*         B  C

Compressor, Gas Turbine             ETI 1250*        B  C   SP

or

5,000 Starts

Fan, ATM                             6,300              C

Indicator, Elapsed Time               OC                C

Valve, GTC Oil Shut-Off               OC                C

* Airframe equivalent hours of 6,300 may be used.

Door System, Chapter 52               OC          A  B  C

Cylinder, Aft Cargo Door            12,600        A  B  C

Cylinder, Ramp Actuating             9,450              C

Cylinder, Ramp Uplock               12,600              C

Uplock, Aft Cargo Door              12,600              C

Valve, Ramp Manifold Control        12,600              C

Fuselage, Chapter 53            See Structural Inspection Program

Nacelles, Chapter 54            See Structural Inspection Program

Stabilizers, Chapter 55         See Structural Inspection Program

Windows, Chapter 56             See Structural Inspection Program

Wings, Chapter 57               See Structural Inspection Program

Effective date _____________________

Page 10 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL SERIES 382, 382B, D, E, F & G

Overhaul      Inspection &

Period        Check Period

Propeller, Chapter 61                 OC          A  B  C   SP

Hub, Dome & Blade Assy., Propeller   4,000        A  B  C   SP

(Note 1)

Pump Housing, Propeller              4,000        A  B  C   SP

(Note 2)

Relay, Prop., Feathering            12,600              C

Spinner, Propeller                    OC          A  B  C

Synchrophaser                         OC                C

Trim Control, Manual Phase            OC                C

Valve Housing, Propeller             4,000*       A  B  C   SP

Note 1:  This includes the Spinner Bulkhead.

Note 2:  This includes the NTS Bracket and Anti-Rotation (Drive)

Lug.

* The overhaul period for valve housings serial C8175 and up or

having a part number with the suffix P4 or having

Hamilton-Standard Service Bulletin No. 36 incorporated is 4,000

hours.  For other valve housings the overhaul period is 2,400

hours.

Power Plant, Chapter 71               OC          A  B  C  EC  SP

Cowling                               OC          A  B  C  EC

Engine Dynafocal Mounts               OC                C  EC

Fire Seals                            OC                C  EC

QEC Cone Mounts                       OC                C  EC

QEC Structure                         OC                C  EC

Engine, Turboprop, Chapter 72         OC          A  B  C  SP

Engine Compressor Section            5,000        A  B  C

(Note 2)

Reduction Gear Assy.                  EO             B  C

Torquemeter, Assy.                    EO             B  C

Turbine Unit 501-D22                  EO          A  B  C

(Note 1)

Turbine Unit 501-D22A                 EO          A  B  C

(Note 3)

Note 1:  At intervals not to exceed 2,000 hours turbine operating

time, perform turbine maintenance inspection in

accordance with Allison Publication 4RC-2 and replace

life limited parts on turbines not modified in

accordance with Allison Commercial Engine Bulletin No.

72-1019.

Note 2:  Operators of Allison D-22 engines having an approved

engine overhaul period greater than 5,000 hours may have

the same approved time for D-22A engines.

Effective date _____________________

Page 11 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL SERIES 382, 382B, D, E, F & G

Overhaul      Inspection &

Period        Check Period

Engine, Turboprop, Chapter 72

continued                          OC          A B C  SP

Note 3:  At an interval not to exceed 3,000 hours turbine section

operating time, perform one hot section inspection in

accordance with Allison Publication 4RC-2, Chapter

72-1-0, for 501-D22A series engines.  On the basis of

satisfactory findings, the interval for this inspection

may be increased at the rate of 1,000 hours until it

coincides with the currently approved engine overhaul

period.

Engine, Fuel and Control,

Chapter 73                         OC          A B C

Control, Speed Sensing              2 EO              C

Control, Temperature Datum            OC              C

Control, Unit, Fuel                   EO              C

Coordinator                           EO              C

Harness, Thermocouple                 OC              C

Heater and Strainer Assy., Eng.

Fuel                               OC              C

Indicator, Fuel Flow                  OC              C  (Note)

Pump, Fuel                            EO              C

Transmitter, Fuel Flow              2 EO              C

Valve, Temperature Datum Control

System                             EO              C

Note:  Bench check at 2 EO.

Ignition, Chapter 74                  OC          A B C

Exciter                               OC              C

Harness Assembly                      OC              C

Igniter Plug                          OC              C

Relay, Ignition                       OC              C

Air, Chapter 75                       OC          A B C EC

Duct, Compressor Bleed Air (Engine

Mounted)                           OC              C EC

Valve, Shut-Off, Inlet Anti-Ice     2 EO              C

Valve, Speed Sensitive                EO              C

Controls, Chapter 76                  OC          A B C EC

Power Lever System and Engine

Coordinator Controls and

Linkages                           OC            B C EC

Effective date _____________________

Page 12 of 12 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL SERIES 382, 382B, D, E, F & G

Overhaul      Inspection &

Period        Check Period

Indicating, Chapter 77                OC          A B C

Generator, Tachometer               2 EO              C

Indicator, Tachometer                 OC              C

Indicator, Torque                     OC              C

Indicator, TIT                        OC              C

Pickup, Torque                        EO              C

Exhaust, Chapter 78                   OC          A B C

Clamp, Tail Pipe                      OC          A B C

Tail Pipe Assembly                    OC          A B C

Oil, Chapter 79                       OC          A B C EC

Actuator, Flap, Oil Cooler          2 EO              C

Cooler, Assy. Eng. Oil                OC              C EC

Indicator, Oil Pressure             20,000            C (Note)

Indicator, Oil Quantity             20,000            C (Note)

Indicator, Oil Temperature          20,000            C (Note)

Indicator, Position, Oil Cooler

Flap                             20,000            C (Note)

Switch Pressure, Oil (95023)          OC              C

Switch Pressure, Oil (95024)          OC              C

Tank, Assy., Eng. Oil                 OC              C EC

Tank Unit, Oil Quantity               OC              C EC

Thermostat                            OC              C

Transmitter, Oil Pressure             OC              C

Note:  Bench check at 10,000 hours.

Starting, Chapter 80                  OC          A B C

Starter                               EO              C

Starter, Valve                      2 EO              C

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 24.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- CONVAIR CV-880

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

OPERATIONS SPECIFICATIONS

PART D                                          Page 1 of 9 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

CONVAIR CV-880

Overhaul      Inspection &

Period        Check Period

Air Conditioning, Chapter 21        12,500

Cabin Supercharger                   3,000

Fan, Condenser                       6,000

Fan, Electronic Cooling              8,000

Freon Package                        3,000

Heater, Dual Cabin Air Electric      3,000

Regulator, Cabin Pressure            6,000

Valve, Cabin Pressure Regulator

Outflow and Safety                3,000

Valve, Condenser Air Modulating      3,000

Valve, Freon Bleed Duct Isolation    5,000

Valve, Ram Air Shutoff               3,000

Valve, Supercharger Drive Shutoff    3,000

Auto Pilot, Chapter 22              12,500

Computer, Flight Control             5,000

Junction Box-Power                   6,000

Rate Controller - Three Axis         6,000

Sensor, Air Data                     6,000

Servo and Drive                      6,000

Stabilization Computer and

Amplifier                         5,000

Transmitter, Autosyn Position        7,500

Trim Servo                           6,000

Vertical Gyro                        3,000

Communications, Chapter 23          12,500

May be determined by assigned

inspector.

Electrical System, Chapter 24       12,500

Ammeter, A.C.                       10,000

Ammeter, D.C.                       10,000

Battery                             O.C.

Bus Protection Panel                 6,000

Constant Speed Drive                 1,800

Contractor Bus Tie, Pilot's

Essential - Ground/Maintenance    6,000

Contractor, External Power          10,000

Contractor, Generator Line & Bus

Tie                               6,000

Control Panel Voltage Regulator      4,000

CSD Air Oil Cooler Shutoff Valve     3,000

CSD Oil Cooler                       7,500

Effective date _____________________

PAGE 2 of 9 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

CONVAIR CV-880

Overhaul      Inspection &

Electrical System, Chapter 24       Period        Check Period

(continued)

CSD Oil Cooler Thermo Sensor         3,000

Frequency Meter                     10,000

Generator                            2,000

Load Controller                      6,000

Relay, Monitor D.C. Essential Bus    6,000

Relay, Monitor Pilot Essential Bus   6,000

Relay, Monitor Pilot Non-Essential

Bus                               6,000

Relay, Phase Sequence                6,000

Relay, Power Failure - Instrument

Essential Bus                     6,000

Relay, Reverse Current               6,000

Relay, Transfer - 28 V. Lighting     6,000

Static Exciter                       6,000

Switch Load Limit                    1,000

Transformer/Rectifier                6,000

Voltmeter, A.C.                     10,000

Voltmeter, D.C.                     10,000

Watt, VAR meter                     10,000

Equipment & Furnishings,

Chapter 25                       12,500

Evacuation Slides                   6 mos.

Fire Protection, Chapter 26         12,500

Agent Container & Cartridge

Assembly                           *

Check Valve, Two Way               5 years

Control Box, Fire & Overheat

Warning                           6,000

Control Unit, Magnetic Amplifier     6,000

Flasher, Overheat Warning            6,000

Plug, Safety                       5 years

Power Relay Box                      6,000

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Flight Controls, Chapter 27         12,500

Actuator, Servo Rudder              10,000

Bata Box                             6,000

Cylinder, Inboard Spoiler           10,000

Cylinder, Outboard Spoiler          10,000

Cylinder, Rudder                    10,000

Cylinder, Rudder Stop               10,000

Dampeners, Flutter, Control

Surfaces                          5,000

Dampeners, Flutter, Flight Tabs      5,000

Dampeners, Gust                      6,000

Indicators, Flap Position           10,000

Effective date _____________________

Page 3 of 9 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

CONVAIR CV-880

Overhaul      Inspection &

Period        Check Period

Flight Controls, Chapter 27

(continued)

Indicators, Stabilizer Position     10,000

Motor, Electric, Stabilizer

Emergency Trim                   10,000

Motor, Electric, Stabilizer Drive    3,000

Motor, Hydraulic, Stabilizer Trim   10,000

"Q" - Pat - Rudder Boost Control     6,000

Relay, Flap Asymmetry Control       10,000

Relay, Stabilizer, Electric Drive

Control                          10,000

Switch, Flap Asymmetry               6,000

Transmitter, Flap Position          10,000

Transmitter, Stabilizer Position    10,000

Valve, Inboard Spoiler              10,000

Valve, Outboard Spoiler             10,000

Valve, Rudder and Stabilizer,

Check                            10,000

Fuel System, Chapter 28             12,500

Pump, Booster and Transfer          10,000

Valve, Firewall Fuel Shutoff        10,000

Valve, Vent 1.50 Inch               10,000

Valve, Vent 2.00 Inch (w/o pressure

relief)                          10,000

Valve, Vent 2.00 Inch (with

pressure relief)                 10,000

Hydraulic System, Chapter 29        12,500

Accumulator, Main                    8,000

Accumulator, Main Landing Gear       8,000

Accumulator, Pump Supply Line        8,000

Filter, High Pressure                7,500

Filter, High Pressure (Purolator)    7,500

Filter, Low Pressure                 7,500

Hydraulic Boost Pump and Motor       3,000

Hydraulic Pump, Engine Driven V.D.   2,000

Pump, Electric Auxiliary             7,500

Transmitter, Pressure                6,000

Valve, Firewall Shutoff              6,000

Ice and Rain Protection,

Chapter 30                       12,500

Valve, Engine Inlet Duct Lip

Anti-Ice Pressure Regulator       3,000

Valve, Leading Edge Anti-Ice

Pressure Regulator and Shutoff    3,000

Valve, Radome De-Ice Pressure

Regulator                         3,000

Valve, Radome De-Ice Suction

Relief                            3,000

Valve, Engine Bleed Air Press. Reg.

Shutoff                           E.O.

Effective date _____________________

PAGE 4 of 9 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

CONVAIR CV-880

Overhaul      Inspection &

Period        Check Period

Ice & Rain Protection, Chapter 30

(continued)

Valve, Windshield Rain Rem.

Shutoff and Isolation             6,000

Switch, Anti-Ice Pressure            3,500

Instrument, Chapter 31              12,500

May be determined by assigned

inspector.

Landing Gear, Chapter 32            12,500

Tire, Main                            OC

Tire, Nose                            OC

Transmission Mechanism (Anti-skid)   7,500

Wheel Assembly, Nose and Main         OC

Lights, Chapter 33                  12,500

May be determined by assigned

inspector.

Navigation, Chapter 34              12,500

May be determined by assigned

inspector.

Oxygen System, Chapter 35           12,500

Cylinders, Oxygen (Supply)            *

Cylinders, Oxygen, Portable and

Equipment                          *

Masks, Crew                          7,500

Regulators, Demand, Oxygen Diluter   7,500

Reducer, Oxygen Pressure             6,000

Valve, Auto Opening and Continuous

Flow Regulator                    6,000

Valve, Oxygen Cylinder             5 years

Pneumatic System, Chapter 36        12,500

Air Flask, Emergency Brakes           *

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date _____________________

Page 5 of 9 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

CONVAIR CV-880

Overhaul      Inspection &

Period        Check Period

Powerplant General, Chapter 71      E.O.

Engine, Chapter 72

Compressor Section                   2,500*

Turbine Section                      1,700*

* Sample one turbine section at

1500 hours, one compressor

section at 2000 hours and one

compressor section at 2300

hours.

Engine Fuel & Control, Chapter 73   O.C.

Fuel Control Unit                   E.O.

Fuel Flow Indicator                  3,000

Fuel Flow Transmitter               E.O.

Fuel Heater                         E.O.

Fuel Pressure Switch                E.O.

Fuel Pump                           E.O.

Engine Ignition, Chapter 74         O.C.

Igniter Plugs                       E.O.

Engine Air, Chapter 75              O.C.

Anti-Icing Valve                    E.O.

Aspirator & Shutoff                 E.O.

Vortex Destroyer                    E.O.

Engine Controls, Chapter 76         O.C.

Engine Control Cables               E.O.

Engine Torque Boxes                 E.O.

Teleflex Cable Conduit              E.O.

Engine Indicating, Chapter 77       O.C.

Amplifier, AVM                       5,000

Detectors, AVM                       5,000

Generator, Tachometer               E.O.

Indicator, AVM                       6,000

Indicator, Exhaust Gas Temperature   8,000

Indicator, Pressure Ratio            6,000

Indicator, Tachometer                7,500

Thermocouples and Harness           O.C.

Transmitter, Pressure Ratio          2,000

Effective date _____________________

Page 6 of 9 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

CONVAIR CV-880

Overhaul      Inspection &

Period        Check Period

Exhaust System, Chapter 78          O.C.

Sound Suppressor                    E.O.

Thrust Reverser                     E.O.

Thrust Reverser Actuator            E.O.

Thrust Reverser Hydraulic Pump      E.O.

Thrust Reverser Control Valve       E.O.

Thrust Reverser Pilot Valve         E.O.

Oil System, Chapter 79              O.C.

Indicator, Engine Oil Pressure      10,000

Indicator, Engine Oil Quantity      12,500

Indicator, Engine Oil Temperature   10,000

Oil Tank                            E.O.

Transmitter, Engine Oil Pressure     7,500

Switch, Engine Oil Pressure         12,500

Engine Starting, Chapter 80         O.C.

Air Turbine Engine Starter          E.O.

Starter Pressure Regulating Valve   E.O.

Effective date _____________________

Page 7 of 9 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

CONVAIR CV-880

Structural Inspection Program

The aircraft structure is divided into zones and a detailed

inspection time limitation is listed for each zone.  The

inspection of the zone shall include all areas of structure,

components, and appliances unless a specific time limitation is

listed for a particular item.  Sample items are identified with

the suffix "S" and will be accomplished on 1/5 of the fleet.

D Check - 225 hours

Overhaul      Inspection &

Zone    Period        Check Period

Doors, Chapter 52                   12,500

Nose Wheel Well Access

Door #1                  2        1,000

Access Doors #12, 13, &     3 & 4    1,000

14, Air Compressor,

Heat Exchanger, and

Cabin Refrigeration

Access Door #20, Aft        7        1,000

Section, Fuselage Sta.

1400 L.H.

Access Door #21, Aft        8        2,500

Section, Fuselage Sta.

1538

Access Door #3, Electrical, 10       2,500 S

L.H. & R.H. Fuselage

Sta. 221

Access Door #4, Electronic  11       2,500 S

Compartment, Fuselage

Sta. 289

Door #9, Forward Cargo      12       2,500 S

Access Door #16, Hydraulic  15       2,500 S

Compartment, Fuselage

Sta. 970

Door #17, Aft Cargo         16       2,500 S

Door #6, L.H. Forward Main  21       2,500 S

Entrance

Door #7, R.H. Forward       21       2,500 S

Service

Door #18, L.H. Aft Main     23       2,500 S

Entrance

Door #19, R.H. Aft Service  23       2,500 S

Fuselage, Chapter 53                12,500

Radome, Nose Sta. 100 to    1        2,500

152

Nose Wheel Well, Sta. 152   2        2,500

to 250

Air Conditioning            3 & 4    2,500

Compartment (Plenum

Chamber)

Tail Section, Sta. 1374     7 & 8    2,500 S

to 1590

Nose Section, Sta. 152 to   10       2,500 S

250

Effective date _____________________

Page 8 of 9 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

CONVAIR CV-880

Zone    Overhaul      Inspection &

Period        Check Period

Fuselage, Chapter 53

(continued)

Electronic - Electrical     11       2,500 S

Compartment, Sta. 250

to 375

Forward Baggage             12       2,500 S

Compartment, Sta. 375

to 603

Water & Misc. Compartment,  13       2,500 S

Sta. 603 to 640

Overwing Compartment        14       2,500 S

Hydraulic Compartment,      15       2,500 S

Sta. 926 to 1002

Aft Baggage Compartment,    16       2,500 S

Sta. 1002 to 1239

Aft Fuselage - Below Floor, 17       2,500 S

Sta. 1230 to 1374

Cockpit, Sta. 187 to 301    20       2,500 S

Entrance and Service -      21       2,500 S

Forward

Fuselage - Passenger,       22       2,500 S

Sta. 403 to 1263

Entrance and Service -      23       2,500 S

Rear

Lavatory and Pressure       24       2,500 S

Dome, Sta. 1325 to 1374

Nacelles, Chapter 54                12,500

Nacelle, #1 Engine          81                        D

Nacelle, #2 Engine          82                        D

Nacelle, #3 Engine          83                        D

Nacelle, #4 Engine          84                        D

Pylon, #1 Engine            85       2,500 S

Pylon, #2 Engine            86       2,500 S

Pylon, #3 Engine            87       2,500 S

Pylon, #4 Engine            88       2,500 S

Stabilizers, Chapter 55             12,500

Horizontal Stabilizer,      60 & 65  2,500 S

Outboard L.H. & R.H.

Horizontal Stabilizer,      62 & 63  2,500 S

Interspar L.H. & R.H.

Elevator and Tabs           61 & 64  2,500 S

Vertical Stabilizer         70 & 71  2,500 S

including Dorsal Fin

and Tip

Rudder and Tabs             72       2,500 S

Effective date _____________________

Page 9 of 9 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

CONVAIR CV-880

Zone    Overhaul      Inspection &

Period        Check Period

Windows, Chapter 56                 12,500

Cockpit - Enclosure Glass   20       2,500 S

Cabin Windows, Emergency    22       2,500 S

Exit

Wings, Chapter 57                   12,500

Wheel Well, Main L.H. &     5 & 6    2,500 S

R.H.

Wing Fillet, Fuselage       9 L & R  2,500 S

Wing, #1 Aux. Fuel Tank,    30       2,500 S

L.H.

Wing, #4 Aux. Fuel Tank,    38       2,500 S

R.H.

Wing, #1 Main Fuel Tank,    31       2,500 S

L.H.

Wing, #4 Main Fuel Tank,    37       2,500 S

R.H.

Wing, #2 Aux. Fuel Tank,    32       2,500 S

L.H.

Wing, #3 Aux. Fuel Tank,    36       2,500 S

R.H.

Wing, #2 Main Fuel Tank,    33       2,500 S

L.H.

Wing, #3 Main Fuel Tank,    35       2,500 S

R.H.

Wing, Center Tie Box        34       3,000

Wing Tip, L.H. & R.H.       40 & 47  2,500 S

Wing Leading Edge,          41       2,500 S

Outboard L.H.

Wing Leading Edge,          46       2,500 S

Outboard R.H.

Wing Leading Edge,          42       2,500 S

Center L.H.

Wing Leading Edge,          45       2,500 S

Center R.H.

Wing Leading Edge,          43 & 44  2,500 S

Inboard L.H. & R.H.

Wing Trailing Edge, L.H.    50 & 57  2,500 S

& R.H.

Flap & Spoiler, Outboard    51 & 56  2,500 S

L.H. & R.H.

Wing, Aileron Area, L.H.    52 & 55  2,500 S

& R.H.

Flap & Spoiler, Inboard     53 & 54  2,500 S

L.H. & R.H.

Effective date _____________________

----------------------------------------------------------------

MAINTENANCE ZONES - CONVAIR 880 - 22-99001

[FIGURE NOT INCLUDED]

NOTES:

1.  WING TO

FUSELAGE

FAIRING OMITTED

FOR CLARITY.

2.  C.S.S. MEANS

CENTER SPAR

STATION.

3.  F.S. MEANS

FUSELAGE

STATION.

4.  W.S. MEANS WING

STATION.

UN-PRESSURIZED FUSELAGE AREAS      ABOVE FLOOR COMPT.

1. RADOME                         20. COCKPIT

2. NOSE WHEEL WELL & GEAR         21. ENTRANCE & SERVICE - FWD

3. AIR-COND (LH)                  22. FUSELAGE - PASSENGER

4. AIR-COND (RH)                  23. ENTRANCE & SERVICE - REAR

5. WHEEL WELL - LH & GEAR         24. LAVATORY & PRESS DOME

6. WHEEL WELL - RH & GEAR         25. FAIRING - ANTENNA - TOP

7. TAIL SECTION - FUSELAGE

8. TAIL CONE                      FUEL TANKS

30. WING - NO 1 AUX FUEL TANK

BELOW FLOOR COMPT'S                    - LH

10. NOSE SECTION                   31. WING - NO 1 MAIN FUEL TANK

11. ELECTRONIC - ELECTRICAL            - LH

12. BAGGAGE - FWD                  32. WING - NO 2 AUX FUEL TANK

13. WATER                              - LH

14. OVER WING                      33. WING - NO 2 MAIN FUEL TANK

15. HYDRAULICS                         - LH

16. BAGGAGE - REAR                 34. WING - FUEL TANK - CENTER

17. AFT FUSELAGE - BELOW FLOOR         SECTION

35. WING - NO 3 MAIN FUEL TANK

WINGS - L.E. & TIPS                    - RH

40. WING TIP - LH                  36. WING - NO 3 AUX FUEL TANK

41. LEAD EDGE - OUTBD - LH             - RH

42. LEAD EDGE - CENTER - LH        37. WING - NO 4 MAIN FUEL TANK

43. LEAD EDGE - INB'D - LH             - RH

44. LEAD EDGE - INB'D - RH         38. WING - NO 4 AUX FUEL TANK

45. LEAD EDGE - CENTER - RH            - RH

46. LEAD EDGE - OUTBD - RH

47. WING TIP - RH                  HORIZONTAL STABILIZER

60. HORIZ STAB - OUTBD - LH

WINGS - TRAILING EDGE & REAR SPAR  61. ELEV. TABS & BAL BD'S - LH

50. WING - TRAILING EDGE - LH      62. HORIZ STAB - INBD - LH

51. WING - FLAP & SPOILER - OUTBD  63. HORIZ STAB - INBD - RH

- LH                           64. ELEV. TABS & BAL BD'S - RH

52. WING - AILERON & BAL BD - LH   65. HORIZ STAB - OUTBD - RH

53. WING - FLAP & SPOILER - INBD

- LH                           VERTICAL STABILIZER

54. WING - FLAP & SPOILER - INBD   70. VERT STAB

- RH                           71. VERT STAB - INSUL STRIP &

55. WING - AILERON & BAL BD - RH       CAP

56. WING - FLAP & SPOILER - OUTBD  72. RUDDER, BAL BD'S & TABS

- RH

57. WING - TRAILING EDGE - RH      PODS & PYLONS

81. ENGINE #1 POD

82. ENGINE #2 POD

83. ENGINE #3 POD

84. ENGINE #4 POD

85. ENGINE #1 PYLON

86. ENGINE #2 PYLON

87. ENGINE #3 PYLON

88. ENGINE #4 PYLON

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 25.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- FAIRCHILD F-27

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

OPERATIONS SPECIFICATIONS

PART D                                          Page 1 of 7 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAIRCHILD F-27

Overhaul      Inspection &

Period        Check Period

Air Conditioning System,

Chapter 21                       12,000

Altimeter, Dual Pressure             3,000

Air Cycle Machine                    3,000

Blower, Cabin (Roots)                2,200

Circuit - Cabin Temperature Sensing  3,000

Controller, Cabin Pressure           5,000

Controller, Cabin Rate               5,000

Controller, Cabin Temperature        5,000

Delivery Silencer                   10,000

Fan, Combustion                      2,000

Heater System                        3,000

Indicator, Cabin Blower Pressure     7,500

Recirculating Fan                    1,000

Transmitter, Cabin Blower Pressure   6,000

Valve, ACM Turbine Bypass            2,000

Valve, Spill                         3,000

Auto Pilot, Chapter 22              12,000

Controller, Altitude                 2,000

Capstan, Primary Servo               2,000

Capstan, Trim Servo                  2,000

Computer Coupler                     2,000

Followup                             2,000

Servo, Primary                       2,000

Servo, Trim                          2,000

Trim Indicator                       4,000

Communications, Chapter 23          12,000

May be determined by the assigned

inspector.

Electrical Power, Chapter 24        12,000

Ammeter, D.C.                        8,000

Battery                             O.C.

Circuit Breakers                    12,000

Control Panel A.C.                   2,000

Control Relay D.C.                   2,000

Control, D.C. Generator              1,000

Generator, D.C.                      1,400

Generator, A.C. Brushless            2,000

Generator, Emergency A.C.            1,300

Inverter                             1,800

Power Failure, A.C.                  2,000

Effective date _____________________

PAGE 2 of 7 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAIRCHILD F-27

Overhaul      Inspection &

Electrical Power, Chapter 24        Period        Check Period

(continued)

Relay, Main Contactor                1,000

Voltmeter, D.C.                      7,000

Equipment and Furnishings,

Chapter 25                       12,000

Emergency Equipment                 6 mos.

Fire Protection, Chapter 26         12,000

Control Box, Fire Detection          4,000

Cartridges, Discharge Valve         2 years

Cylinders (Water and CO2 Hand

Extinguisher)                      *

Cylinders (Engine)                    *

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Flight Controls, Chapter 27         12,000

Cables System                         OC

Control Surface Assembly            12,000

Control Interior Structure          12,000

Control Exterior Covering           12,000

Control Stick Shaker                 2,000

Flap Transmitter Position and

Indicator                         5,000

Flap Actuator                        1,000

Lift Transducer                      1,500

Stall Warning Indicator              1,500

Switch Asymmetry                    12,000

Summing and Relay Unit                OC

Tension Regulator                   10,000

Fuel System, Chapter 28             12,000

Indicator Fuel Quantity and Power

Unit                             12,000

Indicator Fuel Quantity Repeater    12,000

Pump, Fuel Boost                     1,200

Switch, Differential Pressure        6,000

Switch, Pressure Fuel Warning        6,000

Tank Unit, 13.41" Fuel Quantity     12,000

Tank Unit, 20.00" Fuel Quantity     12,000

Tank Unit, 16.25                    12,000

Valve, Hot Air Gate                  3,000

Valves, Electrical and Manual       12,000

Effective date _____________________

Page 3 of 7 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAIRCHILD F-27

Overhaul      Inspection &

Period        Check Period

Ice and Rain Protection,

Chapter 30                       12,000

Ammeter, Deicing                     8,000

Control Windshield Temperature       3,000

Control Panel A.C.                   3,000

Deicer Fixed Installation and

Lines                            12,000

Deicer Boots                        O.C.

Deicing Cycling Timer               O.C.

Ejector, Deicer Boot Assembly        5,000

Gauge, Deicing Suction               5,000

Gauge, Deicing Pressure              5,000

Voltmeter A.C.                       7,000

Valve Suction Relief                 2,000

Windshield Wiper Assembly           O.C.

Instruments, Chapter 31             12,000

May be determined by the assigned

inspector.

Landing Gear, Chapter 32            10,000

Nose Landing Gear Assembly          10,000

Attach Points                       10,000

Under Carriage Main Gear            10,000

Drag Strut Main Gear                10,000

Lock Strut Main Gear                10,000

Brake Assembly                      O.C.

Anti-skid Device                       750

Cable Nose Gear Retract             O.C.

Nose Gear Fork                      10,000

Nose Gear Strut                     10,000

Indicator, Landing Gear Position    10,000

Nose and Main Wheels                O.C.

Main Gear Retract Strut              5,000

Uplock Main Gear                     5,000

Nose Gear Actuator                   2,000

Nose Gear Uplock                     2,000

Nose Gear Steering Actuator          1,500

Valve Steering Shutoff               3,000

Valve Steering Followup              1,500

Valves Pressure Reducing             2,500

Valve, Selector Landing Gear         3,000

Valve, Selector Solenoid Landing

Gear                              1,500

Valve, Brake                         1,500

Valve Brake Emergency                3,000

Effective date _____________________

PAGE 4 of 7 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAIRCHILD F-27

Overhaul      Inspection &

Period        Check Period

Landing Gear, Chapter 32 (continued)

Valve Rapid Exhaust                  1,500

Gearbox Nose Gear Steering           4,000

Nose Gear Centering Cylinder         1,000

Nose Gear Air Motor                  2,500

Actuator Main Gear Uplock            6,000

Actuator Nose Gear Uplock            2,000

Gauge, Brake Pressure                6,000

Hydraulic Pressure Relief Valve      5,000

Hydraulic Pressure Switch            5,000

Hydraulic Solenoid Valve             5,200

Hydraulic Pump and Motor             5,000

Relay Hydraulic Steering             3,000

Rectifier                             OC

Lights, Chapter 33                  12,000

May be determined by the assigned

inspector.

Navigation, Chapter 34              12,000

May be determined by the assigned

inspector.

Oxygen, Chapter 35                  12,000

Oxygen Bottle                         *

Pneumatic System, Chapter 36        12,000

Air Compressor                       1,400

Bottles                               *

Inspect for Corrosion             1 year

Chemical Dryer Housing               4,300

Gauge, Pneumatic Brake Pressure      5,000

Gauge, Pneumatic Emergency Pressure  5,000

Gauge, Primary Pressure              5,000

Separator, Moisture                  1,500

Switch High Pressure Cutoff          1,500

Unloader                             1,500

Valve Pressure Reduction (1000-100)  1,500

Valve Isolation                      3,000

Valve Back Pressure                  2,000

Valve Manual Discharge               3,000

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date _____________________

Page 5 of 7 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAIRCHILD F-27

Overhaul      Inspection &

Period        Check Period

Doors, Chapter 52                   12,000

Doors, Pax and Cargo                 6,000

Emergency Exits                     12,000

Retract Cylinder Cabin Door          5,000

Valve Pressure Reducing              3,000

Fuselage, Chapter 53                12,000

Attach Points                       12,000

Exterior Covering                   12,000

Interior Structure                  12,000

Nose Cap Attach Points              12,000

Belly Interior Overhaul              6,000

Belly Interior, Lavatory and

Galley                            3,600

Nacelles, Chapter 54                12,000

Interior Structure                  12,000

Exterior Covering                   12,000

Stabilizers, Chapter 55             12,000

Dorsal Fin Structure                12,000

Vertical Stabilizer and

Installation                     12,000

Horizontal Stabilizer and

Installation                     12,000

Windows, Chapter 56                 12,000

Windshield Assembly and

Installation                     12,000

Windows                             12,000

Wings, Chapter 57                   12,000

Outer Section

Interior Structure                  12,000

Exterior Covering                   12,000

Control Hinge Points                12,000

Flap Track and Installation         12,000

Center Section

Exterior Covering                   12,000

Interior Structure                  12,000

Fuselage Attach Points              12,000

Flap Tracks and Inst.               12,000

Cables, Pulleys and Fairleads       O.C.

Effective date _____________________

Page 6 of 7 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAIRCHILD F-27

Overhaul      Inspection &

Period        Check Period

Propellers, Chapter 61

Propeller                            2,600

Spinner                              2,600

Propeller Control Unit               4,100

Feathering Pump                      4,200

Alternator Prop Control              1,500

Corrector Motor                      2,000

Propeller Brake                      1,000

Propeller Controls and Installation  2,600

Powerplant General, Chapter 71

Engine Mount                         3,000

Magnaflux                     6,000

Cowling and Installation             3,000

Engine, Chapter 72

Air Intake Assembly                  3,000

Engine                               3,000 *

* Sample one hot section inspection at 2000 hours, one engine

overhaul at 2400 hours and one engine overhaul at 2700 hours.

Engine Fuel and Control, Chapter 73

Fuel Control Unit                    3,000

Fuel Pump                            3,000

Fuel System (Nacelle Forward

Firewall)                         3,000

Fuel Trimmer Actuator                3,000

Indicator, Fuel Flow Dual            5,000

Indicator, Fuel Pressure Dual        8,000

Indicator, Fuel Trim                 7,500

Transmitter Fuel Pressure            3,800

Transmitter Fuel Flow                1,900

Transmitter Fuel Trimmer Position    7,000

Engine Controls, Chapter 76

Engine Controls and Installation     3,000

Cables, Pulleys and Fairleads       O.C.

Controls (Nacelle Aft Firewall)     12,000

Pedestal (cockpit)                  12,000

Engine Indicating, Chapter 77

Generator Tachometer                 5,000

Indicator Tachometer                 5,000

Effective date _____________________

Page 7 of 7 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAIRCHILD F-27

Overhaul      Inspection &

Period        Check Period

Engine Indicating, Chapter 77

continued

Indicator, Tail Pipe Temperature     7,500

Indicator, Torque Pressure           7,500

Transmitter Torque Pressure          3,000

Exhaust, Chapter 78

Exhaust Tail Pipe                    3,000

Oil System, Chapter 79

Oil Radiator and Installation        3,000

Indicator Oil Pressure Dual          7,500

Indicator Oil Temperature Dual       5,000

Switch Oil Pressure Warning          7,000

Transmitter Oil Pressure             7,000

Starting, Chapter 80

Ignition Harness Assembly            3,000

Igniter                              3,000

Starter                              3,000

Starter Relay                        1,500

Water Injection, Chapter 82

W/M Tank and Installation           6,000

W/M Control Unit                    3,000

W/M System (Nacelle Aft Firewall)   6,000

W/M Pump                            3,000

W/M Filter                            600

W/M Pressure Warning Switch         6,000

W/M Tank Indicator                  5,000

W/M Valves Electrical and Manual   12,000

Accessory Gearbox, Chapter 83

Gearbox                              2,200

Drive Shaft                          1,400

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 26.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- CONVAIR CV-990

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

OPERATIONS SPECIFICATIONS

PART D                                        Page 1 of 11 Pages

AIRCRAFT MAINTENANCE

CONVAIR CV-990

Overhaul      Inspection &

Period       Check Period

Air Conditioning, Chapter 21        12,500

Controller, Cabin Pressure           6,000

Condenser, Conditioned Air

Modulating                        5,000

Fan, Electronic Equipment Cooling    6,000

Fan, Freon Pack Condensor            6,000

Fan, Recirculating                   6,000

Indicator, Cabin Compartment Air

Flow                             10,000

Indicator, Cabin Temperature        10,000

Indicator, Turbo Compressor Bearing

Temperature                      10,000

Indicator, Turbo Compressor RPM     10,000

Heater, Electric Flight Deck Air     6,000

Heater, Cabin Air                    6,000

Pack, Freon Refrigeration            5,000

Sensor, Conditioned Air Temperature  5,000

Turbo Compressor                     3,000

Valve, Air Turbine Drive-Shutoff     5,000

Valve, Condenser Air Ground Shutoff 10,000

Valve, Outflow Cabin Pressure        3,000

Valve, Ram Air Shutoff              10,000

Auto Pilot, Chapter 22              12,500

Accelerometer - Linear, Horizontal

and Vertical                      5,000

Amplifier, Servo Auto Pilot          5,000

Computer, Automatic Cutoff           5,000

Computer, Yaw Command                5,000

Computer, Pitch Command              5,000

Computer, Roll Command               5,000

Computer, Pressure                   5,000

Controller, Auto Pilot               5,000

Coupler, Trim                        5,000

Drum-Servo Bracket                   6,000

Indicator, Trim                      5,000

Rack Assy., Gain Calibrator & Relay  5,000

Rack, Stabilization Computer         5,000

Relay, Trim Valve Solenoid Control

& Cockpit                         5,000

Servo & Drive - Aileron & Rudder     6,000

Servo & Drive - Elevator             6,000

Communications, Chapter 23          12,500

May be determined by the assigned

inspector.

Effective date _____________________

PAGE 2 of 11 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

CONVAIR DC-990

Overhaul      Inspection &

Period        Check Period

Electrical Power, Chapter 24        12,500

Ammeters, A.C. & D.C.               10,000

Battery                               OC

Constant Speed Drive                 1,500

Contactor, External Power           10,000

Contactor, Line and Bus Tie          6,000

Contactor, Load Reduction            6,000

Controller, C.S.D. Load             10,000

Frequency Meter                     10,000

Generator                            2,000

Panel, Control                       6,000

Panel, Sync, Bus Protector           6,000

Relay, A.C. Monitor, Pilot's

Essential Bus                     6,000

Relay, A.C. 28 v. Lighting Transfer  6,000

Relay, Essential D.C. Bus Connector  6,000

Relay, Phase Sequence                6,000

Relay, Power Failure Detector        6,000

Relay, Reverse Current               6,000

Relay, Tie Control                   6,000

Relay, Tow Power Contactor Transfer  6,000

Relay, 28 v D.C. Battery             6,000

Static Exciter                       6,000

Transformer - Rectifier - Battery

Charger                           6,000

Voltmeters, A.C. & D.C.             10,000

Wattmeter, A.C.                     10,000

Equipment and Furnishings,

Chapter 25                       12,500

Evacuation Slides                   6 Mos.

Fire Protection, Chapter 26         12,500

Agent Container & Actuator Assy.      *

Cartridge                           3 years replace

Control Box, Fire & Overheat

Warning Alarm Bell                5,000

Fire Extinguisher - Hand (CO2)        *

Fire Extinguisher - Hand (Water)    5 years

Valve, Three Way                    10,000

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Flight Controls, Chapter 27         12,500

Actuator, Flap Control - Inboard

& Outboard                       12,500

Actuator, Horizontal Stabilizer

Trim                             10,000

Actuator, Inboard and Outboard

Spoiler Deactivation              8,000

Actuator, Leading Edge Flap         10,000

Actuator, Outboard Spoiler           6,000

Effective date _____________________

Page 3 of 11 Pages

AIRCRAFT MAINTENANCE

CONVAIR CV-990

Overhaul      Inspection &

Period       Check Period

Flight Controls, Chapter 27

(continued)

Amplifier, Speed Stability

Augmentation                      5,000

Computer, Mach. Sensor and

Transmitter                       5,000

Control Package, Rudder Linkage     10,000

Control Unit - Horizontal

Stabilizer Trim                  10,000

Cylinder, Inboard Spoiler           10,000

Cylinder, Rudder Power               5,000

Cylinder, Rudder Tab Locking        10,000

Damper, Aileron Flutter              5,000

Damper, Aileron Flight Tab Flutter   5,000

Damper, Aileron Gust                10,000

Damper, Elevator Gust               10,000

Damper, Elevator Flutter             5,000

Damper, Elevator Flight Tab Flutter  5,000

Elevator Crossover Tube (Fwd)       12,500

Flap Asymmetry Unit                  8,000

Jack, Rudder Trim Tab               10,000

Jack, Rudder Flight Trim Tab        10,000

Indicator, Flap Position            10,000

Indicator, Longitudinal Trim

Position                         10,000

Motor, Electric, Stabilizer Emer.

Trim                             10,000

Motor, Flap Main Drive Gearbox      12,500

Power Supply - Speed Stability

Augmentation                      5,000

Quadrant, Irreversible Aileron

Spoiler Control                  12,500

"Q" Cylinder Rudder Feel            12,500

Restrictors - Leading Edge Flap     12,500

Spoiler Mixer Installation          12,500

Switch, Leading Edge Flap Pressure   5,000

Swivels, Leading Edge Flap

Actuator Flex Line               10,000

Switch, Rudder Hydraulic Pressure   10,000

Switch, Trim Rate Limit              5,000

Solenoid, Flap Position              5,000

Solenoid, Trim Rate Limit            5,000

Spring, Horizontal Stabilizer Trim

Control Centering                10,000

T Box Assembly - Inboard & Outboard

Flap                             12,500

Valve, Flap Control Servo           12,500

Valve, Flap Control Check           12,500

Valve, Flap Phase Shutoff           12,500

Valve, Inboard & Outboard Spoiler

Servo                            12,500

Valve, Leading Edge Flap Control    12,500

Valve, Power Rudder Servo           10,000

Valve, Rudder Power Limiting Relief 10,000

Valve, Rudder Shutoff                5,000

Effective date _____________________

Page 4 of 11 Pages

AIRCRAFT MAINTENANCE

CONVAIR CV-990

Overhaul      Inspection &

Period       Check Period

Flight Controls, Chapter 27

(continued)

Valve, Rudder Emergency & Auto

Pilot Shutoff                    10,000

Valve, Stabilizer Hydraulic

Emergency & A/P Shutoff          10,000

Valve, Stabilizer Trim Control       5,000

Fuel System, Chapter 28             12,500

Hose, Fire Resistant Flexible        5,000

Impellor Assy., Pump, Hyd., Boost

and Jettison                     10,000

Indicator, Fuel Quantity            10,000

Indicator, Fuel Temperature         10,000

Manifold, Center Section Refuel     12,500

Motor, Hyd., Pump, Boost and

Jettison                          2,500

Pump, Electric, Boost & Transfer    10,000

Valve, Fuel Boost Control            5,000

Valve, Motor Actuated Crossfeed

Gate                              5,000

Valve, Motor Actuated Shutoff

Emergency                        10,000

Valve, Shutoff Fuel Jettison         5,000

Valve, Fuel Boost Control            5,000

Pump, Wing Tank Jettison            10,000

Hydraulic System, Chapter 29        12,500

Accumulator, Main                    8,000

Filter, Hydraulic Pump Case Drain

Line                              8,000

Filter, Low Pressure, Pump Supply

Line                              8,000

Filter, Main System High Pressure    8,000

Indicator, Hydraulic Pressure       10,000

Pump, Engine Driven Hydraulic        1,500

Transmitter, Hydraulic Pressure      8,000

Valve, Check Relief                 10,000

Valve, Hydraulic Firewall Shutoff   10,000

Valve, 125 psi Hydraulic Check       5,000

Pump, Hydraulic Inlet Booster Motor  7,500

Ice and Rain Protection,

Chapter 30                       12,500

Actuator, Pneumatic Rain Clearing    6,000

Ammeter, Empennage De-Ice           10,000

Controller, Defog, Sliding Window

A/1                               8,000

Controller, Empennage De-Ice         8,000

Controller, Temperature & De-Fog,

Pilot's Aft Window W/1            8,000

Control Box Assy., Bleed Air Duct

Overheat Detector, Wing and

Fuselage                          5,000

Control Box, Center Windshield

Anti-Ice                          8,000

Control Box, Side Window Anti-Ice

Temperature                       8,000

Effective date _____________________

PAGE 5 of 11 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

CONVAIR CV-990

Overhaul      Inspection &

Period        Check Period

Ice and Rain Protection, Chapter 30

(continued)

Control Box, Structural Anti-Ice

Overheat Warning                  5,000

Control Box, Structural Overheat

Valve                             6,000

Control Box, Windshield Heat

Temperature                       8,000

Detector, Ice Warning, Engine        6,000

Valve, Anti-Icing Bleed Air Pressure

Regulator                         5,000

Valve, Rain Cleaning Actuator

Solenoid                          6,000

Valve, Relief, Pressure Differential 6,000

Valve, Windshield Rain Removal

Shutoff                           6,000

Instruments, Chapter 31             12,500

May be determined by the assigned

inspector.

Landing Gear, Chapter 32            12,500

Accumulator, Brake                  10,000

Adjuster Assy., Hydraulic Brake,

Nose and Main Gear                5,000

Bottle, Emergency Air Brake           *

Cylinder, MLG Positioner Assembly    3,000

Drive Assy., NLG Anti-Skid Detector  7,500

Indicator, Brake Pressure           10,000

Lever, Landing Gear Control         10,000

Solenoid, Lever Lock                 5,000

Switch, MLG Extend Pressure          5,000

Tires, Nose and Main                  OC

Transmitter, Brake Pressure          5,000

Valve, MLG Emergency Brake Selector  5,000

Wheel Assy., Nose and Main Gear     8 months

Lights, Chapter 33                  12,500

May be determined by assigned

inspector.

Navigation, Chapter 34              12,500

May be determined by assigned

inspector

Oxygen System, Chapter 35           12,500

Cylinder, Oxygen (Supply)             *

Cylinder, Oxygen, Portable and

Equipment                          *

Masks, Crew                          5,000

Masks, Oxygen (Crew Portable)        7,500

Regulator, Diluter Demand            6,000

Valve, Auto Opening & Continuous

Flow Regulator                    6,000

Valve, Oxygen Cylinder              5 years

Valve, Pressure Reducer              6,000

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date _____________________

Page 6 of 11 Pages

AIRCRAFT MAINTENANCE

CONVAIR CV-990

Overhaul      Inspection &

Period       Check Period

Pneumatic, Chapter 36               12,500

Indicator, Bleed Air Pressure       10,000

Transmitter, Bleed Air Pressure      8,000

Valve, Bleed Air Pressure Regulator

Shutoff                           6,000

Water/Waste, Chapter 38             12,500

Pump, Water System Air Compressor,   5,000

Valve, Manual Pressure Release       5,000

Valve, Water System Pressure Relief  6,000

Valve, Aft Drain                     5,000

Valve, Remote Control (Fwd Drain)    5,000

Valve, Check, Potable Water System   5,000

Powerplant General, Chapter 71      O.C.

Engine Mounts, Forward and Aft

Links and Bolts                  E.O.

Engine, Chapter 72                  O.C.

Compressor Section                   2,000 *

Turbine Section                      1,500 *

* Sample one turbine section at

1200 hours, one compressor

section at 1600 hours, and one

compressor section at 1800

hours.

Engine Fuel and Control,

Chapter 73                       O.C.

Actuator, Inlet Guide Vanes         E.O.

Control, Engine Fuel                E.O.

Heater, Fuel                        E.O.

Indicator, Fuel Flow                 5,000

Pump, Engine Fuel                   E.O.

Sensor, Compressor Inlet

Temperature                      E.O.

Switch, Fuel Pump Low Pressure

Warning                          12,000

Transmitter, Fuel Flow               5,000

Valve, Pressurization and Dump      E.O.

Ignition System, Chapter 74         O.C.

Cables                              E.O.

Igniter Plugs                          500

Igniter Unit                        E.O.

Engine Air, Chapter 75              O.C.

Switch, Engine Anti-Icing Air

Pressure                         12,000

Valve, Bleed Air Pressure Regulator

and Check                         6,000

Valve, Engine Anti-Icing            E.O.

Valve, Engine Inlet Anti-Icing

Pressure Regulator and Shutoff    3,000

Effective date _____________________

Page 7 of 11 Pages

AIRCRAFT MAINTENANCE

CONVAIR CV-990

Overhaul      Inspection &

Period       Check Period

Engine Air, Chapter 75 (continued)

Valve, Engine Anti-Icing            E.O.

Valve, Shutoff, 1-Inch Bleed Air

Ejector                          E.O.

Engine Controls, Chapter 76         O.C.

Cable Tension Regulator             10,000

Engine Torque Box                   E.O.

Pylon Torque Box                     5,000

QEC Cables and Conduits             E.O.

Engine Indicating, Chapter 77       O.C.

Amplifier, AVM                       5,000

Detectors, AVM                      E.O.

Generator, Engine Tachometer        E.O.

Generator, Fan Tachometer           E.O.

Indicator, AVM                      10 months

Indicator, Engine Pressure Ratio     8,000

Indicator, Engine Tachometer         7,500

Indicator, Exhaust Gas Temperature   5,000

Indicator, Fan Tachometer            7,500

Transducer, Engine Pressure Ratio   E.O.

Exhaust System, Chapter 78          O.C.

Actuator and Linkage, Thrust

Reverser                         E.O.

Blocker Door Assy., Thrust

Reverser                         E.O.

Blucket Guard Assy., Thrust

Reverser                         E.O.

Interlock Valve, Thrust Reverser    E.O.

Latch Actuator, Thrust Reverser     E.O.

Metering Valve, Thrust Reverser     E.O.

Pump, Thrust Reverser               E.O.

Selector Valve, Thrust Reverser     E.O.

Oil System, Chapter 79              O.C.

Cooler, Main Oil and Constant

Speed Drive                      E.O.

Indicator, Engine Oil Temperature   10,000

Indicator, Engine Oil Pressure      10,000

Indicator, Oil Quantity              6,000

Oil Tank                            E.O.

Tank Unit                           10,000

Transmitter, Engine Oil Pressure     8,000

Switch, Low Pressure Warning        12,000

Engine Starting, Chapter 80         O.C.

Starter, Air Turbine                 3,000

Valve, Starter Air Regulating and

Shutoff                           3,000

Effective date _____________________

Page 8 of 11 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

CONVAIR CV-990

Structural Inspection Program

The aircraft structure is divided into zones and a detailed

inspection time limitation is listed for each zone.  The

inspection of the zone shall include all areas of structure,

components, and appliances unless a specific time limit is listed

for a particular item.  Sample items are identified with the

suffix "S" and will be accomplished on 1/5 of the fleet.

Overhaul      Inspection &

Zone    Period        Check Period

Doors, Chapter 52                   12,500

Electronics Access Door     12       2,500 S

Forward Baggage Door        13.1     2,500 S

Rear Baggage Door           15.1 &   2,500 S

15.2

Forward Entry Door          31.1     2,500 S

Forward Galley Door         34.1     2,500 S

Rear Entry Door             43.1     2,500 S

Rear Galley Door            44.1     2,500 S

Emergency Exit              36.1 &   2,500 S

37.1

Fuselage, Chapter 53                12,500

Radome                      1        2,500 S

Under Wing Bay L.H. & R.H.  3 & 4    5,000

FS 670-870

MLG Well, Inboard Sect.     5.1 &   12,500

FS 87-964                6.1

MLG Well, Outboard Sect.    5.2 &    5,000

6.2

Under Floor, Nose Sect.     11       2,500 S

FS 187-250

Electronic & Electrical     12       2,500 S

Compartment FS 250-375

Forward Baggage Compartment 13       2,500 S

FS 375-622

Air Conditioning            14       2,500 S

Compartment FS 622-678

Rear Baggage Compartment    15       2,500 S

FS 1040-1344

Under Floor, Aft Sect.      16       2,500 S

FS 1344-1487

Flight Deck & Fwd. of Inst. 20 thru  2,500 S

Panel FS 152-301         25

Control Pedestal            22       2,500 S

Flight Engineers Station    24       2,500 S

R.H. FS 250-301

Fuselage, Cabin             31 thru  2,500 S

FS 301-1437              48

Forward Entry Area          31       2,500 S

FS 301-375

Lavatory "A" FS 301-341     32       2,500 S

Lavatory "B" FS 341-384     33       2,500 S

Effective date _____________________

Page 9 of 11 Pages

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

CONVAIR CV-990

Overhaul      Inspection &

Zone    Period        Check Period

Fuselage, Chapter 53

(continued)

Forward Galley Area         34       2,500 S

FS 384-482

Forward Cabin Area L.H.     35       2,500 S

FS 362-482

Forward Cabin Area R.H.     36       2,500 S

FS 482-964

Forward Cabin Area L.H.     37       2,500 S

FS 482-964

Floor and Seat Tracks                5,000

Overwing Area Below Floor   39       2,500 S

FS 678-964

Aft Cabin Area L.H.         41       2,500 S

FS 964-1344

Aft Cabin Area R.H.         42       2,500 S

FS 964-1325

Rear Entry Area             43       2,500 S

FS 1344-1422

Rear Galley Area            44       2,500 S

FS 1325-1422

Lavatory "C" & "D"          47 & 48  2,500 S

FS 1422-1487

Aft Fuselage FS 1487-1640   51       2,500 S

Tail Cone FS 1640-1717      55       2,500 S

Nacelles/Pylons, Chapter 54         12,500

Pylon, #1 Engine            75       5,000

Pylon, #2 Engine            76       5,000

Pylon, #3 Engine            77       5,000

Pylon, #4 Engine            78       5,000

Stabilizers, Chapter 55             12,500

Trailing Edge, Horizontal   52.0 &   2,500

Stabilizer               53.0

Trailing Edge, Horizontal   52.1 &   2,500

Stabilizer               53.1

Trailing Edge, Horizontal   52.2 &   2,500

Stabilizer               53.2

Trailing Edge, Horizontal   52.3 &   5,000

Stabilizer               53.3

Trailing Edge, Horizontal   52.4 &   2,500

Stabilizer               53.4

Trailing Edge, Horizontal   52.5 &   2,500

Stabilizer               53.5

Tip, Horizontal Stabilizer  52.6 &   2,500 S

53.6

Torque Box, Center to Rear  52.7 &   1,000

Spar                     53.7

Torque Box, Center to Rear  52.8 &   2,500 S

Spar                     53.8

Torque Box, Center to Rear  52.9 &   1,000

Spar                     53.9

Torque Box, Center to Rear  52.10 &  2,500 S

Spar                     53.10

Torque Box, Front to Center 52.11 &  5,000

Spar                     53.11

Torque Box, Front to Center 52.12 &  2,500 S

Spar                     53.12

Torque Box, Front to Center 52.13 &  2,500 S

Spar                     53.13

Torque Box, Front to Center 52.14 &  2,500 S

Spar                     53.14

Leading Edge Stub           52.15 &  2,500

53.15

Leading Edge, Horizontal    52.16 &  2,500

Stabilizer               53.16

Elevator and Tabs           56.1 &   2,500 S

57.1

Torque Box, Vertical Fin    54.1     5,000

Torque Box, Vertical Fin,   54.2     2,500 S

Center to Rear Spar

Effective date _____________________

Page 10 of 11 Pages

AIRCRAFT MAINTENANCE

CONVAIR CV-990

Overhaul      Inspection &

Zone     Period       Check Period

Stabilizers, Chapter 55

(continued)

Torque Box, Vertical Fin,   54.3     2,500

Center to Rear Spar

Torque Box, Vertical Fin,   54.4     2,500 S

Front to Rear Spar

Torque Box, Vertical Fin,   54.5     2,500 S

Front to Rear Spar

Torque Box, Vertical Fin,   54.6     2,500 S

Front to Rear Spar

Trailing Edge, Vertical Fin 54.7     5,000

Trailing Edge, Vertical Fin 54.8     1,000

Trailing Edge, Vertical Fin 54.9     5,000

Trailing Edge, Vertical Fin 54.10    1,000

Trailing Edge, Vertical Fin 54.11    5,000

Trailing Edge, Vertical Fin 54.12    1,000

Trailing Edge, Vertical Fin 54.13    5,000

Trailing Edge, Vertical Fin 54.14    1,000

Trailing Edge, Vertical Fin 54.15    5,000

Trailing Edge, Vertical Fin 54.16    1,000

Trailing Edge, Vertical Fin 54.17    5,000

Trailing Edge, Vertical Fin 54.18    1,000

Trailing Edge, Vertical Fin 54.19    1,000

Dorsal - Vertical Fin       54.20    5,000

Leading Edge, Vertical Fin  54.21    2,500

Tip, Vertical Fin           54.22    2,500 S

Rudder and Tabs             58.1     2,500 S

Remove and Inspect Vertical

Stabilizer

Attach Bolts                      5,000

Windows, Chapter 56

Cockpit Sliding Windows     21 & 23  2,500 S

Mechanism

Flight Deck Windshields     21, 22   1,000

& 23

Wings, Chapter 57                   12,500

Tip, Wing                   61 & 68  2,500 S

Leading Edge, Wing,         62.1 &   2,500 S

Outboard                 67.1

Leading Edge, Wing,         63.1 &   2,500 S

Intermediate             66.1

Leading Edge, Wing,         64.2 &   2,500 S

Inboard                  65.2

Leading Edge, Wing, Stub    64.1 &   1,000

65.1

Flaps, Leading Edge         1 thru   2,500 S

8

Fillet, Wing                69.1 &   2,500 S

69.2

Tank, #1 Main               81.1     2,500 S

thru 81.7

Tank, #2 Main               82.5     2,500 S

thru 82.8

Tank, #3 Main               83.5     2,500 S

thru 83.8

Effective date _____________________

Page 11 of 11 Pages

AIRCRAFT MAINTENANCE

CONVAIR CV-990

Overhaul      Inspection &

Zone     Period       Check Period

Wings, Chapter 57

(continued)

Tank, #4 Main               84.1     2,500 S

thru 84.7

Tank, #1 Aux.               85.1     2,500 S

thru 85.6

Tank, #2 Aux.               82.1     2,500 S

thru 82.4

Tank, #3 Aux.               83.1     2,500 S

thru 83.4

Tank, #4 Aux.               89.1     2,500 S

thru 89.6

Fuel Cell, Wing Center      87       2,500 S

Section

Trailing Edge, Wing,        91 & 98  2,500 S

Outboard

Trailing Edge, Wing,        92.3 &   2,500 S

Outboard                 97.3

Trailing Edge, Wing,        92.4 &   1,000

Outboard                 97.4

Trailing Edge, Wing,        92.5 &   2,500

Outboard                 97.5

Trailing Edge, Wing,        92.6 &   1,000

Outboard                 97.6

Trailing Edge, Wing,        92.7 &   1,000

Outboard                 97.7

Trailing Edge, Wing,        92.8 &   1,000

Outboard                 97.8

Trailing Edge, Wing,        92.9 &   2,500

Outboard                 97.9

Trailing Edge, Wing,        93.2 &   1,000

Intermediate             96.2

Trailing Edge, Wing,        93.3 &   2,500

Intermediate             96.3

Trailing Edge, Wing,        93.4 &   1,000

Intermediate             96.4

Trailing Edge, Wing,        93.5 &   1,000

Intermediate             96.5

Trailing Edge, Wing,        93.6 &   2,500

Intermediate             96.6

Trailing Edge, Wing,        93.7 &   1,000

Intermediate             96.7

Trailing Edge, Wing         93.8 &   2,500

Aileron Balance Bay      96.8

Trailing Edge, Wing         93.9 &   2,500

Aileron Balance Bay      96.9

Trailing Edge, Wing         93.10 &  2,500

Aileron Balance Bay      96.10

Trailing Edge, Wing,        94.3 &   1,000

Inboard                  95.3

Trailing Edge, Wing,        94.4 &   2,500

Inboard                  95.4

Trailing Edge, Wing,        94.5 &   1,000

Inboard                  95.5

Trailing Edge, Wing,        94.6 &   1,000

Inboard                  95.6

Trailing Edge, Wing,        94.7 &   2,500

Inboard                  95.7

Trailing Edge, Wing,        94.8 &   1,000

Inboard                  95.8

Flap, Outboard              92.1 &   2,500 S

97.1

Flap, Inboard               94.1 &   2,500 S

95.1

Spoiler, Outboard           92.2 &   2,500 S

97.2

Spoiler, Inboard            94.2 &   2,500 S

95.2

Aileron                     93.1 &   2,500 S

96.1

Anti-Shock Body, Outboard   100 &    2,500 S

103

Anti-Shock Body, Inboard    101 &    2,500 S

102

Effective date _____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 27.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- JET COMMANDER 1121

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

JET COMMANDER 1121

Page 1 of 11

Thorough checks shall be accomplished in accordance with the

applicable procedures as listed in ABC Airlines' Maintenance

Manual.

Preflight (P.F.) shall be accomplished each service calendar day.

Inspection shall be in accordance with the applicable procedures

listed in ABC Airlines' Maintenance Manual.

Station Check (S.C.) shall be accomplished at basic intervals of

90 hours time in service.  Inspection shall be in accordance with

applicable procedures listed in ABC Airlines' Maintenance Manual.

During initial operation, the basic intervals for station checks

will be evaluated in the following manner:

Ten inspections at 75 hours.*

Periodic Inspection (P.I.) shall be accomplished at intervals not

to exceed 175 hours time in service.  Inspection shall be in

accordance with the applicable procedures listed in ABC Airlines'

Maintenance Manual.  During initial operation, the basic

intervals for periodic inspections will be evaluated in the

following manner:

Five inspections at 150 hours.*

* Note - Upon termination of the evaluation period, the

assigned FAA maintenance and avionics inspectors will

review the maintenance inspection findings and the

operating history.  If satisfactory, the carrier will

be authorized to continue at the time established for

the subsequent stage, i.e.,

Station Check - 90 hours

Periodic Inspection - 175 hours

Overhaul times as listed in hours and years are maximum limits of

whichever occurs first.

Aircraft shall not be utilized in air carrier or commercial

operations unless:

a.   The aircraft and its component parts, accessories, and

appliances are maintained in an airworthy condition in

accordance with the schedule of maintenance and

inspection functions and procedures set forth in the

operator's maintenance manual.

b.   OC "On Condition" items will be maintained in

continuous airworthiness condition by periodic and

progressive inspections, checks, services, repair

and/or preventive maintenance and are appropriately

described in the operator's maintenance manual.

c.   Parts or sub-components, not listed below, will be

checked, inspected and/or overhauled at the same time

limits specified for the component or accessory to

which such parts or sub-components are related.

Effective date _____________________

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

JET COMMANDER 1121

Page 2 of 11

Abbreviations used in the Jet Commander maintenance

specifications are defined as follows:

FC  -  Indicates "Functional Check"

BC  -  Indicates "Bench Check"

EO  -  Indicates "Engine Overhaul"

EC  -  Indicates "Engine Change"

OC  -  Indicates "On Condition"

R&R -  Indicates "Remove and Replace" in accordance

with factory recommendations

HYD -  Indicates "Hydrostatic Test"

C   -  Indicates "Calibration"

Effective date _____________________

OPERATIONS SPECIFICATIONS

Page 3 of 11

AIRCRAFT MAINTENANCE

JET COMMANDER 1121

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS or YRS.    P.F     S.C.    P.I.    OTHER

Air-Conditioning,

Chapter 21      10,000     5      X       X       X

Controller-Cabin

Pressure         5,000    2.5                     X

Indicator-Rate of

Climb            4,000     2                      X  C 2000/1yr

Indicator-Alt. &

Diff. Pressure   4,000     2                      X  C 2000/1yr

Turbine-Cooling    5,000    2.5                     X

Separator-Water   OC                                X

Regulator-

Absolute

Pressure         5,000    2.5                     X  FC 4-PI

Filter-Cabin Air  OC        --                      X  R&R 4-PI

Valve-Bleed Air

Flow Control     4,000     2                      X

Valve-Bleed Air

Shutoff          5,000    2.5                     X

Valve-Bleed Air

Check            5,000    2.5                        4-PI

Valve-Emer. Air

Pressure Regulator

Shutoff          5,000    2.5                     X  FC 4-PI

Valve-Outflow      2,000     1                      X

Auto-Pilot,

Chapter 22*     10,000     5      X       X       X

Pedestal

Controller         OC                             X  BC/C 2,000

Computer

Amplifier       OC                                X  BC  1,000

Servos             2,000     2                      X

Trim Coupler       5,000    2.5                     X

Sensing Unit       2,000     2                      X

Rate Gyro          2,000     2                      X

Emergency

Disconnect       5,000    2.5                     X

Altitude

Controller       2,000     2                      X

Servo Mount        2,000     2                      X

Vertical Reference 2,000     2                      X

Communications,

Chapter 23

May be determined

by assigned

inspector.

*  Applies to

Collins auto

pilot.

Effective date

PAGE 4 of 11 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

JET COMMANDER 1121

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS or YRS.    P.F.    S.C.    P.I.    OTHER

Electrical,

Chapter 24      10,000     5      X       X       X

Ammeter, AC         OC                              X  C 2,000

Ammeter, DC         OC                              X  C 2,000

Volt Meters AC/DC   OC                                 C 2,000

Battery N/C         OC              X       X       X

DC Bus & Con-

tactor Box        OC                              X  F C 2,500

AC Control Panel   5,000    2.5                     X

DC Control Panel

Regulator        5,000    2.5                     X

AC Converter

Regulator        2,000     2                      X

Current Trans-

formers           OC                              X

AC Generator        EO

DC Starter

Generator         EO

Equipment &

Furnishings,

Chapter 25

May be determined

by assigned

inspector.

Fire Protection,

Chapter 26      10,000     5      X       X       X

Containers          *                       X       X        *

Detector Control   2,000     1                      X

Relay               OC                              X

Heat Sensing

Units             OC                              X

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Flight Controls,

Chapter 27      10,000     5      X       X       X

Speed Brake &

Control-

Actuator         2,000    2.5     X       X       X

Flap Controls-

Actuator         2,000    2.5     X       X       X

Gust Lock and

Controls          OC              X       X       X

Stabilizer-

Installation      OC              X       X       X

Flap Torque Tube  10,000     5      X       X       X   Note 1

Valve-Flap

Control         10,000     5      X       X       X   Note 1

Valve-Speed Brake 10,000     5      X       X       X   Note 1

Trim Actuators     4,000     2      X       X       X  BC 2,000

Fuel, Chapter 28  10,000     5      X       X       X

Cells               OC              X       X       X   R&R

Boost-Pump AC      4,000     2      X       X       X

Boost-Pump DC      8,000     4      X       X       X   Note 2

Fuel Quantity

Indication

System            OC                              X   C 1,000

Compensator Fuel

Temp.             OC                              X   C 1,000

Effective date _____________________

PAGE 5 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

JET COMMANDER 1121

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS or YRS.    P.F.    S.C.    P.I.    OTHER

Hydraulic,

Chapter 29      10,000     5      X       X       X

Pump Emergency     2,000    2.5     X       X       X

Pump Engine Driven  EO              X       X       X

Regulator-Air-

Pressure         4,000     4                      X

Valve-Reservoir

Relief           4,000     4                      X

Accumulator-

Emergency         4,000     4              X       X

Accumulator-

Regulator        4,000     4              X       X

Primary

Filters - Pressure  OC                              X  R&R 4-PI

Valve-Thermal

Relief-Emergency 4,000     4      X       X       X

Reservoir Air

Filters           OC                                 Note 3

Ice and Rain,

Chapter 30      10,000     5      X       X       X

Boots               OC      2.5     X       X       X

Regulator           OC      2.5             X       X

Valve Distributor   OC      2.5             X       X

Instruments,

Chapter 31

May be determined

by assigned

inspector.

Landing Gear,

Chapter 32      10,000     5      X       X       X

Wheels              OC              X       X       X  Zyglo

wheels ea.

tire ch.

Brakes              OC              X       X       X

Anti-Skid-Control

Units             OC       5                      X  Spin check

at wheel

or brake

change.

Tires               OC              X       X       X

Cable-Emergency

System            OC                              X  FC 4-PI

Bottle-Nitrogen

Pressure           *       *      X       X       X    *

Doors and Linkage   OC              X       X       X

Valve Assy. - Power

Brake            4,000     2      X       X       X

Lights, Chapter 33

May be determined

by assigned

inspector

Navigation,

Chapter 34

Overhaul times may

be determined by

assigned

inspector.                        X       X       X

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date _____________________

PAGE 6 of 11 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

JET COMMANDER 1121

OVERHAUL           INSPECTION AND CHECK PERIOD

HOURS or YRS.    P.F.    S.C.    P.I.    OTHER

Oxygen,

Chapter 35      10,000     5      X       X       X

Cylinders           *               X       X       X

Regulators, Crew   2,500     2      X       X       X

Passenger

regulator

control panel    2,500     2      X       X       X

Masks, Crew         OC              X       X       X

Masks, Passenger    OC                                   Drop

Test

3-PI

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Doors, Chapter 52 10,000     5      X       X       X

Locking mechanism 10,000     5                           Note 1

and pins

Fuselage,         10,000     5      X       X       X

Chapter 53

Connection of     10,000     5                           Note 4

bottom frame

carry thru

structure

between floor

beams, FS 104

thru FS 270 - Z

line .50

Fuselage splice   10,000     5                           Note 4

attachment in

"J" stringers,

Z line 65 and

FS 105.78

Splice at top of  10,000     5                           Note 4

frames FS 105,

FS 134.78 and

FS 163.65, Z

line 65

Splice at inner

caps at lower

centerline, FS

105, FS 134.78 and

FS 163.65, Z

line 10.5

Escape hatch      10,000     5                           500 hrs.

retention blocks                                       or 6 mo.

FS 196 and FS

216. - Z lines

32.45 and 59.45

Seat brace        10,000     5                           Note 4

support.  R/H

side, FS 141 to

FS 158.  R/H and

L/H sides FS 163

thru FS 259.  Z

line 10.5

Clips connecting  10,000     5                           Note 4

window line

fuselage frames

to adjacent

fuselage frame.

R/H side FS

134.78, R/H and

L/H side FS

163.65 thru FS

250 - Z lines

38.75 and 56.25.

Effective date _____________________

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE    Page 7 of 11

JET COMMANDER 1121

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS or YRS.    P.F.    S.C.    P.I.    OTHER

Fuselage, Chapter

53 (Cont.)

Window frames     10,000     5                           Note 4

connecting to

fuselage frames

R/H side FS

134.73, R/H and

L/H side FS

163.65 thru FS

250.  Z lines

38.75 and 56.25.

Splice bolts      10,000     5                           Note 4

through pork

chop fittings

and members

spanning floor

beams.  FS 196

and FS 216.  -Z

lines 1 and 9.

Control idler     10,000     5                           Note 4

attachments

between floor

beams in forward

fuselage and

supported on

frames in aft

fuselage.

FS 76 thru FS

87, FS 125 thru

FS 150, FS 196

thru FS 223, FS

259 thru FS 269,

FS 317 thru FS

328.  Z line

10.5

Aft pressure       5,000     5

bulkhead mold

line "U" cap

channel used for

skin splice.  FS

269.87

"J" stringer      10,000     5                           Note 4

attachment at

pressure bulk-

head FS 269.87

Z line 65.

Center fuel        5,000     5

separation panel

floor to lower

wing FS 270 to

FS 316, Z lines

10.5 thru 38.

Angles to connect  5,000     5

centerfuel

separation panel

to pressure

bulkhead.  FS

270, Z lines

10.5 thru 38.

Angle under wing   5,000     5

rear spar FS

316, Z line 38.

Lower floor beam  10,000     5                           Note 4

cap carry

through fittings

FS 270 and FS

316.  Z line -

10.5.

Effective date _____________________

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE    Page 8 of 11

JET COMMANDER 1121

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS or YRS.    P.F.    S.C.    P.I.    OTHER

Fuselage, Chapter

53 (Cont.)

Engine nacelle    10,000     5                           EC

mount yoke to

fuselage

attachments

FS 404 and

FS 419

Nacelle/Pylons,   10,000     5      X       X       X

Chapter 54

Engine mount      10,000     5                      X    EC

structure

(including

nacelle internal

skins) NS 47.83

thru 102.58

Engine attach     OC                                X    EC

bolts                                                 Magnaflux

Stabilizers,      10,000     5      X       X       X

Chapter 55

Elevator hinge    10,000     5      X       X       X    Note 5

bolts

Elevator spar,    10,000     5              X       X    Note 6

external and

internal

Elevator ribs     10,000     5              X       X    Note 6

Elevator balance  10,000     5                      X    2500 hrs

weights                                                or 2.5

yrs.

Horizontal        10,000     5              X       X    Note 6

stabilizer front

spar and ribs

Horizontal trim   OC                                X    Note 8

actuator bolts

Forward surface   10,000     5                           Note 1

of forward spar,

vertical

stabilizer

Rudder hinge      10,000     5      X       X       X    Note 5

bolts

Rudder balance    10,000     5                      X    2500 hrs

weights                                                or 2.5

yrs.

Rudder tab hinge  10,000     5      X       X       X    Note 4

pin

Rudder tab        10,000     5                      X    2500 hrs

balance weight                                         or 2.5

yr

Forward surface   10,000     5                      X    2500

of forward                                             hrs. or

rudder spar                                            2.5 yrs.

Effective date _____________________

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE    Page 9 of 11

JET COMMANDER 1121

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS or YRS.    P.F.    S.C.    P.I.    OTHER

Windows, Chapter  10,000     5      X       X       X

56

All Glass         OC                X       X       X    Note 7

Wing, Chapter 57  10,000     5      X       X       X

Wing to fuselage  10,000     5                           Note 4

attachments,

WS 33

57 Spar - rear    10,000     5                           Note 4

side

Front spar, main  10,000     5                           Note 4

Dagger fittings   10,000     5                           Note 4

WS 0 WS 62 and

WS 93

Rib, Center WS 0  10,000     5                           Note 4

Ribs - WS 33      10,000     5                           Note 4

thru WS 247

Stringers         10,000     5                           Note 4

Rear spar, main   10,000     5                           Note 4

Front spar        10,000     5                           Note 4

splice, WS 15

RH side upper,

WS 15 LH side

lower

Rear spar splice, 10,000     5                           Note 4

WS 10 RH side

upper, WS 10

RH side lower

Flap hinge pin     2,500    2.5     X       X       X

Aileron hinge     10,000     5      X       X       X    Note 8

bolts

Aileron tab hinge 10,000     5      X       X       X    Note 4

pin

Aileron and tab   10,000     5                      X    Note 4

balance weights

Engine, Chapter 72

CJ 610-1           1,000            X       X       X    Hot

section

500 hrs.

Note 9

Effective date _____________________

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE    Page 10 of 11

JET COMMANDER 1121

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS or YRS.    P.F.    S.C.    P.I.    OTHER

Engine Fuel and

Control, Chapter

73              EO                        X       X

Ignition, Chapter

74              EO                        X       X

Ignitor plug      OC                                     Note 7

Engine Controls,

Chapter 76      OC                X       X       X    EO

Engine Indicating,

Chapter 77      EO                        X       X

Tachometer,

Generator       EO                        X       X

Exhaust

Temperature

Thermocouples   EO                        X       X

Exhaust Pressure

Ratio

Transducer      EO                        X       X

Fuel Flow

Transm@ter     EO                        X       X

Oil Pressure

Transmitter     EO                        X       X

Fuel Pressure

Transmitter     EO                        X       X

Exhaust, Chapter

78              OC                X       X       X

Tail cone         EO                X       X       X

Oil, Chapter 79   EO                                X

Oil tank          EO                                X

Oil pump          EO                                X

Starting, Chapter

80              EO                                X

Starter-Generator (See Chapter 24)

Note 1    Sample 1/3 of fleet at 2,500, 5,000 and 7,500 hours.

Note 2    Sample 1/3 of fleet at 4,000 and 6,000 hours.

Note 3    Inspect 1/3 of fleet at 2nd and 4th Periodic

Inspection.  If found satisfactory, increase time

between inspections to each 8th Periodic Inspection.

Effective date _____________________

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE    Page 11 of 11

JET COMMANDER 1121

Note 4    Inspect at 5,000 hours or 2.5 years.

Note 5    Inspect and magnaflux center bolt at 1,000 and 5,000

hours.

Note 6    Xray 1/3 of fleet at 1,000, 3,000 and 5,000 hours.

Note 7    Inspect, repair and/or replace in accordance with

factory recommendations.

Note 8    Inspect and magnaflux at intervals of 2,500 hours or

2.5 years.

Note 9    Serialized engines listed in CJ 610 Service Bulletin

No. 9 require a combustion liner change at 400 hours

unless Service Bulletin No. 9, Service Bulletin No. 47

or subsequent revisions are incorporated.

Effective date_____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 28.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- DOUGLAS DC-8-62/62F

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                        PAGE 1 of 10 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-62/62F

Following are additional items and/or changes to the original

Douglas DC-8/F aircraft specification listing which apply to the

Douglas DC-8-62/62F aircraft.

Zone diagrams for the Douglas DC-8/F are also applicable to

Douglas DC-8-62/62F aircraft; however, fuselage stations listed

will only apply to the Douglas DC-8/F.

Overhaul      Inspection &

Air Conditioning, Chapter 21        Period        Check Period

Valve, Cold Air Bypass                OC             D,E

Electrical Power, Chapter 24

Constant Speed Rive, 30 KVA         3,000          D - Oil Change

Generator, 30 KVA                   5,000        B,D - Oil Level

check

Panel, Voltage Regulator and

Generator Control                   OC             F/C @ E

Cooler, Air/Oil CSD                   EO             D

Fire Protection, Chapter 26

(62F) Pyrotector (Smoke Detector)     OC          A,B,D,E

Container - Fire Extinguisher          *            B,D,E

Cartridge - Dual Squib              4 years         B,D,E

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Flight Controls, Chapter 27

Cylinder and Control Valve Rudder

Power                                 2E             D

Fuel, Chapter 28

Pump, Residual Fuel Scavenge Center

Wing                                  OC           D - F/C @ E

Heater, Sump, Center Wing               OC           D - F/C @ E

Valve, Fuel Scavenge Selector Center

Wing                                  OC           D - F/C @ E

Ice and Rain System, Chapter 30

Rain Repellent System                   OC       A,B,D

Tail, De-icing                          OC           D,E

Effective date ____________________

Page 2 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-62/62F

Overhaul      Inspection &

Landing Gear, Chapter 32            Period        Check Period

Limiter, Brake Fluid Quantity       12,500             D

Bogie Beam, Main Landing Gear,

Non Swivel                        12,500             D

Valve, Nose Wheel Steering Bypass   12,500             D

Pneumatic, Chapter 36

Heat Exchanger, Bleed Air           O.C.               D - E.C.

Valve, Bleed Air Temperature

Control                           O.C.               D - F/C @

E

Valve, 16th Stage Shut-Off          O.C.               D - F/C @

E.O.

Valve, 12th Stage Check             O.C.               D - F/C @

E.O.

Amplifier, Pneumatic Manifold

Rupture Warning                   O.C.               D,E

Sensing Element, Pneumatic

Manifold Rupture Warning          O.C.               E

Doors, Chapter 52

(62F) Main Cabin Cargo Door

Hydraulic System                  O.C.          See NOTE *

(62F) Cylinder Assembly, Main

Cabin Cargo Door Actuating        O.C.          See NOTE *

NOTE:

*    The design of the main cabin cargo door installation is such

that in the normally latched and locked position, it can be

structurally compared to any fixed portion of the fuselage.

It is only when the door is actuated open on the ground

during cargo loading operations that the heaviest loads are

incurred.  These loads would be greatest at the upper door

hinge and hydraulic actuating cylinder attach points.  The

door seal would also be subject to damage at this time.

Thus, door utilization established inspection frequency.

Under these conditions, Douglas suggests the following

procedures for purposes of inspection:  (1)  Conduct a

general visual area inspection of the upper cargo door hinge

attachments, door jamb, door actuating cylinder attachments,

door seal and latching mechanism at the scheduled "D"

service following use of the aircraft in cargo

configuration.  (2)  If the aircraft is operated solely in

the passenger configuration, conduct a general visual area

inspection (as above) no later than "E" frequency.

Effective date ____________________

Page 3 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-62/62F

Overhaul      Inspection &

Powerplant, Chapter 71              Period        Check Period

Nose Cowl and Fan Duct Attach.,

Fireseal, Engine Mounts, Control  Engine

and Accessory Brackets            Change             D

Engine Air, Chapter 75

Valve, Engine Nose Cowl

Anti-ice Shut-off                 O.C.               D - F/C @

E.O.

Thrust Reverser, Chapter 78

Thrust Reverser Assembly            O.C.             B,D (X-Ray

Reverser

Structure,

on Aircraft

at E

Frequency)

Pump Assembly, Electric Driven      5000               D

Accumulator                         16,000             D

Cylinder, Thrust Reverser Actuator  12,000             D

Valve, Thrust Reverser Control      12,000             D

Cylinder, Stow Latch, Thrust

Reverser                          12,000             D

Filter Assembly                     O.C.               E

Effective date ____________________

Page 4 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-62/62F

STRUCTURE INSPECTION PROGRAM

E Check -      4000 Hours           Overhaul      Inspection &

D Check -       500 Hours           Period        Check Period

Wings

Wing Tip, Zone 5 L/R             5E                 D

Wing Outboard of Sta. Xw 408,

Zone 9 L/R & Zone 6 L/R        5E

Wing Leading Edge Sta. Xfs.

710 to Xw 736 Cant, Zone 7

L/R                            E

Wing Leading Edge Sta. Xw 485

to Xfs. 710, Zone 8 L/R        E

*  No. 1 & 4 Alternate Fuel Tanks,

Zone 9 L/R and Zone 6 L/R      5E                 E-Sample

One Tank

Per

Aircraft

Wing Trailing Edge Sta. Xw

408 to Xw 736 Cant, Aft of

Rear Spar, Zone 10 L/R         E             Aileron Hinge

Brackets and

Bolts 4D

Aileron and Tab, Zone 11 L/R     E             Hinges &

Attachments 4D

Aileron Leading Edge Balance

Weights                        2E

Wing Leading Edge at Outboard

Pylon Sta. Xfs. 526 to Xw

485, Zone 12 L/R               E

Outboard Pylon, Apron and

Nacelle Access Doors, Zone

13 L/R                         E                  2D

*  Pylon Upper Spar and Pylon

Leading Edge attachments,

Zone 13 L/R                    E                  2D

Effective date ____________________

Page 5 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-62/62F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Wings (Continued)

*  Pylon to Wing Front Spar and

Pylon to Wing Attachments,

Zone 13 L/R                      E               2D

Inboard Pylon, Apron and Nacelle

Access Doors, Zone 14 L/R        E               2D

*  Pylon Upper Spar and Pylon

Leading Edge Attachments,

Zone 14 L/R                      E               2D

*  Pylon to Wing Front Spar and

Pylon to Wing Attachments,

Zone 14 L/R                      E               2D

Wing Leading Edge Sta. Xw 408

to Xfs. 526, Zone 15 L/R         E

Wing Leading Edge Sta. Xw 257

to Xw 408, Zone 16 L/R           E

*  No. 1 & 4 Main Fuel Tanks,

Zone 17 L/R                      5E              E-Sample

One Tank

Per

Aircraft

Wing Trailing Edge from Outboard

Auxiliary Spar to Sta. Xw 408,

Zone 18 L/R                      E

Main Landing Gear Support

Fittings and Auxiliary Spars,

Zone 19 L/R                      2E

Wing Leading Edge at Inboard

Pylon Sta. Xfs. 250 to Xw 257,

Zone 20 L/R                      E

Wing Leading Edge Sta. Xw0 to

Xfs. 207, Zone 21 L/R & 22 L/R

External Inspection              E

Wing Leading Edge Xfs Sta. 207

to Xs 250, Zone 20 & Zone 21

External Inspection              E

Wing Leading Edge Xfs Sta. 207

to Xs 250, Zone 20 & Zone 21

Including Forward Face of Wing

Front Spar, as visible.          E

Effective date ____________________

Page 6 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-62/62F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Wings (Continued)

Leading Edge Fuel Tanks, Zone 21

L/R and Zone 22 L/R            5E

No. 2 and 3 Main and Alternate

Fuel Tanks, Zone 23 L/R and

Zone 24 L/R                    5E

Outboard Wing Flap Interior

Structure, Zone 25 L/R         3E

Flap Hinge Support Fittings,

Zone 25 L/R                    2E

Aft Side of Flap Spar, Zone 25

L/R                            4E

Inboard Wing Flap & Links at

the Outboard End of the Flap,

which Connect to the Inboard

End of the Outboard Flap,

Zone 26 L/R                    E

Flap Hinge Support Fittings and

Aft Side of Flap Spar, Zone

26 L/R                         4E

Interior of Center Wing Sta.

Xcw 0 to Xcw 69.5 (Front to

Rear Spar, Zone 27 L/R         5E

NOTE:

*  Specified times for items identified by (*) applicable to all

operators until satisfactory service experience accumulated.

Fuselage  (All Stations are DC-8-62/62F)

Radome, Zone 51                  E

Effective date ____________________

Page 7 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-62/62F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Fuselage (Continued)

Fuselage Turbo Compressor

Compartment, Zone 52           4E

Navigation Antenna Compartment,

Zone 53                        4E

Nose Gear Wheel Well, Zone 54    4E

Nose Wheel Well Tunnel, Zone

55, L/R                        4E

Air Conditioning Accessory

Compartment, Sta. 208 to 270,

Zone 56                        E

Forward Cargo Compartment, Sta.

270 to 640, Zone 57            4E

Forward Cargo Compartment Tunnel

Sta. 270 to 640, Zone 57 L/R   4E

Fuselage Accessory Compartment

Sta. 640 to 680, Zone 58       E

Upper and Lower Front Spar Cap,

Forward Face of Front Spar Web

Upper and Lower Front Spar

Caps and Splice Plates at

Sta. Xcw 0, Zone 58            4E

Aft Cargo Compartment Sta. 980

to 1380, Zone 59               4E

Aft Cargo Compartment Tunnel,

Sta. 980 to 1380, Zone 59 L/R  4E

Fuselage Belly Compartment Sta.

1380 to Pressure Panel at

Sta. 1606, Zone 60             E

Effective date ____________________

Page 8 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-62/62F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Fuselage (Continued)

Aft Fuselage Sta. 1606 to

1730, Zone 61                  E

Aft Face and Periphery of

Pressure Panel at Fuselage

Sta. 1606, Zone 61             E

Fuselage Tail Cone, Zone 62      E

Fuselage Sta. 69 to 83 Above

Cockpit Floor, Zone 63         4E

Fuselage Cockpit Sta. 83 to

148, Zone 64                   4E

Fuselage Cockpit Sta. 148 to

225 Above Floor, Zone 65 L/R   E

Fuselage Sta. 208 to 69 Between

Cockpit Floor and Horizontal

Pressure Panel, Zone 66        E

Forward and Aft Galley Areas

Sta. 340 to 420 and Sta. 1440

to 1520 R. Side, Zone 67       E

Scuff Plates at Forward and Aft

Service Door Jambs, Internal

Inspection of Door Jambs.

Intercostals and Frames at

Fuselage Sta. 355, 391, 1460

and 1500.  Inspection of Door

Hinge Attachments and Door

Snubber Attachments to Jambs,

Zone 67                        4E

Forward and Aft Lavatory Areas,

Zone 68                        4E

Vertical Stabilizer Front and

Center Spar Attachments to

Fuselage Longerons, Between

Fuselage Sta.'s 1540 and 1606,

Zone 68                        4E

Effective date ____________________

Page 9 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-62/62F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Fuselage (Continued)

Upper and Lower Attachments of

Aft Pressure Panel Vertical

Beam (Center Line-Forward

Face Pressure Panel) Fuselage

Sta. 1606, Zone 68             4E

Fuselage Entrance Doors, Zone

69                             4E

(62F) Main Cabin Cargo Door,

Zone 69                        4E

Emergency Exit Doors, Zone 69    4E

Fuselage Sta. 680 to 980 Between

Bottom of Floor and Top of

Wing and Wheel Well, Zone 70   4E

Upper Wing to Fuselage Fillet,

Zone 71 L/R                    4E

Lower Wing to Fuselage Fillet

Sta. 680 to 980, Zone 72 L/R   4E

Fuselage Less Zones 67 & 68,

From Sta. 225 to 1485 Above

Cusp., Zone 73                 4E

(62F) Internal Inspection of

Main Cabin Cargo Door Jamb

Intercostals and Frames at

Fuselage Sta. 330 and 470,

Zone 73                        4E

Left and Right Main Landing Gear

and Wheel Well, Zone 74 L/R    4E

Wheel Well Keel, Zone 74 L/R     E

Effective date ____________________

Page 10 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-62/62F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Fuselage (Continued)

Left and Right Horizontal

Stabilizer Leading Edge,

Zone 75 L/R                    2E

Forward Face of Stabilizer

Front Spar, Zone 75 L/R        E

Left and Right Horizontal

Stabilizer Outer Panel,

Zone 76 L/R                    4E

Horizontal Stabilizer Center

Section, Zone 77               2E

Left and Right Elevator and

Tabs, Zone 78 L/R              E

Vertical Stabilizer Leading

Edge, Zone 79                  2E

Vertical Stabilizer Front Spar

To Rear Spar, Zone 80          2E

Vertical Stabilizer Tip, Zone

81                             3E

Rudder and Tab, Zone 82          2E

Rudder Hinge Fitting and Damper  E

Horizontal Stabilizer Tip, Zone

83 L/R                         2E

Left and Right Aft Fillet,

Zone 84, L/R                   2E

Effective date ____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 29.  OPERATIONS SPECIFICATIONS/AIRCRAFT MAINTENANCE

- DOUGLAS DC-8-63/63F

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                        PAGE 1 of 10 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-63/63F

Following are additional items and/or changes to the original

Douglas DC-8/F aircraft specification listing which apply to the

Douglas DC-8-63/63F aircraft.

Zone diagrams for the Douglas DC-8/F are also applicable to

Douglas DC-8-63/63F aircraft; however, fuselage stations listed

will only apply to the Douglas DC-8/F.

Overhaul      Inspection &

Air Conditioning, Chapter 21        Period        Check Period

Valve, Fan Unloader                   OC              D,E

Filter, Recirculating Fan             OC              D

Valve, Cold Air Bypass                OC              D,E

Electrical Power, Chapter 24

Constant Speed Drive, 30 KVA         3,000            D-Oil

Change

Generator, 30 KVA                    5,000          B,D-Oil Level

Check

Panel, Voltage Regulator and

Generator Control                   OC                E - F/C

Cooler, Air/Oil CSD                   EO              D

Fire Protection, Chapter 26

(63F) Pyrotector (Smoke Detector)     OC          A,B,D,E

Container - Fire Extinguisher          *            B,D,E

Cartridge - Dual Squib              4 years         B,D,E

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Flight Controls, Chapter 27

Cylinder and Control Valve Rudder

Power                               2E              D

Fuel, Chapter 28

Pump, Residual Fuel Scavenge Center

Wing                                OC              D, F/C @ E

Heater, Sump, Center Wing             OC              D, F/C @ E

Valve, Fuel Scavenge Selector

Center Wing                         OC              D, F/C @ E

Ice and Rain Protection, Chapter 30

Rain Repellent System                 OC          A,B,D

Tail De-icing Timer                   OC              D,E

Effective date ____________________

Page 2 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-63/63F

Overhaul      Inspection &

Landing Gear, Chapter 32            Period        Check Period

Bogie Beam, Main Landing Gear,

Non-Swivel                        12,500             D

Energy Absorber, Tailskid           O.C.           A,B,D

Valve, Nose Wheel Steering,

Bypass                            12,500             D

Limiter, Brake Fluid Quantity       12,500             D

Pneumatic System, Chapter 36

Heat Exchanger, Bleed Air           O.C.               D - E.C.

Valve, Bleed Air Temperature

Control                           O.C.               D - F/C @

E

Valve, 16th Stage Shut-off          O.C.               D - F/C @

E.O.

Valve, 12th Stage Check             O.C.               D - F/C @

E.O.

Amplifier, Pneumatic Manifold

Rupture Warning                   O.C.               D,E

Sensing Element, Pneumatic

Manifold Rupture Warning          O.C.               E

Doors, Chapter 52

(63F) Main Cabin Cargo Door

Hydraulic System (Same as 55F)    O.C.          See NOTE *

(63F) Cylinder Assembly, Main

Cabin Cargo Door Actuating        O.C.          See NOTE *

*  NOTE:  The design of the main cabin cargo door installation is

such that in the normally latched and locked position,

it can be structurally compared to any fixed portion of

the fuselage.

It is only when the door is actuated open on the ground

during cargo loading operations that the heaviest loads

are incurred.  These loads would be greatest at the

upper door hinge and hydraulic actuating cylinder

attach points.  The door seal would also be subject to

damage at this time.

Thus, door utilization established inspection

frequency.  Under these conditions, Douglas suggests

the following procedure for purposes of inspection:

(1)  Conduct a general visual area inspection of the

upper cargo door hinge attachments, door jamb, door

actuating cylinder attachments, door seal and latching

mechanism at the scheduled "D" service following use of

the aircraft in cargo configuration;  (2)  If the

aircraft is operated solely in the

Effective date ____________________

Page 3 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-63/63F

Overhaul      Inspection &

Period        Check Period

*  NOTE:  (Continued)

passenger configuration, conduct a general visual area

inspection (as above) no later than "E" frequency.

Powerplant, Chapter 71

Nose Cowl and Fan Duct Attach.

Fireseal, Engine Mounts           Engine

Control & Accessory Brackets      Change             D

Engine Air, Chapter 75

Valve, Engine Nose Cowl

Anti-ice Shut-off                 O.C.               D, F/C @

E.O.

Thrust Reverser, Chapter 78

Thrust Reverser Assembly            O.C.           B,D (X-Ray

Reverser

Structure

on

Aircraft

@ E

Frequency)

Pump Assembly, Electric Driven      5000               D

Accumulator                         16,000             D

Cylinder, Thrust Reverser

Actuator                          12,000             D

Valve, Thrust Reverser Control      12,000             D

Cylinder, Stow Latch, Thrust

Reverser                          12,000             D

Filter Assembly                     O.C.               E

Effective date ____________________

Page 4 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-63/63F

STRUCTURE INSPECTION PROGRAM

E Check -      4000 Hours           Overhaul      Inspection &

D Check -       500 Hours           Period        Check Period

Wings

Wing Tip, Zone 5 L/R             5E                 D

Wing Outboard of Sta. Xw 408,                  Combined Zone 9

Zone 9 L/R & Zone 6 L/R        5E            L/R & Zone 6

L/R

Wing Leading Edge Sta. Xfs 710

to Xw 736 Cant, Zone 7 L/R     E

Wing Leading Edge Sta. Xw 485

to Xfs 710, Zone 8 L/R         E

*  No. 1 & 4 Alternate Fuel Tanks,                     E-Sample

Zone 9 L/R and Zone 6 L/R      5E                   One Tank

Per

Aircraft

Wing Trailing Edge Sta. Xw 408                 Aileron Hinge

to Xw 736 Cant, Aft of Rear                  Brackets and

Spar, Zone 10 L/R              E             Bolts 4D

Aileron and Tab, Zone 11 L/R     E             Hinges &

Attachments 4D

Aileron Leading Edge Balance

Weights                        2E

Wing Leading Edge at Outboard

Pylon Sta. Xfs 526 to Xw 485,

Zone 12 L/R                    E

Outboard Pylon, Apron and

Nacelle Access Doors, Zone

13 L/R                         E                 2D

*  Pylon Upper Spar, and Pylon

Leading Edge Attachments,

Zone 13 L/R                    E                 2D

Effective date ____________________

Page 5 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-63/63F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Wings (Continued)

*  Pylon to Wing Front Spar and

Pylon to Wing Attachments,

Zone 13 L/R                      E               2D

Inboard Pylon, Apron and Nacelle

Access Doors, Zone 14 L/R        E               2D

*  Pylon Upper Spar and Pylon

Leading Edge Attachments,

Zone 14 L/R                      E               2D

*  Pylon to Wing Front Spar and

Pylon to Wing Attachments,

Zone 14 L/R                      E               2D

Wing Leading Edge Sta. Xw 408

to Xfs 526, Zone 15 L/R          E

Wing Leading Edge Sta. Xw 257

to Xw 408, Zone 16 L/R           E

*  No. 1 & 4 Main Fuel Tanks,

Zone 17 L/R                      5E              E-Sample

One Tank

Per

Airplane

Wing Trailing Edge from Outboard

Auxiliary Spar to Sta. Xw 408,

Zone 18 L/R                      E

Main Landing Gear Support

Fittings & Auxiliary Spars,

Zone 19 L/R                      2E

Wing Leading Edge at Inboard

Pylon Sta. Xfs 250 to Xw 257,

Zone 20 L/R                      E

Wing Leading Edge Sta. Xw0 to

Xfs. 207, Zone 21 L/R & 22 L/R

External Inspection              E

Wing Leading Edge Xfs Sta. 207

to Xs 250, Zone 20 & Zone 21

External Inspection              E

Wing Leading Edge Xfs Sta. 207

to Xs 250 Zone 20 & Zone 21

including Forward Face of Wing

Front Spar, as visible.          E

Effective date ____________________

Page 6 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-63/63F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Wings (Continued)

Leading Edge Fuel Tanks,

Zone 21 L/R & Zone 22 L/R      5E

No. 2 & 3 Main and Alternate

Fuel Tanks, Zone 23 L/R &

Zone 24 L/R                    5E

Outboard Wing Flap Interior

Structure, Zone 25 L/R         3E

Flap Hinge Support Fittings,

Zone 25 L/R                    2E

Aft Side of Flap Spar, Zone

25 L/R                         4E

Inboard Wing Flap & Links at the

Outboard End of the Flap,

which Connect to the Inboard

End of the Outboard Flap,

Zone 26 L/R                    E

Flap Hinge Support Fittings and

Aft Side of Flap Spar, Zone

26 L/R                         4E

Interior or Center Wing Sta.

Xcw 0 to Xcw 69.5 (Front to

Rear Spar), Zone 27 L/R        5E

NOTE:  *  Specified times for items identified by (*) applicable

to all operators until satisfactory service experience

accumulated.

Fuselage  (All stations are

DC-8-63/63F, Identical

to DC-8-61/61F)

Radome, Zone 51                  E

Fuselage Turbo Compressor

Compartment, Zone 52           4E

Effective date ____________________

Page 7 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-63/63F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Fuselage (Continued)

Navigation Antenna Compartment,

Zone 53                        4E

Nose Gear Wheel Well, Zone 54    4E

Nose Wheel Well Tunnel, Zone

55 L/R                         4E

Air Conditioning Accessory

Compartment Sta. 8 to 70,

Zone 56                        E

Forward Cargo Compartment Sta.

70 to 640, Zone 57             4E

Forward Cargo Compartment Tunnel

Sta. 70 to 640, Zone 57 L/R    4E

Fuselage Accessory Compartment

Sta. 640 to 680, Zone 58       E

Upper and Lower Front Spar Cap,

Forward Face of Front Spar

Web Upper and Lower Front Spar

Caps and Splice Plates at Sta.

Xcw 0, Zone 58                 4E

Aft Cargo Compartment Sta. 980

to 1540, Zone 59               4E

Aft Cargo Compartment Tunnel,

Sta. 980 to 1540, Zone 59 L/R  4E

Fuselage Belly Compartment Sta.

1540 to Pressure Panel at Sta.

1766, Zone 60                  E

Aft Fuselage Sta. 1766 to 1890,

Zone 61                        E

Effective date ____________________

Page 8 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-63/63F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Fuselage (Continued)

Aft Face and Periphery of

Pressure Panel at Fuselage

Sta. 1766, Zone 61             E

Fuselage Tail Cone, Zone 62      E

Fuselage Sta. -131 to -117

above Cockpit Floor, Zone 63   4E

Fuselage Cockpit Sta. -117 to

-52, Zone 64                   4E

Fuselage Cockpit Sta. -52 to

25 above Floor, Zone 65 L/R    E

Fuselage Sta. 8 to -131 Between

Cockpit Floor and Horizontal

Pressure Panel, Zone 66        E

Forward and Aft Galley Areas

Sta. 360 to 460 & Sta. 1500

to 1620 R. Side, Zone 67       E

Scuff Plates at Forward and Aft

Service Door Jambs.  Internal

Inspection of Door Jambs.

Intercostals & Frames at

Fuselage Sta. 395, 430, 1538

& 1575.  Inspection of Door

Hinge Attachments & Door

Snubber Attachments to Jambs,

Zone 67                        4E

Forward and Aft Lavatory Areas,

Zone 68                        4E

Vertical Stabilizer Front &

Center Spar Attachments to

Fuselage Longerons, Between

Fuselage Sta's. 1700 and 1766,

Zone 68                        4E

Effective date ____________________

Page 9 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-63/63F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Fuselage (Continued)

Upper and Lower Attachments of

Aft Pressure Panel Vertical

Beam (Center Line-Forward

Face of Pressure Panel)

Fuselage Sta. 1766, Zone 68    4E

Fuselage Entrance Doors, Zone

69                             4E

(63F) Main Cabin Cargo Door,

Zone 69                        4E

Emergency Exit Doors, Type I

and Type III, Zone 69          4E

Fuselage Sta. 680 to 980 Between

Bottom of Floor and Top of

Wing and Wheel Well, Zone 70   4E

Upper Wing to Fuselage Fillet,

Zone 71 L/R                    4E

Lower Wing to Fuselage Fillet

Sta. 680 to 980, Zone 72 L/R   4E

Fuselage Less Zones 67 & 68,

From Sta. 25 to 1645 above

Cusp., Zone 73                 4E

(63F) Internal Inspection of

Main Cabin Cargo Door Jamb

Intercostals and Frames at

Fuselage Sta. 130 to 270,

Zone 73                        4E

Internal Inspection of Type I

and Type III Emergency Exit

Door Jambs, Intercostals and

Frames                         4E

Left and Right Main Landing

Gear and Wheel Well, Zone

74 L/R                         4E

Wheel Well Keel, Zone 74 L/R     E

Effective date ____________________

Page 10 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-8-63/63F

STRUCTURE INSPECTION PROGRAM

Overhaul      Inspection &

Period        Check Period

Fuselage (Continued)

Left and Right Horizontal

Stabilizer Leading Edge,

Zone 75 L/R                    2E

Forward Face of Stabilizer

Front Spar, Zone 75 L/R        E

Left and Right Horizontal

Stabilizer Outer Panel,

Zone 76 L/R                    4E

Horizontal Stabilizer Center

Section, Zone 77               2E

Left and Right Elevator and

Tabs, Zone 78 L/R              E

Vertical Stabilizer Leading

Edge, Zone 79                  2E

Vertical Stabilizer Front Spar

to Rear Spar, Zone 80          2E

Vertical Stabilizer Tip, Zone

81                             3E

Rudder and Tab, Zone 82          2E

Rudder Hinge Fittings and

Damper                         E

Horizontal Stabilizer Tip,

Zone 83 L/R                    2E

Left and Right Aft Fillet, Zone

84 L/R                         2E

Effective date ____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 30.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- LOCKHEED MODEL 300 (C-141A)

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                        Page 1 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL 300 (C-141A)

APPLICABILITY

Lockheed fuselage serial numbers 6285 and up.  For aircraft with

fuselage serial numbers other than stated, Maintenance

Specifications will be individually established.  Overhaul and

inspection intervals apply to components and appliances

identified in Lockheed Service Manual Publication SMP 231 dated

June 1, 1967, and revisions thereto.

EFFECTIVITY

Subject to the submission of acceptable maintenance technical

data to an authorized representative of the FAA.

INSPECTION/CHECK REQUIREMENTS

The basic requirements for performing these inspections and

checks are as specified in Part I of Lockheed Service Manual

Publication SMP 231 dated June 1, 1967, and revisions thereto.

"A" INSPECTION/CHECK

To be accomplished each service calendar day.

"B" INSPECTION/CHECK

To be accomplished at intervals not exceeding 125 hours time in

service after the preceding "B" or "C" inspection/check period.

"C" INSPECTION/CHECK

To be accomplished at intervals not exceeding 500 hours time in

service after the preceding "C" inspection/check period.

AIRFRAME STRUCTURAL INSPECTIONS

The frequency and procedure for performing these inspections will

be accomplished as specified in Part I and Part III of Lockheed

Service Manual Publication SMP 231 dated June 1, 1967, and

revisions thereto.

SPECIAL INSPECTIONS

The frequency and procedures for performing these inspections

will be accomplished as specified in Part IV of Lockheed Service

Manual Publication SMP 231 dated June 1, 1967, and revisions

thereto.

Effective date ____________________

Page 2 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL 300 (C-141A)

TERMINOLOGY DEFINITION

Unless otherwise stated herein, the time limitations are listed

in aircraft operating hours.  Letters and terms used denote the

following:

"OC" = On Condition

"EO" = Engine Overhaul

"6 Months" = Six months calendar time

"5 Years"  = Five years calendar time

"E.T.I." = Elapsed time indicator hours

"5000 Starts" = Quantity indicated on unit start counter

"A" = Daily Check (Part I)

"B" = "B" Check (125 hours)  (Part I)

"C" = "C" Check (500 hours)  (Part I)

"2C" = Second "C" Check (Part I)

"3C" = Third "C" Check (Part I)

"6C" = Sixth "C" Check (Part I)

"EC" = Engine Change

"EO" = Engine Overhaul

"EO/FC" = Functional Check required at Engine Overhaul

"S" = Special Inspection (Part IV)

"ST" = Structural Inspection (Part III)

Effective date ____________________

Page 3 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL 300 (C-141A)

Overhaul      Inspection and

Period        Check Period

Air Conditioning, Chapter 21         OC           A B C 2C S

Box, Temperature Control             OC               C 2C

Control, Fan and Venturi, Cabin

Pressure                            6,000             C

Control, Venturi, Cabin Pressure     OC               C

Controller, Cabin Pressure,

Automatic                           3,000         A B C 2C

Controller, Cabin Pressure, Manual  6,000         A B C 2C

Fan Cooling, Electrical Equipment  12,000             C

Fan Cooling, Electronic Components  6,000             C

Heat Exchanger, Primary and

Secondary                            OC             B C

Indicator, Air Pressure, Dual        OC           A B C

Indicator, Rate of Climb           12,000         A B C

Indicator, Pressure Cabin Altitude

and Diff. Pressure                  6,000         A B C

Indicator, Temperature               OC           A B C

Regulator, Pressure, Jet-Pump        OC               C

Sensor, Temperature                  OC               C 2C

Switch, Warning, Cabin Low Pressure  OC               C

Transmitter, Pressure, Air           OC               C

Turbine Assembly, Refrigeration     3,000           B C 2C

Valve, By-Pass Turbine             12,000             C 2C

Valve, Diverter, Air Conditioning  12,000             C

Valve, Flow Control and Shut-Off

(Air Conditioning)                 12,000             C

Valve, Flow Control, Electronic

Cooling                            12,000             C

Valve, Modulating, Floor Heat,

Cargo Compartment                   3,000             C

Valve, Outflow, Cabin Pressure      6,000             C

Valve, Regulator, Air Pressure      6,000             C

Valve, Relief, Air Pressure        12,000             C

Valve, Shut-Off, Alternate Air,

Flight Station                     12,000             C

Valve, Shut-Off, Floor Heat, Cargo

Compartment                        12,000             C

Valve, Shut-Off, Primary Heat

Exchanger Ejector                  12,000             C

Valve, Shut-Off, Ram Air Vent      12,000             C

Valve, Solenoid, Emergency

Depressurization                     OC               C    S

Valve, Temperature Control, Cabin  12,000             C

Water Separator, Air Conditioning    OC             B C    S

Auto Flight, Chapter 22              OC           A B C 2C S

Actuator, Servo AFCS                6,000             C

Actuator, Servo Yaw Damper          6,000             C

Compensator, Mach Trim              3,000             C 2C S

Computer, Aileron, AFCS             1,000             C

Computer, Elevator, AFCS            1,000             C

Computer, Yaw Damper                1,000             C

Effective date ____________________

Page 4 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL 300 (C-141A)

Overhaul      Inspection and

Auto Flight, Chapter 22, Continued  Period        Check Period

Control, Mach Trim                    OC          A B C 2C

Control Panel, Yaw Damper             OC          A B C

Gyro-Rate, Single Axis               3,000          B C

Gyro-Rate, Two Axis                  3,000          B C

Indicator, Trim, AFCS                6,000        A B C

Mounts, Servo, Aileron and Elevator   OC              C

Mounts, Servo, Yaw Damper             OC              C

Panel, Control, AFCS                 3,000        A B C

Sensor, Control Wheel Force         12,000            C

Transmitter, Mach Trim Compensator  12,000            C 2C

Vertical Gyro, AFCS                  1,000            C

Communications, Chapter 23            OC          A B C    S ST

Control, Intercommunications          OC          A B C    S ST

Requirements for additional equipment may be determined by

assigned inspector.

Electrical Power, Chapter 24          OC          A B C 2C S

Battery                               OC          A B C

Constant Speed Drive (CSD)            EO            B C    S

Controller - Load                   12,000            C

Contractor                          12,000            C

Cooler - Oil CSD                      EO            B C

Frequency Meter                     12,000        A B C

Generator - Engine Driven 40 KVA      EO            B C

Generator - APU Driven 40 KVA        6,000          B C

Generator - Emergency Hydraulic

Driven                              OC            B C 2C

Indicator - Temperature CSD Oil     12,000        A B C    S

Loadmeter                             OC          A B C

Panel - Bus Protection                OC              C

Panel - Generator Protection         9,000            C

Panel - Protection Aux. Power       12,000            C

Quick-Attach/Detach Assembly          EO            B C

Regulator-Voltage                   12,000            C

Relay - "Bus Off" Indicator         12,000            C

Relay - Emergency Bus Power         12,000            C 2C

Relay - Essential Bus Power         12,000            C

Relay - Frequency Sensitive         12,000            C 2C

Relay - Isolated Bus                12,000            C 2C

Relay - Isolated Bus Reverse

Current                           12,000            C 2C

Relay - Main D-C Bus                12,000            C

Tank, Oil, CSD                        EO            B C

Transformer - Rectifier Unit          OC            B C

Sensor - Temperature CSD Oil        12,000          B C    S

Switch, Pressure, CSD Oil           12,000          B C

Voltmeter                           12,000        A B C

Effective date ____________________

PAGE 5 of 12 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL 300 (C-141A)

Overhaul      Inspection &

Period        Check Period

Equipment & Furnishings, Chapter 25    OC         A B C      ST

Belt, Flight Crew Safety              6,000       A B C

Belt, Passenger Type Safety           6,000       A B C

Galley - Aircraft Type, Crew         12,000       A B C      ST

Goggles, Smoke                         OC         A B C

Harness, Aircraft Safety, Shoulder    6,000       A B C

Kit, First Aid, Medical             6 months      A B C

Ladder Assy. - Emergency Exit          OC         A B C

Lavatory - Crew                      12,000       A B C      ST

Rope Assembly - Escape                 OC         A B C

Seats - Flight Station               12,000       A B C

Winch - Cargo                          OC             C

Fire Protection, Chapter 26            OC         A B C    S ST

Amplifier - Smoke Detection            OC           B C

Cable - Flex                           OC           B C    S ST

Control Unit - Fire Warning            OC         A B C    S

Detector - Smoke                       OC           B C

Element - Sensing                      OC         A B C    S

Extinguisher - Fire, Portable CO2       *         A B C    S

Extinguisher - Fire, Dry Chemical,

Portable                              *         A B C    S

Generator - Fire Warning (Tone)        OC         A B C    S

Horn, APU Fire Warning SDU-1A          OC         A B C    S

Keyer, Engine Overheat                 OC         A B C    S

Sphere-Charged, and Operating Head,

APU and Engine                        *           B C    S

Valve, Fire Extinguisher, Two-Way

Check                                OC             C    S

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Flight Controls, Chapter 27            OC         A B C 2C S ST

Actuator - Aileron Trim and

Transmitter Assembly                6,000         B C

Actuator - Aileron Artificial Feel

(Cartridge)                         6,000         B C

Actuator - Elevator, Artificial Feel

"Q"                                 3,000         B C

Actuator - Rudder Artificial Feel

(Cartridge)                         6,000         B C

Actuator - Flap Inboard and Outboard  6,000       A B C

Actuator - Rudder Pedal, Bungee

(Rudder Pedal Steering)             6,000         B C

Actuator - Rudder Trim & Transmitter

Assembly                            6,000         B C

Actuator - Spoiler Control, Cable

Servo                               6,000         B C

Actuator - Spoiler Control Servo      6,000         B C

Actuator Assembly - Stabilizer Trim

(PITCH)                             6,000         B C 2C

Actuator Assembly - Aileron Tab

Lockout                             6,000         B C

Actuator Assembly - Control Column

Pusher                              6,000         B C

Effective date ____________________

Page 6 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL 300 (C-141A)

Overhaul      Inspection and

Flight Controls - Chapter 27        Period        Check Period

Continued

Actuator Assembly - Pitch Trim

Arming                               6,000         B C 2C

Aileron Assembly                      OC         A B C     ST

Brake Assembly - Flap Asymmetry     12,000         B C 2C

Broken Cable Detector, Wing Flap      OC           B C 2C

Carriage Assembly - Flap Inboard

and Outboard                         6,000         B C

Chain and Cable Assembly - Flap

Asymmetry                             OC           B C 2C

Computer Amplifier - Flap Asymmetry

System                               6,000         B C 2C

Computer, Stall Warning and

Prevention                           3,000         B C

Control Assembly - Aileron Power     6,000         B C

Control Assembly - Elevator Power    6,000         B C

Control Assembly - Rudder Power      6,000         B C

Control Column Assembly               OC           B C     ST

Elevator Assembly                     OC         A B C     ST

Flap Assembly - Inboard and Outboard  OC         A B C     ST

Gear Box Assembly - Flap Drive       6,000         B C

Indicator - Aileron Trim            12,000           C

Indicator - Flap Position           12,000           C

Indicator - Pitch Trim              12,000           C 2C

Indicator - Rudder Trim             12,000           C

Indicator - Spoiler Position         6,000           C 2C

Limit Switch - Flap Position         6,000         B C

Regulator Assembly - Control Cable

Tension (All Control Systems)         OC           B C     ST

Rudder Assembly                       OC         A B C     ST

Shaker - Control Column             12,000         B C

Spoiler Panels - Inboard, Outboard

Upper and Lower                       OC         A B C     ST

Transmitter, Angle of Attack         6,000         B C

Transmitter - Flap Drive Sprocket,

Position                            12,000           C 2C

Transmitter - Flap Position          6,000           C

Transmitter - Pitch Trim Position    6,000           C 2C

Transmitter - Spoiler Position       6,000           C 2C

Valve, Flow Control, Pitch Trim      6,000         B C

Valve, Spoiler, Shutoff, Manual       OC             C

Fuel System, Chapter 28               OC         A B C 3C S ST

Actuator, Fuel Shut-Off Valve       12,000           C

Control Unit, Fuel Sensing          12,000           C

Indicator, Fuel Pressure            12,000       A B C

Indicator, Fuel Tank Quantity       12,000       A B C 3C S

Indicator, Total Fuel Quantity      12,000       A B C 3C S

Pump, Fuel Boost                     6,000       A B C

Pump, Fuel, SPR Drain               12,000       A B C

Switch, Boost Pump Low Pressure

Warning                               OC         A B C

Effective date ____________________

Page 7 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL 300 (C-141A)

Overhaul      Inspection and

Fuel System, Chapter 28 Continued   Period        Check Period

Switch, Fuel Inlet Pressure           OC      A B C

Tank Unit, Fuel Quantity              OC      A B C 3C    S ST

Transmitter, Fuel Pressure          12,000    A B C

Valve, APU Fuel Shut-Off Supply       OC      A B C

Valve, Fuel Level Control           12,000    A B C         ST

Valve, Fuel, Manual Shut-off          OC          C       S ST

Valve, Fuel Shut-Off                12,000    A B C       S ST

Hydraulic Power, Chapter 29           OC      A B C 2C 3C 6C S ST

Accumulator                         12,000    A B C         ST

Filter-Air Vent Line                  OC        B C 2C    S

Filter - Hydraulic                    OC        B C 3C    S

Fuse - Hydraulic                      OC        B C

Gage - System Pressure, Direct

Reading                               OC      A B C       S

Indicator, Hydraulic Pressure       12,000    A B C       S

Pump - Suction Boost, Hydraulic

Driven                               6,000      B C       S

Pump - Hand Operated                  OC        B C       6C

Pump - Hydraulic, Engine Driven      4,000      B C       S

Pump - Hydraulic, Electric Driven    6,000      B C       S

Pump - Suction Boost, Electric

Driven                               6,000      B C       S

Pressure Transmitter                12,000      B C       S

Reservoir                             OC      A B C       S

Snubber - Pressure Line               OC          C

Switch - Low Pressure Warning         OC          C

Valve - Interconnect                  OC          C

Valve - Inline Relief, Case Drain     OC          C

Valve - Motor Operated, Shut-Off    12,000        C

Valve - Pressure Relief (3560)      12,000        C

Valve - Pressure Shut-Off           12,000        C       S

Valve - Solenoid Operated, 3-way    12,000        C

Valve - Solenoid Operated, 4-way    12,000        C

Valve - Drain Line Shut-Off           OC          C

Ice and Rain Protection, Chapter 30   OC      A B C       S

Auto-Transformer, Windshield Heat     OC          C

Box, Control, Windshield Heat         OC          C

Control Box, Temperature Sensing

Rain Removal                         6,000        C

Controller, Temperature, Empennage

De-Icing System                       OC          C

Detector, Ice                         OC          C

Nozzle, Rain Removal                  OC          C

Sensor, Temperature Control, Wing

Anti-Ice                              OC          C

Switch, Overheat, Wing Anti-Ice       OC          C

Valve, Drain, Windshield Rain

Removal                               OC          C

Valve, Modulating, Wing Anti-Ice    12,000        C

Effective date ____________________

Page 8 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL 300 (C-141A)

Ice and Rain Protection,            Overhaul      Inspection and

Chapter 30 Continued                Period        Check Period

Valve, Pressure Regulating and

Shut-Off, Rain Removal              12,000            C

Valve, Pressure Relief, Rain

Removal Duct                          OC              C

Valve, Shut-Off, Rain Removal       12,000            C

Windshield, NESA                      OC          A B C

Instruments, Chapter 31               OC          A B C      S

Accelerometer                       12,000        A B C

Accelerometer, Sensor, Flight

Recorder                             3,000            C

Clock                                 OC          A B C

Recorder, Flight                     3,000        A B C

Landing Gear, Chapter 32              OC          A B C 6C   S ST

Actuator, MLG Downlock              12,000        A B C

Actuator, NLG Steering               9,000        A B C

Actuator, NLG Up-Down Lock          12,000        A B C

Actuator, Uplock, MLG               12,000        A B C

Assembly, MLG                        9,000        A B C

Assembly, NLG                        9,000        A B C

Brake Assembly, MLG                   OC          A B C

Control Box, Anti-Skid               3,000          B C

Control Box, Touchdown               6,000          B C

Control Panel, Landing Gear           OC          A B C

Cylinder, MLG Actuating              6,000        A B C

Cylinder, NLG Actuating             12,000        A B C

Detector, Anti-Skid                  6,000            C

Fuse, Hydraulic Brake               12,000          B C

Horn, Warning                         OC          A B C

Indicator, Brake Pressure             OC          A B C

Indicator, Panel, Bogie Position      OC          A B C

Relay, MLG Up and Locked        @   OC              C

Relay, Touchdown                      OC              C

Tire, MLG                             OC          A B C

Tire, NLG                             OC          A B C

Transmitter, Pressure, Brake        12,000          B C

Uplock, MLG                         12,000        A B C

Valve, By Pass, Manual                OC              C

Valve, Control, Dual Brake

Anti-Skid                            6,000            C

Valve, Downlock Selector, MLG       12,000          B C

Valve, Dual Metering Brake (Pilot)  12,000          B C

Valve, Flow Regulation, MLG           OC              C

Valve, Flow Regulation, NLG           OC              C

Valve, Main Brake Metering          12,000            C

Valve, Pressure Relief (1200)       12,000            C 6C

Valve, Selector, Brake              12,000            C

Valve, Selector, MLG                12,000            C

Effective date ____________________

Page 9 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL 300 (C-141A)

Overhaul      Inspection and

Landing Gear, Chapter 32 Continued  Period        Check Period

Valve, Selector, NLG                12,000            C

Valve, Selector, NLG Emergency,

Manual                                OC              C

Valve, Shutter, Brake                 OC              C

Wheel, MLG                            OC          A B C Note (1)

Wheel, NLG                            OC          A B C Note (1)

Note (1):  Visually inspect at each tire change and perform

non-destructive inspection at each 15th tire change.

Lights, Chapter 33                    OC          A B C      ST

Control - Master Caution,

Annunciator                           OC          A B C      ST

Light, Anti-Collision                3,000        A B C      ST

Light, Emergency Exit                6,000        A B C      ST

Light, Landing                       3,000        A B C      ST

Lights, Navigation                    OC          A B C      ST

Navigation, Chapter 34                OC          A B C 2C S

Altimeter - Pressure                 6,000        A B C 2C S

Amplifier - Slaving, Gyro Compass    3,000          B C    S

Amplifier - Airspeed - Mach Number   3,000          B C    S

Amplifier - Altitude - Vertical

Speed                                3,000          B C    S

Amplifier - Servo Gyro Compass       3,000          B C    S

Amplifier - Audible Warning           OC            B C    S

Compass - Magnetic, Pilots Standby    OC            B C    S

Computer - Central Air Data          1,000          B C    S

Computer - Flight Director           3,000          B C    S

Controller - Gyro Compass            3,000        A B C    S

Flux Valve and Compensator           3,000          B C    S

Generator - Audible Warning           OC            B C    S

Gyro-Directional                     2,000          B C    S

Gyro-Rate Switching                  3,000          B C    S

Gyro-Vertical                        2,000          B C    S

Indicator - Attitude Director        2,000        A B C    S

Indicator - Airspeed, Mach Number    3,000        A B C 2C S

Indicator - Airspeed, Standby        6,000        A B C 2C S

Indicator - Altitude, Vertical Speed 3,000        A B C    S

Indicator - BDHI                     2,000        A B C    S

Indicator - Horizontal Situation     2,000        A B C    S

Indicator - Total Air Temperature     OC          A B C    S

Keyer, Audible Warning (Underspoiler

Speed Warning)                        OC            B C    S

Power Supply - Gyro Compass          3,000          B C    S

Probe - Total Air Temperature         OC          A B C    S

Rack - Gyro Compass                   OC            B C    S

Sensor - Rate of Turn                2,000          B C    S

Tube - Pitot Static                   OC          A B C 2C S

Requirements for additional equipment may be determined by

assigned inspector.

Effective date ____________________

PAGE 10 of 12 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL 300 (C-141A)

Overhaul      Inspection &

Oxygen Chapter 35                   Period        Check Period

Oxygen                                OC          A B C     S

Cylinder Assembly                     *           A B C     S

Pressure Reducer                    5 years       A B C     S

Gage - Remote Pressure               6,000        A B C     S

Mask, Oxygen                          OC          A B C

Oxygen Cylinder - Portable            *           A B C     S

Regulator, Oxygen                    6,000        A B C     S

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Pneumatic System, Chapter 36          OC          A B C 2C

Indicator-Pressure, Bleed Air

Manifold                            12,000        A B C 2C

Transmitter-Pressure, Bleed Air

Manifold                            12,000            C 2C

Valve - Shut-Off, Bleed Air          6,000            C 2C

Auxiliary Power, Chapter 49           OC          A B C     S

Auxiliary Power Plant           ** E.T.I. 1250    A B C     S

or                   Note 1

5,000 Starts

Tank, Oil, APU                        OC          A B C

** Note 1:  Whichever occurs first.

Doors, Chapter 52                     OC         A B C 2C 6C S ST

Actuator, Cargo Ramp                12,000        A B C

Actuator, Pedal Door and Ramp Lock  12,000        A B C

Actuator, Pressure Door             12,000        A B C

Actuator, Pressure Door Down Lock   12,000        A B C

Actuator, Pressure Door Up Lock     12,000        A B C

Central Gear Box Assy., Pedal Door

Actuator                            12,000        A B C

Jack Screw Assembly, Pedal Door

Actuator                            12,000        A B C

Valve, Flow Regulation              12,000          B C

Valve, Pressure Door, Selector      12,000          B C

Valve, Pressure Reducing, Cargo

Ramp                                12,000          B C

Valve, Selector, Door Locks         12,000          B C

Valve, Shuttle, Ramp Lock &

Pressure Door                       12,000          B C

Fuselage, Chapter 53                Structural inspection

Nacelles, Chapter 54                requirements are as specified

Stabilizers, Chapter 55             in Parts I, III, and IV of

Windows, Chapter 56                 Lockheed Service Publication

Wings, Chapter 57                   SMP No. 231 dated June 1,

1967.

Power Plant, Chapter 71               OC          A B C EC  S

Mount, Engine                         EC            B C EC  S

Cowling                               OC          A B C EC

Firewall                              OC            B C EC

Effective date ____________________

Page 11 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL 300 (C-141A)

Overhaul      Inspection and

Period        Check Period

Engine - Turbine, Chapter 72          OC          A B C EO    S

Engine, Turbo Fan P&W TF-33-P7/

JT3D-5A                              4,000        A B C EO    S

Note I

Note I:  Major Inspection at

2,000 hours.

Engine Fuel and Control, Chapter 73               A B C EO

Actuator, Fuel Shut-Off               EO            B C

Control, Fuel                         EO            B C

Filter Assembly, Fuel De-Icing        OC            B C EO

Heater, Fuel De-Icing                 EO            B C

Indicator, Engine Fuel Inlet

Temperature                         12,000        A B C

Indicator, Fuel Flow                 2,000        A B C

Pump, Fuel                            EO            B C

Switch, Differential Pressure         OC            B C EO/FC

Switch, Inlet Pressure                OC            B C EO/FC

Transmitter, Rate of Flow, Fuel     2 EO            B C

Valve Assembly, Fuel Pressurization

and Dump                              EO            B C

Ignition, Chapter 74                              A B C EO

Cable, Exciter, Electrical Power      EO            B C

Cable, Special Purpose                EO            B C

Exciter, Ignition                     EO            B C

Plug, Igniter                         OC              C EO

Engine Air, Chapter 75                            A B C EO

Actuator, Compressor Bleed            EO            B C

Regulator, Anti-Icing Air             EO            B C

Regulator, Duct Seal Pressure         OC            B C EO/FC

Regulator, Pressure, CSD Oil Tank     OC            B C EO/FC

Valve and Actuator Assembly,

Anti-Icing Air                        EO            B C

Valve Assembly, Breather

Pressurizing                          EO            B C

Valve, Bleed Air Shut-Off             EO            B C

Valve, Check, Duct Seal Pressure      OC            B C EO/FC

Valve, Compressor Bleed               EO            B C

Valve and Control Assembly,

Compressor Bleed                      EO            B C

Valve, Nacelle Preheat                OC            B C EO/FC

Valve, Nose Cowl Anti-Ice             OC            B C EO/FC

Valve, Shut-Off, Compartment Cooling

(Zone I)                              OC            B C EO/FC

Valve, Shut-Off, Compartment Cooling

(Zone II)                             OC            B C EO/FC

Engine Controls, Chapter 76                       A B C EC    ST

Power Lever System, Cables, Pulley,

Rods and Linkages                     OC            B C EC    ST

Tension Regulator, Throttle           OC                EC

Effective date ____________________

Page 12 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED MODEL 300 (C-141A)

Overhaul      Inspection and

Period        Check Period

Engine Indicating, Chapter 77                     A B C 2C   S

Converter, Engine Instrument         3,000          B C

Generator, Tachometer                 EO            B C

Indicator, Engine Pressure Ratio     2,000        A B C 2C

Indicator, Engine Vibration          6,000        A B C

Indicator, Exhaust Gas Temperature   2,000        A B C 2C

Indicator, Tachometer                2,000        A B C

Pick-Up, Engine Vibration             EO              C

Transmitter, Pressure Ratio           EO              C 2C

Exhaust, Chapter 78                               A B C EO   S

Actuator, Thrust Reverser            2EO          A B C EO

Control, Thrust Reverser             2EO            B C EO

Door, Thrust Reverser                 OC          A B C EO

Filter, Thrust Reverser               OC            B C EO

Nozzle Assembly, Primary Exhaust      EO          A B C

Pump, Thrust Reverser                2EO            B C EO

Telescopic Unit, Thrust Reverser      OC          A B C EO

Valve, Flow Regulator, Thrust

Reverser                              OC            B C EO

Valve, Relief                         OC            B C EO/FC

Engine Oil, Chapter 79                            A B C EO   S

Bulb, Temperature                     OC              C EO

Cooler Assembly, Fuel Oil Coolant     EO            B C

Heat Exchanger, Air-Oil               EO            B C

Indicator, Engine Oil Temperature    6,000        A B C

Indicator, Oil Pressure              6,000        A B C

Pump Assembly, Oil                    EO              C

Strainer Assembly, Oil, Main          OC              C EO

Switch, Low Oil Quantity              OC              C EO

Switch, Oil Pressure                  OC              C EO

Tank Assy., Lubricating Oil           EO            B C

Transmitter, Oil Pressure             EO            B C

Valve, Oil Pressure Relief            EO              C

Starting, Chapter 80                  OC          A B C EO

Starter, Engine                       EO            B C

Valve, Pressure Regulating            EO            B C

Effective date ____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 31.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- LOCKHEED JETSTAR - MODEL 1329

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

Page 1 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

LOCKHEED JETSTAR - MODEL 1329

Aircraft shall not be utilized in air carrier or commercial

operations unless:

a.   The aircraft and its component parts, accessories and

appliances are maintained in an airworthy condition in

accordance with the operator's maintenance manual.  Such

manual shall at least include the methods, procedures and

limitations contained in the Lockheed JetStar Handbook of

Operating and Maintenance Instructions.

b.   The aircraft and its component parts, accessories, and

appliances are maintained in an airworthy condition in

accordance with the maximum time limits hereinafter set

forth for the accomplishment of the overhaul, periodic

inspection, and routine checks of the aircraft and its

component parts, accessories, and appliances.

c.   OC "On Condition" items will be maintained in continuous

airworthy condition by periodic and progressive inspections

and checks, services, repair and/or preventive maintenance

and are appropriately described in the operator's

maintenance manual.

d.   Parts or sub-components not listed herein will be checked,

inspected and/or overhauled at the same time limits

specified for the component or accessory to which they are

related.

Abbreviations used in the JetStar Model 1329 maintenance

specifications are defined as follows:

PF - Indicates "Preflight Inspection"

FC - Indicates "Functional Check"

BC - Indicates "Bench Check"

EO - Indicates "Engine Overhaul"

EC - Indicates "Engine Change"

OC - Indicates "On Condition"

R&R - Indicates "Remove and Replace"

HYD - Indicates "Hydrostatic Test"

C - Indicates "Calibration"

ST - Indicates "Scrap Time"

DI - Indicates "Detailed Inspection" in accordance with

manufacturer's methods and procedures

ETI - Elapsed Time Indicated

Effective date ____________________

Page 2 Of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED JETSTAR - MODEL 1329

Preflight Inspection/Check

To be accomplished each service calendar day.

"A" Inspection/Check

To be accomplished at intervals not to exceed 80 hours time

in service after the preceding "B" or "C" Inspection/Check

period.

"B" Inspection/Check

To be accomplished at intervals not to exceed 160 hours time

in service after preceding "B" or "C" Inspection/Check

period.

"C"  Inspection/Check

To be accomplished at intervals not to exceed 640 hours time

in service after preceding "C" Inspection/Check period.

Special Inspections

The frequency and procedure for performing special

inspections will be accomplished as specified in the

operator's maintenance manual.

Overhaul and inspection/check period time limitations

specified in hours and calendar time are maximum limits of

whichever occurs first.

Effective date ____________________

Page 3 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED JETSTAR - MODEL 1329

OVERHAUL         INSPECTION &

HOURS OR YRS.      CHECK PERIOD    OTHER

Air-Conditioning,

Chapter 21      10,000             PF  A  B C

Actuator Emerg.

Press.           2,600/5 yrs.             B C

Controller Cabin

Press.           2,600/5 yrs.             B C

Control Temper-

ature            OC                       B C

Exchanger Heat     2,000                    B C

Fan Turbine Assy.  1,200                    B C

Indicator Cabin

Air Temp.        5,000             PF  A  B C

Indicator Cabin

Rate of Climb    2,600             PF  A  B C

Indicator Duel

Altimeter/Diff.

Press.           4,000             PF  A  B C

Oil Change,

Cooling Turbine    640                    B C

Relay Cabin Press. 2,600/5 yrs.             B C

Regulator Cooling

Fan Assy.        2,600/5 yrs.             B C

Refrigeration

Assy.            3,000                    B C

Valve Bleed-Air

Flow Control     2,600                    B C

Valve Shut-Off

Flt. Station     2,600/5 yrs.             B C

Valve Shut-Off

Emerg. Press.    2,600/5 yrs.             B C

Valve Shut-Off

Engine Bleed     2,600/5 yrs.             B C

Valve Out-Flow

Cabin Press.     1,200                    B C

Valve Needle

Cabin Press.     2,600/5 yrs.             B C

Valve Check        5,000                    B C

Auto-Pilot,

Chapter 22      10,000             PF  A  B C

Accelerometer      OC                         C

Bracket Assy.

Servo Drive      2,000/2 yrs.             B C

Coupler Engage     OC                    A  B C

Computer           OC                       B C  (B C at "C")

Control Altitude   2,000/2 yrs.             B C

Controller         2,000/2 yrs.             B C

Drive Aileron

Servo            2,000/2 yrs.             B C

Drive Elevator and

Rudder Servo     2,000/2 yrs.             B C

Gyro Rate          2,000/2 yrs.             B C

Gyro Vertical      2,000/2 yrs.             B C

Communications,

Chapter 23      10,000             PF  A  B C

To be determined

by assigned

inspector.

Effective date ____________________

PAGE 4 of 11 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED JETSTAR - MODEL 1329

OVERHAUL         INSPECTION &

HOURS OR YRS.      CHECK PERIOD    OTHER

Electrical Power,

Chapter 24      10,000             PF  A  B  C

Battery             OC               PF  A  B  C

Contactor,

Generator Line   4,000                    B  C

Control Panel,

Generator        2,000             PF  A  B  C

Generator, Starter 1,200                    B  C  (Inspect

brushes every

400 hrs.)

Inverter, Rotary     800             PF  A  B  C

Loadmeter          4,000                    B  C

Meter Frequency    4,000             PF  A  B  C

Relay, Battery,

Series            OC               PF  A  B  C

Relay, Inverter

Input             OC               PF  A  B  C

Relay, Inverter

Output            OC               PF  A  B  C

Voltmeter          4,000             PF  A  B  C

Equipment/Furnish-

ings, Chapter

25              10,000             PF  A  B  C

Axe Fire            OC               PF  A  B  C

Belts, Seat         OC               PF  A  B  C

Galley              OC               PF  A  B  C

Harness, Shoulder   OC               PF  A  B  C

Kit, First Aid      OC               PF  A  B  C

Lavatory            OC               PF  A  B  C

Mask, Smoke         OC               PF  A  B  C

Raft, Life                     6 mo. PF  A  B  C

Seats               OC               PF  A  B  C

Vest, Life                     6 mo. PF  A  B  C

Fire protection,

Chapter 26      10,000             PF  A  B  C  (Functional

check every

2 1/2 years)

Actuator

Explosive         OC                      B  C  (Replace every

2 years)

Controller, Fire

detection         OC               PF  A  B  C

Element Sensing     OC               PF  A  B  C

Extinguisher,

Portable          *                PF     B  C

Sphere, Fire

Extinguishing     *                       B  C

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date ____________________

PAGE 5 of 11 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED JETSTAR - MODEL 1329

OVERHAUL       INSPECTION &

HOURS OR YRS.    CHECK PERIOD

Flight Controls, Chapter 27      10,000           PF  A  B  C

Actuator Flap                           6 yrs.           B  C

Actuator Flap Screwjack                 6 yrs.           B  C

Actuator Pitch Trim               2,000                  B  C

Booster Assy. Aileron             3,000                  B  C

Booster Assy. Elevator            3,000                  B  C

Compensator Mach Trim             2,000/2 yrs.           B  C

Contactor Stabilizer Trim Normal  1,000                  B  C

Contactor Stabilizer Trim Emerg.  2,000                  B  C

Coupling Flapdrive, L.E.                5 yrs.           B  C

Gear Box Flapdrive, 120 degree          6 yrs.           B  C

Gear Box Flap                     5,000                  B  C

Motor Hydraulic Flap              5,000                  B  C

Motor Pitch Trim Primary          1,000                  B  C

Stop Hydraulic Flap               5,000                  B  C

Fuel, Chapter 28                 10,000           PF  A  B  C

Indicator, Fuel Quantity          2,600           PF  A  B  C

Hose, Fuel Jettison                     1 yr.            B  C

Pump, Fuel Boost Main.

P/N RR 12040B and

P/N RR 12040E                     300                  B  C

P/N RR 12040D and

P/N RR 12040F                   1,000                  B  C

Pump, Fuel Boost Ext. Tanks       1,200                  B  C

Probes, Fuel Quantity              OC             PF  A  B  C

Valve, Motor Shutoff              5,000                  B  C

Hydraulic Power, Chapter 29      10,000           PF  A  B  C

Accumulator                             2 yrs.    PF  A  B  C

Bottle Air Emerg. Lndg. Gear Ext.  *              PF  A  B  C

Filter, Hydraulic Line,

P/N AC-2768-10                   OC             PF   **B  C

P/N AC-2768-101P and P/N

AC-2768-101NBP             **OC/2,500         PF     B  C

Indicator, Hydraulic Press.       5,000           PF  A  B  C

Pump, Hydraulic Electric          3,000           PF  A  B  C

Pump, Hydraulic Engine            1,200               A  B  C

Regulator, Air Pressure                 18 mo.           B  C

Reservoir, Hydraulic               OC             PF  A  B  C

Valve, Engine Shutoff             5,000                  B  C

Valve, Wing Flap Selector Standby       3 yrs.           B  C

Valve, Wing Flap Selector               3 yrs.           B  C

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Effective date ____________________

Page 6 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED JETSTAR - MODEL 1329

@   OVERHAUL         INSPECTION &

HOURS OR YRS.      CHECK PERIOD    OTHER

Hydraulic Power,

Chapter 29

Cont'd.

Valve, Dual

Shuttle          1,800/3 yrs.             B C

Valve, Speed Brake

Selector,

P/N 263-0046           2 yrs.             B C

P/N 263-0067           3 yrs.             B C

Valve, Thrust

Reserver Selector      3 yrs.             B C

Valve, Air

Charging/Relief  1,200                    B C

Valve, Check

Manual Control         5 yrs.

Valve, Main Gear

Door Selector          3 yrs.

Ice and Rain

Protection,

Chapter 30      10,000             PF  A  B C

Motor, Windshield

Wiper            OC                       B C

Valve, De-Icer

Distributor            5 yrs.             B C

Valve, Pressure

Regulator        2,500                    B C

Instruments,

Chapter 31      10,000             PF  A  B C

Accelerometer,

Vertical         OC                       B C  (BC & C every

4,000 hrs.)

Clock              OC                PF  A  B C

Encoder Trip/Data  2,000             PF  A  B C

Indicator Outside

Air Temp.        OC                PF  A  B C

Recorder Flight

Data             2,000             PF  A  B C

Landing Gear,

Chapter 32      10,000             PF  A  B C

Actuator, Nose

Gear Steering   10,000             PF  A  B C

Actuator, Nose

Gear Retract    10,000             PF  A  B C

Actuator, Main

Gear Side

Brace,

P/N JL/1400-9 and

FL1400-11       10,000             PF  A  B C

P/N JL/1400-7     6,000             PF  A  B C

Anti-Skid System   OC                PF  A  B C

Strut, Main

Landing Gear    10,000             PF  A  B C

Strut, Nose

Landing Gear    10,000             PF  A  B C

Tires, Landing

Gear             OC                PF  A  B C

Valve, Brake

Selector               3 yrs.      PF  A  B C

Valve, Landing

Gear Control           4 yrs.             B C

Valve, Nose

Wheel Steering         3 yrs.             B C

Valve, Steering

Selector               3 yrs.      PF     B C

Valve, Brake

Shuttle          1,800/3 yrs.      PF  A  B C

Wheels, Landing

Gear             OC                PF  A  B C     *

Lights, Chapter

33              10,000             PF  A  B C

Battery,

Emergency/

Charger          OC                PF  A  B C

* Magnaflux wheel tie bolts every third tire change, and

dye or zyglo inner and outer wheel halves every "C"

check.

Effective date ____________________

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED JETSTAR - MODEL 1329

OVERHAUL         INSPECTION &

Lights, Chapter   HOURS OR YRS.      CHECK PERIOD    OTHER

33 Cont'd.

Light, Anti-

Collision         OC               PF  A  B  C

Light, Landing      OC               PF  A  B  C

Light, Navigation   OC               PF  A  B  C

Light, Taxi         OC               PF  A  B  C

Navigation,

Chapter 34      10,000             PF  A  B  C

To be determined by assigned inspector.

Oxygen, Chapter

35              10,000             PF  A  B  C

Cylinder Assy.      *                    A  B  C

Pressure Reducer         18 mo.          A  B  C

Cylinder, Portable  *                PF  A  B  C

Mask/Regulator

Passenger              2 yrs.          A  B  C  (FC at B)

Mask, Crew Oxygen        2 yrs.      PF  A  B  C

Panel Control

Pass. Oxygen           2 yrs.          A  B  C

Regulator Crew

Oxygen                 2 yrs.      PF  A  B  C

Valve Pass. Mask

Container Door

Actuator               3 yrs.          A  B  C

Valve Pass. Mask

Lanyard                3 yrs.          A  B  C  (FC at B)

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 172, Chapter I, Subtitle "B" of

CFR Title 49.

Drag Chute,

Chapter 39      10,000             PF  A  B  C

Parachute Assy.

Deceleration      OC                      B  C    **

Airborne

Auxiliary Power,

Chap. 49        10,000             PF  A  B  C

Auxiliary Power

Unit (Solar)     2,000 ETI         PF  A  B  C

Panel Control

Regulator       10,000                       C

Starter/Generator  2,000 ETI                   C  (Inspect

brushes every

400 hrs.)

Doors, Chapter

52              10,000             PF  A  B  C  (Visual

inspect. every

5000 hrs.)

Door, Entrance    10,000             PF  A  B  C

Hatch, Emergency  10,000             PF  A  B  C

Cone, Nose        10,000             PF  A  B  C

**   If not used within last three months, remove chute, aerate,

dry and repack into container in accordance with applicable

directions.

Effective date ____________________

Page 8 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED JETSTAR - MODEL 1329

OVERHAUL         INSPECTION &

HOURS OR YRS.      CHECK PERIOD    OTHER

Fuselage,

Chapter 53      10,000             PF  A  B C   (Visual inspec.

every 5,000

hrs.)

D.1.  Structure   10,000                             "

members at

connections of

main

frame at F.S.

410.5, 429.5,

450.4, 469.5 and

526 between

floor level and

W.L. 100.

D.1.  Structure   10,000                             "

members at F.S.

F.S. 232 thru

277, 410, 526

to 539 R&R as

required.

D.1.  Structure   10,000                             "

members at F.S.

570, 589, and

608.

D.1.  All main    10,000                             "

frames for

distortion,

corrosion and

cracks.

D.1.  Center      10,000                             "

fuselage upper

and lower

structure FS

257 to 270 for

distortion,

corrosion and

cracks.

D.1.  Forward     10,000                             "

upper and lower

fuselage section

F.S. 158 to 270

for distortion,

corrosion, and

cracks.

D.1.  Aft         10,000                             "

fuselage

upper and

lower section

for corrosion,

distortion, and

cracks.

D.1.  Nose and    10,000                             "

equipment

support

structure

for

distortion,

corrosion, and

cracks.

D.1.  Window      10,000                             "

frames for

stress bulges,

cracks, and

corrosion.

D.1.  Engine      10,000                             "

nacelle mount

yoke

D.1.  Empennage   10,000                          (Visual inspec.

upper, lower                                     every 2,500 &

and center                                       5,000 hrs.)

vertical box

structure for

distortion,

corrosion, and

cracks.

Effective date ____________________

Page 9 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED JETSTAR - MODEL 1329

OVERHAUL         INSPECTION &

HOURS OR YRS.      CHECK PERIOD    OTHER

Nacelle/Pylons,

Chapter 54      10,000             PF  A  B C   EC

D.1.  Engine      10,000                          (Visual inspec.

mount structure                                  every 5,000

box beam and                                     hrs.)

frames at N.S.

51.5 and 100.

D.1.  Nacelle     10,000                             "

attach bolts

and bolts and

fittings.

Stabilizer,

Chapter 55      10,000             PF  A  B C      "

D.1.  Elevator    10,000                             "

Hinge Bolts

D.1.  Elevator    10,000                             "

Counterbalances

D.1.  Elevator    10,000                             "

Spar

D.1.  Elevator    10,000                             "

Ribs

D.1.  Horizontal  10,000                             "

Stabilizer

Front Spar and

Ribs

D.1.  Rudder      10,000                             "

Hinge Bolts

D.1.  Rudder      10,000                             "

Counterbalances

D.1.  Rudder      10,000                             "

Hinge Pins

D.1.  Rudder      10,000                             "

Spar

D.1.  Vertical    10,000                             "

Stabilizer Aft

Hinge Pins,                                     (Visual inspec.

Forward Center                                   & magnaflux

and Aft Scissors                                 every 5,000

Joint Bolts                                      hrs.)

Windows,

Chapter 56      10,000             PF  A  B C

Glass, All

Wings,

Chapter 57      10,000             PF  A  B C

D.1.  Wing to     10,000                          (Visual inspec.

Fuselage Attach                                  at 5,000 hrs.)

Bolts at Left

and Right Attach

Frames at F.S.

410 and 430 for

Distortion,

Corrosion, and

Cracks

D.1.  Visually           3 yrs.

Inspect Fuel

Tank Interior

for Corrosion,

Cracks, & Con-

dition.

D.1.  Wing        10,000                          (Visual inspec.

forward, center,                                 every 5,000

and aft spars                                    hrs.)

for distortion,

corrosion, and

cracks.

Effective date ____________________

Page 10 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED JETSTAR - MODEL 1329

OVERHAUL         INSPECTION &

HOURS OR YRS.      CHECK PERIOD    OTHER

Wings, Chapter

57, Cont'd.

D.1.  Root rib    10,000                          (Visual inspec.

and sheer                                        every 5,000

fittings for                                     hrs.)

distortion,

corrosion, and

cracks.

D.1.  Aileron     10,000                             "

hinges and

attach fittings.

D.1.  Aileron     10,000                             "

Hinge Bolts

D.1.  Aileron     10,000                             "

Counterbalance

weights

D.1.  Wing        10,000                             "

Trailing Edge

Alignment pins

D.1.  Trim Tab    10,000                             "

Control Hinges

and Fittings

D.1.  Wing        10,000                             "

Trailing Edge Flap

Hinges and

Attach Fittings

D.1.  Forward     10,000                             "

Support Assembly

and Auxiliary

Beam (Remove

Landing Gear)

D.1.  Main        10,000                             "

Landing Gear

Mounting Bolts

Powerplant

General,

Chapter 71                         PF  A  B C

Mount Assembly

Engine           EO                       B C

Engine, Chapter 72                   PF  A  B C

Engine P&W

JT12A-6A         1,500             PF  A  B C

Hot Section

Inspection                                      750 hrs.

Engine P&W

JT12A-8          1,200 *           PF  A  B C

Hot Section

Inspection                                      600 hrs.**

* Sample overhaul the number of engines specified below

at 1,000 hrs. to substantiate 1,200 hrs. T.B.O.

** Perform the number of hot section inspections

specified below at 400 hrs. to substantiate 600 hrs.

hot section inspection frequency.

Number of engines          O.H.

1-4                  1

5-9                  2

10-21                 3

22-61                 4

62-100                5

102 & Above            6

Effective date ____________________

Page 11 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LOCKHEED JETSTAR - MODEL 1329

OVERHAUL         INSPECTION &

HOURS OR YRS.      CHECK PERIOD    OTHER

Engine Fuel

and Control,

Chapter 73                         PF  A  B C

Transmitter Fuel

Flow            EO                        B C

Indicator Fuel

Flow             3,600             PF  A  B C

Fuel Control

Engine          EO                        B C

Fuel Pump

Engine          EO                        B C

Ignition,

Chapter 74                         PF  A  B C     EC

Exciter           EO                        B C

Harness Assembly  EO                        B C

Plug Igniter      OC                        B C

Air, Chapter 75                      PF  A  B C     EC

Bleed Valves

Engine Mounted  EO                        B C

Bleed Air Ducts

Engine Mounted  EO                        B C

Engine Controls

Chapter 76                         PF  A  B C     EC

Throttle Quadrant OC                 PF  A  B C

Linkages and

Pulleys         OC                 PF  A  B C

Engine Indicating,

Chapter 77                         PF  A  B C     EC

Generator

Tachometer       3,000             PF  A  B C

Indicator

Tachometer       3,000             PF  A  B C

Indicator Pressure

Ratio            5,000             PF  A  B C

Indicator E.G.T.   5,000             PF  A  B C

Transmitter E.P.R. 3,000                 A  B C

Exhaust,

Chapter 78                         PF  A  B C     EC

Actuator Thrust

Reverser        OC                 PF  A  B C

Reverser Thrust

Assy.            1,800                    B C

Oil, Chapter 79                      PF  A  B C     EC

Indicator Oil

Pressure         3,000                 A  B C

Indicator Oil

Temperature      5,000                 A  B C

Transmitter Oil

Pressure        EO                     A  B C

Effective date ____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 32.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- SHORT TURBO-SKYVAN (SC-7)

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          Page 1 of 6

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

SHORT TURBO-SKYVAN

Thorough checks shall be accomplished at the following inspection

periods and in accordance with the applicable procedures listed

in ABC Airlines' Maintenance Manual.

INSPECTION PERIODS

A.   Daily inspection to be accomplished before first flight

each day.

B.   Inspection to be accomplished each 75 hours of aircraft

time in service.

C.   Inspection to be accomplished each 300 hours of

aircraft time in service.

D.   Inspection to be accomplished each 600 hours of

aircraft time in service.

E.   Inspection to be accomplished each 900 hours of

aircraft time in service.

F.   Inspection to be accomplished each 1200 hours of

aircraft time in service.

Other repetitive inspections and special sampling programs are

specified in notes.

Where a calendar time is quoted as an alternative to aircraft

time in service for overhaul, inspection or sampling; that which

expires first shall be taken as the time at which the action

called for is carried out.

Abbreviations used in the Short Turbo-Skyvan Maintenance

Specifications are defined as follows:

EO  = engine overhaul

OC  = on condition

YRS = years

Note:  Inspection and overhaul periods for familiar aircraft

parts, attachments, accessories and/or other items not

specifically listed in this Standard Maintenance Specification,

may be determined by the assigned inspector.  Where this is not

done, parts or subcomponents which are not listed, will be

checked, inspected and/or overhauled at the same time limits

specified for the component or accessory to which such parts or

subcomponents are related.

Effective date ____________________

PAGE 2 of 6 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SHORT TURBO-SKYVAN

OVERHAUL         INSPECTION AND CHECK PERIOD

HRS. OR YRS.      PERIODIC            OTHER

Air Conditioning,

Chapter 21       10,000            A B C D E F

Manual Regulator

Valve             3,000/3 yrs.               F

Compressor Bleed

Valves, Rigid

and Flexible

Lines            10,000                C              Note 1

Autopilot,

Chapter 22

May be determined by assigned inspector.

Communications,

Chapter 23

May be determined by assigned inspector.

Electrical Power,

Chapter 24       10,000            A B C D E F

Undervoltage Unit    OC                      E

Transistorized

Inverter           OC                      E

Contactor, Battery  6,000/5 yrs.               F

Starter Generator    EO                B

Magnetic Indicator   OC              A         F

Battery              OC                B

Differential Relay  1,200                C

Overvoltage

Protector         1,000                C

Contactor, Cross

Couple                  5 yrs.               F

Voltage Regulator   1,000                C

Equipment &

Furnishings,

Chapter 25

May be determined by assigned inspector.

Fire Protection,

Chapter 26       10,000            A B C D E F

Detector Elements    EO                B       F

Extinguisher -

Engine             *               A                  Note 2

Cartridge Unit            2 yrs.       B

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Flight Controls,

Chapter 27       10,000            A B C D E F

Position Indicator

System            6,000            A   C

Cables, Turnbarrels,

Pulleys Pushrods,

Sprockets &

Chains             OC                        F        Note 3

Effective date ____________________

Page 3 of 6

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SHORT TURBO-SKYVAN

OVERHAUL         INSPECTION AND CHECK PERIOD

HRS. OR YRS.      PERIODIC          OTHER

Fuel System,

Chapter 28       10,000            A B C D E F

Flex Tanks          4 Yrs.           A         F        Note 4

Vent Valve           OC                        F

Collector Tank     10,000            A                  Note 5

Booster Pump        1,000              B

Filter               OC              A         F        Note 6

Pressure Switch     3,000/2 Yrs.               F

Tank Units          4 Yrs.           A                  Note 4

Hydraulic System,

Chapter 29       10,000            A B C D E F

Power Pack          5,000            A B C

Emergency

Accumulator       5,000            A B C

Filter               OC                                 Note 6

Pressure Switch     2,000            A         F

Vent Valve          2,000                      F

Ice & Rain,

Chapter 30       10,000            A B C D E F

De-Icer Boots        OC              A B

Distributor Valve   2,400              B C

Electronic Timer    2,400                C

Regulating & Relief

Valves            2,400                      F        Note 7

Air Intake Anti-

Icing Valve       1,200                C

Contactor, Prop

Anti-Icing        5,000                    E

Cyclic Timer        1,800                    E

Instruments,

Chapter 31

May be determined

by assigned

inspector.

Landing Gear,

Chapter 32       10,000            A B C D E F

Main Leg Assembly  10,000            A B C              Note 8

Shock Absorber     10,000            A B C              Note 8

Steering Jack       5,000            A   C

Nose Gear Leg

Assembly         10,000            A B C              Note 8

Brake Control

Valve             5,000            A   C

Pressure Reducing

Valve             5,000            A   C

Brake Master

Cylinder          5,000            A B C

Pressure Relay      2,400                C

Wheels, Tires and

Brakes             OC              A B C

Lights, Chapter 33

May be determined

by assigned

inspector.

Effective date ____________________

PAGE 4 of 6 PAGES

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SHORT TURBO-SKYVAN

OVERHAUL         INSPECTION AND CHECK PERIOD

HRS. OR YRS.      PERIODIC          OTHER

Navigation,

Chapter 34

May be determined by assigned inspector.

Oxygen, Chapter 35

Cylinders              *

* Hydrostatic and life limits shall be entered here and shall not

exceed those set forth in Part 173, Chapter I, Subtitle "B" of

CFR Title 49.

Doors, Chapter 52    10,000          A B C D E F

Passenger/Crew Doors

and Frames         10,000          A B C              Note 9

Ditching Hatch &

Frames             10,000          A B C              Note 9

Rear Cargo Door &

Frame              10,000          A B C              Note 9

Fuselage, General,

Chapter 53         10,000          A B C D E F

Skin, Outside

Surfaces             OC            A B C

Internal Structure

Including Windows

& Frames           10,000              C           Note 9 & 10

Floor Panels (Cabin) 10,000          A         F     Note 9

Floor Panels (Flight

Deck)              10,000          A         F     Note 9

MLG Attach Fittings

& Structure        Note 12             C           Note 12

NLG Attach Fittings

& Structure        10,000              C           Note 9

Nose Fairing           OC            A   C

Main Spars - Stub

Wings              Note 12                   F     Note 12

Nacelle Structure,

Chapter 54         10,000          A B C D E F

External Structure     OC            A B

Internal Structure     EO                C

Attach Fittings &

Structure          10,000                    F     Note 11

Stabilizers and

Stabilizer Control

Surfaces,

Chapter 55         10,000          A B C D E F

Exterior Surfaces,

Stabilizers          OC            A B C

Interior Structure,

Stabilizers        10,000                  E          Note 9

Exterior Control

Surfaces             OC            A   C

Interior Control

Surface Structure  10,000                  E          Note 9

Attach Fittings &

Hinges             10,000                    F        Note 9

Effective date ____________________

Page 5 of 6

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SHORT TURBO-SKYVAN

OVERHAUL         INSPECTION AND CHECK PERIOD

HRS. OR YRS.      PERIODIC           OTHER

Windows,

Chapter 56       10,000            A B C D E F

DV Window Lock

Mechanism          OC              A   C

Wings, Chapter 57  10,000            A B C D E F

Exterior Surfaces    OC              A B C

Interior Structure 10,000                      F        Note 9

Wing Strut

Exterior Surface   OC              A B C

Wing Strut

Internal         10,000                      F        Note 9

Wing Fuselage

Attachments      10,000                      F        Note 11

Attachment Strut/

Wing             10,000                C              Note 11

Aileron & Tab

Exterior

Surfaces           OC              A B C

Aileron & Tab

Internal

Structure        10,000                    E          Note 9

Flaps Exterior

Surface            OC              A B C

Flaps Interior

Structure        10,000                    E          Note 9

All Hinges &

Brackets         10,000            A   C              Note 9

Propeller,

Chapter 61          750            A B C

Propeller FH 76       750            A B C

Propeller Hub         750            A B C

Engine, Chapter 72    750            A B C

Astazou XII           750            A B C

Engine Controls,

Chapter 76       10,000            A B C D E F

Cables, Turnbarrels

and Pulleys Aft

of Firewall      10,000                C              Note 3

Prop Contactor Box   EO                B

Automatic Control

Box                EO                B

Power Limiter        EO                B

Leak Valve           EO                B

Speed Governor       EO                B

Pitch Motor          EO                B

Prop Microswitch

Assembly           EO                B

Emergency FFP Stop

Switch             EO                B

Engine Indicating,

Chapter 77       10,000            A B C D E F

Power Indicator

Potentiometer      OC              A         F

Percent Power

Indicator         6,000            A         F

Jet Pipe Temp.

Indicator         6,000            A         F

Exhaust, Chapter 78  EO              A B C

Engine Oil,

Chapter 79         EO              A B C

Effective date ____________________

Page 6 of 6

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SHORT TURBO-SKYVAN

Note 1    Remove lagging at 2,500 and 5,000 hours for sample

inspections in accordance with factory instructions.

Note 2    Weigh bottles each 3 months.  Hydrostatic test each 5

years.

Note 3    Check cable tension each year.

Note 4    Check tank quantity indicator capacitance units and

internal surfaces of flex tanks every 2 years.

Note 5    Check collector tank and negative "G" valve-vent, in

accordance with factory instructions, when booster pump

is changed.

Note 6    Replace filter elements at times specified by factory.

Note 7    Sample overhaul 1 valve at 1,200 hours.

Note 8    Sample overhaul main gear and nose gear assemblies at

5,000 hours in conjunction with Note 11.

Note 9    Sample overhaul of structure in accordance with factory

instructions at 5,000 hours or 5 years.

Note 10   Remove windows and skin access panels in accordance

with factory instructions every 5,000 hours or 5 years

in order to check for corrosion of skin and skin

corrugations.

Note 11   Remove and inspect sample bolts and/or pins in

accordance with factory instructions every 5,000 hours.

Note 12   Check for fatigue damage in accordance with factory

instructions initially at 12,000 landings and each

2,000 landings thereafter until a total of 20,000

landings, then every 1,000 landings.

Effective date ____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 33.  OPERATIONS SPECIFICATIONS AIRCRAFT MAINTENANCE

- SIKORSKY S-61L/N HELICOPTER

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

Part D                                        Page 1 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SIKORSKY S-61L/N HELICOPTER

Overhaul      Inspection &

Period        Check Period

Air Conditioning, Chapter 21        9,000

Heater Assembly                     2,000

Ducting, Heater Compartment         O.C.

Fuel Control Assembly, Heater       2,000

Blower, Cabin Ventilation           2,500

Relay, Blower, Heater               O.C.

Relay Heater, Ventilation Blower    O.C.

Relay, Heater Overheat              O.C.

Control Unit, Heater                2,000

Valve, Heater Fuel Shut-off         2,000

Sensing Elements, Cabin Air         O.C.

D.C. Motor, Cabin Air Sensing       1,500

Ignition Unit                       2,000

Switch, Air Ram Pressure            O.C.

Switch, Thermal Overheat            O.C.

Switch, Fan Thermal Overrun         O.C.

Switch, Thermal Cycling             O.C.

Switch, Outside Air Temperature     O.C.

Sensing Element, Heater Discharge   O.C.

Light, Warning                      O.C.

Circuit Breakers                    O.C.

Switches                            O.C.

Rheostat, Temperature Selector      O.C.

Wiring and Connections              O.C.

Ducting Installation, Cabin         9,000

Air Vent Installation, Cabin        9,000

Ducting Installation, Cockpit       9,000

Lines and Fittings, Fuel (Airframe) O.C.

Relay, Time Delay                   O.C.     Functional Check

Valve, Backfire                     O.C.

Automatic Flight Control System, Chapter 22

May be determined by the assigned inspector.

Communications System, Chapter 23

May be determined by the assigned inspector.

Effective date ____________________

Page 2 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SIKORSKY S-61L/N HELICOPTER

Overhaul      Inspection &

Period        Check Period

Electrical Power, Chapter 24        9,000

Power System DC

Battery                             O.C.

Relay, Battery                      O.C.

Regulator, Voltage (DC)             1,200

Relay, Over Volt Field Control      1,200

Generator/Motor                     1,000

Relays, Reverse Current             2,000

Relay, External Power (DC)          O.C.

Relay Motorizing                    2,000

Transformer Rectifier               1,500

Receptacle, External Power (DC)     O.C.

Support, Battery Vibration Absorber 1,000

Power System AC

Generators (AC)                     1,500

Brushless Type (AC)                 2,500

Regulators, Voltage (AC)            1,200

Panels, Supervisory (AC)            1,200

Line Contactors, Generators (AC)    2,000

Relays, External (AC)               O.C.

Relay, External Power Interlock     O.C.

Contactor, Emergency Essential Bus  2,000

Inverter                            1,000

Receptacle, External Power          O.C.

Transformers, Power Step-Down       O.C.

Test Receptacle, AC/DC              O.C.

AC & DC Systems

Wiring and Connections              O.C.

Switches                            O.C.

Circuit Protectors                  O.C.

Relay, Inverter                     O.C.

Lights, Warning                     O.C.

Static Discharge Wicks              O.C.

Relay, Inverter Transfer            O.C.

Equipment and Furnishing,

Chapter 25                        9,000

First Aid Kits

Cabin, Passenger                    O.C.

Cockpit                             O.C.

Effective date ____________________

Page 3 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SIKORSKY S-61L/N HELICOPTER

Overhaul      Inspection &

Period        Check Period

Seats - Cockpit

Seat Belts                          O.C.

Shoulder Harnesses and Reels        9,000

Seats                               9,000

Seats - Passenger Cabin

Seat Belts                          O.C.

Seats and Attachments               9,000

Cabin Interior

Upholstery                          O.C.

Partition, Cabin Movable            O.C.

Fire Protection, Chapter 26         9,000

Fire Detection System - Engine

Control Units, Fire detection       O.C.

Sensing Loops and Fittings **       O.C.     Functional Check

Lights, Warning                     O.C.

Wiring and Connections              O.C.

Circuit Protectors                  O.C.

Switches                            O.C.

Fire Extinguisher - Head

Cabin                               O.C.

Cockpit                             O.C.

Fire Extinguisher System - Engine * Engine Change

Lines and Nozzles *                 O.C.

Handles, Fire Control               O.C.

Switch, Fire Extinguishing          O.C.

Container and Valve Assembly        O.C.

Wiring and Connectors               O.C.

Indicator, Thermal Discharge        O.C.

Supports, Fire Extinguisher

Container                         O.C.

* Directional Flow Check (Nitrogen or Smoke Source)

** Functional Check - Scheduled Engine Change

Using Jetcal Analyzer or Per Sikorsky Maintenance Manual

Effective date ____________________

Page 4 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SIKORSKY S-61L/N HELICOPTER

Overhaul      Inspection &

Period        Check Period

Fuel System, Chapter 28             9,000

Tub Section

Tanks, Fuel                         9,000

Fuel Lines, Fittings                9,000

Pumps, Booster                      1,200

Ejectors                            9,000

Fuel Filter, Airframe               9,000

Valves, Manual Shut-off             9,000

Valve, Cross-feed                   9,000

Pressure Switch, Pump Failure       9,000

Vents, Fuel Tanks                   9,000

Drain Sumps                         9,000

Valves, Fuel Drain                  9,000

Cabin Section Firewall

* Valves, Fuel Shut-off             9,000    Functional Check

Pressure Switches, Fuel Shut-off    9,000

Pressure Fueling System

Valves, High Level Shut-off         9,000

Adapter, Fueling and Defueling      9,000

Valve, Fueling and Defueling        9,000

Float Switches, Intermediate

Level Selector                    O.C.

Lines and Fittings, Fueling Adaptor 9,000

Electrical System

Switches                            O.C.

Circuit Protectors                  O.C.

Lights, Warning                     O.C.

Wiring and Connections              O.C.

Wiring & Conduits (Tank Cells)      O.C.

Lights, Preset                      O.C.

* Functional Check at Engine Change

Effective date ____________________

Page 5 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SIKORSKY S-61L/N HELICOPTER

Overhaul      Inspection &

Period        Check Period

Hydraulic Power, Chapter 29         9,000

Primary Servo System

Reservoir                           O.C.

Pump                                2,000

Manifold Assembly (Includes

6 Items)                          2,000

Relief Valve

Three-Way Solenoid Valve

Filter (Pressure)

Restrictors (By-Pass)

Pressure Switch

Snubber

Check Valves                        O.C.

Hoses, Lines and Fittings           O.C.

Switch, Servo Shut-off              O.C.

Wiring and Connections              O.C.

Lights, Warning                     O.C.

Circuit Protectors                  O.C.

Auxiliary Servo System

Reservoir                           O.C.

Pump                                2,000

Manifold Assembly (Includes

6 Items)                          2,000

Relief Valve

Three-Way Solenoid Valve

Filter (Pressure)

Restrictors (By-Pass)

Pressure Switch

Snubber

Check Valves                        O.C.

Wiring and Connections              O.C.

Switches, Stick Trim                O.C.

Light, Warning                      O.C.

Filter, Auxiliary Servo             O.C.

Ice and Rain Protectors,

Chapter 30                        9,000

Windshield Wiper System

Motor, Wiper                        O.C.

Converters                          O.C.

Arms and Blades, Wiper              O.C.

Wiring and Connections              O.C.

Switch                              O.C.

Effective date ____________________

Page 6 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SIKORSKY S-61L/N HELICOPTER

Overhaul      Inspection &

Ice and Rain Protectors,            Period        Check Period

Chapter 30 (Cont.)

Windshield Washer System

Reservoir                           O.C.

Surgemeter                          O.C.

Nozzles                             O.C.

Hoses, Lines and Fittings           O.C.

Windshield Anti-Icing System

Temperature Controller              O.C.

Auto-Transformers                   O.C.

Windshield Panel, Electropane       O.C.

Wiring and Connections              O.C.

Switches                            O.C.

Pitot Tube Heater System

Heads, Pitot Heat                   O.C.

Wiring and Connectors               O.C.

Lights, Warning                     O.C.

Switches                            O.C.

Relays, Pitot Heater                O.C.

Instruments, Chapter 31             9,000

Power Plant Instruments

Indicators, Gas Generator           O.C.

Indicators, Power Turbine Inlet

Temp.

(Howell Instrument Co.)        O.C.

Indicators, Oil Temperature         O.C.

Indicators, Oil Pressure            O.C.

Transmitters, Oil Pressure

Indicator                         O.C.

Indicators, Fuel Pressure           O.C.

Transmitters, Fuel Pressure

Indicator                         O.C.

Indicators, Triple Tachometer       O.C.

Indicators, Torque Meter            O.C.

Transmitters, Torque Meter

Indicator                         O.C.

Miscellaneous Instruments

Indicator, Transmission Oil

Pressure                          O.C.

Transmitter, Trans. Oil Pressure

Ind.                              O.C.

Indicator, Trans. Oil Temperature   O.C.

Indicator, Primary Hydraulic

Pressure                          O.C.

Indicator, Auxiliary Hyd. Pressure  O.C.

Transmitter, Aux. Hyd. Press. Ind.  O.C.

Indicator, Free Air Temperature     O.C.

Effective date ____________________

Page 7 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SIKORSKY S-61L/N HELICOPTER

Overhaul      Inspection &

Period        Check Period

Miscellaneous Instruments (Cont.)

Ammeter-Voltmeter (DC)              O.C.

Volt-Ammeter (AC)                   O.C.

Indicators, Fuel Quantity           O.C.

Tank Probes, Fuel Quantity          9,000

Control Units, Fuel Low Level       O.C.

Sensors, Fuel Low Level             O.C.

Wire and Connection                 O.C.

Lights, Low Level Warning           O.C.

* Indicator, Landing Gear           O.C.

Transmitter, Primary Hyd. Press.

Ind@                    @ @  O.C.

Landing Gear, Chapter 32            9,000

Main Gear Installation

Strut Assemblies, Shock             5,000

Wheels                              O.C.

Tires                               O.C.

Struts, Energy Absorbing            9,000

Supports                            9,000

Attachment Fitting, Fuselage        9,000

Fairing                             O.C.

Switches, Under Frequency Lockout

Scissors                          O.C.

Wiring and Connections              O.C.

* Hydraulic Pump and Motor Unit     2,000

* Hydraulic Reservoir               2,000

* Filters, Reservoir Panel          O.C.

* Relief and Control Valves         O.C.

* Plug Stat                         O.C.

* Mounting and Supports             O.C.

* Lines and Fittings                O.C.

* Drag Links Upper and Lower        5,000

* Switches                          O.C.

* Control Unit                      O.C.

* Relays, Landing Gear              O.C.

* Relay, Pump Motor                 O.C.

* Emergency Release Control         O.C.

* Shock Strut and Trunnion Assembly 5,000

* Retracting Cylinders              5,000

* Emergency Release Pin, Cables,

and Pulleys                       O.C.

* Uplock Cylinder                   5,000

* Emergency Air Bottle              O.C.

@

* "N" MODEL ONLY

Effective date ____________________

Page 8 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SIKORSKY S-61L/N HELICOPTER

Overhaul      Inspection &

Period        Check Period

Tail Gear Installation

Shock Strut Installation            5,000

Centering Cylinder                  5,000

Attachment, Fuselage                9,000

Wheel                               O.C.

Tire                                O.C.

Control System, Tail Wheel Lock     O.C.

Fairing                             O.C.

Wheel Brake System

Brake Assemblies                    O.C.

Master Cylinders                    9,000

Mixing Valves, Wheel Brake          9,000

Parking Brake Valve                 9,000

Hoses, Lines, Check Valves and

Fittings                          O.C.

Lights, Chapter 33                  9,000

Light Assemblies Position           O.C.

Light Assemblies, Anti-Collision    O.C.

Light Assemblies, Retractable

Landing                           O.C.

Spot Lights, Cockpit                O.C.

Dome Light, Cockpit                 O.C.

Rheostat, Emergency                 O.C.

Light Assemblies, Instruments       O.C.

Rheostats                           O.C.

Light, Master Warning               O.C.

Panel Assemblies, Warning Light     O.C.

Control Unit, Warning Light Dimming O.C.

Dome Lights, Cabin                  O.C.

Reading Lights, Passenger           O.C.

Lights, Cabin Emergency             O.C.

Lights, No Smoking                  O.C.

Lights, Fasten Seat Belts           O.C.

Light Assemblies, Loading           O.C.

Relay, Loading Light                O.C.

Lights, Warning                     O.C.

Wiring and Connections              O.C.

Switches                            O.C.

Riding Light                        O.C.

* "N" MODEL ONLY

Effective date ____________________

Page 9 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SIKORSKY S-61L/N HELICOPTER

Overhaul      Inspection &

Period        Check Period

Navigation, Chapter 34              9,000

Flight and Navigation Instruments

Clocks (Wakeman)                    O.C.

Indicators, Turn and Slip (Allen)   O.C.

Instantaneous Vert. Speed Indicator

(IVIS)

(Specialties Corp.)            O.C.

Indicators, Altimeter (Kollsman)    O.C.

Indicators, Airspeed (Kollsman)     O.C.

Compass, Magnetic (U.S. Gage)       O.C.

Compass, C-4A or C-14A Gyrosyn

System

Amplifier, Gyrosyn Compass          O.C.

Flux Valve and Compensator Assembly O.C.

Control Unit, Gyrosyn Compass       O.C.

Relay, Interlock (DC)               O.C.

Relay, Interlock (AC)               O.C.

Transformer, Power Adapter          O.C.

Gyro and Sync Assembly              O.C.

Servo Amplifier                     O.C.

Annunciator                         O.C.

Vertical Gyro Installation

Indicator, Navigational Lear Model

4005A                             2,500

Gyros, Roll & Pitch Lear Model

7000B                             1,500

Amplifier Navig. Instrument Lear

Model 5510B                       O.C.

Power Adapter Airframe Supplies     O.C.

Wiring Connections                  O.C.

Static & Pitot Systems

Lines and Fittings                  O.C.

Pitot-Static Mast                   MGB OVHL

Doors, Chapter 52 *                 9,000

Cabin

Passenger Doors                     9,000

Release, Mechanisms Door Emergency  9,000

Cargo Door                          9,000

Release Mechanism, Cargo Door       9,000

Lights, Warning, Cargo and

Passenger                         O.C.

* May be accomplished progressively by zones.

(see zone table on page 12 of 15)

Effective date ____________________

Page 10 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SIKORSKY S-61L/N HELICOPTER

Overhaul      Inspection &

Period        Check Period

Doors, Chapter 52 (Cont.)           9,000

Hull

Baggage Doors **                    9,000

Electronic Compartment Door         9,000

Lights, Warning, Baggage &

Electronic Door                   O.C.

Upper Fuselage

Platforms, Engine Servicing         O.C.

Platforms, Transmission Servicing   O.C.

Electrical Systems

Wiring & Connections, Warning

Lights                            O.C.

Switches, Warning Light             O.C.

Fuselage, Chapter 53 *              9,000

Structure, Pylon (Zone 1)           9,000

Structure, Upper Fuselage Engine

Compartment (Zone 2)              9,000

Structure, Upper Fuselage, Main

Gear Box Compartment (Zone 3)     9,000

Support, Main Gear Box (Zone 3)     9,000

Structure, Tail Cone (Zone 4)       9,000

Hull Structure (Zone 6)             9,000

Structure, Cockpit (Zone 7)         9,000

Structure, Electronics Compartment

(Zone 7)                          9,000

Structure, Cabin (Zone 8)           9,000

Structure, Hull (Zone 9)            9,000

Sponsons                            9,000

Stabilizers, Chapter 55 *           9,000

Stabilizer Installation (Zone 1)

Structure, Stabilizer               9,000

Attachment Fittings, Stabilizer     9,000

Support, Tube, Stabilizer           9,000

Windows, Chapter 56 *               9,000

Cockpit

Emergency Escape Exits              9,000

Release Mechanism, Emergency

(Airframe)                        9,000

Windshields and Windows             O.C.

** S-61 L Model Only

* May be accomplished progressively by zones.

(see zone table on page 12 of 15)

Effective date ____________________

Page 11 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SIKORSKY S-61L/N HELICOPTER

Overhaul      Inspection &

Period        Check Period

Windows, Chapter 56 (Cont.)         9,000

Cabin

Windows *                           O.C.

Emergency Escape Exits              9,000

Release Mechanism, Emergency

(Airframe)                        9,000

Rotor System, Chapter 65            9,000

Main Rotor Head Installation

Blades                              O.C.

Main Rotor Head Assembly            1,250

Azimuth Control Star Assembly       1,250

Dampers                             1,250

Bifilar Vibration Assembly          Main Rotor Head O/H

Tail Rotor Installation

Blades                              O.C.

Hub Assembly                        1,250

Flight Controls

Collective Pitch Assembly (Zone 7)  9,000

Collective Pitch Assembly (Zone 8)  9,000

Collective Balance Spring (Zone 7)  9,000

Cyclic Pitch Assembly (Zone 3)      MGB O/H

Cyclic Pitch Assembly (Zone 7)      9,000

Cyclic Pitch Assembly (Zone 8)      9,000

Rudder Flight Control Assembly

(Zone 7)                          9,000

Mixing Unit                         9,000

Force Link Assembly                 9,000

Rudder Flight Control Assembly

(Zone 1)                          9,000

Rudder Flight Control Assembly

(Zone 4)                          9,000

Rudder Flight Control Assembly

(Zone 8)                          9,000

Rudder Pedal Adjusting Installation

(Zone 7)                          9,000

Negative Force Gradient Spring

Assembly                          9,000

Primary Servos                      1,250

Auxiliary Servo with Beeper Trim

Valves                            1,250

Rudder Control Cables               O.C.

Drive Shafts

Tail Drive Shaft, Section I         2,500

Tail Drive Shaft, Section II        2,500

Tail Drive Shaft, Section III       2,500

Tail Drive Shaft, Section IV        2,500

Tail Drive Shaft, Section V         3,000

Support, Tail Drive Shaft Bearings  2,500

* May be accomplished progressively by zones.

(see zone table on page 12 of 15)

Effective date ____________________

Page 12 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SIKORSKY S-61L/N HELICOPTER

Overhaul      Inspection &

Period        Check Period

Rotor System, Chapter 65 (Cont.)    9,000

Gear Boxes

Main Gear Box                       1,250

Intermediate Gear Box               3,000

Tail Gear Box Installation          3,000

Oil Cooler Installation, Main Gear

Box                               MGB O/H

Supports, Oil Cooler Installation   O.C.

Actuator, Rotor Brake Installation  MGB O/H

Accumulator, Rotor Brake            9,000

Relief Valve, Rotor Brake           O.C.

Pressure Switch, Rotor Brake

Warning Light                     O.C.

Master Cylinder, Rotor Brake        9,000

Lines & Fittings, Rotor Brake

Hydraulic                         O.C.

Pressure Switch, MGB Oil Warning    MGB O/H

Lights, Warning                     O.C.

Wiring and Connections              O.C.

Speed Switch, Motor/Generator

(if installed)                    MGB O/H

Note:  Zones and areas referenced are as follows:

ZONE             AREA

1. . . . . . . . Pylon and Stabilizer - Station 622 Aft

2. . . . . . . . Upper Fuselage, Engine Section - Station 178

- 247

3. . . . . . . . Upper Fuselage, Main Gear Box - Station 247

- 362

4. . . . . . . . Tail Cone - Station 493 - 622

5. . . . . . . . Landing Gear (Main and Tail Gear)

6. . . . . . . . Fuel Cells - Station 186 - 323 (Below Water Line

106)

7. . . . . . . . Cockpit and Electronics - Station 0 - 110

8. . . . . . . . Cabin - Station 110 - 493 (Above Water Line 106)

9. . . . . . . . Hull - Station 110 - 186, 323 - 459 (Below Water

Line 106)

Powerplant - General, Chapter 71    1,800

Cowling

Fairing, Intake Duct                O.C.

Cowling, Engine                     O.C.

Firewall                            O.C.

Fire Seal, Rear Support             O.C.

Engine Suspension

Support, Rear                       Eng. O/H

Supports, Front                     Eng. O/H

Effective date ____________________

Page 13 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SIKORSKY S-61L/N HELICOPTER

Overhaul      Inspection &

Period        Check Period

Powerplant - General, Chapter 71

(Cont.)                           1,800

Drive Shaft Installation

Thomas Coupling and Adapter         Eng. O/H

Drive Shaft                         Eng. O/H

Coupling, MGB Input (Drive Shaft

Portion)                          Eng. O/H

Instrumentation

Supports, Indicator Transmitters    9,000

Lines and Fittings, Indicator

Transmitters                      O.C.

Wiring and Connections              O.C.

* Damper Weights and Clamps         O.C.

Engine, Chapter 72                  1,800

Engine

CT58-110-1                          2,000 **

CT58-110-2                          2,400 **

CT58-140-1                          2,400 **

CT58-140-2                          1,500 **

** Major Inspection as defined in G.E. O/H Manual SEI-102

(CT58-110 Engines) and SEI-183 (CT58-140 Engines) is required at

the following intervals:

CT58-110-1                          600

CT58-110-2                          800

CT58-140-1                          800

CT58-140-2                          500

Compressor Section                  Eng. O/H

Combustion & Gas Gen. Section       Eng. O/H

Power Turbine Section               Eng. O/H

Accy Dr. Assy.                      Eng. O/H

Flex. Dr. Shaft                     Eng. O/H ***

*** Lubrication required every 100 hours per SEI-101 or SEI-182.

Lubrication System (Engine)

Lines and Fittings                  O.C.

Lubrication Pump                    Eng. O/H

Oil Cooler                          Eng. O/H

* "N" MODEL ONLY

Effective date ____________________

Page 14 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SIKORSKY S-61L/N HELICOPTER

Overhaul      Inspection &

Period        Check Period

Fuel System (Engine), Chapter 73    Eng. O/H

Lines and Fittings                  O.C.

Fuel Control Unit                   1,600

Flow Divider                        Eng. O/H

Fuel Pump                           1,600

Filter, Centrifugal                 1,600

Filter, Static                      Eng. O/H

Ignition System, Chapter 74         Eng. O/H

Ignitor Unit                        Eng. O/H

Ignitor Plug                        Eng. O/H

Harness, Ignition                   Eng. O/H

Air, Chapter 75                     Eng. O/H

Starter Cover                       O.C.

Intake Duct, Engine Air             O.C.

Boots, Intake Duct Anti-icing

(Heating Element)              O.C.

Thermal Switch, 40 degrees F

Warning                           O.C.

Control Unit, Intake Duct

Anti-icing                        O.C.

Relay, Current Sensing, Warning

Light                             O.C.

Switches, Control                   O.C.

Wiring and Connections              O.C.

Lights, Warning                     O.C.

Relays, Engine Anti-Ice Solenoid    O.C.

Valve, Anti-icing                   Eng. O/H

Lines and Fittings Anti-icing Valve Eng. O/H

Actuator, Variable Vane             Eng. O/H

Pilot Valve, Variable Vane

Actuator                          1,600

Lines and Fittings, Variable Vane

Actuator                          Eng. O/H

Vane Actuator, Linkage and Cable    Eng. O/H

Lines and Fittings Air Bleed

Systems                           Eng. O/H

Lines and Fittings, Compressor

Inlet Temp.                       Eng. O/H

Valve, Starting Bleed (CT58-140-1,

140-2)                            Eng. O/H

Engine Control System, Chapter 76   Eng. O/H

Engine Control System

Control Quadrant Installation       9,000

Cables, Control                     9,000

Pulleys, Control Cable              9,000

Supports, Cable Pulleys             9,000

Control Box, Engine                 9,000

Remote Topping Control Gear Box     9,000

Remote Topping Control Rods         O.C.

Effective date ____________________

Page 15 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SIKORSKY S-61L/N HELICOPTER

Overhaul      Inspection &

Period        Check Period

Engine Control System, Chapter 76

(Cont.)                           Eng. O/H

Emergency Control System

Box Assembly, Teleflex              9,000

Cables, Teleflex                    9,000

Conduit, Teleflex                   9,000

Engine, Indicating, Chapter 77      Eng. O/H

Thermocouple Harnesses              Eng. O/H

Thermocouple Units                  O.C.

Leads, Thermocouple                 O.C.

Generator, Gas Generator Tachometer Eng. O/H

Generator, Power Turbine

Tachometer                        Eng. O/H

Wiring and Connections              O.C.

Engine Exhaust, Chapter 78          O.C.

Exhaust Tail Pipe (Airframe)        O.C.

Oil, Chapter 79                     Eng. O/H

Oil Tank Installation

Hose, Lines and Fittings            O.C.

Support, Oil Tank                   O.C.

Oil Tank                            O.C.

Change Oil (Engine)                 Eng. O/H

Pressure Switches, Low Pressure

Warning                           O.C.     Functional Check

Bulb, Engine Oil Temperature        O.C.

Wiring and Connections              O.C.

Warning Lights, Oil Low Pressure    O.C.

Starting, Chapter 80                Eng. O/H

Starters                            Eng. O/H

Relays, Starters                    Eng. O/H

Wiring and Connections, Starter

(Airframe)                        O.C.

Warning Lights, Starter Drop-Out

Relay                             O.C.

Effective date ____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 34.  OPERATIONS SPECIFICATIONS,

AIRCRAFT MAINTENANCE - LEAR MODEL 24/24B/25

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

Part D                                          Page 1 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

LEAR MODEL 24/24B/25

Inspections shall be accomplished in accordance with the

applicable procedures as listed in ABC Airlines Maintenance

Manual.

Preflight (PF) shall be accomplished each service calendar day.

Inspection shall be in accordance with the applicable procedures

listed in ABC Airlines Maintenance Manual.

Station Check (SC) shall be accomplished at basic intervals of

100 hours time in service.  Inspection shall be in accordance

with applicable procedures listed in ABC Airlines Maintenance

Manual.  During initial operation, the basic intervals for

station checks will be evaluated in the following manner:

Ten inspections at 80 hours. *

Periodic Inspection (PI) shall be accomplished at intervals not

to exceed 200 hours time in service.  Inspection shall be in

accordance with the applicable procedures listed in ABC Airlines

Maintenance Manual.  During initial operation, the basic

intervals for periodic inspections will be evaluated in the

following manner:

Five inspections at 160 hours. *

* Note - Upon termination of the evaluation period, the

assigned FAA maintenance and avionics inspectors will review

the maintenance inspection findings and the operating

history.  If satisfactory, the carrier will be authorized to

continue at the time established for the subsequent state,

i.e.,

Station Check - 100 hours

Periodic Inspection - 200 hours

Overhaul times as listed in hours and years are maximum limits of

whichever occurs first.

In addition to the preflight, periodic, and station checks there

are "other" inspections required.  These inspections are

explained in the notes below or are self-explanatory.

Time retirement items must be replaced where "replace" is

indicated.  (Refer to FAA Approved Lear Report 24/25-S47.)

Effective date ____________________

Page 2 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

LEAR MODEL 24/24B/25

NOTE 1:   Insp. @ ea. 1,000 hrs. or once ea. 1 yr. (use Lear

1,000 hr. insp. form) **

NOTE 2:   Insp. @ ea. 5,000 hrs. or once ea. 5 yrs. (use Lear

5,000 hr. insp. form) **

NOTE 3:   Insp. @ Engine O/H or CHG.

NOTE 4:   Insp. @ ea. 2,500 hrs. (use Lear 2,500 hr. insp. form)

**

NOTE 5:   Insp. @ ea. 500 hrs. or ea. 6 mos. (use Lear 500 hr.

insp. form) **

NOTE 6:   Overhaul and hot section inspections in accordance with

General Electric Service Bulletin (CJ 610) 72-43 (GEB

No. 4) Rev. 7, dated 11/29/68, or subsequent revisions

which are FAA approved.  The "Periodic Inspection"

intervals mentioned in the above Service Bulletin will

be adjusted to coincide with periodic inspection as set

forth on Page 1 of this Specification. **

NOTE 7:   Yearly intervals, engine change, and engine overhaul.

NOTE 8:   Special inspections to be conducted in accordance with

schedule and procedures set forth in Lear and General

Electric Maintenance Manuals. **

(** Specifically identify by revision number and/or date.)

AVIONICS SYSTEMS.  The term "System" means all those

interdependent subassemblies, component parts, etc., necessary

for the proper functioning of the system as a whole.  The term

"Bench Check" includes calibration, if necessary, to return the

unit to service.

Aircraft shall not be utilized in air carrier or commercial

operations unless:

a.   The aircraft and its component parts, accessories, and

appliances are maintained in an airworthy condition in

accordance with the schedule of maintenance and inspection

functions and procedures set forth in the operator's

maintenance manual.

b.   OC "On Condition" items will be maintained in continuous

airworthiness condition by periodic and progressive

inspections, checks, services, repair, and/or preventive

maintenance and shall be appropriately described in the

operator's maintenance manual.

c.   Parts or subcomponents, not listed below, will be checked,

inspected, and/or overhauled at the same time limits

specified for the component or accessory to which such parts

or subcomponents are related.

Abbreviations used in the Lear Model 24/24B/25 maintenance

specifications are defined as follows:

BC - Indicates "Bench Check"

EO - Indicates "Engine Overhaul"

EC - Indicates "Engine Change"

OC - Indicates "On Condition"

HYD - Indicates "Hydrostatic Test"

C - Indicates "Calibration"

SI - Indicates "Special Inspections"

Effective date ____________________

Page 3 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LEAR MODEL 24/24B/25

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS OR YRS.    PF    SC    PI     OTHER

Air Conditioning,

Chapter 21           OC                   X     X

Pre-cooler          6,000     8                   X   Note 1

Motor Compressor

Assy.             6,000     8                   X   Note 1

Condenser           6,000     8                   X   Note 1

Compressor          3,000     3                   X   Note 1

Cabin Rate of Climb

Ind.                 OC                         X   BC/2 yrs.

Cabin Altitude

Controller        5,000     4                   X   Note 1

Cabin Altitude &

Diff. Pressure       OC                         X   BC/2 yrs.

Thermostat             OC                         X   BC/2 yrs.

Outflow Valve       2,000     2                   X   Note 1

Safety Valve        2,000     2                   X   Note 1

Aneroid Sw.            OC                         X   BC/4 yrs.

Flow Control Valve  4,000     4                   X   Note 1

Autopilot,

Chapter 22           OC                   X     X

Computer Amplifier     OC             X     X     X   BC Note 1

Flight Controller      OC             X     X     X   BC Note 1

Altitude Controller    OC             X     X     X   BC Note 1

Servo Pitch            OC             X     X     X   BC Note 1

Servo Yaw, Roll        OC             X     X     X   BC Note 1

Followup Pitch, Yaw

& Roll               OC             X     X     X

Rate Gyro              OC             X     X     X   BC Note 1

Effort Indicator       OC                         X

Lateral Accelerometer  OC                         X

Drum & Brkt. Assy.

(Pitch)              OC                   X     X   Note 5

Drum & Brkt. Assy.

(Yaw)                OC                   X     X   Note 5

Drum & Brkt. Assy.

(Roll)               OC                   X     X   Note 5

Communications

System, Chapter 23   OC             X     X     X

To be determined

by assigned

inspector.

Electrical System,

Chapter 24           OC                   X     X

Starter - Generators   OC                   X     X   BC/800 hrs.

Battery N/C            OC                   X     X

Voltage Regulator   2,000                         X   BC Note 5

Inverter               OC             X     X     X   BC Note 1

Standby Inverter       OC             X     X     X   BC Note 1

Emergency Battery

with Inverter     2,000             X     X     X   BC Note 5

Electrical Warning

Panel                OC             X     X     X   BC Note 1

AC Voltmeter           OC             X     X     X   BC Note 1

DC Voltmeter           OC             X     X     X   BC Note 1

Ammeters               OC             X     X     X   BC Note 1

Starter - Gen

Control Panel        OC                   X     X   BC Note 1

Effective date ____________________

Page 4 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LEAR MODEL 24/24B/25

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS OR YRS.    PF    SC    PI     OTHER

Equipment &            OC                   X     X

Furnishings,

Chapter 25

Flotation Vests        OC             X     X     X   Note 1

Life Rafts             OC             X     X     X   Note 1

Fire Protection,       OC             X     X     X

Chapter 26

Containers             OC             X           X   HYD 5 Yrs.

& Note 5

Two-way Check Valve           1                   X   Note 5

Detector Sense         OC                         X   Note 1

Elements

Relay                  OC                         X

Cartridges        Replace 3 yrs                   X

Pressure & Thermal     OC             X     X     X

Discharge

Portable Fire          OC             X     X     X   BC/12 mos.

Extinguishers

Flight Controls,       OC             X     X     X

Chapter 27

Aileron Trim Motor     OC                   X     X   Note 1

Rudder Trim Motor      OC                   X     X   Note 1

Horizontal Stabilizer 500                   X     X

Trim Motor

Aileron Actuator -  Replace 20,000                X   Note 1

Consisting of

Yoke Assembly

(P/N 2324511-1),

Drive Clevis

(P/N 2324512-3 or

-5), Bearing

Support Assembly

(P/N 2324510-8),

Drive Pulley

Assembly (P/N

2324513-7-8-11 or

-12), and Woodruff

Key (P/N AN

280R40G)

Speed Brake Actuator   OC                         X   Note 1

Speed Brake Valve      OC                         X   Note 1

Restrictor

Spoiler Control        OC                         X   Note 1

Valve

Flap Control Valve     OC                         X   Note 1

Flap Actuator          OC                   X     X   Note 1

Aileron Trim           OC                   X     X   Note 1

Indicator

Rudder Trim            OC                   X     X   Note 1

Indicator

Stabilizer Trim        OC                   X     X   Note 1

Indicator

Control Cables         OC                         X   Note 1

Control Column         OC                         X   Note 4

Effective date ____________________

Page 5 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LEAR MODEL 24/24B/25

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS OR YRS.    PF    SC    PI     OTHER

Fuel System,

Chapter 28           OC             X     X     X

Fuel Quantity

Indicator            OC                         X

Fuel Quantity

Selector Switch      OC                         X

Fuel Quantity

Probe Indicator      OC                         X

Fuel Quantity

Probe OB Wing        OC                         X

Fuel Quantity

Probe Tip Tank       OC                         X

Fuel Quantity

Probe Fuselage       OC                         X

Fuel Pump, Standby  8,000                         X

Fuel Pump, Jet         OC                         X

Motive Flow Valves 10,000     10                  X   Note 2

Firewall Shutoff

Valves           10,000     10                  X   Note 2

Crossfeed Valve    10,000     10                  X   Note 2

Fuel Cell              OC                         X   SI/6 mos.

Fuselage Defuel

Valve            10,000     10                  X   Note 2

Low Press. Fuel

Filter               OC                         X   Note 1

Fuel Vent Check

Valves               OC                         X   Note 1

Fuel Transfer Pump  8,000                         X

Fuselage Fuel Pump  8,000                         X

Hydraulic System,

Chapter 29           OC             X     X     X

Hydraulic Pressure

Indicator            OC                         X

Accumulator         5,000      5                  X

Hydraulic Shutoff   5,000      5                  X

Relief Valve        5,000      5                  X

Pressure Regulator  5,000      5                  X

Hydraulic Pump

(Electric)           OC                         X   Note 1

Engine Pump (Hyd)      EO                         X

Ice & Rain,

Chapter 30           OC             X     X     X

Boots - Electric       OC             X     X     X   Note 1

Pump - Alcohol         OC                         X   Note 1

Tank                   OC                   X     X   Note 1

Pressure Switch        OC               @        X   Note 1

Defog Valve            OC                   X     X   Note 1

Defog Ducts &

Nozzles              OC                   X     X   Note 1

Defog Automatic

Control              OC                   X     X   Note 1

Timer - Electric

Boot                 OC                         X   Note 1

Valve - Wing

Anti-ice             OC                   X     X   Note 1

Sensors - Duct Temp.   OC                         X   Note 1

Instruments,

Chapter 31           OC             X     X     X

To be determined by

the assigned

inspector.

Effective date ____________________

Page 6 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LEAR MODEL 24/24B/25

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS OR YRS.    PF    SC    PI     OTHER

Landing Gear,

Chapter 32           OC             X     X     X

Power Brake Valve      OC                   X     X   Note 2

Parking Brake Valve    OC                   X     X   Note 2

Hydraulic Shuttle

Valve                OC                   X     X   Note 2

Priority Valve

(nose)               OC                   X     X   Note 2

Emergency Air

Pressure Ind.        OC                   X     X   Note 2

Door Uplock Actuator   OC                   X     X   Note 2

Main Gear Door

Actuator             OC                   X     X   Note 2

Gear Extension Valve   OC                   X     X   Note 2

Emergency Brake

Valve                OC                   X     X   Note 2

Gear Door Sequence

Valve                OC                   X     X   Note 2

Shuttle Valve (Gear

Door)                OC                   X     X   Note 2

Shuttle Valve (Gear

Actuator)            OC                   X     X   Note 2

Gear Selector Valve    OC                   X     X   Note 2

Landing Gear

Actuator      Replace 5,000 hrs.          X     X

(Main Gear)

Brake Assembly         OC             X     X     X

Wheel Assembly         OC             X     X     X

Solenoid Valve

(Antiskid)           OC                   X     X   Note 2

Shuttle Valve

(Antiskid)           OC                   X     X   Note 2

Hydraulic Fuse

(Antiskid)           OC                   X     X   Note 2

Actuator (nose

gear)         Replace 20,000 hrs.         X     X

Shuttle Valve          OC                   X     X   Note 2

Strut Nose      Replace 20,000 hrs.         X     X

Oleo Strut Main Replace 5,000 hrs.    X     X     X

Emergency Air

Bottle        12 yrs. scrap         X     X     X   HYD 3 yrs.

Tires                  OC             X     X     X

Nose Wheel Steering

Actuator          3,000                   X     X

Nose Wheel Steering

Amplifier            OC                         X   BC/1 yr.

Antiskid Generator     OC                   X     X

Antiskid Amplifier     OC                         X   BC/1 yr.

Lights, Chapter 33     OC             X     X     X

All lights             OC             X     X     X

Navigation System,

Chapter 34           OC                   X     X

To be determined by

assigned inspector.

Effective date ____________________

Page 7 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LEAR MODEL 24/24B/25

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS OR YRS.    PF    SC    PI     OTHER

Oxygen System,

Chapter 35           OC             X     X     X

Oxygen Bottle &

Regulator            OC                         X   5 yrs. HYD

Oxygen Pressure

Switch               OC                         X   Note 1

Aneroid Pressure

Switch               OC                         X   Note 1

Oxygen Masks (Crew

& Cabin)             OC                         X

Oxygen Pressure Gage   OC                         X

Doors, Chapter 52      OC             X     X     X

Actuator               OC             X     X     X   Note 1

Cabin Door Assembly    OC             X     X     X

Emergency Exits        OC             X           X   Operate at

PI

Fuselage, Chapter 53   OC             X     X     X

Forward Fuselage       OC             X     X     X

Cockpit Area           OC             X     X     X

Tail Cone              OC             X     X     X

Fuselage Special

Inspection                                          Note 8

Cabin Area             OC             X     X     X

Engine Pylon &

Nacelle,

Chapter 54           OC             X     X     X

Engine Mounts and

(Rubbers)         1,000                         X   Note 3

Engine Yoke

Assy.        Replace 20,000                     X   Note 1

Pylon Beams            EC                             Note 8 EC

Engine Mount

Fittings             EC                             Note 8 EC

Beam to Fuselage

Fittings             EC                             Note 8 EC

Effective date ____________________

Page 8 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LEAR MODEL 24/24B/25

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS OR YRS.    PF    SC    PI     OTHER

Stabilizers,           OC             X     X     X

Chapter 55

Severe Turbulence                                   Note 8

and/or Maneuvers

Horizontal         Replace 16,000                 X SI/1,000 hrs.

Stabilizer Assy.

Includes hinge

fittings and

actuator bracket

Horizontal         Replace 16,000                 X SI/5,000 hrs.

Stabilizer Hinge

pin

Vertical           Replace 16,000                 X SI/5,000 hrs.

Stabilizer Hinge

Assembly

(2331025-1)

NAS 464P6 -        Replace 5,000                  X SI/1,000 hrs.

Stabilizer

Actuator Attach

Bolts

Elevator           Replace 16,000     X     X     X SI/1,000 hrs.

Installation

Includes hinge

and hinge

supports, torque

tube, bell

cranks, and dual

push-pull tubes.

Rudder Surface,    Replace 15,500     X     X     X Note 1

Hinges and Hinge

Support

Vertical Stabilizer    OC             X     X     X Note 1

Windows, Chapter 56    OC             X     X     X

All, including

windshield           OC             X     X     X

Wings, Chapter 57      OC             X     X     X Notes 1 & 2

Hard and/or Overweight                              Note 8

Landing Inspection

Severe Turbulence or                                Note 8

Maneuvers

Inspection

Wing Flap          Replace 19,300                 X SI/1,000 hrs.

Assembly, Includes

surface, track &

roller mechanism,

actuator hinge, &

associated support

structure

Aileron Surface,   Replace 20,000           X     X

Hinge & Fittings

Support P/N

2324011-181-2,-1

Aileron Surface,   Replace 5,000      X     X     X SI/1,000 hrs.

Hinge & Hinge

Support, all

others than

above

Aileron Drive      Replace 1,000                  X SI/500 hrs.

Yoke Bolt (P/N

NAS 1304-34H)

Note:  See Lear

SB 23/24/25-193A

Special Inspection                                  Note 8

Effective date ____________________

Page 9 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

LEAR MODEL 24/24B/25

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS OR YRS.    PF    SC    PI     OTHER

Engine Turbine,        OC             X     X     X

Chapter 72

General Electric    Note 8            X     X     X   Hot Section

CJ-610 Series                                       Note 6

Overspeed and/or                                      Note 8

Overtemp.

Engine Fuel and        EO                   X     X

Control,

Chapter 73

Fuel Flow Meters       OC                         X

Fuel Pump           8,000                         X

Ignition, Chapter 74   EO

Ignitor Plug           OC                   X     X

Engine Controls,       EO             X     X     X

Chapter 76

Engine Indicating,     OC             X     X     X

Chapter 77

Tachometer Generator   OC             X     X     X   Note 7

Tachometer Indicator   OC             X     X     X   C Note 7

EPR Indicator          OC             X     X     X   C Note 7

Exhaust Temp. Ind.     OC             X     X     X   C Note 7

Fuel Flow and          OC             X     X     X   C Note 7

Indicator

Oil Pressure Indicator OC             X     X     X   C Note 7

Engine Oil Pressure    OC             X     X     X   C Note 7

Trans.

Low Oil Pressure       OC             X     X     X   C Note 7

Warning Switch

Oil Temp. Bulb         OC             X     X     X   Note 7

Exhaust, Chapter 78    OC             X     X     X

Tail Cone              EO             X     X     X

Oil, Chapter 79        EO             X     X     X

Oil Tank               EO             X     X     X

Oil Pump               EO                   X     X

Effective date ____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 35.  OPERATIONS SPECIFICATIONS, AIRCRAFT MAINTENANCE

FAN JET FALCON

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          Page 1 of 8

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

FAN JET FALCON - 20

Aircraft shall not be utilized in air carrier or commercial

operations unless:

a.   The aircraft and its component parts, accessories, and

appliances are maintained in an airworthy condition in

accordance with the schedule of maintenance and inspection

functions and procedures set forth in the operator's

maintenance manual.

b.   OC "On Condition" items will be maintained in continuous

airworthiness condition by periodic and progressive

inspections, checks, services, repair, and/or preventive

maintenance and shall be appropriately described in the

operator's maintenance manual.

c.   Parts or subcomponents not listed below will be checked,

inspected, and/or overhauled at the same time limits

specified for the component or accessory to which such parts

or subcomponents are related.

Abbreviations used in the FAN JET FALCON maintenance

specifications are defined as follows:

FC - Indicates "Functional Check"

BC - Indicates "Bench Check"

EO - Indicates "Engine Overhaul"

EC - Indicates "Engine Change"

OC - Indicates "On Condition"

HYD - Indicates "Hydrostatic Test"

CAL - Indicates "Calibration"

OP - Indicates "Operational Check"

Inspection, replacement, and/or overhaul of fatigue critical

parts having service life limits will be accomplished as listed,

and in accordance with the S.G.A.C. - Approved Flight Manuals for

Fan Jet Falcon and Fan Jet Falcon Series C, D, E, and F.

Preflight Inspection

To be accomplished each service calendar day.

PVO Inspection/Check

To be accomplished at intervals not to exceed 100 hours time

in service or three months, whichever occurs first.

V.A. Inspection

To be accomplished at intervals not to exceed 800 hours time

in service or twelve months, whichever occurs first.

IGV Inspection

To be accomplished at intervals not to exceed 2,400 hours

time in service or four years, whichever occurs first.

Effective date ____________________

Page 2 of 8

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

FAN JET FALCON - 20

2GV Inspection

To be accomplished at intervals not to exceed 4,800 hours

time in service or seven years, whichever occurs first.

Special Inspections

The frequency and procedure for performing special

inspections will be accomplished as specified in the

operator's maintenance manual.

Overhaul and inspection/check period time limitations specified

in hours and calendar time are maximum limits of whichever occurs

first.

** "Inspections, hydrostatic test, and life limits will be

accomplished as set forth in Part 173, Chapter I, Subtitle "B" of

CFR 49 currently in effect."

Effective date ____________________

Page 3 of 8

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAN JET FALCON

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS/YRS.       PVO    VA   GV   2GV   OTHER

Air Conditioning,      OC             X     X    X     X

Chapter 21

Turbo Compressor    2,400             X     X    X

Regulating Valve    2,400                   X    X

Flow Limiter           OC                   X    X         BC 2GV

Temperature Control    OC                   X    X         FC VA

Valve

Electrical/Radio       OC                   X    X         BC VA

Rack Blowers

Autopilot,             OC             X     X    X     X

Chapter 22

Pedestal Controller    OC             X     X    X         BC VA

Computer Amplifier     OC                   X    X         BC VA

Servos              2,400             X     X    X

Communications,        OC             X     X    X     X

Chapter 23

To be determined by

assigned inspector.

Electrical,            OC             X     X    X     X

Chapter 24

Inverter            2,400                   X    X         Brush

check

VA

Inverter, Static    2,400             X

(Voice Recorder

Emergency)

Starter Generator   E.O               X     X    X         300

hours

brush

check

and

shaft

greas-

ing

Battery Blower      4,800             X     X    X         FC VA

Equipment &            OC             X     X    X     X

Furnishings,

Chapter 25

Fire Protection,       OC             X     X    X     X

Chapter 26

Fire Extinguisher    **OC             X     X    X         6 MO,

Bottle (Hyd. or                                          WT. CK

retire appropriate

for bottle used)

Effective date ____________________

Page 4 of 8

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAN JET FALCON

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS/YRS.       PVO    VA   GV   2GV   OTHER

Fire Protection,

Chapter 26 (Cont'd)

H2O Fire Extinguisher    OC           X                    6 MO.

WT.CK.

CO2 Fire Extinguisher  **OC           X                    6 MO.

(Hyd. or retire                                          WT.CK.

appropriate for

bottle used)

Detector Control         OC           X                    FC VA

Flight Controls,         OC           X     X    X     X

Chapter 27

Double Hydraulic       7 yrs.         X     X    X         FC VA

Servo Control

Jack Aileron

Double Hydraulic       7 yrs.         X     X    X         FC VA

Servo Control

Jack Elevator

Double Hydraulic       7 yrs.         X     X    X         FC VA

Servo Control

Jack Rudder

Variable Bellcrank,    7 yrs.               X    X         FC 2VA

Aileron

Variable Bellcrank,    7 yrs.               X    X         FC 2VA

Elevator

Trim Jack, Aileron    10 yrs.               X    X         FC VA

Trim Jack, Rudder     10 yrs.               X    X         FC VA

Yaw Damp Jack System  1,800                 X    X         FC 2VA

Aux. Artificial Feel, 10 yrs.               X    X         FC 1GV

Aileron

Aux. Artificial Feel, 10 yrs.               X    X         FC 1GV

Elevator

Aux. Artificial Feel, 10 yrs.               X    X         FC 1GV

Rudder

Tailplane Electric    3,600           X     X    X         FC VA

Actuator

Droop Leading Edge    3,600                 X    X         FC VA

Jack

Trim & Air Brake      10 yrs.               X    X         FC VA

Control Box

Flap Reduction Gear    7 yrs.               X    X         FC VA

Assy.

Wing Flap Jack         7 yrs.               X    X         FC VA

Droop Leading Edge &  3,600                 X    X         FC VA

Flap Control Box

Fuel System,             OC           X     X    X     X

Chapter 28

Rear Compartment         OC                 X    X

Tank

Fuel Heater           3,000                 X    X         FC VA

Wing Tank Press.      3,600                 X    X         CAL VA

Reducing Valve

Rear Compartment Tank 3,600                 X    X         CAL VA

Press. Reducing

Valve

Dual Fuel Quantity    1,500                 X    X         CAL VA

Indicators

Fuel Transfer Pump    2,400           X     X    X        Replace

brushes

1,800

hrs.

Effective date ____________________

Page 5 of 8

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAN JET FALCON

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS/YRS.       PVO    VA   GV   2GV   OTHER

Fuel System,

Chapter 28 (Cont'd)

Fuel Shut Off Valve    OC             X     X    X        FC EC

L.P. Crossfeed Valve   OC             X     X    X        FC VA

L.P. Fuel Pump      2,400             X     X    X        Replace

brushes

1,800

hrs.

Hydraulic System,      OC             X     X    X     X

Chapter 29

Hydraulic Pump         EO             X

Engine Driven

Transfer Jack       5,400             X     X    X

Electro Pump        7 yrs.            X     X    X

Selector Valve

Electro Pump        3,600             X     X    X        FC Once

a week.

Ice & Rain,            OC             X     X    X     X

Chapter 30

Instruments,           OC             X     X    X     X

Chapter 31

To be determined by

assigned inspector.

Landing Gear,          OC             X     X    X     X

Chapter 32

Main Landing Gear   2,700

5,400             X     X    X        Per AMD

SB 431

Nose Landing Gear   2,700

5,400             X     X    X        Per AMD

SB 431

Landing Gear Door      OC             X     X    X

Locks

(2 GV Inspection

for door locks

P/N VTS 431)

(1 GV Inspection

for door locks

P/N VTS 442 or

4422)

Parking Brake          OC                   X    X

Telforce Cable

Anti-Skid Detectors 4,800             X     X    X       OP at

wheel

or

brake

change

Nose Gear Wheel       700 Ldgs                           Scrap

(P/N 9533961)                                          after

700

landings

Effective date ____________________

Page 6 of 8

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAN JET FALCON

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS/YRS.       PVO    VA   GV   2GV   OTHER

Lights, Chapter 33     OC             X     X    X     X

All Lights             OC             X     X    X     X

Navigation,            OC             X     X    X     X

Chapter 34

To be determined by

assigned inspector.

Oxygen, Chapter 35     OC             X     X    X     X

Oxygen Bottle        ** 3 yrs.        X     X    X

(Hyd. or retire

appropriate for

bottle used)

Pressure Reducing     3 yrs.          X     X    X

Valve

High Pressure Gauge    OC             X     X    X

Crew Oxygen Mask      3 yrs.          X     X    X

Altitude Sensitive    5 yrs.          X     X    X

Switch

Filler Connection      OC             X     X    X

Solenoid Valve         OC             X     X    X

Shut Off Valve         OC             X     X    X

Pneumatic, Chapter 36  OC             X     X    X     X

Valve, Nacelle         OC                   X    X

Deicing

Valve, Bleed Air       OC                   X    X

Valve, Conditioning    OC                   X    X

Valve, Wing Deicing    OC                   X    X

Drag Chute,            OC             X     X    X     X

Chapter 39

* F.C. to be carried                                     * 6 mos.

out every time drag

chute has been used

or at least every 6

mos. in case of non-

operation.

APU, Chapter 49        OC             X     X    X     X

APU                    *              X     X    X         * See

APU

Manufacturers

recommendation.

Effective date ____________________

Page 7 of 8

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAN JET FALCON

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS/YRS.       PVO    VA   GV   2GV   OTHER

Doors, Chapter 52      OC             X     X    X     X

Main L/G Door          OC             X     X    X

Teleforce Control

L/G Door Emergency     OC             X     X    X

Teleforce Control

Passenger/Crew Door 7 yrs.            X     X    X

Pneumatic Jack

Emergency Exits        OC             X     X    X        O.P. VA

Fuselage, Chapter 53   OC             X     X    X     X

NOTE 1:  Inspect

areas in accordance

with Fan Jet Falcon

Maintenance Manual.

Nacelles, Pylons,      OC             X     X    X     X

Chapter 54

Inspect areas in

accordance with

Fan Jet Falcon

Maintenance Manual.

Stabilizers,           OC             X     X    X     X

Chapter 55

Inspect areas in

accordance with

Fan Jet Falcon

Maintenance Manual.

Windows, Chapter 56    OC             X     X    X     X

Inspect areas in

accordance with

Fan Jet Falcon

Maintenance Manual.

Wings, Chapter 57      OC             X     X    X     X

Inspect areas in

accordance with

Fan Jet Falcon

Maintenance Manual.

Powerplant,            OC             X     X    X     X

Chapter 71

Engine Mount           EC             X     X    X

Effective date ____________________

Page 8 of 8

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAN JET FALCON

OVERHAUL         INSPECTION AND CHECK PERIOD

HOURS/YRS.       PVO    VA   GV   2GV   OTHER

Engine, Chapter 72       OC           X     X    X     X

Turbojet Engine          *            X     X    X

CF 700

Hot Section              *            X     X    X

Inspection

* See engine (G.E.

manufacturer's

recommendations)

Engine Fuel &            EO           X     X    X     X

Control, Chapter 73

Ignition, Chapter 74     EO           X     X    X     X

Igniter Plug            300           X     X    X

Engine

Hours

Engine Air,              EO           X     X    X     X

Chapter 75

Engine Controls,         OC           X     X    X     X

Chapter 76

Throttle Teleforce    3,600

Control in Nacelle

Engine Indicating,       OC           X     X    X     X

Chapter 77

T5 Harness               EO           X     X    X

EPR (PT7) Probe          EO           X     X    X

EPR Transmitter       3,600           X     X    X

Exhaust, Chapter 78      OC           X     X    X     X

Oil, Chapter 79          OC           X     X    X     X

Oil Pressure             EO           X     X    X

Transmitter

Starting, Chapter 80     OC           X     X    X     X

NOTE 1:  Effectivity - Aircraft Serial No. 1 through 53.

Prior to accumulation 4,800 hours time in service or 7 years,

whichever occurs first, accomplish Marcel Dassault Service

Bulletin No. 159 titled, Fuselage - Reinforcement of Stringer

Junction on Frame 33.

Effective date ____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 36.  OPERATIONS SPECIFICATIONS, AIRCRAFT MAINTENANCE

- HAWKER-SIDDELEY DH-125 SERIES

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04-R075.

WASHINGTON

PART D                                          Page 1 of 7

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

HAWKER SIDDELEY DH-125 SERIES

Thorough inspection shall be accomplished in accordance with the

applicable procedures as listed in ABC Airlines Maintenance

Manual.

Preflight (PF) shall be accomplished each service calendar day.

Inspection shall be in accordance with the applicable procedures

listed in ABC Airlines Maintenance Manual.

Period Inspections (PI) the procedure for the performance of

period inspections will be accomplished as specified in ABC's

Maintenance Manual.  Period inspections must be accomplished at

intervals not to exceed 160 hours time in service.

Aircraft shall not be utilized in air carrier or commercial

operations unless:

a.   The aircraft and its component parts, accessories, and

appliances are maintained in an airworthy condition in

accordance with the schedule of maintenance and inspection

functions and procedures set forth in the operator's

maintenance manual.

b.   OC "On Condition" items will be maintained in continuous

airworthiness condition by periodic and progressive

inspections, checks, services, repair, and/or preventive

maintenance and shall be appropriately described in the

operator's maintenance manual.

c.   Parts or sub-components not listed below will be checked,

inspected and/or overhauled at the same time limits

specified for the component or accessory to which such parts

or sub-components are related.

Abbreviations used in the Hawker-Siddeley DH-125 maintenance

specifications are defined as follows:

PF - Indicates "Preflight Inspection"

BC - Indicates "Bench Check"

EO - Indicates "Engine Overhaul"

EC - Indicates "Engine Change"

OC - Indicates "On Condition"

HYD - Indicates "Hydrostatic Test"

C - Indicates "Calibration"

Life Limited Components.

Numerous parts, affecting different models of the DH-125

Aircraft, are life limited and listed under Note 3 of FAA Type

Certificate Data Sheet ABEU.  The limitations must be adhered to

as applicable to the various aircraft.

Effective date ____________________

Page 2 of 7

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HAWKER-SIDDELEY DH-125 SERIES

OVERHAUL         INSPECTION AND CHECK PERIOD

LNDGS., HOURS OR YRS       PF  PI   OTHER

Air Conditioning,    OC                 X   X

Chapter 21

Air Jet Pump         3,000                  X

Air Needle Valve     OC                     X

APU Supply Check     3,000                  X

Valve

APU Shut-off         3,000                  X

Valve

Auxiliary Heating    3,000                  X

Valve

Cabin Temperature    OC                     X

Controller

Cabin Pressure       OC                     X

Control

Fan Operated         3,000                  X

Venturi

Flow Control         3,000                  X

Valve

Initiation Air       3,000                  X

Valve

Main Supply Check    3,000                  X

Valve

Outflow and Safety   3,000                  X

Valve

Pneumatic Relay      3,000                  X

Pressure Regulators  3,000                  X

Ram Air Check Valves 3,000                  X

Ram Air Valve        3,000                  X

Refrigeration        3,000                  X

By-Pass Valve

Refrigeration Unit   2,000                  X

Turbine By-Pass      3,000                  X

Valve

Auto Pilot,          OC                 X   X

Chapter 22

Aileron Servo        3,000              X   X

Air Speed            4,000                  X

Compensator

Compass Amplifier    4,000              X   X

Computer Amplifier   4,000              X   X   BC 1 Year

Controller, Pedestal 5,000              X   X   BC 1 Year

Elevator Servo       3,000              X   X

Emergency Disconnect 4,000              X   X

Instrument Amplifier 4,000              X   X

Rudder Servo         3,000              X   X

Servo Mount          5,000                  X

Steering Computer    4,000              X   X

Trim Tab Servo       3,000              X   X

Vertical, Yaw and    4,000              X   X

Rate Gyros

Communications,      OC                 X   X

Chapter 23

To be determined by

assigned inspector.

Effective date ____________________

Page 3 of 7

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HAWKER-SIDDELEY DH-125 SERIES

OVERHAUL         INSPECTION AND CHECK PERIOD

LNDGS., HOURS OR YRS       PF  PI   OTHER

Electrical System,   OC                 X   X

Chapter 24

Alternator            800               X   X

Alternator Volt.        2 Yrs.          X   X

Control Unit

Compass Inverter    1,000               X   X

Emergency Contactor 4,000                   X

Field Contactors    3,000                   X

Generator           2,000                   X

Contactors

Generator Switching 2,000                   X

Units

Ground Contactor    5,000                   X

Inverters #1 and    1,500 running Hrs.  X   X

#2

Inverter Control    4,000                   X

Relays

Overspeed Relays    3,000                   X

Overvoltage Relays  4,500                   X   BC - 2250 Hrs.

Overvoltage Unit    3,000                   X

Regulators          4,500                   X

Standby Inverter    1,500 running Hrs.  X   X

Start and Battery   4,000                   X

Contactor

Starter Buss        5,000                   X

Contactor

Starter Generators    800               X   X

Time Switch         4,000                   X

Voltage Sensing     4,500                   X

Unit

Voltmeter          10,000               X   X

Equipment &          OC                 X   X

Furnishings,

Chapter 25

To be determined by

assigned inspector.

Fire Protection      OC                 X   X

System, Chapter 26

Actuator Cartridge   OC                     X   Replace 2 Yrs.

APU Fire Detector    OC                 X   X

Container, Fire      OC                 X   X   HYD 5 Yrs.

Extinguisher

Dual Head Valves     OC                     X

Engine Fire          OC                 X   X

Detection

Rear Equipment Bay   OC                     X

Overheat

Flight Control       OC                 X   X

Systems, Chapter 27

Airbrake and Lift    OC                     X

Dump System

Flap System          OC                 X   X

Flap Control Unit   4,500                   X

Flap Jack Screws    3,000                   X

Stall Warning        OC                 X   X

System

Stick Shaker System     4 Yrs.          X   X

Trim Control         OC                     X

Systems

Effective date ____________________

Page 4 of 7

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HAWKER-SIDDELEY DH-125 SERIES

OVERHAUL         INSPECTION AND CHECK PERIOD

LNDGS., HOURS OR YRS       PF  PI   OTHER

Fuel System,       OC                   X   X

Chapter 28

Boost Pumps         1,000               X   X

Check Valves            6 Yrs.              X

Cross Feed System  OC                   X   X

Drain Valves       OC                   X   X

Float Valves            6 Yrs.          X   X

Low Pressure,           4 Yrs.              X

Transfer and

Crossfeed

Valves

Hydraulic System,  OC                   X   X

Chapter 29

Accumulators        3,000               X   X

Aux. Hydraulic     OC                       X

Low Level Light

Brake Modulator     3,000                   X

Units

Cylinders:

Airbrake  3,000                   X

Actuating

MLG,      4,500 Lndgs             X

Retraction

MLG, Door 3,000 Lndgs             X

Actuating

NLG,      6,000 Lndgs             X

Retraction

NLG,      3,600 Lndgs             X

Steering

Wing Flap 3,000                   X

Actuating

Engine Driven Pumps 3,000                   X

Flap Control Unit   4,500                   X

Flow Indicator Unit 5,000                   X

Hand Pump           5,000                   X

Valves:

Brake        3,000                   X

Emergency

Reducer

Brake        3,000                   X

Control

Brake        5,000                   X

Shuttle

Check        5,000                   X

Gear         5,000                   X

Extension

Restrictor

Nose Gear    5,000                   X

Steering

Pump Cut-Out 2,500                   X

Pressure     5,000                   X

Regulating

Ice and Rain       OC                   X   X

Protection,

Chapter 30

Airframe Deicing        2 Yrs.              X

Pump

Fuel Filter Deice       3 Yrs.              X

Pump

Ice Detector System 4,500                   X

Pitot Heat System  OC                   X   X

Windshield Heat    OC                   X   X

Control

Windshield Deicer       3 Yrs.              X

Hand Pump

Wing Deicer Check   3,000/4 Yrs.            X

Valve

Wing Deicer         3,000/4 Yrs.            X

Compensating

Valve

Effective date ____________________

Page 5 of 7

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HAWKER-SIDDELEY DH-125 SERIES

OVERHAUL         INSPECTION AND CHECK PERIOD

LNDGS., HOURS OR YRS       PF  PI   OTHER

Instruments,       OC                   X   X

Chapter 31

To be determined

by assigned

inspector.

Landing Gear,      OC                   X   X

Chapter 32

Anti-Skid System    3,000 Lndgs         X   X

Landing Gear        3,000 Lndgs             X

Control Unit

MLG Assembly        2,000 Lndgs         X   X

MLG Door Assembly  OC                   X   X

MLG Mechanical     OC                       X

Indicator

NLG Assembly        3,000 Lndgs         X   X

NLG Door Assembly  OC                   X   X

NLG Mechanical     OC                       X

Indicator

Parking Brake      OC                   X   X

Control

Wheels, Tires and  OC                   X   X

Brakes

Lights, Chapter 33 OC                   X   X

Anti-Collision     OC                   X   X

Central Warning    OC                   X   X

Unit

Exit Marking       OC                   X   X

Landing            OC                       X

Navigation         OC                       X

Passenger          OC                       X

Emergency

Wing Ice Lights    OC                       X

Navigation,        OC                   X   X

Chapter 34

To be determined

by assigned

inspector.

Oxygen, Chapter 35 OC                   X   X

Cylinders:

Main      *OC                   X   X   *(4 Yrs. Hyd

Check or cyl.

replacement

appropriate to

Cyl)

Portable  *OC                   X   X   *(4 Yrs. Hyd

Check or cyl.

replacement

appropriate to

Cyl)

Masks              OC                   X   X

Pressure Gage      OC                   X   X

Pressure Regulator OC                   X   X

Effective date ____________________

Page 6 of 7

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HAWKER-SIDDELEY DH-125 SERIES

OVERHAUL         INSPECTION AND CHECK PERIOD

LNDGS., HOURS OR YRS       PF  PI   OTHER

Oxygen, Chapter 35

(Cont'd)

Valves:

Flow Selector  OC                     X

Charging       OC                     X

Supply Master  OC                     X

Airborne Auxiliary

Power, Chapter 49  OC                 X   X

Aux. Power Unit       1,000 APU Hrs.    X   X

Fuel Filter           2,000 APU Hrs.    X   X

Generator            OC                     X

Ignitor Unit          1,000 APU Hrs.    X   X

Solenoid Fuel Valve   6,000 APU Hrs.    X   X

Valve Fuel Check          4 Yrs.            X

Doors, Chapter 52    OC                 X   X

Cargo                OC                 X   X

Emergency Exits      OC                     X

Passenger            OC                 X   X

Fuselage, Chapter 53 OC                 X   X

Nacelle/Pylons,

Chapter 54         OC                 X   X

Airframe Engine

Mount Brackets     10,000                 X

Stabilizers,

Chapter 55         OC                 X   X

Elevator and Rudder

Hinge Fittings     OC                     X

Horizontal Stabilizer

Attach Points      OC                     X

Vertical Stabilizer

Attach Points      OC                     X

Wings, Chapter 57    OC                 X   X

Internal Structure   OC                     X

Engine, Chapter 72   OC                 X   X

Engine, Bristol

Siddeley Viper      1,600             X   X

Engine, Mount        OC                     X   EC Detail Insp.

Engine, Cowling      OC                 X   X

Fire, Seal           OC                     X   EC Detail Insp.

Tail Cone            OC                     X   EC Detail Insp.

Effective date ____________________

Page 7 of 7

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HAWKER-SIDDELEY DH-125 SERIES

OVERHAUL         INSPECTION AND CHECK PERIOD

LNDGS., HOURS OR YRS       PF  PI   OTHER

Engine Fuel

System,

Chapter 73      OC                    X   X

Air/Fuel Ratio

Control         EO                        X

Barometric Flow

Control         EO                    X   X

Electric Pressure

Control         EO                    X   X

Flowmeter

Transmitter     EO                    X   X

Fuel Filter       EO                        X

Fuel Pump         EO                        X

Pressure Switches EO                        X

Primer Solenoid   EO                        X

Pressure

Increasing

Valve           EO                        X

Rate Reset Valve  EO                        X

Engine Ignition,

Chapter 74      OC                    X   X

Igniter Plug       375                      X

Exciter System    EO                        X

Glow Plugs        OC                        X

Engine Bleed Air,

Chapter 75      OC                    X   X

Anti-Ice Valve    EO                        X

Engine Controls,

Chapter 76      OC                    X   X

Power Control

Linkage         OC                    X   X   EC Detail Insp.

H.P. Fuel Cock

Linkage         OC                    X   X

Engine Indicating,

Chapter 77      OC                    X   X

Tach. Generator   EO                        X

EGT Probes        EO                    X   X

Power Loss

Indicator       EO                        X

Oil System,

Chapter 79      OC                    X   X

Pressure

Indicator       3,000                     X

Pressure

Transmitter     OC                        X   C at EO

Tank              OC                        X   EC Detail Insp.

Temperature

Indic.          3,000                     X

Temperature Bulb  OC                        X   C at EO

Effective date ____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 37.  OPERATIONS SPECIFICATIONS

- AIRCRAFT MAINTENANCE - HFB 320 HANSA JET

Form Approved

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No 04-R075

WASHINGTON

PART D                                        Page 1 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

HFB 320 HANSA JET

Thorough inspection shall be accomplished in accordance with the

applicable procedures as listed in ABC Airlines Maintenance

Manual.

Preflight shall be accomplished each service calendar day.

Inspection shall be in accordance with the applicable procedures

listed in ABC Airlines Maintenance Manual.

Special Inspections

The frequency and procedure for performing special

inspections will be accomplished as specified in the

operator's maintenance manual.

Overhaul and inspection/check period time limitations

specified in hours and calendar time are maximum limits of

whichever occurs first.

Period Inspections (PI)  Period inspections will be accomplished

as specified in ABC Airlines Maintenance Manual.

Aircraft shall not be utilized in air carrier or commercial

operations unless:

a.   The aircraft and its component parts, accessories, and

appliances are maintained in an airworthy condition in

accordance with the schedule of maintenance and inspection

functions and procedures set forth in the operator's

maintenance manual.

b.   OC "On Condition" items are maintained in continuous

airworthiness condition by periodic and progressive

inspections, checks, services, repairs, and/or preventive

maintenance and shall be appropriately described in the

operator's maintenance manual.

c.   Parts or subcomponents not listed below are checked,

inspected and/or overhauled at the same time limits

specified for the component or accessory to which such parts

or subcomponents are related.

d.   FC/BC items are done in accordance with manufacturer's

recommendations.

Effective date ____________________

Page 2 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE GENERAL

HFB 320 HANSA JET

The following PERIOD INSPECTIONS will be accomplished in

accordance with instructions contained in ABC Airlines

Maintenance Manual.

1.   POST FLIGHT INSPECTION

To be accomplished not to exceed 25 hours time in service as

indicated by "X" under PO column on the following pages.

2.   MID PERIOD INSPECTION

To be accomplished at intervals not to exceed 60 hours time

in service, as indicated by "X" under MP (PI) column on the

following pages.

3.   A PERIOD INSPECTION

To be accomplished at intervals not to exceed 150 hours time

in service, as indicated by "X" under A (PI) column on the

following pages.

4.   B PERIOD INSPECTION

To be accomplished at intervals not to exceed 300 hours time

in service, as indicated by "X" under B (PI) column on the

following pages.

5.   C PERIOD INSPECTION

To be accomplished at intervals not to exceed 600 hours time

in service, as indicated by "X" under C (PI) column on the

following pages.

6.   D PERIOD INSPECTION

To be accomplished at intervals not to exceed 1200 hours

time in service, as indicated by "X" under D (PI) column on

the following pages.

7.   E PERIOD INSPECTION

To be accomplished at intervals not to exceed 2400 hours

time in service, as indicated by "X" under E (PI) column on

the following pages.

Effective date ____________________

Page 3 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE GENERAL

HFB 320 HANSA JET

Abbreviations used in the HFB 320 Hansa Jet maintenance schedule

are defined as follows:

PO  - Indicates Post Flight Inspection

MP  - Indicates Mid Period Inspection

PI  - Indicates Period Inspections

HS  - Indicates Engine Hot Section Inspection

EC  - Indicates Engine Change Inspection

EO  - Indicates Engine Overhaul

OC  - Indicates On Condition

HYD - Indicates Hydrostatic Test

CALIB -Indicates Calibration

FC  - Functional Check

BC  - Bench Check

Life Limited Components:

1.  Main Landing Gear P/N 320-50125/50150    15,000 hours

2.  Nose Landing Gear P/N 320-50165          15,000 hours

3.  Flap Assembly P/N 320-11700/12700        17,500 hours

4.  Frame 28 (Aircraft Serial No. 1023)      10,000 hours

The times quoted above are predicated on one landing per hour.

Effective date ____________________

Page 4 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HFB 320 HANSA JET

OVERHAUL        PERIOD INSPECTIONS

HOURS OR YRS.   PO  MP  A  B   C   D  E

Air-Conditioning System,

Chapter 21                 OC             X   X   X  X   X   X  X

Check Valves, APU, Air

Conditioning               OC                     X  X   X   X  X

Air Flow Regulator         4,000              X   X  X   X   X  X

Cabin Pressure

Differential Indicator     2,400              X   X  X   X   X  X

Rate of Climb, Cabin

Indicator                  2,400              X   X  X   X   X  X

Altitude Selector          5,000              X   X  X   X   X  X

Valves, Control Bleed Air  3,000              X   X  X   X   X  X

Emergency Pressure Shutoff

Valve                      OC                 X   X  X   X   X  X

Temperature Control Valve  3,000              X   X  X   X   X  X

Shutoff Valve              OC                 X   X  X   X   X  X

Discharge Valve            3,000              X   X  X   X   X  X

Emergency Pressure

Controller                 4,000              X   X  X   X   X  X

Cabin Pressure Indicator   2,000              X   X  X   X   X  X

Air Drier                  OC                        X   X   X  X

Dump and Fresh Air Valve   OC                 X   X  X   X   X  X

Pressure Differential

Switch                     OC                 X   X  X   X   X  X

Temperature Sensors, Low

and High Limit             OC                            X   X  X

Water Extractor            OC                 X   X  X   X   X  X

Heat Exchanger             OC                 X   X  X   X   X  X

Auto Pilot System -

Chapter 22                 OC             X   X   X  X   X   X  X

Amplifier, Computer        OC (BC per * next page)   X   X   X  X

Trim Coupler               OC                        X   X   X  X

Effective date ____________________

Page 5 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HFB 320 HANSA JET

OVERHAUL        PERIOD INSPECTIONS

HOURS OR YRS.   PO  MP  A  B   C   D  E

Auto Pilot System -

Chapter 22 (Cont'd)

Airspeed Sensor and

Switch                     OC                        X   X   X  X

Vertical and Yaw Rate

Gyros                      3,000                     X   X   X  X

Altitude Control           OC                        X   X   X  X

Servo Drives               3,000              X   X  X   X   X  X

Controller, Pedestal       3,600              X   X  X   X   X  X

Computers, Steering        OC                     X  X   X   X  X

Emergency Disconnect

Switch                     OC                        X   X   X  X

*   Bench check in accordance with applicable Manufacturer's

Overhaul Manual or equivalent instructions every 2,000 hours

or 18 months, whichever occurs first.

Communications System,

Chapter 23                 OC             X   X   X  X   X   X  X

To be determined by

assigned inspector.

Electrical Power System

- Chapter 24               OC             X   X   X  X   X   X  X

Alternator                 1,200          X   X   X  X   X   X  X

Regulators                 OC             X   X   X  X   X   X  X

Current Transformers       OC                        X   X   X  X

Volt and Ampere Meters     OC             X   X   X  X   X   X  X

Inverters                 *1,000          X   X   X  X   X   X  X

* Inverter Operating Time

Starter Generator          1,200          X   X   X  X   X   X  X

Battery                    OC             X   X   X  X   X   X  X

Contactors, Main, Battery,

Generator                  OC                        X   X   X  X

Effective date ____________________

Page 6 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HFB 320 HANSA JET

OVERHAUL        PERIOD INSPECTIONS

HOURS OR YRS.   PO  MP  A  B   C   D  E

Electrical Power System

- Chapter 24 (Cont'd)

Relays, Feeder Protection  OC                 X   X  X   X   X  X

Relay, Bus Transfer        OC                        X   X   X  X

Relay, Reverse Current     OC                        X   X   X  X

Equipment & Furnishings,   OC             X   X   X  X   X   X  X

Chapter 25

To be determined by

assigned inspector.

Dragchute                  OC             X   X   X  X   X   X  X

(Detail inspection

60-day deployed)

Fire Protection System,    OC             X   X   X  X   X   X  X

Chapter 26

(F/C every 24 months)

Fire Extinguisher          OC             X   X   X  X   X   X  X

Assembly

P/N F2718E/MS33514 or

1526/M33514 "Inspections,

hydrostatic test, and

life limits will be

accomplished as set

forth in Part 173,

Chapter 1, Subtitle B

of CFR 49 currently in

effect."

Check and Distributing     2,000/5 yrs    X   X   X  X   X   X  X

Valves

Element, Sensing, APU      1,500/3 yrs    X   X   X  X   X   X  X

Engine                     EO             X   X   X  X   X   X  X

Extinguisher, Portable     OC             X   X   X  X   X   X  X

"Inspections, hydrostatic

test, and life limits will

be accomplished as set

forth in Part 173,

Chapter 1, Subtitle B of

CFR 49 currently in

effect."

Flight Control System,     OC             X   X   X  X   X   X  X

Chapter 27

Gear Boxes                 OC                        X   X   X  X

Effective date _____________________

Page 7 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HFB 320 HANSA JET

OVERHAUL        PERIOD INSPECTIONS

HOURS OR YRS.   PO  MP  A  B   C   D  E

Flight Control System,

Chapter 27 (Cont'd)

Position Indicators:       OC             X   X   X  X   X   X  X

Aileron

Rudder

Flap

Trim Actuators:

Aileron               1,200                  X  X   X   X  X

Rudder                OC                     X  X   X   X  X

Elevator              4 years                X  X   X   X  X

Trim Switches:             OC             X   X   X  X   X   X  X

Rudder & Aileron

Elevator

Shutoff Valves:            4 years                   X   X   X  X

Anti-Stall Computer        OC             X   X   X  X   X   X  X

(BC 3,000 hours)

Angle of Attack Sensor     OC             X   X   X  X   X   X  X

Stick Shaker               OC             X   X   X  X   X   X  X

Actuators:                 2,400/4 yrs        X   X  X   X   X  X

Flap

Slat

Speed Brake

Stick Pusher Cylinder      5 years        X   X   X  X   X   X  X

"Inspections, hydrostatic

test, and life limits

will be accomplished as

set forth in Part 173,

Chapter 1, Subtitle B

of CFR 49 currently in

effect."

Fuel System, Chapter 28    OC             X   X   X  X   X   X  X

Relief Valves              OC                     X  X   X   X  X

Pump, Fuel Boost           1,200/4 yrs    X   X   X  X   X   X  X

Normal

Emergency

Effective date __________________________

Page 8 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HFB 320 HANSA JET

OVERHAUL        PERIOD INSPECTIONS

HOURS OR YRS.   PO  MP  A  B   C   D  E

Fuel System, Chapter 28

(Cont'd)

Check Valves               OC                     X  X   X   X  X

Methanol Tank              1,500/5 yrs    X   X   X  X   X   X  X

Quantity Transmitters      OC                     X  X   X   X  X

Quantity Indicators        OC             X   X   X  X   X   X  X

Fuel Check Valve (APU)     OC                 X   X  X   X   X  X

Shutoff Valve (APU)        OC                     X  X   X   X  X

Hydraulic Power,           OC             X   X   X  X   X   X  X

Chapter 29

Check Valves               OC                     X  X   X   X  X

Pumps                      2,000          X   X   X  X   X   X  X

Accumulators, Systems (4)  2,400/4 yrs    X   X   X  X   X   X  X

Accumulators, Nose Wheel

Shimmy Damper              2,400/4 yrs    X   X   X  X   X   X  X

Air Pressure Regulator     OC                        X   X   X  X

Reservoir                  OC             X   X   X  X   X   X  X

Filters, Element           600                X   X  X   X   X  X

Pressure Control Valve     2,400                     X   X   X  X

Valves, Shutoff            2,400                  X  X   X   X  X

Valves, Relief             OC                     X  X   X   X  X

Hand Pump                  OC             X   X   X  X   X   X  X

Switches, Low Level,

Low Pressure               OC                        X   X   X  X

Temperature Indicator

& Transmitter              OC             X   X   X  X   X   X  X

Pressure Indicator         OC             X   X   X  X   X   X  X

Pressure Transmitter       2,500          X   X   X  X   X   X  X

Effective date ____________________

Page 9 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HFB 320 HANSA JET

OVERHAUL        PERIOD INSPECTION

HOURS OR YRS.   PO  MP  A  B   C   D  E

Ice and Rain Protection

System, Chapter 30         OC             X   X   X  X   X   X  X

Pressure Switch, Engine

De-ice                     OC                 X   X  X   X   X  X

Solenoid Valve, Engine

De-ice                     OC                 X   X  X   X   X  X

Window Temperature

Regulator                  OC                     X  X   X   X  X

Windshield Wiper Motor     OC                        X   X   X  X

Wiper Gear Box             OC                        X   X   X  X

De-ice and Anti-ice

Warning Indicator          OC                 X   X  X   X   X  X

De-icing and Anti-ice

Control Box                OC                     X  X   X   X  X

Static Ports               OC                 X   X  X   X   X  X

Pitot Head, Fuselage       OC                 X   X  X   X   X  X

Pitot Head, Tail           OC                 X   X  X   X   X  X

Instruments, Chapter 31    OC             X   X   X  X   X   X  X

To be determined by

assigned inspector.

Landing Gear, Chapter 32   OC             X   X   X  X   X   X  X

MLG Assembly               5,000          X   X   X  X   X   X  X

NLG Assembly               5,000          X   X   X  X   X   X  X

MLG Actuator Cylinder      2,400/4 yrs    X   X   X  X   X   X  X

NLG Actuator Cylinder      2,400/4 yrs    X   X   X  X   X   X  X

MLG Locking Cylinder       2,400/4 yrs    X   X   X  X   X   X  X

NLG Locking Cylinder       2,400/4 yrs    X   X   X  X   X   X  X

NLG Centering Cylinder     2,400/4 yrs    X   X   X  X   X   X  X

Effective date ____________________

Page 10 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

NFB 320 HANSA JET

OVERHAUL        PERIOD INSPECTION

HOURS OR YRS.   PO  MP  A  B   C   D  E

Landing Gear,

Chapter 32 (Cont'd)

Emergency Gear,

Mechanical Shutoff Valve   2,400/4 yrs    X   X   X  X   X   X  X

Door Actuator Cylinder     2,400/4 yrs    X   X   X  X   X   X  X

Door Sequence Valves       2,400/4 yrs    X   X   X  X   X   X  X

Door Relief Valves         OC             X   X   X  X   X   X  X

Brake Control Valves       3,000/4 yrs    X   X   X  X   X   X  X

Master Cylinder            3,000/4 yrs    X   X   X  X   X   X  X

Emergency Brake Control

Valve                      3,000/4 yrs    X   X   X  X   X   X  X

Anti-Skid System:                         X   X   X  X   X   X  X

Generator             OC

Control Box           OC

Control Valve         OC

Steering Cylinders         2,400/4 yrs    X   X   X  X   X   X  X

Brake, Wheels and Tires    OC             X   X   X  X   X   X  X

Gear Selector Control

Valves                     2,400/4 yrs    X   X   X  X   X   X  X

Lights, Chapter 33         OC             X   X   X  X   X   X  X

Anti-Collision             OC             X   X   X  X   X   X  X

Landing                    OC             X   X   X  X   X   X  X

Navigation                 OC             X   X   X  X   X   X  X

Exit Markings              OC             X   X   X  X   X   X  X

Passenger Safety Lights    OC             X   X   X  X   X   X  X

Master Caution Light       OC             X   X   X  X   X   X  X

Warning Horn               OC             X   X   X  X   X   X  X

Effective date ____________________

Page 11 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HFB 320 HANSA JET

OVERHAUL        PERIOD INSPECTIONS

HOURS OR YRS.   PO  MP  A  B   C   D  E

Navigation, Chapter 34     OC             X   X   X  X   X   X  X

Flasher                    2,400                  X  X   X   X  X

To be determined by

assigned inspector.

Oxygen, Chapter 35         OC             X   X   X  X   X   X  X

Masks                      OC             X   X   X  X   X   X  X

Pressure Reducer           3 years        X   X   X  X   X   X  X

Pressure Gauge             3 years        X   X   X  X   X   X  X

Orifice Block

(silica gel)               2 years            X   X  X   X   X  X

Portable Bottle            OC             X   X   X  X   X   X  X

"Inspections, hydrostatic

test, and life limits

will be accomplished as

set forth in Part 173,

Chapter 1, Subtitle B of

CFR 49 currently in

effect."

Cylinder                   OC                     X  X   X   X  X

"Inspections, hydrostatic

test, and life limits

will be accomplished as

set forth in Part 173,

Chapter 1, Subtitle B of

CFR 49 currently in

effect."

Airborne Auxiliary Power,

Chapter 49                 OC             X   X   X  X   X   X  X

APU                        *250/500       X   X   X  X   X   X  X

* (APU engine hours)        starts

Panel, Control Regulator   *250/500       X   X   X  X   X   X  X

* (APU engine hours)        starts

Starter/Generator          *250/500           X   X  X   X   X  X

* (APU engine hours)        starts

Doors, Chapter 52          OC             X   X   X  X   X   X  X

Entrance                   OC             X   X   X  X   X   X  X

Effective date ____________________

Page 12 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HFB 320 HANSA JET

OVERHAUL        PERIOD INSPECTIONS

HOURS OR YRS.   PO  MP  A  B   C   D  E

Doors, Chapter 52 (Cont'd)

Emergency Exits            OC             X   X   X  X   X   X  X

Fuselage, Chapter 53       OC             X   X   X  X   X   X  X

Inspect areas in

accordance with the HFB

320 Hansa Jet

Maintenance Manual.

Nacelle/Pylons,

Chapter 54                 OC             X   X   X  X   X   X  X

Fireseal Assembly          OC                     X  X   X   X  X

Engine Mount & Thrust     *OC                     X  X   X   X  X

Strut * (Detail Inspection

at EC)

Inspect areas in

accordance with the HFB

320 Hansa Jet

Maintenance Manual.

Stabilizers, Chapter 55    OC             X   X   X  X   X   X  X

Elevator and Rudder

Hinges                     OC             X   X   X  X   X   X  X

Vortex Generators          OC             X   X   X  X   X   X  X

Elevator and Rudder

Balance Stops              OC                     X  X   X   X  X

Inspect areas in

accordance with the HFB

320 Hansa Jet

Maintenance Manual.

Windows, Chapter 56        OC             X   X   X  X   X   X  X

Wings, Chapter 57          OC             X   X   X  X   X   X  X

Fuselage to Wing          *OC                            X   X  X

Connection Bolts

* (Retorque according to

Maintenance Manual,

Chapter 57-10-0)

Effective date ____________________

Page 13 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HFB 320 HANSA JET

OVERHAUL        PERIOD INSPECTIONS

HOURS OF YRS.   PO  MP  A  B   C   D  E

Wings, Chapter 57 (Cont'd)

Tiptanks                   OC             X   X   X  X   X   X  X

Fence                      OC             X   X   X  X   X   X  X

Vortex Generators          OC             X   X   X  X   X   X  X

Slats                      OC             X   X   X  X   X   X  X

Flaps                      OC             X   X   X  X   X   X  X

Ailerons                   OC             X   X   X  X   X   X  X

Speed Brakes               OC             X   X   X  X   X   X  X

Inspect areas in

accordance with the HFB

320 Hansa Jet

Maintenance Manual.

Engine, Chapter 72         OC             X   X   X  X   X   X  X

Engine CJ-610-1 or -5      1,500          X   X   X  X   X   X  X

*Note 1

Engine - Hot Section       Hot Section                   X   X

*Note 2

Engine Mount               *OC                    X  X   X   X  X

* Detail inspection EC

Engine Fuel and Control,

Chapter 73                 OC             X   X   X  X   X   X  X

Drain Valves               EO                     X  X   X   X  X

Inlet Guide Vane Actuator  EO                     X  X   X   X  X

Fuel Flow Transmitter      2,000          X   X   X  X   X   X  X

Fuel Flow Indicator        1,500          X   X   X  X   X   X  X

Fuel Pressure Transmitter  EO                 X   X  X   X   X  X

Effective date ____________________

Page 14 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HFB 320 HANSA JET

OVERHAUL        PERIOD INSPECTION

HOURS OR YRS.   PO  MP  A  B   C   D  E

Engine Fuel and Control,

Chapter 73 (Cont'd)

Fuel Pump                  EO                 X   X  X   X   X  X

Ignition, Chapter 74       OC             X   X   X  X   X   X  X

Plug, Igniter              375                       X   X   X  X

Ignition Exciter Box       EO                        X   X   X  X

Air, Chapter 75            OC             X   X   X  X   X   X  X

Bleed Air Valve            EO                     X  X   X   X  X

Generator Cooling Duct     EO                     X  X   X   X  X

Engine Controls,

Chapter 76                 OC             X   X   X  X   X   X  X

Thrust Control Unit        EO                 X   X  X   X   X  X

Flex Ball Assembly         OC             X   X   X  X   X   X  X

Engine Indicating,

Chapter 77                 OC             X   X   X  X   X   X  X

Tach, Generator            5,000/4 yrs    X   X   X  X   X   X  X

E.P.R. Transmitter         EO             X   X   X  X   X   X  X

E.G.T. Thermocouple        EO             X   X   X  X   X   X  X

E.G.T. Indicator           OC             X   X   X  X   X   X  X

E.P.R. Indicator           3,000          X   X   X  X   X   X  X

Oil Temp. & Pressure

Transmitters               OC             X   X   X  X   X   X  X

Oil Low Pressure Switch    OC             X   X   X  X   X   X  X

RPM Indicator              5,000/4 yrs    X   X   X  X   X   X  X

Effective date ___________________

Page 15 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HFB 320 HANSA JET

OVERHAUL        PERIOD INSPECTIONS

HOURS OR YRS.   PO  MP  A  B   C   D  E

Exhaust, Chapter 78        OC             X   X   X  X   X   X  X

Tail Cone                  EO             X   X   X  X   X   X  X

Oil, Chapter 79            OC             X   X   X  X   X   X  X

Oil Tank                   EC             X   X   X  X   X   X  X

Oil Pump                   EO             X   X   X  X   X   X  X

Power Plant Notes

* Note 1:  1,800 depending on GE Bulletins accomplished.

* Note 2:  Engine manufacturer recommendation.

Effective date ____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 38.  OPERATIONS SPECIFICATIONS AIRCRAFT

MAINTENANCE - BOEING 727

Form Approved

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04 R075.

WASHINGTON

Page 1 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 727

Inspection/Check Requirements

Checks shall be accomplished in accordance with the

applicable procedures as listed in the airline's

maintenance manual.

"A" Inspection/Check *

To be accomplished before exceeding thirty-five (35)

hours time in service.

"B" Inspection/Check *

To be accomplished before exceeding three hundred (300)

hours time in service.

"C" Inspection/Check *

To be accomplished before exceeding nine hundred (900)

hours time in service.

"D" Inspection/Check *

To be accomplished before exceeding seven thousand

(7,000) hours time in service.

"D" Inspection/Check *

To be accomplished before exceeding seven thousand

(7,000) hours time in service.  (Structural inspections

- one-fourth of operators' fleet will be completed each

7,000 hours; i.e., one-fourth at 7,000; one-fourth at

14,000; one-fourth at 21,000; one-fourth at 28,000).

NOTE:

*    Revision to the times specified for the "A", "B", and

"C" checks can be initiated after accumulation of

satisfactory service experience by the submission of an

amended Operations Specifications - Maintenance to the

assigned inspector for consideration, handling, and

approval.

**   The "D" inspection is based on the premise that the

details of the "A", "B", and "C" checks will be

developed in sufficient depth to assure the

airworthiness of the aircraft until the "D" inspection

interval is reached.

FC - Functional check; check for security and proper

operation.

Effective date ____________________

Page 2 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 727

Overhaul  Inspection

Period    & Check

Period

Air Conditioning, Chapter 21                  O.C.       A,B,C,D

Air Distribution Selector Valve               O.C.       B,C

Air Conditioning Pack Temperature Indicator   O.C.       B,C

Air Cycle Machine                             7,000      B,C

Air Condition Anti-Icing Valve               14,000      B,C

Air Conditioning Pack Shutoff Valve           7,000      B,C

APU Isolation Shutoff Valve                  14,000      B,C

APU Bleed Check Valve                         O.C.       B,C

APU Crossover Check Valve                     O.C.       B,C

Cable Driven Ram Air Door Actuator            O.C.       B,3C

Control Cabin, Temperature Control Valve      O.C.       B,C

Cargo Heating Air Shutoff Valve               O.C.       B,3C

Cabin Temperature Indicator                   O.C.       B,C

Cabin Pressure Manual Controller              O.C.       B,C,D

Cabin Pressure Automatic Controller           O.C.       B,C,D

Cabin Temperature Selector                    O.C.       C,D

Cabin Air Check Valve 3 1/2 in. Diameter      O.C.       B

Cabin Air Check Valve 4 1/2 in. Diameter      O.C.       B,C

Fan Venturi                                  14,000      B,3C

Gasper Fan                                    3,500      B,C

Ground Air Mover Actuator Assembly            O.C.       B,C

Ground Air Mover Fan                          7,000      B,C

Ground Air Connection Check Valve             O.C.

Main Cabin Temperature Control                O.C.       B,C

Motor Driven Ram Air Door Actuator            7,000      B,C

Outflow Valve                                 7,000      A,B,3C

Pressure Equalizer Check Valve                O.C.       B,C,D

Primary Heat Exchanger                        O.C.       D,C

Ram Air Shutoff Valve                         O.C.       B,3C

Ram Air Exhaust Dampers                       O.C.       B,3C

Secondary Heat Exchanger                      O.C.       B,C

Valve Position Indicator                      O.C.       B,C

Water Separator Anti-Icing Thermostat         7,000      B,C

Water Separator                               O.C.       B,3C

Zone Temperature Control Air Shutoff          7,000

Effective date ____________________

Page 3 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 727

Overhaul  Inspection

Period    & Check

Period

Auto Pilot, Chapter 22                        O.C.       A,B,C,D

Aileron Servo Motor and Drive Assembly        7,000      B,3C

Aileron Servo Stop Mechanism                  7,000      B,C

Air Data Sensor                               O.C.       B,C,D

Air Data Sensor Calibrator                    O.C.       B,C,D

Control Panel                                 O.C.       B,C,D

Glideslope Indicator                          O.C.       B,C,D

Position Sensor - Elevator and Elevator Trim  O.C.       B,C,D

Position Sensor - Spoiler                     O.C.       B,C,D

Pitch Control Channel                         7,000      B,C

Pitch Control Channel Calibrator              O.C.       B,C,D

Position Sensor - Rudder                      O.C.       B,C,D

Roll Control Channel                          7,000      B,C

Roll Control Channel Calibrator               O.C.       B,C,D

Rudder Trim and Position Indicator            O.C.       B,C,D

Stabilizer Trim Potentiometer                 O.C.       B,C,D

Stabilizer Trim Servo                         7,000      B,C

Trim Indicator - Elevator and Aileron         O.C.       B,C,D

Warning Light Flasher and Roll Limit

Resistor Module                             O.C.       B,C,D

Yaw Damper Coupler                            7,000      B,C

Yaw Damper Coupler Calibrator                 O.C.       B,C,D

Communications, Chapter 23                    O.C.       A,B,C,D

The maintenance program (overhaul time and

intermediate checks) for this chapter is

to be established in the local Air Carrier

District Office for all units of radio

communication and radio navigation equipment.

Electrical System, Chapter 24                 O.C.       A,B,C,D

AC Voltmeter                                  O.C.       B,C

Battery Charger                               O.C.       B,C

Bus Protection Panel                          O.C.       B,C

Constant Speed Drive                          3,000      B,C

Constant Speed Drive Oil Temperature

Indicator                                   O.C.       B,C

DC Ammeter                                    O.C.       B,C

DC Voltmeter                                  O.C.       B,C

Essential Power Failure Relay                 O.C.       B,3C

Effective date __________________

Page 4 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 727

Overhaul  Inspection

Period    & Check

Period

Electrical System, Chapter 24, continued      O.C.       A,B,C,D

Essential Power Selector Relay                O.C.       B,3C

External Power Transformer - Rectifier        O.C.       B,C

Generator (40 KVA)                            3,000      B,C

Generator Drive Loud Controller               O.C.       B,C

Generator Frequency Meter                     O.C.       B,C

Generator Circuit Breaker                     O.C.       B,C

Generator Control Panel                       O.C.       B,C

Ground Power Relay                            O.C.       B,C

Master Warning Control Unit                   O.C.       B,3C

Reverse Current Contactor                    12,000      B,3C

Static Inverter                               O.C.       B,C

Transformer Rectifier                         O.C.       B,C

Voltage Regulator                             O.C.       B,C

Equipment and Furnishings, Chapter 25         O.C.       A,B,C,D

Equipment Air Flow Detector                   O.C.       B,C

Electric Equipment Blower                     6,000      B,C

Equipment Cooling Air Shutoff Valve          12,000      B,C

Fire Protection, Chapter 26                   O.C.       A,B,C,D

Fire Extinguisher Bottle                     5 years     B,C

Lower Aft Body Overheat Control Unit          O.C.       B,C

Shutoff Valve (Directional Valve)            12,000      B,C-FC

Strut #1 and #3 Overheat Control Unit         O.C.       B,C

Wheel Well Fire Control Unit                  O.C.       B,C

Flight Controls, Chapter 27                   O.C.       A,B,C,D

Aileron Shutoff Valve Cartridge              14,000      B,C,D

Aileron Lockout Gearbox, Outboard             O.C.       B,C,D

Aileron Compensator Assembly                  O.C.       B,C,D

Aileron Hydraulic Pressure Switch Assembly    O.C.       B,C,D

Aileron Control Disconnect Assembly           O.C.       B,C

Aileron Power Control Package                 7,000      B,C

Control Column                                O.C.       B,C,D

Elevator Hydraulic Shutoff Valve Cartridge   14,000      B,C,D

Elevator Hydraulic Compensator Cartridge      O.C.       B,C,D

Elevator Feel Control Assembly                7,000      B,C

Elevator Hydraulic Pressure & Switch

Cartridge                                   O.C.       B,C,D

Effective date __________________

Page 5 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 727

Overhaul  Inspection

Period    & Check

Period

Flight Controls, Chapter 27, continued        O.C.       A,B,C,D

Elevator Feel Computer Package                7,000      B,C

Elevator Power Control Package                7,000      B,C

Flap Asymmetric Shutoff Valve                14,000      B,C

FC-7,000

Flap Drive Gearbox Power Unit                14,000      B,C,D

Flap Drive Gearbox Alternate                 14,000      B,C,D

Flap Drive Gearbox Assembly-Angle-Inboard    14,000      B,C,D

Flap Position Indicator                       O.C.       C,D

Ground Speed Brake Actuator                  14,000      B,C,D

Ground Speed Brake Hydraulic Control Valve   14,000      B,C,D

Ground Spoiler Shutoff Valve                 14,000      B,C,D

Inboard Flap Flow Limiting Valve             14,000      3C,D

Inboard Flap Position Transmitter            14,000      B,C,D

Inboard Flap Drive Offset Gearbox            14,000      B,C,D

Leading Edge Flap Standby Hydraulic Motor    14,000      B,C,D

Leading Edge Flap Actuator and Shuttle Valve 14,000      B,C,D

Leading Edge Slat Actuator and Shuttle Valve 14,000      B,C,D

Leading Edge Flaps and Slats Control Valve   14,000      B,C,D

Leading Edge Flap and Slat Bypass Valve      14,000      B,C,D

Leading Edge Flap Position Switch             O.C.       B,C,D

Leading Edge Slat Position Switch             O.C.       B,C,D

Leading Edge Flap Flow Limiting Valve

(Standby System)                           14,000      B,C,D

Outboard Flap Flow Limiting Valve            14,000      B,C,D

Outboard Flap Drive Angle Gearbox            14,000      B,C,D

Outboard Trailing Edge Flap Transmission

Assembly                                   14,000      B,C,D

Rudder Power Control Unit                    14,000      B,C,D

Rudder Shutoff Valve Cartridge               14,000      B,C,D

Rudder Hydraulic Pressure Compensator

Cartridge                                   O.C.       B,C,D

Rudder Hydraulic Pressure Switch Cartridge    O.C.       B,C,D

Rudder Trim Actuator                          O.C.       B,C,D

Rudder Standby Power Control Unit            14,000      B,C,D

Spoiler Hydraulic Pressure Relief Valve

Cartridge                                  14,000      B,C,D

Spoiler Hydraulic Shutoff Valve Cartridge    14,000      B,C,D

Spoiler Hydraulic Actuator Assembly          14,000      B,C,D

Effective date _________________

Page 6 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 727

Overhaul Inspection

Period   & Check

Period

Flight Controls, Chapter 27, continued        O.C.      A,B,C,D

Speed Brake Lever Control Brake Assembly      O.C.      B,C

Stabilizer Trim Actuator                      7,000     B,C

Stabilizer Trim Drive Motor                   7,000     B,C

Stabilizer Trim Brake                        14,000     B,C

Spoiler Differential Mechanism Assembly       7,000     B,C

Trailing Edge Flap Bypass Valve              14,000     C,D

Trailing Edge Flap Hydraulic Motor           14,000     B,C

Trailing Edge Flap Control Valve             14,000     C,D

Trailing Edge Inboard Flap Transmission

Assembly                                   12,000     C,D

Wing Flap Alternate Drive Motor              12,000     C,D

All Flight Control Cables shall be

tension checked                                       D

Fuel System, Chapter 28                       O.C.      A,B,C,D

Baffle Check Valve                            O.C.      Inspect

for

condition

anytime

tank is

open at

the D

check

Boost Pump                                    7,000     A,B,C,D

Boost Pump Removal Valve                      O.C.      C,D

Boost Pump Bypass Check Valve                 O.C.      C,D

Boost Pump Check Valve                        7,000

Boost Pump Vent Check Valve                   7,000

Engine Shutoff Valve                         14,000     B,C

Fuel Manifold Crossfeed Valve                14,000     B,C

Fuel Dump Control Valve                       7,000

Fuel Dump Nozzle Shutoff Valve               14,000     B,C

Fueling Level Control Pilot Valve             O.C.      C,D

Fueling Level Control Shutoff Valve          14,000

Fueling Shutoff Valve                        14,000

Fueling Manifold Vent Shutoff Valve           O.C.      C,D

Fuel Temperature Probe                        O.C.      C,D

Fuel Temperature Indicator                    O.C.      B,C,D

Fuel Quantity Indicator                       O.C.      C,D

Fuel Quantity Tank Unit                       O.C.      3C

Fuel Quantity Compensator                     O.C.      3C,D

Fuel Quantity Total Indicator                 O.C.      B,C,D

Manual Defueling Valve                        O.C.      B,C

Tank Dump Valve                              14,000     B,C

Effective date __________________

Page 7 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 727

Overhaul  Inspection

Period    & Check

Period

Hydraulic System, Chapter 29                  O.C.       A,B,C,D

Accumulator - System "A"                      O.C.       C,D

Accumulator - System "B"                      O.C.       C,D

Heat Exchanger Assembly                       O.C.       C,D

Indicator, Hyd. Quantity System "A",

"B" and "Standby" Reservoir                 O.C.       B,C,D

Indicator, Remote Pressure                   14,000      C,D

Interconnect Valve, System "A" and "B"       14,000      C,D

Manual Shutoff Valve Cartridge (System

"A" Depressurization)                      14,000      2C

Manual Reservoir Fill Selector Valve          O.C.       A,B

Overheat Sensing Switch                       O.C.       2C,D

Pressure Operated Selector Valve Cartridge

(Standby System)                           14,000      B,C,D

Pump - Engine Driven                          4,000      B,C,D

Pump - AC Motor Driven - System "B"           4,000      B,C,D

Pump - AC Motor Driven (Standby System)      14,000      C,D

Pump - Reservoir Pressure Filling             O.C.       C,D

Pneumatic Pressure Gage, Accumulator          O.C.       B,D

Reservoir - System "A"                        O.C.       C,D

Reservoir - System "B"                        O.C.       D

Reservoir - Standby System                    O.C.       2C,D

Reservoir Pressure Regulating Valve          14,000      2C

Switch Assembly Cartridge, Hyd. Pressure      O.C.       2C,D

Transmitter - Liquid Level System "A"         O.C.       B,C,D

Transmitter - Liquid Level System "B"         O.C.       B,C,D

Transmitter - Liquid Level Standby System     O.C.       B,C,D

Transmitter - Accumulator Pressure           14,000      2C,D

Valve - Pressure Relief Cartridge -

System "A"                                 14,000      2C

Valve Assembly - Hydraulic Suction Shutoff   14,000      2C,D

Valve Assembly Cartridge - Hyd. Motor

Operated (Standby)                         14,000      2C,D

Valve Cartridge - Pressure Relief -

Standby and System "B"                     14,000      2C,D

Ice and Rain Protection, Chapter 30           O.C.       A,B,C,D

Cowl Thermal Anti-Icing Shutoff Valve        14,000      C,D

Inlet Duct Shutoff Valve                     14,000      C,D

Ice Detector                                  O.C.       C,D

Ice Detector Interpreter                      O.C.       C,D

Effective date ____________________

Page 8 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 727

Overhaul  Inspection

Period    & Check

Period

Ice and Rain Protection, Chapter 30,

continued                                   O.C.       A,B,C,D

Thermal Anti-Ice Shutoff Valve               14,000      C,D

Thermal Anti-Ice Engine Bleed Check Valve     O.C.       C,D

Leakage

check at

engine OH

Thermal Anti-Ice Duct Temperature Indicator   O.C.       C,D

Thermal Anti-Ice Isolation Shutoff Valve     14,000      C,D

Thermal Anti-Ice High Pressure Bleed

Shutoff Valve                              14,000      C,D

Thermostatic Modulating Valve                 O.C.     Calibrate

at EO

Windshield Wiper Motor                       14,000      C,D

Instruments, Chapter 31                       O.C.       A,B,C,D

The Maintenance Program (overhaul time and

intermediate checks) for this chapter is

to be established in the local Air Carrier

District Office for all units in this

system including the Flight Recorder.

Landing Gear, Chapter 32                      O.C.       A,B,C,D

Anti-Skid Brake Detector                      7,000      B,C

Anti-Skid Control Shield                     14,000      C,D

Brake System Interconnect Valve              14,000      C,D

Brake Interconnect Pressure Switch           14,000      C

Brake Interconnect Flow Limiting Valve       14,000      C

Brake System Accumulator                      O.C.       B,C,D

Brake Pressure Indicator, Hydraulic           O.C.       B,C,D

Brake Pneumatic Control Valve                 O.C.       D,FC

Brake Pneumatic Pressure Indicator            O.C.       B,C,D

Brake Accumulator & Air Bottle Pressure Gage  O.C.       B,C,D

Brake Accumulator & Air Bottle Pressure

Transmitter                                14,000      B,C,D

Brake Pneumatic System - Hydraulic Transfer

Cylinder                                    O.C.       C,D

Brake Pneumatic Bottle                       5 years     B,C

Brake Deboost Valve                           6,000      A,B,C

Gear Selector Valve                          14,000      C,D

Gear Shuttle and Disconnect Valve            14,000      C,D

Main Gear Sequence Valve                     14,000      C,D

Effective date ____________________

Page 9 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 727

Overhaul  Inspection

Period    & Check

Period

Landing Gear, Chapter 32, continued           O.C.       A,B,C,D

Main Gear Brake Anti-Skid Valve              14,000      C,D

Main Gear Door Safety Valve                  14,000      C,D

Main Gear Hydraulic Actuator                 14,000      C,D

Main Gear Lock Actuator                      14,000      C,D

Main Gear Lock System                         O.C.       C,D

Main Gear Brake Metering Valve                7,000      C

Main Gear Door Sequence Valve                14,000      C,D

Main Gear Door Actuator                      14,000      C,D

Main Gear Assembly (shock strut, side

strut, drag strut & beam, support links,

torsion links, axles)                      14,000      A,B,C,D

Main Gear Axle Sleeve                         O.C.     Wheel or

brake

change

Main Gear Wheel Assembly                      O.C.       A,B,C

Tire

change

Main Gear Brake Assembly                      O.C.       B

Nose Gear Assembly (shock strut, drag brace

strut, torsion links, steering collar)     14,000      A,B,C,D

Nose Gear Wheel Assembly                      O.C.       A,B,C

Tire

change

Nose Gear Brake Assembly                      O.C.       B

Nose Gear Brake Anti-Skid Valve              14,000      C,D

Nose Gear Actuator                           14,000      C,D

Nose Gear Steering Metering Valve            14,000      C,D

Nose Gear Steering Disconnect Valve          14,000      C,D

Nose Gear Bypass Valve                       14,000      C,D

Nose Gear Lock                                O.C.       C,D

Nose Gear Lock Actuator                      14,000      C,D

Nose Gear Lock Retention                     14,000      D

Nose Gear Variable Restrictor                14,000      C,D

Nose Gear Brake Metering Valve                7,000      C

Nose Gear Brake Pressure Reducer Valve       14,000      C,D

Switch Assembly - Hydraulic Pressure          O.C.       C,D

Cartridge

Tail Skid Actuator                           14,000      C,D

Effective date ____________________

Page 10 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 727

Overhaul  Inspection

Period    & Check

Period

Lights, Chapter 33                            O.C.       A,B,C,D

Oscillating Navigation Light                  O.C.       A,B

Rotating Beacon                               O.C.       A,B

Navigation, Chapter 34                        O.C.       A,B,C,D

Ammeter - Pitot Static Heat                   O.C.       C,D

Airspeed Indicator - Air Data System          7,000      C

Air Data Computer                             O.C.       B,C,D

Antenna - Glideslope                          O.C.       B,C,D

ADF Sense Antenna Coupler                     O.C.       B,C,D

ADF Loop Antenna                              O.C.       B,C,D

Angle of Attach Vanes                         O.C.       B,C,D

Control Column Shaker                        14,000      B,C,D

Inertial - Lead Vertical Speed Indicator      7,000      B,C

Machmeter                                     7,000      B,C

Mach Air Speed Warning Switch                 O.C.       C,D

Marker Beacon Antenna                         O.C.       C,D

Pitot Tube Probe                              O.C.       C,D

Ram Air Temperature Indicator                 O.C.       C,D

Ram Air Temperature Bulb                      O.C.       C,D

Static Selector Valve                         O.C.       C,D

Stall Warning Computer                        O.C.       C,D

Total Air Temperature Probe                   O.C.       C,D

Total Air Temperature Indicator               7,000      C

True Airspeed Indicator                      14,000      B,C,D

Oxygen System, Chapter 35                     O.C.       A,B,C,D

Crew Oxygen System Pressure                  14,000      C,D

Crew Oxygen Demand Regulator                  7,000      C

Crew Oxygen System Pressure Reducer          14,000      C,D

Electro-Pneumatic Continuous Flow

Control Unit                                7,000      3C

Oxygen Bottles                               5 Years     A,B,C,D

Oxygen Bottles, Portable                     5 Years     A,B,C,D

Oxygen Shutoff Valve                          O.C.       D

Oxygen System Pressure Indicator              O.C.       A,B,C

Oxygen System Charging Valve                  7,000      C

Pneumatic Continuous Flow Control Unit        7,000      3C

Passenger Oxygen System Latch, Valve and

Manifold Assembly                           O.C.       3C,D

Effective date ____________________

Page 11 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 727

Overhaul  Inspection

Period    & Check

Period

Pneumatic, Chapter 36                         O.C.       A,B,C,D

Air Conditioning Airflow Control Valve        7,000

Air Conditioning Airflow Sensing Venturi

and Servo Unit                              7,000

Bleed Air Heat Exchanger Temperature

Controller                                  O.C.       C,D

Dual Pneumatic Manifold Pressure Gage         O.C.       C,D

Engine Fan Air Modulating Valve               7,000      C

Engine Bleed Shutoff Valve                    3,500      C

Engine No. 2 Bleed Air Shutoff Valve         14,000      C,D

Engine Bleed Air Isolation Shutoff Valve     14,000      C,D

Ground Cart Starting Pneumatic Connector      O.C.       C,D

Heat Exchanger - Pneumatic System             O.C.       C,D

High Pressure Bleed Modulating and

Shutoff Valve                               3,500      C

Pneumatic Manifold Air Pressure Transmitter   O.C.       C,D

Water and Waste, Chapter 38                   O.C.       A,B,C,D

Systems shall be maintained                "On Condition"

Airborne Auxiliary Power, Chapter 49          O.C.       A,B,C,D

Auxiliary Power Unit - Airborne               1,500      A,B,C

APU Exhaust Door Actuator                    14,000      B,C

APU Fire Bottle                              5 years     B,C

Structures, Chapter 50                        7,000 1/4  A,B,C,D

Doors, Chapter 52                             7,000 1/4  A,B,C,D

Emergency Hatches                            14,000 1/4

Fuselage, Chapter 53                          7,000 1/4  A,B,C,D

Fuselage Tension Bolts between BS 360

and 1183                                   14,000 1/4

Fuselage Skin and Stringer Splices in

Crown Area (Stringer S-6 and above)

at BS 360, 480, 740, 870, 1080.45          14,000 1/4

Fuselage Center Engine Inlet Duct             2,500      C

Fuselage Upper and Lower Torque Boxes         7,000

Fuselage Frames at BS 760.95, 785.95,

804.5, 825.95 and 848.95                    7,000 1/2

Center Engine Support                         3,000

Effective date ___________________

Page 12 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 727

Overhaul  Inspection

Period    & Check

Period

Nacelles/Pylons, Chapter 54                   3,000      A,B,C,D

Forward Engine Mount Fittings, Thrust Links

and Aft Engine Mount Fittings               3,000

Stabilizers, Chapter 55                       7,000      A,B,C,D

Horizontal Stabilizer Skin Panel              3,500      B,C

Vertical Fin Skin Panels                      3,500      B,C

Elevator Tab                                  3,500      B,C

Rudder Internal Structure                     7,000 1/4  C

Rudder Hinge Fittings                         7,000 1/4  B,C

Rudder Tabs                                   3,500      B,C

Wings, Chapter 57                             7,000 1/4  A,B,C,D

Right and Left Wing Upper and Lower Interspar 3,500      B,C

Lower Interspar Skin Under Wing Body Fairing

and Wing Center Section                     7,000      B,C

Right and Left Wing Lower Surface at

WS 224.5                                    7,000      C

Wing Body Breather Web and BBL 13.0 Beam      7,000

Right and Left Wing Terminal Forgings         7,000

Right and Left Wing Body Bottle Pin

Retaining Bolts and Forward Lug

Retaining Bolt                              7,000      C

Main Landing Gear Rear Trunnion Support

Beam and Attach Links                       7,000      C

Wing Trailing Edge Skin and Support Structure 7,000      C

Flap Tracks, Carriages, Attachments, and

Supports                                    7,000      B,C

Inboard/Outboard Aileron Balance Panels       7,000      C

Inboard/Outboard Aileron Adjustable Weights   7,000      C

Inboard/Outboard Aileron Tabs                 3,500      B,C

Engine Turbine, Chapter 72                    3,000      A,B,C,D

Accessory and Component Drive Gear Box

Section                                     3,000      B

Air Inlet Section                             3,000      A,B,C

Combustion Section                            3,000     PP NOTE 1

Compressor Section                            3,000      A,B,C

Diffuser Section                              3,000     PP NOTE 1

Exhaust Section                               3,000      A,B,C

Fan Discharge Section                         3,000      B,C

Turbine Section                               3,000      A,B,C

Basic Engine Plumbing, Wiring, and Linkages   3,000      B,C

Effective date ____________________

Page 13 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 727

Overhaul  Inspection

Period    & Check

Period

Engine Fuel and Control, Chapter 73           O.C.       A,B,C,D

Burner Pressure Sense Line Drain              O.C.       B,C

PP NOTE 4

Engine Driven Fuel Pump                       6,000      B,C

Fuel Control Unit - Hamilton Standard JFC-60  6,000      B,C

Fuel Control Unit Inlet Temperature Sensor    6,000      A,B,C

Fuel Strainer (FCU)                           6,000      B,C

PP NOTE 2

Fuel Deicing System                           O.C.       B,C

PP NOTES 2&3

Fuel Flow Transmitter                         6,000      B

Fuel Flow Indicator                           6,000      C

Fuel Flow Power Supply Unit                   6,000

Pressure Differential Warning Transmitter     O.C.       B,C

Pressurizing and Dump Valve                   O.C.       B,C

Plumbing and Wiring                           O.C.       B,C

Fuel Heater                                   O.C.

Fuel Deicing Air Valve                        O.C.

Fuel Pressure Drop Warning Switch             O.C.

Fuel Deicing System Filter                    O.C.       B,C

Ignition, Chapter 74                          O.C.       A,B,C,D

High Tension Leads                            3,000      B,C

Ignition Exciter Unit                         O.C.       B,C

Igniter Plugs Champion AA72S Continuous Duty  O.C.       B,C

Igniter Plugs Champion AA72S Intermittent

Duty                                        O.C.       B,C

Replaceable Gap Assembly                      3,000      B,C

Air, Chapter 75                               O.C.       A,B,C,D

Anti-Icing Air System Plumbing and Wiring     6,000      B,C

Compressor Inlet Anti-Icing Regulator         6,000      B,C

Compressor Inlet Anti-Icing Shutoff Valve     6,000      B,C

Compressor Bleed System Valves and Plumbing   6,000

CSD Ejector Air Shutoff Valve                 6,000      B

CSD Oil Cooler                                6,000      B

Pressure Ratio Bleed Control                  O.C.       B,C

Air Shutoff Valve and Actuator                O.C.       B,C

Anti-Icing Air Regulator                      O.C.       B,C

Engine Controls, Chapter 76                   O.C.       A,B,C

Engine Control Linkages                       O.C.       B,C

Effective date ____________________

Page 14 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 727

Overhaul  Inspection

Period    & Check

Period

Engine Indicating, Chapter 77                 O.C.       A,B,C

Engine Vibration Amplifier Unit               O.C.       C

Engine Vibration Indicator                    O.C.       C

Engine Vibration Pickup          @           E.O.       B

Exhaust Gas Temperature Probes                O.C.       C

Exhaust Gas Temperature Indicator             O.C.       C

Exhaust Pressure @tio Probes and Plumbing    O.C.       A,B,C

Engine Pressure Ratio Transmitter             E.O.       C

Engine Pressure Ratio Indicator               O.C.       C

Tachometer Generator                          E.O.       B

Tachometer Indicators N1 and N2               O.C.       C

Exhaust, Chapter 78                           O.C.       A,B,C

Directional Valve Assembly                    6,000      A,B

Thrust Reverser Actuator                      O.C.       A,B

Thrust Reverser Assembly                      O.C.       A,B

Thrust Reverser Sequence Valve                E.O.

Thrust Reverser Indicating System

Oil System, Chapter 79                        O.C.       A,B,C

Oil Tank and Stick Quantity Indicator         O.C.       A,B,C

Oil System Plumbing and Connections,

Drain Valve                                 E.O.       B,C

Fuel and Oil Cooler and Temperature

Regulator                                   E.O.       B,C

Engine Oil Pressure Transmitter               E.O.       B

Engine Oil Pressure Indicator                 O.C.       C

Oil Quantity Indicator                        O.C.       C

Oil Quantity Tank Unit                        O.C.       B

Low Oil Pressure Switch                       O.C.       B

Oil Filter Bypass Switch                      E.O.       B

Oil Temperature Transmitter                   O.C.       B

Oil Temperature Indicator                     O.C.       C

Oil Strainer                                  O.C.       B,C

Starting System,  Chapter 80                  O.C.       A,B,C

Pneumatic Starter                             6,000      B,C

Starter Pressure Regulating and Shutoff

Valve                                       6,000      B,C

Effective date ____________________

Page 15 of 15

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

BOEING 727

POWERPLANT NOTES

NOTE 1.   Access for inspection is impeded by engine fan duct.

Specific instructions will be established by carriers

to assure that flight crews are aware of indications of

hot section case distress.

NOTE 2.   Filters should be cleaned within 150 hours.

NOTE 3.   Filter should be sampled daily on new aircraft or after

tank repairs until residual is disposed of.

NOTE 4.   Drain at "B" check.

Effective date ____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 39.  OPERATIONS SPECIFICATIONS AIRCRAFT

MAINTENANCE - DOUGLAS DC-9

UNITED STATES OF AMERICA       Form Approved

FEDERAL AVIATION AGENCY       Budget Bureau

WASHINGTON                NO. 04 R075.

Page 1 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-9

Inspection/Check Requirements

Checks shall be accomplished in accordance with the applicable

procedures as listed in the airline's maintenance manual.

"A" Inspection/Check *

To be accomplished at intervals not exceeding fifty (50) hours

time in service.

"B" Inspection/Check *

To be accomplished at intervals not exceeding three hundred (300)

hours time in service.

"C" Inspection/Check *

To be accomplished at intervals not exceeding nine hundred (900)

hours time in service.

"D" Inspection/Check *

To be accomplished at intervals not exceeding seven thousand

(7000) hours time in service.  (One-fourth of fleet at 7000,

one-fourth of fleet at 14,000, one-fourth at 21,000, and

one-fourth of fleet at 28,000).

NOTE:

*    Revision to the times specified for the "A", "B", and "C"

checks can be initiated after accumulation of satisfactory

service experience by the submission of an amended

Operations Specifications - Maintenance to the assigned

inspector for consideration, handling, and approval.

**   The "D" inspection is based on the premise that the details

of the "A", "B", and "C" checks will be developed in

sufficient depth to assure the airworthiness of the aircraft

until the "D" inspection interval is reached.

Effective date __________________

Page 2 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-9

Overhaul  Inspection

Period    & Check

Period

Air Conditioning, Chapter 21                  O.C.       A,B,C,D

Valve - Ram Air                               O.C.       C

Fan - Heat Exchanger Cooling Air              7000       C,D

Actuator - Valve, Cabin Air Outflow           7000       C,D

Controller - Cabin Pressure                   O.C.       C,D

Regulator - Reset, Cabin Pressure Control    12,500      D

Valve - Safety, Cabin Pressure               14,000      C,D

Valve - Pressure Regulator, Air Condition    14,000      C,D

Valve - Flow Control, Air Conditioning       12,500      C,D

Sensor - Pressure Differential, Cabin to

Reference                                   O.C.       C

Indicator - Pressure, Air Conditioning

Supply                                      O.C.       C,D

Indicator - Cabin Rate of Climb               O.C.       C,D

Indicator - Cabin Differential Pressure

and Altitude                                O.C.       C,D

Turbine - Cooling                             7000       C,D

Fan - Cooling, Radio Rack                     7000       C,D

Switch - Differential Pressure, Fan           O.C.       C,D

Indicator - Position, Temp. Control Valve     O.C.       C,D

Transmitter - Temp. Control Valve, Position   O.C.       C,D

Indicator - Cabin Duct Temperature            O.C.       C,D

Thermostat - Water, Separator Discharge       7000       C,D

Valve - Temperature Control, Water

Separator                                  12,500      C,D

Auto Pilot, Chapter 22                        O.C.       A,B,C,D

Computer - Pitch Axis                         7000       C,D

Computer - Roll Axis                          7000       C,D

Computer - Stability Augmentation             7000       C,D

Actuator, Mach Trim and Yaw Damper            7000       C

Drive - Elevator and Aileron Servo            7000       C

Panel - Controller                            O.C.       B,D

Indicator - Trim                              O.C.       B,D

Computer - Air Data                           O.C.       B,D

Communications, Chapter 23

The Maintenance Program (overhaul time and

intermediate checks) for this chapter is to be

established in the local Air Carrier District

Office for all units of the communication systems.

Effective date ____________________

Page 3 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-9

Overhaul  Inspection

Period    & Check

Period

Electrical System, Chapter 24                 O.C.       A,B,C,D

Transmission - Constant Speed Drive           3000       B

Heat Exchanger - Constant Speed Drive

Oil Temperature                             O.C.       C

Indicator - Constant Speed Drive Oil

Temperature                                 O.C.       C,D

Generator, AC 40KVA                           3000       B

Panel, Generator Control                      O.C.       C,D

Panel, Bus Control                            O.C.       C,D

Regulator, Voltage                            O.C.       C,D

Relay - Generator, External Power,

AC, Crosstie, APU                           7000       C

Inverter Emergency                            O.C.       C,D

Transformer Rectifier                         O.C.       C,D

Battery Charger                               O.C.       C,D

Loadmeter (AC and DC)                         O.C.       C,D

AC Voltmeter                                  O.C.       C,D

Frequency Meter                               O.C.       C,D

Battery                                       O.C.       C,D

DC Volt/Ammeter                               O.C.       C,D

Equipment and Furnishings, Chapter 25         O.C.       A,B,C,D

Emergency Equipment                           O.C.       A,B,C,D

Coffeemaker                                   O.C.

Seat Belts                                    O.C.       A,B,C,D

Fire Protection, Chapter 26                   O.C.       A,B,C,D

Fire Detector                                 O.C.       B

Control - Fire Warning Bell                   O.C.       B

Control - Fire Warning Horn, APU              O.C.       B

Container - Fire Extinguisher                5 years     C,D

Cartridge - Dual Squib                       4 years     C,D

Flight Controls, Chapter 27                   O.C.       A,B,C,D

Actuator Aileron Trim                         O.C.       C,D

Damper - Aileron and Elevator                14,000      C,D

Valve - Power Shutoff, Rudder Hydraulic      14,000      C,D

Damper - Rudder                              14,000      C,D

Feel Spring - Rudder Trim and Load            O.C.

Power Package - Hydraulic Rudder Control     14,000      C,D

Actuator Limiter - "Q" Bellows, Rudder

Throw                                       O.C.       C,D

Effective date ____________________

Page 4 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-9

Overhaul  Inspection

Period    & Check

Period

Flight Controls, Chapter 27, continued        O.C.       A,B,C,D

Valve - Elevator Control                     14,000      C,D

Valve - Hydraulic Return Relief              14,000      C,D

Valve - Hydraulic Pressure Reducer and

Bleed                                      14,000      C,D

Cylinder - Elevator Power Control            14,000      C,D

Accumulator - Hydraulic                       O.C.       C,D

Switch - Elevator Press. Low                  O.C.       C,D

Motor Actuator - Primary Longitudinal Trim   14,000      C,D

Motor Actuator - Alternate Longitudinal

Trim                                       14,000      C,D

Jack Screw                                   14,000      C,D

Box - Longitudinal Trim Gear                 14,000      C,D

Valve - Wing Flap Control                    14,000      C,D

Cylinder - Wing Flap Actuating               14,000      C,D

Transmitter - Flap Position                   O.C.       C,D

Indicator - Flap Position, Dual               O.C.       C,D

Actuator - Ground Spoiler, Automatic         14,000      C,D

Valve - Ground Spoiler Control               14,000      C,D

Cylinder - Actuating Ground Spoiler          14,000      C,D

Actuator - Spoiler Flight                    14,000      C,D

Fuel System, Chapter 28                       O.C.       A,B,C,D

Pump - Boost Fuel                             7000       C

Pump - Engine Start                           7000       C,D

Valve - Pressure, Crossfeed (Mech)           14,000      C,D

Valve - Engine Fuel Fire Shutoff             14,000      C,D

Valve - APU - Fuel Shutoff (Solenoid)        14,000      C,D

Indicator - Fuel Quantity Master              O.C.       C,D

Indicator - Repeater, Fuel Quantity           O.C.       C,D

Indicator - Totalizer, Fuel Quantity          O.C.       C,D

Probe - Fuel Quantity                         O.C.       D

Valve - Fuel Fill                            14,000      C,D

Hydraulic System, Chapter 29                  O.C.       A,B,C,D

Pump - Hydraulic - Engine Driven              4000       B

Pump - Hydraulic - Electric, Auxiliary        4000       B

Motor Pump - Reversible                      14,000      B

Pump - Hand - Ground Service                  O.C.       C

Reservoir - Hydraulic System                  O.C.       C,D

Accumulator                                   O.C.       C,D

Valve - Priority                             14,000      C

Valve - Spoiler Shutoff and System

Depressurization                            O.C.       C

Valve - Engine Driven Pump Fire Shutoff      14,000      C

Filters                                       O.C.       C

Effective date ____________________

Page 5 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-9

Overall   Inspection

Period    & Check

Period

Hydraulic System, Chapter 29, continued       O.C.       A,B,C,D

Indicator - Fluid Quantity - Hydraulic        O.C.       C,D

Transmitter - Fluid Quantity                  O.C.       C,D

Indicator - Hydraulic Pressure                O.C.       C,D

Transmitter - Hydraulic Pressure              O.C.       C,D

Switch - Warning - Hydraulic System

Low Pressure                                O.C.       C,D

Thermoswitch - Over Temp Hydraulic Fluid      O.C.       C,D

Ice and Rain Protection, Chapter 30           O.C.       A,B,C,D

Tail De-icer Timer                            7000       C

High Pressure Switches                        O.C.       C,D

Pressure Regulator & Shutoff Valves           7000       C

Temperature Sensors                           O.C.       C

Air Intakes                                   O.C.       A,C,D

Pitot and Static                              O.C.       B,C,D

Wiper and Rain Repellent                      O.C.       C,D

Motor                                        14,000      C,D

Water Lines                                   O.C.       C

Instruments, Chapter 31                       O.C.       A,B,C,D

The Maintenance Program (overhaul time and

intermediate checks) for this chapter is to

be established in the local Air Carrier

District Office for all units in this

system including the flight recorder.

Landing Gear, Chapter 32                      O.C.       A,B,C,D

Main Landing Gear                             7000       A,B,C,D

Nose Landing Gear                             7000       A,B,C,D

Hydraulic Control System                     14,000      C,D

Hydraulic Control System (Wheels and Brakes)  O.C.       C

Hydraulic Brake Control Valve                14,000      C

Accumulators                                  O.C.       A,B

Brake Fluid Quantity Limiter                  7000       C,D

Anti-skid System                              O.C.       C,D

Control Box                                   O.C.       C,D

Wheels                                        O.C.       B

Brakes                                        O.C.       B

Steering Hydraulic Controls                   O.C.       C,D

Steering Control Valve                       14,000      C,D

Bypass & Relief Valve                        14,000      C,D

Steering Cylinder                            14,000      C,D

Nose Wheel Swivel Glands                      O.C.       C,D

Positioning and Warning                       O.C.       A,B,C,D

Effective date ___________________

Page 6 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-9

Overhaul  Inspection

Period    & Check

Period

Lights, Chapter 33                            O.C.       A,B,C,D

Lights - Flight Compartment                   O.C.       B,C,D

Navigational Lights - Wing Tip                O.C.       C,D

Lights - Anti-collision                       O.C.       A,B

Lights - Landing and Taxi                     O.C.       A,B

Battery Pack - Cabin Emergency Lights         O.C.       B

Light - Pilot's Emergency Portable            O.C.       C

Navigation, Chapter 34                        O.C.       A,B,C,D

The Maintenance Program (overhaul time and

intermediate checks) for this chapter is to

be established in the local Air Carrier

District Office for all units in this system.

Oxygen System, Chapter 35                     O.C.       A,B,C,D

Cylinder, Oxygen, Crew                        O.C.       B

Regulator - Oxygen, Crew Cylinder,

Crew Pressure                              14,000      B,D

Regulator - Oxygen, Crew Pressure Breathing  14,000      B,D

Cylinder - Oxygen, Passenger Pressure         O.C.    Hyst. 5 yrs

Regulator - Oxygen, Passenger Pressure       14,000      C,D

Cylinder - Oxygen, Attendants and

Crew Portable                               O.C.    Hyst. 5 yrs

Pneumatic, Chapter 36                         O.C.       A,B,C,D

Valve - Pneumatic Crossfeed                  14,000      C,D

Valve - Check, Pneumatic and APU 8th Stage    E.O.       C

Valve - Augmentation                          7000       C,D

Regulator - Pneumatic Pilot Pressure          7000       C,D

Valve - Ground Connection & Check Pneumatic   O.C.       C,D

Control - Ice Protection Anticipation         O.C.       C,D

Indicator - Pneumatic Pressure                O.C.       C,D

Transmitter - Pneumatic Pressure              O.C.       C,D

Sensor - Overheat, Tail Compartment           O.C.       C,D

Water and Waste, Chapter 38                   O.C.       A,B,C,D

Water Supply                                  O.C.       A,B,C,D

Waste Disposal                                O.C.       A,B,C,D

Effective date ____________________

Page 7 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-9

Overhaul  Inspection

Period    & Check

Period

Airborne Auxiliary Power, Chapter 49          O.C.       A,B,C,D

Gas Turbine                                   2200*      B,C,D

Combustion Chambers                           1100*

Unit & Low Pressure Filters                   500*       C

Acceleration & Overtemp Control Thermostat    O.C.       C,D

Ignition Plug                                 500*       C,D

Starter Motor                                 2200*      C,D

Load Control Thermostat                       O.C.       C,D

Centrifugal Switch                            2200*      C,D

Generator - Tach                              O.C.       B,C

Oil Filter                                               C

* Operating Time for Unit - NOT aircraft time.

Oil Change to be at Manufacturer recommendations.

Structures, Chapter 51                        O.C.       A,B,C,D

Doors, Chapter 52                             O.C.       A,B,C,D

Snubber - Forward Entrance Door               O.C.       B

Motor - Stairway Gearbox Actuator             O.C.       B,C

Motor - Stairway Handrail                     O.C.       B,C

Cylinder - Retract, Ventral Stairs            O.C.       C

Valve - Ventral Stair                         O.C.       C

Passenger Aft Entrance Door                   7,000      B,C,D

Main Gear Support Fittings and Auxiliary

Spars                                       2500       B,C,D

Emergency Exit Doors, Zone 58 (LH and RH)     7000       B,C,D

Forward Passenger Entrance and Service Door   7000       B,C,D

Electrical and Electronics Compartment Door  14,000      B,C,D

Baggage Compartment Doors                     7000

Framing Around Main Cargo Door               14,000

Main Cargo Door                              28,000

Fuselage, Chapter 53                          O.C.       A,B,C,D

Radome and Pressure Bulkhead                  7000       A,B,C,D

Bulkhead Station 786 Internal Structure      28,000      C,D

Floor Beams Station 69 to 148                28,000      C,D

Top of Center Section - Center Aisle

Between Inboard Seat Tracks and Sides      28,000      C,D

Fuselage Internal Structure                  28,000      C,D

Rear Baggage Compartment Interior            28,000      C,D

Effective date ____________________

Page 8 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-9

Overhaul  Inspection

Period    & Check

Period

Fuselage, Chapter 53, continued               O.C.       A,B,C,D

Forward Baggage Compartment Interior         28,000      B,C

Body Station 642 Bulkhead                    28,000      C,D

Nose Wheel Well - Canted Panel - Support

Beams and Adjacent Area                    28,000      A,B,C,D

Fuselage Interior Structure Production

Splice 817 to 908                           7000       D

Nacelle and Pylons, Chapter 54                O.C.       A,B,C,D

Firewall, Pylon, and Engine Mount Fittings    7000

Fuselage Bulkhead and Pylon Spar Stubs        7000       C,D

Pylon Spar and Structure, Station 786         7000       C,D

Stabilizers, Chapter 55                       O.C.       A,B,C,D

Elevator Hinge Attachment, Dampers

and Adjacent Structure                      7000       B,C,D

Vertical Stabilizer Installation and

Dorsal Fin Structure                        7000       B,C,D

Stabilizer Outer Panel to Center Section

Joints, Upper and Lower Surfaces            7000       B,C,D

Rudder Spar and Adjacent Internal Structure

Horizontal Stabilizer                       7000       B,C,D

Vertical Stabilizer Leading Edge Interior    14,000

Elevator Front and Rear Spars, Elevator

Interior Structure, Elevator Tabs          28,000      B,C,D

Horizontal Stabilizer Leading Edge, Tip,

Front Spar and Interior                    28,000      C,D

Windows, Chapter 56                           O.C.       A,B,C,D

Windshield, LH and RH                         O.C.       A,B,C

Window - Cockpit LH and RH Sliding            O.C.       A,B,C

Window - Cockpit LH and RH - Aft              O.C.       A,B,C

Window - Eyebrow LH and RH                    O.C.       A,B,C

Windshield - Center                           O.C.       A,B,C

Wings, Chapter 57                             O.C.       A,B,C,D

Wing Leading Edge Interior                    7000       C,D

Wing Tip - Interior                          14,000      C,D

Wing to Fuselage Upper Attach Angle          14,000

Station 484-645                             7000       C,D

Wing Flaps - Internal                        14,000      C,D

Wing Internal                                14,000

Front Spar - Wing Center Section             28,000      C,D

Effective date ____________________

Page 9 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-9

Overhaul  Inspection

Period    & Check

Period

Powerplant, Chapter 71                        O.C.       A,B,C,D

Nose Cowl                                     O.C.       A,B,C

Engine Turbine, Chapter 72                    4800

Engine Fuel and Control, Chapter 73           O.C.       A,B,C,D

Fuel Heater Valve                             7000       B

Fuel Heater                                   O.C.       B,C

Fuel Pump                                     O.C.       B,C

Valve - Pressurizing and Dump                 O.C.       B,C

De-icer Timer                                 O.C.       B

Fuel Control                                  O.C.       B,C

Indicator - Fuel Temperature                  O.C.       B,C

Indicator - Fuel Flow                         O.C.       B,C

Power Supply, Fuel Flow                       O.C.       C

Switch - Low Fuel Press.                      O.C.       C

Transmitter - Fuel Flow                       7000       B,C

Eductor - Fuel Vapor                          O.C.       B,C

Air, Chapter 75                               O.C.       A,B,C,D

Valve - Engine Anti-ice                       7,000      C

Valve - Shutoff, Cowl Anti-icing              7,000      C

Valve - Thermostat Control, Cowl Anti-icing   O.C.       C

Engine Controls, Chapter 76                   O.C.       A,B,C,D

Engine Indicating, Chapter 77                 O.C.       A,B,C,D

Generator - Tachometer N1 and N2              O.C.       C

Indicator - Tachometer N1 and N2              O.C.       C

Transmitter - Engine Press Ratio              O.C.       C

Indicator - Engine Press Ratio                O.C.       C

Monitor - AVM                                 O.C.       B,C

Indicator - AVM                               O.C.       B,C

Pick-Up AVM                                   O.C.       B,C

Indicator - Exhaust Gas Temp                  O.C.       C

Effective date ____________________

Page 10 of 10

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

DOUGLAS DC-9

Overhaul  Inspection

Period    & Check

Period

Exhaust, Chapter 78                           O.C.       A,B,C,D

Gauge - Accumulator Pressure                  O.C.       B,C

Accumulator, Thrust Reverser                  O.C.       B,D

Actuator - Thrust Reverser Bucket             O.C.       B

Indicating - Thrust Reverser System           O.C.       C

Switch - Low Pressure Warning                 O.C.       C

Reverser - Thrust and Exhaust Nozzle          E.O.       B,C

Valve - Control, Thrust Reverser              O.C.       B,C

Oil, Chapter 79                               O.C.       A,B,C,D

Cooler - Engine Fuel/Oil                      O.C.       B,C

Sensor, Oil Temperature                       O.C.       B,C

Indicator - Oil Pressure                      O.C.       C

Indicator - Oil Quantity                      O.C.       C

Indicator - Oil Temperature                   O.C.       C

Switch - Low Pressure Warning                 O.C.       B,C

Transmitter - Oil Pressure                    O.C.       B,C

Switch - Filter Differential Pressure         O.C.       B,C

Transmitter - Oil Quantity                    O.C.  @@@

Starting, Chapter 80                          O.C.       A,B,C,D

Starter - Pneumatic                           7000       B,C

Valve - Regulating Shutoff, Air Starter       7000       B

Switch - Starter Control                      O.C.       B

Ignition - Exciter                           12,000      B,C

Igniter Plugs                                 2000       B,C

Effective date ____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 40.  OPERATIONS SPECIFICATIONS, AIRCRAFT MAINTENANCE -

HAWKER SIDDELEY 748 SERIES 2A

Form Approved.

UNITED STATES OF AMERICA       Budget Bureau

FEDERAL AVIATION AGENCY       No. 04 R075.

WASHINGTON

PART D                                          Page 1 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

HAWKER SIDDELEY 748 SERIES 2A

Thorough inspection shall be accomplished in accordance with the

applicable procedures as listed in ABC Airlines Maintenance

Manual.

Preflight (Pre/Flt) shall be accomplished each service calendar

day.  Inspection shall be in accordance with the applicable

procedures listed in ABC Airlines Maintenance Manual.

Special Inspections.

The frequency and procedure for performing special

inspections will be accomplished as specified in the

operator's maintenance manual.

Overhaul and inspection/check period time limitations

specified in hours and calendar time are maximum limits

of whichever occurs first.

Check A Inspections.  To be accomplished within 100 hours of

aircraft time in service since last check.

Period Inspections. (PI)  The procedure for the performance of

period inspections will be accomplished as specified in ABC

Airlines Maintenance Manual.  Period inspections must be

accomplished at intervals not to exceed 500 hours of aircraft

time in service.  The #1 period inspection will be accomplished

each 500 hours of aircraft time in service or 90 days, whichever

occurs first.

Aircraft shall not be utilized in air carrier or commercial

operations unless:

a.   The aircraft and its component parts, accessories, and

appliances are maintained in an airworthy condition in

accordance with the schedule of maintenance and inspection

functions and procedures set forth in the operator's

maintenance manual.

b.   OC "On Condition" items will be maintained in continuous

airworthiness condition by periodic and progressive

inspections, checks, services, repair, and/or preventive

maintenance and shall be appropriately described in the

operator's maintenance manual.

c.   Parts or subcomponents not listed below will be checked,

inspected and/or overhauled at the same time limits

specified for the component or accessory to which such parts

or subcomponents are related.

Effective date ____________________

Page 2 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

HAWKER SIDDELEY 748 SERIES 2A

Abbreviations used in the HS/748 Series 2A maintenance

specifications are defined as follows:

PI - Indicates "Period Inspection"

PRE/FLT - Indicates "Preflight Inspection"

FC - Indicates "Functional Check"

BC - Indicates "Bench Check"

EO - Indicates "Engine Overhaul"

EC - Indicates "Engine Change"

OC - Indicates "On Condition"

HYD - Indicates "Hydrostatic Test"

CALIB - Indicates "Calibration"

Life Limited Components

The service life limits for aircraft structural parts and

components which are fatigue critical are listed in the Hawker

Siddeley 748 Recommended Maintenance Schedule, Pages 12 to 18

inclusive.  Engine and propeller life limited parts are listed in

the Hawker Siddeley 748 Recommended Maintenance Schedule, and may

not be changed without CAA or FAA approval.

*  These items do not have a set overhaul period.  If the unit

becomes defective before the quoted hours the unit is repaired.

If the defect occurs after the quoted hours the unit is

overhauled.

**  Inspections, Hydrostatic Test, and Life Limits" will be

accomplished as set forth in Part 173, Chapter 1, Subtitle B of

CFR 49 currently in effect.

Page 3 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HAWKER SIDDELEY 748 SERIES 2A

OVERHAUL    PRE-  INSPECTION AND CHECK

HOURS/YRS.  FLT.  PERIODS

CHECK A  PERIODS OTHER

AIR CONDITIONING,

CHAPTER 21               OC          X     X        X

Fans - Radio Crate

Cooling                 1000/2 yrs.                X

Fan - Ventilation Fan

(AC)                    2 yrs.                     X

Fan - Heat Exchanger

Fan                     2000                       X

Temperature Control

Valve Actuator          5000/3 yrs.                X

Actuators - Spill Valve  1000/2 yrs.                X

Pressure Controller      10,000/     X     X        X

4 yrs.

Duct Relief Valve        10,000/                    X

4 yrs.

Discharge Valve          10,000/                    X

4 yrs.

Temperature Control

Valve                   3 yrs.            X        X

Supercharger             2400                       X

Spill Valve              3000/2 yrs.                X

Cabin Pressure Safety

Valve                   10,000/                    X

4 yrs.

Cold Air Unit            2400                       X

Cabin Pressure Indicator OC                         X    (6000)*

Cabin Height Indicator   OC                         X    (6000)*

Spill Valve Position

Indicator               OC                         X

Cabin Rate of Climb

Indicator               OC          X     X        X    (6000)*

Temperature Control Valve

Position Indicator      OC                         X

Spill Valve Position

Transmitter             OC                         X

Mass Flow Controller     10,000/                    X

4 yrs.

COMMUNICATIONS,

CHAPTER 23               OC          X     X        X

To be determined by

assigned inspector.

Station Box              3 yrs.                     X

ELECTRICAL POWER,

CHAPTER 24               OC          X     X        X

Inverter                 1000                       X

Generator                2400/3 yrs.                X      Brush

change

at 1200.

Alternator               2400/3 yrs.                X      Brush

change

at 1200.

Auto Transformers        OC                         X

Effective date _____________________

Page 4 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HAWKER SIDDELEY 748 SERIES 2A

OVERHAUL    PRE-  INSPECTION AND CHECK

HOURS/YRS.  FLT.  PERIODS

CHECK A  PERIODS OTHERS

EQUIPMENT AND FURNISHINGS,

CHAPTER 25               OC          X     X        X

To be determined by

assigned inspector.

Pilots safety harness    12,000/4 yrs.

FIRE PROTECTION,

CHAPTER 26               OC          X     X        X

Relay Unit               OC                         X    Bench

test at

10,000/5

yrs. &

12,000/6

yrs.

Scrap at

15,000/7

yrs.

Base Unit                10,000/5 yrs.              X

Fire Extinguisher

Cartridge               2 yrs.                     X

Fire Extinguisher

Bottle                **5 yrs.      X     X        X

(Hyd. or retire

appropriate for

bottle used)

FLIGHT CONTROLS,

CHAPTER 27               OC          X     X        X

Flap Motor               5000 Ldgs/                 X

3 yrs.

Flap Carriage Assemblies 5000 Ldgs.  X     X        X

Reversing Contactor      5000 Hrs/                  X

4 yrs.

Start Unit               5000/4 yrs.                X

Flap Position

Transmitter             OC                         X

Flap Position

Indicator               OC          X     X        X

FUEL SYSTEM, CHAPTER 28  OC          X     X        X

Fuel Pump                3200              X        X

Cock Actuator - LP Cock

Pre Saunders Mod. 23    1 yr.                      X

Post Saunders Mod. 23   2 yrs.                     X

Fuel Tank Contents       OC          X     X        X

HYDRAULIC POWER,

CHAPTER 29               OC          X     X        X

Flow Indicator Valve     2500/6 yrs.                X

Venting Valve Assembly   6 yrs.                     X

Venting Valve            6 yrs.                     X

Relief Valve             6 yrs.                     X

Cut-Out Valve            6000/6 yrs.                X

Non Return Valves        6 yrs.                     X

Relief Valve             6 yrs.                     X

Shut Off Valve           OC          X     X        X    FC at EC

Effective date ____________________

Page 5 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HAWKER SIDDELEY 748 SERIES 2A

OVERHAUL    PRE-  INSPECTION AND CHECK

HOURS/YRS.  FLT.  PERIODS

CHECK A  PERIODS OTHER

HYDRAULIC POWER,

CHAPTER 29 (Cont'd)

Hydraulic Pump           5000/6 yrs.       X        X

Pressure Release Valve   6 yrs.                     X

Relief Valve             6 yrs.                     X

Hydraulic Accumulator    6 yrs.                     X

Accumulator Air Bottle   5 yrs.                     X

Hand Pump                6 yrs.                     X

HP/LP Valve              OC

(Starboard wing torsion box)                       X    FC at EC

Hydraulic and Brake Accumulator

Pressure Indicators     OC          X     X        X

ICE AND RAIN PROTECTION

CHAPTER 30               OC          X     X        X

De-icing Timer           6000/6 yrs.                X

Disbribution Valves      7000/6 yrs.                X

Non Return Valves        7000/6 yrs.                X

Regulator Valve          7000/6 yrs.                X

Relief Valves            7000/6 yrs.                X

De-icing Timer           3000                       X

Pump Unit                10,000            X        X

INSTRUMENTS, CHAPTER 31  OC          X     X        X

To be determined by

assigned inspector.

Flight Data Recorder     2000 hrs.   X     X        X

Fatigue Meter            10,000 counts              X

on any one counter.

Pre Mod Z107 or

CN 4233, 30,000

counts Post Mod/2 yrs.

Flight Clock             OC          X     X        X

LANDING GEAR, CHAPTER 32 OC          X     X        X

Selector Valves          6 yrs.                     X

Non Return Valves        6 yrs.                     X

Footmotor                12,000                     X

Brake Control Valve      12,000                     X

Accumulator              10,000      X     X        X

Reducing Valve           12,000                     X

Effective date ____________________

Page 6 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HAWKER SIDDELEY 748 SERIES 2A

OVERHAUL    PRE-  INSPECTION AND CHECK

HOURS/YRS.  FLT.  PERIODS

CHECK A  PERIODS OTHER

LANDING GEAR, CHAPTER 32

(Cont'd)

Pressure Relay           12,000                     X

Steering Selector Valve  10,000 Ldgs.               X

Steering Control Valve   10,000 Ldgs.               X

Steering Jack            10,000 Ldgs.               X

Double Relief Valve      10,000 Ldgs.               X

Nose Down Lock           10,000 Ldgs.      X        X

Main Down Lock           10,000 Ldgs.      X        X

Restrictors              10,000 Ldgs.               X

Up Lock Jack             10,000 Ldgs.      X        X

Nose Down Lock Jack      10,000 Ldgs.               X

Main Down Lock Jack      10,000 Ldgs.               X

Nose Jack                10,000 Ldgs.               X

Main Jack                10,000 Ldgs.               X

Up Lock Jack             10,000 Ldgs.      X        X

Modulator                6000 Ldgs.                 X

Main Landing Gear Leg    10,000      X     X        X

Ldgs.

Cross Beam and Radius

Rod                     10,000 Ldgs.      X        X

Up Locks                 10,000 Ldgs.               X

Nose Landing Gear Leg    10,000 Ldgs.X     X        X

Steering Selector Valve  10,000 Ldgs.               X

Maxarets

Pre Mod 725             3000 Ldgs.                 X

Post Mod 725            OC                         X

LIGHTS, CHAPTER 33       OC          X     X        X

Emergency Lights         OC          X     X        X

NAVIGATION, CHAPTER 34   OC          X     X        X

To be determined by an

assigned inspector.

Lift Transducer          10,000/5 yrs.              X

Signal Summing Unit      5000                       X

Control shaker           5000                       X

Flap Potentiometer       15,000/5 yrs.              X

Artificial Horizon       1500        X     X        X

Controller               3 yrs.                     X

Airspeed Indicator       OC                X        X    *(6000)

Altimeter LH             OC          X     X        X    *(4000)

Altimeter RH             OC          X     X        X    *(4000)

Altitude Alerting Unit   OC                         X    *(6000)

Rate of Climb Indicator  OC          X     X        X    *(6000)

Turn and Slip Indicator  OC                X        X    *(3000)

Compass Type E2B         OC                         X

Effective date _______________________

Page 7 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HAWKER SIDDELEY 748 SERIES 2A

OVERHAUL    PRE-  INSPECTION AND CHECK

HOURS/YRS.  FLT.  PERIODS

CHECK A  PERIODS OTHER

OXYGEN SYSTEM,

CHAPTER 35               OC          X     X        X

Oxygen Cylinder        **5 yrs.      X     X        X

(Hyd or retire

appropriate for

bottle used)

Portable Oxygen Sets   **5 yrs.      X     X        X

(Hyd or retire

appropriate for

bottle used)

Mask                     5 yrs.                     X

DOORS, CHAPTER 52        OC          X     X        X

Airstairs                4000/2 yrs. X     X        X

Selector Valve           10,000 Ldgs.      X        X

Inspect areas in

accordance with Hawker

Siddeley HS-748 Series

2A Maintenance Manual.

FUSELAGE, CHAPTER 53     OC          X     X        X

Inspect areas in

accordance with Hawker

Siddeley HS-748 Series

2A Maintenance Manual.

NACELLES, CHAPTER 54     OC          X     X        X

Inspect areas in

accordance with Hawker

Siddeley HS-748 Series

2A Maintenance Manual.

STABILIZERS, CHAPTER 55  OC          X     X        X

Inspect areas in

accordance with Hawker

Siddeley HS-748 Series

2A Maintenance Manual.

WINDOWS, CHAPTER 56      OC          X     X        X

Inspect areas in

accordance with Hawker

Siddeley HS-748 Series

2A Maintenance Manual.

WINGS, CHAPTER 57        OC          X     X        X

Inspect areas in

accordance with Hawker

Siddeley HS-748 Series

2A Maintenance Manual.

Effective date ____________________

Page 8 of 9

OPERATIONS SPECIFICATIONS,

AIRCRAFT MAINTENANCE

HAWKER SIDDELEY 748 SERIES 2A

OVERHAUL    PRE-  INSPECTION AND CHECK

HOURS/YRS.  FLT.  PERIODS

CHECK A  PERIODS OTHER

PROPELLERS, CHAPTER 61   OC          X     X        X

Propeller Control Unit   3000/3yrs.  X     X        X    Refer to

Feathering Pump Unit     3000/3 yrs. X     X        X    Dowty

Feathering Pump Motor    3000                       X    Rotol

Propeller                3000/3 yrs. X     X        X    Service

Synchronising Alternator 3000/3 yrs.                X    Bulletin

Synchronising Corrector  3000/3 yrs.                X  61-519-11

Low Torque Switch        EO                         X

Propeller Brake Valve    12,000                     X

Non Return Valve         6 yrs.                     X

ENGINE, CHAPTER 72       OC          X     X        X

Engine                   Overhaul life to be in accordance with

Rolls Royce Service Bulletin Da 70-8.

Intake Heater Pad        EO          X     X        X

ENGINE FUEL AND CONTROL,

CHAPTER 73               OC          X     X        X

Fuel Flow Indicator      5000        X     X        X

Fuel Flow Computer       5000                       X

Fuel Flow Transmitters   3000                       X

Fuel Datum Position

Indicator               OC                         X

Fuel Datum Transmitter   OC                         X

Fuel Low Pressure Switch OC                         X    *(6000)

ENGINE AIR, CHAPTER 75   OC          X     X        X

Fuel Heater Valve        EO                         X

ENGINE CONTROL,

CHAPTER 76               OC          X     X        X

Fuel Datum Actuators     4500                       X

Cables                   OC                         X Refer to

life

limits

section

of

Maintenance

Schedule.

ENGINE INDICATING,

CHAPTER 77               OC          X     X        X

R.P.M. Generator         EO                         X

Torque Pressure

Transmitter             EO                         X

Thermocouples            EO                         X

R.P.M. Indicators        OC                         X    *(5000)

R.P.M. Generators        OC                         X    *(5000)

Effective date ____________________

Page 9 of 9

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

HAWKER SIDDELEY 748 SERIES 2A

OVERHAUL    PRE-  INSPECTION AND CHECK

HOURS/YRS.  FLT.  PERIODS

CHECK A  PERIODS OTHER

ENGINE INDICATING,

CHAPTER 77 (Cont'd)

Oil Pressure and

Temperature Indicator   OC                         X    *(6000)

Torque Pressure

Indicator               OC                         X

Torque Pressure

Transmitter             OC                         X

ENGINE OIL, CHAPTER 79   OC          X     X        X

Pressure Transmitter     EO                         X

Oil Pressure Switch      EO                         X

Oil Pressure Transmitter OC                         X

Low Oil Pressure Switch  OC                         X

STARTING, CHAPTER 80     OC          X     X        X

Starter, Motor           4 yrs/EO                   X

WATER INJECTION,

CHAPTER 82               OC          X     X        X

Water Methanol Pump      3200                       X

Water Methanol           OC          X     X        X

Indicators

Water Methanol

Transmitters            OC                         X

ACCESSORY GEARBOX,

CHAPTER 83               OC          X     X        X

Gearbox                  3000/3 yrs.       X        X  Refer to

Dowty

Rotol

Service

Bulletin

83-362-11

Gearbox Drive Shaft      3000/3 yrs.       X        X  Never

exceed

50 Hr

Lub.

Effective date ____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 41.  OPERATIONS SPECIFICATIONS, AIRCRAFT MAINTENANCE -

FAN JET FALCON-10

Form Approved.

UNITED STATES OF AMERICA    OMB No. 04-R0075

DEPARTMENT OF TRANSPORTATION

FEDERAL AVIATION ADMINISTRATION

WASHINGTON

PART D                                          Page 1 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

FAN JET FALCON-10

Aircraft shall not be utilized in air carrier or commercial

operations unless:

a.   The aircraft and its component parts, accessories, and

appliances are maintained in an airworthy condition in

accordance with the schedule of maintenance and inspection

functions and procedures set forth in the operator's

maintenance manual.

b.   OC "On Condition" items will be maintained in continuous

airworthiness condition by periodic and progressive

inspections, checks, services, repair, and/or preventive

maintenance and shall be appropriately described in the

operator's maintenance manual.

c.   Parts or subcomponents not listed below will be checked,

inspected, and/or overhauled at the same time limits

specified for the component or accessory to which such parts

or subcomponents are related.

Abbreviations used in the FAN JET FALCON maintenance

specifications are defined as follows:

FC - Indicates "Functional Check"

IC - Indicates "Inspection Check"

EO - Indicates "Engine Overhaul"

EC - Indicates "Engine Change"

OC - Indicates "On Condition"

HYD - Indicates "Hydrostatic Test"

CAL - Indicates "Calibration"

OP - Indicates "Operational Check"

S - Indicates "Servicing"

Inspection, replacement, and/or overhaul of fatigue critical

parts having service life limits will be accomplished as listed,

and in accordance with the S.G.A.C. - Approved Flight Manuals for

Fan Jet Falcon-10.

Preflight Inspection

To be accomplished each service calendar day.

Inspection "A" Period

To be accomplished at intervals not to exceed 150 hours time in

service or six months, whichever occurs first.

Inspection "B" Period

To be accomplished at intervals not to exceed 1000 hours time in

service or twelve months, whichever occurs first.

Effective date ____________________

Page 2 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - GENERAL

FAN JET FALCON-10

Inspection "C" Period

To be accomplished at intervals not to exceed 2,800 hours time in

service or four years, whichever occurs first.

Inspection "2C" Period

To be accomplished at intervals not to exceed 5,600 hours time in

service or eight years, whichever occurs first.

Special Inspections

The frequency and procedure for performing special inspections

will be accomplished as specified in the operator's maintenance

manual.

Overhaul and inspection/check period time limitations specified

in hours and calendar time are maximum limits of whichever occurs

first.

**  Inspections, hydrostatic test, and life limits will be

accomplished as set forth in Part 173, Chapter 1, Subtitle B of

CFR 49 currently in effect."

* NOTE (1) To be discarded.

* NOTE (2) On coupling unit G.

* NOTE (3) For servicing of extinguisher bottles, see CFR 49,

Part 173.34(e).

* NOTE (4) For servicing of extinguisher, see CFR 49, Part

173.34(e) 11, 14, and 15.

* NOTE (5) See GARRETT maintenance manual.

* NOTE (6) Included in SECAN nozzle assembly.

* NOTE (7) For servicing of oxygen cylinders, see CFR 49, Part

173.34(e) 13.

Page 3 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAN JET FALCON-10

OVERHAUL    INSPECTION AND CHECK PERIOD

HOURS/YRS.    A   B   C  2C   OTHER

AIR CONDITIONING,

CHAPTER 21               OC            X   X   X  X

Pressure reducing valve  OC                X   X  X    FC

Replacement of

diaphragm               2800/4 yrs.

Air conditioning

electrovalve            2800 hrs.         X   X  X

Replacement of brushes  1400 hrs.                     I/C, OP

Pressurization

regulating valves       2800/4 yrs.       X   X  X

Check of removed

diaphragm               2000/2 yrs.                   I/C

Safety valve             2800/4 yrs.       X   X  X

Check of removed

diaphragm               2000/2 yrs.                   I/C

Altitude pressure switch OC                X   X  X

Calibration             2800/4 yrs.                   CAL

Freon compressor motor   5600              X   X  X

Check of brushes        1000/1 yr.                    I/C, OP

Blower                   OC                X   X  X   *NOTE (6)

Replacement of brushes  5600/4 yrs.                   I/C, OP

Freon heat-exchanger

blower                  OC                X   X  X

Replacement of brushes  1000/1 yr.                    OP

Replacement of ball

bearings                2800/4 yrs.                   OP

Temperature regulating

valve                   OC                X   X  X

Replacement of brushes; 2800/4 yrs.                   I/C, OP

check of actuator

condition.

AUTO PILOT, CHAPTER 22   OC            X   X   X  X

To be determined by

assigned inspector.

COMMUNICATIONS,

CHAPTER 23               OC            X   X   X  X

To be determined by

assigned inspector.

Effective date ____________________

Page 4 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAN JET FALCON-10

OVERHAUL    INSPECTION AND CHECK PERIOD

HOURS/YRS.    A   B   C  2C   OTHER

ELECTRICAL POWER,

CHAPTER 24               OC            X   X   X  X

Battery                  OC            X   X   X  X

Removal for servicing   2 mos.                        S

Starter-generator        1500 hrs.         X   X  X

Check of brush wear      300 hrs.                     I/C, OP

and slip ring condition

Battery Blower           OC            X   X   X  X

Check of brushes        5600/8 yrs.                   I/C, OP

EQUIPMENT FURNISHINGS,

CHAPTER 25               OC            X   X   X  X

To be determined by

assigned inspector.

Shoulder Harness &

Harness Reels           OC                X   X  X

FIRE PROTECTION,

CHAPTER 26               OC            X   X   X  X

Freon extinguisher

bottle                **5 yrs.            X   X  X    * NOTE (3)

Weighing                1 yr.             X   X  X    I/C

Replacement of squibs   2 yrs.            X   X  X    I/C

CO2 extinguisher       **5 yrs.            X   X  X    * NOTE (4)

Weighing                6 mos.        X   X   X  X    I/C

FLIGHT CONTROLS,

CHAPTER 27               OC            X   X   X  X

Elevator servo-control   8 yrs.                X  X

Check of travel speed                                 FC/S

and check for leakage                                 2800/4 yrs

on stop;

Lubrication of bearings

Rudder servo-control     8 yrs.                X  X

Check of travel speed                                 FC/S

and check for leakage                                 2800/4 yrs

on stop;

Lubrication of bearings

Effective date ____________________

Page 5 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAN JET FALCON-10

OVERHAUL    INSPECTION AND CHECK PERIOD

HOURS/YRS.    A   B   C  2C   OTHER

FLIGHT CONTROLS,

CHAPTER 27 (Cont'd)

Aileron servo-control    8 yrs.                X  X

RH side

LH side

Check of travel speed                                FC/S

and check for leakage                                2800/4 yrs.

on stop;

Lubrication of bearings.

Trim jack (rudder and

aileron)                10 yrs.               X  X

Check of axial clearance,                            FC

travel and electric                                  2800/4 yrs.

motor (brushes, insulation)

Trim control box         10 yrs.           X   X  X   FC

1000/1 yr.

Main AFS                 OC                X   X  X

Internal lubrication                                 FC/S

and check of radial                                  2800/4 yrs.

clearance.

Secondary AFS (aileron)  10 yrs.           X   X  X   I/C, S

2800/4 yrs.

AMEDEE COUPLING          OC            X   X   X  X

Measurement of gear                                  FC, S

teeth meshing play;                                  2800/4 yrs.

Lubrication

Pressure Relief Valves  8 yrs.            X   X  X   FC,

1000/1 yr.

Anti-gust valve          8 yrs.        X   X   X  X   FC,

150

Main AFS                 OC                X   X  X

Internal lubrication                                 FC, S

and check of radial                                  2800/4 yrs.

clearance.

Secondary AFS (rudder)   OC                X   X  X

Internal lubrication                                 FC, S

and check of radial                                  2800/4 yrs.

clearance.

Main AFS                 OC                X   X  X

Internal lubrication                                 FC, S

and check of radial                                  2800/4 yrs.

clearance.

Effective date ____________________

Page 6 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAN JET FALCON-10

OVERHAUL    INSPECTION AND CHECK PERIOD

HOURS/YRS.    A   B   C  2C   OTHER

FLIGHT CONTROLS,

CHAPTER 27 (Cont'd)

Rudder Linear ARTHUR

Jack                    8 yrs.            X   X  X   FC, S

1000/1 yr.

Secondary AFS (elevator) 10 yrs.           X   X  X   I/C, S

2800/4 yrs.

Electrical ARTHUR Jack   3000 hrs.     X   X   X  X   OP

Check of motor (brushes,                             2800/4 yrs.

insulation, motor stop

overrun)

Electrical stabilizer

jack                    3000 hrs.     X   X   X  X   OP

Check of motor (brushes,                             2800/4 yrs.

insulation)

Potentiometer box        10 yrs.           X   X  X   FC

1000/1 yr.

Airbrake jack            8 yrs.            X   X  X   FC

1000/1 yr.

Airbrake distributor     8 yrs.            X   X  X   FC

1000/1 yr.

Microswitch box          2800 hrs.     X   X   X  X   FC

1000/1 yr.

Switches Stabilizer Trim OC            X   X   X  X   FC, S

1000/1 yr.

Reduction gear motor     2400 hrs.         X   X  X   FC

1000/1 yr.

Screw jacks              2400 hrs.         X   X  X   FC

LH outboard jack                                     1000/1 yr.

RH outboard jack

Inboard jack

Inboard jack

Slat distributor         8 yrs.            X   X  X    FC

1000/1 yr

Effective date ____________________

Page 7 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAN JET FALCON-10

OVERHAUL    INSPECTION AND CHECK PERIOD

HOURS/YRS.    A   B   C  2C   OTHER

FLIGHT CONTROLS,

CHAPTER 27 (Cont'd)

Stand-by slat

distributor             8 yrs.            X   X  X   FC

1000/1 yr.

Slat jacks               8 yrs.            X   X  X   FC

1000/1 yr.

Slat jacks               8 yrs.            X   X  X   FC

1000/1 yr.

Slat jacks               8 yrs.            X   X  X   FC

1000/1 yr.

Stand-by outboard slat

jacks                   8 yrs.    @      X   X  X   FC

1000/1 yr.

Yaw damper jack          8 yrs.            X   X  X   FC

1000/1 yr.

FUEL, CHAPTER 28         OC            X   X   X  X

Booster pump             OC                X   X  X   FC

2800/4 yrs.

Replacement of brushes  1200 hrs.                    OP

Replacement of bearings 2400 hrs.                    OP

LP crossfeed valve

actuator                OC                X   X  X   *NOTE (2)

Check of brushes and                                 OP,

slip ring                                            2800/4 yrs.

Pressure switch          OC                X   X  X

Check of calibration                                 CAL.

2800/4 yrs.

Indicator                2800 hrs.         X   X  X   OP

1000/1 yr.

HYDRAULIC POWER,

CHAPTER 29               OC            X   X   X  X

Pressurization reducing

valves                  OC                X   X  X

Replacement of diaphragm                             FC,

2800/4 yrs.

Effective date ____________________

Page 8 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAN JET FALCON-10

OVERHAUL    INSPECTION AND CHECK PERIOD

HOURS/YRS.    A   B   C  2C   OTHER

HYDRAULIC POWER,

CHAPTER 29 (Cont'd)

Pressure switch          OC                X   X  X

Check of calibration                                 CAL.

2800/4 yrs.

Hydraulic pump           2400 hrs.         X   X  X   OP

1000/1 yr.

Electropump              4800 hrs.         X   X  X   OP

1000/1 yr.

Pressure switch          OC                X   X  X   CAL.

2800/4 yrs.

Pressure transmitter     OC                X   X  X   CAL.

2800/4 yrs.

ICE AND RAIN PROTECTION,

CHAPTER 30               OC            X   X   X  X

Wing anti-icing air

valve                   2800 hrs.     X   X   X  X   OP,

1000/1 yr.

Windshield wiper         OC            X   X   X  X   FC,

1000/1 yr.

Servicing                                            S,

5600/8 yrs.

Anti-icing valve         2800 hrs.         X   X  X   OP,

1000/1 yr.

INSTRUMENTS, CHAPTER 31  OC            X   X   X  X

To be determined by

assigned inspector.

LANDING GEAR, CHAPTER 32 OC            X   X   X  X

Pressure switch          OC                X   X  X   CAL.

2800/4 yrs.

Main gear struts         5600 hrs.     X   X   X  X

Effective date ________________

Page 9 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAN JET FALCON-10

OVERHAUL    INSPECTION AND CHECK PERIOD

HOURS/YRS.    A   B   C  2C   OTHER

LANDING GEAR,

CHAPTER 32 (Cont'd)

Ball joint bearings      5600 hrs.     X   X   X  X

Front

Rear

Main shock strut         5600 hrs.     X   X   X  X

Actuating cylinder

assembly                 5600 hrs.     X   X   X  X

LH side

RH side

Nose gear                5600 hrs.     X   X   X  X

Actuating cylinder

assembly                 5600 hrs.     X   X   X  X

Pressure reducing

solenoid valve           4800 hrs.         X   X  X

Main gear wheel          OC            X   X   X  X

Visual inspection,                                    At each

lubrication of bearings.                              wheel

Eddy current or ultra                                 change

sonic inspection.                                     1500 hrs.,

then at

each tire

change.

Nose gear wheel          OC            X   X   X  X

Visual inspection,                                   At each

lubrication of bearings.                             wheel

Eddy current or ultra                                change

sonic inspection.                                    2800 hrs.,

then at

each tire

change.

Servo-valve              3600 hrs.         X   X  X   FC

1000/1 yr.

Anti-skid speed sensor   OC                X   X  X   CAL.,

2800/4 yrs.

LIGHTS, CHAPTER 33       OC            X   X   X  X

Anti-collision light     OC                X   X  X

Check of motor                                       OP,

2800/4 yrs.

Effective date ____________________

Page 10 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAN JET FALCON-10

OVERHAUL    INSPECTION AND CHECK PERIOD

HOURS/YRS.    A   B   C  2C   OTHER

NAVIGATION, CHAPTER 34   OC            X   X   X  X

To be determined by

assigned inspector.

Encoder altimeter        OC                X   X  X   CAL/2 yrs.

Altimeter                OC                X   X  X   CAL/2 yrs.

PER IDC

Overhaul

Manual.

Mach Meter               OC                X   X  X   CAL/2 yrs.

PER IDC

Overhaul

Manual.

Overspeed warning device OC                X   X  X   CAL/2 yrs

OXYGEN, CHAPTER 35       OC            X   X   X  X

Oxygen cylinder        **3 yrs.        X   X   X  X   S

Service

life

15 yrs

* NOTE (7)

Pressure reducing valve  OC                X   X  X   CAL.,

2800/4 yrs.

Altitude sensitive valve 4 yrs.            X   X  X   FC,

1000/1 yr.

PNEUMATIC, CHAPTER 36    OC            X   X   X  X

(P2) Unit                2400 hrs.     X   X   X  X   I/C,

150/6 mos.

HP isolation pneumatic

valve                   2800 hrs.     X   X   X  X   I/C,

150/6 mos.

DOORS, CHAPTER 52        OC            X   X   X  X

Inspect areas in

accordance with Falcon-10

Maintenance Manual.

Effective date ____________________

Page 11 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAN JET FALCON-10

OVERHAUL    INSPECTION AND CHECK PERIOD

HOURS/YRS.    A   B   C  2C   OTHER

FUSELAGE, CHAPTER 53     OC            X   X   X  X

Inspect areas in

accordance with Falcon-10

Maintenance Manual.

NACELLES, CHAPTER 54     OC            X   X   X  X

Inspect areas in

accordance with Falcon-10

Maintenance Manual.

STABILIZERS, CHAPTER 55  OC            X   X   X  X

Inspect areas in

accordance with Falcon-10

Maintenance Manual.

WINDOWS, CHAPTER 56      OC            X   X   X  X

Inspect areas in

accordance with Falcon-10

Maintenance Manual.

WINGS, CHAPTER 57        OC            X   X   X  X

Inspect areas in

accordance with Falcon-10

Maintenance Manual.

ENGINE, CHAPTER 72       OC            X   X   X  X

Service, inspection and                                * NOTE (5)

overhaul life limits to

be in accordance with

Garrett Air Research

Service Bulletins

TFE731-72-3001 and

TFE-731-72-3002.

ENGINE CONTROLS,

CHAPTER 76               OC            X   X   X  X

Power control

mechanical linkage       4000 hrs.     X   X   X  X  * NOTE (1)

Scrap S,

1000/1 yr.

Effective date ____________________

Page 12 of 12

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

FAN JET FALCON-10

OVERHAUL    INSPECTION AND CHECK PERIOD

HOURS/YRS.    A   B   C  2C   OTHER

ENGINE CONTROLS,

CHAPTER 76 (Cont'd)

Power control linkage    OC            X   X   X  X   IC/S

(cable and box assembly)

LH side

RH side

Lubrication of bearings

and cable.                                           1000/1 yr.

OIL, CHAPTER 79          OC            X   X   X  X

Oil pressure switch      OC                X   X  X   CAL.

2800/4 yrs.

Effective date ____________________

----------------------------------------------------------------

----------------------------------------------------------------

FIGURE 42.  OPERATIONS SPECIFICATIONS, AIRCRAFT MAINTENANCE -

GATES LEARJET MODELS 35/36

Form Approved

UNITED STATES OF AMERICA   OMB. No. 04-R0075

DEPARTMENT OF TRANSPORTATION

FEDERAL AVIATION ADMINISTRATION

WASHINGTON

PART D                                  Preface Page 1 of 1

OPERATIONS SPECIFICATIONS

PREFACE PAGE

AIRCRAFT MAINTENANCE

ABC AIRLINES

LEAR 35/36

Irrespective of the type of operation to be conducted by ABC

Airlines, the continuous airworthiness and inspection program

limitations which are described and specified in these Operations

Specifications shall be applicable to all ABC Airlines aircraft

listed and authorized for use under Federal Aviation Regulations

Part _____.  ABC Airlines shall provide in its currently

effective Maintenance Manual a comprehensive program necessary to

fulfill the responsibility to maintain the aircraft in an

airworthy condition in accordance with the applicable Federal

Aviation Regulations and standards prescribed and approved by the

Administrator.

Aircraft shall not be utilized in air carrier _____ operations

unless:

a.   The aircraft and its component parts, accessories, and

appliances are maintained in an airworthy condition in

accordance with the schedule of maintenance and inspection

procedures and functions set forth in the operator's

maintenance manual.

b.   OC "on condition" items will be maintained in continuous

airworthiness condition by periodic and progressive

inspections, checks, services, repair, and/or preventive

maintenance and shall be appropriately described in the

operator's maintenance manual.

c.   Parts or subcomponents, not listed below, will be checked,

inspected, and/or overhauled at the same time limits

specified for the component or accessory to which such parts

or subcomponents are related.

AVIONICS SYSTEMS.  The term "system" means all those

interdependent subassemblies, component parts, etc., necessary

for the proper functioning of the system as a whole.  The term

"Bench Check" includes calibration, if necessary, to return the

unit to service in accordance with the manufacturer's procedures.

Abbreviations used in the maintenance specifications are defined

as follows:

FC - Indicates "Functional Check"

BC - Indicates "Bench Check"

EO - Indicates "Engine Overhaul"

EC - Indicates "Engine Change"

OC - Indicates "On Condition"

HYD - Indicates "Hydrostatic Test"

C - Indicates "Calibration"

SI - Indicates "Special Inspections"

ESV - Indicates "Engine Shop Visit"

HR - Indicates "Hours"

MO - indicates "Months"

YRS - Indicates "Years"

Effective date ____________________

Page 1 of 13

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ABC AIRLINES

LEAR 35/36

Maintenance and inspections shall be accomplished in accordance

with the applicable procedures as listed in ABC Airlines

Maintenance Manual.

#1 insp.  shall be accomplished prior to the originating flight

from a maintenance base each day.  In the event the aircraft is

away from a station where qualified maintenance personnel are not

available, the #1 inspection shall be accomplished prior to

exceeding 20 hours time in service or seven days, whichever comes

first.

#2 insp.  shall be accomplished at basic intervals of 75 hours

times in service and shall be repeated each 75 hours time in

service after a #3 or #4 inspection has been accomplished.

#3 insp.  shall be accomplished at intervals not to exceed 150

hours time in service.

#4 insp.  shall be accomplished at intervals not to exceed 300

hours time in service.

Te inspection cycle #2, #3, #2, #4, #2, #3, etc., shall be

repeated in this sequence.

In addition to the #1, #2, #3, #4 inspections there are (other)

inspections required.  These inspections are explained in the

notes below or are self-explanatory.

Overhaul times listed in hours, years and cycles are maximum

limits, whichever comes first.  Time replacement items must be

replaced where "replace" is indicated.

ESV - Engine Shop Visit.  The engine shop visit shall be

accomplished at five hundred hours (500) time in service in

accordance with Airesearch TFE 731-72 maintenance manual.

NOTE 1:   Replace engine elements having service life limits as

established in Airesearch Service Bulletin TFE 731-72-3001,

Revision #4, dated 2-28-75 and AD 75-05-12 pertaining to

Airesearch Manufacturing Company.

NOTE 2:   Replace structural components at replacement lives

shown in FAA approved Learjet Report 26-S47.  These replacement

lives are also shown in the Learjet Model 35 Maintenance Manual

(ref. Type Data Sheet No. ATOCE under "Equipment").

Effective date  _______________________

Page 2 of 13

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ABC AIRLINES

LEAR 35/36

OVERHAUL  INSPECTION AND CHECK

HOURS OR  PERIOD

YEARS     #1 #2 #3 #4 OTHER

Chapter 21 - Air Conditioning

Air Conditioning System            OC                  X

Valve, Bleed Air Check             6,000  10           X

Valve, Flow Control                4,000   4           X

Valve, Hot Air Bypass              6,000  10           X

Heat Exchanger                     6,000  10           X

Valve, Ram Air Check               6,000  10           X

Indicator, Temp Control            6,000  10           X

Heater, Cabin Auxiliary            6,000  10           X

Selector, Temperature              6,000  10           X

Unit, Temperature Control          OC                  X

Sensor, Cabin Temperature          OC                  X

Thermostat, Hi Limit               OC                  X

Sensor, Duct Temperature           OC                  X

Sensor, Cabin Skin Temperature     OC                  X

Compressor, Freon                  3,600   3     X  X  X

Motor, Compressor                  6,000  10     X  X  X

Condensor                         10,000  10           X

Dehydrator                        10,000  10           X

Switch, Refrig. Pressure           6,000  10           X

Evaporator                        10,000  10           X

Blower, Cabin                      2,400   4           X

Fan, Cockpit Cooling               2,400   4           X

Valve, Expansion                   6,000   8           X

Valve, Cabin Air Exhaust           4,000   4           X

Valve, Diff Press. Relief          6,000  10           X

Pump, Pressurization Jet           6,000  10           X

Module, Pressurization             6,000  10             FC @

1200 hr

Limiter, Cabin Altitude            OC                  X

Valve, Cabin Safety                4,000   4           X

Aneroid, Cabin Press. Warning      OC                  X FC @

1200 hr

Aneroid, Cabin Pressurization      OC                  X FC @

1200 hr

Indicator, Cabin Temperature       OC                  X

Effective date _______________________

Page 3 of 13

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ABC AIRLINES

LEAR 35/36

OVERHAUL  INSPECTION AND CHECK

HOURS OR  PERIOD

YEARS     #1 #2 #3 #4 OTHER

Chapter 22 - Auto Pilot

Auto Pilot System                  OC                  X

Controller, Autopilot              OC                  X

Computer/Controller, Yaw           OC                  X

Sensor, Air Data                   OC                  X

Computer, Autopilot                OC                  X BC @ 900

hr

Accelerator, Lateral               OC                  X

Indicator, Yaw Damper              OC                  X

Capstan, Servos                    OC                  X SI @ 600

hr

Actuator, Servo                    OC                  X SI @ 600

hr

Computer, Mach Trim                OC                  X

Followup, Mach Trim                OC                  X

Rate Gyro                          OC                  X

Box, Flt. Direct Interface         OC                  X

Chapter 23- Communications         OC         X  X  X  X

To be determined by assigned

inspector.

Effective date _______________________

Page 4 of 13

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ABC AIRLINES

LEAR 35/36

OVERHAUL  INSPECTION AND CHECK

HOURS OR  PERIOD

YEARS     #1 #2 #3 #4 OTHER

Chapter 24 - Electrical Power

Electrical Power System            OC         X  X  X  X

Inverter, Primary                  OC         X  X  X  X

Sensor, AC Overload                OC            X  X  X

Relay, AC Power                    OC            X  X  X

Autotransformer                    OC                  X

Inverter, Secondary                OC         X  X  X  X

Box, AC Parallel Control           OC                  X

Voltmeter, AC                      OC         X  X  X  X

Generator                          OC            X  X  X

Regulator, Gen. Voltage            OC            X  X  X

Sensor, Gen. Overload              OC                  X

Relay, Gen. Feeder Bus             OC                  X

Ammeter, Generator                 OC            X  X  X

Box, Generator Control             OC                  X

Voltmeter, DC                      OC         X  X  X  X

Battery                            OC         X  X  X  X

Relay, Battery                     OC                  X

Switch, Batt. Hi Lim. Temp.        OC            X  X  X

Sensor, Batt. Temp.                OC            X  X  X

Indicator, Battery Temp.           OC         X  X  X  X

Battery, Emergency Light           OC         X  X  X  X

Receptacle, External Power         OC            X  X  X

Relay, External Power              OC            X  X  X

Chapter 25 - Equipment/

Furnishings

Equipment & Furnishings            OC            X  X  X

Seat, Crew                         OC            X  X  X

Seat, Passenger                    OC            X  X  X

Belt                               OC            X  X  X

Harness/Reel Shlder                OC            X  X  X

Life Vests                         24 mo.        X  X  X

Drag Chute                         OC                  X

Effective date _______________________

Page 5 of 13

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ABC AIRLINES

LEAR 35/36

OVERHAUL  INSPECTION AND CHECK

HOURS OR  PERIOD

YEARS     #1 #2 #3 #4 OTHER

Chapter 26 - Fire Protection

Fire Protection System             OC         X  X  X  X FC @ 600

hr

Sphere, Fire Extinguisher      5 yrs. **      X  X  X  X

(ICC/DOT - 4DA)

Cartridges, Explosive, Fire    3 yrs.                  X

Exting.

Valve, Fire Ext. 2 Way Ck          OC            X  X  X FC @ 600

hr

Element, Sensor                    OC         X  X  X  X

Control Unit, Fire Detector        OC         X  X  X  X

Engine, Fire Detector System       OC         X  X  X  X

Extinguisher, Portable             OC            X  X  X

(6BC Dry Chemical)

** Inspections, Hydrostatic Test, and Life Limits will be

accomplished as set forth in Part 173, Chapter 1, Subtitle B of

CFR 49 currently in effect.

Chapter 27 - Flight Controls

Flight Controls                    OC            X  X  X

Aileron                          NOTE 2       X  X  X  X SI @ 600

hr

Drive Assy, Aileron              NOTE 2          X  X  X

Bolt, Ail. Drive Yoke            NOTE 2          X  X  X

Bolt, Ail. Hinge                 NOTE 2          X  X  X

Tab, Aileron Trim                NOTE 2       X  X  X  X

Actuator, Aileron Trim Tab         OC         X  X  X  X FC @ 600

hr

Potentiometer, Ail. Trim           OC            X  X  X FC @ 600

hr

Tab, Aileron Balance             NOTE 2       X  X  X  X

Wheel, Control                   20,000             X  X

Column, Control                  20,000             X  X

Cables, Flight Control           NOTE 2          X  X  X

Indicator, Ail. Trim Pos.          OC            X  X  X FC @ 600

hr

Rudder                           NOTE 2          X  X  X SI @ 600

hr

Hinges, Rudder                   NOTE 2          X  X  X

Supports, Rudder                 NOTE 2          X  X  X

Sector, Rudder Servo               OC            X  X  X

Tab, Rudder                      NOTE 2       X  X  X  X

Actuator, Rudder Trim Tab          OC         X  X  X  X FC @

1200 hr

Potentiometer, Rudder Trim         OC            X  X  X FC @

1200 hr

Indicator, Rudder Trim Pos.        OC         X  X  X  X FC @

1200 hr

Effective date _______________________

Page 6 of 13

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ABC AIRLINES

LEAR 35/36

OVERHAUL  INSPECTION AND CHECK

HOURS OR  PERIOD

YEARS     #1 #2 #3 #4 OTHER

Chapter 27 - continued

Elevator                         NOTE 2          X  X  X SI @ 600

hr

Downspring Assy, Elevator          OC            X  X  X SI @ 600

hr

Stabilizer, Horizontal           NOTE 2          X  X  X

Hinge Pin, Horizontal            NOTE 2                  SI @ 600

Stabilizer                                             hr

Actuator, Horizontal               OC                    SI @ 600

Stabilizer                                             hr

Bolt, Stabilizer Actuator        NOTE 2                  SI @ 600

Attach                                                 hr

Indicator, Horizontal              OC         X  X  X  X FC @ 600

Stabilizer Posi                                        hr

Flap Assembly                    NOTE 2       X  X  X  X

Actuator, Flap                     OC            X  X  X

Support, Flap                    NOTE 2                X

Track, Flap                      NOTE 2                X

Bushings, Flap Roller             1,200                X

Valve, Flap Control                OC                  X

Bolts, Wing Flap Selector        NOTE 2                X

Restrictor, Flap                   OC                  X

Valve, Flap Press, Relief          OC            X  X  X

Indicator, Flap Position           OC         X  X  X  X

Potentiometer, Flap Position       OC            X  X  X

Switch, Flap Airspeed              OC                  X

Spoiler, Assembly                 3,600       X  X  X  X

Actuator Fitting & Bolts         NOTE 2                X

Spoiler

Arm, Spoiler Actuator            NOTE 2          X  X  X

Brackets, Spoiler                 2,400          X  X  X

1/4 Bolt, Spoiler Act Arm        NOTE 2                X

5/16 Bolt, Spoiler Act Arm       NOTE 2                X

Switch, Spoiler Down/Lock          OC                  X

1/4 Bolt, Spoiler Hinge          NOTE 2                X

5/16 Bolt, Spoiler Hinge         NOTE 2                X

Switch, Spoiler Limit              OC            X  X  X

Followup, Spoiler                  OC            X  X  X

Followup, Aileron Aug.-Ail.        OC            X  X  X

Valve, Spoiler Servo               OC                  X

Valve, Spoiler Control             OC                  X

Valve, Spoiler Solenoid            OC                  X

Restrictor

Computer Amp. Spoiler              OC            X  X  X

Effective date ____________________

Page 7 of 13

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ABC AIRLINES

LEAR 35/36

OVERHAUL  INSPECTION AND CHECK

HOURS OR  PERIOD

YEARS     #1 #2 #3 #4 OTHER

Chapter 27 - continued

Filter, Spoiler                      300               X

Computer/Amp. Stall Warning        OC                  X

Transducer, Angle of Attack        OC         X        X

Bias Box, Stall Warning            OC                  X

Shaker, Control Column             OC         X        X

Accelerometer, Stall Warning       OC                  X

Indicator, Angle of Attack         OC                  X

Cutout, Stall Warning Acceler.     OC                  X

Chapter 28 - Fuel

Fuel System                        OC                  X

Pump, Jet                          OC            X  X  X

Valve, Tank Vent Ck.              10,000 10            X

Valve, Tank Jettison               6,000 10              FC @600

hr

Tank, Tip                         20,000      X  X  X  X

Pump, Boost (Standby)              8,000      X  X  X  X

Switch, Wing Float                10,000 10              FC @ 600

hr

Valve, Crossflow Shutoff          10,000 10   X  X  X  X

Valve, Fuselage Transfer          10,000 10   X  X  X  X

Shutoff

Valve, Wing Press. Relief         10,000 10            X

Valve, Wing Vacuum Relief         10,000 10              FC @ 600

hr

Cell, Fuselage Fuel                6,000 10      X  X  X

Switch, Fuselage Tank Trans.       6,000 10      X  X  X

Pres.

Switch, Fuselage Tank Float       10,000 10      X  X  X

Valve, Fuel Shutoff               10,000 10   X  X  X  X

Valve, Motive Flow                10,000 10      X  X  X

PC Board, Fuel Board              10,000 10            X C @ 600

hr

Probe, Fuselage & Wing            10,000 10            X C @ 600

hr

Indicator, Fuel Quantity          10,000 10            X C @ 600

hr

Hoses, Engine Nacelle              2,400               X

Hoses, Aircraft System             6,000 10            X

Effective date ____________________

Page 8 of 13

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ABC AIRLINES

LEAR 35/36

OVERHAUL  INSPECTION AND CHECK

HOURS OR  PERIOD

YEARS     #1 #2 #3 #4 OTHER

Chapter 29 - Hydraulic Power

Hydraulic Power System             OC                  X

Reservoir, Hydraulic              20,000      X  X  X  X

Valve, Hydraulic Shutoff           6,000 10      X  X  X

Pump, Engine Hydraulic             EC                  X

Accumulator, Hydraulic            10,000 10   X  X  X  X

Valve, Engine Hydraulic            OC            X  X  X

Press. Ck.

Valve, Hydraulic Reserv.           OC            X  X  X

Press. Relief

Valve, Hydraulic System            6,000 10            X

Relief

Valve, Emergency Air               OC                    FC @ 600

hr

Indicator, Hydraulic Pressure      OC         X  X  X  X

Pump, Auxiliary Electric           OC         X  X  X  X

Regulator, Reservoir, Pressure     OC            X  X  X

Hoses, Engine Nacelle              2,400               X

Hoses, (all other except

landing gear system)             6,000         X  X  X

Chapter 30, Ice and Rain

Protection

Ice and Rain Protection            OC                  X

Regulator, Press. Anti-Ice         OC                  X

Thermostat, Wing Anti-Ice          OC                  X

Indicator, Temperature             OC                  X

Anti-Ice

Valve, Nacelle Anti-Ice            OC                  X

Shutoff

Valve, Defrost Pressure            OC                  X

Regulator

Tank, Alcohol Anti-Ice             OC            X  X  X

Pump, Motor Driven Anti-Ice        OC            X  X  X

Filter, Alcohol Anti-Ice           OC                  X

Valve, Alcohol Pressure Relief     OC                  X

Pitot/Static System Heater         OC         X  X  X  X

Chapter 31 - Instruments

Instruments System                 OC         X  X  X  X SI @ 600

hr

Clock                              OC         X  X  X  X

Unit, Aural Warning                OC            X  X  X

Flight Recorder                    2,000         X  X  X

Effective date ____________________

Page 9 of 13

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ABC AIRLINES

LEAR 35/36

OVERHAUL  INSPECTION AND CHECK

HOURS OR  PERIOD

YEARS     #1 #2 #3 #4 OTHER

Chapter 32 - Landing Gear

Landing Gear System                OC         X  X  X  X

Strut, Main Gear Shock           NOTE 2                X

Actuator, Main Gear              NOTE 2                X

Valve, Shuttle Gear Actuator       OC                    FC @ 600

hr

Actuator, Door                     OC                  X

Valve, Shuttle Gear Door           OC                  X

Arm, Main Gear Strut Torq.         OC                  X

Strut, Nose Gear                 NOTE 2          X  X  X

Actuator, Nose Gear              NOTE 2          X  X  X

Valve, Nose Gear Priority          OC                  X

Valve, Shuttle, Nose Gear          OC                    FC @ 600

hr

Actuator, Nose Gear Upltch.        OC                  X

Valve, Gear Selector               OC                  X

Valve, Gear Door Sequence          OC                  X

Valve, Emergency Air Shuttle       OC                    FC @ 600

hr

Bottle, Emergency Air

(ICC/DOT) Type D-16            3 yrs.**        X  X  X

Indicator, Emergency Air           OC         X  X  X  X

Valve, Emergency Gear Extend       OC                    FC @ 600

hr

Valve, Emerency Brake              OC                    FC @ 600

hr

Wheel, Main Gear                  2,500       X  X  X  X

Wheel, Nose                        OC         X  X  X  X

Valve, Power Brake                 OC            X  X  X

Valve, Brake Shuttle               OC                    FC @ 600

hr

Brake                              OC         X  X  X  X

Valve, Anti-Skid                   OC                  X FC @ 600

hr

Control Box, Anti-Skid             OC                  X FC @ 600

hr

Computer/Amp, Nose Steer           OC                  X

Actuator, Nose Wheel Steer        3,000          X  X  X

Servo, Nose Steering               OC                  X

Followup, Rudder Pedal             OC                  X

** Inspections, Hydrostatic Test, and Life Limits will be

accomplished as set forth in Part 173, Chapter 1, Subtitle B of

CFR 49 currently in effect.

Effective date ____________________

Page 10 of 13

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ABC AIRLINES

LEAR 35/36

OVERHAUL  INSPECTION AND CHECK

HOURS OR  PERIOD

YEARS     #1 #2 #3 #4 OTHER

Chapter 33 - Lights

Light System                       OC         X  X  X  X

Control Box, Warning Light         OC                  X

Light, Landing/Taxi                OC         X  X  X  X

Light, Strobe                      OC         X  X  X  X

Power Sup. Strobe Light            OC            X  X  X

Dim Assembly, Light                OC                  X

Transformer, Cold Cathode          OC                  X

Lights, Emergency (Interior        OC         X  X  X  X

and Exterior)

Chapter 34 - Navigation            OC         X  X  X  X

To be determined by assigned

inspector.

Effective date ____________________

Page 11 of 13

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ABC AIRLINES

LEAR 35/36

OVERHAUL  INSPECTION AND CHECK

HOURS OR  PERIOD

YEARS     #1 #2 #3 #4 OTHER

Chapter 35 - Oxygen

Oxygen System                      OC                  X NOTE 3

Detector, Flow                     OC                  X

Cylinder, Pressure Oxygen                              X

(ICC/DOT) 3AA                 5 yrs.*

Switch, Oxygen Aneroid             OC                  X

Valve, Lanyard Actuated            OC                  X

Mask, Oxygen                       OC                  X

Indicator, Oxygen Pressure         OC         X        X

Valve, Manual Aneroid Bypass       OC                  X

Valve, Oxygen Solenoid             OC                  X

Valve, Manual Pass. Oxygen         OC                  X

* Inspections, Hydrostatic Test, and Life Limits will be

accomplished as set forth in Part 173, Chapter 1, Subtitle B of

CFR 49 currently in effect.

NOTE 3:  Conduct a special functional check of the passenger

oxygen system every 2,000 to 3,000 hours by simulating a cabin

pressure of 14,000 to 15,000 feet altitude and checking the

oxygen flow at each passenger mask.

Chapter 36 - Pneumatic

Pneumatic System                   OC                  X

Valve, Shutoff/Pressure Reg.       OC                  X

Thermoswitch, Pneumatic System     OC                  X

Chapter 52 - Doors

Door, Cabin Assembly               OC            X  X  X

Actuator, Cabin Door Lock          OC            X  X  X

Door, Emergency                    OC                  X

Chapter 53 - Fuselage

Fuselage Fwd                       OC         X  X  X  X SI @ 600

hr

Cabin                              OC         X  X  X  X SI @ 600

hr

Cockpit                            OC         X  X  X  X SI @ 600

hr

Tail Cone                          OC         X  X  X  X SI @ 600

hr

Fuselage Aft                       OC         X  X  X  X SI @ 600

hr

Chapter 54 - Nacelles/Pylons

Nacelle/Pylon                      OC         X  X  X  X SI @ 600

hr

Mount, Engine Fwd & Aft          NOTE 2          X  X  X SI @ 600

hr

Mount, Bolts                     NOTE 2          X  X  X SI @ 600

hr

Effective date ____________________

Page 12 of 13

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ABC AIRLINES

LEAR 35/36

OVERHAUL  INSPECTION AND CHECK

HOURS OR  PERIOD

YEARS     #1 #2 #3 #4 OTHER

Chapter 55 - Stabilizers

Empennage                          OC         X  X  X  X

Hinge Assembly, Vertical         NOTE 2          X  X  X SI @ 600

Stabil.                                                hr

Chapter 56 - Windows

Windshield                         OC         X  X  X  X

Window, Cabin                      OC         X  X  X  X SI @NOTE

4

Chapter 57 - Wings

Wing                               OC         X  X  X  X SI @NOTE

4

Wing Structure                     OC                    SI @NOTE

4

Chapter 71 - Power Plant

Fwd. & Aft Support Shock Mounts  NOTE 2          X  X  X

and Bolts

Chapter 72 - Engine

Engine                            ESV         X  X  X  X  NOTE 1

Chapter 73 - Engine Fuel &

Control

Engine Fuel & Control System       OC            X  X  X

Control Assy. Fuel                 EC            X  X  X

Pump, Fuel                         EC            X  X  X

Valve, Flow Divider/Drain          EC            X  X  X

Cooler, Fuel/Oil Engine            EC            X  X  X

Computer, Fuel Control             OC            X  X  X

Valve, Surge Bleed                 EC            X  X  X

Valve, Solenoid Control            EC            X  X  X

Transmitter, Fuel Flow             EC            X  X  X

Indicator, Dual Fuel Flow          OC            X  X  X

Chapter 74 - Ignition

Ignition System                    OC               X  X

Ignition Unit                      OC               X  X

Plug, Ignitor                      OC                  X

NOTE 4:  The Special Inspection (SI) at 6,000 hours for systems

56 and 57 is a major inspection requiring performance in

accordance with the Gates Learjet Model 35 Maintenance Manual.

It involves demating the wing from the fuselage and includes

numerous NDT procedures.

Effective date ____________________

Page 13 of 13

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

ABC AIRLINES

LEAR 35/36

OVERHAUL  INSPECTION AND CHECK

HOURS OR  PERIOD

YEARS     #1 #2 #3 #4 OTHER

Chapter 75 - Air

Sensor, Inlet Press/Temp           EC            X  X  X

Engine

Chapter 76 - Engine Controls

Engine Control System              OC               X  X

Engine Control, Cables &           OC               X  X

Linkage

Chapter 77 - Engine Indicating

Engine Indicating System           OC            X  X  X

Transducer, Engine                 EC            X  X  X

Harness, ITT Thermocouple          EC            X  X  X

Engine

Indicator, ITT Engine              OC                  X

Indicator, N1 & N2 Engine          OC                  X

Chapter 79 - Engine Oil

Oil System                         OC            X  X  X

Tank, Oil                          EC         X  X  X  X

Valve, Pressure Breather           EC            X  X  X

Cooler, Oil                        EC               X  X

Valve, Oil Temperature             EC                  X

Switch, Oil Pressure               EC               X  X

Transmitter, Oil Pressure          OC            X  X  X

Bulb, Oil Temperature              EC               X  X

Indicator, Oil Temperature         OC         X  X  X  X

Indicator, Dual Oil Pressure       OC         X  X  X  X

Chapter 80 - Starting

Starting System                    OC               X  X

Starter, Engine                    OC               X  X

Start Timer, Resistance            OC               X  X

Assembly

Start Timer Relay                  OC               X  X

Effective date ____________________

----------------------------------------------------------------

----------------------------------------------------------------

* FIGURE 43.   OPERATIONS SPECIFICATIONS, AIRCRAFT

MAINTENANCE - SOCIETE NATIONALE

INDUSTRIELLE AEROSPATIALE (SNIAS) NORD

262A AND 262A/M-298

Form Approved.

OMB. No. 04-R0075.

UNITED STATES OF AMERICA     Preface Page

DEPARTMENT OF TRANSPORTATION   Page 1 of 3

FEDERAL AVIATION ADMINISTRATION

WASHINGTON

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - PREFACE PAGE

GENERAL

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

Irrespective of the type of operation to be conducted by (name of

operator) the continuous airworthiness and inspection program

limitations which are described and specified in these Operations

Specifications shall be applicable to all (name of operator)

aircraft listed and authorized for use under Federal Aviation

Regulations 135.2 or 121 as the case may be.

The operator shall provide in its currently effective Maintenance

Manual a comprehensive maintenance program necessary to fulfill

its responsibility to maintain the aircraft in an airworthy

condition in accordance with applicable Federal Aviation

Regulations and standards prescribed and approved by the

Administrator.

The aircraft and its component parts, accessories and appliances

shall be maintained in an airworthy condition in accordance with

the maximum time limits hereinafter set forth for the

accomplishment of the overhaul, periodic inspections and routine

checks of the aircraft and its component parts, accessories and

appliances.

"On Condition" items will be maintained in a continuous airworthy

condition by periodic and progressive inspections, checks,

services, repair and/or preventive maintenance and shall be

appropriately described in the operator's Maintenance Manual.

Parts or subcomponents not listed herein will be checked,

inspected and/or overhauled at the same time limitations

specified for the component or accessory to which such parts or

subcomponents are related or at the time period indicated for the

ATA subchapter heading.

Effective date ____________________

Preface Page

Page 2 of 3

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE--PREFACE PAGE

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

Checks, Inspections and Overhaul Time Limits

All inspections, checks and maintenance shall be accomplished in

accordance with the applicable procedures as listed in the (name

of operator) Maintenance Manual.

The following four levels of inspection are defined and detailed

in the appropriate section of the (name of operator) Maintenance

Manual.

L      =  Line Service Inspection to be performed at the

first regular maintenance facility reached during

each day the aircraft is used.

PF     =  Pre Flight Inspection to be performed at intervals

not to exceed 25 hours of aircraft time in service

or 5 calendar days.

* P    =  Periodic Inspection to be performed at intervals

not to exceed 400 hours of aircraft time in

service.

* BIP  =  Basic Inspection Period to be performed at

intervals not to exceed 4,000 hours of aircraft

time in service.

* NOTE 1: Operators having utilization of less than 1,200

hours per year may be required to institute

calendar controlled inspections in lieu of the

flight hours noted herein.

Effective date ____________________

Preface Page

Page 3 of 3

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE--PREFACE PAGE

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

Special Inspections

The frequency and procedure for performing special inspections

will be accomplished as specified in the (name of operator)

Maintenance Manual.

A double asterisk (**) indicates "Inspections, hydrostatic test,

and life limits will be accomplished as set forth in Part 173,

Chapter 1, Subtitle B of CFR 49 currently in effect.  For foreign

manufactured containers identify, retire and test per

manufacturer's technical data currently in effect.

Abbreviations used in the Nord 262A Operations Specification

Aircraft Maintenance are defined as follows:

OC     =  On Condition.  [For the definition of On

Condition, refer to Advisory Circular AC121-1A.]

CALIB  =  Calibration check.  Testing for compliance with

established standards and readjustment for

tolerances as necessary.  May be performed with

unit installed or removed with proper test

equipment.

FC     =  Functional Check.  A qualitative check of a

component, assembly or system to determine that it

is operating in a normal and intended manner.

Does not require quantitative values and is

usually accomplished without removal from

aircraft.

Annual Functional Checks shall be performed during

the 90-day period preceding the season of maximum

system usage.

BC     =  Bench Check.  The removal of a unit from its

position on the aircraft, engine or assembly and

its routing to a shop for a thorough inspection,

check of its performance and compliance with

tolerances as prescribed for any and all of its

functions.  This check shall include minor

adjustments, markings and lubrication.

E.O.   =  Engine Overhaul.

E.O.   =  Engine Change.

Effective date _____________________

Page 1 of 16

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

O/H    L  PF  P  BIP  OTHER

Air Conditioning System

- Chapter 21               24,000     X   X  X   X

Check valve, elect. panel

cooling                     O.C.             X   X

Check valve, emerg.

ventilation                 O.C.             X   X   F/C @ BIP

Check valve, P2 regulation    O.C.             X

Check valve, P2               O.C.             X

Check valve, water separator  O.C.             X

Check valve, engine isolation O.C.             X

Check valve, turbo cooler     O.C.             X

Filter, P2 regulation         O.C.             X

Filter, control air           O.C.             X

Indicator, cabin rate of

climb                       8,000         X  X   X

Indicator, cabin temp.        O.C.          X  X

Indicator, differential                                Calib @

press. & altitude          12,000            X   X   BIP

Regulator, manual

pressurization              O.C.             X   X   F/C @ BIP

Regulator, altitude           O.C.             X

Selector, temperature         O.C.             X   X

Switch, altitude              8,000            X   X

Switch, differential pressure 8,000            X   X

Temperature probe, cabin      O.C.             X   X

Thermostat, cabin             O.C.             X   X

Thermostat, controllable      O.C.             X   X

Thermostat, overtemp warning  4,000            X

Timer, pressurization valve   4,000            X

Turbo cooler & heat exchanger 1,400            X

Valve, depressurization       8,000            X   X

Valve, hot air control        O.C.             X   X

Valve, emergency ventilation  8,000            X   X

Valve, cockpit window defog   O.C.             X

Valve, mixing turbine air     8,000            X   X

Valve, outflow                4,000            X       Clean @ 2P

Valve, outflow & overpressure

relief                      4,000            X

Valve, press. distribution    8,000            X   X

Valve, pressure regulating    8,000            X   X

Valve, P2 bleed shutoff       8,000            X   X

Valve, selector               O.C.             X   X

Water separator               O.C.             X   X   Clean @ P

Effective date ____________________

Page 2 of 16

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

Communications - Chapter 23

The maintenance program

(overhaul and inspection)

for this chapter is to be

established in coordination

with the assigned

Inspector.

Electrical System - Chapter

24                         24,000     X   X  X

AC protection unit            2,500         X  X

Ammeter                       O.C.             X   X   Calib @

BIP

Alternator                    2,000         X  X       Check

brushes

@ 1,000

hours lube

drive

spline per

SL 72-6.

Battery                       O.C.          X  X

Circuit breakers              O.C.          X  X

Inverters, standby & normal   2,000     X   X  X       Clean &

check

brushes @

500 hours.

Relay, reverse current        8,000         X  X

Relay, alternator connect     O.C.          X      X

Relay, AC transfer            O.C.          X  X   X

Relay, ground power           O.C.          X  X   X

Relay, polarized              8,000         X  X   X

Overvoltage cut out           8,000            X   X

Switches                      O.C.          X  X   X

Transformers                  O.C.          X  X   X

Voltage regulator, AC         2,500            X

Voltage regulator, DC         1,500            X

Voltmeter, AC & DC            O.C.          X  X   X   Calib @

BIP

Sensor, battery temp.         O.C.             X

Equipment & Furnishings

- Chapter 25               24,000         X  X   X

Cockpit seats                 O.C.          X  X   X

Passenger seats               O.C.          X  X   X

Fire Protection System

- Chapter 26               24,000     X   X  X   X

Extinguisher, engine **       O.C.      X   X  X   X   Continuity

Check @

BIP or 2

yrs. max.

Extinguisher, engine firing

cartridge                   3 yrs.

Effective date ____________________

Page 3 of 16

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

O/H    L  PF  P  BIP  OTHER

Fire Protection System -

Chapter 26 (Cont'd)

Fire detector engine unit     O.C.      X   X  X       Calib @

E.C.

Fire detector control box     O.C.          X  X

Hand extinguisher CO2 **      O.C.          X  X

Hand extinguisher H2O **      O.C.          X  X

Valve, Tee check              O.C.                 X   F/C @ BIP

Warning horn, fire            O.C.          X  X

Flight Control System

- Chapter 27               24,000     X   X  X   X   Cable

tension

check

annually

Box, flap preset              O.C.          X  X   X

Control column                O.C.          X  X   X

Cylinder, gust lock

actuating                   8,000         X  X   X

Cylinder, flap actuating      8,000         X  X   X

Detector, stall warning       O.C.             X   X   F/C @ BIP

Horn, stall warning           O.C.          X  X

Indicator, flap position      O.C.          X  X   X

Jackscrews, trim tab - oil,

rudder, elev.              12,000         X  X   X

Rudder pedal assemblies      16,000            X   X

Selector, gust lock          12,000         X  X   X

Transmitter, flap position    O.C.          X  X   X

Valve, check restrictor       O.C.          X  X   X

Valve, flap dual selector     8,000         X  X   X

Valve, emergency flap

retraction                  8,000         X  X   X   F/C @ 3P

Valve, ratchet & overload     8,000            X   X

Valve, flap shuttle           8,000            X   X

Valve, thermal expansion     12,000            X   X   F/C @ BIP

Warning system, flap aural    O.C.             X       F/C during

scheduled

gear

retraction

check

Fuel System - Chapter 28     24,000     X   X  X   X

Boost pumps & motor, main

(front)                     1,000         X  X

Boost pumps & motor, standby

(rear)                      2,000         X  X

Cells, fuel tank              O.C.      X   X  X   X   Leak test/

inspection

@ 2 BIP

Connector, pressure

refueling                    O.C.      X      X

Filter, fuel                  O.C.          X  X

Fuel collector manifold       O.C.             X   X

Indicator, fuel quantity      O.C.          X  X   X   Calib @

BIP

Indicator, fuel temp (dual)   5,000         X  X

Effective date __________________

Page 4 of 16

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

AND 262 A/M-298

O/H    L  PF  P  BIP  OTHER

Fuel System - Chapter 28 (Cont'd)

Switch, tank float            O.C.             X   X   F/C @ BIP

Switch, pressure warning     12,000         X  X

Transmitter, fuel quantity    O.C.          X  X   X   Calib @

BIP

Valve, refueling check        O.C.             X   X   F/C @ BIP

Valve, firewall shutoff       8,000            X   X   F/C @ E.C.

Valve, isolating & crossfeed  8,000            X   X   F/C @ BIP

Valve, pressure refueling     8,000            X   X

Valves, tank relief, vent,

sump & pressure refuel vent   O.C.      X   X  X   X   Tank

relief

valves

sump

drains

daily

Hydraulic System - Chapter

29                         24,000     X   X  X   X

Accumulators, surge & main   12,000         X  X   X

Filter, emergency fluid

supply                      4,000            X

Filter, low pressure supply   O.C.             X       Element

change @

3P

Filter, high pressure         O.C.          X  X

Indicator, pressure (triple)  8,000         X  X   X

Pump, hydraulic boost         1,250         X  X

Pump, hydraulic engine

driven                      2 EO          X  X       Shaft Insp

& lube @

E.C.

Pump, hand emergency         12,000     X   X  X   X   F/C @ 3P

Regulator, flap & gear

pressure                    8,000         X  X   X

Reservoir, main & emergency   O.C.          X  X   X

Switch, low pressure warning 12,000         X  X   X

Transmitter, hydraulic level  O.C.          X  X   X   Calib @

BIP

Transmitter, hydraulic

pressure                    8,000         X  X   X

Valves, ground test check     O.C.                 X

Valves, check & restrictor    O.C.             X       F/C @ BIP

Valve, emergency selector     8,000            X   X

Valve, emergency relief       O.C.             X   X   F/C @ BIP

Valve, firewall shutoff       8,000            X   X   F/C @ E.C.

Valve, pressure relief        O.C.      X      X   X   F/C @ BIP

Valve, thermal expansion     12,000            X   X

Effective date ____________________

Page 5 of 16

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

O/H    L  PF  P  BIP  OTHER

Ice & Rain Protection System

- Chapter 30               24,000     X   X  X   X   F/C Annual

Control panel, deicer boots   O.C.          X  X

Deicer boots, airfoil

leading edge                O.C.      X      X

Filter, deicer system         O.C.          X  X       Element

change @

2P

Indicator, deicing pressure   O.C.          X  X   X

Prop & Engine anti-ice

ammeter                     O.C.             X   X

Prop & engine anti-ice cycle

timer                       O.C.             X   X   Annual F/C

Prop & engine spray mat       O.C.          X  X   X   Annual F/C

Regulator, windshield heat    O.C.             X       F/C @ BIP

Relay, windshield heat        O.C.             X

Resistor unit, wipers         O.C.             X

Timer, airfoil deicing cycle  O.C.          X  X   X   Annual F/C

Transmitter, deice pressure   O.C.             X   X   Annual F/C

Valves, check wing deice      O.C.             X   X   Annual F/C

Valve, pressure regulating    8,000         X  X   X

Valve, pressure relief wing

deice                       8,000         X  X   X

Valve, deicing shutoff        8,000         X  X   X

Valve, solenoid operated

cycling                     4,000         X  X   X

Windshield wiper motor &

actuator                    8,000            X   X

Instrument System - Chapter

31                         24,000     X   X  X   X

The maintenance program

(overhaul and inspection)

for this system to be

established in coordination

with the assigned inspector,

except for the following:

Clock                         O.C.          X  X

Instrument panel &

installation                O.C.          X  X   X

Recorder, flight data         2,000         X  X

Landing Gear System

- Chapter 32               24,000     X   X  X   X

Accumulator, main & emerg.

brakes                     12,000         X  X

Accumulator, nose steering   12,000         X  X

Brake assembly                O.C.      X      X

Control unit, gear actuator  12,000            X   X

Cylinder, brake pedal         8,000         X  X   X

Cylinder, retract main &

nose                        8,000            X   X

Cylinder, nose steering       8,000            X   X

Filter, high pressure         O.C.             X   X

Gear retraction & extension

normal & emergency                                   Scheduled

retract

check @ 3P

Effective date ____________________

Page 6 of 16

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

O/H    L  PF  P  BIP  OTHER

Landing Gear System -

Chapter 32 (Cont'd)

Horn, gear warning            O.C.          X  X   X

Indicator, brake pressure

(dual)                      8,000         X  X   X

Indicator, gear position      O.C.          X  X   X

Main & Nose gear assemblies   8,000         X  X   X

Relay, hyd. pressure shutoff  O.C.             X   X   F/C @ BIP

Shock strut, main & nose

gear                        8,000     X      X

Tires                         O.C.      X   X  X

Valve, anti skid control      4,000            X

Valve, brake pressure

control                     4,000         X  X

Valves, check & restrictor    O.C.             X   X   F/C @

scheduled

retract

check

Valve, nose steering

control                     8,000         X  X   X

Valve, emerg. & park brake    8,000         X  X   X

Valve, electric dual

selector                    8,000            X   X

Valve, nose steering shutoff  8,000            X   X

Valve, brake shuttle          O.C.          X  X   X

Wheels                        O.C.      X   X  X

Anti skid control box         O.C.             X       F/C @

sched.

Anti skid generator           4,000            X       retract

check

Lights - Chapter 33          24,000     X   X  X   X

Emergency light system        O.C.      X   X  X

Rotating beacon               2,000     X   X  X

Navigation System - Chapter

34                         24,000     X   X  X   X

The maintenance program

(overhaul and inspection)

for this chapter is to be

established in coordination

with the assigned inspector

except for the following:

Ammeter, pitot heat           O.C.          X  X   X

Compass, magnetic             O.C.             X   X   Swing @ 2

years

Detector, overspeed warning   O.C.             X   X   F/C @ BIP

Pitot static system           O.C.             X   X   Annual

leak ck.

Probe, pitot tube             O.C.          X  X   X

Selector, instrument static   O.C.             X   X   Annual

leak ck.

Effective date ____________________

Page 7 of 16

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

AND 262 A/M-298

O/H    L  PF  P  BIP  OTHER

Oxygen System - Chapter 35   24,000     X   X  X   X

Cylinder O2**                 O.C.      X

Regulator/indicator           O.C.             X       F/C @ time

of cyl.

retest

Masks                         O.C.          X  X

Water/Waste System - Chapter

38                         24,000     X   X  X   X

System plumbing               O.C.             X   X

Structure - Chapters 52

thru 57

Chapters 52 thru 57 - covered in the following pages, are

structural items and therefore do not have specific overhaul

times.  These items, generally speaking, cannot be removed from

the aircraft; and even if they could, nothing could be done from

a maintenance standpoint to restore their original condition.

Therefore, the airworthiness of these items will be determined by

inspection/examinations in extensive detail.  If specific times

are not cited, the items are to be considered "On Condition".  if

the carrier elects to list structural inspection items in some

manner other than FAA-approved specifications, the document must

be referenced in the carrier's specifications and revision

handled in a similar manner to specifications revisions.  X-ray

or other approved NDT methods may be substituted in lieu of

visual inspections where applicable.

Effective date ____________________

Page 8 of 16

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

Detail

Insp. L  PF  P  BIP  OTHER

Doors - Chapter 52           24,000     X   X  X   X

Rear passenger door          12,000

External inspection

- check of safety cables,

hinges, lock hooks                    X   X  X   X

Internal inspection of

door structure, locking

mechanism & hooks                                X

Magnetic particle

inspection of hooks        12,000

Forward cargo door           12,000

External inspection, lock,

hooks and hinges                      X   X  X   X

Internal inspection of

door structure, lock

mechanisms and hooks                             X

Magnetic particle

inspection of hooks        12,000

Nose area and landing gear

doors                       4,000     X   X  X   X

Hinges and operating

mechanism                                    X   X

Emergency exits, overhead,                             or when

window and floor level     24,000                    cabin

lining

replaced

External inspection                   X   X  X

Detailed external

inspection (door removal)

of door structure & latch

mechanism                                        X

Internal inspection, door

structure, latch mechanism

& latch rigging                                  X

Fuselage - Chapter 53        24,000     X   X  X   X

Radome                        4,000                X   Detail &

External inspection                   X   X  X       External/

Fuselage skin                 O.C.                     internal

inspection

External inspection,

skin, joints & cutouts                X   X  X

Internal inspection of

support structure, joints

& cutouts                                        X

Station D pressure bulkhead  12,000

Forward face                                 X   X

Aft face & attach

structure                  12,000

Flight deck area, window

frames and exposed

structure                   4,000         X  X

Instrument panel & supports,

control pedestal, seat

tracks, control attach

structure                   4,000            X

Cockpit window frames,

internal structure, panel

supports, cockpit

structure & system

components                 12,000

Effective date ____________________

Page 9 of 16

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

Detail

Insp. L  PF  P  BIP  OTHER

Fuselage - Chapter 53 (Cont'd)

Flight deck area below floor

line visual inspection of

nose gear support units,

structure and system

components in area                           X   X

Structure inspection with

all cockpit flooring

removed                    12,000

Nose gear area structure      4,000         X  X   X

Inspect for looseness or

misalignment of gear units

or supporting structure                          X

Detailed inspection,

penetrant or other special

type inspection of all

nose gear fixed components

and attachments to fuselage

fittings.  Dimensional

checks of pins and bores   12,000

Inspection of fuselage hull

cutout framing and

reinforcements, main

passenger door, emerg.

exits, cargo door, windows,

outflow valves, etc.       12,000         X  X   X

External inspection of

framing and reinforcements                   X   X

Internal inspection of

hull cutouts &

reinforcements with

upholstery and trim

removed                    12,000

Galley and lavatory areas

Visual inspection of areas

below galley & lavatory

for corrosion               8,000

Area above cabin & cargo

floor seat rails, general

support for seats & cargo

restraints                                X  X   X

Inspection of seat rails,

attach structure, interior

of fuselage skin,

stringers, splices, and

belt frames                12,000

Area below cabin & cargo

floor, fuselage skin

interior, floor support

structure, belt frames                       X   X

Area below cabin & cargo

floors, detailed

inspection of all system

equipment, floor support

structure, fuselage

formers & stringers        12,000

Effective date ____________________

Page 10 of 16

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

AND 262A/M-298

Detail

Insp. L  PF  P  BIP  OTHER

Fuselage - Chapter 53 (Cont'd)

Fuselage center section,

detailed inspection of

fuselage formers and

stringers in area of Sta 9

& 11                        4,000

Wing attach fittings and

bolts.  Magnetic particle

inspection of bolts and

detailed inspection of

immediate fuselage skin

and structure around

fittings                   16,000

Main wheel pod area           4,000     X   X  X   X

Detail inspection of main

gear support arm, tie

rods, brace strut, shock

absorber, gear mountings,

air conditioning

equipment, waer methanol

equipment, hydraulic

reservoir & equipment.     12,000

Rear pressure bulkhead

Detailed inspection of

rear face                                    X   X

Detailed inspection of

fwd. face                  12,000

Tail section, detailed

inspection of splice

joint, systems equipment,

formers, stringers,

empennage attach fittings

and support rods and tail

cone.                       4,000            X   X

Nacelles - Chapter 54        24,000     X   X  X   X

Inspection of firewall and

engine mount attach points  E.C.             X   X

Inspect interior and exterior

of nacelles with tail pipe

removed                     4,000                X

Inspect all flight control

cables, bellcranks &

associated equipment in

nacelles                   12,000            X   X

Detailed visual inspection

of nacelle structure,

center section attach

angles, forward side of

front spar, spar rails and

brackets                    4,000

Engine QEC structure          E.O.          X  X   X

Magnetic particle inspection  4,000                    Engine

of engine mount and                                  mount to

firewall attach bolts.                               engine

attach

bolts

- magnetic

particle

insp. @

E.O.

Effective date ____________________

Page 11 of 16

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

Detail

Insp. L  PF  P  BIP  OTHER

Stabilizers - Chapter 55     24,000     X   X  X   X

Vertical stabilizer, rudder,

tabs & dorsal fin                     X   X  X   X

Detailed visual inspection

of dorsal fin, vertical

fin, vertical fin attach

points, rudder & hinge

points, vertical fin tip

cap area                    4,000

Detailed inspection of

rudder internal                                      During

structure                   O.C.                     cover

replacement

Detailed inspection of

internal structure of

dorsal fin                 12,000

Penetrant inspection of

vertical stabilizer attach

fittings, fin attach bolts

& rudder hinge fittings    12,000

Inspect visible structure at

rudder hinge points and

vertical stabilizer attach

points                     12,000

Horizontal stabilizer,

elevator and elevator tabs            X   X  X   X

Detailed visual inspection

of horizontal stabilizer,

hinge points, attach

points, elevator

structure, elevator

covering and tip caps       4,000

Detailed inspection of

internal structure of

horizontal and vertical

stabilizers                12,000

Penetrant inspection of

horizontal stabilizer

attach points, attach

bolts, attachment bars,

support frames, brace

strut, vee fitting and

elevator hinge fittings    16,000

Detailed inspection of                                 During

elevator internal                                    cover

structure                   O.C.                    replacement

Wings - Chapter 57           24,000     X   X  X   X

Forward fuselage to wing

fairing area, condition of

forward spar and fairing

attach fasteners            4,000

Wing leading edge ribs 7-13

noting condition of spar

and general structure       4,000

Effective date ____________________

Page 12 of 16

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

Detail

Insp. L  PF  P  BIP  OTHER

Wings - Chapter 57 (Cont'd)

Aft fuselage to wing fairing

area, noting mounting of

flap position transmitter,

hydro valves, aft spar and

flap torque tube            4,000

Lower fuselage to wing

fairing area, noting

condition of wing attach

fittings and system

installations               4,000

External inspection of

center wing structure

(ribs 1-21) noting skin

condition, areas adjacent

to attachment fittings to

fuselage, areas adjacent

to nacelle, flap hinge

attach points and outer

wing attach points          4,000

Center wing structure                                  As

(internal structure)                                 required

radiographic inspection in                           by

accordance with                                      airframe

manufacturer's                                       flight

recommendations             O.C.                     cycles

Center to outer wing attach

fittings, perform detailed

inspection of fittings and

bolts as installed          4,000

Outer wing structure (ribs

22-49) noting attachment

fittings at rib 22, hinge

attach points at ribs 25,

30, 35, 43, & 49            4,000

Aft section of wings (ribs

7-49) detailed inspection

of engine nacelle longeron

to rear spar in area of

ribs 15 thru 17, flap

hinge, arms, and cylinder

attach brackets at ribs 7,

17, 25, 30 & 35, aileron

hinge brackets and mounting

areas at ribs 35, 41, 42,

43 & 49.  Check on

condition of aileron

balance curtain             4,000

Wing leading edge area (ribs

22-49) detailed inspection

of skin, interior

structure, wing deicer

equipment by removing

leading edge or use of

radiographic procedure      8,000

Detailed inspection of tip

cap and surrounding area

with cap removed            8,000

Magnetic particle, penetrant

or similar special

inspection of outer/center

wing attach fittings and

bolts                      24,000

Effective date ____________________

Page 13 of 16

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

Detail

Insp. L  PF  P  BIP  OTHER

Wings - Chapter 57 (Cont'd)

Outer wing structure ribs

30-49 detailed interior

inspection with all access

panels opened               8,000

Detailed inspection of

internal area of forward

wing to fuselage fairing.

Remove all inspection

panels.                    12,000

Detailed inspection of

leading edge (ribs 7-13

areas) noting condition

of all equipment

internally housed in the

area                       12,000

Aft wing section (rib 7-35)

flap support fittings,

magnetic particle or

penetrant inspection of

removable parts            12,000

Aft wing/fuselage fairing

area.  Detailed inspection

of entire area including

flap torque tube, mount

brackets & bearings

Penetrant inspection of

aileron quadrants, mount

brackets & bolts           24,000

Magnetic particle, penetrant

or similar special

inspection of center wing

to fuselage attach

fittings, links & bolts    24,000

Outer wing structure (rib

22-30) radiographic

inspection of forward

lower spar rail between

22 & 23, 23 & 24.  Lower

skin forward of rear spar

between ribs 22 & 23, 23 &

24.  Lower skin doublers

between ribs 25 & 26, 28 &

29.  (Drain fuel prior to

inspection)                24,000

Detailed visual inspection

of flaps.  Note condition

of areas adjacent to hinge

arms                        4,000

Magnetic particle or

penetrant inspection of

flap, hinge arms, actuator

attach fittings & bolts    12,000

Detailed visual inspection

of ailerons visible

structure hinge brackets &

adjacent structure          4,000

Magnetic particle or

penetrant inspection of

aileron hinge brackets,

aileron pushrods, and

attach bolts               12,000

Effective date _____________________

Page 14 of 16

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

O/H    L  PF  P  BIP  OTHER

Propeller System - Chapter

61                                    X   X  X   X

Propeller Ratier Figeac

FH-146                      2,000     X   X  X

Auto feather capsule          O.C.          X  X       F/C @

1,000 hrs.

Auto feather pitot masts      O.C.      X   X  X   X

Contactor, feather pump       8,000         X  X

Feather pump                  2,000         X  X

Governor, prop control        E.O.          X  X

Relay unit, prop control      8,000         X  X

Switch, prop feather          O.C.      X   X  X

Powerplant - Chapter 71                 X   X  X   X

Cowling                       O.C.      X   X  X

Engine - Chapter 72

Engine Turbomeca Bartau VI C  2,000     X   X  X       Hot

(Refer to manufacturer's                             section

specification for life                               inspection

limited parts)                                       @ 1/2 E.O.

Engine Fuel System - Chapter

73                                    X   X  X

Fuel control unit             E.O.          X  X

Indicator fuel flow           5,000         X  X

Indicator fuel used           O.C.          X  X

Transmitter fuel flow         5,000         X  X

Transmitter fuel pressure

diff.                       E.O.          X  X

Valve, electrical fuel

shutoff                     2 E.O.        X  X       F/C @ E.O.

Valve, safety shutoff         O.C.          X  X       F/C @ E.O.

Ignition System - Chapter 74                   X

Coil                          E.O.             X

Torch ignitors                E.O.             X

Engine Air System - Chapter

75

Engine anti-ice electro

valve                       O.C.             X       F/C @ E.O.

Engine Controls System

-  Chapter 76

Engine control linkage

(forward of firewall)       O.C.             X       Inspect

E.C.

Effective date ____________________

Page 15 of 16

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SOCIETE NATIONALE INDUSTRIELLE AEROSPATIALE (SNIAS) NORD-262A

O/H    L  PF  P  BIP  OTHER

Engine Indicating - Chapter

77                                    X   X  X   X

Indicator Tachometer          5,000         X  X

Indicator, EGT, oil temp &

pressure                    5,000         X  X

Indicator, torquemeter        5,000         X  X

Switch, P2 starter cutoff     O.C.          X  X

Tachometer generator          2 E.O.        X  X

Thermic corrector             O.C.          X  X       Calib @

E.C.

Torque transmitter            E.O.          X  X

AVM Transducer                O.C.             X       Calib @

E.C.

AVM Indicator                 O.C.             X       Calib @

E.C.

AVM Amplifier                 O.C.             X       Calib @

E.C.

Engine Exhaust - Chapter 78             X   X  X   X

Tailpipe & clamp              O.C.          X  X

Tailpipe insulating blanket   O.C.             X

Engine Oil System - Chapter

79                                           X

Heat exchanger, oil/fuel      O.C.          X  X       F/C @ E.O.

Oil filter                    O.C.             X       Inspect @

1/2 P

Switch, low pressure warning  O.C.          X  X       F/C @ E.O.

Tank, engine oil              O.C.          X  X

Temperature probe             O.C.          X  X       F/C @ E.O.

Transmitter, oil pressure     O.C.          X  X       F/C @ E.O.

Starting - Chapter 80                          X   X

Micro pump                    2 E.O.        X  X

Relay, starting              12,000         X  X   X

Starter/generator             E.O.          X  X       Brush

checks Air

equip-400

hours

SEB - 600

hours

Starter relay box             O.C.          X  X

Effective date ____________________

Page 16 of 16

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE

SOCIETE NATIONALE INDUSTRIELLE AERSPATIALE (SNIAS) NORD-262A

Detail

Insp. L  PF  P  BIP  OTHER

Water Methanol System

- Chapter 82               24,000     X   X  X   X

Filter element                O.C.             X   X   Inspect @

2P

Indicator, water/met. flow    4,000         X  X

Indicator, water/met.

quantity                    8,000         X  X       Calib @

4,000

Metering unit, water/met.

flow                        4,000         X  X

Pump & motor, water/met.

boost                       4,000         X  X

Switch, low pressure warning  8,000         X  X       Calib @

4,000

Transmitter, water/met. flow  4,000         X  X

Transmitter, water/met.

quantity                    O.C.          X  X   X

Valve, check                 12,000            X       F/C @

4,000

Valve, isolation              8,000         X  X

Valve, water/met. control     8,000         X  X

Effective date ____________________

Form Approved.

OMB. No. 04-R0075.

Supplement

Page 1 of 11

UNITED STATES OF AMERICA

DEPARTMENT OF TRANSPORTATION

FEDERAL AVIATION ADMINISTRATION

WASHINGTON

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - SUPPLEMENT

GENERAL

SNIAS N262A/M-298

These pages apply to N262A aircraft modified in accordance with

STC 2369SW.  Those portions of the airframe and/or systems

unaffected by the modification will continue to be maintained in

accordance with the operators' currently approved Operations

Specifications.

Abbreviations and definitions listed for the basic N262A Aircraft

Maintenance Operations Specifications apply to this supplement

also.

Samples listed in this supplement are industry samples and are to

be submitted by the first operator attaining the specified time

limit.

Effective date ____________________

Supplement

Page 2 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - SUPPLEMENT

SNIAS N262A/M-298

ATA CHAPTER                     OH      L   PF  P  BIP OTHER

21 - Air Conditioning and

Pressurization

Valve airflow -          5,000             X      Sample 2 @

2,500

Switch, overpressure

sense                    O.C.              X

Valve, pressure

regulating               5,000             X

Venture, flow limiter    O.C.              X

Switch, bleed air

overheat                 O.C.              X

Air cycle machine        5,000             X      Sample 1 @

2,000, 1 @

4,000

Valve, ACM bypass        O.C.              X      Sample

insp. 2 @

2,000

Separator, water         O.C.              X      Clean or

replace

coalescer

@ P

Switch, temp. supply     O.C.              X

Heat exchanger,          O.C.              X      Leak test

secondary                                         1 @ 2,000,

1 @ 4,000

Sensor, cabin temp.      O.C.              X

Sensor, duct temp.       O.C.              X

Selector, cabin temp.    O.C.              X

Controller, cabin temp.  O.C.              X

Precooler, nacelle       O.C.              X      Leak test

1 @ 2,000,

1 @ 4,000

Effective date ____________________

Supplement

Page 3 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - SUPPLEMENT

SNIAS N262A/M-298

ATA CHAPTER                     OH      L   PF  P  BIP OTHER

22 - Autopilot

Control, altitude

Collins P/N

229-9015-010             O.C.              X

Sensor, airspeed

Collins P/N

229-9016-010             O.C.              X

Servo, trim Collins

P/N 622-0965-001         6,000             X      Sample 1 @

3,000

Control, pitch & turn

Collins P/N 622-1210-001 O.C.              X

Servo, aileron Collins

P/N 622-2366-001         6,000             X      Sample 1 @

3,000

Servo, rudder & elevator

Collins P/N 622-2366-002 6,000             X      Sample 1 @

3,000

Gyro, vertical Collins

P/N 792-6694-001         2,500             X

23 - Communications

* Maintenance program to

be approved by local

ACDO

24 - Electrical

Inverter, solid state

Jet P/N S1-2500B         O.C.          X   X

25 - Furnishings

Seat, passengers & F.A.  O.C.      X   X   X

Galley unit              O.C.          X   X

Effective date ____________________

Supplement

Page 4 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - SUPPLEMENT

SNIAS N262A/M-298

ATA CHAPTER                     OH      L   PF  P  BIP OTHER

26 - Fire Protection

Detector, engine fire    O.C.      X   X   X

Detector, nacelle fire   O.C.      X   X   X

Extinguisher, engine &

APU fire                 O.C.          X   X

27 - Flight Controls

No changes

28 - Fuel System

Filter, fuel             O.C.              X      Inspect @

1/2 P

29 - Hydraulic Power

Valve, electric shutoff  O.C.              X

Pump, hydraulic boost    2,000             X      Sample 1 @

1,000

Limiter, hydraulic flow  O.C.              X

Pump, engine driven      2 E.O.            X      Sample 1 @

1 E.O.

30 - Ice & Rain Protection

Filter, hydraulic

isolating                O.C.              X      Inspect @

3 P

Restrictor, hydraulic

flow                     O.C.              X

Reservoir, hydraulic

isolating                O.C.              X

Relay, prop deice        O.C.              X

Transformer, windshield

heat                     O.C.              X

Ammeter, prop deice      O.C.              X

Effective date ____________________

Supplement

Page 5 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - SUPPLEMENT

SNIAS N262A/M-298

ATA CHAPTER                     OH      L   PF  P  BIP OTHER

30-Ice & Rain Protection Cont'd

Transmitter, deice

pressure                 O.C.              X

Controller, windshield

heat                     O.C.              X

Boot, engine lip deice   O.C.              X      Annual F/C

Boot, airframe deice     O.C.              X      Annual F/C

Valve, hydraulic

shutoff                  O.C.              X

Timer, prop deice        O.C.              X      Annual F/C

Valve check              O.C.              X      Annual F/C

Valve deice distributor  O.C.              X      Annual F/C

Regulator, deice

pressure                 O.C.              X      Annual F/C

Valve, deice

distributor              O.C.              X      Annual F/C

Actuator, inertial

separator                2 E.O.            X      Annual F/C

Brushblock, prop deice   O.C.              X

Timer, airframe deice    O.C.              X      Annual F/C

Indicator, deice

pressure                 O.C.              X      Annual F/C

Separator, deice water   O.C.              X

Valve, hydraulic shutoff O.C.              X      Annual F/C

Switch, deice pressure   O.C.              X      Annual F/C

Effective date ____________________

Supplement

Page 6 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE - SUPPLEMENT

SNIAS N262/M-298

ATA CHAPTER                     OH      L   PF  P  BIP OTHER

31 - Instruments

No Changes

32 - Landing Gear

No Changes

33 - Lights

Strobe lights

Grimes P/N 30-0516-1 &

30-0863-1/2              O.C.          X   X

Power supply, strobe

Grimes P/N 60-2290-1     O.C.              X

Coder, strobe lights

Grimes P/N 70-0125       O.C.              X

34 - Navigation

*Maintenance program to

be approved by local

ACDO

38 - Water/Waste

Toilet, chemical         O.C.      X   X   X

49 - Auxiliary Power          Note:  APU related unit TBO's

stated in APU operation

hours

Valve, APU fuel shutoff  O.C.              X

Valve, APU bleed check   O.C.              X      Bench

check @

3,000

Starter - generator, APU 3,000                    Inspect @

1,000

Filter, APU Fuel         O.C.              X

APU, engine              3,000             X      Sample

inspect 1

@ 1,000 1

@ 2,000

Effective date _____________________

Supplement

Page 7 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE -- SUPPLEMENT

SNIAS N262/M-298

ATA CHAPTER                     OH      L   PF  P  BIP OTHER

52 - 57 Structure Chapters

The basic structure

remains unchanged by the

M-298 modifications and

the structural inspection

requirements are

therefore identical,

however certain

additional sample

inspections are

recommended as follows:

53 - Fuselage

No Change

54 - Nacelles

Zones 412, 422, 413,     1 BIP             X      Sample

423.                                              detailed

Inspection of firewall                            visual

and engine mount attach                           inspection

points                                            1 @ 2,000

and 1 @

4,000

Zones 412, 422, 415,     1 BIP             X      Sample

425                                               detailed

Inspect interior and                              visual

exterior of nacelles                              inspection

1 @ 2,000

and 1 @

4,000

Inspect all flight and   3 BIP             X      Sample 1 @

engine control cables,                            1 BIP & 1

bellcranks and                                    @ 2 BIP

associated equipment in

nacelles

Detailed visual          1 BIP             X      Sample 1 @

inspection of nacelles                            2,000 and

structure, center                                 1 @ 4,000

section attach angles,

forward side of front

spar, spar rails and

brackets

Effective date _____________________

Supplement

Page 8 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE -- SUPPLEMENT

SNIAS N262/M-298

ATA CHAPTER                     OH      L   PH  P  BIP OTHER

55 - Stabilizers

No Change

57 - Wings

No Change

61 - Propeller System

Governor, prop

overspeed                E/O               X

Propeller, assembly      1,500                    Sample

inspect 2

@ 750

Relay, autofeather delay O.C.              X

Shaft, prop sync         O.C.              X      Inspect @

E/O

Control, prop sync       O.C.              X

Pick up, prop sync       2 E.O.            X

Actuator, prop sync      2 E.O.            X      Inspect @

E/O

Switch, auto feather     O.C.              X

Governor, propeller      E.O.              X

71 - Powerplant

Cowl, engine             O.C.              X

Mount, engine            O.C.              X      Mag Part

Insp. @

E.O.

72 - Engine

Engine P & W PT6A-45A    1,500     X   X   X      Sample

Insp. 1 @

1,000 & 1

@ 1,250

Hot Section Insp.        1/2 E.O.

Effective date _____________________

Supplement

Page 9 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE -- SUPPLEMENT

SNIAS N262/M-298

ATA CHAPTER                     OH      L   PF  P  BIP OTHER

73 - Engine Fuel System

Indicator, fuel flow     5,000         X   X

Totalizer, fuel used     5,000         X   X

Controller, fuel heat    2 E.O.            X

Conditioning unit, fuel

flow                     O.C.              X

Valve, fuel shut off     O.C.                     F/C @

engine

change

Pump, fuel engine driven E.O.              X

Transmitter, fuel flow   5,000             X

Heat exchanger, oil/fuel O.C.              X

Pump, engine fuel        E.O.              X

Fuel control unit        E.O.              X

Valve, check             O.C.              X

Transmitter, fuel

pressure                 5,000             X

Pump, EPA fuel drains    O.C.              X      F.C. @ 3P

Indicator, fuel pressure 5,000             X

74 - Ignition

Exciter, ignition unit   O.C.              X

Ignitor                  O.C.              X

76 - Engine Control System

Engine control linkage   O.C.              X      Insp. @

E.O.

Effective date _____________________

Supplement

Page 10 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE -- SUPPLEMENT

SNIAS N262/M-298

ATA CHAPTER                     OH      L   PF  P  BIP OTHER

77 - Engine Indicating

Generator, tachometer

Task P/N AG34            2 E.O.            X

Horn, overtemp warning

Mallory P/N SC 628H      O.C.              X

Indicator, torque

pressure

Edison P/N 217-08221     5,000             X

Transmitter, torque

pressure

Edison P/N 418-04-24     2 E.O.            X

Indicator, ITT

Insco P/N 5021-1028      5,000             X

Indicator, Tachometer

N1 & N2 Insco

P/N 6503-1009/1015       5,000             X

78 - Exhaust

Tailpipe                 O.C.              X

79 - Engine Oil

Probe - oil temp         O.C.              X

Filter, engine oil       O.C.              X      Insp @ 1/4

P

Transmitter, oil

Pressure                 2 E.O.            X

Switch, low oil pressure O.C.              X

Indicator, oil pressure  5,000             X

Indicator, oil temp      5,000             X

Effective date _____________________

Supplement

Page 11 of 11

OPERATIONS SPECIFICATIONS

AIRCRAFT MAINTENANCE -- SUPPLEMENT

SNIAS N262/M-298

ATA CHAPTER                     OH      L   PF  P  BIP OTHER

80 - Starting

Relay, starter/                                   Sample

generator               10,000             X      Insp. 1 @

5,000 & 1

@ 7,500

Starter, generator       2 E.O.            X      Insp. @ 1

1/2 P

82 - Water Methanol

Relay, water methanol

pump                     O.C.              X

Tank, water methanol     O.C.              X

Valve, water methanol

shutoff                  O.C.              X

Indicator, water

methanol qty.            5,000             X

Transmitter, water

methanol qty.            O.C.              X

Transmitter, water

methanol pressure        O.C.              X

Filter, water methanol

supply                   O.C.              X      Insp. @ 2

P

Indicator, water

methanol pressure        5,000             X

Pump, water methanol

boost                    4,000             X

Effective date ____________________