POLAR Spacecraft Status As of: Tues 19 Oct 04  16:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM:AN=1646 STIP data only | NOAA-14J AM:AN=2006 STIP data only | NOAA-15K AM:AN=1822 GAC data only | NOAA-16L PM:AN=1424 GAC&LAC data | NOAA-17M AM: AN=2224 GAC&LAC data | NOAA-N18 Planned PM Plan AN=14:00 |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | NET 2/12/05 |
| CNTL OBP | OBP2 | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | End to End test 20 Oct |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 | B-BUS XSU-1 |  |
| BUS VETO | NO | NO | NO | NO | NO |  |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ SS check Disabled when mode=YGC | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAA Gyro3 TOAR 427 ESA sun glint season | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB Gyro3 TOAR 436 | New ring laser gyro |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mSec +100 mS 31Au04 | PRI Daily Bias –5.5 mS -100 mS 31Au04 | PRI Daily Bias –3 mSec |  |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 |  |
| MIRP | External Synch Rephase Enabled | External Synch Rephase 0730 Daily | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled |  |
| TIP SIDE | 1 | 1 | 2 (since 4/23/03) Channels 224 -227 invalid TOAR 432 | 1 Analog telem drifting TOAR 439 | 1 Analog telem drifting |  |
| DTRs | 3, 4, 5B Safestate 3B since 9 Jun | 1, 2B, 3A, 5 Safestate- 1B | 1, 2, 3, 4 Safestate 1B EOT | 1,2,3,4A Safestate 3A 4B TOAR 418 (STIP only) | 1,2,3,4 Safestate=1B DTR2-SSR DTR5 TOAR 420 | All solid state digital recorders |
| VTX (APT data) | #1 ON 137.50 MHZ N15 conflict ending | OFF Since 8/14/02 | OFF Plan turnon 10/20t N12 conflict ends | INOP OFF since 11/15/00 | #2 ON 137.62 MHZ |  |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #1 137.35 MHZ | #2 137.77 MHZ |  |
| STX #1=1698.0 mhz #2=1702.5 mhz #3=1707.0 mhz #4=2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT 4-Playback 1,2,3-Degraded | 1 – HRPT; 2– Playback; 4 – Playback 3 low power unused | 3 – HRPT TOAR424 low power 1&2 Playback 4 – TIP |  |
| POWER (Array offset, charge and eclipse states, sun angle) Sun-Moon Eclipse occurred 14 Oct 04 | ArrayOff +50 since 8/31/04 Full Sun Battery UVtrip 7/25 Sun Angle 15 bottomed out Batts 1&2=LRC V/T=4 (26Jul) Shunt degraded SA CANT=37 degs | Array Off -55 Since 8/21/03 Eclipse all year Sun Angle at 38 steady trend Batts 1-3= LRC Batts 1&3V/T=8/11 Batt2 VT=9/11 ) Shunt Degraded SA CANT=37 degs | Array Off -45 Since 1/25/01 Full Sun Sun Angle 9 Start uptrend to 15 in mid-Dec Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 * Eclipse all year * SADPOS moved to 0 deg offset 10/14 at 02:15. Cmd back to -40 deg at 07:45 Sun Angle 49 Bottomed out Steady trend Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 68 Steady trend Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs |  |
| AVHRR | Nominal Turned backon 7/28 Chan-2A on 8/3/04 | INOP Scan motor stalled 14 Apr 04 | Nominal Rare major scan motor surges. Last Incident 8/9/03 | NOMINAL No bar code or wave patterns. Scan motor occasionally erratic TCE24 OFF 4/14 Chan 3B only. | Nominal 3A-B switch enabled Scan Motor on watch list | New brushless scan motors |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational TOAR 415 on primary PLLO chans 9-14 bias shift. TOAR 417 on Backup PLLO inop | OFF/INOP Since 10/30/03 Inoperable Red in status. Survival heat on. |  |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal |  |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges ,most recent 8/26/04 IPD Reports of degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal |  |
| HIRS | ON / INOP Turned on 8/30/04 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | VARIABLE FW mode=Hi Powr FW Heater OFF Frequent Filter Motor current “mini” surges Occasional major FM current surges, most recent 6/3/04 | Operational Occasional major FM surges, most recent 4/29/04 IPD Reports of excess noise in space view channels 21May04 Patch Power investigation | NOMINAL 1 Pixel cross track misalignment . |  |
| MHS/MIU |  |  |  |  |  | Integrated on spacecraft Replaces AMSUB |
| MSU | ON / INOP Turned on 8/30/04 For power balance Scan Motor OFF since 3/12/03 | Operational Scan motor and antenna problems |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal |  |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational A-side, AGC Mode (B-side in FG mode) 243 MhZ = INOP. | Nominal A-side All AGC Mode |  |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal |  |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Telescopes inoperative | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 |  |
| SBUV |  | Degraded Grating motor stuck at position –930 on 7/8/04 recovery ops successful 7/9 Flex memory 3 (giant step) ops suspended indefinitely on 12/2/03 Reduced operations started 6/5/03 |  | Operational Plan discrete mode test 21 Oct Flex Mem-3 testing Completed Degraded Ozone data reported TOAR 435 Backup Diffuser inop Primary Diffsuer deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode |  |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Autonomous implementation 10/14at 02:15Z Commanded back to backup at 07:45 | ON ENABLED Disabled 14 Oct 02:15 reenabled 03:30 for sun-moon eclipse |  |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 HIRS FW Heat OFF TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 S/C in strong cooling trend | Nominal TCE24 OFF 4/14 (AVHRR H&L) | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 |  |
|  | N12 | N14 | N15 | N16 | N17 | NOAA-N18 |

COMMENTS/CHANGES:

NOAA-12	The RF conflict with N15 VTX-1 will be ending on 20 Oct 04 at which point the N15 VTX transmitter will be turned

back on.  Because of other RF conflicts, N12 continues to have far fewer passes resulting in less capability for ensuring

nominal health of the spacecraft.  With the data currently available there does not seem to be any problems at this time.

EMOSS monitored the solar eclipse event on N12 between 00:30 and 04:45z on 14 Oct.  There was no significant impact on the spacecraft and no reconfigurations were required in preparation for this event.  Carl Gliniak was EMOSS POC.

NOAA-14:	The N14 power situation remained stable during the past reporting period although minimum battery voltages have started to occasionally fall below 20.5 (illustration 1) as the percentage of time that N14 spends in the dark during each orbit has begun to slowly increase.  This trend is expected to continue through mid-November where the darkness percentage should peak at 23% per orbit.  By that time, it may be possible that a power subsystem reconfiguration will be required to maintain an adequate margin and ensure no undervoltage situation or additional shunt stress occurs.  Discussions and analysis are ongoing.

EMOSS monitored the solar eclipse event on N14 between 00:30 and 04:45z on 14 Oct.  There was no significant impact on the spacecraft and no reconfigurations were required in preparation for this event (illustration 2).  Analysis of the EMOSS eclipse model showed a high degree of accuracy in the predictions of when the eclipse would begin.  Carl Gliniak was EMOSS POC monitoring in the SOCC during the eclipses.

NOAA-15:	The cooling trend on N15 appears to have bottomed out and perhaps reversed itself in conjunction with the sun angle starting a new uptrend (illustration 3).  However, this new uptrend will be shorted lived and only bring the sun angle up to approximately 15 before it again begins to trend downward.  Therefore, many spacecraft component temps will continue to run at relatively low values.   Currently there appear to be no subsystem health or image quality degradation associated with the low temperatures achieved during this cooling trend.

The small AVHRR scan motor mini current surge that was reported in the previous report has since returned back to nominal where it remains as of this writing.  AMSU-B was also nominal during the past reporting period while HIRS filter motor continues to experience mini current surges at least once per week (illustration 4).

EMOSS monitored the solar eclipse event on N15 between 00:30 and 04:45z on 14 Oct.  There was no significant impact on the spacecraft and no reconfigurations were required in preparation for this event although AVHRR did show some reaction (illustration 5).  Analysis of the EMOSS eclipse model showed a high degree of accuracy in the predictions of when the eclipse would begin.  Carl Gliniak was EMOSS POC monitoring in the SOCC during the eclipses.

NOAA-16:	The N16 AVHRR scan motor current, settled back down after a small surge last week and continues to operate almost exclusively within nominal values.  In addition, the synch delta value, which last week suddenly fell to near zero, remains at near zero.  AVHRR thermal profile shows a continued slow uptrend and TCE24 remains powered off to “assist” this warming trend.  All imagery for the week has appeared nominal.  Sally House and Jim Walters are EMOSS POC’s for this payload.  (See illustrations 6-8).

The N16 HIRS filter motor current was also stable and nominal during the past reporting period although it did rise slightly during that time (illustrations 9-10).  In addition, HIRS Patch power, which is currently on the EMOSS “watch list” was stable throughout the past reporting period.

However, the performance profile of the N16 Earth Sensors continues to exhibit behavior suggestive of direct sunlight entering the detectors (as depicted by the ESA ORS voltages and Sun Moon warning status (illustration 11).  This issue started on or about 30 Sept and current opinion is that it is a seasonal event that does not constitute a health issue for the ADACS at this time because GEODAT just blocks out the quadrant that is experiencing the sun glint.  EMOSS engineer Jim Sheperd has already submitted an Event Report on this issue.   Because of the continued stability of the N16 sun angle for the next several weeks, this situation is expected to continue.

The N16 SBUV was somewhat thermally affected by the 14 Oct eclipse which resulted in two solar array offset moves within a 5 hour span.  In addition, the test characterizing the SBUV’s wavelength dependence of the inter-range ratio between range2 and range 3 measurements was concluded on 11 Oct after executing once per day since 4 Sept out of Flex Memory-3 (illustration 12).  A new test, requested to help with the investigation of TOAR 435 is currently planned for implementation on Thursday, 21 Oct.  This new test will be executed using a spacecraft macro.  The macro will be loaded and enabled during the pass at 14:40z.  The macro closes the cal lamp door and commands position mode when the satellite enters darkness, and opens the door and commands discrete mode when the satellite enters light. The macro will execute for four orbits and then it will disable itself.  EMOSS engineer Jon Woodward created and tested the macro and Jim Walters is POC for its implementation.

N16 (cont)

In a correction to lasts week report, N16 did NOT have its SADPOS disabled in preparation for the solar eclipse event on 14 Oct as had been specified.  EMOSS monitored the solar eclipse event on N16 as it occurred on 14 Oct.  During the eclipse, at 02:23:22Z, the N16 SADPOS autonomously took control of the solar array from SADCS and repositioned the solar array offset to zero degrees (from -40 degrees).   During the event, Barrow was in contact with N16 so the situation was immediately detected by engineers and controllers monitoring the support. Symptoms of this event were; several hardware bi-level miscompare flags, a variety of spacecraft subsystem thermal profile changes, and a significant increase in spacecraft pitch while the array was repositioned which quickly damped itself back to nominal.  At no time during this event was there any significant or immediate threat to overall spacecraft status and/or health. The primary engineering concern regarding this unexpected reconfiguration was its implications on shunt loading caused by increased solar array output and manifested by shunt temperatures peaking at 81 degrees C, approximately 20 degrees warmer than average (and 4 degrees below the yellow high limit). While the shunt situation was also not considered a significant threat to spacecraft health, the engineering consensus was to return the spacecraft back to its previous configuration as soon as possible. The recovery operation consisted of clearing the hardware flags and commanding solar array control back to SADCS with SADPOS as backup at 06:00Z followed by commanding the solar array back to -40 degree offset at a 07:45Z.  Each of these operations proceeded nominally and resulted in spacecraft thermal profiles returning back to their pre-event levels.  Investigations by the team determined that the N16 SADPOS takeover occurred, exactly as it was designed to do, because the spacecraft experienced an “unexpected” loss of sunlight, for longer than 8 minutes, the trigger threshold for SADPOS control. The team has concluded that the root cause of this event is attributable primarily to spacecraft documentation (P&CH) that specifies both a variable and an incorrect definition of what constitutes unexpected spacecraft darkness (100 mAmp solar array patch current specified vs. the actual value of no less than 150mAmps).  This incorrect information was then loaded into the EMOSS eclipse analysis model resulting in an underestimation of darkness duration by almost 50% and a recommendation that SADPOS not be disabled for the N16 eclipse.  EMOSS engineers responding to the event, performing the analysis and generating the Event Report were Carl Gliniak, Jon Woodward and Jeff Devine.  (Illustrations 13-17)

NOAA-17:	EMOSS engineers continue to closely monitor the N17 AVHRR scan motor for signs of degraded performance. During

the past week, the performance remained stable as did its synch delta value operating profile. In addition, N17 AVHRR temperatures continue to operate in nominal range and values and there have been no reports or observations of degraded imagery (illustration 18).  Sally House and Jim Walters are EMOSS POC’s.

In a correction to lasts week report, N17 DID have its SADPOS disabled in preparation for the solar eclipse event on 14 Oct at 02:15Z which was returned back to enabled at 03:50Z.  This configuration was commanded because the EMOSS solar eclipse model predicted that the spacecraft would be in “unexpected darkness” for more than 7 minutes, too close to the 8 minute threshold where SAPOS might autonomously take over control of the solar array.  EMOSS engineer Carl Gliniak implemented this commanding and monitored the solar eclipse effects during this interval.  There was no significant impact on the spacecraft originating from this event (illustration 19).  Analysis of the EMOSS eclipse model showed a high degree of accuracy in the predictions of when the eclipse would begin.

The ADACS on N17 was also nominal during the past reporting period although slightly less stable (as measured by yaw update) than is desirable (illustration 20).  Jim Sheperd is EMOSS POC for this issue.

NOAA-N:	EMOSS engineers began regenerating the ascent data base originally delivered in mid-June 2004.  This data base is

scheduled to be re-transmitted to NASA within the next week and into PACS by 2 Nov.  Michelle Settles is EMOSS POC.

EMOSS engineers continue supporting reviews, analysis, testing and product preparations for the 20 Oct end to end test.

MISC:	 Meetings supported by EMOSS included: Internal launch readiness meeting, MOWG, Ascent data base recovery meeting, COP Reviews, N18 Monitoring Guidelines Training and COP reviews.

The next database release is scheduled for Nov. 2.  All approved CCRs should be turned into Michelle no later than Oct. 25.

EMOSS engineer Jim Sheperd supported the scheduling office on the SOMS generated ephemeris loads which appear to be working well.  Future plans are to have these SOMS generated ephemeris loads execute of the of the schedule.

EMOSS engineer Jeff Devine worked with the software office to develop and test a process that will ensure the EMOSS HAF file archive can be reformatted in DMF file that are required by ABE.  The reformatting process was successful but ABE was still unable to generate graphs from the file.  Work is continuing.

Illustration 1:  N14 Power Subsystem Analysis

(Other than battery voltage creeping a little lower, everything looks nominal)

Illustration 2:  N14 Selected Power Values during Sun-Moon Eclipse of 14 Oct 2004

Illustration 3:  N15 Selected Payload Thermal Analysis

(Cooling is over now that sun angle has bottomed out and started to reverse its downtrend.  However, temperatures will probably stay relative low throughout the winter since sun angle will not increase beyond 16 degrees this cycle. Note the effect that the sun-moon eclipse had on AVHRR on JDAY 288.)

Illustration 4:  N15 Payload Motor Health Analysis

(All within nominal or typical values and profiles except for that little

“hic-up” on the AVHRR on day 286 which has since stabilized. Note the effect that the sun-moon eclipse had upon the AVHRR on JDAY 288)

Illustration 5:  N15 Selected Power Values during Sun-Moon Eclipse of 14 Oct 2004.

Illustration 6:  N16 AVHRR Scan Motor Health Analysis

(Continued nominal performance)

Illustration 7:  N16 AVHRR Synch Delta Analysis

(Currently averaging near zero,  about as good as it gets.)

Illustration 8:  N16 AVHRR & other payload Thermal Analysis

AVHRR is nominal but climbing with TCE24 remaining off.  Other payloads are stable and show very minor influences caused by the two solar array moves on 14 Oct (J288).

Illustration 9:  N16 HIRS Health Analysis

(Filter motor current showing a small “build up” that hopefully will not lead to another  major surge event.)

Illustration 10:  N16 HIRS Filter Motor Trends and Tendencies

Illustration 11:  N16 Earth Sensor trends and tendencies.

(Seasonal “sun glint” on the earth sensor is more intense this season because of the 49 degree sun angle being experienced by the spacecraft.  This sun angle will remain relatively stable for a few weeks at least so the glint will continue on each orbit until the angle changes significantly.  This situation is not a health concern because the on-board GEODAT directs the spacecraft to ignore the quadrants where and when this glint is being experienced

Illustration 12:  SBUV Health Analysis

Flex Memory-3 Testing ended on 11 Oct.  A new test is planned for 21 Oct.  Note the influence that the SADPOS/Array Move/Sun-Moon eclipse had on the SBUV.)

Illustration 13:  N16 Predicted (purple line) vs Actual (dark blue line) sun-moon eclipse onset.

(Very closely correlated and definitely close enough to make well informed reconfiguration recommendations.

Illustration 14:  N16 Eclipse contingency situation timeline.

Illustration 15:  N16 Darkness Definition Comparison

(The difference between what the spacecraft actually used and the default value specified in the P&CH which was used in the model to determine the necessity of disabling SADPOS).

Illustration 16:  SADPOS Control & Solar Array Move Effects on ADACS subsystem 14 Oct 2004

(Other than the rapid increase in pitch while the array was in motion there was not a significant effect.).

Illustration 17:  N16 Selected Power Values during Sun-Moon Eclipse of 14 Oct 2004.

1= SADPOS takes control and moves array offset to zero

2= SADPOS is commanded to backup with SADCS back in control

3=Array offset is commanded back to -40 degrees

Illustration 18:  N17 AVHRR Health Analysis

(Holding steady and hopefully continuing to do so.)

Illustration 19:  N17 Sun-Moon eclipse effects on spacecraft power subsystem

(Note that SADPOS was disabled at JDAY 288.1 (02:15Z)  through 288.2 (04:00Z)

Illustration 20:  N17 Attitude Stability Analysis

(Generally nominal; a little less stable than desired on the Yaw Updates)

# N17 CPU Single Event Upset Scrub Analysis (New).

# Last week and total.

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING October 15, 2004

| DAY/DATE | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 |
| --- | --- | --- | --- | --- | --- |
| FRI. 10/08 | N/A | +032 msec | +004 msec | -027 msec | -017 msec |
| SAT. 10/09 | -088 msec | +033 msec | +006 msec | -027 msec | -018 msec |
| SUN. 10/10 | -089 msec | +034 msec | +003 msec | -027 msec | -019 msec |
| MON. 10/11 | -094 msec | +039 msec | +003 msec | -026 msec | -019 msec |
| TUE. 10/12 | N/A | +040 msec | +002 msec | -027 msec | -017 msec |
| WED. 10/13 | -090 msec | +040 msec | +002 msec | -027 msec | -018 msec |
| THU. 10/14 | -091 msec | +035 msec | +002 msec | -027 msec | -017 msec |

EMOSS POC for this chart is JIM SHEPHERD

NOAA-12  	*Alternating +/- 500 millisecond clock jumps will occur at 76-day intervals as long as fractional second daily ETCUP is utilized to manage clock drift. The next +500 millisecond jump is expected on 11/16/04.

Daily ETCUP bias of +6.5 mSec started on 12/10/03.

NOAA-14:  	As of 1223/03 the TIP clock is corrected daily by –-7.0 msec to compensate for drift.

Subtracted 150 mSecs on 30 June

NOAA-15:  	As of 04/23/03 the TIP clock is corrected daily by –-8 msec to compensate for drift.

Added 100 msec to spacecraft command clock on 31 Aug 04

NOAA-16:  	As of 12/23/03 the TIP clock is corrected daily by –5.5 msec to compensate for drift.

Subtracted 100 msec from spacecraft command clock on 31 Aug 04.

NOAA-17:  	As of 12/23/03 the TIP clock is corrected daily by –3 msec to compensate for drift.

Added 125 Msecs3 Feb 04.

POES Engineering Contact List

Government

Renee Smith-Dearing  NOAA POES Constellation Lead 		301-817-4117

Dong Han:  NOAA, POES Payloads					301-817-4127

Nicolaie Todirita (Todi)  NOAA Ground Systems			301-817-4229

EMOSS-2 Contractor

Jeff Devine: EMOSS POES Lead	 				301-817-4020

Jim Walters:  EMOSS, POES Payload Engineer			301-817-4033

Angelique Riley, EMOSS, POES Comm and DHS (outgoing)	301-817-4028

Carl Gliniak, EMOSS POES Power and Thermal 			301-817-4207

Jim Sheperd, EMOSS POES Attitude Control			301-817-4030

Jon Woodward EMOSS, POES Flight Software C&CS		301-817-4019

Sally House EMOSS POES Payloads (in training)			301-817-4026

William Chadwick EMOSS, POES Comm and DHS (in training)	301-817-4015