POLAR Spacecraft Status As of: Tues 9 Nov 04  16:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM:AN=1646 STIP data only | NOAA-14J AM:AN=2006 STIP data only | NOAA-15K AM:AN=1822 GAC data only | NOAA-16L PM:AN=1424 GAC&LAC data | NOAA-17M AM: AN=2224 GAC&LAC data | NOAA-N18 Planned PM Plan AN=14:00 |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | NET 2/14/05 |
| CNTL OBP | OBP2 | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | Spacecraft Panel |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 | B-BUS XSU-1 | Opening Planned |
| BUS VETO | NO | NO | NO | NO | NO |  |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ SS check Disabled when mode=YGC | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAA Gyro3 TOAR 427 ESA sun glint season | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB Gyro3 TOAR 436 | New ring laser gyro |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mSec +100 mS 31Au04 | PRI Daily Bias –5.5 mS -100 mS 31Au04 | PRI Daily Bias –3 mSec |  |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 |  |
| MIRP | External Synch Rephase Enabled | External Synch Rephase 0730 Daily | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled |  |
| TIP SIDE | 1 | 1 | 2 (since 4/23/03) TOAR 432 Channels 224 -227 invalid, closed | 1 Analog telem drifting TOAR 439 | 1 Analog telem drifting |  |
| DTRs | 3, 4, 5B Safestate 3B since 9 Jun | 1, 2B, 3A, 5 Safestate- 1B | 1, 2, 3, 4 Safestate 1B EOT | 1,2,3,4A Safestate 3A 4B TOAR 418 (STIP only) | 1,2,3,4 Safestate=1B DTR2-SSR DTR5 TOAR 420 | All solid state digital recorders |
| VTX (APT data) | #1 ON 137.50 MHZ | OFF Since 8/14/02 | #1 ON Since 10/20/04 | INOP OFF since 11/15/00 | #2 ON 137.62 MHZ | #1=137.0 MHZ #2=137.0125 MHZ |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #1 137.35 MHZ | #2 137.77 MHZ |  |
| STX #1=1698.0 mhz #2=1702.5 mhz #3=1707.0 mhz #4=2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT No HRPT 30 Oct 14:40-19:40 4-Playback 1,2,3-Degraded | 1 – HRPT; 2– Playback; 4 – Playback 3 low power unused | 3 – HRPT TOAR424 low power 1&2 Playback 4 – TIP |  |
| POWER (Array offset, charge and eclipse states, sun angle) | ArrayOff +50 since 8/31/04 Full Sun Battery UVtrip 7/25 Sun Angle 15 bottomed out Batts 1&2=LRC V/T=4 (26Jul) Shunt degraded SA CANT=37 degs | Array Off -55 Since 8/21/03 Eclipse all year Sun Angle at 38 steady trend Batts 1-3= LRC Batts 1&3V/T=8/11 Batt2 VT=9/11 ) Shunt Degraded SA CANT=22 degs | Array Off -45 Since 1/25/01 Full Sun Sun Angle 11 Start uptrend to 15 in mid-Dec Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 * Eclipse all year *SADPOS anomaly SA moves 10/14 Sun Angle 49 Steady trend Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 68 Steady trend Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs |  |
| AVHRR | Nominal Turned backon 7/28 Chan-2A on 8/3/04 | INOP Scan motor stalled 14 Apr 04 | Nominal Rare major scan motor surges. Last Incident 8/9/03 | ERRATIC Wave patterns and elevated SM current started 23 Oct No bar codes TCE24 OFF 4/14 Chan 3B only. | Nominal 3A-B switch enabled Scan Motor on watch list | New brushless scan motors |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational TOAR 415 on primary PLLO chans 9-14 bias shift. TOAR 417 on Backup PLLO inop | OFF/INOP Since 10/30/03 Inoperable Red in status. Survival heat on. |  |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal |  |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges ,most recent 8/26/04 IPD Reports of degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | ON / INOP Turned on 8/30/04 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | VARIABLE FW mode=Hi Powr FW Heater OFF Frequent Filter Motor current “mini” surges Occasional major FM current surges, most recent 6/3/04 | Operational Occasional major FM surges, most recent 4/29/04 IPD Reports of excess noise in space view channels 21May04 Patch Power investigation | NOMINAL 1 Pixel cross track misalignment . | HIRS-4 replacing HIRS-3 |
| MHS/MIU |  |  |  |  |  | Integrated on spacecraft Replaces AMSUB |
| MSU | ON / INOP Turned on 8/30/04 For power balance Scan Motor OFF since 3/12/03 | Operational Scan motor and antenna problems |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal |  |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational A-side, AGC Mode (B-side in FG mode) 243 MhZ = INOP. | Nominal A-side All AGC Mode |  |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal |  |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Telescopes inoperative | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 |  |
| SBUV |  | Degraded Grating motor stuck at position –930 on 7/8/04 recovery ops successful 7/9 Flex memory 3 (giant step) ops suspended indefinitely on 12/2/03 Reduced operations started 6/5/03 |  | Operational TOAR 435 Degraded Ozone data INACTIVE 11/2/04 Backup Diffuser inop Primary Diffsuer deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode |  |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Autonomous implementation 10/14 | ON ENABLED |  |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 HIRS FW Heat OFF TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 S/C in strong cooling trend | Nominal TCE24 OFF 4/14 (AVHRR H&L) | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 |  |
|  | N12 | N14 | N15 | N16 | N17 | NOAA-N18 |

COMMENTS/CHANGES:

NOAA-12	No changes since the last report that can be discerned from the relatively few passes that N12 has currently been able to

provide.

NOAA-14:	The N14 power situation remained stable during the past reporting period with minimum battery voltages apparently “bottoming out” since the previous report (illustration 1).  The primary driver regarding the N14 power balance is maximum eclipse duration which has now about reached its maximum of 23% of each orbit.   Presently, EMOSS engineers believe that this situation is both manageable and beneficial to the N14 shunts and so, while close monitoring will continue no reconfigurations have been recommended.  Carl Gliniak is EMOSS POC.

EMOSS engineer Jim Walters oversaw the implementation of an operation that will restore Diffuser Reflectivity Measurements to the NOAA-14 SBUV Schedule after this operation was inadvertently removed last year during the grating motor anomaly.  This operation will again run out of stored commands once per week 5 minutes after a terminator crossing into darkness, and run in the dark part of the orbit taking 35 minutes to complete.  It is expected that this operation will be conducted on Thursday in conjunction with other N14 SBUV calibration operations although it can be performed on any day of the week.   The first implementation of this “new” standard operation is planned for Thursday 18 Nov.

NOAA-15: 	The N15 AVHRR and AMSU-B scan motor current were nominal during the past reporting period while the HIRS experienced its usual “mini” filter motor current surges (illustration 2 and 3).

NOAA-16:	The N16 AVHRR scan motor continued to behave erratically during the past week with motor current values averaging 265 mAmps and approaching the 280 value where bar codes are usually observed on imagery.  Conversely, bar codes have not yet been observed on the imagery (although wave patterns have been reported) and, for the first time in nearly two weeks, the synch delta value has stopped “pegging out” on each orbit. (The non-pegged synch delta has the added benefit of not requiring an actual rephase of the MIRP on each orbit thus reducing lost data on other payloads.)  Thermally, AVHRR components are at their highest temperatures ever although the baseplate and scan motor remain well below the 28.5 degrees which would require EMOSS to command TCE24 back on to allow component cooling (illustrations 4-7).  Conversely, the N16 HIRS was very stable during the past week operating at its lowest average filter motor current ever and maintaining its thermal stability as well (illustration 8).

The N16 ADACS was nominal during the past reporting period.  The Earth Sensors continues to exhibit behavior suggestive of direct sunlight entering the detectors (as depicted by the ESA ORS voltages and Sun Moon warning status).  EMOSS engineer Jim Sheperd continues to closely monitor the situation (illustration 9).

NOAA-17:	EMOSS engineers continue to closely monitor the N17 AVHRR scan motor for signs of degraded performance. The

scan motor current on this payload continues to edge slowly higher, beyond that which can be attributed to TIP analog drift, and is now reaching all time high values.  Conversely, imagery and synch delta remain nominal (illustration 10-11).

The ADACS on N17 was also nominal during the past reporting period although slightly less stable (as measured by N16) than is desirable (illustration 12).  Jim Sheperd is EMOSS POC for this issue.

NOAA-N:	Re-testing of end to end test problem areas (SCT and ephemeris loads) are scheduled for tomorrow, 10 Nov.   The

N18 Comm. Panel is expected to be opened following the completion of SEPET testing to examine the S-Band transmitter that demonstrated less than optimum performance during testing.  This examination is expected to result in a launch delay of up to several weeks if it is performed.  EMOSS engineer Jon Woodward updated the latest flight timetable (using the FT Tool) with MHS/MIU commands as well as several other alterations and submitted it to NASA for their review.

MISC:	EMOSS engineers are currently supporting an anomaly investigation that is occurring at Fairbanks CDA.  Since 8 Nov,

neither the SOCC or Fairbanks  (in normal mode) have been able to load large block files (i.e. Stored Command Table) into any spacecraft at the Fairbanks CDA.  Single commands and simple loads (such as ephemeris) have been successfully loaded at Fairbanks since this problem started and large loads to POES spacecraft have been successful at Wallops (and all such loads have been moved to Wallops until this situation has been resolved).  At the present time, spacecraft hardware has been discounted as a source of the problem and the current focus is on possible problems with the S-band command generator (VHS transmitted command loads do work at Fairbanks) or the Comm Controllers.

On 4 Nov, EMOSS engineer Jon Woodward reset all KLM (N15, 16 and 17) STESM tables to ensure that only Gyro 1 and 2 for these spacecraft are powered on and gyro-3 remains powered off (which the previous STESM would have turned on if implemented).  These operations all completed nominally.

EMOSS engineers have initiated page comparisons for a new CWS software release.  Account difficulties and system problems have resulted in delays for completing this process.  Currently, COB Friday, 12 Nov is the deadline for completion, assuming everything works nominally.

Illustration 1:  N14 Power Subsystem Analysis

(Battery voltages appear to have stabilized recently and everything looks nominal)

Illustration 2:   N15 Payload Motor Health Analysis

(All within nominal or typical values and profiles)

Illustration 3:   N15 HIRS Health Analysis

(Nothing unusual for this HIRS.)

Illustration 4:  N16 AVHRR Scan Motor Health Analysis

(Not especially auspicious.)

Illustration 5:  N16 Synch Delta Analysis

(No longer “pegging out” and MIRP rephase is not occurring during South Pole enable operation.)

Illustration 6:  N16 AVHRR Thermal analysis.

(Warm as its ever been and getting warmer still.  TCE24 remains off in order to maintain warmer temperatures.)

Illustration 7:  N16 AVHRR Imagery Analysis

(No apparent degradation, not even the lost frame of data when MIRP rephase enabled occurs over the South Pole.  Reports of wave patterns have been received by EMOSS.)

Illustration 8:  N16 HIRS Analysis

(Stable.)

Illustration 9:  N16 ADACS Health Analysis

Nominal with sun glint still in ESA detector on each rev.

Illustration 10:  N17 AVHRR Health Analysis

(Holding steady to slightly higher.)

Illustration 11:  N17 Synch Delta Analysis

(nominal and steady)

Illustration 12:  N17 Attitude Stability Analysis

(Generally nominal)

# N17 CPU Single Event Upset Scrub Analysis

# Last week and total.

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING November 5, 2004

| DAY/DATE | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 |
| --- | --- | --- | --- | --- | --- |
| FRI. 10/29 | -096 msec | +046 msec | -009 msec | -018 msec | -019 msec |
| SAT. 10/30 | -099 msec | +047 msec | -009 msec | -017 msec | -020 msec |
| SUN. 10/31 | -098 msec | +051 msec | -010 msec | -018 msec | -019 msec |
| MON. 10/01 | -097 msec | +049 msec | -011 msec | -018 msec | -017 msec |
| TUE. 10/02 | -099 msec | +045 msec | -012 msec | -018 msec | -017 msec |
| WED. 10/03 | -100 msec | +051 msec | -013 msec | -013 msec | -017 msec |
| THU. 10/04 | -100 msec | +052 msec | -015 msec | -014 msec | -017 msec |

EMOSS POC for this chart is JIM SHEPHERD

NOAA-12  	*Alternating +/- 500 millisecond clock jumps will occur at 76-day intervals as long as fractional second daily ETCUP is utilized to manage clock drift. The next +500 millisecond jump is expected on 11/16/04.

Daily ETCUP bias of +6.5 mSec started on 12/10/03.

NOAA-14:  	As of 1223/03 the TIP clock is corrected daily by –7.0 msec to compensate for drift.

Subtracted 150 mSecs on 30 June

NOAA-15:  	As of 04/23/03 the TIP clock is corrected daily by –8 msec to compensate for drift.

Added 100 msec to spacecraft command clock on 31 Aug 04

NOAA-16:  	As of 12/23/03 the TIP clock is corrected daily by –5.5 msec to compensate for drift.

Subtracted 100 msec from spacecraft command clock on 31 Aug 04.

NOAA-17:  	As of 12/23/03 the TIP clock is corrected daily by –3 msec to compensate for drift.

Added 125 Msecs3 Feb 04.

POES Engineering Contact List

Government

Renee Smith-Dearing  NOAA POES Constellation Lead 		301-817-4117

Dong Han:  NOAA, POES Payloads					301-817-4127

Nicolaie Todirita (Todi)  NOAA Ground Systems			301-817-4229

EMOSS-2 Contractor

Jeff Devine: EMOSS POES Lead	 				301-817-4020

Jim Walters:  EMOSS, POES Payload Engineer			301-817-4033

Angelique Riley, EMOSS, POES Comm and DHS (outgoing)	301-817-4028

Carl Gliniak, EMOSS POES Power and Thermal 			301-817-4207

Jim Sheperd, EMOSS POES Attitude Control			301-817-4030

Jon Woodward EMOSS, POES Flight Software C&CS		301-817-4019

Sally House EMOSS POES Payloads (in training)			301-817-4026

William Chadwick EMOSS, POES Comm and DHS (in training)	301-817-4015