POLAR Spacecraft Status As of: Tues 24 July 07, 17:00 EST

(Changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM 16:59=AN STIP data only No IPD processing | NOAA-15K AM: 17:49=AN GAC data only | NOAA-16L PM: 15:04=AN GAC&LAC data | NOAA-17M AM: 22:23=AN GAC&LAC data | NOAA-18N PM 13:49=AN GAC & LAC data |
| --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 Recursive SCT | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU-1 | B-BUS XSU-1: TOAR444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO |
| ADACS | Nominal Mode Autonomous swap to YGC 30 Aug 06, commanded back to nominal 31 Aug RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | RGYRO Mode Estimate Y-ROLL Rgmode=PASSIVE Gyros-1 & 3 Inop/Off Gyro chans XA-ZB Pitch wheel bias 2400 Gyro2 safe macro | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB GAS Enabled Dec 05 | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447 Z-momentum transition complete Pitch Torquer again active |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI daily bias -8 mS -500 mS 12/31/05 | PRI Daily Bias –5.5 mS -1500 mS 31Dec05 | PRI Daily Bias –3 mS -1500 mS 31Dec05 | PRI No daily bias -1500 mS 31Dec05 |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 2 (since 4/3/03) 3 channels inop | 2 since 4/18/05 (analog drifting?) | 2 Swapped 9/20/06 | 1 Analog telem drifting |
| Recorders (DTR, SSR) | DTRs 3A, 4, 5B Safestate 5B 4b low pressure | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=SSR 2B 4A Pressure leak | SSRs 1,2,3,4,5 Safestate=5B Current spikes |
| VTX (APT data) | #1 ON 137.50 MHZ | #1 ON As of 19 June 07 | OFF / INOP since 11/15/00 | #2 ON 137.62 MHZ | #2 ON 137.9125 MHZ |
| BTX | #1 136.77 MHZ | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ |
| STX 1 = rcp 1698.0 mhz 2 = lcp 1702.5 mhz 3= rcp 1707.0 mhz 4= rcp 2247.5 mhz | 1 – HRPT; 2,3 - Playback | 2-Omni HRPT 2 Omni=rcp Power TOAR 446 4-Playback 1,2,3-Degraded | 2 – HRPT 1– Playback 4 – Playback & MCM usage 3 low power unused | 3 – HRPT TOAR424 low power 2 & 1 Playback STX-1 Power drop STX-4 no modulation | 1 - HRPT 3 - Playback 2-Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, eclipse states and sun angle) | ArrayOff -60 since 5/23/07 Full Sun Sun Angle 16 uptrend to 20 in early Jan 07 Shunt degraded SA CANT=37 degs PSSS trigger =18.5 | Array Off -45 Since 1/25/01 Full Sun Sun Angle 13 Uptrend to 18 early Jan 07 SA CANT=37 degs BVR Phase Control auton swap 7/19/07 | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 34 Steady trend SA CANT=22 degs Transitioning to full sun S/C in Sept 07 | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 66 Steady trend SA CANT=37 degs | Array Off. -40 Since 6/6/05 Eclipse all year Sun Angle 63 uptrend to 65 on 1 Jan 07 SA CANT=22 BVR Phase Control auton swap 3/29/06 & 1/4/07 |
| AVHRR | Nominal HRPT and APT data only | Nominal Channel 3B only Occasional minor scan motor instabilities | Nominal Recent SM current increases TCE24 OFF 4/14/04 Channel 3B only | Nominal 3A-B switch enabled Previous scan motor current mini surges | Nominal Channel 3B only Scan motor current drop 29 Aug 06 |
| AMSU-A1 |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Full Scan mode |
| `AMSU-A2 |  | Nominal | Nominal | Nominal | Nominal |
| AMSU-B |  | Operational Bias in All Chans. Degraded Chan-3 | Operational Space Position-3 Chan-8 degradation | Nominal | Replaced by MHS |
| HIRS | ON/Inop Turned On 4/30/05 for power balance Filter Wheel OFF | NOMINAL FW Abrupt return to nominal 7/12/05 After years of minor and major current surges FW mode=Hi Powr | NOMINAL New all time high filter motor current reached 9/17/06. Imagery occasionally exhibits high levels of radiometric noise | NOMINAL 1 Pixel cross-track misalignment. | Operational Filter Heat OFF. LW channel 1-12 noise TOAR 448 Loose LWIR lens. LW imagery erratic. |
| MHS/MIU |  |  |  |  | Nominal Fly Wheel Motor Current Spiking but not alarming since 27 Dec 06 Entered Motor Spin State on 27 March 07 |
| MSU | ON/Inop Turn on 7/9/07 for power balance |  |  |  |  |
| SSU |  |  |  |  |  |
| DCS RFI investigation | Nominal | Nominal | Nominal Pseudo message turned on 1/5/06 | Nominal | Nominal DRU’s 1-7 On DRU8 inop/off |
| SARR |  | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | Nominal A-Side All AGC Mode Since 15 Aug 05 |
| SARP |  | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | Nominal A-side 23 May05 |
| SEM | ON/Nominal Autonomous reset 8 Jun 06, back to nominal 10 June Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 TED level=3 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=6 P-CDEM-HVPS=5 27 Jun 0615:30z | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=4 27 June 06 16:00z | Nominal Elec-CH-HVPS=1 27 June 06 17:00z Prot-CH-HVPS=0 |
| SBUV |  |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops TOAR 463 sun glint IBSL test performed 12 Sept 06 Grating motor investigation | Nominal Anode mode since 6 July 05 13:30z Electronics turnoff taken out of STESM safestate table TOAR 462 sun glint |
| SADPOS |  |  | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer =12 mins |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | TCE26 & 15H Telem valid TOAR 432 closed TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 Spacecraft in thermal uptrend | Nominal TCE24 OFF 4/14/05 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 AMSU-A1 survival heaters on 10/29/03 | All TCE’s active HIRS filter heater turned OFF 9/28/06 |

COMMENTS/CHANGES:

NOAA-12:	There were relatively no changes to the rest of the NOAA-12 health situation during the past week.  MSU power balance appears to continue to hold stable at the motor's turn on temperature of 70 C.

NOAA-15:	There were relatively no changes to the NOAA-15 health situation during the past week.

NOAA-16: 	There was relatively no change in the performance of the NOAA-16 payload subsystems during the past week and the rest of the spacecraft subsystems were also nominal during this time.

The BVR Phase Controller switched from Primary to Back-up on 19 July 2007 at 18:11z.  See Figures 1 & 2.  There was no apparent cause for the switch.  There have been 2 other switches on NOAA-18 on 3/29/06 & 1/4/07, but never one on NOAA-16. A TOAR is being submitted.  The BVR Phase Controller was commanded back to the primary side on 20 July 2007 @ 20:12z.  There has been no repeat of the switch.

NOAA-16 will be in full sunlight beginning in mid-September.  This is the first time ever it will not be eclipsing.

NOAA-17: 	There was relatively no change in the performance of the NOAA-17 payload subsystems or health and safety during the past week.

HIRS channel 1 period monitor is looking a little noisy and brushing the limit values. The limits are being analyzed to determine if they should be backed off a few counts to allow for the spikes in telemetry this point experiences on a regular basis. .

No updates or conclusion were reached about the Attitude disturbance last week on 17 July 2007.  The investigation will continue. .

NOAA-18:	There were relatively no changes to the NOAA-18 health situation during the past week.

AMSU-A1 motor 2 current spikes (around lower latitudes) magnitudes have begun decreasing. It appears to have seasonal coupling. This is under monitor for changes along with the related position reference count points.

MetOp A:	Here is a summary of the MetOp-A issues over the past week and upcoming events as provided by Eumetsat engineers:

- The ADCS and SARR analog telemetry showed a slight drop in temperature on July 20 – 21, but recovered on July 22.  This temperature decrease is time correlated with the IASI Heater-Refuse anomaly that occurred on July 20 @ 04:30 UTC, but the ADCS and SARR units are accommodated on different panels than the IASI units and separated by the internal structure of the PLM.

- The SEM DPU analog telemetry showed a significant drop in temperature (approx. 4 deg C) on July 20-21, but recovered on July 22.  This temperature decrease is time correlated with the IASI Heater-Refuse anomaly that occurred on July 20 @ 04:30 UTC.  Although the SEM DPU is accommodated on a different panel than the IASI units, it is in the same internal compartment of the PLM structure and the drop in temperature seems explainable.

- The AMSU instruments’ Digital A telemetry showed a slight increase in temperature during the first half of the week and then a decreasing trend through the second half of the week.  This only amounted to 0.2-0.3 K and is not very significant.  The NEdT values are stable for all channels and well within specification.

- The SARR analog telemetry showed a slight drop in temperature on July 20-21.  This temperature decrease is time correlated with the IASI Heater-Refuse anomaly that occurred on July 20 @ 04:30 UTC.  The SARR units are accommodated internally in the PLM in close proximity to the IASI units.

- HIRS Filter Wheel resyncs have remained at the same rate as reported last week (approximately once every 92 seconds).

- Investigation of the HRPT transmitter failure continues.

Figure 1 NOAA-16 Battery Voltage Regulator Phase Controller (2007/199@23:27z-200@23:27z)

Figure 2 NOAA-16 Battery Voltage Regulator Phase Controller (zoomed in to anomaly time)