POLAR Spacecraft Status As of: Tues July 19, 15:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM: 1651=AN STIP data only | NOAA-14J AM: 2039=AN STIP data only | NOAA-15K AM: 1806=AN GAC data only | NOAA-16L PM: 1441=AN GAC&LAC data | NOAA-17M AM: 2225=AN GAC&LAC data | NOAA-18N Trans PM 14:00=AN APT/HRPT/GAC |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 XSU1 TOAR 444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ SS check Disabled when mode=YGC | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAA | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB Gyro-2 current spike under investigation | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447 |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS +100 mS 31Aug04 | PRI Daily Bias –5.5 mS -100 mS 31Aug04 | PRI Daily Bias –3 mS | PRI 23 May05 |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Rephase 0730 Daily | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 1 | 2 (since 4/23/03) 3 Channels inop | 2 since 4/18/05 | 1 Analog telem drifting | 1 |
| Recorders (DTR, SSR) | DTRs 3A, 4, 5B Safestate 5B | DTRs 1, 2B, 5 Safestate- 1B | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=DTR 1B | SSRs 1,2,3,4,5 Current spikes TOAR 450 |
| VTX (APT data) | #1 ON 137.50 MHZ | OFF Since 8/14/02 | #1 ON 137.50 MHZ | INOP OFF since 11/15/00 | #2 ON 137.62 MHZ | #2 ON 137.9125 MHZ |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ |
| STX #1=1698.0 mhz #2=1702.5 mhz #3=1707.0 mhz #4=2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT Power drop TOAR 446 4-Playback 1,2,3-Degraded | 1 – HRPT; 2– Playback; 4 – Playback 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 Power drop TOAR 443. | 3 - HRPT 1&2 Playback STX1&3 swapped 28June05 4-Standby |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) | ArrayOff +60 since 6/23/04 Eclipse season 21Apr-17Aug Sun Angle 36 downtrend to 12 mid-Oct 05 Batts 1&2=LRC Batt !&2 V/T=4 Shunt degraded SA CANT=37 degs | Array Off -55 Since 8/21/03 Eclipse all year Sun angle 51 Steady trend Batts 1-3= LRC Batts 1&3V/T=7/11 Batt2 VT=8/11 SS trigger =18.98 Shunt Degraded SA CANT=22 degs | Array Off -45 Since 1/25/01 Eclipse Season 16 May-23 Jul Sun Angle 30 downtrend to 2 degs on 10 Oct 05 Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 58 Start downtrend to 41 on 30 Oct 05 Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 70 Steady trend Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs | Array Off. -40 Since 6/6/05 Eclipse all year Batts 1-3=LRC Batts 1-3 V/T=4/8 SA CANT=22 PSSS enabled 30May |
| AVHRR | Nominal | INOP Scan motor stalled 14 Apr 04 | Nominal Rare major scan motor surges. Last Incident 11/18/04 | Degraded TCE24 OFF 4/14/04 Bar coded imagery since 29June05 Channel 3B only. | Nominal 3A-B switch enabled | Nominal 3A-B switch Enabled 6/23/2005 |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Space view 1 Since 6/7/05 |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal | Nominal Space view-2 since 6/08/05 |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 IPD Reports of degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | OFF/Inop Turned off 6/23/05 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | NOMINAL Upgraded to Yellow status 16 May 05 FW Abrupt return to nomial at 09:00Z TOAR 445 CLOSED 12 July 05 FW mode=Hi Powr FW Heater OFF Frequent Filter | Operational High levels of imagery radiometric noise TOAR 441 open Occasional major FM surges, most recent 12/9/04 | NOMINAL 1 Pixel cross track misalignment . | ON TOAR 448 Noise in long wave channels 1-12. Some improvement reported. Investigation ongoing Tested in high power mode 12 July |
| MHS/MIU |  |  |  |  |  | Nominal Final config on 6/4 Now Operational |
| MSU | OFF/Inop Turned off for power balance 6/23/05 | Operational Scan motor and antenna problems |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal | ON DRU’s 1-7 On DRU-8 TOAR 449 turned off 6/13 |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | ON A-Side 121, 243, 406 FIXED GAIN MODE Since 18 Jul 05 |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | ON A-side 23 May All DRU’s on |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Tscopes inop | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 | ON Turned on 6 June at 14:05z |
| SBUV |  | Degraded Grate motor sticks Flex memory 3 (giant step) ops suspended 12/2/03 Reduced operations |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops Procedure changes forthcoming | ON Anode mode since 6 July 13:30z OV testing continues |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer changed to 12 minutes 12July |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 HIRS FW Heat tuned ON 17 Apr and OFF on 18 Apr TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 | Nominal TCE24 OFF 4/14 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 | All TCE’s active |
|  | N12 | N14 | N15 | N16 | N17 | N18 |

COMMENTS/CHANGES:

NOAA-12	No change from last week although the N12 battery’s maximum discharge voltage continue to slowly trend upward

during the past week in conjunction with the continued waning of eclipse season (expected to end completely in mid-August). Additional reconfigurations are anticipated for the N12 power subsystem in the coming weeks that may include turning HIRS and MSU back on and moving the solar array offset.  Specific operations are not yet defined.  Carl Gliniak is EMOSS POC for this situation.

NOAA-14:	No changes since previous report.  Power balance remains stable with no problems detected during the past week.

NOAA-15:	The N15 AMSU’s, AVHRR and HIRS were all nominal and stable last week (illustration 1).  N15 continues progressing nominally through its eclipse season (illustration 2) which is now waning and expected to end late this week or early next week.  No power subsystem reconfigurations are expected.

NOAA-16:	The N16 AVHRR scan motor current was stable to slightly higher during the past week (illustration3) while its synch

delta remained generally pegged most of the time and a large percentage of its imagery continued to produce bar code noise (illustration 4).  Otherwise N16 payloads were generally nominal and stable during the past week (Illustration 5) as were the remainder of N16 subsystems.

In order to support the N18 pitch oscillation (TOAR 447) investigation, at NASA request, EMOSS engineer Carl Gliniak configured the spacecraft to dwell on the SA Boom movements (NSADPLY) for one orbit on 19 July at 14:45z before configuring the dwell back to Bus Voltage at 17:50z.  This operation completed nominally.

NOAA-17:	EMOSS continues closely monitoring the N17 gyro-2 spin motor current which was generally stable during the past

week (illustration 6).  That stability notwithstanding, to bring more attention to bear on the N17 gyro situation, EMOSS POC Jim Sheperd submitted TOAR 451 on this component because of its recent instabilities.  Otherwise, there was no change in N17 last week with all payloads operating in a nominal fashion (illustration 7).

N17 SBUV standard operations will be altered in the near future.  One change will replace the SOMS proc TUESF1DS with SBFLX1DS for Tuesday SBUV schedules (with relative timing retained). Previously the SBUV was placed in sweep mode every Tuesday for 14 orbits.  The SOMS proc TUESF1DS was created to replace SBFLX1DS on Tuesdays.  It includes commanding to ensure the SBUV would go to sweep mode when it completed.  Now we only want to keep the SBUV in sweep mode for 4 orbits on Tuesdays, so the extra commands in TUES1FDS erroneously place us in sweep mode.  Jim Walters is POC

A second N17 SBUV change occurs on the first Saturday of every month when the SBUV will go into cathode mode for four orbits.  These four orbits are to be chosen such that the daylight portion of the orbit does not fall on the continental US.  The SOMS procedure used to implement this is SATCATH.PRC.  The version of this proc to be used is the 11 July 2005 version.  Previously, the earlier version of SATCATH.PRC placed the SBUV in cathode mode for 14 orbits, and not the desired 4 orbits.  Jim Walters is POC

As with N16, in order to support the N18 pitch oscillation (TOAR 447)  investigation, at NASA request, EMOSS engineer Carl Gliniak configured the spacecraft to dwell on the SA Boom movements (NSADPLY) for one orbit on 19 July at 15:30z before configuring the dwell back to Bus Voltage at 18:30z.

NOAA-18:	Some OV testing and reconfigurations continue for N18 primarily those in support of TOAR investigations.  On 19

July at 13:30z, EMOSS engineer Jon Woodward oversaw an operation that Replaces Euler attitude angle errors in the SCP1 CPU telemetry table 1 with that of MIMU raw gyro data.  This state will be maintained until 20 July at 19:30z and is being conducted to provide notch filter testing for pitch angle noise in support of TOAR 447 (excess pitch oscillation).

The final planned OV test concerns that of the SARR which on 18 July at 20:05z had its 121, 243, and 406 receivers switch to fix gain mode (from AGC mode.)  Will Chadwick was EMOSS POC for planning the operation and Jim Walters oversaw its execution.  This configuration is expected to last 1-2 weeks after which it will be placed back into AGC mode for nominal operations.  There is no illustration for this operation because of an ABE data gap that occurred just prior to its implementation.

See illustrations 8-12 for a summary of N18 performance over the past week.

Illustration 1:  N15 Payload Motor Current Analysis:

(Nominal and stable)

Illustration 2:  N15 EPS Analysis

(Nominal and improving)

Illustration 3:  N16 AVHRR Scan Motor Analysis

(Just a little worse than last week.)

Illustration 4:  N16 AVHRR Imagery & Synch Delta Analysis

(No better than last week.)

Illustration 5:  N16 Payload Motor Current Analysis

(Nominal and stable)

Illustration 6:  N17 ADACS Analysis

(Generally nominal and stable but not as much as desired)

Illustration 7:  N17 Payload Motor Current Analysis

(Nominal and stable)

Illustration 8:  N18 Payload motor current analysis

(Nominal and stable.  Note the big rise during HIRS high power mode operation and the lower value that it stabilized at after returning to low power.)

Illustration 9:  N18 MHS Health Analysis (ABE data)

(Generally nominal and stable.  Spike filtering in place within Greta process for MHS)

Illustration 10:  N18 EPS Health Analysis

(Nominal and stable.)

Illustration 11:  N18 DHS/Comm Health Analysis

(Nominal and stable except for a few DDR current spikes)

Illustration 12:  N18 ADACS Health Analysis

(About the same as last week and last month)

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING July 15, 2005

| DAY/DATE | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 | NOAA-18 |
| --- | --- | --- | --- | --- | --- | --- |
| FRI. 07/08 | -276 msec * | +211 msec | -217 msec | +128 msec | +071 msec | -059 msec |
| SAT. 07/09 | -277 msec * | +212 msec | -216 msec | +128 msec | +071 msec | -058 msec |
| SUN. 07/10 | -277 msec * | +213 msec | -218 msec | +133 msec | +070 msec | -058 msec |
| MON. 07/11 | -278 msec * | +211 msec | -218 msec | +133 msec | +072 msec | -057 msec |
| TUE. 07/12 | N/A | +212 msec | -218 msec | +134 msec | +072 msec | -056 msec |
| WED. 07/13 | -281 msec * | +213 msec | -219 msec | +133 msec | +072 msec | -057 msec |
| THU. 07/14 | -281 msec * | +213 msec | -222 msec | +134 msec | +072 msec | -054 msec |

EMOSS POC for this chart is JIM SHEPHERD

NOAA-14:  As of 12/23/03 the TIP clock is corrected daily by –7.0 msec to compensate for drift.

NOAA-15:  As of 04/22/03 the TIP clock is corrected daily by –8.0 msec to compensate for drift.

NOAA-16:  As of 12/23/03 the TIP clock is corrected daily by -5.5 msec to compensate for drift.

NOAA-17:  As of 12/23/03 the TIP clock is corrected daily by –3.0 msec to compensate for drift.

NOAA-12:  As of 12/10/03 the TIP clock is corrected daily by +6.5 msec to compensate for drift.

*    A clock jump of +500 milliseconds on 01/31/05 due to fractional second daily ETCUP. A clock

jump of +500 milliseconds on 04/17/05 due to fractional second daily ETCUP. Alternating +/-

500 millisecond clock jumps will ccur at 76-day intervals as long as fractional second daily

ETCUP is utilized to manage clock drift. The next +500 millisecond jump is expected on 07/02/05.

POES Engineering Contact List

Government

Renee Smith-Dearing  NOAA POES Constellation Lead 		301-817-4117

Dong Han:  NOAA, POES Payloads				301-817-4127

Micky Fitzmaurice:  NOAA, POES Bus, IJPS	 	    	301-817-4016

Nicolaie Todirita (Todi): NOAA Ground Systems			301-817-4229

EMOSS-2 Contractor

Jeff Devine: EMOSS POES Lead	 				301-817-4020

Jim Walters:  EMOSS, POES Payload Engineer			301-817-4033

Carl Gliniak, EMOSS POES Power and Thermal 			301-817-4207

Jim Sheperd, EMOSS POES Attitude Control			301-817-4030

Jon Woodward EMOSS, POES Flight Software C&CS		301-817-4019

Sally House EMOSS POES Payloads 				301-817-4026

William Chadwick EMOSS, POES Comm and DHS			301-817-4015