(IWM – 8) Gross Crop Irrigation Water Requirement GUIDE

| Steps to Calculate the Crop Irrigation Water Requirement | Enter Results | Example Calculation (Alfalfa) | Results | NM IWM Manual References & Notes: |
| --- | --- | --- | --- | --- |
| STEP 1 | Fc = ECe(ct)/ECiw Fc = Ratio of the Crop Threshold Salinity (ECe(ct) ) to the Electrical Conductivity of irrigation water (ECiw). Units: dS/m |  | Fc = 2.0/1.0 = Alfalfa ECe(ct) = 2.0 dS/m ECiw = 1.0 dS/m | 2.0 | Crop Salt Tolerance Table for NM Irrigation Water Quality Sampling |
| STEP 2 | LF = 0.3086/Fc1.702 LF = Leaching Fraction (for conventional irrigation; e.g. surface irrigation). |  | LF = LF = 0.3086/2.01.702 LF = 0.3086/3.254 | 0.095 | Salinity Assessment GUIDE for Selected Crops |
| STEP 3 | NIR = ETc/(1 – LF) NIR = Net Irrigation Requirement (in.) ETc = Crop Evapotranspiration (in.) |  | NIR = NIR = 40.01/(1 – 0.095) NIR = 40.01/0.905 ETc = 40.01 inches for Alfalfa | 44.21” | NM Crop Consumptive Use Requirements (NRCS FOTG – Section 1: Irrigation Guide for NM) |
| STEP 4 | Ea = Irrigation needed (in.) ÷ Irrigation applied (in.) Ea = Irrigation Application Efficiency |  | Ea = Ea = 2.06/2.5 2.06” (Irr. needed) ÷ 2.5” (Irr. applied) Irr. applied: 7.5 (cfs) x 2.0 (hrs.) ÷ 6.0 (acres) = 2.5” applied. | 0.824 (82.4%) | Irrigation Water Req. Guide (e.g. 3’ root zone & Silt Loam soil @ 10% LF = 2.06” needed) QT = DA Calculations for Assessing IWM Requirements |
| STEP 5 | Fg = NIR/Ea Fg = Gross Irrigation Application needed |  | Fg = Fg = 44.21/0.824 | 53.7” | The calculation of Fg is used in the Planning & Design of Irrigation Systems and the development of IWM Plans |
| STEP 6 | (# Irr. /yr.) x (in. applied/Irr.) = Total in. applied/ac./yr. (Note: in. applied/Irr. is based on an avg.) |  | 13 Irrigations x avg. of 2.5”/Irr. = (e.g., Irrigated field approximately every 2-wks on a fixed schedule (Apr. – Oct.) | 32.5” | Amount of Irr. Water applied can differ substantially from the planned Gross Irrigation application needed |
| STEP 7 | Fg – (Total in. applied/ac./yr.) = (Note: evaluate reason(s) for the difference between Fg & Total in. applied/ac./yr.) |  | 53.7” (Fg) – 32.5” (Total in. applied/ac./yr.) = | 21.2” | In this example, it is clear that consumptive use is not being met. |
| ECe(ct) is taken from a soil saturation extract & the ECiw value is taken from a water test (EC units: dS/m = mmhos/cm = mS/cm). | The LF equation used for High Frequency Irrigation is: LF = 0.1794/Fc3.0417 (e.g. Drip irrigation) rudy garcia 2008 |