MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A10110 | In-Flight Anomaly Number -- | Contractor Report Number E-101-3 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title TRANSDUCER OUTPUT SIGNAL HAD ELECTRICAL NOISE |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT 1 | Sys_Lvl N | Misc Codes A (4) B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE LH2 ULL PRES TRNSDCR | PART# PD7400098-039 | SER/LOT# 1455 | MANUFACTURER GULTON |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE LH2 ULL PRES TRNSDCR | PART# PD7400098-039 | SER/LOT# 1455 | MANUFACTURER GULTON |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode UC - UNSAT | Cause ETE - EI-TEST-ENVR |
| System ELECTRICAL | Defect CN - CONTAM | Material C - EEE | Work Contact J. ADAMS | Fail Date 05/15/1986 |
| Received at MSFC 07/01/1986 | Date Isolated -- | FMEA Reference 3.4.1.2 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location GULTON | Symptom EVM - CON/MEG FAIL | Time Cycle -- |
| Effectivity Text LWTS 16, 20, 21, 22, 24/SUB |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 02/14/1995 | CN RSLV SBMT 02/23/1987 | Defer Date -- | Add Date -- | R/C Codes 2 - MFG -- -- |
| Assignee |
| Design P. MULLER | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| Approval |
| Design P. MULLER | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete JE | MSFC Closure Date 11/06/1987 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description REF: MARS T-10487 AND CAPS E-091 AND E-082. THE TRANSDUCER EXCEEDED THE MAXIMUM ALLOWABLE WIPER-TO-ELEMENT CONTACT RESISTANCE OF 25 OHMS AT SEVERAL POINTS IN ITS PRESSURE RANGE. THE HIGHEST MEASURED RESISTANCE WAS 258 OHMS |
| Contractor Investigation/Resolution R/A: ADDITIONAL INSPECTION STEPS HAVE BEEN ADDED TO REDUCE THE FREQUENCY OF OCCURENCE. 7/1/86 LAUNCH CONSTRAINT - NONE - TRANSDUCERS MUST PASS ATP AT VENDOR AND ARE THEN TESTED WHEN INSTALLED INTO TANK AT MAF. TRANSDUCER IS TO BE RETURNED TO MMC/MAF FOR FA. 8/21/86 PRB STATUS - TWO ADDITIONAL NOISE FAILURES ON -039. FAILURE ANALYSIS TO BE CONDUCTED ON THE ADDITIONAL FAILURES. 9/18/86 PRB STATUS - FA COMPLETE FAILURE CAUSED BY MICROSCOPIC CONTAMINATION. CONSIDERED NORMAL PRODUCTION FALLOUT. NO CORRECTIVE ACTION PLANNED. ECD 10-31-86 10/16/86 PRB STATUS - CONTAMINATION IDENTIFIED AS FRICTIONAL POLYMERS WHICH IS INHERENT TO MANUFACTURING PROCESS. FAILURE IS CONSIDERED NORMAL PRODUCTION FALLOUT. ECD AT MMC IS 11-7-86. 1/29/87 PRB STATUS - CLOSURE IN WORK. CAPS ECD 1-30-87. 2-23-87 - CORRECTIVE ACTION HAS ALREADY BEEN OBTAINED AS PART OF CAPS E-082. AS A RESULT OF THE FAILURES DOCUMENTED IN CAPS E-082, ADDITIONAL MARTIN MARIETTA PROCUREMENT QUAILTY MANDATORY IN- SPECTION POINTS WERE ADDED TO THE VENDORS MANUFACTURING DOCUMENTATION. THE INSPECTIONS INCLUDE: 1) EXAMINATION OF THE WIPER AND OF THE RESISTIVE ELEMENT FOR SURFACE FINISH, AND 2) EXAMINATION OF THE COMPLETED INTERNAL MECHANISM FOR ASSEMBLY AND CLEANLINESS JUST PRIOR TO INSTALLATION OF THE CASE. THE INSPECTIONS SERVE TO REDUCE THE FAILURE RATE OF THE TRANSDUCERS. THIS TASK HAS BEEN COMPLETED AND DOCUMENTED IN CAPS E-082. CAPS E-082 REMAINS OPEN DUE TO ADDITIONAL IN- VESTIGATIONS OF FAILURE DUE TO SHORTED TURNS. THIS PROBLEM IS SUBMITTED TO MSFC FOR CLOSURE REVIEW AND APPROVAL |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A10110 | IFA# -- | Contractor RPT# E-101-3 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD7400098-039 | Asmnt Part Name LH2 ULL PRES TRNSDCR | Asmnt Serial/Lot# 1455 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD EIC - EI-CONTAM | FAIL MODE UC - UNSAT |
| Asmnt FMEA 3.4.1.2 | Asmnt FM 2 | FMEA CSE G | FMEA SCSE 1 |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |