| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 2 to Document 41-E |
|  | 22 August 2007 |
|  | Original: English |
| Asia-Pacific Telecommunity Administrations |
| common proposals for the work of the conference |
| Agenda item 1.2 |

1.2	to consider allocations and regulatory issues related to the Earth exploration-satellite (passive) service, space research (passive) service and the meteorological satellite service in accordance with Resolutions 746 (WRC-03) and 742 (WRC-03)

Introduction

# 1	Resolution 746 (WRC-03)

resolves

“1	to invite ITU-R to conduct sharing analyses between geostationary meteorological satellites operating in the space-to-Earth direction and the fixed, fixed-satellite and mobile services in the band 18-18.4 GHz to define appropriate sharing criteria with a view to extending the current 18.1-18.3 GHz geostationary meteorological satellites allocation in the space-to-Earth direction to 300 MHz of contiguous spectrum;”

An expansion of the current meteorological-satellite service (MetSat) allocation is desirable as the next-generation geostationary MetSat systems are expected to have bandwidth requirements up to 300 MHz. A primary allocation to the geostationary MetSat (space-to-Earth) exists already in the band 18.1-18.3 GHz based on RR No. 5.519.

In order to secure the necessary frequency spectrum for the next-generation geostationary meteorological satellite (MetSat) systems, APT supports extension of the existing 18 GHz MetSat allocation by 100 MHz. However, existing services (FS, FSS including feeder-links for the BSS Plan (Regions 1 and 3) and MS) must be protected from harmful interference due to the possible extension of the MetSat allocation.  Additionally, extending the ±8° coordination arc currently applicable to FSS networks in this band, to the MetSat in the band 18.1-18.4 GHz is appropriate. This could be accomplished through appropriate modifications to Table 5-1 in RR Appendix 5.

# 2	Resolution 742 (WRC-03)

resolves

1	“to invite ITU-R to conduct sharing studies between the passive services and the fixed and mobile services in the band 36-37 GHz in order to define appropriate sharing criteria;”

This agenda item addresses sharing between the Earth exploration-satellite service (passive) and the space research service (passive), and the fixed service and the mobile service in the band 36-37 GHz.  Sharing scenarios have been analysed and mitigation techniques have been identified, leading to possible technical limits to allow sharing.

With respect to the sharing criteria between active and passive services in the bands 36-37 GHz, the protection of passive services should not place additional undue constraints on other allocated services. Sharing criteria should be appropriately defined based on the results of the ITU-R studies. Single-entry emission limits taking into account the results of the compatibility analysis and the sharing criteria are proposed to be included in the RR. These limits would be non-retroactive for the terrestrial active systems notified or brought into use before a date [to be decided by WRC-07]. Possible modifications to the Radio Regulations are shown below. Resolution 742 (WRC-03) should be deleted.

# Proposals – Resolution 746 (WRC-03)

ARTICLE  5

Frequency allocations

Section IV  –  Table of Frequency Allocations
(See No. 2.1)

MOD	ASP/41A2/7

15.4-18.4 GHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 18.1-18.4 FIXED FIXED-SATELLITE (space-to-Earth) 5.484A 5.516B (Earth-to-space) 5.520 MOBILE MOD 5.519 5.521 |

MOD	ASP/41A2/8

5.519	Additional allocation:  the band 18.1-18.4 GHz is also allocated to the meteorological-satellite service (space-to-Earth) on a primary basis. Its use is limited to geostationary satellites and shall be in accordance with the provisions of Article 21, Table 21-4.

Reasons:	APT supports the extension in the upper part.

ARTICLE  9

Procedure for effecting coordination with or 
            obtaining agreement of other administrations1, 2, 3, 4, 5, 6, 7, 8    (WRC-03)

Section II  –  Procedure for effecting coordination12, 13

Sub-Section IIA  –  Requirement and request for coordination

MOD	ASP/41A2/9

9.41		Following receipt of the BR IFIC referring to requests for coordination under Nos. 9.7 to 9.7B, an administration believing that it should have been included in the request or the initiating administration believing that an administration identified under No. 9.36 in accordance with the provisions of No. 9.7 (GSO/GSO) (items 1), 2), 3), 4), 5) and 6) of the frequency band column), No. 9.7A (GSO earth station/non-GSO system) or No. 9.7B (non-GSO system/GSO earth station) of Table 5-1 of Appendix 5 should not have been included in the request, shall, within four months of the date of publication of the relevant BR IFIC, inform the initiating administration or the identified administration, as appropriate, and the Bureau, giving its technical reasons for doing so, and shall request that its name be included or that the name of the identified administration be excluded, as appropriate.     (WRC-2007)

Reasons:	APT believes the current regulatory provision is well balanced and does not impose any additional undue constraints on the existing services.

APPENDIX  5  (Rev.WRC-03)

Identification of administrations with which coordination is to be effected or 
agreement sought under the provisions of Article 9

TABLE  5-1     (Rev.WRC-03)

Technical conditions for coordination
(see Article 9)

MOD	ASP/41A2/10

TABLE  5-1 (continued)     (Rev.WRC-07)

| Reference of Article 9 | Case | Frequency bands (and Region) of the service for which coordination is sought | Threshold/condition | Calculation method | Remarks |
| --- | --- | --- | --- | --- | --- |
| No. 9.7 GSO/GSO (cont.) |  | 3) 17.7-20.2 GHz, (Regions 2 and 3), 17.3-20.2 GHz (Region 1) and 27.5-30 GHz | i) Bandwidth overlap, and ii) any network in the FSS and any associated space operation functions (see No. 1.23) with a space station within an orbital arc of ( 8° of the nominal orbital position of a proposed network in the FSS |  | With respect to the space services listed in the threshold/condition column in the bands in 1), 2), 3), 4), 5 and 6), an administration may request, pursuant to No. 9.41, to be included in requests for coordination, indicating the networks for which the value of (T/T calculated by the method in § 2.2.1.2 and 3.2 of Appendix 8 exceeds 6%. When the Bureau, on request by an affected administration, studies this information pursuant to No. 9.42, the calculation method given in § 2.2.1.2 and 3.2 of Appendix 8 shall be used |
|  |  | 4) 18.1-18.4 GHz 5) Bands above 17.3 GHz, except those defined in § 3) and 4) | i) Bandwidth overlap, and ii) any network in the FSS or MetSat service and any associated space operation functions (see No. 1.23) with a space station within an orbital arc of (8° of the nominal orbital position of a proposed network in the FSS or MetSat service i) Bandwidth overlap, and ii) any network in the FSS and any associated space operation functions (see No. 1.23) with a space station within an orbital arc of (8° of the nominal orbital position of a proposed network in the FSS (see also Resolution 901 (WRC-03)) |  |  |

TABLE  5-1 (continued)     (Rev.WRC-07)

| Reference of Article 9 | Case | Frequency bands (and Region) of the service for which coordination is sought | Threshold/condition | Calculation method | Remarks |
| --- | --- | --- | --- | --- | --- |
| No. 9.7 GSO/GSO (cont.) |  | 6) Bands above 17.3 GHz | i) Bandwidth overlap, and ii) any network in the FSS or BSS, not subject to a Plan, and any associated space operation functions (see No. 1.23) with a space station within an orbital arc of (16° of the nominal orbital position of a proposed network in the FSS or BSS, not subject to a Plan, except in the case of a network in the FSS with respect to a network in the FSS (see also Resolution 901 (WRC-03)) |  |  |
|  |  | 7) All frequency bands, other than those in 1), 2), 3), 4), 5 and 6), allocated to a space service, and the bands in 1), 2), 3), 4), 5 and 6) where the radio service of the proposed network or affected networks is other than the space services listed in the threshold/condition column, or in the case of coordination of space stations operating in the opposite direction of transmission | i) Bandwidth overlap, and ii) Value of T/T exceeds 6% | Appendix 8 | In application of Article 2A of Appendix 30 for the space operation functions using the guardbands defined in § 3.9 of Annex 5 of Appendix 30, the threshold/condition specified for the FSS in the bands in 2) applies. In application of Article 2A of Appendix 30A for the space operation functions using the guardbands defined in § 3.1 and 4.1 of Annex 3 of Appendix 30A, the threshold/condition specified for the FSS in the bands in 4) applies |

APPENDIX  7  (Rev.WRC-03)

Methods for the determination of the coordination area around an earth 
station in frequency bands between 100 MHz and 105 GHz

ANNEX  7

System parameters and predetermined coordination distances for 
determination of the coordination area around an earth station

MOD	ASP/41A2/11

TABLE  8d

Parameters required for the determination of coordination distance for a receiving earth station

| Receiving space radiocommunication service designation | Meteorological- satellite | Fixed-satellite | Fixed-satellite 3 | Broadcasting- satellite | Earth exploration- satellite 4 | Earth exploration- satellite 5 | Space research (deep space) | Space research | Fixed- satellite 6 | Fixed- satellite 5 | Mobile-satellite | Broadcasting-satellite, fixed-satellite | Mobile-satellite | Radio-navigation | Broadcasting-satellite |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Unmanned | Manned |  |  |  |  |  |  |  |
| Frequency bands (GHz) | 18.1-18.4 | 18.8-19.3 | 19.3-19.7 | 21.4-22.0 | 25.5-27.0 | 25.5-27.0 | 31.8-32.3 | 37.0-38.0 | 37.5-40.5 | 37.5-40.5 | 39.5-40.5 | 40.5-42.5 | 43.5-47.0 | 43.5-47.0 | 84-86 |
| Transmitting terrestrial service designations | Fixed, mobile | Fixed, mobile | Fixed, mobile | Fixed, mobile | Fixed, mobile | Fixed, mobile | Fixed, radio- navigation | Fixed, mobile | Fixed, mobile | Fixed, mobile | Fixed, mobile | Broadcasting, fixed | Mobile | Mobile | Fixed, mobile, broadcasting |
| Method to be used | § 2.1, § 2.2 | § 2.1, § 2.2 | § 2.2 | § 1.4.5 | § 2.2 | § 2.1 | § 2.1, § 2.2 | § 2.1, § 2.2 | § 2.2 | § 2.1 | § 1.4.6 | § 1.4.5, § 2.1 | § 1.4.6 | – | § 1.4.5 |
| Modulation at earth station 1 | N | N | N |  | N | N | N | N | N | N | N | – | N |  |  |
| Earth station interference parameters and criteria | p0 (%) |  | 0.05 | 0.003 | 0.01 |  | 0.25 | 0.25 | 0.001 | 0.1 | 0.001 | 0.02 | 0.003 |  |  |  |  |  |
|  | n |  | 2 | 2 | 1 |  | 2 | 2 | 1 | 1 | 1 |  | 2 |  |  |  |  |  |
|  | p (%) |  | 0.025 | 0.0015 | 0.01 |  | 0.125 | 0.125 | 0.001 | 0.1 | 0.001 |  | 0.0015 |  |  |  |  |  |
|  | NL (dB) |  | 0 | 0 | 0 |  | 0 | 0 | 0 | 0 | 1 | 1 |  |  |  |  |  |
|  | Ms (dB) |  | 18.8 | 5 | 5 |  | 11.4 | 14 | 1 | 1 | 6.8 | 6 |  |  |  |  |  |
|  | W (dB) |  | 0 | 0 | 0 |  | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  |  |
| Terrestrial station parameters | E (dBW) in B 2 | A |  | – | – |  | – | – | – | – | – | – | – | – |  |  |  |
|  |  | N | 40 | 40 | 40 | 40 | 42 | 42 | –28 | –28 | 35 | 35 | 35 | 44 | 40 | 40 |  |
|  | Pt (dBW) in B | A |  | – | – |  | – | – | – | – | – | – | – | – |  |  |  |
|  |  | N | –7 | –7 | –7 | –7 | –3 | –3 | –81 | –73 | –10 | –10 | –10 | –1 | –7 | –7 |  |
|  | Gx (dBi) |  | 47 | 47 | 47 | 47 | 45 | 45 | 53 | 45 | 45 | 45 | 45 | 45 | 47 | 47 |  |
| Reference band- width 6 | B (Hz) |  | 107 | 106 | 106 |  | 107 | 107 | 1 | 1 | 106 | 106 | 106 | 106 |  |  |  |
| Permissible interference power | Pr( p) (dBW) in B | −115 | –140 | –137 |  | –120 | –116 | –216 | –217 | –140 |  |  |  |  |  |  |
| 1 A: analogue modulation; N: digital modulation. 2 E is defined as the equivalent isotropically radiated power of the interfering terrestrial station in the reference bandwidth. 3 Non-geostationary mobile-satellite service feeder links. 4 Non-geostationary-satellite systems. 5 Geostationary-satellite systems. 6 Non-geostationary fixed-satellite service systems. |

SUP	ASP/41A2/12

RESOLUTION  746  (WRC-03)

Issues dealing with allocations to science services

Reasons:	APT believes this resolution is not required after the proposed modifications are made to the Radio Regulations for Issues A and B.

# Proposals – Resolution 742 (WRC-03)

ARTICLE  5

Frequency allocations

Section IV  –  Table of Frequency Allocations
(See No. 2.1)

MOD	ASP/41A2/13

34.2-40 GHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 36-37 EARTH EXPLORATION-SATELLITE (passive) FIXED MOBILE SPACE RESEARCH (passive) 5.149 ADD 5.A12 |

ADD	ASP/41A2/14

5.A12 	For sharing of the band 36-37 GHz between the Earth exploration-satellite (passive) service and the fixed and mobile services, Resolution [ASP/AI1.2/1-36 GHz SHARING] (WRC-07) shall apply.      (WRC-07)

Reasons:	Passive sensor measurements in this band are currently being used to determine rain, snow, ocean ice, cloud liquid and water vapour properties for use in numerical weather prediction models and other scientific applications including studies the hydrological cycle or global water circulation.  Currently, this band is lightly used worldwide by the fixed and mobile services.  It is necessary to establish an appropriate operational environment to protect the future use of Earth exploration-satellite (passive) and space research (passive) services in this band without imposing undue constraints on the fixed and mobile services.

ADD	ASP/41A2/15

RESOLUTION [ASP/AI1.2/1-36 GHz Sharing] (WRC-07)

Sharing criteria applied to the use of the frequency band 36-37 GHz

The World Radiocommunication Conference (Geneva, 2007),

considering

a)	that the frequency band 36-37 GHz is allocated to the Earth exploration-satellite service (EESS) (passive) and to the space research service (SRS) (passive) on a primary basis;

b)	that the frequency band 36-37 GHz is allocated to the fixed service and to the mobile service on a primary basis;

c)	that the EESS (passive) interference levels are contained in Recommendation ITU-R RS.1029;

d)	that the band 36-37 GHz is not available for high-density applications in the fixed service (see No. 5.547);

e)	that the band 36-37 GHz is of primary interest to the EESS (passive) to measure rain, snow, ocean ice, cloud liquid and water vapour;

f)	that this frequency band is used by passive sensors to study natural phenomena producing radio emissions at frequencies fixed by the laws of nature, and therefore shifting frequency to avoid or mitigate interference problems may not be possible;

g)	that the EESS (passive) operating in the band 36-37 GHz may suffer from interference from the emissions of systems of active services;

h)	that studies have concluded that appropriate sharing criteria applicable to both passive and active services would reduce this interference to a level that would permit  passive sensors to operate successfully in this band, while allowing continuing operation of active services in the same band;

i)	that Recommendation ITU-R RS.[10/36 GHz MITIGATE] provides the technical and operational characteristics for passive sensors in the Earth exploration-satellite (passive) service to facilitate sharing of the 36-37 GHz bands with the fixed and mobile services;

j)	that Recommendation ITU-R F.[10/36 GHz MITIGATE] provides the technical and operational characteristics for the stations of fixed service to facilitate sharing of the 36-37 GHz bands with the Earth exploration-satellite (passive) service,

resolves

that, in order to facilitate sharing between active and passive services in the band 36-37 GHz, stations in the fixed and mobile services brought into use on or after the date of entry into force of the WRC-07 Final Acts shall comply with the sharing criteria contained in Tables 1 and 2 of Annex 1.

ANNEX 1 to resolution [asp/ai1.2/1-36 ghz SHARING] (WRC-07)

Sharing criteria in the band 36-37 GHz

1	The words used in this Annex are defined as follows:

Point-to-point communication is defined as communication provided by a link, for example, a radio-relay link between two stations located at specified fixed points.

Point-to-multipoint communication is defined as communication provided by links, for example, radio-relay links between a single station located at a specified fixed point (also called hub station in this Annex) and a number of stations located at specified fixed points (also called customer stations in this Annex).

Automatic transmit-power control (ATPC) is a technique in which the output power of a microwave transmitter is automatically varied in accordance with path conditions. In normal path conditions, the ATPC maintains the transmitter output power at a reduced level. The ATPC is characterized by the ATPC range which is defined as the difference between the maximum and minimum value of transmitter power.

2	The sharing criteria applied to the fixed service are given in Table 1-1.

3	The sharing criteria applied to the mobile service are given in Table 1-2.

TABLE 1-1

Sharing criteria applied to the fixed service

| Parameter | Value |
| --- | --- |
| Maximum elevation angle | 20° |
| Point-to-point systems – Maximum transmitter power | –10 dBW 1 |
| Point-to-multipoint systems – Maximum transmitter power of hub stations – Maximum transmitter power of customer stations | –5 dBW –10 dBW |
| 1 In the case of the fixed station point-to-point systems using ATPC, the maximum transmitter power may be increased by a value corresponding to the ATPC range up to a maximum of –7 dBW. |

TABLE 1-2

Sharing criteria applied to the mobile service

| Parameter | Value |
| --- | --- |
| Maximum transmitter power for the station of fixed use 1 | –10 dBW |
| Maximum transmitter power for the station of nomadic use 2 | –3 dBW |
| 1 Fixed use under the mobile service is wireless application in which the location of the end-user termination and the network access point to be connected to the end-user are not fixed but are seldom changed. The activity factor is taken to be 100%. 2 Nomadic use is defined as a wireless application in which the location of the end-user termination may be in different places but it must be stationary while in use. The activity factor is taken to be usually much less than the threshold value of 40%. |

Reasons:	The studies performed under Agenda item 1.2 and Resolution 742 (WRC-03) have shown that these sharing criteria would allow EESS (passive) sensors to operate successfully in the band 36-37 GHz without imposing undue constraints on the fixed and mobile services. See ASP/41A2/14.

SUP	ASP/41A2/16

RESOLUTION  742  (WRC-03)

Use of the frequency band 36-37 GHz

Reasons:	The study has been completed in ITU-R under this Resolution and therefore it can be deleted.

____________