JHF(JKJ) Electron Cloud Issues

July 8, 2002

I. Primary electrons

- Ionization yield  at 1 nTorr. -- SNS is   at 10 nTorr.

- Lost proton yield is , assuming beam loss of , and 100 e/lost p. -- Tandem studies for glancing angle effect and TiN coated surface.

- Foil region yield is , but 217 keV ones are swept away and tens of eV ones localized.  -- SNS study and specification?

II. Simulation

- Use the electrons produced by lost protons as primary.

- Electrons survive long bunch gap, baseline shifts up, --which seems not agreeable with the PSR observation.

III. Proton ring parameters

- Simulation results can be approximately explained by  . -- the factor  seems from ,  is  no. of oscillations, ...,

- -- PSR (=6.7%, ISIS (=0.5% ?

IV. Instability

- Resonator type impedance is used for EC effect. Some important issues such as the electron density and distribution are not settled, ...  -- Further justification?

- Energy spread is used as the damping force (dispersion relation U>1, unstable).  -- Electron neutralization with the beam is not taking into account.

V. Secondary yield

- Argon sputtering

- -- Beam scrubbing and baking effects, not from JHF report, but from SPS.

# Text boxes

Proton beam

Electron / primary electron

(R. Macek, ECloud02)

JHF simulated PSR

PSR observation

E-sweeper signal

Electrons, detected with 45 V bias

Simulated neutralization factor

Inj.       Ext.   50GeV

Inj.       Ext.   3GeV

SNS

AGS

ISIS

PSR

TiN, yield 0.8 at 400 eV

TiN, yield 1.9 at 200 eV

After argon ion sputtering

As received

(J.M. Jimenez, ECloud02)

Added

(N. Hilleret, Chamonix, 2000)

Cu

Cu

Graphite

Ti

TiN

Reflected e not included