WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A12995 | In-Flight Anomaly Number -- | Contractor Report Number E-135 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title TUMBLE VALVE SWITCH MODULE FAILED TO ARM |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1 |
| HCRIT -- | Sys_Lvl -- | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE SWITCH MODULE | PART# 80933003704-239 | SER/LOT# 1489 | MANUFACTURER MAF |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EAN - OUTPUT LOSS | Cause UF - UA-FLIGHT |
| System ELECTRICAL | Defect -- | Material C - EEE | Work Contact L. COLON | Fail Date 07/02/1990 |
| Received at MSFC 07/09/1990 | Date Isolated 07/05/1990 | FMEA Reference 3.5.1.2 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom EA - FAILS OFF | Time Cycle -- |
| Effectivity Text -- |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary THE CAUSE OF THE FAILURE COULD NOT BE DETERMINED |
| Last MSFC Update 12/02/1991 | CN RSLV SBMT 07/31/1990 | Defer Date -- | Add Date 07/11/1990 | R/C Codes 0 - EXPL -- -- |
| Assignee |
| Design A. JACKMAN | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. LADNER |
| Approval |
| Design J. MCEUEN | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. LADNER |
| PAC Assignee T. HESTER | PAC Review Complete TBH | MSFC Closure Date 08/16/1990 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary CLOSED EXPLAINED |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description THE SWITCH MODULE FAILED TO "ARM" DURING TESTING IN THE MAF HARNESS FABRICATION SHOP. TEST PROCEDURE 80933003704-239 CHECKS ELECTRICAL FUNCTION OF THE MODULE FOLLOWING INSTALLATION OF TWO ELECTRICAL CONNECTORS ON THE WIRE LEADS OF THE MODULE CRITICALITY: THE SWITCH MODULE IS CRIT. 1; FMEA ITEM CODE 3.5.1.2; "FAILS TO ARM" NOTE: THE SWITCH MODULE IS LIMITED LIFE CONTROLLED |
| Contractor Investigation/Resolution THE SWITCH MODULE IS PART OF THE ELECTRICAL SYSTEM THAT CONTROLS THE FIRING OF THE TUMBLE VALVE ON THE ET. THE MODULE IS CONVERTED TO THE 809 SERIES PART NUMBER BY THE INSTALLATION OF TWO ELECTRICAL CONNECTORS ONTO THE WIRE LEADS OF THE PD PART. THE FAILURE OCCURRED DURING IN-PROCESS TESTING THAT VERIFIES PROPER INSTALLATION OF THE CONNECTORS THE FAILURE INDICATION WAS THE INTERNAL RELAY OF THE MODULE DID NOT ACTUATE UPON APPLICATION OF POWER TO THE COIL. IN SERVICE ON AN ET THE FAILURE WOULD HAVE PREVENTED THE "FIRE" SIGNAL FROM REACHING THE TUMBLE VALVE EXPLOSIVE INITIATOR TASK I FAILURE INVESTIGATION: A FAILURE ANALYSIS WILL BE PERFORMED ON THE SWITCH MODULE RESPONSIBILITY: J. ADAMS/3741 - E. HARTLEY/3740 COMPLETED: 7/26/90 CLOSURE STATEMENT: DESPITE DETAILED TESTING, IT WAS NOT POSSIBLE TO DETERMINE THE CAUSE OF THE FAILURE. THE ORIGINAL FAILURE HAD OCCURRED UPON INITIAL APPLICATION OF POWER TO THE MODULE FOLLOWING INSTALLATION OF THE ELECTRICAL CONNECTORS ON THE WIRE HARNESS. THE TEST HAD BEEN DISCONTINUED DUE TO THE END OF THE SHIFT AND THE POWER HAD BEEN TURNED OFF. AT THE START OF THE NEXT WORK DAY, POWER WAS APPLIED AND THE RELAY IMMEDIATELY "ARMED" FAILURE ANALYSIS INVOLVED ELECTRICAL TESTS OF CONTINUITY, INSULATION RESISTANCE, AND RELAY OPERATING VOLTAGES AS WELL AS DISASSEMBLY AND EXAMINATION OF THE COMPONENTS. NO DEFECT COULD BE FOUND. REFERENCE: FAILURE ANALYSIS REPORT T-110192 TASK CLOSED TASK II CORRECTIVE ACTION NO CORRECTIVE ACTION IS REQUIRED. THIS IS AN ISOLATED CASE. THERE ARE THREE SEPARATE SERIES OF TESTS PERFORMED ON THE SWITCH MODULE AFTER INSTALLATION ON AN ET. AT MAF THE TEST REQUIREMENT IS MMC-ET-TM04K-B, NO. 2.2.11 AS CARRIED OUT BY TEST PROCEDURE 6C108/208-AT. AT KSC TESTS ARE REQUIRED BY BOTH OMRSD FILE IV AND FILE II. THE FILE IV REQUIREMENT IS NO. T75STA.850 AS CARRIED OUT BY OMI NO. T1160, STEPS 05-043 THROUGH 05-058. THE FILE II REQUIREMENT IS NO. S00000.135 AS CARRIED OUT BY OMI T1160, STEPS 15-000 THROUGH 15-035. ALL THREE SETS OF TESTS CHECK OPERATION INCLUDING "FIRING" AN EXPLOSIVE SQUID SIMULATOR TASK CLOSED TASK III CLEARANCE OF EFFECTIVITIES: ETS 35 AND 37 CLEARED. THE TUMBLE VALVE CIRCUITS HAVE BEEN DEACTIVATED ALL OTHER ETS CLEARED. THIS FAILURE WAS AN ISOLATED CASE. THERE ARE SUFFICIENT TESTS ON THE COMPLETED ETS TO ASSURE PROPER OPERATION TASK CLOSED TASK IV CAPS CLOSURE SUMMARY THIS IS AN EXPLAINED CLOSURE OF THE CAPS FOR AN INTERMITTENT FAILURE A TUMBLE VALVE SWITCH MODULE FAILED TO "ARM" DURING AN IN-PROCESS TEST AT MAF. THE FAILURE DID NOT REPEAT. FAILURE ANALYSIS WAS UNSUCCESSFUL IN DETERMINING THE CAUSE OF THE FAILURE. THERE ARE SUFFICIENT TESTS OF THE MODULE AFTER INSTALLATION ON AN ET TO ASSURE OPERATION. THIS IS AN ISOLATED CASE TASK CLOSED 8/20/90 PAC NOTE: CHIEF ENGINEERS OFFICE FEELS THAT THIS IS AN UNEXPLAINED CLOSURE |
| MSFC Response/Concurrence |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A12995 | IFA# -- | Contractor RPT# E-135 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 80933003704-239 | Asmnt Part Name SWITCH MODULE | Asmnt Serial/Lot# 1489 |
| HCRIT CD -- | FCRIT CD 1 | CAUSE CD UA - UNK-ONE | FAIL MODE EA - FAILS OFF |
| Asmnt FMEA 3.5.1.2 | Asmnt FM 2 | FMEA CSE A | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# PD7100082-009 | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |