- Radial and Vertical Builds

Following are the dimensional outputs from the spreadsheet (r,z centers and dr,dz builds)

| A | 1.50 |  |  |  |
| --- | --- | --- | --- | --- |
| R0 | 1.20 |  |  |  |
| R0+a | 2.00 |  |  |  |
| kappa | 3.00 |  |  |  |
| kappa*a | 2.40 |  |  |  |
| Outboard SOL gap | 0.10 |  |  |  |
|  | R(m) | Z(m) | dR(m) | dZ(m) |
| TF Midplane | 0.000 | 0.000 | 0.300 | 4.320 |
| TF End | 0.000 | 4.540 | 1.200 | 3.720 |
| PF1 | 0.950 | 4.900 | 0.500 | 0.500 |
| PF2 | 4.980 | 4.900 | 0.561 | 1.121 |
| PF3 | 4.980 | 2.811 | 0.561 | 1.121 |
| Outboard First Wall | 2.125 | 0.000 | 0.050 | 9.300 |
| Blanket | 2.450 | 0.000 | 0.600 | 9.300 |
| Hot Shield | 2.900 | 0.000 | 0.300 | 9.300 |
| Cold Shield | 3.250 | 0.000 | 0.400 | 9.300 |
| Outer VV/TF Return | 3.925 | 0.000 | 0.750 | 12.800 |
| Top VV/TF Return | 2.075 | 5.900 | 2.950 | 1.000 |

| A | 1.50 |  |  |  |
| --- | --- | --- | --- | --- |
| R0 | 1.50 |  |  |  |
| R0+a | 2.50 |  |  |  |
| kappa | 3.00 |  |  |  |
| kappa*a | 3.00 |  |  |  |
| Outboard SOL gap | 0.10 |  |  |  |
|  | R(m) | Z(m) | dR(m) | dZ(m) |
| TF Midplane | 0.000 | 0.000 | 0.400 | 5.400 |
| TF End | 0.000 | 5.196 | 1.600 | 3.607 |
| PF1 | 1.150 | 5.500 | 0.500 | 0.500 |
| PF2 | 5.504 | 5.500 | 0.608 | 1.215 |
| PF3 | 5.504 | 2.858 | 0.608 | 1.215 |
| Outboard First Wall | 2.625 | 0.000 | 0.050 | 10.500 |
| Blanket | 2.950 | 0.000 | 0.600 | 10.500 |
| Hot Shield | 3.400 | 0.000 | 0.300 | 10.500 |
| Cold Shield | 3.750 | 0.000 | 0.400 | 10.500 |
| Outer VV/TF Return | 4.425 | 0.000 | 0.750 | 14.000 |
| Top VV/TF Return | 2.425 | 6.500 | 3.250 | 1.000 |

End of TF straight section is set to dz=0.9*2*kappa*a

Total TF height (equal to height of VV) is set to dz=2*(kappa*a+4)

Inboard first wall + SOL dr = 0.1

Outboard SOL dr = 0.1

Outboard first wall, blanket, shield dz = 2*(kappa*a+2.25)

Outboard first wall dr = 0.05

Blanket dr = 0.6

Shield (hot + cold) dr = 0.7

Clearance gap shield to outer VV (TF return) dr = 0.1

Outer VV (TF return) dr = 0.75

- R0=1.2m machine, Basic (HH=1.4, 1MW/m^2) and Maximum performance (HH=1.8, P_aux limited to level required for Basic case)

| R0 | 1.200 | 1.200 |
| --- | --- | --- |
| A | 1.500 | 1.500 |
| R0+a | 2.000 | 2.00 |
| kappa | 3.000 | 3.000 |
| delta | 0.400 | 0.400 |
| qMHD | 7.482 | 7.482 |
| qcyl | 2.57 | 2.57 |
| qcyl/qcyl(A) | 100.0% | 100.0% |
| Bt | 2.425 | 2.346 |
| fH20 | 25.0% | 25.0% |
| TH20max | 87.6 | 87.6 |
| TCumax | 150.0 | 150.0 |
| Sigmax | 94.2 | 88.1 |
| Javgtf | 5.15E+07 | 4.98E+07 |
| Itf | 14.6 | 14.1 |
| Ip | 12.573 | 12.161 |
| Beta_N_thermal | 2.44% | 4.04% |
| Beta_N_total | 4.13% | 5.63% |
| Beta_N/Beta_N(A) | 59.4% | 80.9% |
| Beta_T | 15.8% | 26.2% |
| Beta_P | 47.1% | 77.9% |
| xne | 9.49E+19 | 1.42E+20 |
| fGW | 17.1% | 26.4% |
| alpha_n(A) | 0.250 | 0.250 |
| alpha_T(A) | 1.000 | 1.000 |
| fBS | 30.2% | 50.0% |
| Tempavg | 13.538 | 14.058 |
| HH | 1.400 | 1.800 |
| Tau_E*HH | 0.601 | 0.777 |
| Q | 2.438 | 4.262 |
| P_Brem | 1.9 | 4.3 |
| P_line | 8.4 | 10.1 |
| P_aux | 29.5 | 29.5 |
| P_fusion | 72.0 | 125.7 |
| P_alpha | 14.4 | 25.1 |
| fTC | 41.3% | 24.1% |
| Eta_CD | 0.34 | 0.35 |
| P_CD | 29.5 | 29.5 |
| P_CD/P_aux | 100.0% | 100.0% |
| P_aux_input | 65.6 | 65.6 |
| ∑P_tf | 158.8 | 148.5 |
| ∑P_pf | 42.0 | 40.6 |
| P_bop | 20.0 | 20.0 |
| ∑P_elec input | 286.3 | 274.7 |
| Xnwall | 1.1 | 1.9 |
| Qn_wall | 0.60 | 1.04 |
| Qn_tm | 1.00 | 1.75 |
| Port Height (delta Z) | 1.60 | 1.60 |
| #NBI Port | 2 | 2 |
| Available Test Module Area | 12.8 | 12.80 |
| #Test Module Ports | 7 | 7 |
| T fueling rate | 11.0 | 19.23 |
| fN | 81.56% | 81.6% |
| FBR | 97.9% | 97.9% |
| T consumption rate | 0.23 | 0.41 |
| n/s/W | 7.28E+10 | 1.33E+11 |
| frad_core | 20.0% | 20.0% |
| Q_fw | 0.213 | 0.299 |
| frad_div | 55.3% | 63.4% |
| Q_div | 15.0 | 15.0 |

- R0=1.5m machine, Basic and High Performance Cases

| R0 | 1.500 | 1.500 |
| --- | --- | --- |
| A | 1.500 | 1.500 |
| R0+a | 2.50 | 2.50 |
| kappa | 3.000 | 3.000 |
| delta | 0.400 | 0.400 |
| qMHD | 7.898 | 8.753 |
| qcyl | 2.71 | 3.01 |
| qcyl/qcyl(A) | 105.6% | 117.0% |
| Bt | 2.665 | 2.665 |
| fH20 | 25.0% | 25.0% |
| TH20max | 72.6 | 89.1 |
| TCumax | 108.5 | 140.4 |
| Sigmax | 100.0 | 100.0 |
| Javgtf | 3.98E+07 | 3.98E+07 |
| Itf | 20.0 | 20.0 |
| Ip | 16.362 | 14.766 |
| Beta_N_thermal | 2.20% | 6.22% |
| Beta_N_total | 3.65% | 6.78% |
| Beta_N/Beta_N(A) | 52.4% | 97.4% |
| Beta_T | 13.5% | 34.4% |
| Beta_P | 44.9% | 140.3% |
| xne | 8.00E+19 | 3.30E+20 |
| fGW | 17.3% | 78.9% |
| alpha_n(A) | 0.250 | 0.250 |
| alpha_T(A) | 1.000 | 1.000 |
| fBS | 28.8% | 90.0% |
| Tempavg | 16.667 | 10.389 |
| HH | 1.400 | 1.800 |
| Tau_E*HH | 0.959 | 1.290 |
| Q | 3.352 | 19.997 |
| P_Brem | 2.9 | 40.0 |
| P_line | 10.6 | 20.1 |
| P_aux | 33.5 | 28.1 |
| P_fusion | 112.4 | 562.2 |
| P_alpha | 22.5 | 112.4 |
| fTC | 33.4% | 4.4% |
| Eta_CD | 0.42 | 0.26 |
| P_CD | 33.5 | 28.1 |
| P_CD/P_aux | 100.0% | 100.0% |
| P_aux_input | 74.5 | 62.5 |
| ∑P_tf | 201.7 | 206.3 |
| ∑P_pf | 60.6 | 54.5 |
| P_bop | 20.0 | 20.0 |
| ∑P_elec input | 356.8 | 343.2 |
| Xnwall | 1.1 | 5.4 |
| Qn_wall | 0.60 | 2.98 |
| Qn_tm | 1.00 | 5.00 |
| Port Height (delta Z) | 2.00 | 2.00 |
| #NBI Port | 2 | 2 |
| Available Test Module Area | 22.00 | 24.00 |
| #Test Module Ports | 6 | 6 |
| T fueling rate | 17.20 | 86.00 |
| fN | 82.7% | 82.7% |
| FBR | 99.2% | 99.2% |
| T consumption rate | 0.14 | 0.68 |
| n/s/W | 9.25E+10 | 4.81E+11 |
| frad_core | 20.0% | 20.0% |
| Q_fw | 0.180 | 0.798 |
| frad_div | 43.7% | 72.4% |
| Q_div | 15.0 | 15.0 |