MSFC PRACA : 2003-02-12 08:41

MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A17395 | In-Flight Anomaly Number -- | Contractor Report Number E-166 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title AFT SRB/ORBITER WIRE HARNESS (303W04) FAILED DIELECTRIC WITHSTAND VOLTAGE (1500) TEST |
| EICN# -- | ELEMENT ET | Contractor LMMSS | FSCM# -- | FCRIT 1R |
| HCRIT -- | Sys_Lvl -- | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE 303W04 WIRE HARNESS | PART# 03714-160 | SER/LOT# 800780 | MANUFACTURER LMMSS |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EL - SHORT | Cause M - MANUFG |
| System ELECTRICAL | Defect -- | Material -- | Work Contact J. VARRIELLO | Fail Date 04/20/1999 |
| Received at MSFC 04/22/1999 | Date Isolated 04/20/1999 | FMEA Reference 3.12.4.2 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom EL - SHORT | Time Cycle -- |
| Effectivity Text ET 104 |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date 09/07/1999 | Contractor Req Defer Until Date 05/15/1999 | LVL 3 Close -- | Remark / Action 05/15/1999 |
| Investigation / Resolution Summary |
| Last MSFC Update 06/28/1999 | CN RSLV SBMT -- | Defer Date 05/04/1999 | Add Date 04/22/1999 | R/C Codes -- -- -- |
| Assignee |
| Design J. RATLEY | Chief Engineer J. LUSK | S & MA J. GREEN | Project -- | Project MGR P. COUNTS |
| Approval |
| Design J. RATLEY | Chief Engineer J. LUSK | S & MA A. ADAMS | Project -- | Project MGR P. COUNTS |
| PAC Assignee R. TUCKER | PAC Review Complete RT | MSFC Closure Date 06/23/1999 | Status C - CLOSED | F/A Completion 04/29/1999 |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID N040378 |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description PROBLEM THE WIRE HARNESS FAILED THE POST INSTALLATION TM04 DIELECTRIC WITHSTAND VOLTAGE (1500 V) TEST AT MAF CRITICALITY: THE 303W04 WIRE HARNESS IS CRIT. 1R; FMEA ITEM CODE: 3.12.4.2, "FAILS SHORTED" PREVIOUS CAPS: E-24, E-68, E-80, E-107, E-128, E-148, E-164 REVISION 'A' IS DATED 05/15/1999 |
| Contractor Investigation/Resolution GENERAL: THE AFT SRB/ORBITER CABLE (303W04) ON ET-104 WAS BEING TESTED IN FINAL ASSEMBLY AT MAF. THE TESTS INCLUDE A 500 VOLT INSULATION RESISTANCE (IR) TEST AND A 1500 VOLT DIELECTRIC WITHSTANDING VOLTAGE TEST FOLLOWED BY ANOTHER 500 VOLT IR TEST OF EVERY CIRCUIT IN THE CABLES. THE HARNESS HAD A RESISTANCE LESS THAN THE MINIMUM ACCEPTABLE VALUE OF 2 MEGOHMS AT 1500 VOLTS REQUIRED BY TEST PROCEDURE-6C101-FA. THE FAILURE OCCURRED BETWEEN CONTACT 303W04J04-H AND ET STRUCTURE GROUND TASK I FAILURE/PROBLEM INVESTIGATION A. THE CABLE WILL BE REMOVED FROM ET-104 AND FAILURE ANALYSIS WILL BE PERFORMED BY RELIABILITY ASSURANCE RESPONSIBILITY: J. VARRIELLO - 3741/ D. WESTPHAL - 3740 ECD: 05/20/1999 COMPLETED: 04/29/1999 TASK CLOSED SINCE THE FACT ANALYZER FOUND THE FAILURE WAS "H" TO ET STRUCTURE IN FINAL ASSEMBLY, THE INITIAL INVESTIGATION WAS FOCUSED ON THIS SCENARIO. THE HARNESS WAS MOVED TO HARNESS FABRICATION AREA, AND TP-6C143-HA WAS PERFORMED USING THE FACT ANALYZER TO EXECUTE ACCEPTANCE TESTS FOR 1500 DWV, CONTINUITY, AND 500 IR. THE HARNESS PASSED ALL TESTS. THE FAILURE OF "H" TO OVS/ET STRUCTURE GROUND COULD NOT BE DUPLICATED DURING VISUAL INSPECTION OF THE OVS, A DISCREPANT AREA OF FRAYED DAMAGE WAS FOUND ABOUT 92.5 INCHES FROM THE POTTED BACKSHELL OF 303W04P44. THE OVS WAS REMOVED AND FURTHER VISUAL EXAMINATION IN THE AREA WHERE THE OVS WAS DAMAGED REVEALED A SMALL SPLIT IN ONE OF THE UNDERLYING KAPTON(R) WRAPPED CONDUCTORS. THIS SINGLE CONDUCTOR (303W04J04-H) WAS CONNECTED TO A BIDDLE, AND VOLTAGE WAS INCREASED TO 1000V ATTACHING A 3-INCH PIECE OF COPPER BRAID TO THE GROUND LEAD FROM THE BIDDLE AND ALLOWING IT TO BRUSH AGAINST THE DEFECT AREA RESULTED IN AN ARCING SPARK FROM THE COPPER BRAID TO THE CHARRED SPLIT MICROSCOPIC EXAMINATION OF THE "CHARRED SPLIT" FOUND THAT IT WAS A SLICE IN THE KAPTON(R) WIRE EXTENDING APPROXIMATELY HALF WAY AROUND THE WIRE, AND THE "CHARRED SPLIT" WAS CLEARLY A PUNCTURE THROUGH ALL LAYERS OF KAPTON(R) INSULATION EXTENDING INTO THREE OF THE NICKEL PLATED COPPER STRANDS. REFERENCE FAILURE ANALYSIS REPORT N021019 B. MEET WITH THE PRODUCTION OPERATION MANAGERS TO DISCUSS IMPORTANCE OF PROPER HANDLING OF FLIGHT HARDWARE DURING MANUFACTURE, TRANSPORTATION, AND INSTALLATION AND TO DETERMINE MOST EFFECTIVE WAY TO INFORM TECHNICIANS RESPONSIBILITY: J. VARRIELLO - 3741 / D. WESTPHAL - 3740 A. PANKS - 3671 / M. JAVERY - 3680 ECD: 05/10/1999 COMPLETED: 05/07/1999 TASK CLOSED A MEETING OF THE AREA PRODUCTION OPERATIONS MANAGEMENT AND QUALITY CONTROL MANAGEMENT WAS HELD, AND IT WAS AGREED THAT A RETRAINING SESSION WITH EACH PRODUCTION OPERATIONS TECHNICIAN WAS REQUIRED TO PREVENT FUTURE OCCURRENCES OF THIS ISSUE THIS WAS ACCOMPLISHED VIA CREW MEETINGS. (REF: EMAIL FROM A PANKS, DEPT. 3671) CAUSE MISHANDLING OF HARNESS WHICH DAMAGED THE WIRE, KAPTON(R) INSULATION, AND OVS RESULTING IN THE (1500 V) DWV FAILURE TASK II CORRECTIVE ACTION ALL TECHNICIANS IN HARNESS FABRICATION AND FINAL ASSEMBLY WERE WALKED THROUGH THE EXACT CAUSE OF THE FAILURE AND RE- INSTRUCTED ON THE IMPORTANCE OF CARE DURING HANDLING OF ALL ELECTRICAL HARNESSES TO MINIMIZE THE POSSIBILITY OF UNDETECTED DAMAGE TO THE HARDWARE TASK CLOSED TASK III CLEARANCE OF EFFECTIVITIES ALL ET'S CLEARED. ALL ET'S SUCCESSFULLY PASSED THE TM04 DIELECTRIC WITHSTAND VOLTAGE FINAL ACCEPTANCE TEST TASK CLOSED TASK IV CAPS CLOSURE SUMMARY DURING TESTING OF SRB WIRE HARNESS (303W04) IN FINAL ASSEMBLY, A FAILURE OF CONTACT "H" TO ET STRUCTURE OCCURRED DURING THE 1500 DWV TEST. THE WIRE HARNESS PASSED THE FIRST 500 VDC IR TEST, FAILED THE 1500 DWV TEST, AND THEN PASSED THE SUBSEQUENT 500 VDC IR TEST. THE HARNESS WAS REMOVED AND REPLACED VISUAL INSPECTION FOUND AN AREA OF FRAYED DAMAGE ON THE OVS ABOUT 92.5 INCHES FROM THE POTTED BACKSHELL OF 303W04P44. THE CAUSE WAS FOUND TO BE A SLICE IN A SINGLE CONDUCTOR (303W04J04-H) UNDERNEATH THE DAMAGED AREA OF OVS PRACTITIONERS WERE BRIEFED ON THE CAUSE OF THE FAILURE AND RE- INSTRUCTED OF THE IMPORTANCE OF CARE DURING HANDLING OF ALL ELECTRICAL HARNESSES TO MINIMIZE THE POSSIBILITY OF UNDETECTED DAMAGE TO THE HARDWARE TASK CLOSED THIS CAPS IS CLOSED. NO FURTHER ACTION IS REQUIRED |
| MSFC Response/Concurrence 05/04/99 - MSFC APPROVES CLOSED WITH ACTION STATUS. THIS STATUS IS EFFECTIVE THROUGH 09/07/99 06/23/99 - MSFC CONCURS WITH CLOSURE RATIONALE. THIS PR IS CLOSED |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A17395 | IFA# -- | Contractor RPT# E-166 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 80931003714-160 | Asmnt Part Name 303W04 WIRE HARNESS | Asmnt Serial/Lot# 800780 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD M - MANUFG | FAIL MODE EL - SHORT |
| Asmnt FMEA 3.12.4.2 | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |