WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A10538 | In-Flight Anomaly Number -- | Contractor Report Number E-106-2 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title LH2 ULLAGE PRESSURE TRANSDUCER FAILED OUTPUT TEST |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT 1 | Sys_Lvl N | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE LH2 ULL PRES TRNSDCR | PART# PD74000998-079 | SER/LOT# 1549 | MANUFACTURER GULTON |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE LH2 ULL PRES TRANSDC | PART# PD7400098-079 | SER/LOT# 1549 | MANUFACTURER GULTON |
| Test/Operation A - ATP | Prevailing Condtion S - SHIPPING | F / U F | Fail Mode EV - NOT-TO-SPEC | Cause ES - EI-SHIP |
| System ELECTRICAL | Defect -- | Material C - EEE | Work Contact J. ADAMS | Fail Date 12/09/1986 |
| Received at MSFC 02/13/1987 | Date Isolated -- | FMEA Reference 3.4.1.2 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location GULTON | Symptom EG - SIG HI OR LO | Time Cycle -- |
| Effectivity Text LWTS 16, 20, 21, 22, 24/SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 02/13/1995 | CN RSLV SBMT 09/16/1987 | Defer Date -- | Add Date -- | R/C Codes 2 - MFG -- -- |
| Assignee |
| Design P. MULLER | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| Approval |
| Design P. MULLER | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete JE | MSFC Closure Date 11/06/1987 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description TRANSDUCER HAD AN OUTPUT VOLTAGE VERSUS PRESSURE ERROR OF 71 MILLIVOLTS (LOW) AT 22 PSID. THE MAXIMUM ALLOWABLE ERROR IS 50 MILLIVOLTS. REF CAPS E-091, E-101 AND E-082 |
| Contractor Investigation/Resolution R/A - ADDITIONAL INSPECTION STEPS HAVE BEEN ADDED TO REDUCE THE FREQUENCY OF OCCURRENCE. LAUNCH CONSTRAINT - NONE, THE FAILURE OCCURED DURING ACCEPTANCE TESTING AT THE VENDOR. ALL PRESSURETRANSDUCERS ARE TESTED AGAIN WHEN INSTALLED IN AN ET. THIS STATEMENT WAS COORDINATED WITH ET PROJECT MANAGER G. P. BRIDWELL......... 02-12-87 - BACKGROUND INFORMATION - THE TRANSDUCER FAILED TO MEET REQUIREMENTS OF THE VENDOR ACCEP- TANCE TEST PLAN. IT IS EXPECTED THAT SOME TRANSDUCERS WILL HAVE AN UNACCEPTABLE OUTPUT VOLTAGE VERSUS PRESSURE DUE TO THE STRINGENT REQUIREMENT OF A MAXIMUM ALLOWABLE ERROR OF +/- 1% IN THE FLIGHT PRESSURE OPERATING BAND. FAILURE ANALYSIS AND TESTING ECD IS 4/30/87 5/28/87 - STATUS UPDATE - NO CHANGE. FAILURE ANALYSIS ECD 6/12/87 9/17/87 CLOSURE UPDATE (REF. MMC CAPS E-106B): TASK I FAILURE ANALYSIS T-35914 ANALYSIS WAS PERFORMED BY THE VENDOR AT THE DIRECTION OF MMC RELIABILITY ASSURANCE. CLOSURE STATEMENT THE PROBABLE CAUSE WAS INADVERTENT DROPPING/MISHANDLING OF THE TRANSDUCER BY VENDOR PERSONNEL TASK II CORRECTIVE ACTION NO CORRECTIVE ACTION IS REQUIRED. THIS FAILURE IS CONSIDERED NORMAL PRODUCTION FALLOUT. THE VENDOR'S WORKER TRAINING AND MANUFACTURING PLANS ALREADY ADDRESS THE CAUSES OF THESE FAILURES. HOWEVER, OCCASIONAL FAILURES ARE EXPECTED DUE TO THE NATURE OF THE TRANSDUCER DESIGN AND THE LIMITATIONS OF THE VENDOR'S FACILITIES. CORRECTIVE ACTIONS, PREVIOUSLY DEVELOPED AS PART OF CAPS E-082, ARE EXPECTED TO REDUCE THE NUMBER OF CONTAMINATION CAUSED FAILURES. TASK CLOSED TASK III CLEARANCE OF EFFECTIVITIES THERE ARE NO CONSTRAINTS. THE FAILURES WERE DETECTED DURING VENDOR ACCEPTANCE TESTING. FAILURES FROM THESE CAUSES ARE CONSIDERED NORMAL PRODUCTION FALLOUT. TASK CLOSED TASK IV CAPS CLOSURE SUMMARY THE TRANSDUCER FAILED DURING VENDOR ACCEPTANCE TESTS. FAILURE ANALYSIS FOUND THE PROBABLE CAUSE TO BE OF A TYPE CONSIDERED TO BE NORMAL PRODUCTION FALLOUT. NO CORRECTIVE ACTIONS ARE REQUIRED. CORRECTIVE ACTIONS, PREVIOUSLY DEVELOPED AS PART OF CAPS E-082, ARE EXPECTED TO REDUCE THE NUMBER OF CONTAMINATION CAUSED FAILURES. THIS PROBLEM IS SUBMITTED TO MSFC FOR CLOSURE REVIEW AND APPROVAL |
| MSFC Response/Concurrence |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A10538 | IFA# -- | Contractor RPT# E-106-2 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD7400098-079 | Asmnt Part Name LH2 ULL PRES TRNSDCR | Asmnt Serial/Lot# 1549 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD ES - EI-SHIP | FAIL MODE EG - SIG HI OR LO |
| Asmnt FMEA 3.4.1.2 | Asmnt FM 2 | FMEA CSE G | FMEA SCSE 1 |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |