1553 to SRC/SFE Interface Proposal:

Updated: 08/14/00:

This is the newest subaddress map of the SFE/SRC to 1553 interface.

SubAddress		Register/Function			R/W	   #words

| 0 | MODE Command | W | Mode Code |
| --- | --- | --- | --- |
| 1 | SRC VME CSR1 | R | 1 word |
|  | SRC Readout Controller CSR1 |  | 1 word |
|  | SFE0 VME CSR1 |  | 16 words |
|  | …. |  |  |
|  | SFE16 VME CSR1 |  |  |
| 2 | SFE Write-only: Reset SFE boards CSR | W | 1 word |
|  | Clear latched errors CSR |  | 1 word |
|  | Reset output FIFO read pointer CSR |  | 1 word |
|  | Reset output FIFO CSR |  | 1 word |
|  | Reset TMCs CSR |  | 1 word |
| 3 | SFE0 Group A Chan Enable Mask | R/W | 32 words |
|  | SFE0 Group A Analog Chan selection |  |  |
|  | …. |  |  |
|  | SFE16 Group A Chan Enable Mask |  |  |
|  | SFE16 Group A Analog Chan selection |  |  |
| 4 | SFE0 Group B Chan Enable Mask | R/W | 32 words |
|  | SFE0 Group B Analog Chan selection |  |  |
|  | …. |  |  |
|  | SFE16 Group B Chan Enable Mask |  |  |
|  | SFE16 Group B Analog Chan selection |  |  |
| 5 | SFE0 Group C Chan Enable Mask | R/W | 32 words |
|  | SFE0 Group C Analog Chan selection |  |  |
|  | …. |  |  |
|  | SFE16 Group C Chan Enable Mask |  |  |
|  | SFE16 Group C Analog Chan selection |  |  |
| 6 | SFE0 Master Controller CSR0 | R/W | 16 words |
|  | …. |  |  |
|  | SFE16 Master Controller CSR0 |  |  |
| 7 | SRC Readout Controller CSR0-3 | R/W | 4 words |
| 8 | SRC Trigger Manager CSR0-6 | R/W | 7 words |
| 9 | SRC HOTLINK CSRs: L2 & L3 | R/W | 2 words |
| A | SFE0 LAT_PRE | R/W | 32 words |
|  | SFE0 ADC_DEL |  |  |
|  | …. |  |  |
|  | SFE16 LAT_PRE |  |  |
|  | SFE16 ADC_DEL |  |  |
| B | SFE0 L1_DEL | R/W | 32 words |
|  | SFE0 L1STRG_LAT |  |  |
|  | …. |  |  |
|  | SFE16 L1_DEL |  |  |
|  | SFE16 L1STRG_LAT |  |  |
| C | Crate Analog Data: A_Crate0 (Voltage, temp, etc.) | R | 7 words |
|  | …. |  |  |
|  | Crate Analog Data: A_Crate6 |  |  |
| D | SRC Board Main CSR0 | R/W | 2 words |
|  | System Status Register |  |  |
| E | SFE0 | All TMCs CSR0 | All TMCs CSR1 | R/W | 32 words |
|  |  | All TMCs CSR2 | All TMCs CSR3 |  |  |
|  | …. |  |  |
|  | SFE16 | All TMCs CSR0 | All TMCs CSR1 |  |  |
|  |  | All TMCs CSR2 | All TMCs CSR3 |  |  |
| F | Interrupt Vectors: IRQ7 | R/W | 3 words |
|  | IRQ6 |  |  |
|  | IRQ5 |  |  |
| 10 | SFE number for Thresholds setting | R/W | 1 word |
| 11 | SFEx Threshold 0 | SFEx Threshold 1 | R/W | 24 words |
|  | …. | …. |  |  |
|  | SFEx Threshold 46 | SFEx Threshold 47 |  |  |
| 12 | SRC Test Pulse Delay | R/W | 1 word |
|  | SRC Test Pulse Xing Preset |  | 1 word |
|  | SRC Test Pulse L1 Xing Preset |  | 1 word |
|  | SFE0 Test Pulse Amplitude |  | 16 words |
|  | …. |  |  |
|  | SFE16 Test Pulse Amplitude |  |  |
| 13 | SLP Delay0 | R/W | 24 words |
|  | SLP Amplitude0 |  |  |
|  | …. |  |  |
|  | SLP Delay11 |  |  |
|  | SLP Amplitude11 |  |  |
| 14 | NOT USED | - | - |
| 15 | NOT USED | - | - |
| 16 | NOT USED | - | - |
| 17 | NOT USED | - | - |
| 18 | NOT USED | - | - |
| 19 | NOT USED | - | - |
| 1A | NOT USED | - | - |
| 1B | NOT USED | - | - |
| 1C | WRITE to 4-Port RAM | W | Multiblock |
| 1D | READ from 4-Port RAM | R | Multiblock |
| 1E | NOT USED | - | - |
| 1F | MODE command | W | Mode Code |

MODE COMMAND CODES:

MC							R/W

| 09 | Reset RAM pointer | (T/R = 1) | None |
| --- | --- | --- | --- |
| 0A | Reset SRC | (T/R = 1) | None |
| 0B | DSP Service Request | (T/R = 1) | None |
| 0C | L2 & L3 FIFO Reset | (T/R = 1) | None |
| 0D | SRC CLR_ERRS | (T/R = 1) | None |
| 0E | SYSRESET | (T/R = 1) | None |
| 0F | - | - | - |

# Text boxes

15 Hz.

Analog

5 words x 16

1-bit fields

18 words

15 Hz.

Digital

19 words