# Stiffness of Strip Lines for Numi Horn 2

Zhijing Tang

November 7, 2001

A finite element model is created to calculate the stiffness of the strip lines for Numi horn number 2.

The width of the strip lines is 8 inches, and the thickness is 3/8 inch, as well as the spaces between the strip lines. Again, by symmetry, only 4 strip lines are modeled. Plate element is used to model the strip lines, beam element is used to model clamps, which are offset by 3.5 inches. At the top of the strip lines, there is a one-inch thick plate to model the fixture.

The model is shown in the figure. The ends connected to horn is assume fixed, and the top plate is moved a distance of 0.013 inch, which is the amount of thermal expansion of the horn in the axial direction. The reaction forces are calculated as shown in the table. Also listed in the table are the reaction forces when the top plate moves in the other two directions. Remember that the total reaction force should be twice the listed value.

Figure. Finite element model of horn 2 strip lines

Table. Reaction forces of the horn 2 strip lines

for a movement of 0.013 inch

x-move

FX  =   16.88750

FY  =  -13.18778

FZ  = -0.9406203

MX  =  -141.3218

MY  =  -157.1583

MZ  =  -358.4100

y-move

FX  =  -13.18778

FY  =   23.44266

FZ  =  0.7255012

MX  =   236.1031

MY  =   130.3883

MZ  =   457.2923

z-move

FX  = -0.9406203

FY  =  0.7255012

FZ  =   17.76504

MX  =   192.1775

MY  =  -282.7687

MZ  =   17.77759

SUMMATION POINT= 0.00000E+00 0.00000E+00  14.000