1.	AIRCRAFT MUST HAVE THE FOLLOWING DOCUMENTS ON BOARD (AS PER FAR 91.9, 91.203 & 23.1589) [“AROW”]:

a.	 CURRENT AIRWORTHINESS CERTIFICATE.

b.	 CURRENT REGISTRATION CERTIFICATE.

c.	 CURRENT AIRPLANE FLIGHT MANUAL OR PILOT'S OPERATING HANDBOOK.

d.	 CURRENT WEIGHT AND BALANCE PAPERWORK.

2.	FOR DAY VFR FLIGHT, THE AIRCRAFT MUST HAVE THE FOLLOWING WORKING INSTRUMENTS AND EQUIPMENT (AS PER FAR 91.205):

a.	 AIRSPEED INDICATOR.

b.	 ALTIMETER.

c.	 MAGNETIC DIRECTION INDICATOR (COMPASS).

d.	 TACHOMETER FOR EACH ENGINE.

e.	 OIL PRESSURE GAUGE FOR EACH ENGINE USING PRESSURE SYSTEM.

f.	 TEMPERATURE GAUGE FOR EACH LIQUID-COOLED ENGINE.

g.	 OIL TEMPERATURE GAUGE FOR EACH AIR-COOLED ENGINE.

h.	 MANIFOLD PRESSURE GAUGE FOR EACH ALTITUDE ENGINE.

i.	 FUEL GAUGE INDICATING QUANTITY OF FUEL IN EACH TANK.

j.	 GEAR POSITION INDICATOR IF AIRCRAFT HAS RETRACTABLE GEAR.

k.	 EMERGENCY LOCATOR TRANSMITTER (REQUIRED IN ALL CAP AIRCRAFT).

3.	FOR NIGHT VFR FLIGHT, THE AIRCRAFT MUST HAVE THE FOLLOWING ADDITIONAL WORKING INSTRUMENTS, AS WELL AS ALL INSTRUMENTS REQUIRED FOR DAY VFR FLIGHT (AS PER FAR 91.205):

a.	POSITION LIGHTS.

b.	ANTICOLLISION LIGHTS.

c.	SPARE FUSES ACCESSIBLE TO THE PILOT IN FLIGHT.

4.	FOR IFR FLIGHT, THE AIRCRAFT MUST HAVE THE FOLLOWING ADDITIONAL WORKING INSTRUMENTS AND EQUIPMENT, AS WELL AS ALL INSTRUMENTS REQUIRED FOR DAY AND NIGHT VFR FLIGHT (AS PER FAR 91.205):

a.	 RADIO AND NAVIGATION EQUIPMENT APPROPRIATE TO FACILITIES USED.

b.	 GYROSCOPIC RATE-OF-TURN INDICATOR (TURN AND BANK OR TURN COORDINATOR).

c.	 SLIP-SKIP INDICATOR (“BALL” IN RATE-OF-TURN INDICATOR).

d.	 CLOCK WITH SWEEP-SECOND HAND OR DIGITAL PRESENTATION.

e.	 GYROSCOPIC PITCH AND BANK INDICATOR (ARTIFICIAL HORIZON).

f.	 GYROSCOPIC DIRECTION INDICATOR (DIRECTIONAL GYRO).

5.	REQUIRED INSPECTIONS (AS PER FAR 43.17 & FAR 91.207):

a.	PITOT-STATIC, ALTIMETER AND TRANSPONDER SYSTEMS CHECKED AND CERTIFIED WITHIN  PRECEDING  24  CALENDAR  MONTHS.

b.	VOR EQUIPMENT OPERATIONALLY CHECKED WITHIN PRECEDING 30 DAYS AND 	FOUND WITHIN TOLERANCE (4 º COMPARISON GROUND OR FLIGHT;  6 º AIRBORNE  	VOR CHECK POINT) FOR IFR FLIGHT.

c.	EMERGENCY LOCATOR TRANSMITTER BATTERY MUST BE REPLACED WHEN 50% OF ITS USEFUL LIFE HAS ELAPSED.

INOPERATIVE  EQUIPMENT    IS  TO  BE  PLACARDED  AS  SUCH   BY  PIC!

CAP AIF  ―  EQP_INST     REV  00  ―  OCT 06	LOCAL  REPRODUCTION  AUTHORIZED	© CIVIL AIR PATROL 2006.   ALL RIGHTS RESERVED.

# Text boxes

EQUIPMENT / INSPECTION /

DOCUMENT  REQUIREMENTS