Technical requirements document

8/30/05

Complete Detector:

Responsible for defining: PM

| Item | Number/description | Spares | Comments |
| --- | --- | --- | --- |
| M64 PMTs | 485 | 65 |  |
| PMT Boxes | 485 | 65 |  |
| Hexes (ID planes) | 196 | 12 | Assume 3% waste in production also |
| OD Modules | 1612 | 89 | Assume 3% waste in production also |
| Frames (2 planes/frame) | 98 |  | About 4.3 m tall |
| Cables per PMT | 8 |  |  |
| HCAL’s | 2.5 cm absorbers, one per plane DS and one per module US |  |  |
| ECAL |  |  |  |
| Lead alloy absorbers | 30 cm from the edge of the ID and 0.2 cm thick |  |  |
| Toroid steel/absorber veto | 10 cm thick |  |  |
| Scint. Strips lengths | 205-400 cm |  |  |
| Two scint planes per module (1 frame per module) |  |  |  |
| 1 active target module has 2 x-layers and one each of U and V layers |  |  |  |
| beam targets the detector dead center | 3400mm off the floor |  | TDR states beam centerline enters the detector at 3.4 meters off the floor |
| Outer detector (OD) | 6 towers, each 1/6 of a hexagon |  | Each tower has 6 slots, nominally 1.6 cm wide to hold the scintillator. |
| OD scint towers | 4 or 6 OD modules or stories stacked radially outward |  |  |
| OD Module | 2 roughly square scint strips nested to make a rectangular package |  |  |
| OD Scint strips | Square, with 1.9cm sides |  | Arranged in rectangular layers of two (TDR fig 57) |
| ID scint planes (hex) | Hexgonal assemblies of 128 strips |  | Each hex is a single view (X, U or V) |
| ID scint. strips | Triangular, 1.7 cm height, 3.3 cm base, with embedded WLS fiber |  | Get drawing from ANna |
| Strongbacks |  |  |  |
| Detector placement | 1.75 m upstream of MINO |  | MINERvA TDR |

Full Module Prototype (FMP):

Responsible for defining: PM

| Item |  | Comments |
| --- | --- | --- |
| Average cable length | 1.31 m | From AT Wide PMT rack prototype, preliminary, assumes all fiber connectors are located on top of the detector. If some connectors are located on the side (say for "U" and "V" oriented scintillators), then this number could jump. Do not know where the connectors will be located that read out OD scintillators. Not scaled to reflect the smaller dimensions of the narrow detector modules. |
| Total cable | 485x8X1.31m = 5.08 Km |  |
| Total length of clear fiber cable | 8X5.08Km=40.6Km |  |

The fractions of cables of each length then, would be: (for whole detector or prototype?)

Cable Length		Fraction

3' 6"			3/14 (.214)

4'			1/7  (.142)

4' 8"			9/14 (.642)

The reason why the fraction is so high for the 4'8" cables is our ignorance of the positioning of the connectors for the OD scintillators.  This is one of the open design questions, so I assigned the longest length to the cables reading out the OD scintillators to be conservative.  The final detector will likely have more than 3 cable lengths (particularly for the narrower modules).

Single Plane Prototype (SPP)  (WBS 1.1, 1.2, 1.3)

Responsible for defining:

|  | need | Spare | Total | Comments |
| --- | --- | --- | --- | --- |

Vertical Slice Test III (VST III): (WBS 1.1, 1.2, 1.4?)

Responsible for defining: Howard Budd

|  | need | Spare | Total | Comments |
| --- | --- | --- | --- | --- |

Outer Detector Scintillator Package Prototype  (WBS1.3, ..)

Responsible for defining: Jeff Nelson

|  | need | Spare | Total | Comments |
| --- | --- | --- | --- | --- |

Quality Control Procedure Prototype  (WBS 1.2, 1.4, …)

Responsible for defining:

|  | need | Spare | Total | Comments |
| --- | --- | --- | --- | --- |

PMT Box Prototype  (WBS 1.5, …)

Responsible for defining: Tony Mann

|  | need | Spare | Total | Comments |
| --- | --- | --- | --- | --- |

PMT Tester Prototype  (WBS1.6,…)

Responsible for defining: Ioanna Niculescue, George Tzanakas

|  | need | Spare | Total | Comments |
| --- | --- | --- | --- | --- |

DAQ/ Electronics Prototypes  (WBS1.7, …)

Responsible for defining: Dave Casper

|  | need | Spare | Total | Comments |
| --- | --- | --- | --- | --- |

OD Frames Prototype  (WBS 1.8, …)

Responsible for defining: Jim Kilmer

|  | need | Spare | Total | Comments |
| --- | --- | --- | --- | --- |

Scale Model Assembly Prototypes  (WBS 1.9)

Responsible for defining: Bob Bradford, Jim Kilmer

|  | need | Spare | Total | Comments |
| --- | --- | --- | --- | --- |

Fiber Weave Pattern schematic (8/8/05)