NOTAMS – WATRS.doc

MISCELLANEOUS WATRS PLUS NOTAMS – 11 July 08

A0151/03 - QXXXX BEACON CODE PROCEDURES IN THE WEST ATLANTIC ROUTE SYSTEM (WATRS AREA EFFECTIVE IMMEDIATELY, ALL AIRCRAFT TRANSITIONING INTO THE WEST ATLANTIC ROUTE SYSTEM (WATRS VIA FIXED ATS ROUTES SHALL REMAIN ON THE LAST ATC-ASSIGNED BEACON CODE. WIE UNTIL UFN. CREATED: 07 MAR 15:05 2003

A0096/08 - QXXXX NEW YORK CENTER OCEANIC IS EXPERIENCING AN UNACCEPTABLY HIGH NUMBER OF ICAO FLIGHT PLANS THAT ARE NOT BEING CORRECTLY ROUTED. OPERATORS AND DISPATCHERS FLIGHT PLANNING WITHIN THE NEW YORK OCEANIC FIR ARE REMINDED OF THE BELOW REQUIREMENTS WHEN OPERATING WITHIN THE NEW YORK OCEANIC FIR UNDER CURRENT OPERATING PROCEDURES AND THOSE PROPOSED FOR JUNE 5, 2008, IN SUPPORT OF THE WATRS PLUS ROUTE STRUCTURE REDESIGN AND SEPARATION REDUCTION. FAILURE TO COMPLY WITH THESE REQUIREMENTS WILL REDUCE THE EFFECTIVENESS AND EFFICIENCY OF THE WATRS PLUS PROJECT AND WILL NEGATIVELY AND NEEDLESSLY AFFECT BOTH PARTICIPATING AND NON-PARTICIPATING AIRCRAFT. OPERATORS SHOULD REVIEW AND COMPLY WITH THE CURRENT AND PROPOSED PROVISIONS LISTED BELOW AND DOCUMENTED IN U.S. DEPARTMENT OF TRANSPORTATION PUBLICATION NOTICES TO AIRMEN DOMESTIC/INTERNATIONAL, DATED FEBRUARY 14, 2008, IN: PART 3: INTERNATIONAL NOTICES TO AIRMEN SECTION 2: INTERNATIONAL OCEANIC AIRSPACE NOTICES. WIE UNTIL 30 JUN 23:59 2008. CREATED: 15 FEB 00:10 2008

A0096/08 - QXXXX SPECIFIC REGION: ATLANTIC PARAGRAPH: NEW YORK FIR SUB-PARAGRAPH: ICAO FLIGHT PLAN ADDRESSING IN THE NEW YORK OCEANIC FIR: ALL FLIGHT ENTERING THE NEW YORK OCEANIC CTA/FIR SHOULD ADDRESS FLIGHT PLANS TO KZWYZOZX. FLIGHTS ENTERING THE NEW YORK OCEANIC CTA/FIR FROM DOMESTIC UNITED STATES AIRSPACE OR BERMUDA SHOULD ADDRESS FLIGHT PLANS TO BOTH KZWYZOZX AND KZNYZQZX THEN RESTATED IN: PART 3: INTERNATIONAL NOTICES TO AIRMEN SECTION 2: INTERNATIONAL OCEANIC AIRSPACE NOTICES SPECIFIC REGION: ATLANTIC PARAGRAPH: OPERATIONAL POLICY AND PROCEDURES SUB-PARAGRAPH 7. FLIGHT PLANNING REQUIREMENTS. B. ICAO FLIGHT PLAN AFTN ADDRESSING FOR OPERATIONS IN THE NEW YORK OCEANIC CTA/FIR (INCLUDING WATRS). ALL FLIGHTS ENTERING THE NEW YORK OCEANIC CTA/FIR SHALL ADDRESS FLIGHT PLANS TO KZWYZOZX. FLIGHTS ENTERING THE NEW YORK OCEANIC CTA/FIR FROM DOMESTIC U.S. AIRSPACE OR BERMUDA SHALL ADDRESS FLIGHT PLANS TO BOTH KZWYZOZX AND KZNYZQZX. IF OPERATORS DO NOT ADDRESS FLIGHT PLANS TO KZWYZOZX, 50 NM LATERAL SEPARATION WILL NOT BE APPLIED TO THEM. THE NOTICE, ALONG WITH OTHER WATRS PLUS INFORMATION IS ALSO AVAILABLE ON UNDER "OPERATING POLICY" ON THE FAA WATRS PLUS WEBPAGE. (HTTP://WWW.FAA.GOV/ABOUT/OFFICE_ORG/HEADQUARTERS_OFFICES/ATO/SERVICE _UNITS/ENROUTE/OCEANIC/WATRS_PLUS/) PLEASE FORWARD ANY QUESTIONS TO PETER HRUZ, NEW YORK CENTER (001) 631-468-1018. WIE UNTIL 30 JUN 23:59 2008. CREATED: 15 FEB 00:11 2008

A0332/08 - QXXXX POSITION REPORTING IN NY OAC/FIR WATRS AREA. EFFECTIVE IMMEDIATELY AND UNTIL FURTHER NOTICE OPERATORS ARE REMINDED THAT WHEN CLEARED DIRECT FROM ONE FIX TO ANTHOER, BOTH FIXES BECOME COMPULSORY REPORTING POINTS, EVEN IF BOTH ARE CHARTED AS NON-COMPULSORY FOR THE ROUTE BEING DEPARTED OR JOINED. EXAMPLE "A" - ROUTE: SQUAD DARUX L456 THANK. SQUAD, DARUS, EMAKO VINSO AND BOXAR WOULD BE COMPULSORY REPORTING POINTS. EXAMPLE "B" - ROUTE: OKONU L454 GRAMN LAMAR. OKONU, PERDO GRAMN AND LAMER WOULD BE COMPULSORY REPORTING POINTS. NOTE: THE EXAMPLES USED ABOVE HIGHLIGHT FIXES THAT WILL BECOME EFFECTIVE ON 5 JUNE 2008 AS PART OF THE WATRS PLUS PROJECT. PLEASE FORWARD ANY QUESTIONS TO: PETER.C.EHRLEIN@FAA.GOV,001-631-468-1021. WIE UNTIL UFN. CREATED: 18 MAY 19:00 2008

A0337/08 - NEW YORK OCEANIC FIR DATA LINK PROCEDURES EFFECTIVE IMMEDIATELY AND UNTIL FURTHER NOTICE. NOTE: THIS NOTAM UPDATES AND SUPERSEDES/REPLACES NOTAM A0338/05 AND THE GUIDANCE IN THE U.S. DEPARTMENT OF TRANSPORTATION, NOTICES TO AIRMEN, DOMESTIC/INTERNATIONAL PUBLICATION, PART 3 INTERNATIONAL NOTICES TO AIRMEN, PAGE 3-INTL-51/52, SECTION TITLED "NEW YORK OCEANIC FIR DATA LINK PROCEDURES". THE NOTICES TO AIRMEN MANUAL WILL CONTAIN THE TEXT OF THIS NOTAM IN THE 3 JULY 2008 EDITION. NEW YORK ARTCC PROVIDES FULL CONTROLLER PILOT DATA LINK COMMUNICATIONS (CPDLC) AND AUTOMATIC DEPENDANT SURVEILLANCE-CONTRACT (ADS-C) SERVICES THROUGHOUT IT'S OCEANIC AIRSPACE TO FANS-1/A CAPABLE FLIGHTS. THE NEW YORK OCEANIC FIR FANS LOGON ADDRESS IS "KZWY". CADS LOGON IS NOT SUPPORTED. FLIGHTS SHOULD USE ADS FOR POSITION REPORTING AND CPDLC FOR ALL OTHER ATC COMMUNICATIONS WHILE IN THE NEW YORK OCEANIC AREA. SEE SECTION 4 OF THIS NOTAM FOR MORE INFORMATION. 1. LOGON/ENTRY PROCEDURES FOR AIRCRAFT ENTERING THE KZWY DATA LINK SERVICE AREA FROM NON-DATA LINK AIRSPACE: PART 1 OF 7. WIE UNTIL UFN. CREATED: 19 MAY 17:33 2008

A0337/08 - 1) LOGON TO KZWY AT LEAT 15 MINUTES BUT NOT MORE THAN 45 MINUTES PRIOR TO ENTERING THE NEW YORK OCEANIC CTA/FIR. 2) PRIOR TO ENTERING THE NEW YORK OCEANIC FIR CONTACT ARINC ON HF OR VHF PROVIDING THE INFORMATION AS OUTLINED IN SECTION 7 BELOW. 2. AIRCRAFT ENTERING THE NEW YORK OCEANIC FIR FROM ADJACENT CPDLC AIRSPACE: CPDLC AND ADS SERVICES WILL BE FORWARDED AUTOMATICALLY BETWEEN NEW YORK, SANTA MARIA, AND GANDER OCA'S. CPDLC CONNECTIONS WILL BE TRANSFERRED APPROXIMATELY 5 MINUITES PRIOR TO THE BOUNDARY CROSSING POINT. PILOTS SHOULD DETERMINE THE STATUS OF THE FANS CONNECTION WHEN CROSSING THE NEW YORK OCEANIC FIR BOUNDARY. END PART 2 OF 7. WIE UNTIL UFN. CREATED: 19 MAY 17:34 2008

A0337/08 - 1) IF "KZWY" IS THE ACTIVE CONNECTION, WHEN CROSSING THE NEW YORK OCEANIC FIR BOUNDARY THE PILOT SHALL: A) CONTACT ARINC ON HF PROVIDING THE INFORMATION AS OUTLINED IN SECTION 7 BELOW. 2) IF "KZWY" IS NOT THE ACTIVE CENTER, WHEN CROSSING THE NEW YORK OCEANIC FIR BOUNDARY THE PILOT SHALL: A) TERMINATE THE CPDLC CONNECTION, THEN LOG-ON TO "KZWY". B) CONTACT ARINC ON HF PROVIDING THE INFORMATION AS OUTLINED IN SECTION 7 BELOW. 3. FLIGHTS OVER FLYING NEW YORK BERMUDA RADAR AIRSPACE PRIOR TO ENTERING NEW YORK BERMUDA RADAR AIRSPACE, AIRCRAFT WILL RECEIVE AN END SERVICE MESSAGE THAT WILL RESULT IN TERMINATION OF CPDLC. AIRCRAFT SHALL RE-LOG-ON TO "KZWY" PRIOR TO RE-ENTERING THE NEW YORK OCEANIC CTA/FIR WHEN THEY ARE ADVISED BY ATC TO CONTACT ARINC ON HF. 4. POSITION REPORTS - POSITION REPORTS SHOULD BE MADE VIA ADS. THE TWO TYPES OF ADS CONTRACTS THAT WILL BE ESTABLISHED WITH EACH AIRCRAFT ARE A TWENTY (20) MINUTE PERIODIC REPORT RATE AND A FIVE (5) MILE LATERAL DEVIATION EVENT. THIS IS IN ADDITION TO NORMAL WAYPOINT REPORTS. OPERATORS SHOULD NOT USE CPDLC FOR POSITION REPORTS BUT IT SHOULD BE USED FOR ALL OTHER ATC COMMUNICATIONS. POSITION REPORTS SHOULD BE MADE VIA HF IF ADS IS NOT AVAILABLE. KZWY CANNOT ACCEPT CPDLC POSITION REPORTS CONTAINING LATITUDE AND LONGITUDE IN THE ARINC 424 FORMAT (E.G. 4050N) END PART 3 OF 7. WIE UNTIL UFN. CREATED: 19 MAY 17:35 2008

A0337/08 - 5. CONTROLLER PILOT DATA LINK COMMUNICATIONS (CPDLC) FAILURE IN THE EVENT OF DATA LINK FAILURE OR OUTAGES, FLIGHT CREWS SHALL CONTACT NEW YORK RADIO VIA HF VOICE FOR ROUTINE COMMUNICATIONS. SATVOICE CONTACT SHOULD BE LIMITED TO DISTRESS AND URGENCY SITUATIONS 6. EXIT PROCEDURES FOR AIRCRAFT EXITING THE KZWY DATA LINK SERVICE AREA TO ADJACENT NON-CPDLC AIRSPACE AIRCRAFT APPROACHING NEW YORK CENTER DOMESTIC, NEW YORK CENTER BERMUDA RADAR, SAN JUAN, PIARCO, JACKSONVILLE, MIAMI, MONCTON, AND GANDER DOMESTIC CAN EXPECT A CPDLC UPLINK MESSAGE CONTAINING THE VHF FREQUENCY ASSIGNMENT FOR THE NEXT FACILITY. CPDLC END SERVICE WILL BE SENT APPROXIMATELY 5 MINUTES PRIOR TO THE BOUNDARY CROSSING POINT. END PART 4 OF 7. WIE UNTIL UFN. CREATED: 19 MAY 17:38 2008

A0337/08 - 7. HIGH FREQUENCY (HF) AND VERY HIGH FREQUENCY (VHF) COMMUNICATIONS REQUIREMENTS PRIOR TO ENTERING THE KZWY OCEANIC AREA 1) CONTACT NEW YORK RADIO (ARNIC) ON HF OR VHF AND IDENTIFY THE FREQUENCY WHICH CALLS ARE BEING MADE ON. 2) IDENTIFY THE FLIGHT AS ADS AND/OR CPDLC CONNECTED. 3) STATE THE NAME OF THE NEXT CTA/FIR TO BE ENTERED ALONG WITH THE LATITUDE AND LONGITUDE OR WAYPOINT EXIT POINT LEAVING THE ZNY FIR. 4) REQUEST A SELCAL CHECK. 5) EXPECT TO RECEIVE PRIMARY AND SECONDARY HF FREQUENCY ASSIGNMENTS FROM NEW YORK RADIO FOR THE ROUTE OF FLIGHT WITHIN THE DATA LINK SERVICE AREA. END PART 5 OF 7. WIE UNTIL UFN. CREATED: 19 MAY 17:38 2008

A0337/08 - IF THE FLIGHT WILL EXIT ZNY OCEANIC AIRSPACE INTO DOMESTIC AIRSPACE (INCLUDING OVERHEAD NEW YORK BERMUDA RADAR) 1) IDENTIFY THE FLIGHT AS ADS AND/OR CPDLC CONNECTED. 2) STATE THE TRACK LETTER IF OPERATING ON THE ORGANIZED TRACK SYSTEM (OTS). 3) STATE THE NAME OF THE NEXT CTA/FIR TO BE ENTERED ALONG WITH THE LATITUDE AND LONGITUDE OR WAYPOINT EXIT POINT LEAVING THE ZNY FIR. 4) REQUEST A SELCAL CHECK. NOTE 1: ARINC MAY REQUIRE FLIGHTS TO CONTACT THEM AT 60 WEST FOR HF FREQUENCY UPDATES. END PART 6 OF 7. WIE UNTIL UFN. CREATED: 19 MAY 17:39 2008

A0337/08 - NOTE 2: HF FREQUENCY UPDATES ARE REQUIRED DUE TO FREQUENCY PROPAGATION. NOTE 3: PILOTS MUST MAINTAIN SELCAL WATCH AT ALL TIMES WITHIN THE NEW YORK OCEANIC FIR. EXAMPLE TRANSMISSIONS RANDOM ROUTE: "NEW YORK RADIO, (N12345), ON (11396). ADS AND CPDLC CONNECTED, EXIT POINT (SUMRS), (MIAMI) NEXT, SELCAL (AD-CD) ." ORGANIZED TRACK: "NEW YORK RADIO, (N12345), NAT TRACK (WHISKEY), EXIT POINT (44N50W), (GANDER) NEXT, SELCAL (AB-CD)" 8. QUESTIONS - DIRECT QUESTIONS TO THE NEW YORK CENTER AIRSPACE AND PROCEDURES OFFICE, TELEPHONE: 001-631-468-1018, FAX 001-631-468-4229 DURING NORMAL BUSINESS HOURS, MONDAY-FRIDAY. DURING ALL OTHER TIMES, CONTACT NEW YORK CENTER NORTH ATLANTIC SUPERVISOR: 001-631-468-1496, OR AERONAUTICAL RADIO SUPERVISOR: 001-631-244-2483. ADDITIONAL INFORMATION CONCERNING CPDLC CAN BE FOUND AT: HTTP://WWW.FAA.GOV/ATS/ATO/130.HTM. END PART 7 OF 7. WIE UNTIL UFN. CREATED: 19 MAY 17:40 2008

A0369/08 - CLARIFICATION TO NOTAM A0367/08 "WATRS PLUS FAA NAVIGATION CHART DISCREPANCIES" THIS NOTAM PROVIDES A CLARIFICATION TO NOTAM A0367/08 "WATRS PLUS FAA NAVIGATION CHART DISCREPANCIES" PUBLISHED (29 MAY 2008). NOTAM A0367/08 INDICATED IN "CATEGORY A: FIXES REQUIRING DELETION" OF THE "COMMENTS" SECTION OF "ITEM A3 (GRANN INTERSECTION)" AND "ITEM A4 (KRAFT INTERSECTION)", THAT THE SAN JUAN VERMO4 SID WAS NOTAMED UNUSABLE. THE VERMO4 SID WAS NOT NOTAMED UNUSABLE, ONLY THE "GRANN" AND "KRAFT" TRANITIONS OF THE VERMO4 SID WERE NOTAMED UNUSABLE. PLEASE MAKE THE FOLLOWING TWO CORRECTIONS TO THE A0367/08 NOTAM. 1. CATEGORY A: FIXES REQUIRING DELETION, ITEM A3, FIX NAME: GRANN. COMMENT SHOULD READ "GRANN IS A FIX ON THE VERMO4 SID FROM SAN JUAN, THIS TRANSITION OF THE VERMO4 SID HAS BEEN NOTAMED UNUSABLE, THE FIX WILL BE DELETED IN CONJUNCTION WITH THE SID BEING MODIFIED". 2. CATEGORY A: FIXES REQUIRING DELETION, ITEM A4, FIX NAME: KRAFT. COMMENT SHOULD READ "KRAFT IS A FIX ON THE VERMO4 SID FROM SAN JUAN, THIS TRANSITION OF THE VERMO4 SID HAS BEEN NOTAMED UNUSABLE, THE FIX WILL BE DELETED IN CONJUNCTION WITH THE SID BEING MODIFIED". OPERATORS ARE ENCOURAGED TO OBATIN CURRENT INFORMATION ON THE WATRS PLUS PROJECT AT THE FOLLOWING WEB SITE: HTTP://WWW.FAA.GOV/ABOUT/OFFICE_ORG/HEADQUARTERS_OFFICES/ATO/SERVICE_ UNITS/ENROUTE/OCEANIC/WATRS_PLUS. 30 MAY 16:06 2008 UNTIL UFN. CREATED: 30 MAY 16:23 2008

A0370/08 - UPDATE TO WATRS PLUS TRANSITION ROUTE DEFINITION AND PROCEDURES (NOTAM A0308/08) THIS NOTAM MODIFIES CURRENT NOTAM A0308/08 TITLED; "WATRS PLUS TRANSITION ROUTE DEFINITION AND PROCEDURES". THE ONLY MATERIAL CHANGE THAT THIS NOTAM TRANSMITS FROM THE ORIGINAL IS THE DELETION OF THE FOLLOWING STATEMENT: UNDER THE SECTION "TIME SCHEDULE FOR 5 JUNE 2008", DELETE THE "AT 1000Z" SECTION --STARTING POINT OF DELETION--- "AT 1000Z: AT 1000Z TIME, AIRCRAFT MAY START FILING WATRS PLUS ROUTES (E.G., "LIMA" AND "MIKE" ROUTES) USING NORMAL ROUTE FILING PRACTICES (I.E., NO LONGER NECESSARY TO FILE INDIVIDUAL STAND-ALONE FIXES)." ---ENDING POINT FOR DELETION--- THE INTENT OF THE DELETION OF THE ABOVE STATEMENT IS TO ELIMINATE A POSSIBLE PROCEDURAL INCONSISTENCY AS TO WHEN AN OPERATOR MAY START FILING FLIGHT PLANS UTILIZING THE NEW WATRS PLUS ROUTE STRUCTURE. NOTAM A0308/08 STATES THAT "AIRCRAFT ENTERING WATRS PLUS AIRSPACE AT/AFTER 1100Z INTENDING TO OPERATE ON OCEANIC ROUTES SHALL HAVE FILED AND SHALL BE CLEARED ON WATRS PLUS ROUTES (E.G. L-456, M-203)". TO MEET THIS REQUIREMENT, OPERATORS ARE NOT REQUIRED TO WAIT UNTIL 1000Z ON 5 JUNE 2005 TO START FILING THE NEW WATRS PLUS ROUTES. OPERATORS ARE ENCOURAGED TO OBTAIN CURRENT INFORMATION ON THE WATRS PLUS PROJECT AT THE FOLLOWING WEB SITE: HTTP://WWW.FAA.GOV/ABOUT/OFFICE_ORG/HEADQUARTERS_OFFICES/ATO/SERVICE_ UNITS/ENROUTE/OCEANIC/WATRS_PLUS. 30 MAY 15:49 2008 UNTIL 05 JUL 23:59 2008. CREATED: 30 MAY 16:26 2008

A0444/08 - IT HAS COME TO THE ATTENTION OF NEW YORK CENTER THAT CERTAIN AIRCRAFT ARE NOT DEPICTING THE ACCURATE LATITUDE AND LONGITUDE FOR NEW WATRS PLUS FIXES SQUAD AND KINGG IN THEIR FMS DATABASES. ALL OPERATORS ARE ADVISED THAT KZNY NOTAM A0385/08, ISSUED 03 JUNE 2008, IS CURRENT, AND DEPICTS THE CURRENT AND CORRECT LATITUDES/LONGITUDES FOR THOSE FIXES, AS WELL AS FOR FIX OKONU. THAT NOTAM HAD UPDATED A PREVIOUS VERSION AS THE CONTENT EXPLAINS. PLEASE ENSURE THAT ALL FMS DATABASES ARE UPDATED AND INCOMPLIANCE WITH THE PROVISIONS OF NOTAM A0385/08. REGARDS, NEW YORK ARTCC. 03 JUL 15:00 2008 UNTIL UFN. CREATED: 03 JUL 14:52 2008

A0414/08 - QXXXX NEW YORK OCEANIC WATERS PLUS FLIGHT PLANNING CLARIFICATION: ROUTING VIA M204 SOORY EFFECTIVE: IMMEDIATELY AND UNTIL FURTHER NOTICE AIRCRAFT FLIGHT PLANNING EITHER: (EASTBOUND) VIA M204 SOORY OR, (WESTBOUND) VIA SOORY M204 ARE NOT REQUIRED TO FILE A 06000W COORDINATE. THE CLOSE PROXIMITY OF SOORY INTERSECTION TO 06000W WILL SUFFICE AS A REPORTING POINT FOR 06000W. PLEASE FORWARD ANY QUESTIONS TO: PETER.C.EHRLEIN@FAA.GOV, OR 001(631)468-1018. WIE UNTIL UFN. CREATED: 16 JUN 15:00 2008