MSFC PRACA : 2003-02-12 08:41

MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A15785 | In-Flight Anomaly Number -- | Contractor Report Number E-157 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title TRANSDUCER FAILED ATP |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT -- | Sys_Lvl N | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE LH2 ULLAGE PRESSURE | PART# PD7400098-089 | SER/LOT# 1618 | MANUFACTURER GULTON |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EL - SHORT | Cause ESW - EI-SHIP-WORK |
| System ELECTRICAL | Defect DD - DETACH | Material C - EEE | Work Contact JOHN ADAMS | Fail Date 01/19/1994 |
| Received at MSFC 01/24/1994 | Date Isolated 01/19/1994 | FMEA Reference 3.4.1.2 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location GULTON | Symptom EL - SHORT | Time Cycle -- |
| Effectivity Text NONE |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 04/12/1994 | CN RSLV SBMT 03/03/1994 | Defer Date 01/25/1994 | Add Date 01/24/1994 | R/C Codes 0 - EXPL -- -- |
| Assignee |
| Design R. MOYE | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR P. COUNTS |
| Approval |
| Design R. MOYE | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR P. COUNTS |
| PAC Assignee B. HURST | PAC Review Complete BH | MSFC Closure Date 03/10/1994 | Status E - CLOSED-E | F/A Completion 01/10/1994 |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID T-119553 |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description A TRANSDUCER FAILED A TEST OF APPLIED PRESSURE VERSUS OUTPUT VOLTAGE ACCURACY DURING SUPPLIER ACCEPTANCE TESTING(ATP). THE TRANSDUCER INDICATED A LOWER PRESSURE THAN THAT WHICH WAS APPLIED CRITICALITY: THE TRANSDUCER IS LISTED AS CRIT. 1R: FMEA ITEM CODE 3.4.1.2 "FAILS WITH LOW READING" NOTE: THE TRANSDUCER IS LIMITED LIFE CONTROLLED * REVISION "B" CLOSES ALL TASKS. SEE ASTERISKS FOR CHANGES |
| Contractor Investigation/Resolution GENERAL: AN LH2 ULLAGE PRESSURE TRANSDUCER WAS BEING TESTED AT THE SUPPLIER GULTON-STATHAM TRANSDUCERS, PER ACCEPTANCE TEST PLAN(ATP) 3031-13803 THE TRANSDUCER FAILED THE CALIBRATION ACCURACY TEST OF ATP PARAGRAPH 5.2 WHICH FOLLOWS THE PROOF PRESSURE TEST. AT AN APPLIED PRESSURE OF 32 PSIA THE OUTPUT VOLTAGE WAS 2.427 V; THE MINIMUM ACCEPTABLE VOLTAGE IS 2.450 V THE TRANSDUCER IS USED TO MEASURE THE ULLAGE PRESSURE IN THE LIQUID HYDROGEN PROPELLANT TANK DURING BOTH GROUND PROPELLANT LOADING AND IN FLIGHT. THE TRANSDUCER IS ATTACHED TO A SHOCK MOUNT ON THE FORWARD DOME OF THE HYDROGEN TANK, WITHIN THE INTERTANK. THE TRANSDUCER COVERS THE RANGE OF 12 TO 52 PSIA. THE ORBITER PROVIDES 5 VDC TO THE TRANSDUCER AND RECEIVES A VOLTAGE FROM THE TRANSDUCER PROPORTIONAL TO THE ULLAGE PRESSURE. THE PRESSURE MEASUREMENT IS USED TO CONTROL THE SPACE SHUTTLE MAIN ENGINE(SSME) GASEOUS HYDROGEN FLOW CONTROL VALVE TASK I. FAILURE INVESTIGATION THE TRANSDUCER FAILURE WAS DOCUMENTATED ON MARS T-119553, ITEM 4. THE MARS WILL BE DISPOSITIONED FOR FAILURE ANALYSIS TO BE PERFORMED AT GULTON-STATHAM RESPONSIBILITY: J. ADAMS/3741 -- D. WESTPHAL/3740 L. COLON/4120--J. COOL/.4120 G. PICHON/3830--M. COMBS/3830 * COMPLETE * CLOSURE STATEMENT ANALYSIS IDENTIFIED THE "STOP SHAFT" OF THE TRANSDUCER MECHANISM AS HAVING BECOME LOOSE. THE STOP SHAFT SERVES TO BOTH LIMIT THE CAPSULE TRAVEL AND TO SECURE THE WIPER DRIVE MECHANISM TO THE CAPSULE. THE LOOSENESS OF THE STOP SHAFT ACCOUNTS FOR THE CALIBRATION SHIFT FOLLOWING PROOF PRESSURE TEST. EPOXY GLUE, INTENDED AS STAKING TO PREVENT LOOSENING OF THE SHAFT, WAS STILL IN PLACE ON THE SHAFT BUT NO LONGER ADHERED TO THE ADJACENT PARTS A DENT WAS FOUND IN THE TRANSDUCER CASE; THIS INTRODUCED THE POSSIBILITY OF HANDLING DAMAGE INDUCED MECHANICAL SHOCK HAVING CAUSED THE EPOXY BOND TO FAIL. THE TRANSDUCER HAD FAILED IN SUPPLIER ATP FOLLOWING REWORK OF THE TRANSDUCER LEAD WIRES; THIS ALLOWS THE POSSIBILITY OF REWORK INDUCED FAILURE. OTHER POSSIBLE CAUSES ALSO EXIST. REVIEW OF THE SUPPLIERS MANUFACTURING PROCESSES FAILED TO DISCOVER ANY ESCAPE WHICH COULD HAVE DIRECTLY CAUSED THE FAILURE TASK CLOSED TASK II. CORRECTIVE ACTION *NO CORRECTIVE ACTION FOR THE FAILURE IS POSSIBLE. THE ROOT CAUSE IS UNKNOWN. THE TRANSDUCER FAILED FOLLOWING REWORK OF THE LEAD WIRES REVIEW OF THE SUPPLIERS DOCUMENTATION AND DIRECT OBSERVATION OF THE LEAD WIRE REWORK PROCESSES, ACCOMPLISHED AS PART OF CAPS E-153, FOUND NO DEFICIENCIES OR LACK OF CONTROLS. REVIEW OF THE FAILURE HISTORY OF THIS TRANSDUCER TYPE FOUND NO SIMILAR PREVIOUS FAILURES TASK CLOSED TASK III. CLEARANCE OF EFFECTIVITIES *THIS IS AN EXPLAINED CLOSURE OF THE CAPS ALL ETS CLEARED. THE TRANSDUCER FAILED DURING THE SUPPLIER ACCEPTANCE TESTS AND ALL DELIVERED TRANSDUCERS HAVE PASSED THE TESTS NOTE: THIS IS ALSO THE DEFERRAL RATIONALE TASK CLOSED TASK IV. CAPS CLOSURE SUMMARY *WHILE THE MECHANICAL DEFECT RESPONSIBLE FOR THE FAILURE WAS IDENTIFIED, THE ROOT CAUSE REMAINS UNKNOWN. THIS PRECLUDES EFFECTIVE CORRECTIVE ACTION. REVIEW OF THE SUPPLIERS PROCESSES FOUND NO DEFICIENCIES. THERE HAVE BEEN NO PREVIOUS FAILURES DUE TO THIS TYPE OF PROBLEM. THE SUPPLIER ATP IS AN EFFECTIVE SCREEN FOR THE PROBLEM TASK CLOSED THIS CAPS IS CLOSED |
| MSFC Response/Concurrence 1/24/94 - DEFERRAL RATIONALE: BASED ON THE INFORMATION IN "TASK III. CLEARANCE OF EFFECTIVITIES" (ABOVE), THIS PROBLEM HAS BEEN DEFERRED FOR THE NEXT SIX (6) MONTHS PER NSTS 08126, REVISION E, PARAGRAPH 3.3.10.1, ITEM D WHICH STATES "THE PROBLEM CONDITION IS CLEARLY SCREENED BY PREFLIGHT CHECKOUT OR SPECIAL TESTS (I.E., FAILURE MODE SHOULD NOT OCCUR FOLLOWING THE TEST)." APPROVED:__PARKER V. COUNTS_(SIGNED) DATE:__1/25/94____________ PARKER V. COUNTS ET PROJECT MANAGER |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A15785 | IFA# -- | Contractor RPT# E-157 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD480098-089 | Asmnt Part Name LH2 PRES TRANSDUCER | Asmnt Serial/Lot# 1618 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD ESW - EI-SHIP-WORK | FAIL MODE EL - SHORT |
| Asmnt FMEA 3.4.1.2 | Asmnt FM 2 | FMEA CSE G | FMEA SCSE 4 |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |