WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A13494 | In-Flight Anomaly Number -- | Contractor Report Number E-142-2 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title TRANSDUCER FAILED INSULATION RESISTANCE TEST DURING ATP |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT -- | Sys_Lvl N | Misc Codes A (1) B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE TEMP. TRANSDUCER | PART# PD7400244-029 | SER/LOT# 1633 | MANUFACTURER ROSEMOUNT |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EL - SHORT | Cause ETW - EI-TEST-WORK |
| System ELECTRICAL | Defect CN - CONTAM | Material C - EEE | Work Contact J. ADAMS | Fail Date 02/15/1991 |
| Received at MSFC 02/19/1991 | Date Isolated 02/18/1991 | FMEA Reference 3.9.13.3 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location ROSEMOUNT | Symptom EV - NOT-TO-SPEC | Time Cycle -- |
| Effectivity Text DEFERRAL WILL EXPIRE 08/26/91; CLOSED 05/15/91 |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary VENDOR ERROR - THE PROBABLE CAUSE WAS HANDLING DAMAGE DURING VENDOR ACCEPTANCE TEST |
| Last MSFC Update 02/13/1995 | CN RSLV SBMT 04/11/1991 | Defer Date -- | Add Date 02/20/1991 | R/C Codes 2 - MFG -- -- |
| Assignee |
| Design R. MOYE | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. LADNER |
| Approval |
| Design R. MOYE | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. LADNER |
| PAC Assignee T. HESTER | PAC Review Complete TH | MSFC Closure Date 05/15/1991 | Status C - CLOSED | F/A Completion 04/11/1991 |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID MARS T-115404 |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary CLOSED, 04/11/91 |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description A TRANSDUCER FAILED THE INSULATION RESISTANCE TEST SEGMENT OF THE VENDOR ACCEPTANCE TEST PLAN. THE TRANSDUCER HAD AN INSULATION RESISTANCE LESS THAN THE REQUIRED 50 MEGOHMS AT 50 VDC. THE TRANSDUCER IS LIMITED LIFE CONTROLLED SERIAL NUMBER 1633 FAILED DURING VENDOR ACCEPTANCE TEST PER ROSEMOUNT PROCEDURE D88309178, PARAGRAPH 4.2. THE UNIT HAD AN INSULATION RESISTANCE OF 2 MEGOHMS; THE REQUIREMENT IS 50 MEGOHMS OR GREATER AT 50 VDC. THE FAILURE WAS DOCUMENTED ON MARS T-115404 |
| Contractor Investigation/Resolution |
| MSFC Response/Concurrence THE PD7400244-029 TRANSDUCER IS BEING PROCURED FOR USE IN THE NOSE CONE AND INTERTANK AREAS OF THE ET TO MONITOR GAS TEMPERATURE. THE TRANSDUCER IS AUTHORIZED FOR USE ON ET-61/SUBSEQUENT 2/26/91 - DEFERRAL RATIONALE: THIS PROBLEM REPORT IS DEFERRED FOR THE NEXT SIX MONTHS PER NSTS 07700, VOLUME XI, PARAGRAPH 3.4.1, ITEM C AND NSTS 08126, REV. D, PARAGRAPH 3.3.10.1, ITEM A WHICH STATES, "THE PROBLEM IS NOT APPLICABLE TO THE FLIGHT(S) (SYSTEM NOT INSTALLED OR USED ON THE FLIGHT)." THESE TRANSDUCERS ARE AUTHORIZED FOR USE ONLY ON ET-61/SUBSEQUENT ***APPROVED BY ET PROJECT MANAGER, G. LADNER ON 02/26/91*** TASK I. FAILURE INVESTIGATION INVESTIGATIVE ACTIONS ACCOMPLISHED BY THE VENDOR AT THE TIME OF THE FAILURES, AND DOCUMENTED ON THE MARS, DETERMINED THAT THE CAUSE OF BOTH FAILURES WAS MOISTURE SENSITIVITY OF THE SENSING ELEMENT TIP. WIPING THE SENSING ELEMENTS WITH A TOWEL FOLLOWING THE WET INSULATION RESISTANCE TEST FAILURES RESTORED THE PROPER INSULATION RESISTANCES THE PROBABLE CAUSE OF THE FAILURES WAS HANDLING DAMAGE DURING THE VENDOR ACCEPTANCE TEST AS BOTH UNITS HAD PASSED IN-PROCESS IR TESTS IMMEDIATELY PRIOR TO BEGINNING THE ACCEPTANCE TEST SEQUENCE TASK CLOSED TASK II. CORRECTIVE ACTION THE FAILURES WERE THE RESULT OF HANDLING DAMAGE/PERSONNEL ERROR ROSEMOUNT HAS DEVELOPED NON-METALLIC PROTECTIVE COVERS AND A CARRYING TRAY TO REDUCE THE LIKELIHOOD OF DAMAGE. THE COVERS AND TRAYS ARE REQUIRED FOR ALL FUTURE PRODUCTION. REFERENCE: ROSEMOUNT, INC., MANUFACTURING CHANGE ORDER 26586 TASK CLOSED TASK III. CLEARANCE OF EFFECTIVITIES ALL ETS CLEARED. THE TRANSDUCERS FAILED DURING VENDOR ACCEPTANCE TESTING AND ALL INSTALLED TRANSDUCERS HAVE PASSED THE VENDOR TESTS THERE ARE NO PD7400244 TRANSDUCERS ON DELIVERED ETS; THEY ARE AUTHORIZED FOR ET-61/SUBSEQUENT TASK CLOSED TASK IV. CLOSURE SUMMARY THE TRANSDUCERS FAILED DURING VENDOR ACCEPTANCE TESTING. THE FAILURES WERE THE RESULT OF HANDLING DAMAGE WHICH OCCURRED DURING THE ACCEPTANCE TEST. THE MANUFACTURER HAS DEVELOPED PROTECTIVE COVERS AND TRAYS TO REDUCE HANDLING DAMAGE. THE COVERS AND TRAYS WILL BE USED IN ALL FUTURE PRODUCTION TASK CLOSED **CLOSURE RATIONALE SUBMITTED FOR MSFC REVIEW** **CLOSED BY ET PROJECT MANAGER, G. LADNER ON 05/15/91** |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A13494 | IFA# -- | Contractor RPT# E-142-2 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD7400244-029 | Asmnt Part Name TEMP. TRANSDUCER | Asmnt Serial/Lot# 1633 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD ETW - EI-TEST-WORK | FAIL MODE EL - SHORT |
| Asmnt FMEA 3.9.13.3 | Asmnt FM 3 | FMEA CSE B | FMEA SCSE 2 |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |