WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A14060 | In-Flight Anomaly Number -- | Contractor Report Number E-146 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title TEMPERATURE TRANSDUCER FAILED INSULATION RESISTANCE TEST |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT -- | Sys_Lvl N | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE TEMPERATURE TRNSDCR | PART# PD7400244-029 | SER/LOT# 1634 | MANUFACTURER ROSEMOUNT |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EL - SHORT | Cause ESW - EI-SHIP-WORK |
| System ELECTRICAL | Defect DA - ROUGH | Material D - DIE | Work Contact J. ADAMS | Fail Date 09/12/1991 |
| Received at MSFC 09/13/1991 | Date Isolated 09/12/1991 | FMEA Reference 3.9.10.3 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location ROSEMOUNT | Symptom EL - SHORT | Time Cycle -- |
| Effectivity Text ET-61/SUBSEQUENT |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date 01/15/1992 | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary FAILURE ANALYSIS COMPLETED; PROBABLE CAUSE: HANDLING DAMAGE |
| Last MSFC Update 03/17/1992 | CN RSLV SBMT 01/24/1992 | Defer Date 04/17/1992 | Add Date 09/18/1991 | R/C Codes 0 - EXPL -- -- |
| Assignee |
| Design R. MOYE | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. LADNER |
| Approval |
| Design R.D. MOYE | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. LADNER |
| PAC Assignee T. HESTER | PAC Review Complete TH | MSFC Closure Date 02/07/1992 | Status C - CLOSED | F/A Completion 01/16/1992 |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID MARS T-117700 |
| Related Document Title -- |
| Related Document Type -- | Related Document ID E-134, E-136, E-142 |
| Related Document Title PREVIOUS CAPS |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary OPEN |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description A TRANSDUCER FAILED THE INSULATION RESISTANCE TEST SEGMENT OF THE VENDOR ACCEPTANCE TEST PLAN. THE TRANSDUCER HAD AN INSULATION RESISTANCE LESS THAN THE REQUIRED 50 MEGOHMS AT 50 VDC. FMEA CODE 3.9.10.3 ADDRESSES TRANSDUCERS IN THE NOSE CONE; FMEA CODE 3.9.13.3 ADDRESSES TRANSDUCERS IN THE INTERTANK |
| Contractor Investigation/Resolution |
| MSFC Response/Concurrence GENERAL: THE PD7400244-029 TRANSDUCERS ARE BEING PROCURED FOR USE IN THE NOSE CONE AND INTERTANK AREAS OF THE ET TO MONITOR GAS TEMPERATURE. THE TRANSDUCERS ARE AUTHORIZED FOR USE ON ET-61/SUBSEQUENT SERIAL NUMBER 1634 FAILED DURING VENDOR ACCEPTANCE TEST PER ROSEMOUNT PROCEDURE D8830178, PARAGRAPH 4.2. THE UNIT HAD AN INSULATION RESISTANCE OF 10 MEGOHMS; THE REQUIREMENT IS 50 MEGOHMS OR GREATER AT 50 VDC. THE FAILURE WAS DOCUMENTED ON MARS T-117700 TASK I. FAILURE INVESTIGATION THE FAILURE AND THE ASSOCIATED CAUSES ARE BEING INVESTIGATED FIRST ECD: OCTOBER 4, 1991 SECOND ECD: OCTOBER 31, 1991 THIRD ECD: JANUARY 15, 1992* * STATUS - THE ATP TEST METHODS ARE BEING EVALUATED AS A POSSIBLE FAILURE CAUSE COMPLETED: JANUARY 16, 1992 CLOSURE STATEMENT INVESTIGATION BY ROSEMOUNT PERSONNEL FOUND HANDLING DAMAGE TO THE PARYLENE -C COATING ON THE TIP OF THE SENSING ELEMENT OF THE TRANSDUCER DUE TO DIFFICULTIES DURING THE INVESTIGATION, THE POINT IN TIME AT WHICH DAMAGE TO THE COATING OCCURRED WAS NOT DETERMINED. THE DAMAGE MAY HAVE OCCURRED DURING ATP OR DURING THE INVESTIGATION WHICH FOLLOWED REFERENCE: MARS T-117700. HOWEVER, FAILURE ANALYSES ASSOCIATED WITH PREVIOUS CAPS ON THIS TRANSDUCER DESIGN HAVE SHOWN THAT DAMAGE TO THE COATING CAN RESULT IN INSULATION RESISTANCE FAILURES. ROSEMOUNT FOUND NO TECHNICAL PROBLEMS WITH THE ATP TEST METHODS WHICH WOULD INDUCE FALSE FAILURE INDICATIONS TASK CLOSED TASK II. CORRECTIVE ACTION NO CORRECTIVE ACTION IS REQUIRED. AS A PART OF THE CORRECTIVE ACTION ASSESSMENT FOR CAPS E-136C, ELECTRICAL ENGINEERING, DETERMINED THAT THE FAILURE RATE FOR SUCH DEFECTS WILL REMAIN LOW AND DOES NOT JUSTIFY A CHANGE TO THE SENSOR DESIGN. ROSEMOUNT IMPLEMENTED THE USE OF PROTECTIVE COVERS AND CARRYING TRAYS TO REDUCE THE LIKELIHOOD OF HANDLING DAMAGE AS PART OF THE CORRECTIVE ACTION FOR CAPS E-142 ROSEMOUNT ALSO TOOK ACTIONS TO MAKE THEIR WORKERS MORE AWARE OF THE DELICACY OF THE TRANSDUCERS, ALTHOUGH THIS WAS NOT FORMALLY DOCUMENTED THE FAILURE DOCUMENTED ON THIS CAPS IS THE FIFTH VENDOR ATP INSULATION RESISTANCE FAILURE ATTRIBUTED TO HANDLING DAMAGE SINCE PARYLENE -C COATING WAS ADDED TO THE SENSING ELEMENT BY DESIGN CHANGE. A TOTAL OF EIGHTY-FOUR TRANSDUCERS HAVE BEEN SUBMITTED TO VENDOR ATP SINCE THE PARYLENE -C COATING WAS ADDED TASK CLOSED TASK III. CLEARANCE OF EFFECTIVITIES ALL ETS CLEARED. THE TRANSDUCERS FAILED DURING VENDOR ACCEPTANCE TESTING AND ALL INSTALLED TRANSDUCERS HAVE PASSED THE VENDOR TESTS TASK CLOSED ****************************************************************** * 10/17/91 - DEFERRAL RATIONALE THIS PROBLEM REPORT IS DEFERRED FOR THE NEXT SIX MONTHS BY THE FOLLOWING RATIONALE: "THE PROBLEM IS NOT APPLICABLE TO THE FLIGHTS (SYSTEM NOT INSTALLED OR USED ON THE FLIGHTS PLANNED FOR THIS TIME PERIOD)." APPROVAL: ___GERALD C. LADNER (SIGNED)_____ DATE: ____10/17/91______ GERALD C. LADNER ET PROJECT MANAGER PAC NOTE: 01/10/92 - ET-61 WAS ACCEPTED BY NASA ON FORM DD-250 ON 10/15/91. THIS ET HAS SUBJECT ROSEMOUNT TRANSDUCER(S) INSTALLED THEREFORE, THE SENTENCE "THERE ARE NO PD7400244 TRANSDUCERS ON DELIVERED ETS; THEY ARE AUTHORIZED FOR ET-61/SUBSEQUENT." WAS REMOVED FROM THE CLEARANCE OF EFFECTIVITIES PARAGRAPH BY REVISION B TO THE CAPS (01/09/92) CONCUR: _______GERALD C. LADNER_(SIGNED)____ DATE:___1/13/92_______ GERALD C. LADNER ET PROJECT MANAGER TASK IV. CLOSURE SUMMARY THE PROBABLE CAUSE OF THE FAILURE WAS HANDLING DAMAGE DURING VENDOR ATP THE FAILURE RATE IS ACCEPTABLY LOW. NO CORRECTIVE ACTION IS REQUIRED TASK CLOSED |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A14060 | IFA# -- | Contractor RPT# E-146 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD7400244-029 | Asmnt Part Name TEMPERATURE TRNSDCR | Asmnt Serial/Lot# 1634 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD ESW - EI-SHIP-WORK | FAIL MODE EL - SHORT |
| Asmnt FMEA 3.9.10.3 | Asmnt FM 3 | FMEA CSE B | FMEA SCSE 2 |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |