POLAR Spacecraft Status As of: Weds May 11  12:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM: 1648=AN STIP data only | NOAA-14J AM: 2019=AN STIP data only | NOAA-15K AM: 1817=AN GAC data only | NOAA-16L PM: 1430=AN GAC&LAC data | NOAA-17M AM: 2224=AN GAC&LAC data | NOAA-N18 Planned PM Plan AN=14:00 |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | 12May05 10:30Z Slip due to winds |
| CNTL OBP | OBP2 | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | Dress Rehearse #1 Completed 13Jan |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 XSU1 TOAR 444 | B-BUS XSU-1 | Dress Rehearse #2 Completed 14Apr05 |
| BUS VETO | NO | NO | NO | NO | NO | Dress rehearse #3 Completed 9 May 05 |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ SS check Disabled when mode=YGC | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAA | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB | New ring laser gyro |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS +100 mS 31Au04 | PRI Daily Bias –5.5 mS -100 mS 31Au04 | PRI Daily Bias –3 mS |  |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 |  |
| MIRP | External Synch Rephase Enabled | External Synch Rephase 0730 Daily | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled |  |
| TIP SIDE | 1 | 1 | 2 (since 4/23/03) 3 Channels inop | 2 since 4/18/05 | 1 Analog telem drifting |  |
| DTRs | 3A, 4, 5B Safestate 5B | 1, 2B, 5 Safestate- 1B | 1, 2, 3, 4 Safestate 1B EOT | 1,2,3,4A Safestate 3A 4B STIP only | 1,2,3,4 Safestate=1B DTR2-SSR | All solid state digital recorders |
| VTX (APT data) | #1 ON 137.50 MHZ Conflict with N15 | OFF Since 8/14/02 | OFF (15Apr-16May) Conflict with N12 | INOP OFF since 11/15/00 | #2 ON 137.62 MHZ | #1=137.1 MHZ #2=137.9125 MHZ |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #1 137.35 MHZ | #2 137.77 MHZ |  |
| STX #1=1698.0 mhz #2=1702.5 mhz #3=1707.0 mhz #4=2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT 4-Playback 1,2,3-Degraded | 1 – HRPT; 2– Playback; 4 – Playback 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 output power drop TOAR 443. | STX-3 Replaced at VAFB |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) | ArrayOff +50 since 8/31/04 Eclipse season 21Apr-17Aug Batt UVtrip 7/25/04 Sun Angle 27 up to 37 mid-June Batts 1&2=LRC V/T=4 Shunt degraded SA CANT=37 degs | Array Off -55 Since 8/21/03 Eclipse all year Sun angle 44 up trend to 52 in June Batts 1-3= LRC Batts 1&3V/T=7/11 Batt2 VT=8/11 SS trigger =18.98 Shunt Degraded SA CANT=22 degs | Array Off -45 Since 1/25/01 Full Sun Eclipse Season starts 21 May Sun Angle 22, up- trend to 32 in June Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 54 Steady trend Batts 1-3= LRC V/T=4/8 SA CANT=22 degs SADPOS timer increased 5 Apr | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 69 Uptrend to 72 at the end of May Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs SADPOS timer increased 5 Apr |  |
| AVHRR | Nominal | INOP Scan motor stalled 14 Apr 04 | Nominal Rare major scan motor surges. Last Incident 11/18/04 | Operational TCE24 OFF 4/14/04 Occasional Image Wave patterns Chan 3B only. | Nominal 3A-B switch enabled | New brushless scan motors |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative Record low component temps reversed trend | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop Channel 9-14 noise improved since 1/19 | OFF/INOP Since 10/30/03 Survival heat on. |  |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal |  |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 IPD Reports of degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | ON / INOP Turned on 8/30/04 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | INOP Downgraded to RED status 19 Apr 05 TOAR 445 submitted FW mode=Hi Powr FW Heater OFF Frequent Filter Excessively high FM temps and currents continue | DEGRADED Longwave channel imagery improved radiometric noise level is still high TOAR 441 submitted 11 Jan05 Considering high power mode Occasional major FM surges, most recent 12/9/04 | NOMINAL 1 Pixel cross track misalignment . | HIRS-4 replacing HIRS-3 |
| MHS/MIU |  |  |  |  |  | Replaces AMSUB |
| MSU | ON / INOP On For power balance Scan Motor OFF since 3/12/03 | Operational Scan motor and antenna problems |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal |  |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Switched back to mode AA 26Apr05 14:10Z A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode |  |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal |  |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Telescopes inoperative | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 |  |
| SBUV |  | Degraded Grate motor sticks Flex memory 3 (giant step) ops suspended 12/2/03 Reduced operations |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops Procedure change starting 17 May |  |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Timer changed to 12 (from 8 mins 5 Apr | ON ENABLED Timer changed to 12 (from 8 mins 5 Apr |  |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 HIRS FW Heat tuned ON 17 Apr and OFF on 18 Apr TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 | Nominal TCE24 OFF 4/14 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 |  |
|  | N12 | N14 | N15 | N16 | N17 | NOAA-N18 |

COMMENTS/CHANGES:

NOAA-12	There were no changes on N12 during the past reporting period.

NOAA-14:	Spacecraft is operating nominally and power subsystem remains stable and above safe state threshold values as the

long slow increase in percentage darkness time per orbit continues through mid-June 05.  Otherwise there were no changes to N14 during the past reporting period.

NOAA-15:	The N15 HIRS filter wheel remained at severely elevated (albeit not record high) temperatures and currents last week although it did remain generally stable.  Imagery remains completely degraded, period monitor values excessive and filter wheel synch always out of synch.  No further discussion has ensued regarding the possibility of toggling the filter motor in the hope of breaking the filter wheel through whatever is obstructing it.  N15 HIRS remains red in status (inoperative) in high power mode with heaters OFF.  (See illustration 1).

NOAA remains concerned about the possible influence that the HIRS situation will have on the spacecraft subsystem, notably AMSU’s, and the AVHRR (power was originally a concern as well but has proven to be a non-issue).  The N15 AVHRR scan motor current has shown some indications of less stable scan motor current and has thermally been approaching record highs (and may even have actually exceeded record highs if one takes into consideration the drop in values that followed the N15 TIP swap).  In addition, synch delta has continued to slowly increase and is running at its highest level this year (although it remains well below MIRP rephase thresholds) while imagery still appears to be nominal (illustrations 2-4).  The N15 AMSU-B also appears to be performing in a slightly less stable manner but its scan motor currents and temps remains within nominal values (illustration 5).  The two other AMSU’s (A1 and 2) have been stable and nominal throughout the past reporting period (illustration 6).

The N15 eclipse season is expected to start within the next 2 weeks, EMOSS engineer Carl Gliniak has generated a

floor procedure in preparation for this event.  No reconfigurations are expected although additional assessments will be

performed as the spacecraft progresses through this eclipse season.

N15 VTX-1 (APT data) remains turned off due through 16 May to an RF conflict with N12.

NOAA-16:	The N16 AVHRR scan motor current and especially synch delta continued to degrade over the past week.  Several

confirmed and several other probable (but unconfirmed) MIRP rephases have occurred in recent days as the synch delta has degraded.  Conversely, even with relatively high scan motor currents, the N16 AVHRR imagery appears to be relatively nominal with the only degradation being the single frames of lost data that occurs when the MIRP rephases.  Even wave patterns, which almost always occurred at the scan motor currents at recent levels, are not apparent in the imagery reviewed by EMOSS engineers.  Also on the favorable side are the AVHRR scan motor temps which have been nominal and stable throughout 2005 even though the AVHRR TCE has been powered off during that entire period.   (See illustrations 7-10.)

The N16 HIRS was nominal and stable last week (illustration 11) as were the N16 AMSU’s and ADACS subsystem.

NOAA-17:	The N17 AVHRR scan motor current and temps were both very stable during the past week while synch delta and

AVHRR component temps were very stable and imagery remained nominal (illustrations 12 and 13).   The two remaining AMSU’s (A2 and B) were also nominal during the same time period (illustration 14).  The N17 HIRS was also generally stable during the past week although its period monitor appeared to be slightly less stable than the week before.  However, in analyzing this period monitor value over the course of the mission, this slight reduction of stability appears to be well within nominal operating ranges (illustrations 15 and 16).  NOTE:  THE ILLUSTRATIONS FOR N17 DATA INCLUDE MERGED FILES OF ABE AND GRETA DATA.  AS THE ILLUSTRATIONS SHOW, THEY APPEAR TO MATCH UP PERFECTLY.

At the request of the Polar Program Office EMOSS engineer Jim Walters is overseeing a change in the N17 SBUV standard operating procedure.  The NOAA-17 SBUV currently spends 14 orbits in sweep mode every Tuesday.  This will be reduced to 4 orbits in sweep mode.  These orbits should not cross over the CONUS, or at least not do so in daylight.  The SOMS procedure SBSWMODE will be run every Tuesday and the wait time in this procedure must be changed to 24240 seconds.  These schedule changes are intended to be permanent and will be implemented beginning 17 May 05.

NOAA-N:	EMOSS Supported the final (#3) dress rehearsal is scheduled on 9 May and is a go for launch.  The launch slipped 24

hours from to 12 May (same time, approx 10:30Z) because of high winds with at the launch site (Vandenberg).  The EMOSS on-console support schedule for launch and OV are included at the back of this report.

MISC:	 Integrating ABE into the Greta process continues to make progress and meet with difficulty at the same time.  The

primary problem is one of “results success/failure variability” when running “fixed” scripts and inputs.  Jeff Devine is EMOSS POC for this effort.

Illustration 1:  N15 HIRS Health Analysis:

(Inoperative and no improvement)

Illustration 2:  N15 AVHRR Analysis

(Looking for cause effects from HIRS anomaly, none readily apparent, but the small increase on JDAY 125 is something to keep an eye on.)

Illustration 3:  N15 AVHRR Analysis in perspective

(Scan motor current rise not especially significant from a historical perspective but the temps are approaching all time highs and, if the drop caused by the TIP swap in Apr 2003 is taken in to account, may even be at all time highs.)

Illustration 4:  N15 AVHRR Imagery and Synch Delta Analysis

(Looking for cause effects from HIRS anomaly, none readily apparent but there is a non-auspicious trend that seems to be developing on the synch delta value that may require further attention in the weeks ahead.)

Illustration 5:  N15 AMSU-B Analysis

(Looking for cause effects from HIRS anomaly, none readily apparent although the AMSU-B scan motor current continues showing some minor instabilities that are well within normal operating profiles.)

Illustration 6:  N15 AMSU-A1and 2 Analysis

(Looking for cause effects from HIRS anomaly, none readily apparent, in fact, power usage, as measured by bus current appears slightly lower since the HIRS started drawing additional current.)

Illustration 7:  N16 AVHRR Health

(The scan motor current has been better and its not trending in a favorable direction.)

Illustration 8:  N16 AVHRR Imagery Analysis

(Imagery looks OK today, notwithstanding the elevated scan motor current, wave patterns have not been readily apparent from an EMOSS perspective of imagery analysis.

Illustration 9:  N16 Synch Delta Analysis

(Definitely not a favorable trend)

Illustration 10:  N16 Imagery Analysis relative to synch delta

(Also, definitely not a favorable trend.  Not all rephases are “detectable” relative to the EMOSS process.  Use of GAC imagery that includes South Polar Region provides the best evidence of rephases occurring.)

Illustration 11:  N16 HIRS Analysis

(Stable.)

Illustration 12:  N17 AVHRR Analysis

(Stable and nominal note the inclusion of ABE data into this primarily Greta data graph.)

Illustration 14:  N17 Synch Delta Analysis

(Generally stable and nominal)

Illustration 13:  N17 Synch Delta Analysis

(Generally stable and nominal)

Illustration 14:  N17 AMSU-A2 and B Health Analysis

(Stable and nominal.  Note the use of ABE data within this primarily Greta data graph.)

# Illustration 15:  N17 HIRS Health Analysis

(Nominal and generally stable except for the Period Monitor value which appears a little less stable than last week.)

# Illustration 16:  N17 HIRS Period Monitor in perspective

(Well within historical norms.)

# N17 MEMORY SCRUB REPORT

# Last week

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING May 6, 2005

| DAY/DATE | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 |
| --- | --- | --- | --- | --- | --- |
| FRI. 04/29 | N/A | +177 msec | -153 msec | +083 msec | +034 msec |
| SAT. 04/03 | +715 msec | +180 msec | -154 msec | +084 msec | +034 msec |
| SUN. 05/01 | +716 msec | +179 msec | -156 msec | +084 msec | +033 msec |
| MON. 05/02 | +719 msec | +174 msec | -157 msec | +084 msec | +035 msec |
| TUE. 05/03 | N/A | +175 msec | -157 msec | +084 msec | +036 msec |
| WED. 05/04 | +717 msec | +177 msec | -160 msec | +084 msec | +036 msec |
| THU. 05/05 | N/A | +177 msec | -159 msec | +088 msec | +037 msec |

EMOSS POC for this chart is JIM SHEPHERD

NOAA-12  	*Alternating +/- 500 millisecond clock jumps will occur at 76-day intervals as long as fractional second daily ETCUP is utilized to manage clock drift..

Daily ETCUP bias of +6.5 mSec started on 12/10/03.

NOAA-14:  	As of 1223/03 the TIP clock is corrected daily by –7.0 msec to compensate for drift.

Subtracted 150 mSecs on 30 June

NOAA-15:  	As of 04/23/03 the TIP clock is corrected daily by –8 msec to compensate for drift.

Added 100 msec to spacecraft command clock on 31 Aug 04

NOAA-16:  	As of 12/23/03 the TIP clock is corrected daily by –5.5 msec to compensate for drift.

Subtracted 100 msec from spacecraft command clock on 31 Aug 04.

NOAA-17:  	As of 12/23/03 the TIP clock is corrected daily by –3 msec to compensate for drift.

Added 125 Msecs3 Feb 04.

EMOSS ON Console Schedule for N18 Launch and OV

POES Engineering Contact List

Government

Renee Smith-Dearing  NOAA POES Constellation Lead 		301-817-4117

Dong Han:  NOAA, POES Payloads				301-817-4127

Micky Fitzmaurice:  NOAA, POES Bus, IJPS	 	    	301-817-4016

Nicolaie Todirita (Todi): NOAA Ground Systems			301-817-4229

EMOSS-2 Contractor

Jeff Devine: EMOSS POES Lead	 				301-817-4020

Jim Walters:  EMOSS, POES Payload Engineer			301-817-4033

Angelique Riley, EMOSS, POES Comm and DHS			301-817-4028

Carl Gliniak, EMOSS POES Power and Thermal 			301-817-4207

Jim Sheperd, EMOSS POES Attitude Control			301-817-4030

Jon Woodward EMOSS, POES Flight Software C&CS		301-817-4019

Sally House EMOSS POES Payloads 				301-817-4026

William Chadwick EMOSS, POES Comm and DHS			301-817-4015