POLAR Spacecraft Status As of: Tues 29 Mar 05  16:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM: 1648=AN STIP data only | NOAA-14J AM: 2019=AN STIP data only | NOAA-15K AM: 1817=AN GAC data only | NOAA-16L PM: 1430=AN GAC&LAC data | NOAA-17M AM: 2224=AN GAC&LAC data | NOAA-N18 Planned PM Plan AN=14:00 |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | Launch date 11May05 |
| CNTL OBP | OBP2 | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | Dress Rehearse #1 Completed 13Jan |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 | B-BUS XSU-1 | Dress Rehearse #2 14Apr05 |
| BUS VETO | NO | NO | NO | NO | NO |  |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ SS check Disabled when mode=YGC | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAA | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB | New ring laser gyro |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS +100 mS 31Au04 | PRI Daily Bias –5.5 mS -100 mS 31Au04 | PRI Daily Bias –3 mS |  |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 |  |
| MIRP | External Synch Rephase Enabled | External Synch Rephase 0730 Daily | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled |  |
| TIP SIDE | 1 | 1 | 2 (since 4/23/03) 3 Channels inop | 1 Analog telem drifting Plan swap 19Apr | 1 Analog telem drifting |  |
| DTRs | 3A, 4, 5B Safestate 5B As of 8 Dec 04 | 1, 2B, 5 Safestate- 1B 3B inop 2/1/05 | 1, 2, 3, 4 Safestate 1B EOT | 1,2,3,4A Safestate 3A 4B STIP only | 1,2,3,4 Safestate=1B DTR2-SSR | All solid state digital recorders |
| VTX (APT data) | #1 ON 137.50 MHZ | OFF Since 8/14/02 | #1 ON 137.50 MHZ | INOP OFF since 11/15/00 | #2 ON 137.62 MHZ | #1=137.1 MHZ #2=137.9125 MHZ |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #1 137.35 MHZ | #2 137.77 MHZ |  |
| STX #1=1698.0 mhz #2=1702.5 mhz #3=1707.0 mhz #4=2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT 4-Playback 1,2,3-Degraded | 1 – HRPT; 2– Playback; 4 – Playback 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 Swapped with STX-4 22 Mar 05 STX-1 output power drop TOAR 443. | STX-3 frequency drift problem caused launch slip. Replaced at VAFB undergoing testing |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) Sun-Moon Eclipse predicted For 8 Apr 05. 18:00-23:00Z Minor effects on all spacecraft. No reconfigurations recommended | ArrayOff +50 since 8/31/04 Full Sun Battery UVtrip 7/25/04 Sun Angle 23 Uptrend to 37 in mid-June Batts 1&2=LRC V/T=4 Shunt degraded SA CANT=37 degs | Array Off -55 Since 8/21/03 Eclipse all year Sun angle 38 up trend to 52 in June Batts 1-3= LRC Batts 1&3V/T=7/11 Batt2 VT=8/11 SS trigger =18.98 Shunt Degraded SA CANT=22 degs | Array Off -45 Since 1/25/01 Full Sun Sun Angle 12, up- trend to 32 in June Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 54 Steady trend Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 68 Uptrend to 72 at the end of May Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs |  |
| AVHRR | Nominal | INOP Scan motor stalled 14 Apr 04 | Nominal Rare major scan motor surges. Last Incident 11/18/04 | Operational TCE24 OFF 4/14/04 Occasional Image Wave patterns Chan 3B only. | Nominal 3A-B switch enabled | New brushless scan motors |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative Record low component temps reversed trend | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop Channel 9-14 noise improved since 1/19 | OFF/INOP Since 10/30/03 Survival heat on. |  |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal |  |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 IPD Reports of degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | ON / INOP Turned on 8/30/04 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | Operational FW mode=Hi Powr FW Heater OFF Frequent Filter Motor current “mini” surges Occasional major FM current surges, most recent 12/9/04 | DEGRADED Longwave channel imagery improved radiometric noise level is still high TOAR 441 submitted 11 Jan05 Occasional major FM surges, most recent 12/9/04 HIRS filter heater turned OFF 1/18/05 | NOMINAL 1 Pixel cross track misalignment . | HIRS-4 replacing HIRS-3 |
| MHS/MIU |  |  |  |  |  | Replaces AMSUB |
| MSU | ON / INOP Turned on 8/30/04 For power balance Scan Motor OFF since 3/12/03 | Operational Scan motor and antenna problems |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal |  |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode |  |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal |  |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Telescopes inoperative | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 |  |
| SBUV |  | Degraded Grating motor sticks Flex memory 3 (giant step) ops suspended indefinitely on 12/2/03 Reduced operations |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode |  |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Autonomous implementation 10/14 | ON ENABLED |  |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 HIRS FW Heat OFF TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 S/C record low thermal cycle ended 27 Feb | Nominal TCE24 OFF 4/14 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 |  |
|  | N12 | N14 | N15 | N16 | N17 | NOAA-N18 |

COMMENTS/CHANGES:

NOAA-12	There were no changes on N12 during the past reporting period.

NOAA-14:	Spacecraft is operating nominally and power subsystem remains stable and well above safe state threshold values as the long slow increase in percentage darkness time per orbit continues (illustration 1) through mid-June 05.

NOAA-15:	The N15 AVHRR showed a slight rise in scan motor current during the past week as component temperatures also continued there uptrend (illustration 2).  The synch delta was also slightly higher but like the scan motor current is not, at the moment, something that is cause for immediate concern.  The AVHRR imagery on N15 continues to be nominal.

The N15 HIRS continued its series of mini-surges and return to nominal during the past week with no reports of imagery degradation being received by EMOSS and no loss of filter wheel synch (illustration 3).

The AMSU’s on N15 were all nominal during the post week as their thermal trends continued upward as did the solar array current which is now well above the NSCPONE darkness threshold (illustration 4).

NOAA-16	The N16 AVHRR scan motor current was stable to very slightly higher last week with stable temperatures and synch

delta values generally stable but rising slowly.  In addition, although the scan motor current is maintaining somewhat higher than it has since early Dec 2004, imagery has not degraded and even wave patterns are less evident now as they were several weeks ago when the scan motor current was lower  (illustrations 5&6).  As has been the case since Nov 2004, there has still been no MIRP rephases since Nov 2004 and no bar coded imagery since last summer.  TCE 24 remains powered off.

The N16 HIRS filter motor was generally stable to very slightly higher last week remaining close to but below its all

time high values (illustration 7).  EMOSS continues to detect HIRS imagery degradation and also receive reports of same, while the HIRS filter wheel synch and period monitor values remain relatively nominal and stable.

EMOSS engineers continue preparing for a TIP swap on N16 currently planned for 19 April 05.  Jon Woodward and Will Chadwick are EMOSS POC’s for this operation.

The N16 ADACS was nominal during the past week as depicted in illustration 8.

NOAA-17:	The N17 AVHRR scan motor current was very stable to slightly higher during the past week while synch delta and

AVHRR component temps were very stable and imagery remained nominal (illustration 9).    EMOSS is continuing to monitor this payload very closely.

The STX-1 transmitter is no longer in use with STX-4 now taking all of STX-1 playback requirements.  STX-4 is performing nominally since taking over this responsibility (illustration 10).  STX-1 remains very capable of for future implementation if the need should arise and will remain in reserve for such a time.  Will Chadwick is EMOSS POC for this subsystem.

The N17 ADACS was nominal during the past week as depicted in illustration 11.

NOAA-N:	No changes since previous report.  EMOSS engineers are now preparing for the second dress rehearsal scheduled for

14 Apr.  The new launch support calendar has once again been made available to the general public.  The new web link to review this calendar is  http://sgt-mets.com/~ddipaula/poes-cal.doc

MISC:	A sun-moon eclipse has been predicted by the EMOSS eclipse model.  This eclipse will affect all POES spacecraft over

the course of 3 orbits from approximately 17:59 through 23:04Z on 8 Apr 05.  After careful analysis (see graphs at the back of this report) EMOSS is recommending that no reconfigurations be implemented during this event.  Additional analysis will continue to be performed prior to this event to ensure the latest information has been considered.   Kim Kolb, Jim Sheperd, Carl Gliniak, Jon Woodward and Jeff Devine are all involved in this analysis.

For the first time ever, ABE data is being graphically depicted in this Weekly  report (Illustration 1; N14 power).  This data was extracted from the ABE software and merged into the Greta process which has historically been the source of most graphics in this report.  Previously, all such graphics created by the Greta process were first extracted from Greta software.  This coupling of capabilities offers a new proof of concept and carries the potential to provide future benefit to the POES program by expanding the capability, flexibility and redundancy of both ABE software and the Greta process with no capitol expenditures required.  Jeff Devine is EMOSS POC for evolving this process.

Illustration 1:  N14 Power Analysis

(Nominal as the percentage of time that the spacecraft spends in darkness slowly increases (to 30% in mid-June)

NOTE:  DATA THAT FALLS WITHIN THE YELLOW BOX (JDAY 87) WAS EXTRACTED FROM ABE vs. GRETA SOFTWARE.  THIS IS THE FIRST EVER SUCESSFUL EXTRACTION OF ABE TELEMETRY DATA OUTPUT INCORPORATED INTO THE GRETA PROCESS.

Illustration 2:  N15 AVHRR Health Analysis

(Nominal but showing a possible inauspicious trend on scan motor current.)

Illustration 3:  N15 HIRS Health Analysis

(Typical operational behavior)

Illustration 4:  N15 Power Analysis

(Nominal)

Illustration 5:  N16 AVHRR Health Analysis

(Generally stable with scan motor current spending most of its time in an area where imagery affects may vary.)

Illustration 6:  N16 AVHRR Imagery Analysis (HRPT)

Most recent image nominal, all GACS during the past week were also nominal.

TREND DATA					      HISTORY DATA

Illustration 7:  N16 HIRS Health Comparison Analysis (long term vs. recent).

(Just a little less stable than preferred with a somewhat less than desirable trend.)

Illustration 8:  N16 ADACS Analysis

(Nominal)

Illustration 9:  N17 AVHRR Health Analysis

(Much the same as previous two weeks although showing a slight increase in scan motor current.)

Illustration 10:  N17 STX 1 vs. 4 Analysis

Illustration 11:  N17 ADACS Analysis

(stable and nominal)

# N17 MEMORY SCRUB REPORT

# Last week and Cumulative

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING March 25, 2005

| DAY/DATE | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 |
| --- | --- | --- | --- | --- | --- |
| FRI. 03/18 | -182 msec | +146 msec | -116 msec | +061 msec | +018 msec |
| SAT. 03/19 | -181 msec | +155 msec | -117 msec | +060 msec | +016 msec |
| SUN. 03/20 | -184 msec | +155 msec | -117 msec | +061 msec | +019 msec |
| MON. 03/21 | -184 msec | +155 msec | -119 msec | +060 msec | +019 msec |
| TUE. 03/22 | -184 msec | +150 msec | -120 msec | +061 msec | +018 msec |
| WED. 03/23 | -183 msec | +153 msec | -122 msec | +065 msec | +021 msec |
| THU. 03/24 | -185 msec | +152 msec | -124 msec | +065 msec | +020 msec |

EMOSS POC for this chart is JIM SHEPHERD

NOAA-12  	*Alternating +/- 500 millisecond clock jumps will occur at 76-day intervals as long as fractional second daily ETCUP is utilized to manage clock drift. Next +500 mS jump is expected on 1/30/05.

Daily ETCUP bias of +6.5 mSec started on 12/10/03.

NOAA-14:  	As of 1223/03 the TIP clock is corrected daily by –7.0 msec to compensate for drift.

Subtracted 150 mSecs on 30 June

NOAA-15:  	As of 04/23/03 the TIP clock is corrected daily by –8 msec to compensate for drift.

Added 100 msec to spacecraft command clock on 31 Aug 04

NOAA-16:  	As of 12/23/03 the TIP clock is corrected daily by –5.5 msec to compensate for drift.

Subtracted 100 msec from spacecraft command clock on 31 Aug 04.

NOAA-17:  	As of 12/23/03 the TIP clock is corrected daily by –3 msec to compensate for drift.

Added 125 Msecs3 Feb 04.

POES Engineering Contact List

Government

Renee Smith-Dearing  NOAA POES Constellation Lead 		301-817-4117

Dong Han:  NOAA, POES Payloads					301-817-4127

Micky Fitzmaurice:  NOAA, POES Bus, IJPS			 301-817-4016

Nicolaie Todirita (Todi): NOAA Ground Systems			301-817-4229

EMOSS-2 Contractor

Jeff Devine: EMOSS POES Lead	 				301-817-4020

Jim Walters:  EMOSS, POES Payload Engineer			301-817-4033

Angelique Riley, EMOSS, POES Comm and DHS (outgoing)	301-817-4028

Carl Gliniak, EMOSS POES Power and Thermal 			301-817-4207

Jim Sheperd, EMOSS POES Attitude Control			301-817-4030

Jon Woodward EMOSS, POES Flight Software C&CS		301-817-4019

Sally House EMOSS POES Payloads (in training)			301-817-4026

William Chadwick EMOSS, POES Comm and DHS (in training)	301-817-4015

POES Eclipse Analysis for 8 April 2005 depicts the east to west movement of the solar eclipse across the earth surface.  The poles are not effected by this years biannual solar event leaving all but N15 YAW updates values completely clear,  reducing the number of times POES spacecraft experience this event, and allowing all spacecraft to orbit through the solar event without losing 100% sun (maximum loss 70% by N15).

N12 Sun-Moon Eclipse Analysis for 8 Apr 05 (grey box indicates the values at which the BYRILLUM telemetry mnemonic indicates darkness.)

Effects and reconfiguration recommendations for N12 (none)

-Power balance:  Eclipse effect negligible, no reconfigurations recommended

-SADPOS Takeover:  Not applicable on N12, no reconfigurations possible

-Autonomous YGC Mode:  No yaw updates during any reduced sun period.

No reconfigurations recommended

N14 Sun-Moon Eclipse Analysis for 8 Apr 05 (grey box indicates the values at which the BYRILLUM telemetry mnemonic indicates darkness. Yellow box indicates the percent illumination values that would have to be reached during GEODAT predicted sunlight that could cause an autonomous switch to YGC mode during a Yaw Update)

Effects and reconfiguration recommendations for N14 (none)

-Power balance:  Eclipse effect negligible, no reconfigurations recommended

-SADPOS Takeover:  Not applicable on N14, no reconfigurations possible

-Autonomous YGC Mode:  A yaw updates does occur at the very end of the only sun

blockage period that N14 will experience.  However, the illumination value never approaches that which could threaten an autonomous switch to YGC mode.

No reconfigurations recommended

N15 Sun-Moon Eclipse Analysis for 8 Apr 05 (grey box indicates the values at which the BYRILLUM telemetry mnemonic indicates darkness.

Effects and reconfiguration recommendations for N15 (none)

-Power balance:  Eclipse effect negligible on this full sun spacecraft despite the

(comparatively) “prolonged” period in BRYILLUM darkness. No reconfigurations recommended

-SADPOS Takeover:  Not applicable on N15, no reconfigurations possible although the

7.5 minute “dark” period would be close to the 8 minute threshold for SADPOS takeover on N16 or N17. No reconfigurations possible

-Autonomous YGC Mode:  (see next page)

N15 Yaw Update Analysis (cont, Zoom IN from previous page)

Grey box indicates the values at which the BYRILLUM telemetry mnemonic indicates darkness. Yellow box indicates the percent illumination values that would have to be reached during GEODAT predicted sunlight that could cause an autonomous switch to YGC mode during a Yaw Update)

-Autonomous YGC Mode:  (from previous page) A yaw updates does occur during this

eclipse event but the predicted degree of sunlight lost (45%, equating to 55% illuminated) does not approach the value that would threaten an autonomous switch to YGC mode (80% equating to 20% illuminated).  Therefore, no reconfigurations are recommended.

N16 Sun-Moon Eclipse Analysis for 8 Apr 05 (grey box indicates the values at which the BYRILLUM telemetry mnemonic indicates darkness.

Effects and reconfiguration recommendations for N16 (none)

-Power balance:  Eclipse effect negligible; expect full charge before going back into

Earth-sun eclipse, no reconfigurations recommended

-SADPOS Takeover:  SADPOS is applicable on N16.  However, the darkness threshold

is never breached during this event, let alone breached for the 8 minutes that would result in SADPOS takeover.  Therefore, no reconfigurations are recommended.

-Autonomous YGC Mode:  No yaw updates will occur while the sun-

moon eclipse is occurring.  No reconfigurations

recommended.

N17 Sun-Moon Eclipse Analysis for 8 Apr 05 (grey box indicates the values at which the BYRILLUM telemetry mnemonic indicates darkness.

Effects and reconfiguration recommendations for N17 (none)

-Power balance:  Eclipse effect negligible; expect full charge before going back into

Earth-sun eclipse, no reconfigurations recommended.

-SADPOS Takeover:  SADPOS is applicable on N17 and while the darkness threshold

is breached during this event, it is for significantly less time (5 minutes, rounded high) than the 8 minutes required for SADPOS takeover. (This analysis uses the Flight Software specs value for the BRYILLUM flag to start the 8 minute timer vs. the less conservative P&CH.  Therefore, no reconfigurations are recommended.

-Autonomous YGC Mode:  No yaw updates will occur while the sun-

moon eclipse is occurring.  No reconfigurations

recommended.