MSFC PRACA : 2003-02-12 08:41

MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A15773 | In-Flight Anomaly Number -- | Contractor Report Number E-156 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title LIQUID LEVEL SENSOR FAILED ATP |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT -- | Sys_Lvl N | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE LOX LEVEL SENSOR | PART# 74L4-1 | SER/LOT# 1649 | MANUFACTURER SIMMONDS |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EN - OPEN | Cause U - UNKNOWN |
| System ELECTRICAL | Defect DC - BROKEN | Material C - EEE | Work Contact JOHN ADAMS | Fail Date 01/10/1994 |
| Received at MSFC 01/12/1994 | Date Isolated 01/10/1994 | FMEA Reference 3.6.1.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location SIMMONDS | Symptom EN - OPEN | Time Cycle -- |
| Effectivity Text -- |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date 01/21/1994 | Contractor Req Defer Until Date 01/31/1994 | LVL 3 Close -- | Remark / Action 01/31/1994 |
| Investigation / Resolution Summary |
| Last MSFC Update 04/12/1994 | CN RSLV SBMT 01/31/1994 | Defer Date 01/20/1994 | Add Date 01/12/1994 | R/C Codes 0 - EXPL -- -- |
| Assignee |
| Design R. MOYE | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR P. COUNTS |
| Approval |
| Design R. MOYE | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR P. COUNTS |
| PAC Assignee B. HURST | PAC Review Complete BH | MSFC Closure Date 02/10/1994 | Status C - CLOSED | F/A Completion 01/10/1994 |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID T-121356 |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description A LOX LEVEL SENSOR FAILED THE SUPPLIER ACCEPTANCE TEST. THE SENSING ELEMENT DEVELOPED AN OPEN CIRCUIT UPON IMMERSION IN CRYOGENIC FLUID DURING THE FIRST THERMAL SHOCK TEST CRITICALITY: THE 74L4-1 LOX LEVEL SENSOR IS CRIT. 3 IN ALL POSITIONS ON THE ET FOR THE SENSING ELEMENT OPEN CIRCUIT. HOWEVER, THE 74L4-1 SENSOR IS VIRTUALLY IDENTICAL TO THE 74L4-2 LH2 LEVEL SENSOR. THE 74L4-2 LEVEL SENSOR IS CRIT. 1R; FMEA ITEM CODE 3.6.1.1; " FAILS WITH FALSE WET SIGNAL." NOTE: THE SENSOR IS LIMITED LIFE CONTROLLED * REVISION "A" CLOSES ALL TASKS. SEE ASTERISKS FOR CHANGES |
| Contractor Investigation/Resolution GENERAL: THE 74L4-1 LOX LEVEL SENSOR WAS UNDERGOING THE ACCEPTANCE TEST AT THE SUPPLIER, B.F. GOODRICH AEROSPACE, SIMMONDS PRECISION DIVISION, VERGENNES, VERMONT. THE TESTING IS CONTROLLED BY ACCEPTANCE TEST PLAN 946, REVISION S. THE TRANSDUCER DEVELOPED AN OPEN CIRCUIT WHEN IMMERSED IN LN2 FOR THE FIRST OF THE SEVEN THERMAL SHOCK CYCLES PER PARAGRAPH 6.4.10 OF THE ATP. THE SENSOR WAS REMOVED FROM THE LN2 AND EXAMINED; THE BROKEN SENSING ELEMENT COULD BE SEEN WITHIN THE SENSOR HOUSING. THE FAILURE WAS DOCUMENTED ON MARS T121356 THE LEVEL SENSOR UTILIZES THE DECREASE IN THE ELECTRICAL RESISTANCE OF A METAL WHEN COOLED TO DETECT THE PRESENCE OF A CRYOGENIC FLUID THE SENSOR USES A GOLD FLASHED PLATINUM WIRE, .0005 INCH IN DIAMETER, AS THE SENSING ELEMENT. THE LEVEL SENSOR SIGNAL CONDITIONER, WHICH IS MOUNTED IN THE ORBITER, PROVIDES A CONSTANT CURRENT TO THE SENSING ELEMENT WHICH CAUSES IT TO RISE IN TEMPERATURE. THE TEMPERATURE AND RESISTANCE OF THE ELEMENT DECREASE RADICALLY WHEN IMMERSED IN A CRYOGENIC LIQUID. THE SIGNAL CONDITIONER DETECTS THE DECREASE IN RESISTANCE AND CONVERTS IT TO A "WET" OUTPUT SIGNAL. THE SIGNAL CONDITIONER IS ALSO DESIGNED TO GIVE A "WET" SIGNAL IN THE EVENT OF AN OPEN CIRCUIT IN THE LEVEL SENSOR THE SENSOR HAS AN ALUMINUM CASE WHICH IS PRODUCED BY INVESTMENT CASTING. VERY FEW OF THE INTERNAL SURFACES, AND NONE OF THE EXTERNAL SURFACES, ARE FINISH MACHINED FOR DIMENSIONAL CONTROL. THE INTERNAL SURFACES OF THE CASE AND THE COVER ARE PAINTED WITH A SPRAYED-ON, BAKED, TEFLON PAINT. THE PAINT PREVENTS WETTING OF THE CASE, I.E RETENTION OF CRYOGENICS, AND ALSO PROVIDES SOME ELECTRICAL INSULATION BETWEEN THE CASE AND THE SENSOR ELEMENT. THE ELEMENT IS SUPPORTED BY A CERAMIC SUBSTRATE. THE SUBSTRATE HAS FIRED-ON GOLD CIRCUIT PATHS WHICH PROVIDE A MEANS TO TERMINATE THE ELEMENT WIRE BY WELDING. THE SENSOR OUTPUT WIRES ARE ATTACHED TO THE SUBSTRATE BY STEEL TERMINALS HELD IN PLACE WITH RIVETS AND SPRING WASHERS TASK I. FAILURE INVESTIGATION THE FAILED SENSOR WAS DOCUMENTED ON MARS T121356. THE MARS WAS DISPOSITIONED FOR FAILURE ANALYSIS, TO BE PERFORMED AT MAF RESPONSIBILITY: R. RAMSEY/3830 -- M. COMBS/3830 J. ADAMS/3741--D, WESTPHAL/3840 * COMPLETED: JANUARY 21, 1994 * CLOSURE STATEMENT THE SENSOR WAS RECEIVED FROM SIMMONDS PRECISION IN GOOD CONDITION VISUAL EXAMINATION OF THE SENSOR CONFIRMED THAT ONE END OF THE FRACTURED ELEMENT WIRE COULD BE SEEN WITHIN THE SENSOR. WHEN THE CASE WAS OPENED IT WAS DETERMINED THAT THE FRACTURE HAD OCCURRED NEAR THE CENTER OF THE ELEMENT. THE TWO ENDS OF THE WIRE AT THE FRACTURE WERE REMOVED FROM THE ELEMENT ASSEMBLY AND MOUNTED ON A SAMPLE CARRIER FOR EXAMINATION IN A SCANNING ELECTRON MICROSCOPE (SEM). THE FRACTURE FACES OF THE WIRE WERE INDICATIVE OF A TENSILE OVERLOAD IN A DUCTILE MATERIAL. THE EXTREME DELICACY OF THE SENSING ELEMENT MAKES IT SUSCEPTIBLE TO IMPACT DAMAGE FROM FOREIGN MATERIALS IN THE LIQUID NITROGEN USED DURING ACCEPTANCE TESTING AND TO INSUFFICIENT SLACK IN THE ELEMENT. THERE WERE NO INDICATIONS AS TO WHICH OF THE TWO LIKELY POSSIBILITIES WAS THE CAUSE TASK CLOSED * CAUSE THE ROOT CAUSE IS UNKNOWN. THE MOST PROBABLE CAUSE WAS EITHER: 1) IMPACT DAMAGE FROM A FOREIGN OBJECT IN THE LN2; OR 2) PERSONNEL ERROR DURING SENSING ELEMENT MANUFACTURE WHICH RESULTED IN EXCESSIVE TENSION IN THE ELEMENT TASK II. CORRECTIVE ACTION * NO CORRECTIVE ACTION FOR THE FAILURE IS POSSIBLE. THE CAUSE OF THE FAILURE COULD NOT BE DETERMINED. REVIEW OF THE ASSOCIATED TEST AND MANUFACTURING STEPS FOUND NO INDICATIONS THAT THE EXISTING CONTROLS HAD BEEN DEVIATED FROM OR THAT THE CONTROLS WERE INADEQUATE. THERE HAS BEEN A SINGLE PREVIOUS SUPPLIER ATP FAILURE OF A 74L4 SENSOR DUE TO IMPACT DAMAGE CAUSING FRACTURE OF THE ELEMENT. THERE HAS BEEN NO SUPPLIER ATP FAILURE OF A 74L4 SENSOR DUE TO INCORRECT TENSION CAUSING FRACTURE OF THE ELEMENT TASK CLOSED TASK III. CLEARANCE OF EFFECTIVITIES * THIS IS AN EXPLAINED CLOSURE OF THE CAPS * ALL ETS CLEARED. THE SENSOR FAILED DURING VENDOR ACCEPTANCE TESTING AND ALL INSTALLED SENSORS HAVE PASSED THE VENDOR TESTS. THERE ARE TESTS OF SENSOR RESISTANCE AFTER INSTALLATION ON THE ET THAT WOULD DETECT THE FAILURE NOTE: THIS IS ALSO THE DEFERRAL RATIONALE TASK CLOSED TASK IV. CAPS CLOSURE SUMMARY * THIS IS AN EXPLAINED CLOSURE OF THE CAPS * THE CAUSE OF THE FAILURE OF THE LEVEL SENSOR DURING SUPPLIER ATP COULD NOT BE DETERMINED. NO CORRECTIVE ACTION WAS POSSIBLE. REVIEW OF THE SUPPLIERS TEST AND MANUFACTURE CONTROLS FOUND NO DEFICIENCIES. THERE ARE SUFFICIENT TESTS OF SENSOR PERFORMANCE IN THE ET BUILD CYCLE TO ASSURE PERFORMANCE ON THE FLIGHT VEHICLE TASK CLOSED |
| MSFC Response/Concurrence 1/12/94 - DEFERRAL RATIONALE: BASED ON THE INFORMATION IN "TASK III. CLEARANCE OF EFFECTIVITIES" (ABOVE), THIS PROBLEM HAS BEEN DEFERRED FOR THE NEXT SIX (6) MONTHS PER NSTS 08126, REVISION E, PARAGRAPH 3.3.10.1, ITEM D WHICH STATES "THE PROBLEM CONDITION IS CLEARLY SCREENED BY PREFLIGHT CHECKOUT OR SPECIAL TESTS (I.E., FAILURE MODE SHOULD NOT OCCUR FOLLOWING THE TEST)." APPROVED: ____PARKER V. COUNTS(SIGNED)____ DATE:____1/20/94______ PARKER V. COUNTS ET PROJECT MANAGER |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A15773 | IFA# -- | Contractor RPT# E-156 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 74L4-1 | Asmnt Part Name L02 LEVEL SENSOR | Asmnt Serial/Lot# 1649 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD U - UNKNOWN | FAIL MODE EN - OPEN |
| Asmnt FMEA 3.6.1.1 | Asmnt FM 1 | FMEA CSE A | FMEA SCSE 2 |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |