POLAR Spacecraft Status As of: Tues July 26, 16:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM: 1651=AN STIP data only | NOAA-14J AM: 2039=AN STIP data only | NOAA-15K AM: 1806=AN GAC data only | NOAA-16L PM: 1441=AN GAC&LAC data | NOAA-17M AM: 2225=AN GAC&LAC data | NOAA-18N Trans PM 14:00=AN APT/HRPT/GAC |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 XSU1 TOAR 444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ SS check Disabled when mode=YGC | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAA | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB Gyro-2 investigation | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447 |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS +100 mS 31Aug04 | PRI Daily Bias –5.5 mS -100 mS 31Aug04 | PRI Daily Bias –3 mS | PRI No daily bias |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Rephase 0730 Daily | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 1 | 2 (since 4/23/03) 3 Channels inop | 2 since 4/18/05 | 1 Analog telem drifting | 1 |
| Recorders (DTR, SSR) | DTRs 3A, 4, 5B Safestate 5B | DTRs 1, 2B, 5 Safestate- 1B | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=DTR 1B | SSRs 1,2,3,4,5 Current spikes TOAR 450 |
| VTX (APT data) | #1 ON 137.50 MHZ | OFF Since 8/14/02 Plan reactivation of VTX-2 on 7/28 at 14:00z | #1 ON 137.50 MHZ | INOP OFF since 11/15/00 | #2 ON 137.62 MHZ | #2 ON 137.9125 MHZ |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ |
| STX #1=1698.0 mhz #2=1702.5 mhz #3=1707.0 mhz #4=2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT Power drop TOAR 446 4-Playback 1,2,3-Degraded | 1 – HRPT; 2– Playback; 4 – Playback 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 Power drop TOAR 443. | 3 - HRPT 1&2 Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) | ArrayOff +60 since 6/23/04 Eclipse season 21Apr-20Aug Sun Angle 34 downtrend to 12 mid-Oct 05 Batts 1&2=LRC Batt !&2 V/T=4 Shunt degraded SA CANT=37 degs | Array Off -55 Since 8/21/03 Eclipse all year Sun angle 51 Steady trend Batts 1-3= LRC Batts 1&3V/T=7/11 Batt2 VT=8/11 SS trigger =18.98 Shunt Degraded SA CANT=22 degs | Array Off -45 Since 1/25/01 Eclipse Season 16 May-30 Jul Sun Angle 28 downtrend to 2 degs on 10 Oct 05 Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 57 Start downtrend to 41 on 30 Oct 05 Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 70 Steady trend Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs | Array Off. -40 Since 6/6/05 Eclipse all year Batts 1-3=LRC Batts 1-3 V/T=4/8 SADE swap to side-2 planned for 7/27/05 SA CANT=22 PSSS enabled 30May |
| AVHRR | Nominal | Nominal Stalled Scan motor Abruptly returned to nominal 16 July 14:30z 14 Apr 04 | Nominal Rare major scan motor surges. Last Incident 11/18/04 | Degraded TCE24 OFF 4/14/04 Bar coded imagery since 29June05 Channel 3B only. | Nominal 3A-B switch enabled | Nominal 3A-B switch Enabled 6/23/2005 |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Space view 1 Since 6/7/05 Warm target testing to support HIRS TOAR 7/25/05 |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal | Nominal Space view-2 since 6/08/05 Warm Target testing to support HIRS TOAR 7/26/05 |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | OFF/Inop Turned off 6/23/05 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | NOMINAL Upgraded to Yellow status 16 May 05 FW Abrupt return to nomial at 09:00Z TOAR 445 CLOSED 7/12/05 FW mode=Hi Powr FW Heater OFF | Operational High levels of imagery radiometric noise TOAR 441 open Occasional major FM surges, most recent 12/9/04 | NOMINAL 1 Pixel cross track misalignment . | ON TOAR 448 Noise in long wave channels 1-12. Some improvement reported. Tested in high power mode 12 July |
| MHS/MIU |  |  |  |  |  | Nominal Final config 6/4/05 |
| MSU | OFF/Inop Turned off for power balance 6/23/05 | Operational Scan motor and antenna problems |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal | ON DRU’s 1-7 On DRU-8 TOAR 449 turned off 6/13 |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | ON A-Side 121, 243, 406 FIXED GAIN MODE Since 18 Jul 05 |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | ON A-side 23 May |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Tscopes inop | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 | ON Turned on 6 June at 14:05z |
| SBUV |  | Degraded Grate motor sticks Flex memory 3 (giant step) ops suspended 12/2/03 Reduced operations No data reported by products division 7/25/05 |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops Procedure changes forthcoming | ON Anode mode since 6 July 13:30z OV testing continues |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer changed to 12 minutes 12July |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 HIRS FW Heat tuned ON 17 Apr and OFF on 18 Apr TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 | Nominal TCE24 OFF 4/14 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 | All TCE’s active |
|  | N12 | N14 | N15 | N16 | N17 | N18 |

COMMENTS/CHANGES:

NOAA-12	No change from last week although the N12 battery’s maximum discharge voltage continue to slowly trend upward

(now above 20 volts) during the past week in conjunction with the continued waning of eclipse season (expected to end completely in mid-August). Additional reconfigurations are anticipated for the N12 power subsystem in the coming weeks that may include turning HIRS and MSU back on and moving the solar array offset.  Because of the waning eclipse season some battery Day-Night history flags are starting to show up which will become non applicable as soon as eclipse season ends.  Specific operations are not yet defined.  Carl Gliniak is EMOSS POC for this situation.

NOAA-14:	On 16 July at 14:30z, the N14 AVHRR apparently fixed itself.  The scan motor current abruptly dropped to nominal as

did its component temperature and synch delta values (illustrations 1, 2, 3). AVHRR HRPT Imagery also returned to nominal (illustration 4).  The payload has remained nominal ever since and, on 21 July, its status was upgraded to YELLOW (from RED).  In response to this event, EMOSS is coordinating with Scheduling to turn N14 APT data (VTX-2) back on for the first time in over 3 years (without conflicting with N17 APT data) on 28 July at 14:00z for 4 days after which it will enter into RF conflict with N17 and be turned off again.  EMOSS engineer Sally House discovered the AVHRR improvement and Will Chadwick is EMOSS POC for the APT turnon operation.

The change in N14 AVHRR did not impact the spacecraft power balance to any discernable degree.  Power balance remains stable with no problems detected since the previous support (illustration 5).

EMOSS engineers received reports from the Products (Ozone) division that N14 SBUV had stopped producing any data on 25 July.  EMOSS investigation into this already seriously degraded showed no temperature or current surges being observed and the grating position changing nominally (although it was changing much more frequently on the day in question, illustration 6).  Products was eventually able to make products from some of their ingests but their grating monitoring program indicated some unusual grating errors and some of the data was flagged in sweep mode EMOSS engineer Sally House is investigating.

NOAA-15:	The N15 AMSU’s, AVHRR and HIRS were all nominal and stable last week (illustration 7).  N15 continues progressing nominally through its eclipse season (illustration 8) which is now waning and expected to end late this week or early next week.  No power subsystem reconfigurations are expected.

NOAA-16:	The N16 AVHRR scan motor current was stable to slightly higher during the past week (illustration 9) while its synch

delta remained generally pegged most of the time and a large percentage of its imagery continued to produce bar code noise (illustration 10).  Otherwise N16 payloads were generally nominal and stable during the past week (Illustration 11) as were the remainder of N16 subsystems.

NOAA-17:	The N17 payload suite were also nominal and stable during the past week (illustration 12).  Meanwhile, EMOSS

continues closely monitoring the N17 gyro-2 spin motor current which was also stable during the past week

(illustration 13).  One less than nominal situation which did occur on N17 during the past week was an inordinate number of single event upsets on CPU2 that had to be scrubbed on 24 July (illustration 14). However, by mid-day this situation ceased and returned back to normal.

NOAA-18:	Some OV testing and reconfigurations continue for N18 primarily those in support of TOAR investigations.  On 25

July at 17:15z, EMOSS engineers Jim Walters oversaw an operation that parked the AMSU-A1 at a warm target for one orbit and then back to full scan mode.  This operation was repeated on 26 July at 15:35 using both the AMSU-A1 and AMSU-A2 payloads.  These tests were requested by NASA in support of the HIRS long wave noise (TOAR 448) investigation.

In support of the pitch oscillation investigation (TOAR 447), EMOSS engineer Jon Woodward is planning on implementing a swap of the Solar Array Drive electronics from side-1 to side-2.  The reason for this swap is that pitch noise may be caused by a broken pole in Side 1's motor windings and a switch to side 2 will help verify this possibility.

See illustrations 15-19 for a summary of N18 performance over the past week.

Illustration 1:  N14 AVHRR Health Analysis:

(An unexpected recovery)

Illustration 2:  N14 AVHRR Health Analysis (cont)

Illustration 3:  N14 Synch Delta Analysis

(From perfectly “pegged” to nearly perfect)

Illustration 4:  N16 AVHRR Imagery Analysis

(From unusable to nominal.  APT turnon planned for 28 July for 4 days on VTX-2)

Illustration 5:  N14 Power Analysis

(No impact from AVHRR situation, stable and nominal)

Illustration 6:  N14 SBUV Analysis

(No readily obvious reasons for data product problems observed on JDAY 206 although there is an increase I grating position movements on JDAY 206, the day in question.)

Illustration 7:  N15 Payload Analysis

(Generally nominal and stable.)

Illustration 8:  N15 Power Analysis

(Nominal and stable as eclipse season winds down.)

Illustration 9:  N16 AVHRR Health analysis

(Just a little worse than last week.)

Illustration 10:  N16 AVHRR Imagery Analysis

(No better than last week.  Synch deltas pegged all the time as well.)

Illustration 11:  N16 Payload Health Analysis

(Nominal and stable.)

Illustration 12:  N17 Payload Health Analysis

(Nominal and stable)

Illustration 13:  N17 ADACS Health Analysis

(Generally nominal and stable)

Illustration 14:  N17 CPU Single Event Upset Analysis

(Note the erratic behavior in CPU2ER2.)

Illustration 15:  N18 Payload Health Analysis

(Nominal and stable)

Illustration 16:  N18 HIRS Health Analysis

(Nominal and stable, from an engineering perspective.  Long channel noise still apparent and being investigated

Illustration 17:  N18 Power Analysis

(Nominal and stable)

Illustration 18:  N18 DHS/Comm Analysis

(Note how STX-1 and STX-4 have been swapped as far as their playback usage is concerned.)

Illustration 19:  N18 ADACS Analysis

(Nominal and stable, other than the pitch oscillation TOAR which is still being investigated.)

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING July 22, 2005

| DAY/DATE | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 | NOAA-18 |
| --- | --- | --- | --- | --- | --- | --- |
| FRI. 07/15 | -282 msec | +217 msec | -223 msec | +134 msec | +074 msec | -052 msec |
| SAT. 07/16 | -283 msec | +220 msec | -222 msec | +135 msec | +075 msec | -050 msec |
| SUN. 07/17 | -285 msec | +220 msec | -223 msec | +134 msec | +075 msec | -049 msec |
| MON. 07/18 | -285 msec | +220 msec | -223 msec | +135 msec | +074 msec | -047 msec |
| TUE. 07/19 | -286 msec | +216 msec | -225 msec | +135 msec | +076 msec | -048 msec |
| WED. 07/20 | -287 msec | +217 msec | -226 msec | +136 msec | +078 msec | -046 msec |
| THU. 07/21 | -294 msec | +216 msec | -227 msec | +135 msec | +078 msec | -045 msec |

EMOSS POC for this chart is JIM SHEPHERD

NOAA-14:  As of 12/23/03 the TIP clock is corrected daily by –7.0 msec to compensate for drift.

NOAA-15:  As of 04/22/03 the TIP clock is corrected daily by –8.0 msec to compensate for drift.

NOAA-16:  As of 12/23/03 the TIP clock is corrected daily by -5.5 msec to compensate for drift.

NOAA-17:  As of 12/23/03 the TIP clock is corrected daily by –3.0 msec to compensate for drift.

NOAA-12:  As of 12/10/03 the TIP clock is corrected daily by +6.5 msec to compensate for drift.

*    A clock jump of +500 milliseconds on 01/31/05 due to fractional second daily ETCUP. A clock

jump of +500 milliseconds on 04/17/05 due to fractional second daily ETCUP. Alternating +/-

500 millisecond clock jumps will ccur at 76-day intervals as long as fractional second daily

ETCUP is utilized to manage clock drift. The next +500 millisecond jump is expected on 07/02/05.

POES Engineering Contact List

Government

Renee Smith-Dearing  NOAA POES Constellation Lead 		301-817-4117

Dong Han:  NOAA, POES Payloads				301-817-4127

Micky Fitzmaurice:  NOAA, POES Bus, IJPS	 	    	301-817-4016

Nicolaie Todirita (Todi): NOAA Ground Systems			301-817-4229

EMOSS-2 Contractor

Jeff Devine: EMOSS POES Lead	 				301-817-4020

Jim Walters:  EMOSS, POES Payload Engineer			301-817-4033

Carl Gliniak, EMOSS POES Power and Thermal 			301-817-4207

Jim Sheperd, EMOSS POES Attitude Control			301-817-4030

Jon Woodward EMOSS, POES Flight Software C&CS		301-817-4019

Sally House EMOSS POES Payloads 				301-817-4026

William Chadwick EMOSS, POES Comm and DHS			301-817-4015