## Exercise 2—Effects of using improper scale offset

- The line shown on the rating on the next page was drawn using rating table 1.0 (on third page). Rating tables are often used to display the discharge predicted for a given gage height. These tables are developed by interpolating between input points, which are points where you tell the computer what the discharge is for a given gage height. Input points are shown using asterisk on the attached tables.

- Your assignment is to plot 3 or 4 points between gage heights of 6.10 and 8.20 using data from rating table 1.1 (on fourth page). Figure out where these points fall in relation to the rating curve drawn below. Why don’t they plot on the line?

### ADAPS did the interpolation using the wrong offset for the curve in Table 1.1, so the interpolation was done incorrectly. The offset of 0.0 used in Table 1.1 was too low resulting in a concave-downward line.

### ��

1                        UNITED STATES DEPARTMENT OF INTERIOR - GEOLOGICAL SURVEY - WATER RESOURCES DIVISION                  PAGE  1

EXPANDED RATING TABLE                                          TYPE: LOG

06000001                                               DATE PROCESSED: 11-14-1991 @ 14:57 BY KLWAHL

ADAPS TRAINING SITE NO. 1                                                                   DD:    1    TYPE: 001    RATING NO:  1.0

OFFSET: 5.0  BREAK,OFFSET: (6.1,5.0)                                                               START DATE/TIME: 10-01-91  (0001)

BASED ON _______ DISCHARGE MEASUREMENTS, NOS ________, AND ________, AND IS ______ WELL DEFINED BETWEEN ______ AND ______ CFS

COMP BY _____ DATE ________    CHK. BY _____ DATE ________

Prob. 4 -- Correct offset

GAGE                                                                                                                    DIFF IN Q

HEIGHT                       DISCHARGE IN CUBIC FEET PER SECOND           (STANDARD PRECISION)                              PER

(FEET)        .0         .1         .2         .3         .4         .5         .6         .7         .8         .9        FOOT

6.0                   10.0*      11.6       13.2       15.0       16.8       18.8       20.8       22.8       25.0       19.2

7.0        27.3       29.6       32.0       34.5       37.0       39.7       42.3       45.1       48.0       50.9       26.5

8.0        53.8       56.9       60.0*      63.3       66.7       70.2       73.8       77.4       81.1       84.9       35.0

9.0        88.8       92.7       96.7      101        105        109        113        118        122        127         42.2

10.0       131        136        141        146        150        155        160        165        171        176         50.0

11.0       181        186        192        197        203        208        214        220        226        231         56.0

12.0       237        243        249        255        262        268        274        281        287        293         63.0

13.0       300*       306        313        319        326        333        339        346        353        360         67.0

14.0       367        374        381        388        395        402        410        417        424        432         72.0

15.0       439        447        454        462        470        477        485        493        501        509         78.0

16.0       517        525        533        541        549        558        566        574        583        591         83.0

17.0       600        608        617        625        634        643        652        661        669        678         87.0

18.0       687        696        706        715        724        733        742        752        761        771         93.0

19.0       780        790        799        809        819        828        838        848        858        868         98.0

20.0       878        888        898        908        918        928        939        949        959        970        102

21.0       980        990       1000       1010       1020       1030       1040       1050       1070       1080        110

22.0      1090       1100       1110       1120       1130       1140       1150       1160       1180       1190        110

23.0      1200       1210       1220       1230       1240       1260       1270       1280       1290       1300        110

24.0      1310       1330       1340       1350       1360       1370       1390       1400       1410       1420        120

25.0      1430       1450       1460       1470       1480       1500       1510       1520       1530       1550        130

26.0      1560       1570       1580       1600       1610       1620       1640       1650       1660       1680        130

27.0      1690       1700       1710       1730       1740       1750       1770       1780       1790       1810        130

28.0      1820       1830       1850       1860       1880       1890       1900       1920       1930       1940        140

29.0      1960       1970       1990       2000       2010       2030       2040       2060       2070       2090        140*

30.0      2100*

��

1                        UNITED STATES DEPARTMENT OF INTERIOR - GEOLOGICAL SURVEY - WATER RESOURCES DIVISION                  PAGE  1

EXPANDED RATING TABLE                                          TYPE: LOG

06000001                                               DATE PROCESSED: 11-14-1991 @ 14:58 BY KLWAHL

ADAPS TRAINING SITE NO. 1                                                                   DD:    1    TYPE: 001    RATING NO:  1.1

OFFSET: .0  BREAK,OFFSET: (6.1,.0)                                                                 START DATE/TIME: 10-01-91  (0010)

BASED ON _______ DISCHARGE MEASUREMENTS, NOS ________, AND ________, AND IS ______ WELL DEFINED BETWEEN ______ AND ______ CFS

COMP BY _____ DATE ________    CHK. BY _____ DATE ________

Prob 4 -- Incorrect offset

GAGE                                                                                                                    DIFF IN Q

HEIGHT                       DISCHARGE IN CUBIC FEET PER SECOND           (STANDARD PRECISION)                              PER

(FEET)        .0         .1         .2         .3         .4         .5         .6         .7         .8         .9        FOOT

6.0                   10.0*      11.0       12.2       13.4       14.7       16.1       17.7       19.3       21.1       14.4

7.0        23.0       25.1       27.3       29.7       32.2       35.0       37.9       41.0       44.3       47.9       28.7

8.0        51.7       55.7       60.0*      62.6       65.3       68.0       70.9       73.8       76.8       79.9       31.4

9.0        83.1       86.3       89.7       93.1       96.7      100        104        108        112        116         36.9

10.0       120        124        129        133        138        142        147        152        157        162         47.0

11.0       167        173        178        184        190        196        202        208        214        220         60.0

12.0       227        234        240        247        254        262        269        277        284        292         73.0

13.0       300*       305        311        316        322        328        333        339        345        351         56.0

14.0       356        362        368        374        381        387        393        399        406        412         63.0

15.0       419        425        432        438        445        452        459        465        472        479         67.0

16.0       486        493        501        508        515        522        530        537        545        552         74.0

17.0       560        568        575        583        591        599        607        615        623        631         80.0

18.0       640        648        656        665        673        682        690        699        708        717         85.0

19.0       725        734        743        752        762        771        780        789        799        808         92.0

20.0       817        827        837        846        856        866        876        886        896        906         99.0

21.0       916        926        936        946        957        967        978        988        999       1010        104

22.0      1020       1030       1040       1050       1060       1080       1090       1100       1110       1120        110

23.0      1130       1140       1150       1170       1180       1190       1200       1210       1230       1240        120

24.0      1250       1260       1270       1290       1300       1310       1320       1340       1350       1360        120

25.0      1370       1390       1400       1410       1430       1440       1450       1470       1480       1490        140

26.0      1510       1520       1530       1550       1560       1570       1590       1600       1620       1630        130

27.0      1640       1660       1670       1690       1700       1720       1730       1740       1760       1770        150

28.0      1790       1800       1820       1830       1850       1860       1880       1890       1910       1930        150

29.0      1940       1960       1970       1990       2000       2020       2040       2050       2070       2080        160*

30.0      2100*

# Text boxes

(6.10, 10)

(8.2, 60)

(13.0, 300)

6

7

8

9

15

Scale offset = 5.0