WPEC SG21: Assessment of Neutron Cross-Section Evaluations for the Bulk of Fission Products

59-Pr-141 Review

Pavel Oblozinsky, BNL, August 2003

### 1. General

### Properties: Stable nucleus, natural abundance 100.00%.

EXFOR data

Experimental data are generally available; in particular, total, capture and (n, 2n) were measured; (n,n’) data available around 5 MeV; (n,p) and (n,() available around 14 MeV.

### Evaluations

ENDF/B-VI	Thermal and resonance region was re-evaluated in 1999 by Oh (KAERI) and Mughabghab (BNL), included into ENDF/B-VI release 7. Fast region datas back to 1980, by Schenter and Schmittroth (ORNL). In 2002, fast region re-evaluated by Lee (KAERI) and Oblozinsky (BNL), submitted to ENDF/B-VII

JEF-2	Year of origin 1982, by Gruppelaar (Petten) and Menapace (Bologna), with some later improvements.

BROND-2	None.

JENDL-3 	Year of origin 1990, by JNDC FP Working Group.

CENDL-3	Year of origin 2000, by Songbai Zhang and Qingbiao Shen (CNDC Beijing).

### 2. Thermal and resonance region

For summary, see Table 1 and 2.

ENDF/B-VI

- Thermal cross sections re-evaluated in 1999, some changes compared to BNL-325 (1981); results close to JEF-2 and JENDL-3.

- RR region – re-evaluated in 1999 using MLBW formalism, up to 10.049 keV.

- UR region – revised in 1999, up to 146.47 keV.

JEF-2

- Thermal cross sections based on BNL-325 (1981).

- RR region  – parameters taken from BNL-325 (1981).

- UR region – no data.

JENDL-3

- Thermal capture cross sections based on BNL-325 (1981).

- RR region up to 13.226keV, MLBW formalism used with parameters from BNL-325 (1981) with some updates.

- UR region (13.226 keV – 100 keV) based on BNL-325 (1981).

CENDL-3

  - Taken from unspecified release of ENDF/B-VI (before release 7).

Recommendation/Conclusion

In the thermal and resonance region the most recent evaluation is ENDF/B-VI (release 7), it was performed in 1999 under guidance of Said Mughabghab. ENDF/B-VI is recommended.

3. Fast neutron region

#### ENDF/B-VI methodology

- Failry up-to-date methodology already in 1980.

- Extra comment: In 2002, completely new evaluation was prepared for ENDF/B-VII. It uses up-to-date methodology, based on model calculations with the code EMPIRE (statistical model, pre-equilibrium model, FKK model) and RIPL input parameter library, adjusted to reproduce experimental data.

#### JENDL-3 methodology

- Methodology fairly up-to-date, all important nuclear reaction processes taken into account.

- Above 100 keV spherical optical model and statistical model code CASTHY used. Total cross section above 5 MeV taken from experimental data.

- Pre-equilibrium effects included using code PEGASUS.

- (n, p) and (n,() normalized at 14.5 MeV to systematic values by Forrest. (n,() below 13.2 keV calculated from resonance parameters.

- Angular distributions are provided, either based on CASTHY or considered isotropic.

##### JEF-2 methodology

- Adopted RCN evaluation, based on statistical model and fits.

- Charged particle production taken from REAC-ECN-4 library.

##### CENDL-3 methodology

  - Methodology fairly up-to-date, all important nuclear reaction processes taken into account.

  - Above 100 keV, spherical optical model used, with own OM parameters.

  - Reaction channels calculated using statistical + pre-equilibrium model code SUNF.

  - Direct contributions to (n,n’) calculated by DWUCK4.

  - Angular distributions are provided, either based on optical model calculations, SUNF or considered isotropic.

Comparison of evaluations

- MT=1	 JEF-2 probably best; below 0.2 MeV data in ENDF/B-VI and JENDL-3 are

somewhat high, while CENDL-3 is clearly too high.

- MT= 4	 All evaluations are approximately equivalent and reasonable.

- MT=16	 All files reasonable, JENDL-3 probably the best.

- MT=102	 JENDL-3 and also ENDF/B-VI are the best, JEF-2 and CENDL-3 tend to

underestimate data at higher incident energies.

- MT=103	 JENDL-3 is the best, followed by CENDL-3.

- MT=107	 JENDL-3 and CENDL-3 are the best, JEF-2 has unrealistic shape.

###### Recommendation/Conclusion

  - In the fast energy region, JENDL-3 is based on up-to-date methodology, it is fairly complete evaluation that compares well with experimental data in all channels. JENDL-3 is recommended.

  - There is new (2002) evaluation submitted for inclusion into ENDF/B-VII. In case this new evaluation will be accepted by ENDF/B-VII, then ENDF/B-VII rather than JENDL-3 is recommended.

Table 1. Thermal cross sections, resonance integral and one-group capture values for Pr-141.

| Source | Total (barn) | Capture (barn) | Elastic (barn) | Resonance Capture Integral (barn) | One-group Capture (barn) [2] |
| --- | --- | --- | --- | --- | --- |
| ENDF/B-VI | 14.20 | 11.50 | 2.70 | 17.6 | 1.50E-1 |
| JEF-2 | 14.07 | 11.48 | 2.59 | 17.9 | 1.54E-1 |
| JENDL-3 | 14.04 | 11.50 | 2.54 | 18.4 | 1.57E-1 |
| CENDL-3 | 13.51 | 11.50 | 2.01 | 17.6 | 1.56E-1 |
| Mughabghab 2003 [1] |  | 11.5(0.3) |  | 17.4(2.0) |  |

Table 2. Summary of resolved and unresolved resonance region for Pr-141.

| Library | Year | First Author | RRR | URR | Remarks |
| --- | --- | --- | --- | --- | --- |
| ENDF/B-VI, release 7 | 1999 | R.Q. Wright | 10.049 keV MLBW | 10.049 keV-146.67 keV | Re-evaluated under guidance of S. Mughabghab. MLBW formalism adopted. |
| JEF-2 | 1982 | Gruppelaar | 5.77274 keV |  | Based on BNL-325 (1981). |
| JENDL-3 | 1990 | JNDC FP Work. Group | 13.226 keV MLBW | 13.226 keV – 100 keV | Taken from JENDL-2 with some update. |
| CENDL-3 | 2000 | S. Zhang |  |  | Taken from earlier version of ENDF/B-VI (before release 7). |

#### References

- S.F. Mughabghab, Thermal neutron capture cross sections, resonance integrals and g-factors, Report INDC (NDS)-440 (IAEA, Vienna, February 2003).

- H. Gruppelaar et al, Status of pseudo-fission-product cross sections for fast reactors, Final Report of Subgroup 17, Report NEA/WPEC-17, ECN-R-98-014 (NEA, Paris, 1998). Recalculated systematically for all 211 FP and all 5 evaluated libraries by I. Sirakov (BNL, 2002), see http://www.nndc.bnl.gov/sg21/nucl/acs/accs.htm.